"Documentation" for the RTTY program.

         The  basic  program you will recognize as PC-TALK III and all
         credit due the authors is hereby acknowledged.  My  objective
         was  to  not  modify  any of the functions of PC-TALK III and
         best I know that's the case.  The only exception I can  think
         of  is that <ALT-J> in the original PC-TALK III does the same
         thing as <ALT-K> (redefine the function  keys)  and  I  stole
         <ALT-J> for another function.  Otherwise refer to the PC-TALK
         III  documentation  first  and  then  look   here   for   the
         modifications  I  made.   I am assuming an AEA CP-1 interface
         with with a  serial  interface.   Whether  it  will  work  on
         anything  else...that's  up to you.  I used an article is the
         September 1981 issue of QST as a reference  for  the  speeds,
         codes  and general RTTY stuff.  Other reference material that
         might help ( and that I used ) were the  Technical  Reference
         Manual for the IBM-PC and the Basic Manual for the IBM-PC.

         <ALT-?> Definitions.

         <ALT-U>
         This turns on or off the RTTY translation process.  When  the
         program  starts  RTTY is off.  <ALT-U> will display "RTTY ON"
         and  will  begin  translating  the  incoming   and   outgoing
         characters between ASCII and RTTY 5 bit "BOUDOT" code.

         <ALT-J>
         This  is  hard  coded  to spit out my call sign, the date and
         time.  To be done properly this should be part of the default
         file but I got lazy.  You could certainly alter the call sign
         to your own.  Matter of fact I would prefer it!

         <ALT-H>
         This  switches  between  COM1:   and  COM2:.   A  message  is
         displayed to indicate the  current  status  and  the  program
         initializes to the default file.

         <ALT-B>
         This  will  allow  you  to  enter a different data rate.  The
         program will ask you for a new speed.  If you respond with  a
         <?>  the  program  will return with the current setting.  For
         example, entering 45.45 will result in the proper  "bits  per
         seconds" setting for standard "60 WPM" RTTY.

         <ALT-N>
         This will switch between the two  versions  of  FIGS  that  I
         found in the previously mentioned artical.

         <ALT-A>
         This will turn the transmitter on and off.   What  it  really
         does  is  set  or reset the "Request to Send" line out of the
         serial port.  Nothing will be displayed.

         <ALT-O>
         This  will  force  a  switch  between LTRS and FIGS.  This is
         sometimes  handy  if  you  happen  to  loose  one  of   those
         characters and end up receiving garbage because you're in the
         wrong case.


         Operation

         In general, the standard way of getting RTTY "up" is to first
         start the the RTTY program.  When it is ready it will display
         the  message  "Ready".   Then  you can set the communications
         port address using <ALT-H> to the port  where  the  interface
         is.   (I have two serial ports and simply switch between them
         using <ALT-H>).  Then you use one of  the  dialing  directory
         entries  to  set the number of data and stop bits.  The entry
         name is not important other than to remind you  what  it  is.
         Hit  <ALT-D>  and  select  the entry you have set up with the
         proper communications parameters and hit  enter.   The  phone
         number  should be left blank ( although I haven't ever  tried
         it with a number there.  It won't do anything other than send
         the  number out the port!  ) The speed can be set to anything
         because you will set that later  with  the  <ALT-B>  command.
         Data  and  stop  bits are important here and this is the only
         way to alter them.  Since Basic and the original PC-TALK  III
         logic  opens  the  serial  port  when  executing  the <ALT-D>
         command, the speed will be set at whatever  you  had  in  the
         dialing  directory.   Problem  is  that  Basic  only  accepts
         certain values ( see the manual ) and causes  error  messages
         on  anything  it  doesn't  like.   Therefore  one of the next
         commands ought to be the <ALT-B> command to  set  the  speed.
         Again,  due  to Basic and previous program logic, the program
         will turn on the transmitter as soon as the  <ALT-D>  command
         is  executed.  You may or may not want to turn it off at this
         point.  The last thing that is necessary is to  turn  on  the
         RTTY  tranlation  process with <ALT-U>.  There you are, ready
         to send and receive Radio TeleTYpe.

         One  word  of advise.  Compile this thing!  Basic has a nasty
         habit of wondering off into never-never land  when  it  comes
         time  to  clean  up  the  string  character  space.  For this
         program this process can take as long  as  5  minutes!   Once
         compiled  the  clean-up  time  is less than 1 second.  (Don't
         ask.  If you must then ask IBM!) Also, heed the  warnings  in
         the PC-TALK III documentation concerning communication buffer
         sizes.

         If you have any questions I will be glad to answer any that I
         can.  I make no claims about quality of the code  or  whether
         it conforms to any known standards.  Enjoy.

         Steve Darling KA9DCA
         3408 33rd Street
         Moline, Illinois 61265
         (309) 762-5342