Lanalyse!  Network Performance Analysis Tool
 
                    (c) 1991 by EbSoft

Lanalyse allows you to remotely monitor the various status 
information provided by NETBIOS on any NETBIOS network node.  You 
need not have started your network operating system to run Lanalyse.

HOW TO USE THE PROGRAM:

You may create a text file named NodeList.LAN in the current 
directory.  This file contains the names of the nodes you wish to 
scan, each on its own line with a <CR><LF>.  These names can be 
any valid NETBIOS name, i.e. machine name or user name.  If 
NodeList.LAN does not exist, only the local node will be scanned 
for analysis.

After determining which of the specified nodes are avilable on the 
network, Lanalyse presents you with a picklist of available nodes 
on the left of the screen, and on the right side of the screen, a 
detailed analysis of NETBIOS status for the selected node.

The information presented is as follows:

Adapter:  This is the 6-byte LAN adapter permanent node name.
Type: Adapter type - TRN = Token Ring Network Adapter
                     PCN = PC Network Adapter
Software Version:  major and minor NETBIOS revision levels  
Hours Up:  Time since last adapter reset.

Error Counts:
  Total Packets Xmit/Rcv: Packet counts since reset.
  Rcv Reject: Occasions where received frames were rejected
  Xmt Reject: Occasions where transmetted frames were rejected
  Data Frame: Count of bad data frames received
  Aborted Xmit: Count of unsuccessful transmissions
  Retransmit: Count of retransmitted frames
  No Buffers: Occasions where receiver was out of buffers
  T1 Timeout: Number of times the adapter's T1 timer has expired
  Ti Timeout: Number of times the adapter's Ti timer has expired

Network Resources:
  NCBs available: Amount of Network Control Blocks presently available
  NCBs last reset: Max NCBs as set at last reset
  Max NCBs: Max NCBs as defined by driver/card
  Sessions Active: Amount of NETBIOS Sessions presently active
  Sessions last reset: Max sessions as set at last reset
  Max Sessions: Max sessions as defined by driver/card

Node Names:  This is a listing of up to eight NETBIOS node names 
             assigned to the adapter.  The actual count is shown.

In its default mode, Lanalyse will only recognise machine names 
under PC LAN Program, because PCLP appends an ASCII 03 to the end 
of user names.  You can include user names in the scan by using 
the /PCLP switch when invoking Lanalyse, or by setting a DOS 
environment variable called LANALYSE to /PCLP with the DOS command
SET LANALYSE=/PCLP

Press <F1> within Lanalyse for the help screen.