Image Alchemy


                                     Version 1.4



                                   March 18, 1991









                                    User's Manual











                                        TM
                           Image Alchemy   was written by

                                 Marcos H. Woehrmann
                                 Allan N. Hessenflow
                                   David Kettmann




                  Copyright (c) 1990-1991 by Handmade Software, Inc.
                       All Rights Reserved   15951 Los Gatos Blvd., Suite 7
                                             Los Gatos, CA  95032
                                             +1 408 356-4143 (Fax)
                                             +1 408 358-1292 (Voice)

                                             UUCP: hsi@netcom.COM
                                               or: apple!netcom!hsi
                                             Cserve: 71330,3136





                        Shareware Fundamentals and Specifics

          We encourage you to freely copy and distribute the shareware
          version of Image Alchemy provided that:

               1.   No fee beyond normal media, duplication, and shipping
                    costs may be charged.

               2.   Shareware vendors and computer user groups who charge
                    less than $7.00 per disk may distribute Image Alchemy,
                    but Handmade Software must be supplied with a copy of
                    the first catalogue issue offering each new revision of
                    Image Alchemy.

               3.   Others may only distribute Image Alchemy with the
                    written permission of Handmade Software.  In all cases,
                    it must be clearly stated to the purchaser that he or
                    she is receiving an unregistered copy of a shareware
                    product

               4.   The distribution files must be distributed in their
                    original forms.  The unrestricted version may not be
                    distributed.


          If you received Image Alchemy as shareware (i.e. you downloaded
          from a bulletin board, you received it from a friend, it came
          with some hardware you purchased, or you bought a disk from a
          software library), and if you use it beyond a two week trial
          period, you must register the program using the accompanying
          order form.

          For the $79.95 registration fee, you will receive the current,
          retail version of Image Alchemy without the 640 by 480 image size
          restriction.  You will be notified of significant upgrades to
          Image Alchemy, you will be placed on a mailing list to receive
          information about future products from Handmade Software, and you
          will be entitled to phone and email support.

          Registered users are entitled to minor updates for a nominal fee
          (not to exceed $5.00 for disks or $20.00 for tapes).  Registered
          users are also entitled to major updates at a substantially
          reduced price.











   Image Alchemy v1.4    Copyright (c) 1990-91 Handmade Software Inc.    Page 2




                               What is Image Alchemy?

          Image Alchemy is a software utility that has two functions in
          life:

          First, Image Alchemy performs JPEG compression.  This is a new
          standard for image compression that can achieve much higher
          compression ratios than conventional compression techniques.  It
          achieves this high compression ratio by not entirely preserving
          the original image (this is referred to as "lossy" compression).
          For further information see the What is JPEG Compression section
          below.  Image Alchemy is the first shareware program to perform
          JPEG compression and decompression.

          Second, Image Alchemy converts between various graphics file
          formats.  Image Alchemy understands a wide variety of file
          formats including industry standards such as GIF and TIFF.
          Currently we support 15 different formats, and we are always
          adding new formats; in fact, our goal is to have Image Alchemy be
          able to read and write every type of graphic file in the world.


                                Hardware Requirements

          IBM PC:

          At least an 80286 IBM PC AT or clone.

          At least 380k of free memory (Image Alchemy will run much faster
          if you have more than 400k of memory available).  Some
          conversions and some images require more memory (Alchemy will
          attempt to use all available system memory, so if you get out of
          memory errors or warnings try removing as many TSRs as you can).

          A hard drive with at least as much free space as three times the
          size of the image being converting (i.e. a 640x480 image will
          require approximately 1 meg of free space).

          A VGA or 8514/A board, if you want to view images (tested VGA
          boards include those with the Paradise, Everex, Trident, Video 7,
          and the Tseng Labs Chipsets, tested 8514/A boards include IBM and
          those with the Western Digital Chipset)

          MS-DOS or PC-DOS 3.x or greater


          Sun:

          A SPARC or 680x0 equipped Sun (either a Sun 3, Sun 4,
          SPARCstation, or SPARCserver).

          SunOS 4.0.3 or greater


   Image Alchemy v1.4    Copyright (c) 1990-91 Handmade Software Inc.    Page 3




                                    Introduction


          To install Image Alchemy copy the file alchemy.exe (for MS-DOS
          users) or alchemy (for Sun users) to your hard disk.  There are
          no support files or configuration files which need to be copied.
          Image alchemy comes with a sample JPEG compressed image,
          sample.jpg.  You might want to copy it to your hard drive to
          follow along with the examples below.


          To use Image Alchemy:

          alchemy -option [-option, ...] inputFileName [outputFileName]


          The inputFileName is any valid file name (including an optional
          path).  The outputFileName is optional;  if it is not specified
          Image Alchemy generates one by substituting an appropriate
          extension to the input file name.  If the outputFileName does not
          include an extension one will be added (you may prevent this by
          appending a period "." to the outputFileName).

          Options are preceded by a dash ("-"). Those options which take a
          parameter may have it immediately following the option or
          separated by a space (for example, either -c128 or -c 128 is
          acceptable).

          The only option that is required is the output file format (or
          the viewing option, for IBM PC users).  Image Alchemy will make
          reasonable decisions for all of the other options.

          The options are documented below.  The order of the options is
          only significant in the case of the -z, -D, and -V options.  The
          options can appear anywhere in the command line (certain options
          take parameters; in this case the parameters must follow the
          option).  The case of the options is significant.

          Three options which are unique in their operation are -z, -D, and
          -V.  These options all mean different things depending on how
          many times they are specified (for example, -D 150, has a
          different meaning then -D 150 -D 150).  This isn't a problem in
          actual usage, but is something you should be aware of.











   Image Alchemy v1.4    Copyright (c) 1990-91 Handmade Software Inc.    Page 4




                                Image Alchemy Options


          Information:


               -h   Help.  Display command summary.

               -?   Display about information.  Includes support, ordering,
                    and version information.


          Output file options (details on each of the supported file
          formats can be found below in the Details on Supported File
          Formats section):

               -a compressionType
                    Generate a tArga file.  Optionally specify the
                    compression type used to store the file.
                    Compression types supported are:
                         0:Raw
                         1:RLE
                    The default is RLE Compression.

               -e previewType
                    Generate an Encapsulated PostScript file.  Optionally
                    specify the preview type.  Preview types supported are:
                         0:None
                         1:Device Independent
                    The default is Device Independent

               -g   Generate a Gif file.

               -i   Generate an Ilbm file (also known as an Iff file, also
                    known as an LBM file).



















   Image Alchemy v1.4    Copyright (c) 1990-91 Handmade Software Inc.    Page 5




               -j[a] quality
                    Generate a Jpeg file.  Optionally specify the use of
                    Arithmetic coding and the quality.
                    If you specify an a immediately after the -j (as in -
                    ja), Alchemy will generate a JPEG file compressed using
                    Arithmetic encoding instead of the default Huffman
                    encoding (see the JPEG section in the Supported File
                    Formats section below for more information).
                    Quality may vary between 1 and 100.  The default is 32.
                    The higher the number the higher the quality of the
                    image and the lower the compression ratio.  Quality
                    factors below 10 will produce images with significant
                    loss of quality.
                    Since JPEG compression was designed for use with
                    continuous tone images (such as produced by a scanner
                    or digitizer), poor results can be expected when
                    compressing line drawings.  Alchemy will not compress
                    files which have less than 32 colours in them unless
                    you explicitly override this by using the -O option.

               -k   Generate a PBM/PGM/PPM file.

               -l   Generate a paLette file.

               -m   Generate a Macintosh pict file.

               -n   Generate an SilicoN Graphics Image file

               -p   Generate a Pcx file.

               -P   Generate a PCL file.

               -r   Generate a Raw file.

               -s   Generate a Sun raster file.

               -t compressionType
                    Generate a Tiff file.  Optionally specify the TIFF
                    compression type used to store the file.
                    Compression types supported are:
                         0:None
                         1:LZW
                         2:PackBits
                         3:Group III Fax
                         4:Group IV Fax
                         9:PICIO
                         10:SGI RLE
                    The default is LZW Compression.






   Image Alchemy v1.4    Copyright (c) 1990-91 Handmade Software Inc.    Page 6




               -w compressionType
                    Generate a Windows BMP file.  Optionally specify the
                    BMP compression type used to store the file.
                    Compression types supported are:
                         0:None
                         1:RLE
                    The default is None.


          Palette Options:

               -24  Specify that the output file should be 24 bit (true
                    colour).  This is the default for JPEG files (which
                    must be 24 bit) and is not allowed for GIF and PCX
                    files (which must be paletted).  The other file
                    formats, which may be either 24 or 8 bit, default to 24
                    bit if the input file is 24 bit (certain file formats
                    may only be 8 bits if the images are grey scale, in
                    that case Alchemy will automatically switch to true
                    colour for output).

               -8   Specify that the output file should be paletted (up to
                    8 bits).  This is the default for GIF and PCX files and
                    is not allowed for JPEG files.  The actual number of
                    bits is determined by the -c option (below).  If the
                    input file is true colour the output file will be
                    quantized and dithered (see the -c and -d options
                    below).

               -b   Specify that the output file should be grayscale.  If
                    the input is paletted or a -8 is specified, -c can be
                    used to specify the number of gray levels.

               -c colours
                    Specify the number of colours for the output file.
                    Only applicable for paletted files (see -8, above).
                    The number of colours may be between 2 and 256.
                    If the input file has a larger number of colours than
                    specified for the output file, the image will be
                    quantized using Heckbert's median cut algorithm and
                    dithered (see -d, below).
                    Converting an image with a large number of colours to a
                    small number of colours (less than 8) may give poor
                    results.
                    For further information on Heckbert's median cut
                    algorithm see the Colour and Dithering section below.








   Image Alchemy v1.4    Copyright (c) 1990-91 Handmade Software Inc.    Page 7




               -d ditherType
                    Specifies the type of dithering, if any, to apply to
                    the image.
                    DitherType can be:
                         0:None
                         1:Floyd-Steinberg
                         2:Stucki
                         3:Jarvis, Judice, & Ninke
                    The default is Floyd-Steinberg.
                    Floyd-Steinberg is the fastest (except for no
                    dithering) and usually produces the best results.
                    Stucki and Jarvis, Judice, & Ninke both tend to cause
                    an image to appear more grainy on low resolution output
                    devices (such as CRTs).  However they produce better
                    results than Floyd-Steinberg on high-resolution low
                    colour devices such as laser printers.
                    This option only has an effect if the number of colours
                    is being reduced or the image is being remapped to a
                    new palette.  Dithering is used to reduce colour
                    banding in an image caused by the palette not having a
                    perfect match for every colour in the image.  However,
                    dithering does take time and can cause the image to
                    look grainy, so it can be disabled.
                    For further information on dithering see the Colour and
                    Dithering section below.

               -E   Convert image for best possible quality viewing using
                    an EGA board and monitor.  This option reduces the
                    palette resolution to 2 bits and automatically
                    specifies the following:  -8 -c16 -z0 -z1 -z0.
                    The -c16 option can be overridden by using an explicit
                    -cn option (but n has to less than 16).

               -f filename
                    Match the output to a palette read from a file.  The
                    input image will be remapped to use the palette found
                    in the specified filename.  This can be useful if you
                    are combining several images into a collage or want to
                    match an image to a pre-existing palette.  The
                    resulting image will be dithered (unless you specify no
                    dithering by using the -d option).

               -F filename
                    False colour an image using the palette from a file.
                    The input image will be changed to use the palette
                    found in the specified filename but no attempt at
                    picking the best match will be done.  This feature can
                    be used to add false colour to monochrome images.  The
                    output file is not dithered.  Only applicable to
                    paletted input files.




   Image Alchemy v1.4    Copyright (c) 1990-91 Handmade Software Inc.    Page 8




               -u   Use a Uniform Palette.  Instead of using the Heckbert
                    median cut algorithm to generate a palette for the
                    image use a palette with entries which are evenly
                    distributed in the RGB colour cube (actually the cube
                    is distorted because the human eye is not equally
                    sensitive to red, green, and blue).  The advantage of
                    using a uniform palette is that it's fast because a
                    custom palette need not be generated.  However, this is
                    at the expense of image quality since the palette isn't
                    generated based on image content.  When just viewing a
                    true colour image on a paletted display a uniform
                    palette is used.
                    The -c option can be used in conjunction with -u to
                    specify the size of the uniform palette; in that case
                    Image Alchemy will generate a palette with not more
                    than the specified number of colours (but not less than
                    8).  The palette size will not necessarily match the
                    specified size, as the actual size must be the product
                    of three integers, and Alchemy will attempt to pick
                    integers that roughly correspond to the sensitivity of
                    the human eye to red, green, and blue (30%, 59%, and
                    11%).

               -z sortType (first usage)
                    Sort the image palette.  This option only has an effect
                    if the palette is being generated by Image Alchemy
                    using Heckbert's median cut algorithm.  SortType can
                    be:
                         0:None
                         1:popularity
                         2:luminance (white to black)
                         3:rgb
                         4:luminance (black to white)
                    The default is None.
                    See below for an example of the -z option.

               -z selectionType (second usage)
                    If you specify a Palette sort parameter you may also
                    specify a palette selection parameter.  SelectionType
                    can be:
                         0:mean
                         1:median
                         2:corner
                    The default is mean.
                    See the Colour and Dithering section below for an
                    explanation of these choices.








   Image Alchemy v1.4    Copyright (c) 1990-91 Handmade Software Inc.    Page 9




               -z swapType (third usage)
                    If you specify both a Palette sort parameter and a
                    Palette selection parameter you may also specify a
                    palette swap parameter.  SwapType can be:
                         0:None
                         1:IBM (colour 0 is black, 7 is white)
                         2:Macintosh (colour 0 is white, 255 is black)
                         3:Sun (colour 0 is white, 1 is black)
                    The default is based on the file type being written out
                    (IBM for Gif, Macintosh for Mac PICT, Sun for Sun
                    Raster, and None for all others).

                    Example:  for the -z option(s):
                         -z4 -z0 -z3  :sort colours by luminance, use the
                    mean of the Heckbert box for the colour, and move the
                    colours around so that the lightest colour is colour 0
                    and the darkest colour is colour 1.

                    Note that it is not possible to specify a swapType
                    without first specifying both a sortType and a
                    selectionType.  See the Colour and Dithering section
                    below for more information.
































   Image Alchemy v1.4    Copyright (c) 1990-91 Handmade Software Inc.    Page 10




          Misc Options:

               -D aspectRatio
                    Specify aspect ratio for the output image.  The aspect
                    ratio of an image is the ratio of the width of a single
                    pixel to the height of a single pixel.  This option
                    lets you specify this ratio when writing a file or
                    displaying an image (the only file types which support
                    aspect ratio are JPEG, TIFF, Raw, Mac PICT, ILBM, and
                    Targa; specifying this option when writing out other
                    files will have no effect).  Ordinarily aspect ratio is
                    specified as two numbers separated by a colon, for
                    example 1:1 or 1:1.2.  However to simplify the user
                    interface Alchemy expects a single number which is the
                    percentage of the width of a pixel to its height (so to
                    specify 1:1.2 use -D 83, since 100/1.2 is 83).

                    Example: if you are converting a 640x350 IBM EGA PCX
                    image (which has an aspect ratio of 35:48) to a TIFF
                    image you can say -D 73 (73 is 100/48*35) and the TIFF
                    image will have the correct aspect ratio and an
                    intelligent TIFF reader will make use of the
                    information.  Alchemy attempts to preserve aspect ratio
                    whenever possible, but since so few file formats have
                    aspect ratio information this hardly ever happens.

                    This option can also be used when displaying an image
                    on an IBM PC.  See the Display options section below
                    for more information.


               -D dotsPerInchX -D dotsPerInchY
                    Specify image resolution in dots per inch.  You must
                    specify both dotsPerInchX and dotsPerInchY, even if
                    they are the same.  This option is ignored when writing
                    a file format which does not have image resolution (the
                    only have formats which include image resolution are
                    JPEG, Raw, TIFF, and Mac PICT).  Reasonable values to
                    use for dotsPerInch include:  72 (the resolution of a
                    13 inch monitor display 640x480) and 300 (the
                    resolution of a laser printer).  Alchemy will preserve
                    this information when converting files whenever
                    possible.

                    Note that it is not possible to specify both an aspect
                    ratio and a dots per inch value for an image.  This is
                    because specifying a dots per inch value automatically
                    implies an aspect ratio.  And in fact there are no file
                    formats which support independent aspect ratio and dots
                    per inch values.




   Image Alchemy v1.4    Copyright (c) 1990-91 Handmade Software Inc.    Page 11




               -o   Overwrite output file if it exists.  Image Alchemy will
                    not overwrite an existing file unless the -o option is
                    specified.

               -O   Override JPEG compression warning.  See the -j option
                    above for information.

               -q   Apply Smoothing when decompressing a JPEG image.
                    Because JPEG compression works on 8x8 pixel blocks
                    there tend to be discontinuities at the edges of these
                    blocks producing block artifacts.  Smoothing attempts
                    to reduce these artifacts.  Smoothing is really only
                    necessary at very low quality settings (Q less than
                    10);  even then the effects are not particularly
                    significant.

               -x   Display image statistics.  Displays image type, size,
                    number of colours, aspect ratio, and compression ratio.
                    Can not be combined with other options.

               -X pixels
                    Change the horizontal dimension of the image to the
                    specified number of pixels.  Currently Alchemy does
                    simple pixel replication or elimination.  Future
                    versions will allow more complex types of scaling in
                    both dimensions.

               -Y pixels
                    Change the vertical dimension of the image to the
                    specified number of pixels.  Currently Alchemy does
                    simple pixel replication or elimination.  Future
                    versions will allow more complex type of scaling.






















   Image Alchemy v1.4    Copyright (c) 1990-91 Handmade Software Inc.    Page 12




          Display options (IBM PC only):

          In addition to the file conversion options listed above Image
          Alchemy can display images on a VGA or 8514/A equipped IBM PC.

          The current version of Image Alchemy supports 320x200x256,
          640x400x256, and 640x480x256 display modes for VGA and
          640x480x256, 1024x768x256, and 1280x1024x256 display modes for
          8514/A (the exact resolutions supported depend on the model board
          installed).

          Because of various incompatibilities between different VGA boards
          640x400x256 and/or 640x480x256 mode is not supported on all
          boards and has not been tested on all boards that are supported.
          The 320x200x256 mode is a standard VGA IBM mode and should work
          on all VGA boards.  VGA boards which have been tested for the the
          higher resolution modes include Paradise, Tseng Labs 3000 & 4000,
          Video 7, Trident, and Everex chipset based VGA Boards.  Support
          for others is included but has not been tested and may be
          accessed through the -vv option (see below).

          Image Alchemy requires AI to be installed to use 8514/A displays
          which aren't based on the Western Digital chipset (Alchemy should
          also be able to display on AI compatible boards which are not
          8514/A (such as 340x0 based boards), but this has not been
          tested).  For Western Digital based 8514/A boards, no driver is
          required.

          Alchemy checks for a display board in the following order:
          Western Digital 8514/A, AI based 8514/A, extended VGA, standard
          VGA.  Alchemy automatically uses the lowest resolution mode which
          will display the entire picture.

          The image will be centered in the display (for images which are
          larger than the display Alchemy will center the display in the
          picture).



               -v horizontalResolution
                    View file using high resolution mode (640x400x256 or
                    640x480x256 for VGA, up to 1280x1024x256 for 8514/A).
                    If displaying on a Western Digital chipset 8514/A an
                    optional parameter may follow the -v command.  This
                    parameter specifies horizontal resolution and may be
                    either 640, 1024, or 1280.  The default is to use the
                    lowest resolution which can fit the entire image.  If
                    the image is true colour, a uniform palette will be
                    used and the image will be dithered (dithering may be
                    disabled by use of the -d option, see above).  See the
                    Colour and Dithering section below.



   Image Alchemy v1.4    Copyright (c) 1990-91 Handmade Software Inc.    Page 13




               -vv  Force view.  If Image Alchemy can identify the VGA
                    board you have installed and has support for it, but
                    has not been tested with it, you will be given the
                    option of rerunning the program with the -vv option
                    instead of the -v option.  This will force viewing of
                    the file.
                    Please contact Handmade Software if you use this option
                    and viewing works correctly on your VGA board so that
                    we can add it to the list of tested boards.

               -V   View using 320x200x256 mode.  This is a standard VGA
                    mode which works on all VGA boards (including those
                    built-in to PS/2 computers).  This command is most
                    useful combined with the -V option below.

               -V   Scale image to fit on monitor and correct aspect ratio.
                    After specifying the view type, -v, -vv, or -V, you may
                    also specify that the image should be scaled to fit on
                    the display by using a second -V option (which means
                    you end up typing -v -V, -vv -V, or -V -V).

                    This command will scale the image and correct the
                    aspect ratio of the image by removing rows and/or
                    columns from the image.

                    Note that this option can also be useful for displaying
                    images which are not larger than the screen but which
                    have an aspect ratio different than the display.

                    Also note that Alchemy assumes that the aspect ratio of
                    a display pixel is 1:1 when in 640x480 mode and 1:1.2
                    when in 640x400 mode or 320x200 mode.  Furthermore
                    Alchemy assumes that the aspect ratio of pixels in
                    640x400 and 320x200 images is 1:1.2 and the aspect
                    ratio of pixels in 640x350 images is 35:48.  You can
                    override any of these assumptions with the -D option
                    (for a further discussion of aspect ratio see the -D
                    command, above).

                    Don't worry if this is confusing;  in practice Alchemy
                    deals with everything automatically if you use the
                    second -V option (there is however a problem with
                    display 320x400 IFF and HAM files, see the Answers to
                    Frequently Asked Questions section below for more
                    information).









   Image Alchemy v1.4    Copyright (c) 1990-91 Handmade Software Inc.    Page 14




                                      Examples


          To convert the JPEG file sample.jpg to a Targa file called
          sample.tga use the following command:

          alchemy -a sample.jpg


          To convert the 24 bit Targa file sample.tga to a 256 colour Gif
          file called new.gif:

          alchemy -g sample.tga new.gif


          To convert the 256 colour Gif file, new.gif, to a 64 colour PCX
          file called new.pcx:

          alchemy -p -c64 new.gif


          To view the Gif file new.gif (only applicable on IBM PCs with
          appropriate VGA board):

          alchemy -v new.gif


          To convert sample.jpg to a black and white, two colour GIF file
          use a text editor to create a file called BW.PAL which contains
          the following:

          PAL
          2
          0 0 0
          255 255 255

          then:

          alchemy -g sample.jpg -f bw.pal

          (Or, you could have said alchemy -g sample.jpg -b -c2, but that
          wouldn't have demonstrated the -f option).

          To view the resulting file in 320x200x256 mode, scaling the image
          to fit the display:

          alchemy -V -V sample.gif







   Image Alchemy v1.4    Copyright (c) 1990-91 Handmade Software Inc.    Page 15




                          Details on Supported File Formats


          Image Alchemy currently has support for the image file formats
          listed below.  Where we know of restrictions or limitations they
          are listed.  If you have trouble reading in and image in one of
          the file formats we claim to support please contact us (see What
          if Image Alchemy Messes Up, below).

          Image Alchemy identifies the type of file being read by checking
          various magic numbers and other information that varies from
          format to format.  It is possible for Image Alchemy to
          incorrectly identify a file; if this happens please contact us.


          .BMP      Windows BitMaP
                    Microsoft Corporation
                    Reads and writes 1, 4, 8, and 24 bit files.  Reads and
                    writes RGB (raw), RLE4, and RLE8 files.
                    Since no Windows 3.0 software we have (including the
                    Windows 3.0 supplied utilities) can read nor write RLE4
                    or RLE8 files, writing RLE compressed files is not
                    recommended because that option has not been tested
                    (Alchemy can read RLE files that it wrote, but that
                    isn't a very significant test).


          .EPI      Encapsulated PostScript
          .EPSI     Adobe Systems Incorporated
                    Output only.
                    Writes Encapsulated Postscript files.  If the output
                    file is grayscale, it will work with any PostScript
                    device (grayscale output can be forced with the -b and
                    -8 options).  If it's truecolour, then the CMYK
                    extensions or a level 2 device is required.  For
                    paletted files, a level 2 device is always required.
                    Colour files can be forced to produce EPS files
                    requiring only the CMYK extensions by using the -24
                    option.















   Image Alchemy v1.4    Copyright (c) 1990-91 Handmade Software Inc.    Page 16




          .JPG      Handmade Software JPEG Files
                    Handmade Software, Inc.
                    Joint Photographic Experts Group (JPEG) JPEG-8-R8 draft
                    standard.
                    Reads and writes baseline JPEG with YCbCr CCIR-601
                    colour space, interleaved components, Huffman or
                    Arithmetic encoded.  Image Alchemy can read files with
                    any component subsampling up to 4x4; it always writes
                    2h:1v 1h:1v 1h:1v.  For grayscale images, it uses a
                    single component.  Image Alchemy can only recognize
                    grayscale files if the input is either paletted or 8
                    bit grayscale.  Image Alchemy Huffman encoded JPEG
                    files comply with the industry standard `JFIF'
                    interchange format.

                    Grayscale images that have been JPEG compressed will
                    decompress as paletted images (with a 256 level
                    grayscale as a palette); others will be 24 bit.

                    JPEG files can be Huffman or Arithmetic encoded.
                    Arithmetic encoding has the advantage of making the
                    file approximately 20% smaller, but has the
                    disadvantage of taking approximately 10% longer to
                    compress and decompress and the resulting file will no
                    longer be JFIF standard.


          .IFF      Interchange File Format/InterLeaved Bit Map
          .LBM      Commodore-Amiga Corp.
                    Reads 1 through 8 bit, 24 bit, and Ham images; writes 1
                    through 8 bit and 24 bit images.  If you're writing an
                    Ilbm file for use on an Amiga, you probably want to
                    write either a paletted file with 32 colours or a 24
                    bit file.  24 bit Ilbm files can then be converted to
                    one of the Amiga specific display modes with various
                    third-party utilities.


          .GIF      Graphics Interchange Format
                    CompuServe, Incorporated.
                    Reads and writes 1 bit through 8 bit GIF87A files,
                    reads 1 through 8 bit GIF89A files (discarding all but
                    the first image).  Reads both non-interleaved and
                    interleaved files;  writes non-interleaved files.










   Image Alchemy v1.4    Copyright (c) 1990-91 Handmade Software Inc.    Page 17




          .PAL      HSI Palette Files
                    Handmade Software, Inc.
                    Contain only Palette Information.
                    Useful in conjunction with the -f option (see above).
                    PAL files are ASCII files which can be edited with a
                    text editor.

                    The PAL file format:  the first line contains the
                    letters "PAL", the next line contains an integer
                    indicating the number of palette entries, the rest of
                    the file consists of lines of 3 numbers each (separated
                    by spaces), representing the red, green, and blue
                    values for each of the colours (the numbers vary
                    between 0 and 255;  0 0 0 is black, 255 255 255 is
                    white, 255 0 0 is bright red, etc.).  See the Examples
                    section above for a sample PAL file.

                    Converting a .PAL file to another image format is
                    allowed but doesn't make much sense (since there won't
                    be any image data).


          .PCL      HP Printer Command Language
                    Hewlett-Packard Company
                    Reads and writes 1 bit files (PCL files must be 1 bit,
                    black and white;  if you attempt to write out any other
                    file type Alchemy will automatically switch to that
                    mode).
                    Only pays attention to raster images in the file;
                    attempts to skip everything else.  Due to the enormous
                    number of options allowed in PCL files this option has
                    not been thoroughly tested.  See the Answers to
                    Frequently Asked Questions section below for more
                    information.


          .PCX      PC Paintbrush
                    ZSoft Corp.
                    Reads and writes 1, 4, and 8 bit images.
                    PCX format files are often written out incorrectly;
                    Alchemy attempts to figure out what is wrong and make
                    intelligent decisions (things Alchemy can deal with
                    include PCX files without palettes, files missing the
                    last line of image data, and files with illegal (and
                    incorrect) combinations of bits per pixel and planes).









   Image Alchemy v1.4    Copyright (c) 1990-91 Handmade Software Inc.    Page 18




          .PICT     Macintosh PICT format
          .PIC      Apple Computer, Inc.
                    Reads 1, 2, 4, 8, 16, and 32 bit images; writes 1, 2,
                    4, 8, and 32 bit images.
                    Only pays attention to pixMaps in the pict; attempts to
                    skip everything else.  Due to the enormous number of
                    options allowed in PICT files this option has not been
                    thoroughly tested.  See the Answers to Frequently Asked
                    Questions section below for more information.


          .PBM      Portable BitMap
          .PGM      Portable GrayMap
          .PPM      Portable PixelMap
          .PNM      Portable aNyMap
                    Jef Poskanzer's Portable BitMap Package
                    Reads and writes 1, 8 (grayscale only), and 24 bit
                    RAWBITS (binary) images.  For more information on the
                    Portable BitMap Package see the References section
                    below.


          .RAST     Sun Raster Files
          .RAS      Sun Microsystems, Inc.
                    Reads 1, 8, 24, and 32 bit images.  Writes 1, 8, and 32
                    bit images.
                    Supports Standard, BGR, RGB, and Byte Encoded (RLE)
                    files.


          .RAW      HSI Raw Files
                    Handmade Software Inc.
                    Reads and writes 8 and 24 bit images.  Used internally
                    by Image Alchemy when converting between certain
                    combinations of other formats.  Can also be explicitly
                    read and written.  If you are interested in adding HSI
                    Raw support to your software please contact us for more
                    information.


          .SGI      Silicon Graphics Image Files
                    Silicon Graphics, Inc.
                    Reads and writes 1, 8 (grayscale only), and 24 bit
                    files.  Reads Verbatim (uncompressed) and RLE files.
                    Write uncompressed files.









   Image Alchemy v1.4    Copyright (c) 1990-91 Handmade Software Inc.    Page 19




          .TGA      Targa Files
                    Truevision Corp.
                    Reads 8, 15, 16, 24, and 32 bit images, ignoring the
                    alpha channel for 32 bit images; writes 8 and 24 bit
                    images.  8 bit output files are paletted unless the
                    palette is all gray, in which case the output is a
                    grayscale file.


          .TIFF     Tagged Image File Format Files
          .TIF      Microsoft Corp. and Aldus Corp.
                    Reads 1, 4, 8, 24, and 32 bit images (ignoring the
                    alpha channel for 32 bit images); writes 1, 4, 8, and
                    24 bit images.  Can read TIFF class B, G, R, and some P
                    (those with 1, 4, or 8 bits per pixel) files.  Writes
                    class B, G, P, and R files, depending on the input file
                    and options specified.

                    1,4, and 8 bit output files are paletted unless the
                    palette is all gray, in which case the output is a
                    grayscale file.  Output compression types supported are
                    raw, LZW, PackBits, Group III fax, Group IV fax, PICIO,
                    and SGI RLE.  Input compression types supported are
                    raw, LZW, PackBits, Group III fax, Group IV fax, CCITT
                    RLE (both byte and word aligned), NeXT, Thunderscan,
                    PICIO, and SGI RLE.


          General Notes:

          Image Alchemy automatically recognizes and reads MacBinary files
          (MacBinary files are generated when you accidently leave
          MacBinary mode on when transferring a file from a Macintosh).

          Gamma, aspect ratio, and resolution values are preserved whenever
          possible.

          Colour correction tables are currently ignored.
















   Image Alchemy v1.4    Copyright (c) 1990-91 Handmade Software Inc.    Page 20




                                Colour and Dithering


          Colour images are normally stored in one of two ways: as an array
          of direct colour values (usually red, green, and blue) (referred
          to as a truecolour file in this document) or as an array of
          indices into a colourmap which contains red, green, and blue
          colour values (referred to as a paletted file in this document).
          The only reason for the existence of paletted images is that they
          take less memory, so the hardware to display them is cheaper.
          The dominance of paletted hardware is changing as the price of
          memory and the processing power it takes to update large amounts
          of memory at a reasonable speed drops (a Targa 32 board is an
          example of a truecolour board, a VGA board is an example of a
          paletted board).  However, until truecolour graphics devices
          become the norm, there's a need to convert images from truecolour
          to paletted.  This conversion is done in two steps: the first is
          to generate a palette for use by the image;  the second is to map
          the image to the new palette.

          Image Alchemy supports two methods of generating a palette.  The
          simplest and fastest method is to use a palette containing
          colours which are uniformly distributed in the RGB cube, referred
          to as a uniform palette.  This has the advantage that it's fast
          and the same palette can be used for any image; the primary
          disadvantage is that most images don't contain colours from
          everywhere in the RGB cube, so this palette wastes entries
          representing colours that aren't needed for the particular image
          being converted.

          Image Alchemy also supports Heckbert's median cut algorithm.
          This algorithm first builds a three dimensional histogram
          indicating how popular any given colour in the RGB cube is in the
          image being converted.  It then proceeds to subdivide this
          histogram cube (by dividing boxes in half) until it has created
          as many boxes as there are palette entries.  The decision as to
          where to divide a box is based on the distribution of colours
          within the box.  This algorithm attempts to create boxes which
          have approximately equal popularity in the image.  Palette
          entries are then assigned to represent each box.  There are other
          methods of generating a palette from an image, but Heckbert's
          algorithm is generally regarded as the best tradeoff between
          speed and quality.











   Image Alchemy v1.4    Copyright (c) 1990-91 Handmade Software Inc.    Page 21




          You can change the method used to select a colour for each box by
          use of the -z options.  The default method is to use the mean of
          all the colours in the box (this gives the mathematically correct
          result).  However for some images slightly better results can be
          obtained by using the center of the box (without regard to where
          the pixels are in the box).  For images with a very small number
          of different colours (less than 16) better results can be
          obtained by using a corner of the box (the boxes tend to be large
          when reducing an image to a small number of colours; picking a
          colour near the center of the box will give you muddy colours, by
          using the corner of the box you get more saturated colours).

          The next step is to map the image to the new palette; this is
          where dithering becomes important.  The simplest approach is to
          map every colour in the original image to the palette entry which
          is closest to it (which Image Alchemy does if you specify no
          dithering).  However, since the palette entries generally
          represent several different colours in the original image, this
          results in colour banding (where areas of smooth colour changes
          in the original become areas of one solid colour in the paletted
          version).  This can be alleviated by dithering (or modulating)
          the image data such that any given pixel may not be mapped to
          it's closest palette entry, but the average over some area of the
          image will be closer to the correct colour than it would
          otherwise be.  Image Alchemy uses a class of algorithms called
          "error-diffusion" to do dithering.  These algorithms work by
          using the closest palette entry to a colour and then distributing
          the error (the difference between the desired colour and the
          chosen palette entry) to the pixels below and to the right of the
          current pixel.  This process is repeated for every pixel in the
          image, using the colour values which have been modified due to
          the error from previous pixels.

          For more information on Heckbert median cut and dithering see the
          appropriate reference listed in the References section below.



















   Image Alchemy v1.4    Copyright (c) 1990-91 Handmade Software Inc.    Page 22




                              What is JPEG Compression?


          J.P.E.G. stands for the "Joint Photographic Experts Group".  This
          is a group of experts who defined a standard compression scheme
          for still images, commonly called JPEG Compression.  Currently
          the standard is still in draft form.  The standard will hopefully
          be finalized in 1991.

          JPEG Compression consists of a series of reasonably complex
          mathematical operations.  These include colour space conversion,
          Discrete Cosine Transform, quantization, and Huffman or
          Arithmetic encoding.  After these steps you end up with an image
          which takes fewer bits to store than you started out with.

          However, when you decompress a JPEG compressed image you end up
          with an image that is not quite the same as the original image
          (which is why JPEG Compression is referred to as "lossy").  You
          might well ask why anyone would want to compress an image using a
          lossy technique?  It turns out that lossy compression ratios are
          much better than lossless compression ratios and the loss is
          generally very small.  And, in fact, every operation of
          converting an image is lossy (the original photographic or
          electronic process which captured the image was lossy, scanning
          or digitizing the image was lossy, displaying the image on a
          monitor is lossy, and printing the image is lossy).

          JPEG compression typically involves the following steps:

          1.   The image is converted to a colourspace with separate
               luminance and chrominance (Image Alchemy uses CCIR-601
               YCbCr).  This is done because the luminance information (Y)
               is far more important to the human eye than the chrominance
               information (Cb and Cr); by separating them it's possible to
               compress the chrominance information more than the luminance
               information.  This step is not specified in the JPEG draft
               (it doesn't discuss colourspace at all), but is standard
               practice.

          2.   The luminance and chrominance information are seperately
               transformed to the frequency domain using a discrete cosine
               transform acting on 8x8 pixel blocks (the chrominance
               information may be subsampled first).

          3.   The transformed data is quantized (which simply means some
               information is thrown away).  The samples representing
               higher frequencies are generally quantized more than those
               representing low frequencies.






   Image Alchemy v1.4    Copyright (c) 1990-91 Handmade Software Inc.    Page 23




          4.   This quantized data is then compressed using an entropy
               encoder (Huffman and Arithmetic coding are allowed by the
               draft JPEG standard; only Huffman is allowed by the JFIF
               standard).

          This data then corresponds the JPEG Interchange Format and is
          ready to be stored in a file.  However the JPEG Interchange
          Format does not include enough information to actually be able to
          convert the file back to an image.  Specifically the colourspace
          used and the aspect ratio or the resolution of the image are not
          included.  Until recently there was no standard way of putting
          this information in a JPEG file.  On March 1, 1991
          representatives of several JPEG hardware and software developers
          (including C-Cube, Radius, NeXT, Storm Tech., the PD JPEG group,
          Sun, and Handmade Software) got together at C-Cube and
          established the JPEG File Interchange Format (JFIF).  If you
          would like more information on the JFIF standard please contact
          us.


          If you are interested in getting a copy of the the current draft
          JPEG standard contact:
               X3 Secretariat
               Computer and Business Equipment Manufacturers Institute
               311 First Street NW, Suite 500
               Washington, DC  20001-2178

               The last time we talked with them the charge was $8.00,
               including shipping.

























   Image Alchemy v1.4    Copyright (c) 1990-91 Handmade Software Inc.    Page 24




                        Answers to Freqently Asked Questions


          Q:   When I convert a gray-scale Gif file to a JPEG file and then
               back to a Gif file the final Gif file is twice the size of
               the original.  Why is this?

          A:   The input Gif file was probably a 16 or 32 colour gray scale
               file.  When you converted it to a JPEG file the number of
               colours in the file was lost (JPEG gray scale files are
               always 256 colour).  When the JPEG file was converted back
               to a Gif file Alchemy assumed you wanted 256 colours in the
               file.  And a 256 colour Gif file is bigger than a 16 colour
               Gif file (because of the way Gif compression works).  To
               prevent this you can use a -c32 option in the command line;
               this forces Image Alchemy to use that many colours for the
               output file.


          Q:   Why can't PHIPS read the Targa file I wrote with Image
               Alchemy?

          A:   Some software which reads Targa files can not handle
               compressed files.  By using -a0 instead of just -a, Image
               Alchemy will write out an uncompressed Targa file.  In
               addition, some software can read true colour Targa files,
               but can not read paletted or gray scale files.  Image
               Alchemy can be forced to write out a true colour file by
               using the -24 option.


          Q:   Why is decompressing or compressing a JPEG image so slow?

          A:   There are a large number of calculations that have to be
               done during JPEG compression.  This is an inherent
               limitation of JPEG compression.  Image Alchemy has been
               optimized quite a bit to reduce the number of calculations,
               and we are working to further reduce the number of
               calculations.  If you are transferring files over modems or
               storing them on slow media (tape) the compression times are
               usually more than made up for by the decrease in
               transmission or retrieval times.












   Image Alchemy v1.4    Copyright (c) 1990-91 Handmade Software Inc.    Page 25




          Q:   Why can't my favorite desktop publishing package read the
               TIFF file I wrote with Image Alchemy?

          A:   TIFF is an extremely versatile standard; it can handle
               anything from 1 bit images to full colour images with an
               alpha channel and TIFF allows many different types of
               compression.  Unfortunately this versatility means that it's
               difficult for a single piece of software to be able to read
               in every valid TIFF file.

               If the software specifies the classes of TIFF it can read,
               you can force Alchemy to write out a specific TIFF class by
               using the following options:
                  class B: -8 -b -c2 -t2     (preferred if input is
                       bilevel)
                  class G: -8 -b -t1         (preferred if input is
                       grayscale)
                  class P: -8 -t1            (preferred if input is
                       paletted)
                  class R: -24 -t1           (preferred if input is true
                       colour)

               If the supported classes are not specified experiment with
               various combinations of -24, -8, -b, and -cn.  In this case
               it is usually best to use no compression (-t0) while
               experimenting with the other options, as many TIFF readers
               have difficulty with compressed files.  When you find a set
               of options that works, then you can try various compression
               modes to save space.  Be aware that using -b will force the
               output file to be gray scale and you will lose all the
               colour information in the file (most DTP programs only have
               support for gray scale TIFF files).

               You may also have to use the -Dn -Dn option to specify the
               resolution of the image (this is especially true when
               converting from a file format which does not have a value
               for image resolution).  You can generally tell if this is
               necessary because the program you are using to read in the
               TIFF file will claim that the file is unreasonably large or
               small.  Generally, if you are using a 300 DPI Laser Printer
               you want to make the TIFF file 300DPIx300DPI (-D 300 -D
               300).

               If you would like further information specific to using
               Image Alchemy with your word processor or desktop publishing
               program please contact us; we will be maintaining a list of
               how to make Alchemy work with other software packages.
               Similarly if you figure out how to import files into a
               specific package let us know and we will add your tips to
               our documentation.




   Image Alchemy v1.4    Copyright (c) 1990-91 Handmade Software Inc.    Page 26




          Q:   When I convert a 32 bit Targa file to a PCX file and then to
               a JPEG file it doesn't look nearly as good as if I convert
               the Targa File directly to the JPEG file.  What can I do to
               maintain high quality in JPEG compressed files?

          A:   When the Targa file was converted to the PCX file Image
               Alchemy had to reduce the number of colours in the file (the
               original Targa File had up to 16 Million Colours, PCX files
               are limited to 256 colours).  This step is known as colour
               quantization (Image Alchemy uses the Heckbert Median Cut
               method for quantization, see the Colour and Dithering
               section above).  The difficulty with colour quantization is
               that it leaves artifacts known as colour banding.  To reduce
               this phenomenon Image Alchemy dithers the image (you can see
               the effect of colour banding by turning off dithering by
               using the -d option).  Unfortunately a dithered image does
               not JPEG compress very well (dithering adds a lot of high-
               frequency information to an image; JPEG compression attempts
               to remove much of that information).  In addition JPEG
               images are always continuous colour images, so when the JPEG
               file is decompressed it has to be colour quantized and
               dithered again.  Dithering a previously dithered image
               reduces the quality even more.  The solution is to use the
               best starting quality you can for JPEG compression, ideally
               a continuous tone image.  The compressed image size will be
               smaller than if you had started with a paletted image and
               the quality will be better.


          Q:   When I view a JPEG compressed image on my VGA board the
               quality isn't nearly as good as when I first convert it to a
               Gif file and then view it.  Why is this?

          A:   To save time Alchemy automatically uses a uniform palette
               when you are just viewing the image.  When converting to a
               different file format Alchemy does Heckbert quantization to
               generate a palette.  The difference in image quality is the
               difference between using a uniform palette and an optimum
               palette.  See the Colour and Dithering section above for
               more information on palette generation.














   Image Alchemy v1.4    Copyright (c) 1990-91 Handmade Software Inc.    Page 27




          Q:   I've converted a Mac PICT file to a Gif file, but the Gif
               file is missing some or all of the information that was in
               the PICT file.  What happened to it?

          A:   PICT files are a combination of drawing commands (such as
               lines, rectangles, and circles) and raster areas (called
               pixMaps).  Alchemy can only read the raster portion of the
               files.  Programs such as MacDraw and MacDraft write out
               files with drawing commands, programs such as MacPaint write
               out files which are entirely raster areas (pixMaps), and
               some programs, such as SuperPaint can write out files which
               are either or a combination of both.  If you are using such
               a program check the documentation on how to write out files
               in "paint" mode.


          Q:   I've converted an HP PCL file to a Gif file, but the Gif
               file is missing some or all of the information that was in
               the PCL file.  What happened to it?

          A:   PCL files have the same problem as PICT files (see above);
               they are a combination of drawing commands (such as lines
               and rectangles) and raster areas (called rasters) and
               Alchemy can only convert the raster areas in PCL files.  In
               addition they contain a lot of font and text information,
               which is also lost.  Unfortunately there isn't any general
               way to preserve this data.

               One way which works under Microsoft Windows 3.0 is to
               install Adobe Type Manager (ATM).  ATM automatically
               intercepts any text commands and converts them to rasters.
               And in fact, the standard Windows 3.0 HP PCL driver only
               generates rasters.  So the file will appear in its entirety
               when converted by Alchemy.  Contact us if you want further
               information on using Alchemy with Windows 3.0.


          Q:   I keep getting "Out of Memory trying to ..." messages.
               Help!

          A:   Image Alchemy is running of of memory.  First attempt to
               maximize the amount of memory available by removing as may
               TSRs as you can.  If this doesn't help please contact us
               with the following information: your computer configuration
               (amount of available memory, size of hard disk), operating
               system version, and what you are trying to do (input file
               information (size of image and type of file) and options
               specified).  Alchemy can generally convert images as large
               as 2000 pixels across and an infinite number of pixels down.
               However there are certain conversions which require more
               memory than others.



   Image Alchemy v1.4    Copyright (c) 1990-91 Handmade Software Inc.    Page 28





          Q:   Why can't Image Alchemy read in JPEG files produced by
               Kodak's ColorSqueeze (or Sun's VFCtool)?

          A:   The JPEG standard is still in draft form.  Until it is a
               mature standard various manufacturer's will implement
               different versions of it.  As of March 1, 1991 Image Alchemy
               currently supports the JFIF format and should work with any
               other JPEG software which also claims JFIF compatibility.
               If other software you are using claims to support the JFIF
               format and you are having trouble please contact us.  If the
               other software does not support JFIF contact the
               manufacturer and tell them they should send you an update
               which supports JFIF (you can tell them to contact us if they
               need a copy of the JFIF standard).


          Q:   I told Alchemy to convert a PCX file to an 8 bit Gif file
               (using the -8 option).  Yet when I get statistics on the
               file (using -x) Alchemy reports the file has 16 colours?

          A:   Alchemy will always store the file using the smallest bits-
               per-pixels allowable for the given image (this results in
               the smallest possible file).  In this case the input file
               only had 16 colours in it.

               Things can get more unpredictable with formats such as Sun
               Raster (which require 1 bit files to be black and white) and
               SGI (which requires 8 bit files to be grayscale).  In these
               cases Alchemy will always do the best it can (giving you a
               warning message if it does something which may surprise you
               later).






















   Image Alchemy v1.4    Copyright (c) 1990-91 Handmade Software Inc.    Page 29




          Q:   I converted a PCX file with 16 colours to a 16 shade gray
               TIFF file using the -b and -p options.  The 16 colour PCX
               file had some shades of gray in it which were changed in the
               TIFF file.  How can I prevent this?

          A:   The short answer is:  you can't.  The long answer is:  there
               is a work around.

               The problem is that gray-scale TIFF files have a uniformly
               spaced gray palette (this is required as part of the TIFF
               standard).  So if you create a 16 shade gray TIFF file it
               will have the following shades of gray in it: 0, 17, 34, 51,
               68, 85, ..., 255.  However the 16 colour PCX file you
               started with probably didn't have those exact colours in it
               (for example, PCX files written out by Windows 3.0 Paint
               have shades of gray which correspond to 0, 128, 192, and
               255).  So Alchemy did the best it could and matched the
               input colours to the output colours.

               The solution is to tell Alchemy to write out a 256 colour
               gray scale TIFF file (which you do by adding a -c256 to the
               -b and -t options).  This file still has a uniform gray
               palette; but that palette now contains every colour:  1, 2,
               3, 4, ..., 255.  So Alchemy can map the colours 128 and 192
               to their exact match.  This does have the disadvantage of
               making the resulting 256 colour TIFF file twice as large as
               the 16 colour TIFF file; but this is the only way to
               guarantee that Alchemy can find an exact match for all the
               shades of gray in the input file.


          Q:   Why do you only allow specifying image resolution in Dots
               Per Inch?  Don't you realize that most of the world is
               metric?

          A:   Yes, we do realize that the entire world, with the exception
               of the United States and Great Britain, claims to use the
               metric system exclusively (and Great Britain will presumably
               change in 1992).  However this isn't true.  A laser printer
               manufactured in Japan is still 300 dots per inch (not
               11.811... dots per mm) and a 19 inch monitor sold in Europe
               is called a 19 inch monitor (actually a 19 inch monitor is
               called a 20 inch monitor in Europe, they measure the total
               picture tube diagonal, not just the viewing area).  And this
               even applies to non high-tech things:  the wheels on my
               German car are 16 inches in diameter (though the tires I buy
               for it are 225 mm wide, even in the United States).







   Image Alchemy v1.4    Copyright (c) 1990-91 Handmade Software Inc.    Page 30




          Q:   I am using Alchemy to display a 320x400 IFF image created by
               an Amiga.  When I use just the -v option the image comes out
               tall and skinny.  When I use the -v -V option, which is
               supposed to correct the aspect ratio, instead of things
               getting better they get worse (the image is even skinnier).
               What's going on?

          A:   As near as we can tell Amiga software has a different idea
               of what aspect ratio is than the rest of the world.

               For displays aspect ratio is defined as the ratio of the
               width of a single pixel to the height of a single pixel.  So
               if you have square pixels (which you do on a standard
               monitor in 640x480 mode) the aspect ratio is 1 to 1 (usually
               written as 1:1).  When you change display modes you are
               generally not changing the height and width of the total
               display area; what is changing is the width and height of
               each pixel, so the aspect ratio changes.  For example, a
               640x400 display has an aspect ratio of 1:1.2 (that means
               each pixel is 1.2 times as tall as it is wide (which makes
               sense since 480/400 equals 1.2)).  A 640x200 display
               (remember IBM CGA graphics mode?) has an aspect ratio of
               1:2.4 (which is a pretty extreme aspect ratio).  Now this is
               where it gets interesting.

               The aspect ratio number stored in Amiga IFF files for
               320x400 images is 1:1.1, which means the pixels are 1.1
               times as tall as they are wide, so therefore the actual
               image should be the equivalent of a 320x440 image with
               square pixels.  And this is what Alchemy will attempt to
               display when you use the second -V (actually Alchemy never
               makes any dimension larger, so the actual image Alchemy
               displays is 291x400, which is the same ratio as 320x440).
               However this is obviously wrong, as you can tell when you
               actually look at an image.  As near as we can tell the
               actual aspect ratio of these images is 5:3 (the math we used
               to come up with this number is 640/320:480/400).  And in
               fact if you tell Alchemy to override the aspect ratio by
               using a -D 167 option (167 because 5/3*100 is 166.6666) the
               image displays correctly.  Why Amigas create images which
               claim they are 1:1.1 remains a mystery.


          Q:   Do you give multiple copy discounts?  Do you have site
               licenses?  Are you interested in licensing the source code?

          A:   Yes.  Yes.  Yes.  Contact us for more information.







   Image Alchemy v1.4    Copyright (c) 1990-91 Handmade Software Inc.    Page 31




                                   Version History


                                    v1.4 03/18/91

                     Released for Sun SPARC, Sun 3, and IBM PC.

          Format changes:
          Added Arithmetic coding and decoding for JPEG compression.
          Added 1 bit PCX file support.
          Added new compression types to Targa.
          Added PBM/PGM/PPM support.
          Added GIF89A support for reading.
          Added SGI support.
          Added Windows BMP support.
          Added writing Group III, Group IV, PICIO, and SGI RLE Tiff
          compression types.
          Added Encapsulated PostScript output.
          Added HP PCL support.

          Display option changes:
          Added support for Video 7, Trident, Tseng 4000, IBM 8514/A
          display boards.
          Added 320x200x256 display mode.
          Added image scaling during display (which allows display of the
          entire image on the screen and preserves aspect ratio).
          Center images on screen during displaying.
          During display the screen is now cleared to the darkest colour.

          Misc changes:
          Added image scaling
          Added conversion to monochrome images.
          Preserve and allow specification of aspect ratio or dots per
          inch.
          Added false colour palette conversion.
          Added optimized EGA image generation support.
          Added support for very large images.
          Added palette sorting, paletted swapping, and palette selection
          parameters.
          Added Stucki and Jarvis, Judice, & Ninke Dithering.

          Fixed Bugs:
          Writing certain 1 bit Sun Raster files
          Reading incorrectly written PCX files
          Reading 24 bit RLE compressed Sun Raster files
          Reading incorrectly written ILBM files.








   Image Alchemy v1.4    Copyright (c) 1990-91 Handmade Software Inc.    Page 32




                                    v1.3 02/05/91

                         Released for Sun SPARC and IBM PC.

          Added checking for supported VGA boards, warning if board is
          recognized but not supported.

          Fixed bug with reading and writing 8 bit Sun Raster files which
          have an odd width.

          Temporary files are now removed when program exits because of an
          error.

          Added support for reading Sun Run-Length-Encoded (RLE) files.

          Added reading support for interleaved GIF files.

          Added 8 bit RAW files.

          Added optional smoothing on JPEG reading.

          Added support for any colour component subsampling on JPEG
          reading.

          Targa files are now written bottom-up to make other Targa
          software happy.

          Added palette matching and PAL files.

          Made memory use more efficient (requiring less virtual memory on
          Suns and less overlay swapping on PCs).

          Numerous miscellaneous performance improvements, (dramatic for
          some conversions; hardly noticeable for others).


                                    v1.2 01/16/91

                        First release for Sun SPARC systems.

          Fixed several minor bugs (primarily aesthetic).

          Made PCX file identifying and reading more robust.


                                    v1.1 01/14/91

                              First release for MS-DOS.






   Image Alchemy v1.4    Copyright (c) 1990-91 Handmade Software Inc.    Page 33




                                 Coming Attractions


          A better user's manual (yeah!).

          A Macintosh Version (the Mac version is working except for the
          GUI (graphical user interface].

          Support for GUI (Windows 3.0 for the IBM and OpenLook 2.0 for
          Suns).

          Optimum Huffman table generation for JPEG writing.

          Support for TIFF files containing JPEG compressed data.

          Faster JPEG File reading and writing.

          Emphasizing flesh tones during palette generation (for both
          Uniform palettes and Heckbert generated palettes).

          Gamma, Brightness, and Contrast Adjustment.

          Wildcards for input filenames.

          Display of images on Targa boards on IBM PCs.

          Use of Expanded and/or Extended memory on IBM PCs for faster
          operation.

          Display of large images with scrolling (especially on PCs).

          Image Resizing (scaling and/or cropping).

          Binary versions for other machines (we have written what we
          consider very transportable code (the same source code compiles
          on IBM PCs, Macs, and Suns), the biggest limitation on generating
          new binaries is access to machines, if you can provide help in
          this regard please contact us).

          New file formats, including:
               Utah RLE
               QDV
               MTV
               BPX










   Image Alchemy v1.4    Copyright (c) 1990-91 Handmade Software Inc.    Page 34




                          What if Image Alchemy Messes Up?


          We have made every effort to insure that Image Alchemy can read
          all files in its supported formats.  However, because of poorly
          written standards and non-adherence to standards there are
          undoubtedly certain files that Image Alchemy does not read
          correctly.

          If you come across any files which Image Alchemy has trouble with
          please contact us with as much of the following information as
          you have:  version of Image Alchemy you are using, type of file,
          type of computer which generated it, name and version of software
          which wrote the file, size of image, and the number of colours in
          image.  We may ask you to send us the file so that we can figure
          out what went wrong.  If you send us a file we will attempt to
          modify Image Alchemy so that it can read the file.  And if by
          some miracle we manage to get it to work, we will send you an
          updated copy of Image Alchemy.

          Similarly, if any files that Image Alchemy writes can not be read
          by other software we want to know that also.  Since we do not own
          a copy of every software package we may ask you to send us a copy
          of a file that can be read by that package; we will then compare
          that to a file written out by Image Alchemy to determine what the
          problem is.

          By the way, contact us even if you are not a registered user.  We
          figure the best way to get you to register is to be nice to you.




                                     Trademarks

          Image Alchemy is a trademark of Handmade Software, Inc.

          All other products or services mentioned, including: IBM PC AT,
          VGA, 8514/A, Paradise, Everex, Trident, Video 7, Tseng Labs,
          Wester Digital, MS-DOS, PC-DOS, SPARC, Sun, SPARCstation,
          SPARCserver, SunOS, Targa, PostScript, EPS, Encapsulated
          PostScript, Gif, ILBM, IFF, Macintosh, Silicon Graphics, SGI,
          PCX, TIFF, Windows, Windows BitMaP, EGA, PCL, HP, AI, PS/2, HAM,
          PC Paintbrush, MacBinary, PHIPS, ColorSqueeze, VFCtool, Amiga,
          CServe, and CompuServe, are trademarks, registered trademarks, or
          service marks of their respective companies or organizations.








   Image Alchemy v1.4    Copyright (c) 1990-91 Handmade Software Inc.    Page 35




                                     Disclaimer

          Handmade Software, Inc. makes no warranty of any kind, either
          expressed or implied, including but not limited to implied
          warranties of merchantability and fitness for a particular
          purpose.

          In no event shall Handmade Software, Inc. be liable for any
          errors contained herein or for incidental or consequential
          damages in connection with the furnishing, performance, or use of
          the Image Alchemy product or documentation.











































   Image Alchemy v1.4    Copyright (c) 1990-91 Handmade Software Inc.    Page 36




                                       Credits


          Sam Leffler
               Image Alchemy's TIFF I/O is based on libtiff which is
               Copyright by Sam Leffler and is used with his permission.
               Libtiff is available by anonymous ftp as
               ucbvax.berkeley.edu:pub/tiff/*.tar.Z or
               uunet.uu.net:graphics/tiff.tar.Z.

          John Bridges
               Image Alchemy's VGA display routines are based on VGAKIT,
               originally written by John Bridges.

          Marc Schneider
               Who provided assistance with the Sun implementation of Image
               Alchemy including Beta testing and answering questions about
               the internal format of Sun Raster files.

          Jack Waterman
               Who proofread the manual more times than anyone should have
               to read anything (any remaining misteaks are because we made
               changes after he read it for the final time).



                                     References


          Floyd-Steinberg Dithering
               Floyd-Steinberg, Stucki, and JJN dithering are described in
               "Digital Halftoning", by Robert Ulichnet, MIT Press.

          Heckbert Colour Quantization
               Originally described in "Color Image Quantization for Frame
               Buffer Display", SIGGRAPH '82 Proceedings, p. 297.


















   Image Alchemy v1.4    Copyright (c) 1990-91 Handmade Software Inc.    Page 37




          The following people have written image file conversion software
          similar to Image Alchemy.  Each of their packages is available
          via anonymous ftp.  These programs are only available as source
          code and generally require UNIX or one of its variants.


          Michael Mauldin - Fuzzy Pixmap Manipulation (FBM)
               Available by anonymous ftp as
               nl.cs.cmu.edu:/usr/mlm/ftp/fbm.tar.Z,
               uunet.uu.net:pub/fbm.tar.Z, and ucsd.edu:graphics/fbm.tar.Z.

          Jef Poskanzer - Portable BitMap (PBMPLUS)
               Available by anonymous ftp as
               expo.lcs.mit.edu:contrib/pbmplus.tar.Z and
               ftp.ee.lbl.gov:pbmplus.tar.Z.
               Jef also maintains the "Frequently Asked Questions" list in
               comp.graphics, which is a great source of information on
               graphics.

          Paul Raveling - Img Software Set
               Available by anonymous ftp as
               expo.lcs.mit.edu:contrib/img_1.3.tar.Z and
               venera.isi.edu:pub/img_1.3.tar.Z































   Image Alchemy v1.4    Copyright (c) 1990-91 Handmade Software Inc.    Page 38


                            Image Alchemy 1.4 Order Form

     Qty    Description                                       Price     Total

     _____  Image Alchemy for IBM PC AT on 3.5" Disk          $79.95  __________

     _____  Image Alchemy for IBM PC AT on 5.25" Disk         $79.95  __________

     _____  Image Alchemy for Sun 4 on 3.5" Disk              $79.95  __________

     _____  Image Alchemy for Sun 4 on 1/4" Tape              $99.95  __________

     _____  Image Alchemy for Sun 3 on 1/4" Tape              $99.95  __________


                                                       Sub-Total:     __________

                   California Residents add applicable sales tax:     __________

       Shipping and handling  ($4 UPS Ground, $8 UPS Second Day):     __________
       per copy            ($15 FedEx, $7 International AirMail)

                                                           Total:     __________


     Circle Payment form:       Check       MC       Visa       Amex


     Card #:______________________________________     Exp. Date:   ____________


     Signature: _____________________________________________________

     You must include the address your credit card bill is sent to as the
     billing address for MC/Visa/Amex orders.

     Ship to:                             Bill to:
     Name: ______________________________ Name: ________________________________

     Company: ___________________________ Company: _____________________________

     Address: ___________________________ Address: _____________________________

     City: ______________________________ City: ________________________________

     State: _________   Zip: __________   State: _________  Zip: ____________

     Phone: (______) __________________   Fax: (______) ____________________


     Mail:     Handmade Software, Inc.
               15951 Los Gatos Blvd., Suite 7
               Los Gatos, CA  95032

     Call:     +1 408 358 1292
     Fax:      +1 408 356 4143
     email:    hsi@netcom.COM
     email:    71330,3136 (CompuServe)