#### This article refers to the 3 switch version without the AB-BC jumper ####


                  MODIFYING THE HAYES 1200B MODEM TO IGNORE

              THE STATUS OF THE DATA TERMINAL READY (DTR) LINE

                    by Kim Redlack, Capital PC User Group
                                   3/15/84


    INTRODUCTION

    In the IBM Personal Computer whenever the ASCII communications adapter
    is opened the PC provides a signal to the modem indicating that it is
    ready to receive data.  This signal is present on pin 20 of the
    connecting cable and is referred to as the DTR line.  The 300 and 1200
    Hayes freestanding Smartmodems have a switch which permits the user to
    set the modem to monitor or ignore the DTR line.  If the DTR line is
    monitored and the communications adapter is closed the DTR signal
    disappears and the modem then hangs up.  Presence of the DTR signal is
    indicated by the TR indicator light being lit.

    Because some communications programs open and close the communications
    adapter during execution, setting this switch to ignore the DTR line
    maintains the connection to the telephone line and the remote computer
    throughout program execution.

    The Hayes 1200B board modem which mounts in an expansion slot inside
    the IBM PC does not contain such a switch.  As a result, some programs
    will not work with this modem.  The modification described below may be
    used to cause the 1200B to ignore the DTR line thus permitting these
    programs to function properly.

    MODIFICATION

    Modification of the 1200B modem involves the very simple procedure of
    soldering a small wire jumper between two pins of one of the integrated
    circuits on the modem board.  Modification should not, however, be
    attempted unless you are familiar with printed circuit board soldering
    techniques because damage to the modem could result.  Be sure and use a
    low heat pencil tipped soldering iron.

    First place the 1200B circuit board component side down on your work
    table so that the edge connectors are located at the top right. In this
    position the 25 pin DB-25 connector should be on your right.  Next
    locate integrated circuit #5.  This is a 16 pin IC on the bottom of the
    board about one-third of the way in from the right edge of the board.
    It can be identified by a small upside down "5" on the circuit board.
    Although the markings may vary with the manufacturer, the integrated
    circuit on our board was a Motorola IC marked "MC14051B" on top and "CP
    FF8320" below.

    When you have located this IC you should see a heavy foil connecting
    pins 2, 4 and 15. This foil can be seen between the two rows of
    connecting pins.  The pins of the IC when viewed from this side are
    numbered clockwise from the lower left corner of the IC.  Pins 1-8 are
    from bottom to top on the left side and pins 9-16 are from top to
    bottom on the right side.

                        --------------
                        | 8o     o9  |   IC #5 (bottom view)
                        | 7o     o10 |
                        | 6o     o11 |
                        | 5o     o12 |
                        | 4o--|  o13 |   <-----|  Jumper here to
                        | 3o  |  o14 |         |  connect these
                        | 2o--|--o15 |   <-----|  two pins.
                        | 1o     o16 |
                        |_____ï______|


    Having identified the proper IC you should now be able to locate pins
    13 and 15.  You will find them on the right side where the heavy foil
    should be seen connected to pin 15. Prepare a small jumper wire about
    one inch long.  A small solid conductor wire is recommended.  A small
    amount of insulation should be stripped from each end and the wire
    should then be bent into a "U" shape so that its ends can easily be
    soldered to pins 13 and 15.  Once you are satisfied that the wire is
    properly shaped you are ready to solder it in place.  A very small
    amount of solder should be used to prevent a solder bridge from forming
    an unwanted connection between other adjacent pins.  Once your
    soldering is complete, inspect the results carefully to make sure that
    no unwanted connections have been made.  If all appears well then
    carefully bend the wire flush with the board and replace it into your
    PC.  If all is well you will find that the modem now ignores the status
    of the DTR line and your programs will operate properly.  Good luck.