USERS MANUAL

                  X.00 A Low Level Serial I/O Communications Driver
                        for MS DOS and like Operating Systems.

                        Copyright (c) 1990 by Raymond L. Gwinn
                                 12469 Cavalier Drive
                              Woodbridge, Virginia 22192
                                 All Rights Reserved

                                    July 29, 1990


                               Fidonet address 1:265/1
                                  Data 703-494-8331








                                                                          i
















                                     INTRODUCTION

          Previously,  the documentation  for X00  was little  more  than a
          collection of notes.  The notes were added  to as the development
          process continued and enhancements were made.  I honestly did not
          suspect  that X00  would become as  widely used  as it  is.  This
          manual is an attempt at some decent documentation for X00.

          But who  do I document  for?  The user  that is setting  up a BBS
          just wants to get X00 installed  and to move on to more important
          things.  The user that is having problems needs information about
          serial  I/O communications  in general  and the  PC specifically.
          The application developer (programmer) needs detailed information
          about each individual function and the information generated.

          This manual is intended for the X00 user.  A separate Application
          Programmers manual is being written.

          This manual and the software distributed with it is provided with
          no guarantees.  Use at your own risk.








                                                                         ii

                                  TABLE OF CONTENTS


          WHAT IS X00 . . . . . . . . . . . . . . . . . . . . . . . . .   1

          Warranty  . . . . . . . . . . . . . . . . . . . . . . . . . .   1

          Licensing Information . . . . . . . . . . . . . . . . . . . .   2
               Non-Commercial License . . . . . . . . . . . . . . . . .   2
               Commercial License . . . . . . . . . . . . . . . . . . .   2

          GETTING STARTED . . . . . . . . . . . . . . . . . . . . . . .   4
               Installing X00 . . . . . . . . . . . . . . . . . . . . .   4
               Quick Start  . . . . . . . . . . . . . . . . . . . . . .   4

          OVERVIEW OF X00 USAGE . . . . . . . . . . . . . . . . . . . .   5
               General Information  . . . . . . . . . . . . . . . . . .   5
                    X00 loaded as a DOS Device Driver . . . . . . . . .   5
                    X00 loaded as a TSR . . . . . . . . . . . . . . . .   5
                    COMn and PORTn  . . . . . . . . . . . . . . . . . .   5

          COMMAND LINE OPTIONS  . . . . . . . . . . . . . . . . . . . .   6
               Specifying number of ports . . . . . . . . . . . . . . .   6
               B option, Locking Baud, Data, Parity and Stop bits . . .   6
               Valid locked baud rates  . . . . . . . . . . . . . . . .   7
               Eliminate  . . . . . . . . . . . . . . . . . . . . . . .   7
               Defer  . . . . . . . . . . . . . . . . . . . . . . . . .   7
               DV . . . . . . . . . . . . . . . . . . . . . . . . . . .   8
               FIFO . . . . . . . . . . . . . . . . . . . . . . . . . .   8
               NOFIFO . . . . . . . . . . . . . . . . . . . . . . . . .   9
               NOPOST . . . . . . . . . . . . . . . . . . . . . . . . .   9
               SLOWCPU  . . . . . . . . . . . . . . . . . . . . . . . .   9
               R, Set Receive Buffer Size . . . . . . . . . . . . . .    10
               T, Set Transmit Buffer Size  . . . . . . . . . . . . .    10
               VP or Master Interrupt Enable  . . . . . . . . . . . .    10
               Mapping port assignments . . . . . . . . . . . . . . .    10
               Un-installing X00  . . . . . . . . . . . . . . . . . .    12

          Multi-Tasking . . . . . . . . . . . . . . . . . . . . . . .    13

          THE BIOS INT 14h EMULATOR . . . . . . . . . . . . . . . . .    15

          IRQ SHARING . . . . . . . . . . . . . . . . . . . . . . . .    16

          Appendix A, Hardware Port and IRQ Assignments . . . . . . .    17
               Addresses and IRQs for COM1 and COM2 . . . . . . . . .    17
               Defacto standard for COM3 and COM4 . . . . . . . . . .    17
               Addresses and IRQ for COM3 through COM8 on the PS/2  .    17








                                                                        iii


          Appendix B, SIO Chips . . . . . . . . . . . . . . . . . . .    18
               8250 . . . . . . . . . . . . . . . . . . . . . . . . .    18
               8250A  . . . . . . . . . . . . . . . . . . . . . . . .    18
               16450  . . . . . . . . . . . . . . . . . . . . . . . .    19
               16C451 . . . . . . . . . . . . . . . . . . . . . . . .    19
               16550 Non A  . . . . . . . . . . . . . . . . . . . . .    19
               16550A . . . . . . . . . . . . . . . . . . . . . . . .    19
               16550AF  . . . . . . . . . . . . . . . . . . . . . . .    19
               16550AFN . . . . . . . . . . . . . . . . . . . . . . .    19
               16550s Made by Western Digital . . . . . . . . . . . .    20
               16C551 . . . . . . . . . . . . . . . . . . . . . . . .    20
               16C552 . . . . . . . . . . . . . . . . . . . . . . . .    20
               82510  . . . . . . . . . . . . . . . . . . . . . . . .    20

          Appendix C, Multi-Port Serial I/0 Cards . . . . . . . . . .    21
               Connect-Com 4  . . . . . . . . . . . . . . . . . . . .    21
               4 and 8 Port Boards from Decision-Computer . . . . . .    21
               Stargate Plus 8 board from Software Link . . . . . . .    22

          INDEX . . . . . . . . . . . . . . . . . . . . . . . . . . .    23








                                                                          1

                                     WHAT IS X00

          X00 is  a Serial Input/Output  (SIO) communications  driver.   It
          provides  an interface  between  an application  program and  the
          serial communications hardware.

          X00 was  originally designed as  a FOSSIL  driver.  FOSSIL  is an
          acronym containing the first  character of several communications
          programs.   The FOSSIL specification is basically an extension of
          the PC's BIOS services for serial communications.

          Except as noted in  the Programmers Manual, X00 meets  the FOSSIL
          level 5  specification.   X00 provides additional  functions that
          are not contained in the FOSSIL level 5 specification.

          X00 only works with 8250 (TYPE) serial I/O devices.  Such devices
          include the 8250A,  16450, 16550, 16550A and  the 82510.   If you
          have a PC that  is an IBM or  near compatible which has  a serial
          communication  port, it is likely  that it contains  one of these
          devices.  XU, a  utility distributed with X00, will  identify the
          existence of compatible SIO devices.

          Like  other  Device Drivers,  X00  will do  very  little standing
          alone.  There must be an application(s) program to use X00 before
          you will gain benefit.

          Since  the introduction  of the  FOSSILs, a  great number  of new
          communications  programs have  come into  existence.   I like  to
          think  that the FOSSILs are  largely responsible for  this.  Many
          programs that contain their own communications drivers have added
          FOSSIL support.  One notable example is RBBS.

          Many  programs  written  to  use  BIOS's   serial  communications
          services will also work  with X00.  This gives those programs the
          benefits of buffered interrupt driven I/O.

          Warranty

          There is none.  Use at your own risk.








                                                                          2


                                Licensing Information

          Non-Commercial License:

          A  non-commercial license  for  use of  X00  is included  in  the
          distribution file called LICENSE.TXT.

          I  have received  several unsolicited  checks from users  of X00.
          All  of the checks  have been returned  or uncashed.   To date, I
          have not accepted any payments for X00.  If you feel that  X00 is
          useful  enough that some sort  of payment is  justified then read
          on.

          Our  local (public)  High School  desperately needs  funds.   The
          school officials work at keeping the students off the streets and
          away from  drugs.   The local School  Board is unable  to provide
          needed  funds for  non-academic activities.   I suggest  a $10.00
          contribution be sent to:

               Woodbridge Senior High School
               3001 Old Bridge Road
               Woodbridge, Virginia, 22192

          You  can make the  check payable to  "WSHS, Ballfield Improvement
          Fund".   Please make a  note "X00 contribution"  somewhere on the
          check.

          Many of you have used X00 for years.  I believe  $10.00 is easily
          affordable to most X00 users.   Please take the time to sit down,
          make out the check, address the envelope and mail a contribution.

          Shareware authors that wish to  distribute X00 with their product
          should contact me.  Permission will usually be granted.

          Commercial License:

          Commercial Licenses will  be liberally  granted in  return for  a
          donation (usually tax deductible).   Each commercial license will
          be individually granted.  That is, there is no single policy that
          can be stated  here.  Some  generally uniform commercial  license
          policies follow.

          1 - X00 is usually licensed by product.

          2 - All  commercial licensees of X00 will receive  a special copy
          of X00 that will identify, at boot time, the commercial product.

          3 -  I may require a fully licensed, fully featured, copy of your
          product for personal use on multiple computers.








                                                                          3

          4 - The required  contribution, which is never to  me personally,
          will usually be a one time contribution of $100.00.

          5 -  Proof of licensing belongs to you.   That is, I am not going
          to be responsible for keeping records.  I suggest that you keep a
          copy of the donation  check so that you can  send me a copy  if a
          question  arises.    Otherwise  you  may  have  to  make  another
          contribution.

          6  - You may  only distribute versions  of X00 that  contain your
          product name in the X00 banner (at boot time).

          7 - If you wish  to have the latest version of  X00 automatically
          sent to you with your product name in the X00 banner, then do the
          following:  Send me a check  for $10.00, in advance, along with a
          pre-addressed mailing label.  If you require a 3.5 inch diskette,
          then write "3.5 inch" on the pre-addressed mailing label and send
          $15.00 (instead of  $10.00).   For updates, the  check should  be
          made  out to Raymond  L. Gwinn.   The checks will  be cashed when
          received.  Individuals that wish to receive a mailed  copy of the
          latest X00 version may  also use this  procedure.  Once you  have
          received an  update, you will need  to resend the  update fee and
          pre-addressed mailing  label if  you desire  to receive the  next
          update.

          8  -   Your  contribution  check  should   state  "X00  Licensing
          contribution" in the Memo or comment field.

          If  you write  me about  a commercial  license, please  include a
          voice phone number.  You may  not receive a response if the voice
          phone number is omitted.  Correspondence should be sent to:

                    Raymond L. Gwinn
                    12469 Cavalier Dr.
                    Woodbridge, Va. 22192

          Prior to making the special version of X00 available, I  may wait
          for  the check to clear the bank.   If the check bounces, I will,
          most  likely, not give any further  consideration to a commercial
          license.








                                                                          4


                                   GETTING STARTED

          Installing X00

          X00  is distributed  as a  ZIP file.   To extract  the individual
          files  from the distribution file you need the program PKUNZIP or
          an  equivalent.   PKUNZIP  is  a  product of  PKWARE  and  can be
          downloaded from  almost any  bulletin board  system  (BBS).   You
          probably already have PKUNZIP and know how to use it, otherwise I
          doubt that  you would be reading  this.  When PKUNZIP  is used to
          extract the various files, -AV should appear after each file name
          as it is extracted.  In addition, the message:

               Authentic files Verified!

          should appear after the extraction process.  If this message does
          not appear, or  appears with a name other than  Raymond L. Gwinn,
          the file is not an original X00 distribution file.

          The  only file  that the  basic user  actually needs  is X00.SYS.
          Copy  this file to a convenient directory or subdirectory on your
          system.   I suggest that all users  also install XU.EXE also.  XU
          can provide important  information about X00 that  may be helpful
          when problems occur.


          Quick Start

          Copy X00.SYS and XU.EXE to the root  directory of your boot drive
          or diskette.

          If you  are going  to use  standard communications  ports, either
          COM1 or COM2 on  a PC or AT, or COM1 through COM8 on a PS/2, then
          add the following line to your CONFIG.SYS file:

               DEVICE=X00.SYS E

          If  you wish  to have  more than  one communications  port active
          simultaneously,  then  modify the  command  line  to include  the
          number of simultaneously active  ports you wish to support.   For
          example,  if you are using DESQview and you  wish to run a BBS in
          two  different  windows,  then  add the  following  line  to your
          CONFIG.SYS file:

               DEVICE=X00.SYS E 2

          It  should be  noted that the  above command  tells X00  how many
          ports that are to  be used simultaneously, not which  ports.  The
          application program may use ANY 2 serial ports in any order.

          If your setup is more complex, you must read on.








                                                                          5

                                OVERVIEW OF X00 USAGE

                                 General Information

          Things  can get  a little confusing  here.   At the  time of this
          writing,  X00 is almost (if not completely) unique in its ability
          to function as a DOS device driver or as a Terminate (or Torment)
          and Stay Resident program (TSR).

          X00 loaded as a DOS Device Driver

          If X00 is to be used as a DOS device driver, it must be installed
          using  the CONFIG.SYS  file.   For a  precise description  of the
          CONFIG.SYS file  and  its  function, please  refer  to  your  DOS
          manual.  Basically,  you use a text  editor to add a  line to the
          CONFIG.SYS  file.    The  line  that  you add  is  DEVICE=X00.SYS
          followed by optional parameters.  The optional parameters will be
          described later.  If X00.SYS is  not in the current directory you
          will need to provide a DOS path  to the directory containing X00.
          For  example, if X00.SYS is in  a subdirectory called COMM on the
          hard  disk drive  C, the  line  in the  CONFIG.SYS file  would be
          DEVICE=C:\COMM\X00.SYS.

          X00 loaded as a TSR

          If  X00 is  to be  used as  a Terminate  and Stay  Resident (TSR)
          program,  then you must rename  or copy X00.SYS  to X00.EXE.  The
          EXE  version of  X00 must  be in  the current  directory or  in a
          directory  in the  DOS  path when  it is  executed.   X00.EXE  is
          executed like  any other DOS program.   That is, you  type X00 at
          the  DOS prompt followed by any optional parameters.  In reality,
          you will probably be using a batch file to execute X00.


          COMn and PORTn

          X00 allows communications ports  to be swapped around.   That is,
          the serial port that DOS calls COM1 can be mapped (reassigned) to
          any X00 port.   Therefore, when a  reference in this  document is
          made about  PORTn, it  refers to  the serial  I/O device  that is
          mapped to  that X00  port.   When  a reference  is  made to  COM1
          through  COM8,  it  refers to  the  serial  I/O  device that  DOS
          knows/uses as COMn.   Also worth noting  is that DOS numbers  the
          serial  I/0 devices  starting at  1 (COM1  through COM8)  and X00
          numbers them starting at 0 (PORT0 through PORT7).

          X00's  default is to assign  PORT0 through PORT7  to COM1 through
          COM8.








                                                                          6

                                 COMMAND LINE OPTIONS

          The  command line options are  included in the  command line that
          invokes X00.  In several  cases only the first 1 or  2 characters
          of the option need be entered.  In other cases, the entire option
          name  must  be  spelled out.    Unless  otherwise  stated in  the
          following descriptions,  the entire  option name must  be spelled
          out.  The parameters are given one after another on the same line
          and in any order.  The length of the command line is limited only
          by DOS.

          Specifying number of ports

          If a  single  decimal number  is  in  the X00  command  line,  it
          specifies  the number  of  ports that  X00  is to  simultaneously
          support.   The default is  one port.   The maximum  value of  the
          number of ports is 4 for non PS/2 systems and 8 for PS/2 systems.
          If you  desire to use more than 4 ports  on a non PS/2, each port
          address must  be specified (see mapping  port assignments below).
          Input  and output  buffers are  allocated for  each of  the ports
          specified.  Examples of usage are:

               When X00 is loaded as a Device Driver
                    DEVICE=X00.SYS 3
                    DEVICE=X00.SYS 8

               When X00 is loaded as a TSR
                    X00 3
                    X00 8

          B option, Locking Baud, Data, Parity and Stop bits

          Normally, the  application program sets  the baud rate  and other
          parameters  controlling the  serial  I/O hardware.   Some  modems
          provide  better  performance  when  the  communications  from the
          computer to modem is constant (Locked).  That is, the computer to
          modem speed is not the same as the modem to modem speed.  If this
          option  is   used,  the  modem  must   support  RTS/CTS  hardware
          handshaking and the feature must be enabled on the modem.

          The B command  line option  requires 2 parameters  and allows  an
          optional  third parameter.  The  option is specified  in the form
          B,PORTn,BAUD  RATE,PARITY.  You  will most  likely never  want to
          lock the parity, data and stop bits.  Examples of usage are:

               When X00 is loaded as a Device Driver
                    DEVICE=X00.SYS B,0,2400 B,1,19200 or
                    DEVICE=X00.SYS B,1,19200,8N1

               When X00 is loaded as a TSR
                    X00 B,0,2400 B,0,19200 or
                    X00 B,1,19200,8N1








                                                                          7


          Valid locked baud rates are: 75, 110, 135.5, 150, 300, 600, 1200,
          1800, 2000,  2400, 3600, 4800,  7200, 9600, 19200,  28800, 38400,
          57600, and 115200.

          I can  think of few conditions  where it is necessary  to use the
          optional  third  parameter of  the B  command  line option.   The
          optional  third parameter is made up of 3 characters that specify
          the  locked setting for data  bits per character,  parity bit and
          stop bit(s) in  that order.  The optional  third parameter can be
          made up of  any combination  of the following  first, second  and
          third characters.

                    First     Second         Third
                    5         N = None       1
                    6         E = Even       2
                    7         O = Odd
                    8         M = Mark (always 1)
                              S = Space (always 0)


          The first  character  specifies  the  number  of  data  bits  per
          character,  the second  character specifies  the handling  of the
          parity bit and the  third character specifies the number  of stop
          bits.   When 5 data bits and  2 stop bits (eg 5N2) are specified,
          the  number of stop bits will actually  be 1.5.  As stated above,
          locking of the parity etc, is not advisable.

          Anytime an application program attempts to program the baud rate,
          parity etc, through X00, the locked values will be substituted.

          Eliminate

          Normally,  when X00 is loaded a copyright notice is displayed for
          5 seconds.  Using the eliminate  option will disable the 5 second
          display  of the copyright  notice.  Only the  first letter (E) is
          required to invoke this option.  Examples of usage are:

               When X00 is loaded as a Device Driver:
                    DEVICE=X00.SYS ELIMINATE or
                    DEVICE=X00.SYS E

               When X00 is loaded as a TSR
                    X00 ELIMINATE or
                    X00 E

          Defer

          The Defer option  creates problems  on most systems.   The  Defer
          option should be avoided by most users.  X00 must  use several of
          the  80x86 interrupts.  Normally,  X00 will hook  itself into the
          80x86 interrupts when it is executed.  The Defer option tells X00








                                                                          8

          to  postpone hooking  into some  interrupts until  an XU  CAPTURE
          command  is  executed.    If  the defer  option  is  used  and  a
          subsequent  XU  CAPTURE  is  not  issued,  X00  may not  function
          correctly.  Additionally,  the XU CAPTURE must be  executed prior
          to  executing  a multitasker  like DESQview.    Only the  first 2
          letters (DE) need  to used to specify  this option.   Examples of
          usage are:

               When X00 is loaded as a Device Driver
                    DEVICE=X00.SYS DEFER or
                    DEVICE=X00.SYS DE

               When X00 is loaded as a TSR
                    X00 DEFER or
                    X00 DE

          The  default for  Defer is  off.   That is,  X00 will  by default
          immediately hook into all necessary 80x86 interrupt vectors.

          DV

          The  DV command  line option is  only of interest  to those using
          DESQview.   The  default for  this option  is off.   When  on (DV
          specified  in the  command line),  X00 will  make DESQview  Pause
          calls when it seems that  the application program is idle.   This
          may make  time available for other  tasks to use.   Refer to your
          DESQview manuals for details about the DESQview pause command.

          If you are  using DESQview, try  the DV option.   If it does  not
          adversely affect your system, leave it enabled (on).  Examples of
          usage are:

               When X00 is loaded as a Device Driver
                    DEVICE=X00.SYS DV

               When X00 is loaded as a TSR
                    X00 DV

          FIFO

          Only the first  letter of the command  (F) is required to  invoke
          this option.  Some of the serial I/O hardware  devices have First
          In First Out (FIFO) buffers.  This command line option is used to
          specify the  number of characters that X00 can load into the FIFO
          during  a single  transmit  interrupt.   In  general this  number
          should be set  the size of the  FIFO minus 1.   For example,  the
          popular 16550A has a 16  byte FIFO on both transmit and  received
          data.  Thus, if this option is used, I suggest the value of 15 be
          used for the 16550A.  Examples of usage are:

               When X00 is loaded as a Device Driver
                    DEVICE=X00.SYS FIFO=10








                                                                          9

                    DEVICE=X00.SYS F=15

               When X00 is loaded as a TSR
                    X00 FIFO=15
                    X00 F=8

          The size of the receive FIFO is always set to the maximum by X00.

          NOFIFO

          This command line option is used to completely disable the use of
          hardware FIFOs.  Examples of usage are:

               When X00 is loaded as a Device Driver
                    DEVICE=X00.SYS NOFIFO

               When X00 is loaded as a TSR
                    X00 NOFIFO

          NOPOST

          Normally,  when X00 is executed,  it will alter  the COM1 through
          COM4 hardware port addresses  in BIOS RAM to match  the addresses
          being used by X00.  By doing so, many DOOR type programs that use
          INT  14h  for  their serial  I/O  will  work  correctly with  X00
          installed.   This option (NOPOST) instructs X00 to leave the BIOS
          RAM unchanged.  Examples of usage are:

               When X00 is loaded as a Device Driver
                    DEVICE=X00.SYS NOPOST

               When X00 is loaded as a TSR
                    X00 NOPOST

          SLOWCPU

          This command line option  is provided for those using  slower PCs
          and those using software  that executes large amounts of  code on
          an interrupt  level (such  as the timer  tick).  When  SLOWCPU is
          specified,  X00 will make  the serial ports  the highest priority
          interrupt.     This  feature  allows   (most)  4.77  mhz  PCs  to
          receive/transmit at full  speed.  This option  may cause problems
          in  some  environments.    Most  protected  mode  programs,  like
          DESQview, will not  allow the  priority of the  interrupts to  be
          changed.

               When X00 is loaded as a Device Driver
                    DEVICE=X00.SYS SLOWCPU

               When X00 is loaded as a TSR
                    X00 SLOWCPU








                                                                         10

          R, Set Receive Buffer Size

          The R command line option allows the user to set the  size of the
          receive buffer.   The default size  of the receive buffer  is 512
          bytes.   The size  of the  buffer must  be a power  of 2.   Valid
          buffer sizes are:  256, 512,  1024, 2048, 4096,  8192, 16384  and
          32768.   If an invalid buffer  size is specified, the  next lower
          correct buffer size is used.

          Many users needlessly set  the size of the receive  (or transmit)
          buffer too large.  Examples of usage are:

               When X00 is loaded as a Device Driver
                    DEVICE=X00.SYS R=1024
                    DEVICE=X00.SYS R=2048

               When X00 is loaded as a TSR
                    X00 R=1024
                    X00 R=2048


          T, Set Transmit Buffer Size

          This option is identical to the R command line option (see above)
          except it sets the size of the transmit buffer.


          VP or Master Interrupt Enable

          VP stands for Vector Port which  is not a very good name for  the
          option.  Some multiple port serial I/O cards default  to only two
          ports enabled when power is turned on.  A specified value must be
          written to an  I/O port  to enable the  additional serial  ports.
          Simply stated the VP  command line option says to write the given
          value to the given port.  Examples of usage are:

               When X00 is loaded as a Device Driver
                    DEVICE=X00.SYS VP=03FF,80

               When X00 is loaded as a TSR
                    X00 VP=3FF,80

          Both  of the above  examples in effect  says, write the  value 80
          (hex) the I/O port at 3FF.



          Mapping port assignments

          This  is the most complicated command line option for many users.
          By default,  X00 maps up to  8 serial I/O ports  (PORTS 0 through
          7).  X00 will (attempt to) determine the hardware architecture on








                                                                         11

          which  it is  being executed.   If  a PS/2  is detected  then the
          default Serial I/O  port addresses will be set to  match the PS/2
          (see Appendix .   If X00  detects that the  system is not a  PS/2
          type system, then the default port addresses are as follows:  1 -
          Standard  addresses for COM1 and  COM2, 2 -  The defacto standard
          for COM3  and COM4,  and nothing for  COM5 through COM8  (ports 4
          through 7).

          Port mapping is necessary if your hardware configuration does not
          match the PS/2 or  defacto standard for  non PS/2 systems.   COM1
          and COM2  are the  same for the  PC, XT,  AT and PS/2.   However,
          hardware  specifications for COM3  through COM8  became available
          only when IBM released the PS/2.

          Many  multiple  serial port  cards  are  available for  pre  PS/2
          systems that use a defacto standard.  The most common assignments
          that I have  seen for COM3 and COM4 are: COM3 at port address 3E8
          using  IRQ 3.  COM4  at port address 2E8 using  IRQ 4.  Above the
          fourth port,  I have not  observed anything resembling  a defacto
          standard.

          X00 will  support almost any serial  I/O card.   However, in most
          cases,  port mapping  is required  for anything  beyond  COM1 and
          COM2.

          Mapping port assignments uses two basic forms.  They are:
               PORTn=COMn,IRQn
               PORTn=HEXADDRESS,IRQn

          Where:
               PORTn is the X00 port number and must be 0 through 7.

               COMn is a standard DOS port and must be COM1 through COM8.

               IRQn is the IRQ use by the serial port and must be IRQ0
               through IRQ15.

               HEXADDRESS is a hexadecimal I/O port address that addresses
               the serial I/O device.

          In both basic forms, the IRQn is optional.  X00 defaults all IRQn
          to IRQ3  except COM1 which  defaults to IRQ4.   Examples of usage
          are:

               When X00 is loaded as a Device Driver
                    DEVICE=X00.SYS 0=COM4
                    DEVICE=X00.SYS 0=COM4,IRQ5
                    DEVICE=X00.SYS 0=2E8,IRQ3
                    DEVICE=X00.SYS 2=2E8

               When X00 is loaded as a TSR
                    X00 0=COM4








                                                                         12

                    X00 0=COM4,IRQ5
                    X00 0=2E8,IRQ3
                    X00 2=2E8


          Un-installing X00

          When X00 is installed as a TSR, it can be  un-installed by simply
          executing X00 with no command line parameters.  If you wish to be
          sure that you do not accidently un-install X00, always execute it
          with a harmless parameter like X00 E.








                                                                         13

                                    Multi-Tasking

          By  far, DESQview seems to be the multi-tasking software that X00
          is  most  often used  with.    At the  time  of  this writing,  I
          personally use DESQview to run a multi line BBS.

          I believe it is best to load X00 before the multi-tasking program
          and  to load  it as a  device driver.   This  enables all windows
          (tasks)  access to X00.   Loading X00 first  also allows multiple
          windows to share the same IRQ.

          If  you have loaded X00 prior to  DESQview, you need to configure
          the window  for no  communications.   That is,  answer NO  to the
          configuration   questions,   Uses  Serial   Ports   and  Optimize
          communications.     I  also  suggest  that   you  enable  printer
          management within the window.  Enabling printer management allows
          a  remote drop  to DOS  to work  on many  systems.   The Optimize
          communications  option and  the  Printer  management  option  are
          established with  the DESQview  SETUP program.   The  Uses serial
          ports  (Y,N,1,2) option is in  the "Change a  Program" portion of
          window configuration.

          In  several  cases  I  have  gained  a  significant  increase  in
          performance by turning X00 on prior  to executing a program.  Two
          notable cases are GATEWAY and DOORWAY.  I used XU to turn X00 on.
          For example, XU PORT:n:ON just before invoking DOORWAY or GATEWAY
          produced significantly better input and output from the programs.
          Depending  on your environment, an  XU PORT:n:OFF may  have to be
          issued after  the program terminates.   Also note that the  n for
          PORTn is 1 less than the n in GATEn and COMn.

          The communications windows seem  to work better if the  ticks for
          the  foreground and  background  are set  relatively  low.   Most
          people that  I have talked to use 2 ticks for both foreground and
          background.  Only experimentation will determine the best setting
          for your system.

          If you do  not wish to share  an IRQ, you can  load X00 as a  TSR
          inside  a DESQview window.  When loaded inside a DESQview window,
          X00 is  only available to programs in that window.  X00 should be
          configured  to  support   only  1  serial  port  and  you  should
          specifically name the port that X00 will use in the command line.
          For example use X00 0=COM1,  instead of X00 1 or just  plain X00.
          Identifying the specific  serial port  to be used  in the  window
          eliminates the chance that X00 will interfere with another active
          window.

          I strongly recommend that you use the 16550A (or later)  SIO chip
          if you are using a multi-tasking system of any kind.








                                                                         14


          Most programs written to use BIOS INT 14h will work directly with
          X00's enhanced services.  You should try turning  X00 on using an
          XU  PORT:n:ON  command  just  prior  to  executing  the  program.
          Programs  that  do not  have their  own  interrupt I/O  will most
          likely give better performance.








                                                                         15

                              THE BIOS INT 14h EMULATOR

          X00 is a  BIOS INT 14h enhancement.   So what  is the need for  a
          BIOS  emulator also?   Well, when X00  is turned off  for a given
          port,  it  does  not process  the  INT  14h  functions using  the
          enhanced code.   Prior  to the introduction  of the BIOS  INT 14h
          emulator, X00 simply passed calls to inactive serial ports to the
          BIOS INT 14h.

          Serial   communications  has   changed  considerably   since  the
          definition of  the original BIOS for  the PC.   However, the BIOS
          services for  serial  communications have  changed  very  little.
          Many  program are still written  to use the  original BIOS serial
          communications  services.  Many older  programs that use the BIOS
          communications services are still widely used.

          Problems occur  when advanced  high  speed modems  are used  with
          these programs.  Many of the  programs are totally unaware of the
          concept of RTS/CTS handshaking that most of the high speed modems
          use.  The programs cannot be aware that the user  may have mapped
          the port  addresses.   BIOS  for  all systems  (that  I know  of)
          support only  4 serial  communications ports except  PS/2 systems
          which support 8.

          I added  the BIOS emulator to X00 to support many of the programs
          that  are not (or cannot  be) aware of  the active communications
          environment.

          By default,  X00's BIOS INT 14h  emulator is enabled.   It can be
          disabled by adding USEBIOS to the command line that invokes X00.

          When the emulator is enabled, port mapping, baud rate locking and
          hardware handshaking for the serial  port(s) are maintained and 8
          serial ports are supported.   If the serial  I/O chip is  FIFOed,
          the  emulator allows the FIFOs to be  used.  This means that many
          programs  written to use  BIOS can be  used in  the more advanced
          communications environments.

          The BIOS  emulator can  be activated and  deactivated dynamically
          using XU.








                                                                         16

                                     IRQ SHARING

          Sharing the same IRQ for multiple communications ports is not for
          the weak of heart (or mind).

          Most popular  multitasking software  seems to do  everything they
          can to  prevent the sharing of  a single IRQ between  two or more
          tasks (windows).   This big brother attitude  of the multitaskers
          is cause of most of the  problems in sharing a single IRQ between
          several  serial  communications  ports.    Several communications
          ports  sharing a single IRQ is not  too difficult to manage.  The
          problem is the multitaskers not allowing the sharing of an IRQ by
          more than one task (window).

          In any  case, version 1.20 of X00  has been tested with DESQview,
          RBBS  and  8 comm  ports  sharing  IRQ 3.    I  have also  tested
          MultiLink  with  2  comm  ports  sharing  the  same  IRQ.    With
          MultiLink, I had to use  the NASTY option.  Do not  use the NASTY
          option with DESQview.

          The  method  I  have developed  to  force sharing  of  an  IRQ by
          multiple  comm   ports  should   work  on  most,   if  not   all,
          multitaskers.  It is too big a job, and too costly for me to test
          them all.

          Some general rules are as follows:

          1  - X00 should  be loaded before  the multitasker.   That is, if
          your multitasker allows the  loading of device drivers  into each
          window, DO NOT DO  IT if you wish to  share an IRQ.  Load  X00 at
          boot time and it should then be available to all tasks (windows).

          2 - Two different  boards (plugged into different slots)  can not
          share the same IRQ.  This is a hardware limitation and can not be
          corrected  by software.  This means that  you can not plug in two
          internal  modems, set them  for the same  IRQ and  expect them to
          work.   This  does not  apply to  PS/2 systems.   The  problem of
          multiple  boards sharing the same IRQ was corrected in the PS/2's
          buss design.

          3 -  When  configuring  the DESQview  windows,  we  specified  NO
          communications  in the  window.   Remember, it  is X00  (which is
          hopefully  outside   any  window)   that  is  doing   the  actual
          communications and not the application program inside the window.

          4 - X00 can not  (will not) share an IRQ with other software.  If
          you attempt to run a program in a window that uses an IRQ that is
          being used by X00, the results are unpredictable.

          5 - Do not load X00 into EMS memory.  Loading high is okay.








                                                                         17

                    Appendix A, Hardware Port and IRQ Assignments

          I have  obtained the following information  from various sources.
          Accuracy is not guaranteed.  In fact, nothing in this document is
          guaranteed.

          Addresses and IRQs for COM1 and COM2

               COM1 uses 03F8h and IRQ4
               COM2 uses 02F8h and IRQ3

          Defacto standard for COM3 and COM4 for PC, XT and AT

               COM3 uses 03E8h and IRQ4
               COM4 uses 02E8h and IRQ3

          Addresses and IRQ for COM3 through COM8 on the PS/2

               COM3 uses 3220h and IRQ3
               COM4 uses 3228h and IRQ3
               COM5 uses 4220h and IRQ3
               COM6 uses 4228h and IRQ3
               COM7 uses 5220h and IRQ3
               COM8 uses 5228h and IRQ3

          All  PCs prior to the PS/2 only  used 12 bits to address hardware
          I/0 ports.   Systems prior to  the PS/2 and EISA  can not address
          the standard  addresses for COM3 through COM8.  If an AT of below
          attempts  to  address  COM3   through  COM8  using  the  standard
          addresses, only  the low 12 bits  of the address are  used.  That
          is,  the high digit of  the hexadecimal address  will be ignored.
          This  means that any reference to COM3 through COM8 will actually
          address ports 220h through 22Fh.

          You  should avoid  expansion boards that  use ports  220h through
          22Fh unless the expansion board is a serial I/O board. 

          X00 will (attempt to) determine the hardware architecture that it
          is being executed  on and  use to appropriate  port addresses  as
          defaults.








                                                                         18

                                Appendix B, SIO Chips


          The following is a collection of comments developed from hearsay,
          random documents, experience,  and technical specifications.  So,
          take it with a grain of salt.  Order information from the various
          manufactures if you want accurate information.

          A very good reference book that I use is  available from National
          Semiconductor Corporation.   It  covers most  of the  SIO devices
          (also  called UARTs)  that you will  find in all  PCs and clones.
          The title  of the book is  Microcommunications Elements Databook.
          The publication number (manual number) is  400066.  I am not sure
          that   the   book  can   be   ordered   directly  from   National
          semiconductor.  They  may   require  that  you  get   it  from  a
          distributor.   In any case, the address on the back of the manual
          is:

               National Semiconductor Corporation
               2900 Semiconductor Drive
               P.O. Box 58090
               Santa Clara, CA 95052-8090

               Tel:(408)721-5000
               TWX:(910)339-9240

          8250

          As best that I know, the 8250 was the first  SIO chip (integrated
          circuit) that was  used by the  IBM PC  and many clones.   In  my
          opinion,  it was a poor choice  on the part of IBM.   I feel many
          superior devices, at comparable  prices, were readily  available.
          At that time, I feel the 8251A or the 8530 would have been better
          choices.   I feel IBM  used the 8250  to insure the PC  would not
          have   synchronous  communications   capability  in   a  standard
          configuration.

          From  a hardware standpoint the 8250 is a relatively slow device.
          It is advisable that programmers not perform successive inputs or
          outputs to this device.  It seems that software programs can load
          the various registers of the 8250 faster  than it can process the
          information.    The  8250  had  a  total  of  7 registers.    The
          specifications state that 56kb is the maximum baud rate.

          8250A

          I believe the 8250A is the  8250 with some bug fixes.  I  have no
          idea  what  the bugs  may  have  been.   A  quick  glance at  the
          specifications shows the speed  of the 8250 and 8250A  to be much
          the  same.   The 8250A  added an  8th register.   This additional
          register enables software to detect if an 8250 is installed.  The
          specifications state that 56kb is the maximum baud rate.








                                                                         19

          16450

          The  16450 seems to be a speeded up  version of the 8250A.  There
          is no  direct way (that  I know  of) for software  to detect  the
          difference between an 8250A and a 16450.  I believe the 16450 was
          developed to  eliminate the  need for  software to  insert delays
          between successive  accesses to  the device.   The specifications
          indicate the 16450 is a much faster device than its predecessors.
          The additional speed is only the speed at which the processor can
          access the  device.  The maximum baud rate for the 16450 is still
          stated at  56kb.  However, I  have been told by  some people that
          they have run the  16450 successfully at much higher speeds. I do
          not believe there was ever a 16450A.

          16C451

          The  16C451 is a CMOS version  of the 16450.  CMOS  is a term for
          the  material and  manufacturing process  used to make  the part.
          CMOS typically uses less  power than other technologies.   If you
          are  not  designing hardware,  you should  view  the 16C451  as a
          16450.

          16550 Non A

          It is  hard to  find a 16550  (Non A).   I  was told by  National
          Semiconductor that  they did  everything  they could  to get  all
          16550s  back.  X00 (and  XU) will detect a 16550  and tell you if
          you have one.   I am told  that the 16550 was  installed in early
          PS/2 systems.

          The 16550  was the first  shot at  a FIFOed version  of the  8250
          family  from  National semiconductor.    However, I  was  told by
          National  Semiconductor  that the  FIFOs  of  the 16550  are  not
          reliable and  they should not be enabled.  X00 will treat a 16550
          like  a 16450.    In  this mode,  they  are  reliable.   National
          Semiconductor would not provide  me with a specification for  the
          16550.  However, I suspect  its maximum baud rate is the  same as
          the 16550A which is 256kb.


          16550A, 16550AF and 16550AFN

          In the  manuals  that I  have,  National Semiconductor  does  not
          explain  the differences between the  16550A and the  16550AF.  I
          suspect the AF part may have a few bug fixes.  I believe the N in
          AFN  describes packaging,  ceramic  versus  plastic,  DIP  versus
          surface mount etc.

          In  the opinion  of the  author, there is  no substitute  for the
          16550A (and its  successors) in the 8250 type series.  The 16550A
          is compatible with software written for the entire family of 8250








                                                                         20

          type  devices.  Programs that  are 16550A aware  can provide much
          improved performance over previous devices.

          The  maximum  baud rate  for the  16550A  is specified  at 256kb.
          However, due to the hardware design of the PC et al, 115kb is the
          maximum baud rate that can be programmed.

          The 16550A can be  plugged into the same socket that  contains an
          8250, 8250A  or 16450.  If  your SIO expansion board  has the SIO
          chips  in  sockets,  you can  upgrade  to  the  16550A by  simply
          removing the old chips and replacing them with 16550As.

          The key to  the performance increase of the 16550A  is its FIFOs.
          It has 16 byte FIFOs for both transmit and receive data.

          16550s Made by Western Digital

          I have been told, but I have not verified for myself, that 16550s
          made  by Western  Digital have  a problem  with their  FIFOs when
          working at 2400 baud or below.

          16C551

          The  16C551 is  a CMOS  version of  the 16550AF.   See  the above
          description of  the 16C451 for a discussion of CMOS.  Do not feel
          you need to upgrade from a 16550A or AF to a 16C551.  There is no
          gain from an existing users point of view.

          16C552

          The 16C552 is two 16C551s  on a single chip.  These  devices will
          start showing up on multi-port serial I/O cards.

          82510

          I  believe Intel is the only company that manufactures the 82510.
          The 82510  is feature rich with several  modes of operation.  Its
          default  mode is to operate as  a 16450.  The 82510  has a 4 byte
          FIFO  for both  transmit and  receive  data.   A 4  byte FIFO  is
          sufficient to provide significant performance over a basic 16450.

          The  82510 is small in size.  Therefore,  it is found in many lap
          tops.

          The 82510 is  somewhat of a sleeper.  I believe  it would be much
          more widely used if Intel had promoted it more.  However, given a
          choice  between  the 82510  and the  16550A,  I would  select the
          16550A.








                                                                         21

                       Appendix C, Multi-Port Serial I/0 Cards

          I  get many requests for information  about multi-port serial I/O
          card.   I will describe  the boards  that I know  about (or  have
          heard about) here.  I  will add to the list as  I receive precise
          information from users.

          My  personal experience  is with two  boards that  allow multiple
          serial I/O ports to share  a single IRQ.  The first board  that I
          experimented with  was the  Connect-Com 4  from Software  Link in
          Atlanta Georgia.  The second board is the 4 PORT RS-232 CARD from
          Decision-Computer International in Taipei, Taiwan.

          Connect-Com 4

          I found the manual for the Connect-Com 4 to be very confusing and
          their  tech support  even less helpful.   I  was able  to get the
          board  configured to  use  the standard  COM1  and COM2  and  the
          defacto standard for COM3  and COM4.  If you use  the Connect-Com
          4, I suggest  that you use it  in this manner.   This means  that
          COM1 and COM3 will use IRQ4 and COM2 and COM4 will use IRQ3.  The
          Connect-Com 4  has an  8 position DIP  switch for  configuration.
          The setting that I used was positions 2, 3, 7 and  8 ON (up), and
          all  other positions OFF (down).  In retrospect the Connect-Com 4
          seems  a bit expensive.   However, once  configured properly, the
          Connect-Com  4  worked without  problem.   Software  Link  can be
          reached in Atlanta Georgia at 404-448-5465.

          4 and 8 Port Boards from Decision-Computer

          The second  board that I have personally used, and the one that I
          am  currently using  is from  Decision-Computer.   The  manual is
          written  well enough that I  did not need  any technical support.
          There are two boards of interest from Decision-Computer, one is a
          4 port  serial I/O card  and the  other is an  8 port  serial I/O
          card.   I read  somewhere in the  documentation (which  I can not
          find  at this  time)  that  the  boards are  a  clone  of  boards
          available from AST.

          The boards from  Decision-Computer are configured by jumpers.   I
          use 4  ports of  the 8  port card.   I  selected the  (so called)
          Compatible Mode.  This means that the first two  serial I/O ports
          operate   as  standard  COM1   and  COM2  using   IRQ4  and  IRQ3
          respectively.  The jumper setting for Compatible Mode is  clearly
          shown  in  the manual  (page  8  of my  manual).    The I/O  port
          addressed used in that mode are  also clearly defined on the same
          page.

          A second jumper that must be set (JP2) defines the number of wait
          states.   I set  the  jumper in  position 3  which  means 2  wait
          states.  This was  for a 20 mhz  386 system.  This setting  works
          fine for me.  More wait  states may be required or less  may work








                                                                         22

          on your system.   The amount of time lost due to  wait states for
          serial I/O is very minimal.

          The  last jumper(s) for the Decision-Computer 8 port RS-232 board
          is the selection of the IRQ(s) for ports other than  the first 2.
          I selected  IRQ3 for the additional  ports that I am  using (I am
          only using 4 of the 8).  This means that the first port (COM1) is
          using IRQ4, all of the other (3) ports are using  IRQ3.  Position
          2 of JP3 (left side) is the jumper that I installed.

          Now  for the  seemingly tough  part.   I  ordered the  board from
          Decision-Computer in  Taipei, Taiwan.   Why?  Simple,  the price.
          The 4 port version of the card is $36.00 US dollars.  The  8 port
          version of the  card is $100.00  US dollars.   I have not  really
          looked very hard, but I have not seen anything near  this pricing
          in the US.

          With a few exceptions, I found ordering from Taiwan about as easy
          as ordering  from a US company.  The exceptions are, they like to
          use a FAX for ordering  etc. and you will have to pay in advance.
          I  have ordered several items from Taiwan, paying in advance, and
          I  have not  lost  a nickel  yet.   Decision-Computer  will  send
          brochures  if  you request  them.   They  can be  reached  at the
          following address (FAX is best):

               Decision-Computer International Co., LTD.
               4/F No. 31-3 Alley 4, Lane 906
               Ming-Shen East Road Taipei, Taiwan
               R. O. C.

               Tel: (02) 766-5753 or 765-9782 or 796-5786
               FAX: 886-2-7665702
               TELEX: 16059 DECISION

          To send a FAX from this area to Decision, I dial:
               011-886-2-7665702

          The  best  way to  order  is to  have  your bank  wire  the money
          directly to Taiwan.   Be sure that you specify Federal Express as
          the shipper  from Taiwan to  the US.   Federal Express  will take
          care  of any  Customs hassle.   In  most cases  there will  be no
          customs fees.   In the worst case that I  have experiences, I had
          to pay Federal 2 or 3 dollars in customs fees.

          Stargate Plus 8 board from Software Link

          Dan  Fox originally helped me with the testing of multiple serial
          I/O ports sharing  a single IRQ.  He informed  me that the serial
          I/O board that he uses is a  Stargate Plus 8 Board.  He purchased
          the board  from Software  Link in Atlanta  Georgia, 404-448-5465.
          Dan has all 8 ports using IRQ3.








                                                                         23

                                        INDEX

          16450 . . . . . . . . . . . . . . . . . . . . . . . . . . . .  19
          16550 Non A . . . . . . . . . . . . . . . . . . . . . . . . .  19
          16550A  . . . . . . . . . . . . . . . . . . . . . . . . . . .  19
          16550AF . . . . . . . . . . . . . . . . . . . . . . . . . . .  19
          16550AFN  . . . . . . . . . . . . . . . . . . . . . . . . . .  19
          16550s Made by Western Digital  . . . . . . . . . . . . . . .  20
          16C451  . . . . . . . . . . . . . . . . . . . . . . . . . . .  19
          16C551  . . . . . . . . . . . . . . . . . . . . . . . . . . .  20
          16C552  . . . . . . . . . . . . . . . . . . . . . . . . . . .  20
          8250  . . . . . . . . . . . . . . . . . . . . . . . . . . . .  18
          8250A . . . . . . . . . . . . . . . . . . . . . . . . . . . .  18
          82510 . . . . . . . . . . . . . . . . . . . . . . . . . . . .  20
          Addresses and IRQ for COM3 through COM8 on the PS/2 . . . . .  17
          Addresses and IRQs for COM1 and COM2  . . . . . . . . . . . .  17
          Appendix A, Hardware Notes  . . . . . . . . . . . . . . . . .  17
          Appendix B, SIO Chips . . . . . . . . . . . . . . . . . . . .  18
          Appendix C, Multi-Port Serial I/0 Cards . . . . . . . . . . .  21
          B option, Locking Baud, Data, Parity and Stop bits  . . . . . . 6
          Baud rates  . . . . . . . . . . . . . . . . . . . . . . . . . . 7
          BIOS RAM  . . . . . . . . . . . . . . . . . . . . . . . . . . . 9
          CAPTURE . . . . . . . . . . . . . . . . . . . . . . . . . . . . 8
          COMn and PORTn  . . . . . . . . . . . . . . . . . . . . . . . . 5
          CONFIG.SYS  . . . . . . . . . . . . . . . . . . . . . . . .  4, 5
          Defacto standard for COM3 and COM4  . . . . . . . . .  11, 17, 21
          Defer . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 7
          DESQview  . . . . . . . . . . . . . . . . . . . . .  4, 8, 13, 16
          DV  . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 8
          Eliminate . . . . . . . . . . . . . . . . . . . . . . . . . . . 7
          FIFO  . . . . . . . . . . . . . . . . . . . . .  8, 9, 15, 19, 20
          FOSSIL  . . . . . . . . . . . . . . . . . . . . . . . . . . . . 1
          GETTING STARTED . . . . . . . . . . . . . . . . . . . . . . . . 4
          IRQ SHARING . . . . . . . . . . . . . . . . . . . . . . . . .  16
          Licensing Information . . . . . . . . . . . . . . . . . . . . . 2
               Commercial License . . . . . . . . . . . . . . . . . . . . 2
               Non-Commercial License . . . . . . . . . . . . . . . . . . 2
          Locked  . . . . . . . . . . . . . . . . . . . . . . . . . . . . 6
          Locking . . . . . . . . . . . . . . . . . . . . . . . . . . . . 6
               Baud . . . . . . . . . . . . . . . . . . . . . . . . . . . 6
               Data . . . . . . . . . . . . . . . . . . . . . . . . . . . 6
               Parity and Stop bits . . . . . . . . . . . . . . . . . . . 6
               Valid locked baud rates  . . . . . . . . . . . . . . . . . 7
          Mapping port assignments  . . . . . . . . . . . . . . . . . .  10
          Multi-Tasking . . . . . . . . . . . . . . . . . . . . . . . .  13
          NOFIFO  . . . . . . . . . . . . . . . . . . . . . . . . . . . . 9
          NOPOST  . . . . . . . . . . . . . . . . . . . . . . . . . . . . 9
          Number of data bits . . . . . . . . . . . . . . . . . . . . . . 7
          Number of stop bits . . . . . . . . . . . . . . . . . . . . . . 7
          Parity bit  . . . . . . . . . . . . . . . . . . . . . . . . . . 7
          PKUNZIP . . . . . . . . . . . . . . . . . . . . . . . . . . . . 4
               Authentic files  . . . . . . . . . . . . . . . . . . . . . 4








                                                                         24

          Port assignments  . . . . . . . . . . . . . . . . . . . . . .  10
          Quick Start . . . . . . . . . . . . . . . . . . . . . . . . . . 4
          R, Set Receive Buffer Size  . . . . . . . . . . . . . . . . 9, 10
          RBBS  . . . . . . . . . . . . . . . . . . . . . . . . . . . .  16
          SIO . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 1
          SIO Chips . . . . . . . . . . . . . . . . . . . . . . . . . .  18
          SLOWCPU . . . . . . . . . . . . . . . . . . . . . . . . . . . . 9
          Specifying number of ports  . . . . . . . . . . . . . . . . . . 6
          T, Set Transmit Buffer Size . . . . . . . . . . . . . . . . .  10
          Terminate and Stay Resident . . . . . . . . . . . . . . . . . . 5
          THE BIOS INT 14h EMULATOR . . . . . . . . . . . . . . . . . .  15
          TSR . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 5
          Uninstalling X00  . . . . . . . . . . . . . . . . . . . . . .  12
          VP or Master Interrupt Enable . . . . . . . . . . . . . . . .  10
          Warranty  . . . . . . . . . . . . . . . . . . . . . . . . . . . 1
          WHAT IS X00 . . . . . . . . . . . . . . . . . . . . . . . . . . 1