ZIP.DOC                                                               Page 1

ZIP, the Zip Code Insulation Program, is a public domain computer program
developed by the National Institute of Standards and Technology (NIST,
formerly the National Bureau of Standards) under the sponsorship of the United
States Department of Energy (DOE)*.  As ZIP is in the public domain, it may be
copied and distributed freely.  

The following narrative is taken from the User's Guide to ZIP 1.0, the Zip
Code Insulation Program (ORNL/TM-11009 or NISTIR 88-3801).  For information on
how to obtain this Guide, write to      
        David McElroy
        Oak Ridge National Laboratory
        Bldg 4508, Mail Stop 6092
        PO Box 2008
        Oak Ridge, TN 37831-6092

ZIP 1.0, the ZIP-Code Insulation Program, determines economic levels of
insulation for attics, exterior walls, floors over unheated areas, slab
floors, and basement and crawlspace walls for new and existing houses in any
3-digit ZIP Code location in the United States.  The economic levels are based
on climate data and energy prices for the specific location, the type of
heating and cooling system in the house, and current installed insulation
prices.  ZIP runs on an IBM-PC or compatible microcomputer, with or without a
printer.  Default energy and insulation price data are provided on the ZIP
disk.  However, the resulting calculations are improved if the user provides
estimates of current energy and insulation prices at the building site, as
requested during the analysis.

The original ZIP program was written to calculate economic levels of
insulation reported by 3-digit ZIP Code in the Department of Energy's
Insulation Fact Sheet (DOE/CE-0180, 1987).  This program has now been
enhanced and documented for more general use.  The version of ZIP described
here is intended for use by any government or private agency (such as a
utility) being asked to provide advice to consumers on economic levels of
insulation for new or existing houses.  ZIP can also be used by insulation
manufacturers, insulation installers, and by homeowners (either on their own
personal computer or at some central location such as a home show, utility
office, or energy conference).  Where local building codes have more
stringent insulation requirements than those calculated by ZIP, the former
will of course take precedence.

ZIP and its supporting data files are all provided on a single 5-1/4 inch
floppy disk for use with microcomputers having an MS-DOS operating system
(typical IBM-PC/XT/AT and compatible systems).  Both a compiled and source-
code version of the program are provided.  The compiled version can run by
typing "ZIP" at the ready prompt.  The source-code, written in Microsoft
QuickBASIC 4.0, is provided for documentation purposes only and must be
recompiled, using the QuickBASIC compiler, if any changes are made.


----------
*  Neither NIST nor DOE assumes any liability resulting from the use of the 
information provided by the ZIP program or from any errors or omissions in the
program.
ZIP.DOC                                                               Page 2


The economic levels of insulation calculated by ZIP are based on an
incremental type of analysis.  Successive levels of insulation in each part of
the house are evaluated independently to determine how far it pays to keep
adding insulation and when to stop.  For example, in an attic an economic
analysis is performed at R-0 (no insulation), R-11, R-19, R-22, R-30, R-38,
and R-49, each time adding just enough insulation to the previous level to get
to the new level. As long as increasing the level from one R-value to the
next is found to be cost effective, that increment will be included in the
report of cost effective insulation levels for that location.  If it is not
cost effective, that increment will not be included.  In general, the colder
the climate and the higher the cost of energy, the more it pays to add
insulation and the higher the economic levels resulting from the analysis.  

Economic calculations are based on a reduction in long-term heating and
cooling costs.  For new houses, a thirty-year life is used in calculating the
economic level of insulation.  That is, the economic level of insulation
calculated for a new house will be the level which has the lowest combined
insulation cost plus energy cost over a thirty-year period.  For existing
houses, a twenty-year life is used in the calculations.  

In performing these calculations, a minimum seven percent annual rate of
return, over and above general inflation, is used to discount future savings
to present value.  If inflation is currently five percent, this is
approximately equivalent to requiring a minimum twelve percent rate of return
on the investment.   Each increment of insulation must earn at least this much
"interest" to be considered cost effective.  Residential energy savings are
not taxed, so that this is in effect an after-tax rate of return on
investment.  Moreover, the first increments of added insulation typically
return much higher dividends than the last increment.  Thus the average rate
of return tends to be considerably higher than the minimum acceptable level.

The results of the economic analysis for the designated location are displayed
on the screen, as shown in screen 1.1 for a new house in ZIP Code 809XX
(Colorado Springs).  The reference location is typically the location
designated by the U.S. Postal Service as the main post office for the three-
digit ZIP Code. The number of annual heating degree days (base 65F) and
cooling degree hours over 74F are shown for the designated location, along
with the heating and cooling systems used in the analysis.  

Screen 1.1 shows the screen display of economic levels for all of the
components that can be evaluated by ZIP.  In general, however, economic levels
are displayed only for those components selected for analysis by the user for
the particular application.  Screen 1.2 shows additional information for
floors over crawlspaces and crawlspace walls that can be displayed by pressing
<PgDn>.  To return to the ZIP analysis screen, press <PgUp>.

Energy savings and their estimated dollar value computed in the analyses are
not shown in the screen display.  These calculations are based on uniform
surface areas for a typical house under average operating conditions for a
typical year.  They would not provide any meaningful estimate of savings for
the user's house.  
ZIP.DOC                                                               Page 3

Note that the economic levels of insulation both under floors over crawlspace 
and on crawlspace walls are shown.  However, only one of these would be used
in most houses.  For crawlspaces that do not need ventilation and can be
closed off, it is usually more economical to insulate the walls than the floor
if the wall area is less than the floor area.  If the crawlspace cannot be
safely closed off, the floor above should be insulated instead.  In this
latter case, care must be taken to insulate water pipes and any ductwork in
the unheated area.  



             Screen 1.1.  Display of ZIP Analysis for New House
ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
º                  Economic Insulation Levels for Zip 809XX                  º
º                  Reference Location: Colorado Springs, CO                  º
º   Heating system: HEAT PUMP               Cooling system: HEAT PUMP        º
º -------------------------------------------------------------------------- º
º                            New House Construction                          º
º                                                                            º
º                Attic Insulation                            R-38            º
º                Wood-Frame Wall Insulation                  R-19            º
º                Masonry Wall Insulation                     R-11            º
º                Floors over Crawlspace                                      º
º                   (If crawlspace walls are uninsulated)    R-30            º
º                Crawlspace Wall Insulation                                  º
º                   (If floor above is uninsulated)          R-19            º
º                Slab-Edge Insulation                        R- 4            º
º                Insulation of Basement Walls:                               º
º                 Exterior Insulation for Deep Basement      R- 8            º
º                 Interior Insulation for Deep Basement      R-11            º
º                 Exterior Insulation for Shallow Basement   R- 8            º
º                 Interior Insulation for Shallow Basement   R-11            º
º                                                                            º
º -------------------------------------------------------------------------- º
º                    Press <PgDn> for additional information.                º
º             Press <SHIFT> <PrtSc> to print this screen if desired.         º
º                  Press <ESC> to exit, R to do another analysis:            º
ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼




The insulation levels and corresponding costs in the insulation data file used
by the ZIP program are the same for both new and existing houses, with the
exception of the insulation for exterior wood-frame walls.  In new houses, it
is much less costly to insulate a wall before the inside surface is finished
than it is to blow insulation into an existing wall cavity.  Moreover, for a
house under construction, thicker walls or insulated sheathing can be used to
improve the its overall insulation effect, while in a completed house, the
addition of insulation is generally limited to the available cavity in the
existing wall.  

ZIP.DOC                                                               Page 4

                                 Screen 1.2
ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
º                          Additional information                            º
º                                                                            º
º       Insulate either the floor over the crawlspace or the crawlspace      º
º       walls, not both.  Consult an insulation specialist to determine      º
º       which is more appropriate for your house.                            º
º                                                                            º
º       Crawlspace walls should only be insulated if the crawlspace is       º
º       closed off, unventilated, and dry all year.   The ground should      º
º       be covered with a vapor barrier (e.g., 4- or 6-mil polyethylene      º
º       sheeting) to minimize moisture migration into the crawlspace.        º
º       Note: some building codes may not allow unventilated crawlspaces.    º
º       If radon gas is a problem at the building site, closing off the      º
º       crawlspace may not be advisable.                                     º
º                                                                            º
º       When insulating floors over crawlspaces or other unheated areas,     º
º       make sure that water pipes are freeze-protected and ductwork is      º
º       well insulated in those areas.                                       º
º                                                                            º
º -------------------------------------------------------------------------- º
º             Press <SHIFT> <PrtSc> to print this screen if desired.         º
º                Press <PgUp> to show economic insulation levels:            º
º                                                                            º
ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼


Five different heating systems are recognized in the ZIP program: natural gas,
oil, and electric furnaces, electric baseboard, and electric heat pump.  Two
different cooling systems can also be handled: central and window electric air
conditioners.  (An evaporative cooling system can also be specified, but this
is not treated as a true air conditioning system.)  In addition, the user can
specify the approximate operating efficiency of the heating and cooling
systems (low, medium, high, or very high).  These system specifications are
needed to determine the energy savings corresponding to any given level of
insulation.  If there is ductwork in attics, crawlspaces, or other unheated
areas, an adjustment is also made to the equipment efficiency in order to
reflect duct losses.

ZIP will run on an IBM-PC/XT/AT or compatible MS-DOS microcomputer with
approximately 256 K of random access memory (RAM).  A printer is also useful
-- but not necessary -- for making hard copies of the ZIP screen displays. 
With a printer, any screen display can be printed by holding down the <Shift>
key and pressing <PrtSc> (or equivalent command).

ZIP.DOC                                                               Page 5

The following files can be found on the original ZIP disk:

     ZIP.EXE        The executable version of ZIP. 
     CLIMATE.DAT    A file of climate data, keyed to three-digit ZIP Codes.
     INSCOST.NEW    A file of default insulation price data for new houses.
     INSCOST.RET    A file of default insulation price data for existing
                         houses.
     ZIP.BAS        The source code version of ZIP.  
     ZIP.DOC        A short explanation of the ZIP program.

Files of default energy price projections for DOE regions 1 through 10:*

     ENPRICES.1           ENPRICES.4           ENPRICES.7  
     ENPRICES.2           ENPRICES.5           ENPRICES.8  
     ENPRICES.3           ENPRICES.6           ENPRICES.9  
                                               ENPRICES.10 
                             


All of these files (except ZIP.BAS and ZIP.DOC) are needed to run ZIP.  Copy
these files to a new disk for running the program, and store the original disk
in a safe place.  There is no disk operating system (DOS) on the original ZIP
disk.  Thus you should copy the files on this disk to a disk which has been
formatted with DOS or to your fixed (hard) disk.  If you are copying these
files to a fixed disk, you might want to copy them to a subdirectory named
ZIP.

To start the program, simply type ZIP at the ready prompt (e.g., A> ZIP ) and
press the carriage return <CR> (sometimes labeled as the <ENTER> key).  All
user entries must be completed by pressing <CR>.  The initial screen will
prompt you for the first three digits of the ZIP Code for the location to be
analyzed.  For example, someone living in ZIP Code area 333 (Florida) would
enter 333.  

Additional prompts for heating and cooling equipment types and efficiencies,
fuel costs, components to be evaluated, and insulation costs will be
displayed.  After completing these queries, ZIP will display the economic
levels of insulation and additional related information.

-----------
* DOE regions are as follows:
1 ME, NH, VT, MA, CT, RI                 6 TX, NM, OK, AR, LA
2 NY, NJ,                                7 KA, MO, IA, NE
3 PA, MD, WV, VA, DC, DE                 8 MT, ND, SD, WY, UT, CO
4 KY, TN, NC, SC, MS, AL, GA, FL         9 CA, NV, AZ, HI
5 MN, WI, MI, IL, IN, OH                10 WA, OR, ID, AK


ZIP.DOC                                                               Page 6



        A technical note on the default energy and insulation prices 
             accessed by ZIP from the ENPRICES and INSCOST files

All prices, as displayed on the screen, are currently expressed in 1988
dollars.  They are automatically converted to 1988 dollars from 1985 dollars
(as they are stored on the disk) using a 12 percent cumulative inflation
factor (i.e., a GNP deflator of 1.12) over the three year period.  If you
intend to change the default prices in the data files you must be careful to
specify the proper inflation factor (i.e., GNP deflator) in these data files. 
If, for example, you change these price data in the files to 1989 dollars for
use in 1989, then the GNP deflator should be set to 1.0 (i.e., zero cumulative
inflation).  If you wish to retain the price data currently in the files but
want to convert it to a later year (e.g., 1989) in the screen display, you
must change the GNP deflator in the files to reflect the cumulative inflation
from 1985 to date.  These changes can be made with a simple text editor,
saving the file in the text (ASCII) mode when finished.  See the ZIP User's
Guide, pages 26 and 27, for the format of the insulation price files.  Pages
24, 25 and 29 show the format for the energy price files.

Note that the energy price projections in the ENPRICES files must be stated in
constant dollars, i.e., net of general price inflation.  The year in the
second line (1985 in the current file) designates the first year for which a
price is given.  The integer on the third line (26 in the current file)
designates the number of years for which prices are contained in the file. 
The current year for screen display is determined from the clock in your
computer; therefore it must be set to the proper year.  The current price for
screen display is based on the price for the current calender year, multiplied
by the GNP deflator in the file.  The energy prices for future years contained
in the ENPRICES file are used to determine the rate of energy price increase
from year to year (net of general inflation), regardless of whether you use
the default prices or enter your own price.  That is, if the 1988 price for
natural gas is 7.02 and the 1989 price is 7.47, then the implicit assumption
is that natural gas prices will rise at a rate 6.4% greater than prices in
general for that year.  If the number of prices in the price file is less than
the period of analysis (20 years for existing houses, 30 years for new
houses), a zero energy price increase is assumed for those years in which no
energy prices are available.