Graphic Adapter Compatibility
-----------------------------

This short technical document is intended for vendors or
manufacturers of "clone" video display adapters which claim
full compatibility with the IBM standard, but do not comply
with some documented hardware features of the Motorola 6845
CRT controller, used in the IBM MDA, CGA, and VGA.

The original IBM Color Graphics Adapter (CGA) was equipped with
a Motorola 6845 CRT controller chip.  As implemented in the IBM
PC's BIOS, the CGA supports 8 background colors and 16
foreground colors in text mode (BIOS video modes 0 thru 3).  In
addition, the foreground can be made to blink by adding 128 to a
non-blinking color attribute byte.  All IBM and fully-compatible
EGA and VGA adapters also support these CGA text modes.

The ability to have a blinking foreground can be exchanged for
the ability to have a high-intensity background.  In the
Motorola 6845, this is done by setting bit 5 of the Mode Select
Register.  The MSR is a 6-bit, write-only register mapped at I/O
address X'3D8' for the CGA and address '3B8' for the MDA.
When bit 5 is set, adding 128 to the color attribute byte of a
character will cause that character's background to become a
high-intensity color.  This feature is fully documented in the
IBM PC Technical Reference Manual, pages 2-55 through 2-65 (CGA)
and page 2-46 (MDA).

This feature was formalized when IBM introduced the EGA and the
EGA BIOS extension.  Video interrupt 10h, EGA BIOS function 10h,
subfunction 03h allows the programmer to chose between
foreground blinking and background intensity.  This is a
documented feature of the PCJr, EGA, VGA and MCGA video
adapters.

Any EGA, VGA, or MCGA which claims IBM compatibility should
fully support this function.   For CGA and MDA, hardware and
register-level compatibility is required -- the adapter must
have a Mode Select Register mapped at I/O address X'3D8'.  For
EGA/VGA, and MCGA, the adapter's ROM must support the proper
video BIOS functions to implement this feature.

If the feature is not supported, attempt to write to the 
non-existent hardware register will cause unpredictable video
behavior and possibly total system lockup.