PIPEDATA V3.0 (TM)

                                  DOCUMENTATION
                  Copyright (C) 1984, 1987, 1988 by R.L. Guillen
                               All Rights Reserved







                                      - * -
                            Ventura Publishing Company
                       P.O. Box 6718, Kennewick, Wa. 99336




































 


          Page 1.
          PIPEDATA V3.0
          (C) 1988 by R.L. Guillen
          


                               TABLE OF CONTENTS 




          INTRODUCTION                                          Page 3

          PRELIMINARY INSTRUCTIONS                                   4 
            Backing Up Your Diskette                                 5
            Starting the program                                     5

          DETAILED OPERATING INSTRUCTIONS                            6
            The Screen Editor                                        6
              Input Column Editor                                    7
              Input Error Detection                                  8
              Input Column Cursor Control                            8
              Input Column Variables                                 9
            Keyboard Commands                                       11
              C Key - Calculate Command                             11
              H Key - Help Command                                  11
              M Key - Erase Help Window Command                     12
              Z Key - Clear Entry (Zap) Command                     12
              P Key - Print out report Command                      12
              Q Key - Quit the Program Command                      12
              R Key - Reset the Program Command                     12
            Program Basis                                           13
          BACKGROUND                                                14






























 



          Page 2.
          PIPEDATA V3.0



                                PIPEDATA V3.0  (TM) 

                     Copyright (C) 1984,1988 by R.L. Guillen
                          All Rights Reserved Worldwide.
                                      - * -

          The author reserves all commercial rights  to  this  program.
          The author does allow that this program be freely distributed
          and shared with others,  provided that it is not sold or that
          any consideration of its use is charged.  The author requests
          that if you like this program and use it in your job ,or work
          that you register its use.  If you work for a company and you
          use it in your job then you or your company must register it,
          or you and your company may be liable for infringement of its
          commercial use.  The word "use" means that you implement this
          program  to  help  you do any part of your work,  and you get
          paid for that time.  You are free to evaluate its use, but if
          you decide to use it, you must register it.  This manual must
          accompany the program on the diskette, and must not be copied
          in printed form by any means whatsoever  without the  written   
          permission from the author.   Violators will be prosecuted.

                                    TRADEMARK 

          PIPEDATA V3.0   is a trademark of Ventura Publishing Company.
          IBM-DOS is a trademark of International Business Machines.
          MS-DOS is a trademark of Microsoft, Inc.


                                    DISCLAIMER 

          This  software  was  created  from  sources  believed  to  be
          reliable.  No  intent  has  been made to make this program an
          educational medium,  only a calculation tool to  be  used  by
          those  that  are familiar with Fluid Mechanics,  or a similar
          field.  Software should always be used at the  discretion  of
          the  user,  and  therefore  we can only offer it on an "AS IS
          BASIS" to anyone wishing it.  This program is offered without
          warrantee of any kind,  expressed or implied,  including  fit
          for any merchantable purpose,  quality, or workmanship of any
          kind whatsoever.  The sole decision to use or not to use  the
          software provided,  therefore, rests soley with the user, and
          the user agrees that by using this software,  that he or  she
          agrees not to hold the author, or the authorized publisher of
          this program responsible for any liability due to its use, or
          any  inability   to   use   it   whatsoever,   consequential,
          incidental,  or otherwise,  including but not limited to loss
          of earnings, profits, damages of any kind, or by any claim by
          any other party even when advised of the possibility of  such
          damages.  No  warrantees  are expressed or implied to correct
          program errors  or  "bugs",  nor  shall  the  author  or  his
          authorized publisher be liable to correct,  or advise of them
          at any time.  Thoroughly test before relying on it.




 



          Page 3.
          PIPEDATA V3.0




                                  INTRODUCTION 


          PIPEDATA V3.0  is a compiled computer program written for the
          IBM PC, PCjr.,  and all IBM/MS-DOS compatibles.  This program
          allows  the  engineer  to rapidly calculate piping resistance
          losses used  to  size  piping.  Components  involve  straight
          pipe, pipe elbows (45 and 90 degree bends), gate valves, ball
          valves,  swing check valves,  globe valves,  and user defined
          elevation changes.

          The  program  is  based  on  the  Darcy  equation  which   is
          applicable to incompressible,  and compressible (with certain
          restrictions on the amount of  pressure  drop)  fluid  flows.
          The program uses the pipe fitting and valve K factor formulas
          as  found in Crane Technical Paper No.  41O,  which is widely
          known and used,  and state of the art explicit equations that
          determine  friction  factors without iterative or convergence
          calculations for  determining  fluid  pressure  drop  through
          round circular pipe.  All the component calculation equations
          are built-in to the program.

          The  program  has an easy to use editor that is ideal for use
          in repetitive,  or investigative "What If" situations for all
          components  used in this program.  A window provides the user
          with commercial pipe sizes and pipe schedule dimensional data
          for  steel  pipe up to 36 inches in size when needed.  If you
          need a much more powerful  program  than  this  one,  may  we
          suggest  our  Pipeflow (TM) program which is described in one
          of the help menu window items.


























 



          Page 4.
          PIPEDATA V3.0



                             PRELIMINARY INSTRUCTIONS 


          This  section  provides  the  preliminary steps that the user
          should take before loading and running the  program  diskette
          on  the  computer.  As  with  all computer software,  certain
          precautions should always be followed  before  executing  any
          new program.



                             Backing Up Your Diskette 


          Before using your PIPEDATA  program  you  should  backup  the
          master diskette obtained,  onto  another diskette called your
          "Working Diskette".  This single working diskette should then
          be labeled PIPEDATA (TM) V3.0 ,  Copyright (C) 1984,  1988 by
          R.L.  Guillen.  You  should  then  store  the master diskette
          provided in a safe  place.  The  copy  procedure  may  be  as
          follows, for a two floppy drive IBM/MS DOS computer.

          1.  Load your DOS diskette into your A drive, and turn on the
              computer master switch for a boot startup.

          2.  Load  a fresh diskette into the B drive of your computer,
              this will be your working diskette.  If the  diskette  is
              unformatted, then follow the following procedure in order
              to format your diskette, using your B drive.

              a.) To  format  your diskette in the B  drive,  enter the
                  following information  at  the  DOS  prompt  of  your
                  screen, so that your screen shows the following:

                                  A>FORMAT B:/S 

              b.) Then press your ENTER key, hereon to be designated as
                  <CR>.  The  "/S"  will copy the system BIOS,  and the
                  COMMAND.COM file onto your new diskette,  and make it
                  a bootable diskette.

          3.  After  formatting  the  B  diskette,  take  out  the  DOS
              diskette from the A drive,  and store it in a safe place.
              Insert the PIPEDATA master diskette provided into  the  A
              drive  now.  Leave  the formatted diskette in the B drive
              of your computer to be used as your single working copy.


          4.  At the DOS prompt of your computer, type the following on
              your keyboard.







 



          Page 5.
          PIPEDATA V3.0



                               COPY PIPEDATA.COM B: 

              so that your computer screen shows the following:

                              A>COPY PIPEDATA.COM B: 

              then press <CR>.

          5.  After  copying  your  master  diskette,  do  a  directory
              listing of your B drive, and you should see that you have
              copied the PIPEDATA.COM  file.  Now,  remove  the  master
              diskette from the A drive,  and store it in a safe place.
              Also remove the working diskette in  your  B  drive,  and
              place  it in the A drive.  You are now set to start using
              the PIPEDATA  program.



                                Starting PIPEDATA 


          If you followed the previous instructions you are now set  to
          start  using  the  PIPEDATA   program.  You should see the DOS
          "A>" prompt on the left side of your computer screen.

          To start the program, type PIPEDATA, or PIPEDATA.COM   after
          the DOS prompt, so that your computer looks as follows:

                                  A>PIPEDATA.COM 

          Then  if everything is alright,  press your <CR> key to start
          the execution of your program.  Upon execution, your computer
          screen will roll  up  to  show  the  opening  screen  of  the
          PIPEDATA  program.  The  opening screen will request that you
          enter any key on your keyboard to proceed.  Press any  letter
          key.

          Upon pressing any key, the PIPEDATA computer screen will look
          somewhat as noted on the next page with the preset values:


















 



          Page 6.
          PIPEDATA V3.0



     -----------------------------------------------------------------------
     PIPEDATA V3.0, (C) Copyright 1988, by R.L. Guillen, All Rights Reserved

     DATA VARIABLES----  INPUTS:            CALCULATIONS:     RESULTS:
     Fluid Temp. deg,F->_60                 Pipe nom. size =
     Init. Pressure,psi                     Pipe Vel., fps =
     Density- lb/ft^3 -  62.371             Reynolds Number=
     Viscosity- Cp ----  1.2                Friction Factor=
     Pipe Roughness----  .00015             Total Dp, psi  =
     Flow Rate- GPM ---                     Component Dp,  =
     Pipe ID. Inches --
     Pipe Length, Feet-  100
     Qty 90ø Std Elbows
     Qty 45ø Std Elbows                 Note: _ is the blinking cursor,
     Qty Ball Valves --                       and > is the input pointer.
     Qty Gate Valves --
     Qty Globe Valves -                 The number under the INPUTS: column
     Qty Swing Checks -                 show that the program is preset to
     Elevation change -                 the input variable for 60 degree
     (+/-) feet of head                 water flowing through clean steel
      + = up, - = down                  pipe, having a length equal to 100
                                        feet in length.



     Z-Zap  H-Help Menu  C-Calculate  A-Add  P-Print report  R-Reset  Q-Quit
     ------------------------------------------------------------------------



                         DETAILED OPERATING INSTRUCTIONS 


          This  section  presents the detailed keyboard usage necessary
          to control the PIPEDATA program.


                                The Screen Editor 


          The  PIPEDATA Screen consists of basically three screen parts
          that enable a  single  screen  for  data  input,  calculation
          output,  and  a  window area that displays the help files and
          the PIPEDATA subprogram window.  These can be seen  as  shown
          in the following example:












 



          Page 7.
          PIPEDATA V3.0



     -----------------------------------------------------------------------
     PIPEDATA V3.0,(C) Copyright 1988, by R.L. Guillen, All Rights Reserved
                                       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
   * DATA VARIABLES----  INPUTS:       ³    CALCULATIONS:     RESULTS:    ³
                         ÚÄÄÄÄÄÄÄÄÄ¿   ³                      ÚÄÄÄÄÄÄÄÄÄ¿ ³
     Fluid Temp. deg,F->_³         ³   ³    Pipe nom. size =  ³   O C   ³ ³
     Init. Pressure,psi  ³    I    ³   ³    Pipe Vel., fps =  ³   U O   ³ ³
     Density- lb/ft^3 -  ³    N    ³   ³    Reynolds Number=  ³   T L   ³ ³
     Viscosity- Cp ----  ³    P    ³   ³    Friction Factor=  ³   P U   ³ ³
     Pipe Roughness----  ³    U    ³   ³    Total Dp, psi  =  ³   U M   ³ ³
     Flow Rate- GPM ---  ³    T    ³   ³    Component Dp,  =  ³   T N   ³ ³
     Pipe ID. Inches --  ³         ³   ³                      ÀÄÄÄÄÄÄÄÄÄÙ ³
     Pipe Length, Feet-  ³    C    ³   ³   THIS IS THE PIPEDATA WINDOW    ³
     Qty 90ø Std Elbows  ³    O    ³   ³ ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ ³
     Qty 45ø Std Elbows  ³    L    ³   ³ ³                              ³ ³
     Qty Ball Valves --  ³    U    ³   ³ ³                              ³ ³
     Qty Gate Valves --  ³    M    ³   ³ ³                              ³ ³
     Qty Globe Valves -  ³    N    ³   ³ ³                              ³ ³
     Qty Swing Checks -  ³         ³   ³ ³                              ³ ³
     Elevation change -  ÀÄÄÄÄÄÄÄÄÄÙ   ³ ³   THIS IS THE HELP WINDOW    ³ ³
     (+/-) feet of head                ³ ³                              ³ ³
      + = up, - = down                 ³ ³                              ³ ³
                                       ³ ³                              ³ ³
   * NOTE: Changing any variable in the³ ³                              ³ ³
     input column will reset all the   ³ ³                              ³ ³
     output column values to zero.  So ³ ³                              ³ ³
     to get the latest calcs, press the³ ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ ³
     C key to calculate these.         ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
     Z-Zap  H-Help Menu  C-Calculate  A-Add  P-Print report  R-Reset  Q-Quit
     ------------------------------------------------------------------------


                               Input Column Editor 

          The PIPEDATA program has a small keyboard editor that  allows
          entering  numerical  data  in an efficient manner for problem
          variable  definition.  The  editor  is  set  to  control  the
          keyboard  for  numerical  problem  input,  and  keyboard  key
          commands that are inherent to producing calculations,  and in
          showing program help file  windows.  Primarily,  the  program
          allows  entering  only  numbers.  The  following  letters are
          valid for input data, since these are used extensively in the
          literature with mathematical numbers: ".", "+", "-", and "E".
          An example of a number using these letters,  as may  be  used
          for  numerical  entries  in  this  program,   is  the  number
          1.097E+9, and another is +11.23E-09.  The use of the + on the
          left side is not necessary for identifying positive  numbers.
          In  this  program,  negative  numbers  are  not  accepted for
          problem entries.  Note:  Entering negative numbers for  input
          data variables will cause the programs' input error detection
          schemes  used  during  calculation's  to detect the numerical
          entry as an input error. (Except for the elevation input.)





 



          Page 8.
          PIPEDATA V3.0



                              Input Error Detection 

          During keyboard number entry there is an input error scanning
          subroutine that will question the user if  a  possible  input
          error  is  detected  as  a value is entered.  This subroutine
          will check to see that the entry is a  number,  by  comparing
          the  length  of the entry to its value.  This subroutine will
          detect some common input errors.  Should you hear a beep, and
          see the words "INPUT ERROR?" appear over  the  input  column,
          check  your entered information.  If you do not encounter any
          errors,  please  do  not  panic,   just  check  your  entered
          information,  and  if  it  is adequate continue entering your
          data.  As an example of this,  if you were to enter ".00" the
          beep  will  sound  and  the question will be posed for you to
          check your input, and if it is adequate,  you can continue to
          type  in,  so that if the entered value is ".009" the program
          will then consider your entered value to then be an  adequate
          number  and  the "INPUT ERROR?" question will disappear.  The
          program is also error trapped to avoid division by zero,  and
          in  such  cases  where  this  could  happen  the  program  is
          sufficiently protected,  and will request that the particular
          variable  that the program finds affecting the calculation as
          in error to be re-entered correctly.  Particularly, note that
          when the program beeps, and the words "INPUT REQ.=*"  appears
          over the input variable column, and an "*"  appears in one of
          the input variable slots,  that this means that  the  program
          has  detected  an  absolute  input  error  at  the  indicated
          variable,  and prevents further program execution.  The  user
          is advised that he then correct the indicated data.


                           Input Column Cursor Control 

          This program  utilizes  five  cursor  control  keys  for  the
          purpose  of entering problem data,  and for making changes to
          the problem data.  Five cursor control keys are used  in  the
          program for data entry purposes and are as follows:

            Cursor Up Key     - moves the input pointer and cursor  up.
            Cursor Down Key   - moves the input pointer and cursor down.
            <CR>  Key         - moves the input pointer down only.  This
                                key  does  not  need  to  be  used   for
                                entering  information,  and is available
                                for those that  are  used  to  "entering
                                numbers".
            Del Key          -  deletes the rightside of an entry.
            Backspace Key    -  deletes the rightside digit of an entry.

          Note:  Use of the above keys is not available while accessing
          the PIPEDATA window.







 



          Page 9.
          PIPEDATA V3.0



                              Input Column Variables 

          The program allows the  user  to  define  the  value  of  any
          program variable in the input column.  The user is limited to
          enter  numbers  up  to ten digits maximum,  including decimal
          points, and the letters that are often used with numbers, all
          previously mentioned.  Numbers entered that exceed ten digits
          in length will cause the program to print "INPUT  ERROR?"  as
          mentioned,  and  will  not  allow  the user to enter any more
          numbers for the value of the variable being  defined  in  the
          input  column.  An  explanation of each input column variable
          as used in the program is as follows:  (Refer to the Keyboard
          Command  section  for  certain  letter key commands listed in
          this section.)

          a.) FLUID  TEMPERATURE  VARIABLE - The fluid temperature,  is
              preset by the program to 60 degrees Fahrenheit to reflect
              other preset variable values  used  in  the  program  for
              water.  This  data variable is not a required variable in
              the  program,   and  is  available  solely  for  use   in
              referencing   the   temperature   of   any   fluid  being
              considered.  Leaving this variable blank,  has no  effect
              on program operation.

          b.) INITIAL  PRESSURE VARIABLE - The initial  pressure of the
              fluid in units of pounds per square inch,  is also not  a
              program  required  variable,  as  is  the  case for fluid
              temperature.  Leaving this variable blank,  has no effect
              on  program operation,  and is intended for reference use
              only.

          c.) DENSITY VARIABLE - The density of the fluid  is  required
              in  all  cases,  and  is requested in units of pounds per
              cubic foot.  The program preset value  is  62.371,  which
              corresponds  to  the density of water at 60 degrees,  and
              one atmosphere.  The user is not restricted to  use  only
              this value, and may change it at any time, to whatever is
              necessary  for  any  fluid  being considered.  This value
              must be greater than zero.

          d.) VISCOSITY VARIABLE - The fluid viscosity is  required  in
              all cases,  and is requested in units of centipoise.  The
              program preset value is 1.2,  which  corresponds  to  the
              viscosity  of  water  at 60 degrees,  and one atmosphere.
              The user is not restricted to use this  value  only,  and
              may  change it at any time,  to whatever is necessary for
              the fluid being considered.  This value must  be  greater
              than zero.









 


          Page 10.
          PIPEDATA V3.0




          e.) PIPE  ROUGHNESS  VARIABLE - The  roughness of the pipe is
              required in all cases,  and is required in  dimensionless
              form.  The  program preset value of .00015 corresponds to
              new  clean  commercial  steel  pipe.   The  user  is  not
              restricted to use only this value,  and may change it  at
              any time to whatever is necessary for the  pipe  material
              being considered.  This value must be greater than zero.

          f.) FLOW RATE VARIABLE - The fluid flow  rate  through  round
              circular pipe is required in all cases,  and is requested
              in units of standard gallons per minute.  This value must
              be greater than zero.

          g.) PIPE ID VARIABLE - The internal diameter of any  pipe  is
              required  in  all  cases,  and  is  required  in units of
              inches.  The  user  may  access help screen on pipe sizes
              for help on commercial steel pipe data, and answering all
              the prompted questions posed by  PIPEDATA.  The  user  is
              not  restricted  to  use  only  standard pipe dimensions.
              This variable when used with  pipe  fittings,  or  valves
              represents the pipe diameter.

          h.) PIPE LENGTH VARIABLE - The length  of  the  pipe  is  not
              required  input  for  all  cases,  such as for components
              other  than  pipe.  However,  the  value must not be less
              than zero.  The program preset value of 1OO feet is  used
              to  reflect  the often tablulated pipe length value,  and
              the user may change this variable to any length  of  pipe
              he wishes to find the pressure drop for pipe only.

          i.) QTY  90  DEGREE  ELBOWS - This  represents  the number of
              Standard 90 degree elbows in the pipe line.  This  number
              must not be less than zero.

          j.) QTY  45  DEGREE  ELBOWS - This  represents  the number of
              Standard 45 degree elbows in the pipe line.  This  number
              must not be less than zero.

          k.) QTY BALL VALVES - This represents  the number of Standard
              ball valves in the pipe line.  This number  must  not  be
              less than zero.

          l.) QTY GATE VALVES - This represents  the number of Standard
              gate valves in the pipe line.  This number  must  not  be
              less than zero.

          m.) QTY GLOBE VALVES - This represents the number of Standard
              globe valves in the pipe line.  This number must  not  be
              less than zero.








 


          Page 11.
          PIPEDATA V3.0




          n.) QTY  SWING  CHECK VALVES - This  represents the number of
              Standard globe valves in the pipe line.  This number must
              not be less than zero.

          o.) ELEVATION CHANGE - This represents the overall  elevation
              change in the piping between the two points considered in
              the  calculations.  Entering  a  positive number does not
              require  entering the "+" sign.  If it is a negative drop
              in elevation,  you do need to enter the "-" sign ahead of
              the number, such as "-200".


                                Keyboard Commands 

          In addition  to  the  keyboard  entry  of  numbers,  used  in
          defining  the  values  for any of the program variables,  the
          program accepts certain letter commands that execute  certain
          things.  Applicable  command  keys  are  always  shown on the
          bottom line of the program screen.  A  description  of  these
          letter  key  commands  is  as follows:  (Note - These are not
          accessible while using the PIPEDATA pipe size window.)

          C Key - Calculate Command 
          Pressing   this   key  will  tell  the  computer  to  do  the
          calculations using all entered values under the input column.
          The program will check to see that no information is  missing
          for any required input variable,  and if it is,  the "*" will
          be placed in  the  variable  that  the  program  beleives  is
          causing  a  problem  in  performing  a  calculation,  and the
          calculation will be aborted.  On the other hand, if there are
          no  detectable  errors,   the  program   will   execute   the
          calculation, and print the results under the output column on
          the upper right side of the screen.

          H Key - Help Command 
          Pressing this key will request the main help screen directory
          to appear in the  lower  right  side  of  the  screen.  After
          accessing this directory listing,  the only keys that work on
          the keyboard,  are  the  cursor  up,  cursor  down,  and  the
          numerical keys;  1,  2,  3,  etc., up to the maximum numbered
          item listed in the directory.  Pressing the number 1 key will
          automatically bring up that help file screen  to  the  window
          occupied  by  the  main  help  screen  window.  The  user may
          supersede the use of any directory item,  and still leave the
          directory listing on the window by pressing the cursor up, or
          cursor  down  keys,  and  continue  entering or editing input
          data.










 


          Page 12.
          PIPEDATA V3.0




          M Key - Erase Help Window 
          Pressing this key while using the editor will erase any  help
          screen  on the right side of the screen.  This command is not
          accessible during the use of the PIPEDATA subprogram.

          Z Key - Clear Entry (Zap) 
          Pressing  this key will erase any numerical input entered for
          any of the variables found on the input column,  and sets the
          value  of  the variable equal to 0.0,  even though the number
          0.0 will  not  appear  on  the  input  column.  This  key  is
          convenient in deleteing numbers with just one keystroke,  and
          then entering new values.  Think of this key as a ZAP key.

          P- Print report 
          Pressing this key will print a calculation report directly to
          the printer.  Use this key anytime to save a hard copy of the
          previously executed calculations or intermediate  calculation
          progressions.

          Q Key - Quit the Program 
          Pressing the Q key will cause the  program  to  emit  a  beep
          sound,   and   pose  a  question  to  the  user,   requesting
          acknowledgement on quitting the program and returning back to
          DOS,  or  of returning to the program.  The user must enter Y
          to resume quitting the program,  or if the user does not wish
          to terminate the program, must press any other key other than
          the Y key to return to the program.

          R Key - Reset the Program 
          Pressing  this  key  will  cause  the  program  to beep,  and
          question the user on whether to  Reset  the  program  to  the
          opening  screen,  or  to  resume  with the program set to the
          current values.  Entering the Y key results  in  the  program
          being  reset  to  the  original  opening screen,  and all the
          information is reset.  Entering any other key other than  the
          Y  will not affect current program settings.  This command is
          useful for resetting all of the parameters to  original  form
          with minimal editing.



















 


          Page 13.
          PIPEDATA V3.0




                                  Program Basis 


          This program is based on the general application of the Darcy
          equation.  The general statement of this equation is:


                          h = f x L x V^2 / (2 x g x D)        ( 1. )
                                                                    


          where the left side is expressed in terms of  feet  of  fluid
          column.

          a.) For straight pipe sections, valves, and fittings.

                     h = 0.00259 x K x Q^2 / d^4               ( 2. )


          b.) For pipe, fittings, valves:                      ( 3. )

          K = 12 x F x L / d  for pipe,     K = 30 x Ft for 90ø elbows.
          K = 16 x Ft for 45ø elbows,       K = 8 x Ft for gate valves.
          K = 3 x Ft for Ball valves,       K = 340 x Ft for globe valves.
          K = 100 x Ft for swing check valves,                 
                     
              where               K = F x L / D                ( 4. )

          The friction factor F  is  solved  in  this  program  by  the
          following equation.  ( 5.)

          F={-2 x Log[(E/(3.7d))-5.02 x Log((E/(3.7d))+(14.5/Re))]}^-2

          Known as the Shacham equation (Chemical Engineering, 12/4/81,
          page 91.).  Ft is at full turbulence, i.e.  Re >= 10 ^8.

          The equation appears quite complicated but  the  formula  has
          the  advantage of not requiring an iterative solution for the
          friction factor f, nor definition of a convergence criterion.
          In fact,  the solution for F is given directly and with  good
          accuracy ( 1 percent accuracy claimed for the solutions given
          by  the  Colebrook equation ) for practically the entire flow
          range above laminar.  The formula is used in this program for
          Reynolds numbers greater  than  2000.  For  Reynolds  numbers
          less  than  2000  the  friction  factor  is  computed  by the
          following well used equation:














 


          Page 14.
          PIPEDATA V3.0




                                      F = 64/Re                  ( 6. )

          This equation is widely used for laminar flow because of  its
          simplicity.  Further equations and definitions as used in the
          program are as follows:

          K factors for valves and fittings are based on those given by
          Crane Technical Paper No.410 appendix  A  for  the  different
          valves   and   fittings   used   in  this  program.


                                    BACKGROUND 

          Ventura  Publishing  Company  is a small software development
          and  Publishing  Company  located  in  Kennewick,  Washington
          State.  We started in 1984 under the name of Ventura Co., and
          later in 1986 changed our name to Ventura Publishing, because
          that is what we are really doing.  We are  basically  writing  
          software for engineers.  You will occasionally see our ads in
          Design News magazine, or other technical publications.
 
          In 1985,  I  published the first version of PIPEDATA and made 
          it  available  as  a compiled program that provided the basic 
          pipe size database,  still used in this program.  In 1987   I
          incorporated  the  input  data  screen editor,  and gave this 
          program a new feature for calculating straight  pipe  losses.  
          With  this version I  have incorporated more features that  I
          thought would give this program more calculating power.  

          If  you  like  this  program,  and can use it in your work  I
          request that you register its use with us,  so  that  I   can
          continue  to  add  new  features to it.  Registration will do
          several things for you,  1.) it will ensure the  continuation
          of  this  program,  2.)  it  will  get you a copy of the next
          updated revision, and finally  3.) it gives you usage  rights
          that you do not have unless you register it.  4.) It will get
          you  on  our  mailing  list  so that we can inform you of new
          software offerings, and of special deals.

          To register the program, just fill out the order/registration
          form that can be printed directly by  the  program.  To  find
          this  form,  access  the HOW TO ORDER program help file,  and
          print it out.  Enclose your check for the  requested  amount.
          You  can  also just send us a memo,  and we will send you the
          latest revision too.












 


          Page 15.
          PIPEDATA V3.0





          Why are we making PIPEDATA available this way?

          We have several reasons,  1.) It makes you aware that we  are
          here.  2.)  It  gives  us a chance to also tell you about our
          other software  offerings.  Starting  with  this  version  of
          PIPEDATA  we are going to be adding a DATA series of software
          programs for engineers.  We intend to add about  one  or  two
          each month.  These will not be Shareware, but are low cost.

          We are also starting to include software offerings from other
          engineering software authors,  so if you have a program  that
          you  currently  market,  and  would  like  for us to help you
          market it.  Please give us a call.  Also call us too,  if you 
          need a program  to do your work.  We may just have it, or can 
          get it for you.

          If you wish to know our current offerings,  you can give us a
          call  at 509-582-2064,  or write us a note,  and we will send
          you our current offerings.

          Some of the programs that we have in the mill right now, or 
          planned include:

          * orifice sizing * gas properties program * liquid properties
          * rupture disks  * ASME shell sizing  * pipe stress analysis 
          * structural beam sizing  * heat transfer  * mathematics 
          * and others.
          
                                      - * -
                            VENTURA PUBLISHING COMPANY
                                  P.O. BOX 6718
                               KENNEWICK, WA 99336