READ
                                          THIS
                                         BEFORE
                                        PRINTING!!!!

        This document has been formatted in a special way. Virtually all dot
        matrix printers have a condensed mode which prints 132 characters
        across a standard 8 1/2 inch page.  When this file is printed out in
        condensed mode, the resulting printed pages can be cut down to 5 1/2 X
        8 1/2 inches.  The cut pages will fit nicely in the back of your
        DOS manual for storage.

        Typically, you can turn on this mode by sending a special control
        sequence to the printer from BASIC.  For example, you can turn on the
        condensed mode of the IBM/Epson printer with the BASIC statement:
        LPRINT chr$(15).  If your printer has such a condensed mode, turn it
        on now, before printing the rest of this document.























































                                           (tm)
                                      CHASM

                                 Cheap Assembler
                          for the IBM Personal Computer

                                  User's Manual
                      (c) 1985, 1986, 1987 by David Whitman
                                  Version 4.10
























    David Whitman
    P.O. Box 1157
    North Wales, PA 19454
    (215) 234-4084 (evenings)
























                      Table of Contents


    Why CHASM?.....................................................1
    What can CHASM do?.............................................2
    What WON'T it do?..............................................3
    System Requirements............................................4
    Advanced and Subset CHASM......................................5
    Modifiying CHASM's I/O Defaults................................6
    Syntax........................................................11
    Labels........................................................13
    Operands......................................................16
    Operand Expressions...........................................22
    Resolution of Ambiguities.....................................25
    Pseudo-Operations.............................................29
    Macros........................................................38
    Structures....................................................48
    8087 Support..................................................52
    Outside the Program Segment...................................54
    Running CHASM.................................................55
    Error and Diagnostic Messages.................................59
    Execution of Assembled Programs...............................64
    Notes for Those Upgrading to This Version of CHASM............76
    Miscellaneous and A Word From Our Sponsor.....................80
    Appendix A: 8088 Mnemonic List................................85
    Appendix B: 8087 Mnemonic List................................87
    Appendix C: Differences Between CHASM and TOA.................88
    Appendix D: Description of Files..............................92
    Appendix E: Bug Reporting Procedure...........................93
    Appendix F: Using CHASM on "Compatible" Systems...............94
    Advanced Version Order Form...................................96
    Index........................................................100































                                                                    1

    >>Why CHASM?<<

    Why go to the trouble to write an assembler, when one already
    exists?  The IBM Macro Assembler is a very powerful software tool
    available off the shelf.  It supports features such as macros,
    multiple segments, and linking to external procedures.

    Unfortunately, the cost of all this power is complexity. The
    Macro Assembler is so complicated that IBM warns beginners it is
    only suitable for "experienced assembly language programmers".

    For most users, this sophistication is more of a hindrance than
    an aid.  Even when writing short, simple programs, the user is
    saddled with a set of confusing pseudo-ops only appropriate for
    large, multi-segment programs.  Producing a fast loading
    executable file requires running three separate programs (MASM,
    LINK and EXE2BIN) before you can get down to testing.

    The macro assembler is totally unsuitable for use with BASIC.
    Although it is *possible* to produce machine language BASIC
    subroutines with the Macro Assembler, the process is incredibly
    convoluted and confusing.

    To top it all off, the Macro Assembler costs an overpriced $125.

    CHASM is, I hope, a more reasonable compromise between power and
    accessibility.  CHASM is simple to use and understand.  Unlike
    the Macro Assembler, CHASM doesn't require a second LINK step to
    produce a working program.  CHASM also produces fast loading
    programs without the use of the utility EXE2BIN.

    CHASM supports several different simple mechanisms for getting
    machine language routines into BASIC and Turbo Pascal, the two
    most popular languages for the IBM Personal Computer.

    Finally, the suggested payment for CHASM is a modest $40.

    A Note for Beginners:

    Before going on, you might find it useful to print and read the
    file PRIMER.DOC, included on your CHASM disk.  PRIMER is a gentle
    introduction to assembly language, which will teach you some of
    the vocabulary and key concepts you will need to start out with.





















                                                                    2

    >>What can CHASM do?<<

    CHASM is a tool for translating assembly language into the native
    machine language of the 8088 microprocessor.  Using CHASM, you
    can write down easy to remember "mnemonics" which are then
    converted into the relatively incomprehensible series of ones and
    zeros that your PC prefers to work with.

    In addition to simple mnemonic translation (such as provided by
    the mini-assembler in DEBUG), CHASM provides a great many
    "convenience" features which make writing machine language much
    easier.

    CHASM allows you to define labels for branching, rather than
    requiring you to figure out offsets or addresses to jump to.
    CHASM also lets you give symbolic names to any constants or
    memory locations you use, to make your program easier to
    understand.

    You can instruct CHASM to make your file "BLOADable" so that
    BASIC can load it as a subroutine.   A utility is also provided
    to convert machine language into BASIC "DATA" statements, so that
    BASIC can "POKE" routines into memory.  Similarly, for Turbo
    Pascal CHASM can produce external procedures and functions, or a
    file of Turbo "INLINE" statements.

    CHASM has intelligent error and diagnostic messages which guide
    you in correcting mistakes and ambiguities in your program.  A
    nicely formatted listing is produced during assembly, to help
    during debugging.

    In general, CHASM is designed to eliminate much of the confusion
    and dirty work involved in writing machine language for the IBM
    PC.

    Using CHASM, you can produce:

       1. Lightning fast "stand-alone" programs.

       2. Machine language subroutines for BASIC programs, both
          interpreted and compiled.

       3. Machine language procedures and functions for Turbo Pascal.





















                                                                    3

    >>What WON'T it do?<<

    In the interest of simplicity, CHASM has the following
    restrictions:

    1. Multiple segment definitions are not allowed. CHASM assumes
       that your entire program fits in one segment, that the cs, ds,
       and es registers all point to this same segment, and that the
       ss register points to a valid stack area.  An equivalent
       statement is that CHASM produces COM files, not EXE files.

    2. Linking to Microsoft languages is not supported.  You can't
       use CHASM to produce object modules for use with IBM/Microsoft
       Pascal or FORTRAN.


















































                                                                    4

    >>System Requirements<<

    Minimum system requirements to use CHASM are:

         IBM PC or true compatible (must emulate IBM BIOS)
         128K of memory            (some systems need 192K)
         1 disk drive
         80 column display
         DOS 2.0 or later.

    Note the DOS 2 requirement.  To provide *true* DOS 2 support, it
    was necessary to give up DOS 1 compatibility.  If you're still
    using DOS 1, you'll need to upgrade to DOS 2.0 or later to use
    CHASM.

    IBM PCjrs, and some compatibles seem to require 192K of memory.
    In general, adding more memory will allow you to assemble larger
    programs.  CHASM can take advantage of all available memory, up
    to a megabyte.

    CHASM will run faster if your source files and object files are
    on a hard disk or RAM disk.

    If you have a non-IBM computer, please read about the /VIDEO
    switch in "Modifying CHASM's I/O Defaults" and also the appendix
    titled "Using CHASM on Compatible Systems"






































                                                                    5

    >>Advanced and Subset CHASM<<

    CHASM is available in two flavors, Advanced and Subset.
    The two versions vary in their capabilities and method of
    distribution.

    The subset version is the budget release.  It may be freely
    copied by individuals as "user-supported" software, and is
    available from user groups and bulletin boards across the
    country.  Every time the subset runs, it prints a banner page
    suggesting a payment of $40 to the author.  As its name
    suggests, Subset CHASM does not support all the features of
    Advanced CHASM.

    Advanced CHASM is the deluxe release.  It runs twice as fast, and
    has a number of features not supported by the subset:

          macros
          conditional assembly
          8087 support
          include files
          structures

    Advanced CHASM is only available directly from Whitman Software.
    Users who make the suggested $40 payment receive an upgrade to
    Advanced CHASM.  Details, and an order blank are given at the
    end of this document.

    Throughout this document, features supported only by the
    advanced version will be marked as follows:

      ==>Advanced version only.

    Attempts to use these features in the subset version will
    generally result in error messages, with the advanced feature
    otherwise being ignored; however, unpredictable behavior could
    result in some instances.



























                                                                    6

    >>Modifying CHASM's I/O Defaults<<

    CHASM supports the use of a configuration file, which can be used
    to override some of CHASM's I/O defaults.  If you are willing to
    accept CHASM's defaults, you may skip this section - on most
    systems, CHASM will work perfectly well without the file
    described below.

    The configuration process involves supplying a text file named
    CHASM.CFG on your default drive.  You can create this file with
    any text editor or word processor.

    You have some freedom in where you put the configuration file.
    If CHASM.CFG is not found in the current directory, CHASM will
    also try the following paths:

          \CHASM\CHASM.CFG
          \CHASM.CFG

    The file should contain a series of text "switches" of the
    following form:

    /SWITCH, xx [, yy, zz,...]

    Where "/SWITCH" is a reserved word, listed below, and xx, yy, zz
    are numbers.  The brackets around yy and zz indicate that these
    numbers are optional - don't put brackets in CHASM.CFG.

    Each switch should start a new line, and the switch and each of
    the numbers should separated by one or more blanks or commas.

    The following switches are implemented:

    /VIDEO      Video access method.  With this switch, you can
                control the method CHASM uses to write data on your
                video screen.  Three settings are currently
                supported:

                /VIDEO 0  Direct write to screen memory.

                /VIDEO 1  Direct write to screen memory, but only
                          during the horizontal retrace interval.

                /VIDEO 2  Write using BIOS calls.




















                                                                    7

    /VIDEO      (continued) In general, the lower a number you
                specify for /VIDEO, the faster CHASM will run.

                /VIDEO 0 is the fastest mode, and is intended for use
                with either the IBM monochrome display adapter or the
                EGA adapter.  You can use /VIDEO 0 with the CGA
                adapter, but some annoying "snow" and flicker may
                result.

                /VIDEO 1 is intended for use with the CGA adapter.
                It is almost as fast as /VIDEO 0, and the snow is
                eliminated.  /VIDEO 1 is CHASM's default mode.

                /VIDEO 2 is intended for non-IBM systems that emulate
                the IBM BIOS, but have significantly different screen
                hardware.  If you have trouble running CHASM on a
                "compatible" system, try setting /VIDEO 2.  Use of
                /VIDEO 2 will slow CHASM down significantly.

    /FG         Foreground color.  Users with color monitors may
                select a foreground color from the following list:

                0    Black               8    Gray
                1    Blue                9    Light Blue
                2    Green              10    Light Green
                3    Cyan               11    Light Cyan
                4    Red                12    Light Red
                5    Magenta            13    Light Magenta
                6    Brown              14    Yellow
                7    White              15    High Intensity White

                Example: (Magenta)

                /FG 5

    /BG         Background color.  Selections 0-7 above are
                available. Example: (Cyan)

                /BG, 3

























                                                                    8


    /132        Printer 132 column mode.  The numbers following this
                switch are the ASCII codes for the characters which
                cause your printer to go into condensed mode.  You
                may specify as many characters as you like.  If you
                don't provide this switch, CHASM will truncate source
                lines in listings to avoid going over 80 columns. You
                can also include characters to activate any special
                features of your printer you want CHASM to use during
                printing.  Example: (for IBM printer)

                /132, 15

    /80         Printer 80 column mode.  Similar to /132, but the
                numbers represent the characters to return your
                printer to normal.  Include the codes for any
                characters you want CHASM to send to your printer
                before returning you to DOS.  The following example
                turns off condensed mode and causes a Form Feed on
                the IBM printer:

                /80, 18, 12

    /FF         Formfeed.  A value of zero tells CHASM that your
                printer doesn't recognize ASCII 12 as a formfeed
                command.  Any other value, and CHASM assumes that
                formfeeds will be recognized.  The default is no
                formfeed character.

                If /FF is off, CHASM will simulate formfeeds with a
                series of linefeeds.  However, most printers respond
                quicker to a formfeed than to multiple line feeds, so
                set /FF on if possible.  Example: (on)

                /FF 1

    /PAGELEN    CHASM assumes that there are 66 lines to each printed
                page.  If you use different sized paper, enter the
                number of lines per page after this switch.
                Example: (European standard)

                /PAGELEN 72






















                                                                    9


    /LINES      By default, CHASM will print 58 lines on each printed
                page, then skip over the perforation to the next
                page.  You can change this number to suit your paper
                and personal taste.  Example:

                /LINES 50

    /BEEP       Enables/Disables audible warning when errors are
                discovered in your source program.  The following
                values are supported: (default is 1)

                /BEEP 0      (no beeping)
                /BEEP 1      (beep for all errors/diagnostics)
                /BEEP 2      (beep only for FIRST error/diagnostic)

     /DWIDTH    When listing to a disk file, CHASM normally truncates
                listing lines to 80 columns to prevent wrap-around
                when viewing the file.  In some instances, such as
                disk-based print spooling with DOS's PRINT utility,
                you may wish to override this truncation.  You can
                enter a new truncation limit after this switch.
                Example: (128 column lines)

                /DWIDTH 128

     /DPAGE     For easier scanning, listings sent to disk files do
                not normally contain page breaks.   If you want to
                produce printable listing files, you can turn on page
                breaks by setting /DPAGE to any value other than
                zero.  Example: (page breaks on)

                /DPAGE 1































                                                                   10


      /PATH     Path Strategy.  Affects the way CHASM constructs the
                default file names for list and object files.  If
                /PATH is set to 0 (the default), any drive or path
                specified on the source file name will be included in
                the default file names.  If /PATH is set to anything
                else, path and drive info are removed, thus putting
                the default list and object files in the current
                directory of the logged drive.  The following table
                shows how this works:

                /PATH | Source filename   | Default object file
                ------|-------------------|-------------------------
                   0  | a:\chasm\test.asm |   a:\chasm\test.com
                   1  | a:\chasm\test.asm |   test.com

                /PATH only affects how the default file names are
                constructed - CHASM won't edit filenames that you
                explicitly type in.

     /TIMER     Enables/Disables reporting of total assembly time. A
                value of 0 turns off timing, anything else turns it
                on.  The default is off.  This switch is used
                internally at Whitman Software to benchmark new
                versions of CHASM.

    A sample CHASM.CFG file, suitable for use with the IBM dot matrix
    printer, is included on your CHASM distribution disk.




































                                                                   11

    >>Syntax<<

    CHASM accepts a standard DOS text file for input.  In this
    context, "standard DOS text file" means:

        1. Lines are terminated with a CR/LF pair.

        2. The end of the file is marked with an EOF marker (cntl-Z).

    Virtually every word processor or editor produces files which
    meet these criteria.  Some word processors have to be in a
    special mode to produce standard DOS files.  (For example, in
    WordStar, you have to be in "non-document" mode.) The user's
    manual for your editor should inform you if any special mode
    needs to be activated.

    Some users have reported problems with the user-supported word
    processor PC-Write.  Under certain circumstances, older
    versions of PC-Write can produce lines ending with just a LF
    (violation of rule 1) or files which aren't terminated with an
    EOF marker (violation of rule 2).  If you use PC-Write, make sure
    you have the latest version.

    Lines may be any combination of upper and lower case characters.
    CHASM does not distinguish between the two cases: everything
    except single quoted strings are automatically converted to upper
    case during the parsing process.  Thus, BUFFER, Buffer, buffer,
    and bUFFer all refer to the same symbol.

    The characters  blank ( ), comma (,), single quote (') semi-colon
    (;) and TAB are reserved, and have special meaning to CHASM (see
    below).  The characters + - * / ) ( are reserved for use as
    operators in expressions.

    Each line must be no more than 80 characters long and have the
    following format:

       Label Operation Operand(s) ;comment

    The different fields of an input line are separated by the
    delimiters blank ( ), comma (,) or TAB.  Any number of any
    delimiter may be used to separate fields.






















                                                                   12

    Explanation of Fields:

    Label: A label is a string of characters, beginning in column 1.
       Depending on the operation field, the label might represent a
       program location for branching, a memory location, or a
       numeric constant (see the section titled "Labels" for more on
       this topic). No reserved characters can appear within the
       label, and to ensure that CHASM can distinguish between labels
       and numeric constants, the first character of a label must
       *not* be a numeric (i.e. 0-9). Anything beginning in column 1,
       except a comment, is considered a label.

    Operation: Either a pseudo-op (see the section with the same
       name) or an instruction mnemonic as defined in "The 8086
       Book" by Rector and Alexy.  A list of acceptable mnemonics is
       given in Appendix A.

       Note 1: Except as modified below,"The 8086 Book" is the
          definitive reference for use with CHASM.

       Note 2: There are several ways to resolve some ambiguities in
          8086 assembly language.  Please read page 3-285 of The 8086
          Book, and "Resolution of Ambiguities" in this document.

    Operand(s): A list of one or more operands, as defined in
       the section titled "Operands", separated by delimiters.

    Comment: Any string of characters, beginning with a semicolon
       (;). Anything to the right of a semicolon will be ignored by
       CHASM.

    Note that except for the case of an operation which requires
    operands, or the EQU pseudo-op which requires a label, all of the
    fields are optional.  The fields MUST appear in the order shown.






























                                                                   13

    >>Labels<<

    The symbol in the label field of an input line can be interpreted
    in four different ways by CHASM:

      1. A program location which may be branched to.

      2. A memory location for data storage.

      3. An equated symbol, which takes the place of a numeric
         constant.

      4. A macro name, which takes the place of a series of
         frequently used source code lines.

    The default interpretation of a symbol is a program location for
    branching.  This default is modified by the presence of one of
    the following pseudo-ops in the instruction field:

    DB, DS, or DW:

          Normal:  The symbol is a memory location.

          In a Structure: The symbol is a numeric constant.

    EQU:

          Normal:  The symbol is a numeric constant.

          Memory Option:  The symbol is a memory location.

    MACRO:
         The symbol is a macro name.

    A given symbol may have only ONE of the above interpretations!
    Attempts to branch into a memory location or an equated symbol
    will result in error messages.  Similarly, CHASM will not allow
    you to treat program code as a data area.  Examples:

    TEXT DB  'Hit any key when ready'  ;memory location
         MOV  AL,TEXT                  ;ok
         JMP  TEXT                     ;wrong!
    LOOP MOV  AX,CX                    ;program location
         JMP  LOOP                     ;ok
         MOV  AX, LOOP                 ;wrong!



















                                                                   14

    If for some arcane reason you *need* to branch into a data area,
    you can fool CHASM by placing a label on an otherwise blank line,
    immediately before the data area.  Example:

          JNZ NPU
          RET
    NPU                                ;dummy label for jump
          DB  D8H, 00H                 ;an 8087 instruction

    If you have a masochistic urge to crash your system by writing
    self-modifying code, there are at least two ways you can defeat
    CHASM's injunction against using program code as a data area.

    The first way is to use DS to declare zero bytes of storage
    immediately before the code you want to access.  A label on the
    null DS will have the same offset as the immediately following
    code.  Example:

           MOV   JUNK1, 9090         ;change endless loop to NOP
    JUNK1  DS    0
    JUNK   JMP  JUNK

    A sneakier approach is to load the OFFSET of a program
    location into a register, then use the register for indirect
    addressing. Using the optional displacement field, you can even
    address the middle of an instruction.  Examples:

           MOV   BX, OFFSET(CALL)
           MOVB  1[BX], 00H          ;change interrupt number in code
    CALL   INT   0

    In general, I cannot recommend trying to get around CHASM's type
    restrictions.  If you find yourself in a situation where it
    seems necessary to fool CHASM, there's probably a safer, more
    direct way to legally program what you're trying to accomplish.

    Labels can be up to 80 characters long, but only the first 15
    characters are significant.  For example, CHASM considers the
    following labels identical:

       VERYLONGLABELOVER15CHARACTERS
       VERYLONGLABELOVER






















                                                                   15

    To avoid ambiguity, a given string can legally appear in the
    label field of only ONE statement.  If the same string appears on
    more than one instruction, all instances after the first will
    receive an error message.  Remember that labels are only
    significant to 15 characters, and if the first 15 characters are
    identical, an error will occur.

    TWO   EQU  '2'      ;first use is ok
    TWO   PROC FAR      ;wrong! symbol already defined

    CHASM has a number of reserved strings which are "predefined" in
    the symbol table, and will generate an error message if used as
    labels.  All the register names are reserved, as are the indirect
    address mode combinations.  The only other reserved strings are
    the words "NEAR" and "FAR", and the symbol "$". Examples:

    AX   MOV  AX, DX      ;wrong! (register name)
    [DI] ADD  AX, BX      ;wrong! (indirect address)
    FAR  CALL GETINPUT    ;wrong! (reserved word)
    $    SUB  AX, DX      ;wrong! (reserved word)












































                                                                   16

    >>Operands<<

    The following operand types are allowed.

    1. Immediate data: A number, stored as part of the program's
       object code.  Immediate data are classified as either byte,
       expressible as an 8 bit binary integer; or word, expressible
       as a 16 bit binary integer.  If context requires it, CHASM
       will left-pad byte values with zeroes to convert them to word
       values.  Attempts to use a word value where only a byte will
       fit will cause an error message to be printed.

       Immediate data may be represented in 9 ways:

          A. An optionally signed decimal number in the range -32768
             to 32767.  Examples:

             MOV AL, 21
             MOV BX, -6300

          B. A series of up to 4 hex digits, followed by the letter
             H.  The first digit must be non-alphabetic, i.e. in the
             range 0-9, to allow CHASM to distinguish between numbers
             and symbols. If necessary, a leading zero, which does
             not count in the four allowed digits, may be added to
             fulfill the non-alphabetic condition.

             If the RADIX pseudo-op has been used to change the
             default number base to 16, the final H can optionally be
             omitted.  Examples:

             ADD   CX, 0B123H   ;leading zero required
             RADIX 16           ;change default number base
             ADD   DL, 12       ;same as 12H

         C.  A series of up to 16 binary digits, followed by the
             letter B.  Examples:

             MASK   EQU   00000111B
                    MOV   AL, 10000000B
























                                                                   17

          D. A symbol representing types A, B or C above, defined
             using the EQU pseudo-op.  Examples:

             MASK EQU 10H
             MAX  EQU 1000
                  AND  CL,MASK
                  SUB  AX,MAX

          E. The offset of a label or storage location returned by
             the OFFSET operator.  OFFSET always returns a word
             value. OFFSET is used to get the address of a named
             memory location, rather than its contents.  Example:

                    MOV DI,OFFSET(BUFFER)
             BUFFER DS  0FFH

          F. The ASCII value of a printable character, represented by
             the character enclosed in single quotes (').  Thus, the
             following lines will generate the same object code:

                MOV AL,41H  ;ascii code for 'A'
                MOV AL,'A'

          G. When producing Turbo Pascal INLINE code, the function
             TURBO(x) assembles as 16 bit immediate data.

          H. ==>Advanced version only:
             Labels within structures become immediate operands whose
             values equal their offset within the structure.  See the
             section titled "Structures" for more detail and
             examples.

          I. ==>Advanced version only:
             The length of a structure, returned either by the LENGTH
             operator, or simply the structure's name.  See the
             section titled "Structures" for more detail and
             examples.

          J. An expression that evaluates out to type Immediate.
             Examples:

                    MOV AX, (3+2)*5
                    MOV DX, MEMLOC1-MEMLOC2

             See the "Operand Expressions" section for more details.



















                                                                   18

    2. Register Operands

       A. An 8 bit 8088 register from the following list:
          AH    AL
          BH    BL
          CH    CL
          DH    DL

       B. A 16 bit 8088 register from the following list:

          AX   BX   CX   DX   SP   BP   SI   DI

       C. An 8088 segment register from the following list:

          CS   SS   DS   ES

       D. An 8087 stack register from the following list:

          ST ST(1) ST(2) ST(3) ST(4) ST(5) ST(6) ST(7)

          Note: ST can also be referenced as ST(0).

    3. Memory Operands: The contents of a memory location addressed
       by one of the following methods.  Note that none of the memory
       addressing options specifies the *size* of the operand.  8088
       instructions have word or byte sized operands, and 8087
       instructions can have word, short, long or temporary real
       operands.  See the section titled "Resolution of Ambiguities"
       for more on this topic.

       All memory operands can optionally be preceded with a segment
       override to specify the segment register to be used in
       accessing memory.  The override takes the form of a segment
       register, followed by a colon, followed by the memory operand.
       No intervening delimiters are allowed.  Examples:

            MOV AX, ES:[80H]   ;80H into the extra segment
            MOV CS:[DI], SI     ;indirect with DI in the code segment

       Segment overrides are also discussed in the section titled
       "Resolution of Ambiguities".























                                                                   19

       A. Direct Memory Address.

          1. A number or other immediate operand, enclosed in
             brackets, indicating an offset into the data segment.
             Example:

             BUFFER EQU 5A5AH
                    MOV BH, [BUFFER]
                    MOV [80H], DI
                    MOV AX, CS:[TURBO(I)]

          2. A symbol, defined to be a variable (i.e. a named memory
             location) using the EQU pseudo-op.  Example:

             FCB EQU [80H]
                 MOV DI,FCB

          3. A symbol, defined to be a variable by its use on a
             storage defining pseudo-op.  Examples:

                  MOV AX,FLAG
                  MOV DATE,BX
             FLAG DS 1
             DATE DB 31

          4. The special symbol '$'.  $ returns an address of value
             equal to the current setting of CHASM's location
             counter.  This address can be used as either a memory
             location or a program location for branching.  Used by
             itself, $ has little utility, but it is a very powerful
             tool when used in expressions.  Example:

                  MOV AX, $+4    ;get the byte after this instruction

          5. An expression that evaluates out to type address.
             Example:

                    MOV AX, buffer+3
             BUFFER DS 20

             See the "Operand Expressions" section for more details.























                                                                   20

       B. Indirect Memory Address:  The address of the operand is the
          sum of the contents of the indicated register(s) and a
          displacement.  The register, or sum of registers, are
          enclosed in square brackets: []

          The displacement is optional, and takes the form of either
          an immediate operand or the label of a memory location,
          placed without intervening delimiters to the left of the
          first bracket.

          Immediate data written as decimal numbers, with values
          between 127 and -128 generate a signed 8 bit offset.
          Values outside this range, or those expressed in some
          other manner generate 16 bit offsets.

          The following indirect modes are provided:

          1. Indirect through a base register (BX or BP).  Examples:

             ENTRYLENGTH EQU 6
                         MOV AX, ENTRYLENGTH[BP]
                         MOV DL, -2[BX]
                         MOV CX, TURBO(COUNT)[BP]
                         MOV MEMLOC[BX], AX
             MEMLOC      DB  00H

          2. Indirect through an index register (DI or SI).
             Examples:

             MOV [DI], CX
             MOV CX, -5[SI]

          3. Indirect through the sum of one base register and one
             index register.  Examples:

             MOV [BP+DI], SP      ;note that no spaces are
             MOV BX, 10H[BX+SI]   ;allowed within the
             MOV CL, [BP+SI]      ;brackets.
             MOV DH, -2[BX+DI]

























                                                                   21

    4. Labels

       A label on most instructions may be used as an operand for
       call and jump instructions.  See the section titled "Labels"
       for more information.  Examples:

       START    PROC NEAR
                CALL GETINPUT
                JMPS START
                ENDP
       GETINPUT PROC NEAR

    5. Strings

       A string is any sequence of characters (including delimiters)
       surrounded by single quotes (').  If you want to use the
       single quote character inside a string, put two of them
       in a row for each one you want in the string. Example:

       DB 'This is a ''string'' with embedded quotes'












































                                                                   22

    >>Operand Expressions<<

    CHASM can perform arithmetic calculations at assemble time, to
    help you generate memory addresses and immediate data constants.

    The following operand types can participate in operand
    expressions:

         immediate data
         program locations
         data storage locations

    Actually, for the purpose of expression evaluation, CHASM treats
    both program locations and data storage locations identically.
    Thus, really only two types of operands are allowed in
    expressions: immediate and address.

    Symbols standing for immediate operands must have been defined
    prior to use in an expression, or you may get Phase Errors (see
    the error message section for a discussion on this topic).  You
    should put all your EQU and STRUC pseudo-ops at the beginning of
    your program, before any machine instructions.

    The following arithmetic operators are available:

         +  addition
         -  subtraction
         *  multiplication
         /  integer division

    Note that / performs *integer* division.  5/2 evaluates to 2.

    The normal rules of precedence apply.  To force evaluation
    contrary to normal precedence, you can use parenthesis: ().

         MOV AX  2+5*3   ;means mov ax, 17 because * outranks +
         MOV AX, (2+5)*3 ;means mov ax, 21

    No delimiters can appear within an expression.  If you separate
    the parts of an expression with delimiters, CHASM will try to
    interpret each part as a separate operand.

         MOV [BX], BUFFER + 3    ;WRONG!!
         MOV [BX], BUFFER+3      ;ok




















                                                                   23

    The type of an operand expression is determined by the individual
    operand types that are combined within it.  In evaluating each
    operation in an expression, the result type follows this rule:

         If the two operand types are the same, the result type is
         IMMEDIATE.

         If the two operand types are different, the result type is
         an ADDRESS.

    In expressions, both program locations and data storage locations
    are considered identical.  An expression which evaluates to type
    address can be used in either a MOV or a JMP.

    The result type of a complicated expression is determined by
    replacing individual binary operations with their result, and
    evaluating the (simpler) expression thus formed, following the
    above rules.

    Here's a program fragment with some expressions, and a discussion
    of their types and significance:

    EXPSAMPLE PROC  NEAR
              MOV   AX, 3+5         ;immediate, calculated value
              MOV   DX, STRING-END  ;immediate, length of string
              MOV   STRING+5, 'A'   ;address, fifth byte of string
              JMP   EXPSAMPLE+100H  ;address, used as program loc.
              JMP   STRING+100H     ;valid address syntax, but silly
    STRING    DB    'MESSaGE'       ;data area
    END                             ;marks position of end of string


    The special symbol '$' returns the current value of CHASM's
    location counter for use in expressions.  $ is of type address.
    Thus, $-1 is the address of the byte immediately prior to the
    instruction currently being assembled.




























                                                                   24

    The rules for typing expressions were set up to produce the "most
    useful" result type, taking a guess as to why one would want to
    do a given calculation.  If the type isn't what you have in mind,
    you can coerce CHASM using square brackets or the OFFSET
    function:

          MOV AX, 3+5              ;immediate
          MOV AX, [3+5]            ;coerced to address
          MOV DX, $+4              ;address
          MOV DX, OFFSET($+4)      ;coerced to immediate

    Under certain circumstances, CHASM can get confused when you use
    OFFSET or LENGTH functions in expressions.  The problem occurs if
    the expression starts with a function, and ends with a close
    parenthesis:

          MOV AX, OFFSET(BUFFER)*(3+2)    ;will be misinterpreted

    CHASM will try to interpret this as the offset of "BUFFER)*(3+2",
    and you'll get the error message "Illegal or undefined argument
    for OFFSET".  The solution is to enclose the whole works in
    parenthesis, to force CHASM to recognize it as an expression:

          MOV AX, (OFFSET(BUFFER)*(3+2))  ;correct








































                                                                   25

    >>Resolution of Ambiguities<<

    The language defined in "The 8086 Book" contains a number of
    ambiguities which must be resolved by an assembler.  This is
    discussed throughout the book, but pages 3-285 and 3-286
    specifically cover this topic.  CHASM's solutions of these
    problems are discussed in this section.

    A. 8088 Memory references:

    When one specifies the address of a memory location, it is
    unclear how large an operand is being referenced.  An operand
    might be a byte, or a word.

       1. If a register is present as an operand, it is assumed that
          the memory operand matches the register in size.  An
          exception to this rule are the shift and rotate
          instructions, where the CL register is used as a counter,
          and has nothing to do with the size of the other operand.
          Examples:

          MOV MASK, AX  ;mask is a word
          MOV DH, [BX]  ;BX points to a byte
          NEG [SI]      ;error, operand of unknown size
          SHR FLAG, CL  ;error, flag is of unknown size

       2. If no register is present, (or if the only register is CL
          being used as a counter) the size of the memory operand is
          specified by adding the suffix "B" or "W" to the
          instruction mnemonic.  Examples:

          NEGB [SI]        ;SI points to a byte
          SHRW FLAG, CL    ;flag is a word
          MOVW MASK, 0AH   ;mask is a word
          MOVB MASK, 0AH   ;mask is a byte
          MOVW MASK, 9A9AH ;must specify size even though
                           ;immediate operand implies word



























                                                                   26

    B. 8087 Memory References:

       All real and integer 8087 memory references are ambiguous as
       to the operand size.  Integer operands could be word, short,
       or long.  Reals can be short, long or temporary real.  As with
       8088 memory references, you specify the size using a suffix:

             W: word
             S: short
             L: long
             T: temporary real

       For more details and examples, see the section on 8087
       support.

    C. Indirect Branching.

    The 8088 supports two flavors of indirect branching: intra, and
    intersegment.  A register is set to point at a memory location
    which contains a new value for the program counter, and in the
    case of intersegment branching, a new value for the CS register
    as well.

    The syntax of "The 8086 Book" does not specify which flavor of
    branch is being invoked.  CHASM adds the suffixes "N" (for near,
    or intrasegment) and "F" (for far, or intersegment) to the
    indirect CALL and JMP mnemonics.  Examples:

       CALLN [BX]    ;intrasegment call
       JMPF  [DI]    ;intersegment jump
       JMP   [BP]    ;error, unspecified flavor

    D. Long and Short Jumps

    Two types of relative jumps are supported by the 8088: short
    (specified by a signed 8 bit displacement) and long (specified by
    a 16 bit displacement).  Both are implemented in CHASM as a jump
    to a label.

    The short jump is specified by mnemonic JMPS. Since one of the
    displacement bits is used to indicate direction, only seven are
    left to express the magnitude of jump.  JMPS (and similarly, all
    the jump on condition instructions) is thus limited to branching
    to labels within a range of -128 to +127 bytes.




















                                                                   27

    CHASM reserves mnemonic JMP for the long jump.  JMP may be used
    to jump anywhere within the program segment, but the object code
    generated is less compact than that from JMPS.

    Examples:

       START PROC NEAR
             JMPS END     ;short jump
             JMP  START   ;long jump
       END   ENDP


    E. Instruction Prefixes.

    The 8088 supports three instruction prefixes:

       1. SEG: segment override. An alternate segment register is
          specified for a reference to memory.

       2. REP, REPE,REPNE,REPZ,REPNZ: repeat. A string primitive is
          repeated until a condition is met.

       3. LOCK: Turns on the LOCK signal. Only useful in
          multi-processor situations.

    SEG is implemented as a modifier attached to a memory operand.
    If you want to override the default segment register for a memory
    access, precede the memory operand with the segment register
    followed by a colon.  Examples:

       MOV AX, ES:FLAG     ;flag is in the extra segment
       MOV CS:[100H], DX   ;offset 100H in the code segment
































                                                                   28

    The other prefixes are implemented as separate instructions. They
    appear on a separate line, immediately before the instruction
    which they modify.  For compatibility with earlier versions of
    CHASM, you can also specify segment overrides on a separate line,
    using the mnemonic SEG. Examples:

       REP
       MOVSB           ;move bytes until CX decremented to 0
       SEG SS
       MOV AX,BUFFER   ;buffer is in the stack segment
       LOCK
       MOV [8FFH], AX  ;lock bus to ensure data is transferred
                       ;before other processors try to access it

    Note for 8087 users:  You may get unexpected results using the
       separate instruction form of SEG on 8087 instructions.  Use
       the operand modifier form for segment overrides on 8087
       instructions.














































                                                                   29

    >>Pseudo-Operations<<

    The following pseudo-ops are implemented:

    BSAVE: Generate object code in BSAVE format.

      Instructs CHASM to build a header in the format of BASIC's
      BSAVE command.  The resulting object code file may be BLOADed
      by BASIC programs.  No operands are required, and the pseudo-op
      may appear anywhere within the source code. Example:

            ORG    0     ;no psp
      SUBRT PROC   FAR   ;subroutine for BASIC program
            BSAVE        ;make BLOADable object file

    COUNT ...ENDC:  Count bytes.

      COUNT was available in earlier versions of CHASM. With the
      addition of operand expression support, COUNT became obsolete,
      and was eliminated to make room for new features.

      Existing programs using COUNT can be modified as in the
      following example.  The length of the string is calculated by
      subtracting two labels, one just before the string, one just
      after it:

      MESSAGE    COUNT
      MSG_TXT    DB   'This utility requires DOS 2.0!' beep cr lf
                 ENDC
                 MOV CX, LENGTH(MESSAGE)

      becomes:

      MSG_TXT    DB   'This utility requires DOS 2.0!' beep cr lf
      MSG_END
                 MOV   CX, MSG_END-MSG_TXT




























                                                                   30

    DB: Declare Bytes

      Memory locations are filled with values from the operand list.
      Any number of operands may appear, but all must fit on one
      line. Acceptable operands are immediate data, or strings
      enclosed in single quotes (').  DB interprets strings as a
      series of ASCII bytes.

      If a label appears, it is redefined as a memory location, and
      the data area may be referred to using the label, rather than
      an address. Examples:

            MOV AX,MASK
      MASK  DB  00H,01H
      STG   DB  'A string operand'

      CHASM generates an error message ("Data too large") if word
      operands (such as OFFSETs, or numbers greater than 255) are
      found in the DB operand list. DW should be used for declaring
      words.

    DM: Declare Multiple Bytes

      Like COUNT, DM became obsolete when operand expressions became
      available, and has been eliminated to make room for new
      features.  Existing programs using DM can be modified as
      follows:

          DM  500, ENTRYLENGTH

      becomes:

          DS  500*ENTRYLENGTH































                                                                   31

    DS: Declare Storage

      Used to declare large blocks of identically initialized
      storage.  The first operand is required, a number specifying
      how many bytes are declared.  If a second operand in the form
      of a number 0-FFH appears, the locations will all be
      initialized to this value.  If the second operand is not
      present, locations are initialized to 0.   As with DB, any
      label is redefined as a memory location.  To save space, the
      object code does not appear on the listing.  Examples:

         DS 10         ;10 locs initialized to 0
         DS 100H,1AH   ;256 locs initialized to 1AH

    DW: Declare Words

      Used to unambiguously assign a word of storage for each item in
      the operand list.  Any number of immediate operands may appear,
      but all must fit on one line.  As with DB, any label is
      redefined as a memory location. Example:

          DW 0012H, FFFFH       ;four bytes declared

    EJECT: Begin New Print Page

      When listing is enabled, causes CHASM to move to the top of the
      next listing page.  Normally has no effect on listings sent to
      the screen or to disk, although you can enable EJECTs in disk
      listings with CHASM's /DPAGE configuration switch.

    EJECTIF: Conditional Page Break

      Requires one immediate operand.  If listing is enabled and
      fewer than that many lines are left on the current page of the
      listing, CHASM will move to the top of the next page.

      If you put an appropriate EJECTIF at the beginning of each
      procedure or section of your programs, CHASM will keep them in
      one piece.  Like EJECT, EJECTIF normally has no effect on
      listings to the screen or disk.  You can enable EJECTIF for
      disk listings with CHASM's /DPAGE configuration switch.
      Example:

          EJECTIF 20    ;following procedure is 20 lines long




















                                                                   32

    ENDP: End of Procedure

      See PROC (below) for details.

    ENDSTRUC: End of Structure

      ==>Advanced version only.  See STRUC (below) for details.

    EQU: Equate

      Used to equate a symbolic name with a number. The symbol may
      then be used anywhere the number would be used.  Use of symbols
      makes programs more understandable, and simplifies
      modification.

      An alternate form of EQU encloses the number in square
      brackets: []. The symbol is then interpreted as a memory
      location, and may be used as an address for memory access. This
      version is provided to allow symbolic reference to locations
      outside the program segment. Examples:

         MOFFSET    EQU 0B000H
         MONOCHROME EQU [0000H]

      Warning: Difficult to debug errors may result from using a
      ======>  symbol prior to its being defined by EQU.  You are
      strongly urged to group all your equates together at the
      beginning of programs, before any other instructions. See
      "Phase Error" in the Error Message section.

    INLINE: Generate Turbo Pascal inline statements

      Instructs CHASM to output object code in the form of a text
      file, suitable for including in Turbo Pascal inline statements.
      The resulting object file is not directly executable, but with
      minimal editing, can be compiled by Turbo Pascal as inline
      data.

      INLINE can appear anywhere in your source file, and requires no
      operands.

      See the "Execution of Assembled Programs" section of this
      document for examples, and more details.





















                                                                   33

    IFXX... [ELSE]... ENDIF: Conditional Assembly

      ===> Advanced version only.

      CHASM's conditional assembly pseudo-ops can be used to cause
      macros to expand differently according to the parameters
      supplied on the invocation.  Many different IF pseudo-ops are
      provided, to allow testing for (in)equality, relative size, and
      (non)existence of parameters.  You can also test whether a
      parameter is a register, and if so, what type.

      For more details and examples, see the Macro section of this
      document.

    INCLUDE: Include file

      ==>Advanced version only.

      INCLUDE requires one string operand, a filename enclosed in
      single quotes.  If desired, you can specify a drive and/or a
      path as part of the filename.

      The contents of the specified file are logically inserted into
      the source file at the point where the INCLUDE appears.
      INCLUDEs cannot be nested: an error message will be printed if
      the specified file itself contains an INCLUDE.  Example:

          INCLUDE '\ASM\STDIO.HDR'    ;bring in standard library

    LIST: Enable listing output

      Output to the list device is enabled, presumably after a NOLIST
      was encountered.  No operands required.































                                                                   34

    MACRO ...ENDM: Macro Definition

      ==> Advanced version only.

      Declares a macro.  MACRO requires no operands, and signals
      CHASM that the following lines constitute a macro definition,
      and are to be stored for later use, rather than assembled in
      place.  A label is required on the MACRO statement to name the
      defined macro.

      ENDM terminates the macro definition, and requires no operands.

      For more information and examples, see the section titled
      "Macros".

    MAP: Generate map file

      ==> Advanced Version Only.

      Generates a file with the same name as your source file but
      with extension .MAP, containing label information for use by
      symbolic debuggers.  Works with Advanced Trace86 by Morgan
      Computing, and maybe other debuggers.  See "Execution of
      Assembled Programs" for more details.

      The MAP pseudo-op can appear anywhere in your program, and
      requires no operands.

    NOLIST: Disable listing output

      Normal output to the list device is disabled.  Error messages
      are listed as usual.  No operands required.

    ORG: Origin

      Allows direct manipulation of the location counter during
      assembly.  By default, CHASM assembles code to start at offset
      100H, thus leaving room for the program segment prefix normally
      built by COMMAND or DEBUG.  In situations where no PSP is
      provided, such as routines to be called from BASIC, you should
      override this default with ORG, or incorrect assembly may
      result.






















                                                                   35

      ORG requires one operand, a number between 0 and FFFFH, which
      represents the new setting of CHASM's location counter.
      Although the location counter may be reset anywhere within a
      program, generally this pseudo-op should be used before any
      machine executable instructions for meaningful results.

      Example:

         ORG 0   ;Code will be assembled for starting
                 ;offset of 0

    PROC ...ENDP: Procedure Definition

      Declares a procedure.  One operand is required on PROC, either
      the word NEAR, or the word FAR.  This pseudo-op warns CHASM
      whether to assemble returns as intra (near) or intersegment
      (far).  Procedures called from within the program being
      assembled should be declared NEAR.  Generally, all others
      should be FAR.  ENDP terminates the procedure, and requires no
      operands.  If a RET is encountered outside of a declared
      procedure, an error occurs.  Procedures may be nested, up to 10
      deep.  Example:

      MAIN  PROC  FAR
            ...
            ...      ;body of procedure
            ENDP

    RADIX:  Default Number Base

      CHASM's default radix is 10, meaning that numbers are assumed
      to be in base 10 unless they end in "B" or "H".  The RADIX
      pseudo-op allows you to change this default.  Allowed RADIX
      values are 16 and 10.  Setting RADIX 16 allows you to specify
      hex numbers without the trailing "H".





























                                                                   36

      Note that when RADIX 16 is in effect, there is no way to
      specify numbers in base 1 (binary) or base 10 (decimal).  To
      write in either of these bases, shift back to RADIX 10.  For
      example:

         RADIX 16
         mov   ax, 1B     ;means 1B in hexadecimal
         mov   ax, 20     ;means 20 in hexadecimal
         mov   ax, 30H    ;trailing "H" allowed, but not necessary
         RADIX 10
         mov   ax, 1B     ;means 1 in binary
         mov   ax, 20     ;means 20 in decimal
         mov   ax, 30H    ;means 30 in hexadecimal


    STRUC ...ENDSTRUC: Structure Definition

       ==> Advanced version only.

      Declares a structure.  STRUC requires no operands, and signals
      CHASM that the following lines constitute a structure template,
      and not actual storage declaration.  If a label appears on the
      STRUC, the label is equated with the length of the structure.

      ENDSTRUC terminates the structure definition, and requires no
      operands.

      Inside the structure, storage defining pseudo-ops behave
      somewhat differently.  See the section titled "Structures" for
      more information. Example:

          DIRENTRY STRUC      ;disk directory entry
          NAME     DS    8
          EXT      DS    3
          ATRIB    DS    1
          RESERVED DS   10
          TIME     DS    2
          DATE     DS    2
          START    DS    2
          SIZE     DS    4
                   ENDSTRUC























                                                                   37

    WAITON / WAITOFF: Toggle Automatic WAIT Assembly

      CHASM normally assembles WAIT instructions before most 8087
      instructions.  After a WAITOFF pseudo-op is encountered, CHASM
      will not add WAITs.  This allows you to let the 8088 and 8087
      run in parallel for greater speed, putting in WAITs manually
      where synchronization is important.  WAITON turns automatic
      WAIT assembly back on.

    CHKJMP / NOCHKJMP

      Following a CHKJMP pseudo-op, CHASM will check each JMP
      instruction to see if it could have been coded as JMPS (to
      produce tighter code).  JMP instructions with displacements
      smaller than 128 bytes will be flagged with a diagnostic
      message ("Could Use JMPS").  NOCHKJMP turns off JMP checking.

    = : Assignment to Assembler Variable

      CHASM supports the use of "assembler variables", which can be
      dynamically redefined throughout your program.  The assignment
      operator "=" acts similarly to pseudo-op EQU.  A label on a "="
      line will be defined as equivalent to the operand, until it is
      redefined by another assignment statement.  Unlike EQU, with
      "=" you can assign any valid operand type (except string) to
      the assembler variable. These assignments do *NOT* result in
      object code generation - they simply redefine a symbol to have
      different meanings to CHASM in different parts of your program.
      For example:

       x    =   [80]
            mov ax, x      ;means mov ax, [80]
       x    =   bx
            mov ax, x      ;x  redefined, means mov ax, bx
       x    =   100H
            mov ax, x      ;redefined again, means mov ax, 100H




























                                                                   38

    >>Macros<<

    ==>Advanced version only.

    Macros are an advanced feature.  Beginners may wish to skip this
    section until they become more experienced with CHASM and
    assembly language programming.

    A. Introduction

       Macros are a shorthand way of writing frequently used
       sections of code.  Using macros, you can write a code fragment
       once, then any time you want to use it, just reference it by
       name.  Once you define a macro and give it a name, anywhere
       CHASM sees the name will be automatically "expanded" into the
       previously defined code.

       For example, suppose you were writing a large program, and at
       the beginning of each subroutine you pushed all the general
       purpose registers onto the stack to save their contents.
       Every subroutine would start out something like this:

             push ax       ;save register contents
             push bx
             push cx
             push dx

       Before long, you'd get pretty sick of writing the same thing
       for each subroutine.  Macros are a way to put some of the
       boring, repetitive nature of assembly language into the hands
       of the assembler, freeing you up for the more creative
       aspects.  Here's how you define a CHASM macro to take the
       place of this code fragment:

       savestate  macro
                  push ax           ;save general purpose registers
                  push bx
                  push cx
                  push dx
                  endm
























                                                                   39

       Note the MACRO and ENDM statements.  These signal to CHASM
       that the enclosed code is a macro definition to be saved for
       later use, rather than code to be assembled at this point in
       your program.  The MACRO statement also gives a name
       (SAVESTATE) to the macro, which will take the place of the
       stored code.

       Now, at the beginning of each subroutine you can just write
       "SAVESTATE" when you want to push the general purpose
       registers. Here's an example:

       get_input  proc  near
                  savestate
                  ...
                  ...
                  endp

       Given the previous macro definition, the above example is
       *exactly* equivalent to:

       get_input  proc  near
                  push ax
                  push bx
                  push cx
                  push dx
                  ...
                  ...
                  endp

       The only difference is that less busy work is required on your
       part.

       Macros are NOT subroutines!  Subroutines are coded once, then
       called within your program at run time.  Macros are expanded
       in-line at assembly time, and the code is inserted into your
       program at the invocation point.  If you invoke the macro 20
       times in your program, you'll end up with 20 copies of the
       macro code.


























                                                                   40

       Although this does waste some memory space, you save execution
       time by eliminating the subroutine call and return process.
       At a minimum, it takes 32 machine cycles to call a subroutine.
       The four instruction macro given above requires 40 cycles to
       execute.  If it were coded as a subroutine, the time to
       execute it would almost *double*.  Macros trade off space for
       speed.

    B. Macro Parameters

       CHASM's macros allow 9 user defined parameters, which are
       evaluated at expansion time.  The parameters work just like
       those in DOS batch files.  Here's an example of a macro with
       one parameter.  PRINT calls DOS function 9 to print a string
       on the console.  A parameter is used to specify the name of
       the string to be printed:

       print    macro
                mov  ah, 09H          ;specify print string function
                mov  dx, offset(%1)   ;point to string
                int  21H              ;call DOS
                endm

       Given this definition, when CHASM sees a line like:

             print title

       The following code gets inserted in its place:

             mov  ah, 09H
             mov  dx, offset(title)
             int  21H

       Note how the "%1" in the macro definition got replaced by
       "title" which was put as an operand on the invocation of the
       macro.  You can put up to 9 operands onto a macro invocation,
       and they will be substituted for the dummy parameters %1
       through %9.


























                                                                   41

       If you put a label on a macro invocation, two things happen.
       As usual, the label represents a program location for
       branching, with offset equal to the beginning of the expanded
       macro.  You can branch into the expanded macro by using the
       label as an operand on a jump or call instruction.  In
       addition, if the special dummy parameter "%0" is used in the
       macro definition, it is replaced with the label text when the
       macro is expanded.  This feature is provided to facilitate
       writing loops within macros.

       If you fail to provide an operand for any dummy parameter used
       in the macro definition, CHASM substitutes a null string of
       length zero.  To leave one parameter blank, but provide
       replacements for parameters with higher numbers, use the
       special operand "%B" for the one you want blank.  For example:

            def_mem  macro
            %1       db  %2, %3
                     endm

                     def_mem twobytes, 128, FFH
                     def_mem %B, 'Hit any key when ready...'

       Expands to:

            twobytes  db 128, FFH
                      db 'Hit any key when ready...'

    C. Internal Labels

       A potential problem exists if you put a label on a statement
       within a macro.  The first time the macro gets invoked,
       everything works fine.  However, remember that a given label
       can only be used once.  The second time you invoke the macro,
       the line with the label will get a "Duplicate definition"
       error message.

       CHASM offers "internal labels" for use within macros.  When
       expanding macros, CHASM replaces these internal labels with a
       unique text, different for each invocation of the macro.
























                                                                   42

       Macro internal labels are of the form:

           %Lx

       The "%L" signals CHASM that you want an internal label.  The
       "x" can be any character that isn't a delimiter.  By using
       different characters, you can define many different labels in
       each macro.

       Within the macro, you use the internal label symbol just like
       a normal label.  For example:

           INTLAB MACRO
           %LA    MOV AX, DX
                  JMPS %LA
                  ENDM

       Each time this macro is invoked, all occurrences of "%LA" will
       be replaced with a different text.  (The replacement text will
       be of the form "%LAnnnn" where "nnnn" is a number.)

       Using the symbol table dump on your listing, you can figure
       out what text CHASM used in any given invocation.  DON'T try
       to use this information to branch into the macro invocation
       from the outside.  Editing your source file can cause CHASM to
       use a different substitution text the next time you assemble.
       Internal labels are intended for macro INTERNAL use only.

    D. Macro Nesting

       Macro invocations can be nested, up to 10 deep.  Invocations
       are maintained on a stack, and each invocation has it's own
       set of parameters and internal labels.

       CHASM does not check for recursive macro calls.  If you call a
       macro from within itself, it's quite possible to get caught in
       an endless loop.  This can also happen indirectly, where a
       macro invokes another macro, which ends up calling the first.
       If you get caught, you can escape by hitting Ctrl-Break.

       Experienced programmers can use macro recursion along with
       expressions and conditional assembly to create some really
       elegant macros.  However, this is definitely not for beginners
       or the faint of heart.  Enter at your own risk.




















                                                                   43

    E. Conditional Macro Expansion

       This advanced feature allows you to write general purpose
       macros which expand in different ways based on the parameters
       used on the invocation.

       For example, suppose you wanted to write a macro to do
       operating system calls.  Many of the DOS functions just load
       the function number into AH, then call DOS with an interrupt.
       Here's a macro to do this:

       doscall  macro
                mov ah, %1
                int 21H
                endm

       Given the above definition, "DOSCALL 1" will expand into a
       call to DOS function #1, keyboard input.

       Unfortunately, not all DOS calls are quite so simple.  For
       example, the call for printing a string to the console
       requires that the offset of the string be loaded into DX.
       Different system calls are going to require somewhat different
       handling.  One approach would be to write separate macros for
       each function.  However, with 87 different functions in DOS 2,
       this starts to get unwieldy.

       A more general approach is to incorporate some "intelligence"
       into the macro, and let it expand differently for different
       DOS functions.  Here's a slightly more general macro, which
       loads DX whenever the "print string" function is requested:

       doscall  macro
                mov ah, %1
                ife %1 9
                   mov dx, offset(%2)
                endif
                int 21H
                endm

























                                                                   44

       "IFE" is short for "If Equal".  The "IFE" and "ENDIF" bracket
       a line of macro code which will be included during expansion
       only if the "IFE" statement is satisfied.  In this example,
       the MOV DX statement will be included only if the first
       parameter is equal to 9.  The enclosed line is indented in
       this example to help show the structure of the macro, but
       indentation is not required.

       Given the above definition, "DOSCALL 1" expands to only two
       lines:

          mov ah, 1
          int 21H

      However, "DOSCALL 9, STRING" expands to three lines:

          mov ah, 9
          mov dx, offset(string)
          int 21H

       CHASM supports twelve different conditional test statements.
       They are:

            IFE       "if equal"
            IFNE      "if not equal"
            IFGT      "if greater than"
            IFGE      "if greater than or equal"
            IFLE      "if less than or equal"
            IFLT      "if less than"
            IFB       "if blank"
            IFNB      "if not blank"
            IFREG     "if a register"
            IFREG8    "if an 8 bit register"
            IFREG16   "if a 16 bit register"
            IFSEGREG  "if a segment register"

       Most of the conditionals take two operands, and perform a
       comparison.  The operands are evaluated, and their values are
       compared according to the condition being tested.  Strings are
       compared in the normal alphabetical order sense.  Examples:

            IFE   15, 0FH       ;is true
            IFGT  'ABCD' 'EFGH' ;is false
            IFLE  20H, 128      ;is true




















                                                                   45

       IFB and IFNB require only one operand, which should be a dummy
       parameter.  These conditionals test whether the parameter was
       left "blank" or if a replacement was provided on the
       invocation.

       The IFREG conditionals take one operand.  They return true if
       the operand is a register in the following sets:

            IFREG:    any register
            IFREG8:   AH, AL, BH, BL, CH, CL, DH, DL
            IFREG16:  AX, BX, CX, DX, DI, SI, BP, SP
            IFSEGREG: CS, DS, ES, SS

       You can place as many lines as you like between an IF
       statement and the ENDIF.  All will be included if the
       condition tested is true, and none will be included if it's
       false.

       An optional "ELSE" construct is also provided.  Statements
       after the ELSE get included only if the tested condition is
       false. CHASM's conditional assembly syntax can be summarized
       as follows:

           IF.....            ;if statement with parameter(s)
             s1                  ;statements included if true
             s2                  ;    "         "      "   "
           ELSE               ;end of "true" option, begin "false"
             s3                  ;statements included if false
             s4                  ;    "         "      "   "
           ENDIF              ;end of conditional assembly

       IF statements can be nested, up to 10 deep.  During nesting,
       CHASM assumes that ELSEs are paired with the latest unfinished
       IF statement.  For example:

       example macro
               ife %1, 1
                  db 'Outer IF is true'
                  ifb %2
                     'Inner IF is true'
                  else
                     'Where do I belong?'
                  endif
               endif




















                                                                   46

       "EXAMPLE 1, 5" expands to:

              db 'Outer IF is true'
              db 'Where do I belong?'

       But "EXAMPLE 2" produces no expansion at all.

       This is easiest to follow if you use "structured" indenting
       when writing the macro, as in the example above. Remember,
       however, that CHASM ignores indenting and follows the
       "latest unfinished" rule in figuring out which IF gets the
       ELSE.  Don't fool yourself with improper indentation.

    F. Final Notes:

       The conditional assembly pseudo-ops are not restricted to use
       in macros, although there aren't that many useful non-macro
       applications.

       CHASM won't recursively expand parameters.  For example:

           RECUR MACRO
                 XOR %1, %2
                 ENDM

                 RECUR AX, %1

       expands to:

                XOR AX, %1   ;actual expansion

       NOT to:

                XOR AX, AX   ;won't happen

       Like equates and structures, macro definitions should all be
       placed at the beginning of your programs, before the macro
       gets invoked.  If you invoke a macro before it's defined, a
       phase error will occur.

























                                                                   47

       Macro definitions are stored and expanded blindly by CHASM,
       with no syntax checking.  Dummy parameter symbols can appear
       in any of the input line fields.  Any errors in a macro
       definition will only become evident when CHASM expands the
       macro and attempts to assemble the result.

       In keeping with the "shorthand" philosophy of macros, the
       results of macro expansion don't normally appear on the
       listing.  If you want to see the expansion for debugging
       purposes, insert a LIST pseudo-op as the first line of the
       macro definition.

       Once you start writing macros, you might find it useful to
       gather them together into a single file.  You can then pull
       this file into the beginning of all your programs with an
       INCLUDE pseudo-op.  Macros which don't get invoked won't add
       anything to the object code produced, and you'll save yourself
       the trouble of typing in the ones you *do* need.  If you put a
       NOLIST at the beginning and a LIST at the end of your INCLUDE
       file, you don't even have to look at the definitions on your
       listings.











































                                                                   48

    >>Structures<<

    ==>Advanced version only.

    Structures are an advanced feature.  Beginners may wish to skip
    this section until they become more experienced with CHASM and
    assembly language programming.

    CHASM's structure capability allows you to generate a "template"
    with which to organize repetitive data structures.  As an example
    of a repetitive data structure, consider a phone list.  Each
    entry in the list has three components:

         Name    - 20 characters
         Address - 50 characters
         Phone   - 10 characters

    Each entry thus uses a total of 80 bytes of storage.  To declare
    a list with 500 entries, you would declare 80 x 500 = 4000 bytes:

         PHONELIST  DS  4000   ;500 entries @ 80 bytes/entry

    That's easy enough, but now what's the offset of the 346th
    address field?  This is starting to get confusing, and time
    consuming to figure out.

    Furthermore, hard-coding numbers (like that 4000, above) into a
    program is never a good idea.  What's going to happen when you
    decide to add a zip code field, or make more room in the name
    field because you just met Alexandria Zbrievskivich?  You'd have
    to go through and change by hand each number which depended on
    the actual layout of your data.  Murphy's law guarantees that
    it'll take somewhere between "several" and "too many" assemblies
    to find them all.

    Structures allow you to set up a symbolic template which makes it
    much easier to manage structured data like this phone list.  By
    using symbols defined in the structure, rather than bare numbers,
    a change in data structure doesn't mean a frantic search
    throughout your entire program to make corrections.  If you
    change the structure definition, the symbols take on new values
    automatically.






















                                                                   49

    Here's what the phone list structure looks like:

         LISTENTRY  STRUC
         NAME       DS 20
         ADDRESS    DS 50
         PHONE      DS 10
                    ENDSTRUC

    Note the STRUC and ENDSTRUC statements.  They mark the beginning
    and end of the structure, and give it a name (LISTENTRY).

    Within the structure are storage defining pseudo-ops.  DS is used
    in this example, but DB and DW could also be used.  ORG can be
    used within a structure, but any 8088 instruction will result in
    an diagnostic message and termination of the structure
    definition.

    Inside a structure, the storage defining pseudo-ops
    behave somewhat differently than normal.  No actual storage is
    set aside, but CHASM keeps track of how much space would normally
    be declared.

    Labels on pseudo-ops get assigned values equal to their offset
    within the *structure*, not within the program as a whole.  Also,
    CHASM will treat the labels as immediate operands, rather than
    memory locations.  The result of the structure given above is to
    generate three immediate operands, with the following values:

         NAME    =  0
         ADDRESS = 20
         PHONE   = 70

    CHASM does one other piece of useful book-keeping during
    structure definitions.  If a label appears on the STRUC
    pseudo-op, it gets treated as an immediate operand, whose value
    is equal to the total length of the structure.

    You can either use the STRUC label directly as an operand, or if
    you like "pretty" code, use the LENGTH operator on it.  In this
    example, both LISTENTRY and LENGTH(LISTENTRY) are immediate
    operands of value 80.

    (Inside note: LENGTH is a null operator, provided mainly for
    aesthetic reasons.  Using LENGTH will often make your code more
    readable, but is equivalent to using just the label itself.)



















                                                                   50

    Like equates and macros, structures should be placed at the
    beginning of your programs before any machine instructions,
    otherwise phase errors can occur.  If you *do* embed structures
    inside your program, you can eliminate any phase errors by using
    the LENGTH function to reference any of the immediate operands
    generated by the embedded structure.

    The immediate operands generated during a structure definition
    can be very useful in writing your program.  Following the phone
    list example, here's a better way to declare storage for the
    list:

       NUMENTRYS  EQU 500
       PHONELIST  DS  LISTENTRY*NUMENTRYS ;500 entries of length
                                          ;defined by the structure.

    Now if you add another field to the structure, PHONELIST will
    automatically increase in size.

    The 8088's indirect addressing modes, coupled with structures,
    make a very powerful combination for accessing structured data in
    memory.  Suppose AX contains the number of the entry you want to
    work on.  You can calculate the address of the entry as follows:

        MOV BX, LENGTH(LISTENTRY)    ;length per entry
        MUL AX, BX                   ;times entry number
        ADD AX, OFFSET(PHONELIST)    ;plus the starting offset
        MOV BX, AX                   ;BX <== frame pointer

    BX is now a "frame pointer" - it points to the beginning of the
    desired entry.  You can access the various parts of the entry
    using the optional displacement field in the indirect address.
    For example, here's how you would store the letter 'A' into the
    first byte of the address field:

         MOV  ADDRESS[BX], 'A'

    As another example, the following line reads the third letter of
    the name into the AL register:

         MOV  AL, NAME+3[BX]























                                                                   51

    The first entry in a structure almost invariably has value 0.
    CHASM "optimizes" indirect addresses with structure-generated
    constants equal to zero, generating the no-offset form of the
    address.  In this example:

        MOV AX, NAME[BX]

    actually assembles as MOV AX, [BX] rather than MOV AX, 0[BX]
    The resulting code is more compact, and runs faster.

    The more complicated indirect modes can be used to scan through
    or point within the fields.  The following program fragment gets
    the fourth digit in the phone number:

         MOV DI, 4             ;specify 4th digit
         MOV AL, PHONE[BX+DI] ;read it into AL

    Often times, you'll want to process entries sequentially.  To
    move to the next entry, you just add the length of the entry to
    the frame pointer:

         ADD   BX, LENGTH(LISTENTRY)    ;point to next entry

    The preceding examples should give you a feel for what you can
    do with structures, but do not exhaust all the possibilities.
    Experiment with this feature, and many of your programs will be
    both more readable and more easily modified.





































                                                                   52

    >>8087 Support<<

    ===> Advanced version only.

    In addition to the normal 8088 instructions, CHASM's Advanced
    version supports all the 8087 mnemonics.  Look in the appendices
    for a list available instructions.

    Several books describing the functions of the 8087 instructions
    are available.  CHASM's 8087 support is based on Appendix D of
    Intel's 8087 Support Library, and the book "Assembly Language
    Programming for the IBM Personal Computer" by David J. Bradley
    (Prentice-Hall, 1984).

    ALL the 8087 instructions that reference memory for a real or
    integer quantity are ambiguous as to the size of operand.
    Integers can be Word (2 bytes), Short (4 bytes) , or Long (8
    bytes).  Reals can be Short (4 bytes), Long (8 bytes) or
    Temporary Real (10 bytes).

    As with 8088 memory references, CHASM resolves ambiguities using
    a suffix.  The following suffixes can be added to mnemonics to
    specify operand size:

       W: word
       S: short
       L: long
       T: temporary real

    Here are some examples of using suffixes:

       FADD   [200H]    ;wrong! ambiguous memory reference
       FADDT  [200H]    ;add 10 byte temporary real
       FILD   CS:[DI]   ;wrong! ambiguous memory reference
       FILDW  CS:[DI]   ;load 2 byte integer

    CHASM automatically generates a WAIT instructions prior to most
    8087 instructions.  The only exceptions are the "No Wait"
    instructions with a "N" as the mnemonic's second letter.
    Examples:

        FYL2X   ;automatically preceded by WAIT
        FNCLEX  ;no wait form of FCLEX





















                                                                   53

    If you'd prefer to manually add WAITs only where needed to
    synchronize critical instructions, the WAITOFF pseudo-op disables
    CHASM's automatic WAIT assembly.  Using fewer WAITs allows the
    8088 and 8087 to run in parallel more often, giving better
    performance.  Make sure you synchronize with a WAIT before
    allowing the 8088 to access a location being modified by the
    8087.  You can turn CHASM's automatic WAIT assembly back on using
    a WAITON pseudo-op.

    You must use the operand modifier form for segment overrides on
    8087 instructions.  A separate SEG instruction will modify
    CHASM's automatically generated WAIT instruction, and won't
    affect the intended 8087 instruction.  Example:

        SEG CS
        FLDS [100H]     ;wrong!
        FLDS CS:[100H]  ;correct















































                                                                   54

    >>Outside the Program Segment<<

    As mentioned previously, CHASM does not support multiple segment
    definitions.  Provision is made for limited access outside of the
    program segment, however.

    A. Memory References:
       To access memory outside the program segment, you move a new
       segment address into the DS register, then address using
       offsets in the new segment.  The memory option of the EQU
       pseudo-op allows you to give a variable name to offsets in
       other segments. For example, to access DOS's equipment flag:

          BIOS_DATA   EQU  40H
          EQUIP_FLAG  EQU  [0010H]
                      MOV  AX,BIOS_DATA  ;can't move immed. to DS
                      MOV  DS,AX
                      MOV  AX,EQUIP_FLAG ;get bios equipment flag

    B. Code Branching:
       CHASM supports 4 instructions for branching outside the
       program segment.

       1. Direct CALL and JMP

          New values for the PC and CS registers are included in the
          instruction as two immediate operands.  Example:

          BIOS         EQU  0F000H            ;RAM bios segment
          DISKETTE_IO  EQU  0EC59H            ;disk handler
                       JMP  DISKETTE_IO,BIOS

       2. Indirect CALLF and JMPF

          Four consecutive bytes in memory are initialized with new
          values for the PC and CS registers.  The CALLF or JMPF then
          references the address of the new values.  Example:

          BIOS        EQU   0F000H           ;RAM bios segment
          PRINTER_IO  EQU   0EFD2H           ;printer routine
                      MOV   [DI],PRINTER_IO
                      MOV   2[DI],BIOS
                      CALLF [DI]





















                                                                   55

    >>Running CHASM<<

    A. Prompt Mode

       From DOS, type:

         CHASM

       If you're using the Subset version, a hello screen is printed,
       followed by the message:

         Hit Esc to exit, anything else to continue...

       Advanced CHASM skips the commercial message.

       You're now presented with a series of prompts:

          Source code file name? [.asm]

       Type in the name of the file which contains your program.  If
       you don't include an extension for the filename, CHASM
       assumes it to be .ASM.  If CHASM is unable to find the file,
       it will give you the option of naming another file, or
       returning to DOS.  Note that anywhere CHASM expects a
       filename, you can optionally include a drive and/or path.

       Assuming your file is present, CHASM prompts:

          Direct listing to Printer (P), Screen (S), or Disk (D)?
          [nul:]

       Respond with either an upper or lower case letter.  If you
       just press enter, no listing will be produced.  If you select
       "D", CHASM will prompt:

          Name for listing file? [fname.lst]

       Type in a name for the listing file.  If you just press ENTER,
       the name defaults to that of your source file, with an
       extension of .LST.
























                                                                   56

       Listing Notes:

          1. The setting of the /PATH configuration switch controls
             the exact form of the default list file name.

          2. Regardless of where the listing is sent, error messages
             are always echoed to the screen.

          3. Suppressing the listing will result in faster assembly.

       The final prompt is:

          Name for object file? [fname.com]

       Type in a name for the assembled program.  If you just press
       ENTER, the name defaults to that of your source file, with an
       extension of .COM.

       Note: The setting of the /PATH configuration switch controls
             the exact form of the default object file name.

       CHASM now assembles your program.  A status line is maintained
       on the screen, showing how many lines have been processed,
       along with how many errors have been discovered.  CHASM makes
       two passes over your source file, outputting the listing and
       object code on the second pass.  You can pause assembly at any
       time by hitting Cntl-S (or just S).  Hitting any key then
       resumes assembly. You may abort assembly and return to DOS at
       any time by hitting Esc, Ctrl-C or Ctrl-Break.

       At the end of the second pass, a final summary of the assembly
       process is printed.  It will look something like:

          0 Error(s) detected
          0 Diagnostic(s) offered

       954 (3BAH) Bytes of object code generated

       This information should be self-explanatory.  The number of
       bytes is given in both decimal and hex format.
























                                                                   57

       If labels appeared in your program, a dump of the symbol table
       will follow.  This lists each user-defined symbol, along with
       its value (in hex). The symbols are printed in alphabetical
       order.  Each value is preceded by a one-letter code, which
       tells the symbol's type:

                P: a program location
                M: a memory location for data
                I: immediate data

       Upon exit, CHASM sets the system variable ERRORLEVEL to
       (surprise!) the total number of errors discovered in your
       source file. If you run CHASM from a batch file, you can use
       this feature to automatically invoke your text editor if
       errors were discovered.

    B. Expert Mode:

       This mode allows you to specify all i/o information on the
       command line which invokes CHASM.  The syntax is:

          CHASM sourcefile [p|s|d|/] [listfile|/] [objectfile]

       Items within brackets ([]) are optional. You may select *one*
       of any list of items separated by a bar (|).

       Basically, you just include on the command line all your
       responses to the normal prompts.  Each response must be
       separated from the others by either a space or comma.

       If you don't specify the list device/file or the object file,
       they default to NUL: and sourcename.COM respectively.  To
       represent a carriage return (to specify a default choice, but
       allow modifying a later response) use the character slash (/).






























                                                                   58

       Expert mode examples:

          1. Source file is EXAMPLE.ASM, no listing, object file
             EXAMPLE.COM:

                CHASM example

          2. Source file is SDIR.ASM, list to printer, object file
             SDIR.COM:

                CHASM sdir p

          3. Source file is MYFILE.PRG, list to disk file MYFILE.LST,
             object file SUBR.COM:

                CHASM myfile.prg d / subr.com
















































                                                                   59

    >>Error and Diagnostic Messages<<

    Error messages generated on pass one appear on the listing before
    any source code is printed, and mention the line number to which
    they refer.  The majority of messages occur during pass two, and
    will appear in the listing immediately prior to the line which
    caused the message.  Unless the listing itself is going to the
    screen, messages and the source line which generated them will be
    echoed there.

    Add Leading Zero to Hex Constant: Diagnostic.  The unknown
       symbol could be interpreted as a hexadecimal number if a
       leading zero was added.

    CHASM Internal Error: XX PC: YYYY or
    CHASM I/O Error: XX PC: YYYY
       Sigh. You just discovered a problem in CHASM itself.  Please
       contact Whitman Software, following the procedure in the
       appendix on Bug Reporting.

    Could Use JMPS: Diagnostic.  The specified label requires an
       offset of less than 128 bytes; specifying the short jump would
       result in more compact code.  The assembled code is correct,
       however.

    Conditional Nested Too Deeply:  IF statements can only be nested
       10 deep.

    Data too Large:  You are attempting to use a word of immediate
       data where only a byte is allowed.

    Duplicate Definition of XXX in (linenum): Pass 1 error.  An
       attempt was made to define a symbol already present in the
       symbol table.

    ELSE without IF: An ELSE was encountered, but no corresponding
       conditional pseudo-op was found.

    ENDIF without IF: An ENDIF was encountered, but no corresponding
       conditional pseudo-op was found.

    ENDM without MACRO:  An ENDM was encountered, but no
       corresponding MACRO was found.

    ENDP without PROC: An ENDP was encountered, but no corresponding
       PROC was found.


















                                                                   60


    ENDSTRUC without STRUC: An ENDSTRUC was encountered, but no
       corresponding STRUC was found.

    EQU Without Label: No symbol was found to equate with the
       operand.

    File not found: XXX in (linenum).  Pass one error.  CHASM was
       unable to find the file XXX, specified in the INCLUDE
       pseudo-op.

    Heap Full: Too many XXX.  Usually a Pass one error.
       You've run out of memory for the symbol and macro tables.  You
       shouldn't see this message unless you have only 128K and are
       assembling a very large program.

    Illegal Label: XXX in (linenum). Pass one error.  The symbol
       XXX begins in column one and has as its first character a
       number, or a plus or minus sign.  Alternatively, you tried to
       use a reserved word or symbol as a label.

    Illegal Operation for Structure - ENDSTRUC Implied: Diagnostic.
       The current line is within a structure, and is not a storage
       defining pseudo-op.  CHASM generates an ENDSTRUC, which
       terminates the structure definition, then assembles the line
       normally.

    Illegal or Undefined Argument for LENGTH:  The argument for the
       LENGTH  function was not present in the symbol table as an
       immediate operand on pass 2.

    Illegal or Undefined Argument for OFFSET: The argument for the
       OFFSET function was not present in the symbol table as a near
       label or memory location on pass 2.

    Missing ENDM:  The end of the input file was encountered, and at
       least one MACRO had not been terminated by an ENDM.

    Missing ENDP: The end of the input file was encountered, and at
       least one PROC had not been terminated by an ENDP.

    Missing ENDSTRUC: The end of the input file was encountered, and
       at least one STRUC had not been terminated by an ENDSTRUC.





















                                                                   61

    Multiple Segment Overrides are Illegal:  Diagnostic.  You have
       specified more than one segment override on this instruction.
       The first override is used, and the other(s) ignored.

    Nested INCLUDE: An INCLUDE was encountered in an INCLUDEd file.
       The INCLUDE pseudo-op cannot be nested.

    Nested Structure: A STRUC was encountered inside a structure.
       Structures cannot be nested.

    No Name For Macro:  Diagnostic.  The macro statement did not have
       a label.  CHASM is unable to give a name to the macro, and you
       will be unable to reference it.

    Operands Not Compatible:  The size of the two operands does not
       match.

    Phase Error: A label or memory location is found to have
       different values on pass 1 and pass 2.  A difficult to debug
       error: generally the problem is not caused by the statement
       which received the error message. The problem is caused by an
       improper statement before this one, but after any other labels
       (otherwise *they* would have received the error message).

       When phase errors are discovered, CHASM prints this message,
       then resynchronizes the location counter to match the offset
       calculated on pass one.  If further phase errors are reported,
       the line responsable for each subsequent error will be located
       between two Phase Error messages, but after any unflagged
       labels.

       There are four documented ways to generate phase errors.

       1. A previous instruction used a symbolic immediate operand
          prior to the symbol's definition.

       2. A previous instruction made improper use of a forward
          referenced label, either an attempt to branch into a data
          area, or to access a code area as if it was data.

       3. The label on the flagged statement is defined more than
          once in the program.

       4. A previous instruction invoked a macro prior to its
          definition.



















                                                                   62

       Whitman Software would appreciate hearing about any other
       situations which cause the Phase Error message to appear.

    Parameter Too Large for Expansion: Diagnostic. Replacement of the
       dummy parameter would cause the macro line to exceed CHASM's
       internal 255 character limit for manipulating strings.
       Generally this message will be accompanied by the "Source Line
       Truncated" message, warning that a line has exceeded the
       allowed 80 columns.

    Procedures Nested Too Deeply: Procedures may be
       nested no more than 10 deep.

    Source Line Truncated:  The length of the input line exceeded 80
       characters.

    Specify Word or Byte Operation: Diagnostic.  CHASM suggests that
       the Syntax Error might be resolved by adding the suffix "B" or
       "W" to the instruction mnemonic.  Most, but not all, ambiguous
       memory references are flagged with this diagnostic.

    Syntax Error: (OP) (DEST), (SOURCE).  CHASM was unable to find a
      version of the instruction (OP) which allows the operands
      (DEST) and (SOURCE).  Either the instruction doesn't exist, or
      it is an inappropriate choice for the given operands.  The (OP)
      (Dest), (Source) is a reconstruction of your source line based
      on how CHASM parsed it.  A comparison of the reconstruction and
      your original source code will sometimes help pinpoint the
      error.

      Syntax Error messages are followed by two diagnostics which
      spell out in words CHASM's best guess about the operands.
      Again, a comparison between CHASM's guesses and what you
      really meant can help find the problem.

    Too Far For Short Jump: The displacement to the specified label
       is not in the range -128 to +127.

    Undefined Operand for EQU: Any operands on an EQU statement must
       have been previously defined.

    Undefined Symbol XXX: The symbol XXX was used as an operand, but
       never appeared as a label, and is not a predefined symbol.





















                                                                   63

    Unrecognized Operand XXX: XXX is used in the DB or DW operand
       list, but is not a valid immediate operand. (or string, in the
       case of DB).





























































                                                                   64

    >>Execution of Assembled Programs<<

    A. Object code format

       The object code file produced by CHASM is in the form of a
       memory image, exactly as will be present in your computer at
       run time.  No link step is required.  Provided that the segment
       registers are set correctly, the architecture of the 8088
       guarantees that code is self-relocating, and will run correctly
       loaded anywhere in memory.  Storing a program as an exact image
       of memory at run time is called the COM format by IBM.

       This COM format is *not* that produced by the IBM assembler.
       The output of the IBM assembler is in the form of an "object
       module" suitable for input to the linker.  The object module
       is not directly executable, but must first be "filtered"
       through the linker.  This adds an extra step to the process of
       producing a working program, but gives you the option of
       combining multiple object modules into one program.  The
       resulting linked program is *still* not a memory image, but
       has a header which is used to perform relocation during
       loading.  This linked program plus header is called the EXE
       format by IBM.

    B. Running Assembled Programs From DOS

       DOS provides a loader for running machine language programs.
       To run a program, you merely type its name, without the
       extension.  This is what you're doing every time you use a DOS
       external command such as FORMAT or CHKDSK.  In fact, the COM
       format is named after "external COMmand".

       When DOS loads a program, it examines the file extension to
       determine what format the file is in, either COM or EXE.  This
       is why CHASM defaults to using the extension .COM for your
       object file.  If you plan to run the program from DOS, don't
       change the extension.

       For COM programs, DOS builds a 255 byte long "program segment
    prefix" and sets the segment registers to point to this PSP. The
    contents of the file are then loaded verbatim right after the
    PSP, at offset hex 100 in the segment defined by the segment
    registers.  As soon as loading is complete, your program is
    executed starting with the instruction at hex 100.




















                                                                   65

       Although you can totally ignore the PSP, you should read pages
    E-3 through E-11 of the DOS manual to see what DOS puts there for
    you.  It turns out there are some real goodies which your program
    might want to use.

       When your program is done, it must transfer control back to
       DOS, otherwise the 8088 will continue to fetch what it
       believes are instructions from whatever garbage or bit-hash
       happens to follow your program in memory.  The easiest way to
       return to DOS is to execute the instruction:

         INT 20H

       This is the vectored interrupt reserved by DOS for program
       termination.

       While we're on the topic of vectored interrupts, you would be
       well rewarded to study both the DOS Technical Reference and
       Hardware Technical Reference Manuals to find out what happens
       when you execute some of the other interrupts.  Some very
       useful functions, such as file handling and screen i/o, are
       available at the machine language level through this
       mechanism.  Information on interrupts is also available in
       Peter Norton's book "Programmer's Guide to the IBM PC", which
       is cheaper than buying both of IBM's reference manuals, and
       also more readable.

       Looking at things the other way, by changing the interrupt
       vector for a given function to point to your own code, you can
       override the way DOS or the BIOS does something, and do it
       your way.  DOS even provides a method (via interrupt 27H) by
       which your new code can be grafted onto DOS, and not be
       overwritten by other programs.

    C. Debugging Assembled Programs

       IBM provides an excellent utility with DOS, called DEBUG.COM.
       By specifying your program's name as a parameter when invoking
       DEBUG, you can observe your program execute with DEBUG's trace
       and other functions.  To debug your program, from DOS type:

          DEBUG progname.COM






















                                                                   66

       DEBUG builds a PSP and loads your program just like DOS does,
       but you have the added power of the debugging commands to
       monitor your program while it runs.  See chapter 6 of the DOS
       manual for more details about using DEBUG.

       On the topic of debugging, I can recommend most highly a
       program called TRACE86, from Morgan Computing (10400 N.
       Central Expressway, Suite 210, Dallas, TX 75231).  The program
       replaces DEBUG, and although rather steeply priced, makes the
       IBM debugger look silly.  I've been using TRACE86 for some
       time now, and wouldn't be without it.

    D. Using Assembled Programs in BASIC

       To incorporate a machine language subroutine in a BASIC
       program, write it in assembly language, then assemble it with
       CHASM.  You should read page C-7 of the BASIC manual for some
       conventions to use in writing your subroutine.  In particular,
       note that you must declare the routine to CHASM as a FAR
       procedure using the PROC pseudo-op, and that the last
       instruction of the routine should be a RET.

       Unlike programs which are run directly from DOS, your routine
       will not be preceded by a program segment prefix.  You should
       prevent CHASM from leaving room for a PSP by putting an ORG 0
       pseudo-op at the beginning of your routine. If you don't
       include the ORG, memory references will not be assembled
       correctly.  Example:

            ORG  0    ;no psp
       SUBR PROC FAR  ;far procedure
            ...       ;body of subroutine
            RET
            ENDP

       CHASM supports two methods for getting assembled routines into
       BASIC programs.  The methods differ in whether the routine is
       included in the BASIC program file, or in a separate file.

       A utility program called COM2DATA is provided for including
       machine language within BASIC program files.  The program is
       distributed in source code form (file COM2DATA.ASM) and must
       be assembled with CHASM prior to use.  The program functions
       as a DOS 2 filter, reading a COM file in from the standard
       input, and writing a series of BASIC DATA statements to the
       standard output.


















                                                                   67


       COM2DATA's syntax is as follows:

         COM2DATA [<infile] [>outfile] [linenum]

       You specify the input and output files as with any DOS 2
       filter.  The linenum parameter sets the starting line number
       used on the BASIC code produced.  If you don't specify
       linenum, it defaults to 1000.

       If you MERGE the file of DATA statements into your BASIC
       program, the program can then READ the data and POKE it into
       memory.  An example program to do this is given on page C-6 of
       the BASIC manual.  An alternative approach would be to store
       the routine in a string variable, which could later be located
       with the VARPTR function.

       If you would prefer to keep your machine language subroutine
       in a separate file, include a BSAVE pseudo-op somewhere within
       your assembly language source code.  CHASM will build a header
       on the object code produced, which will mimic that built by
       BASIC's BSAVE command.  The resulting file may be BLOADed by
       BASIC to any location in memory.

       You transfer control to your routine with either the USR
       function, or the CALL statement.  Syntax for these statements
       can be found in the BASIC manual.





































                                                                   68


    E. Using Assembled Programs with Turbo Pascal:

       CHASM and Turbo Pascal work splendidly together, complementing
       each other's strong points.  You can use CHASM to provide new
       functions you wish Turbo had, or to fine tune a critical
       procedure for optimum speed.   CHASM itself is written in a
       combination of Turbo Pascal and CHASM.

       CHASM supports two techniques for producing machine language
       code for Turbo Pascal: external procedures or functions, and
       Turbo INLINE code.

    1. External Procedures and Functions:

       Turbo loads external procedures and functions within the same
       segment as the rest of your Pascal program.  You have no
       control of the exact load location (more on this later), but
       on the other hand, you don't have to worry about setting aside
       a special location for your procedures (as in BASIC).  Since
       your external procedure is loaded in the same segment as the
       Pascal code, it should be declared NEAR to CHASM:

         EXTERNAL PROC NEAR
                  ...           ;body of procedure
                  ...
                  ENDP

       Turbo passes parameters to your procedure/function via the
       stack.  To work effectively, a good grasp of the stack
       structure is critical.  Read the Turbo manual for information
       on internal data formats and parameter passing, to see just
       what to expect on the stack.  Also, remember that the stack
       grows *down* from the top of memory.

       If you're going to access the stack in your procedure, the
       first thing you should do is set up BP as a stack pointer.
       Since Turbo also uses BP, you have to save the current value
       first.  The obvious place to save it is on the stack...

          PUSH BP           ;save old BP
          MOV  BP, SP        ;and set up to indirectly address stack






















                                                                   69

       You can now access the parameters on the stack using offsets
       relative to the BP register.  Note that since you PUSHed BP,
       everything is 2 bytes deeper onto the stack than what Turbo
       originally sent you.

       Here's an example.  Suppose you declare the following external
       function in Turbo:

          function Sum(x,y: int): int;
             external 'sum.com';

       After you've pushed BP, here's how the stack looks:

           stack contents           indirect address
        ----------------------------------------------
           <function result>             8[BP]
           <value of parameter y>        6[BP]
           <value of parameter x>        4[BP]
           <return address to Turbo>     2[BP]
           <old BP value>                 [BP]

       The indirect addresses go up two at a time, since each item on
       the stack is a word (two bytes) long. You can access the
       parameters using their indirect addresses. We'll talk more
       about the "function result" area later; ignore it for now.
       Here's the code for an external function to add two integer
       parameters:

       SUM  PROC NEAR
            PUSH BP          ;save old BP
            MOV  BP, SP      ;set up stack pointer

            MOV  AX,  4[BP]  ;get parameter x
            MOV  ADD, 6[BP]  ;add parameter y
                             ;leave sum in AX to return to Turbo

            POP  BP          ;restore old BP for Turbo
            RET  6           ;clear params and "result" off stack
            ENDP

























                                                                   70

       A more elegant way to access the parameters is by using a
       CHASM structure to define their offsets on the stack:

       STACK    STRUC
       OLDBP    DW   0000H
       RETADDR  DW   0000H
       XPARAM   DW   0000H
       YPARAM   DW   0000H
                ENDSTRUC

       With this structure added to the above example, you could
       access the parameters like this:

                MOV  AX, XPARAM[BP]    ;get parameter X

       Functions return scalar results by having the value in AX upon
       return.  The function in the above example saves some time by
       calculating the value in AX in the first place.  Upon exit,
       the function POPs BP, to restore the value Turbo was using.

       Note the RET 4 in the example.  This returns to Turbo, while
       simultaneously POPing (and discarding) 4 bytes off the stack.
       This clears off the two parameters which Turbo passed.  If
       there were three parameters, you'd use a RET 6; if none, a
       simple RET would do. When Turbo receives control, it assumes
       that you've cleaned up the stack by removing all parameters.
       If you don't do this properly, a run-time error, or even a
       system crash will result.

       (Typical scenario:  Turbo tries to return from one of its own
       subroutines, thinking the top of the stack has the return
       address.  Unfortunately, the top is really an integer
       parameter, left over from your external function.  Turbo's
       RET sends control into some random area of memory, and boom -
       the system crashes.)

       It's easy to get confused about the exact contents of the
       stack.  If your procedure doesn't seem to be working right,
       the first thing to suspect is Turbo and you have different
       ideas about what's where on the stack.  A DEBUG session can
       usually straighten things out.























                                                                   71

       Boolean functions constitute a special case which is poorly
       documented in the Turbo Pascal manual.  Boolean functions must
       return their result in two ways:

           1. by setting the zero flag (Z = false, NZ = true)

           2. and by returning either 0 (false) or 1 (true) in AX

       The first return method is assumed by Turbo if you use the
       function in a conditional statement, the second if you assign
       the value of the function to a variable.  You need to return
       the result both ways to cover all possible uses of your
       function.

       When external functions are called, in addition to the normal
       parameters, Turbo passes something called the "function
       result" on the stack.  When the result is a scalar type (other
       than real), this seems to be intended just as a local work
       area for you to use, since Turbo ignores any value you store
       there.  (For non-real scalars, the result is actually
       returned in AX).

       In fact, like a parameter, the function result must be POPed
       off the stack when your function returns to Turbo. Unlike
       scalar parameters (which always occupy a word of stack memory,
       even if they are defined as byte), the function result is the
       exact length of the result type.  Thus for a boolean function,
       you have to POP off one extra byte above and beyond those for
       clearing off the parameters.

       Functions which return either a real or non-scalar result use
       the "function result" area to return their result, since it
       won't fit in AX.  For these types of functions, you shouldn't
       pop the "function result" area before returning, since Turbo
       is expecting to find it on top of the stack.

       A problem of addressability can crop up if your external
       procedure tries to maintain its own local variables and/or
       constants.  The problem is that you have no way of knowing
       just where Turbo is going to load your procedure within the
       shared segment.  As such, the address CHASM calculates for any
       memory locations are going to be offset from their real values
       by some unknown constant, the offset of the procedure within
       the shared segment.  This is called a relocation problem.




















                                                                   72

       Fortunately, there's a way around this problem, but it
       requires using a trick.  Your program has to figure out, *at
       run time*, just where it's located in memory.  If you could
       find out the offset of any known point in your procedure,
       you'd "have your bearings" so to speak, and could go on.

       The trick is as follows.  The 8088 CALL instruction pushes the
       address of the next instruction onto the stack, then branches
       to the location given in the CALL.  By performing a dummy
       CALL, then stealing the value off the stack, we have the
       location of a known spot in the procedure.   By subtracting
       the offset within the procedure of that known location, we get
       a pointer to the beginning of the procedure which can be used
       to access everything else.  Here's an example:

       LOCAL  PROC NEAR
              PUSH BP                     ;set up to access stack
              MOV  BP, SP                 ; ditto

              CALL DUMMY                  ;establish addressability
       DUMMY  POP  BX                     ;  "           "
              SUB  BX, OFFSET(DUMMY)

              MOV  AX, 4[BP]                ;get parameter
              SEG  CS                       ;offset relative to CS
              ADD  OFFSET(TOTAL)[BX], AX    ;maintain running total

              POP  BP
              RET  2
       TOTAL  DW   0000H
              ENDP

       We use indirect addressing here.  After the funny business
       with the CALL, POP, SUB sequence, BX has a pointer to the
       beginning of the procedure.  Using indirect addressing, we
       take that pointer and add in the offset of the memory location
       we want to access.  In this example we're using a local
       variable to maintain a running total of the parameter which
       gets passed.

























                                                                   73

       Note the SEG CS just before the ADD which accesses the
       location TOTAL.  Since we found our bearings by stealing the
       address of a program instruction, our offset is known relative
       to the CS register, NOT the DS which is normally used to
       access data.  The SEG CS forces the 8088 to calculate the
       address using CS rather than the default DS register.  Every
       time you access a memory location within your procedure, you
       *MUST* do it relative to CS by using a segment override.

       Turbo requires that you preserve the values of the following
       registers:

            BP, CS, DS, SS

       If you want to use these registers in your routine, the
       easiest way to preserve them is to PUSH them onto the stack at
       the beginning of your routine, then POP them just before
       returning.  As near as I can tell, you can safely trash the
       other registers.


    2. INLINE Code

       An alternative method of incorporating code into Turbo Pascal
       is through Turbo's inline statement.  The inline statement is
       intended for short routines or patches where you just give
       Turbo a list of numbers representing the code.  In addition to
       numbers, you can also include variable names in the inline
       list.  Turbo replaces them with their offsets at compile time.

       CHASM's INLINE pseudo-op is provided to facilitate producing
       Turbo inline code.  If you put an INLINE pseudo-op in your
       CHASM source file, rather than producing a normal object code
       file, CHASM produces a text file formatted to include in a
       Turbo inline statement.  For example:

           inline        ;shift to inline mode
           mov  ah, 0FH  ;call bios for video mode
           int  10H      ;  ditto

       produces the following object file:

                        {    inline       ;shift to inline mode    }
          $B4/$0F/      {    mov ah, 0FH  ;call bios for video mode}
          $CD/$10/      {    int 10H      ;  ditto                 }



















                                                                   74

       Object code is output in text form, as hex constants.  A
       comment with the source code for each line is also generated.

       The INLINE pseudo-op can appear anywhere in your source file,
       and it requires no operands.

       Object files produced from source files with an INLINE
       pseudo-op are NOT executable!  They contain text suitable for
       inclusion in Turbo Pascal inline statements.  It's probably a
       good idea to override CHASM's default name for the object
       file, and specify something with an extension other than COM
       to prevent DOS from trying to run the program.

       Your inline code must preserve the BP, SP, DS and SS
       registers. If you need to modify these registers, you should
       PUSH the ones you need at the beginning of your code, and POP
       them at the end.

       Turbo's inline statement allows you to insert variable names
       in with the list of numbers.  At compile time, Turbo will
       replace the name with the 16 bit offset of the variable in its
       native segment.  (See the Turbo Pascal manual for a discussion
       of internal data formats and the native segment of variables.)

       CHASM supports this capability with the TURBO() function.
       CHASM treats TURBO() as 16 bit immediate data during assembly.
       However, in place of the two bytes of data, CHASM outputs the
       function argument literally for Turbo to evaluate:

          inline
          mov   bl, turbo(flag)[bp]     ;local variable "flag"
          mov   ax, cs:[turbo(maxcode)] ;typed constant "maxcode"
          lds   si, turbo(y)[bp]        ;pointer to var parameter "y"

       produces:

                              {      inline                        }
          $8A/$9E/FLAG/       {      mov   bx, turbo(flag)[bp]     }
          $2E/$A1/MAXCODE/    {      mov   ax, cs:[turbo(maxcode)] }
          $C5/$B6/Y/          {      lds   si, turbo(y)[bp]        }
























                                                                   75

    F. Symbolic Debugging

       ===> Advanced Version Only

       The MAP pseudo-op (available in CHASM's advanced version)
       generates a file containing label information that can be used
       by debugging software to show label names in your program
       during debugging.  This makes debugging *much* easier, since
       you don't have to keep looking at a listing to tell where you
       are in your program.

       The map file is formatted to be used by Advanced Trace86 from
       Morgan Computing, but may be usable by other debuggers.  If
       you're using CHASM's map files with another debugger, please
       write so that other's can share this information.

       In AT86, the following command sequence will load in a
       program, including labels:

           N program.MAP
           LL
           N program.COM
           L

       The LL (load labels) command has to come before you load the
       program, since AT86 uses the program area as a workspace when
       loading labels.

       The map file contains data about both program locations and
       data locations.  AT86 handles the program labels correctly, so
       the label appears both on the labeled line, and is referenced
       on any JMP or CALL to the labeled line.  Data locations get
       partial support.  The location is labeled, but only memory
       references with a CS: segment override use the symbolic name.






























                                                                   76

    >>Notes for Those Upgrading to This Version of CHASM<<

    CHASM is not yet carved in stone - improvements and corrections
    are made fairly frequently, based on both my own experience in
    using the program, and the comments of outside users.  This
    section summarizes the changes which have been made since version
    1.2 was released.  Changes followed with an asterisk (*) denote
    modifications which could invalidate programs written under
    earlier versions of CHASM.

    Version   Notes

    4.10      Fixed bug which caused lockup when using negative
              numbers with RADIX 16 in effect.  Document
              improvements, including index.

    4.09      Speed enhancement. MUL, IMUL, DIV, IDIV now accept more
              operand options.  Memory labels now allowed as indirect
              offsets.  Some bugs in COM2DATA fixed.

    4.08      New option in /BEEP switch.  MAP pseudo-op for use with
              symbolic debuggers.

    4.07      Speed enhancement.  Intersegment JMP and CALL fixed.
              Expressions now allowed in the subset.  Characters + -
              * / ) ( are now reserved for expressions only. (*)

    4.06      Speed enhancement.  Turbo Pascal INLINE facility.
              /VIDEO configuration switch.  New conditionals: IFREG,
              IFREG8, IFREG16, IFSEGREG.  New pseudo-ops: INLINE,
              RADIX, CHKJMP, NOCHKJMP.  New function: TURBO(). Single
              quotes now allowed in strings (use two).  Obsolete
              COUNT, ENDC and DM pseudo-ops no longer supported. (*)

    4.05      Speed enhancement.  Characters now work in expressions.
              EJECT and EJECTIF appear *before* page breaks.  /DPAGE
              configuration switch.  Parameter collection on macro
              invocations now halts before comments.  SHL can now
              also be written as SAL.

    4.04      RET with displacement is now assembled correctly.
              Parser bug fixed which crashed on strings with '/'.






















                                                                   77

    4.03      Assembler variables.  Operand size incompatibility now
              reported. FSUB now assembles correctly.  Intermittent
              bug in expressions with forward references fixed.
              Indirect memory references with offsets and segment
              overides now assemble correctly.  Only the first
              occurrence of a phase error is now reported.

    4.02      DS storage assembly is now turned off during structure
              definitions.  Structures assemble faster. Intermittent
              problem with macro parameter expansion cleared up.

    4.01      8087 support.  WAITON and WAITOFF pseudo-ops. Internal
              labels for macros.  Corrects bug which caused crash on
              certain syntax errors.

    4.00      Total rewrite in Turbo Pascal.  Subset replaces
              interpreted version as free distribution release.
              Faster assembly.  Symbol and macro tables now use all
              available memory.  Nested macros permitted.  Operand
              expressions. $ now returns location counter value.  New
              syntax for segment overrides.  Conditional pseudo-ops
              now evaluate operands.  Improved error and diagnostic
              messages.  DOS 2 or later now required (*). DOS 2 path
              support for files. Setting of DOS 2 ERRORLEVEL. EJECTIF
              pseudo-op added. New configuration switches: /DWIDTH,
              /FF /TIMER, /PATH. CHASM.CFG must now have only one
              switch per line (*).

    3.15      Macros added. New pseudo-ops: MACRO, ENDM, IFE, IFNE,
              IFB, IFNB, ELSE, ENDIF.

    3.14      Interpreted version frozen at version 2.13, further
              changes apply only to compiled version.  Memory
              requirement raised to 128K.  INCLUDE, STRUC, ENDSTRUC,
              DM, DW, LIST, NOLIST, COUNT and ENDC pseudo-ops added.
              Alternate mnemonics for the jump on condition
              instructions, and alternate syntax for the DIV and MUL
              instructions.  Binary numbers added.

    2.13      Assembly can now be aborted with the Esc key. Negative
              decimal numbers are working again.  Input lines now
              limited to 80 characters, and labels must begin with a
              non-numeral. (*)

    2.12      Listings can now be suppressed.  Error messages echoed to
              the console on non-screen listings. Expert mode added.


















                                                                   78


    2.11      Pagination improved.  Listings now time stamped. OFFSETs
              and word values now allowed in DB operand list.

    2.10      Equated symbols allowed in the DB operand list.  Status
              line improved.

    2.09      The first digit of hexadecimal constants must now be in
              the range 0-9. A leading zero is permitted on four digit
              hex constants, to allow fulfilling this condition. (*)

    2.08      Configuration process expanded.  CHASM now skips over
              perforations on printed listings.  EJECT pseudo-op added.

    2.07      Oops.  Configuration file now works as advertised.

    2.06      CHASM now supports reverse long jumps.

    2.05      Compiled version released.  BSAVE pseudo-op.
              Configuration process simplified.

    2.04      TABs are now expanded and replaced with blanks, for
              compatibility with IBM text editors.

    2.03      Two bugs corrected.  The first involved incorrect
              assembly of indirect memory references with
              displacements in the range 128-255.  The second caused
              a crash if a hex number longer than 4 digits used.

    2.01      COM2DATA utility added.

    2.00      Corrected a bug in the DS and DB pseudo-ops which caused
              the last label in a program to be redefined as a memory
              location.  Also, the TAB character was added as a new
              delimiter, and PRIMER.DOC was added to the CHASM package.

    1.9       The short jump is now represented with mnemonic JMPS, for
              compatibility with DEBUG version 1.1. (*)

    1.8       The operand type "character" was added as a new way to
              represent immediate data.

    1.7       The DS operator now works for blocks larger than 255
              bytes.  Also, the OFFSET function now works properly in
              the displacement field of an indirect memory reference.



















                                                                   79

    1.6       A revision of this document.  Some sections were improved
              slightly, and in response to user requests, a section on
              execution of assembled programs was added.

    1.5       Corrected an error which generated the message "Data too
              Long" if the value FFH was used as 8 bit immediate data.

    1.4       User interface improved.  CHASM now traps some common
              input errors such as misspelling a file name, or
              forgetting to turn on your printer.

    1.3       A speed enhancement.  Version 1.3 benchmarks about 5
              times faster than version 1.2.



















































                                                                   80

    >>Miscellaneous and A Word From Our Sponsor...<<

    A. Programming Notes:

       1. CHASM is written in a combination of Turbo Pascal and
          CHASM.  This is less incestuous than it sounds: the
          program was written in Turbo, then profiled to single
          out the critical routines.   The rate determining sections
          were rewritten in optimized assembly language, and
          assembled with the original Turbo Pascal version of CHASM.
          These routines were then incorporated as Turbo external
          procedures and functions in a new version of CHASM.

          The speed enhancements possible by "helping out" Turbo with
          CHASM can be quite dramatic.  Replacing four rate limiting
          routines out of the over two hundred routines in CHASM gave
          almost a four-fold speed increase!

          CHASM's source code is available to registered users by
          sending a formatted disk and stamped return mailer.  If you
          make any improvements, I'd like to hear about them for
          possible inclusion in future releases.

          Please note that although you can modify CHASM for your own
          use, under NO CIRCUMSTANCES may you distribute modified or
          translated versions, either in the public domain or for
          profit.

    B. Red Tape and Legal Nonsense:

       1. Disclaimer:

          CHASM is distributed as is, with no guarantee that it will
          work correctly in all situations.  In no event will the
          Author be liable for any damages, including lost profits,
          lost savings or other incidental or consequential damages
          arising out of the use of or inability to use these programs,
          even if the Author has been advised of the possibility of
          such damages, or for any claim by any other party.

          Despite the somewhat imposing statement above, it *is* my
          intention to fix any bugs which are brought to my attention.
          See the appendix on Bug Reporting for more details.





















                                                                   81

       2. Copyright Information:

          The entire CHASM distribution package, consisting of the
          main program, documentation files, and various data and
          utility files, is copyright (c) 1983, 1984, 1985 and 1986
          by David Whitman.  The author reserves the exclusive right
          to distribute this package, or any part thereof, for
          profit. The name "CHASM (tm)", applied to a microcomputer
          assembler program, is a trademark of David Whitman.

          CHASM's Subset version and various subsidiary files may be
          copied freely by individuals for evaluation purposes.  It
          is expected that those who find the package useful will
          make a contribution directly to the author of the program.
          The Subset version identifies itself by displaying a banner
          page giving the author's address and inviting free copying.
          ONLY VERSIONS DISPLAYING THIS BANNER PAGE MAY BE COPIED.

          CHASM's Advanced version is only available to registered
          users who have made the $40 suggested payment.  Registered
          users may copy the program for backup purposes, but must
          restrict use of the program to either one user or one CPU,
          at their option.

          CHASM's source code is made available for educational
          purposes and to allow users to customize for their own
          personal use.  Under NO CIRCUMSTANCES may modified versions
          or translations into other computer languages be
          distributed, either in the public domain or for profit.

          User groups and clubs are authorized to distribute CHASM's
              Subset version under the following conditions:

          1.  No charge is made for the software or documentation.  A
              nominal distribution fee may be charged, provided that
              it is no more than $8 total.

          2.  Recipients are to be informed of the user-supported
              software concept, and encouraged to support it with
              their donations.

          3.  The program and documentation are not modified in ANY
              way, and are distributed together.





















                                                                   82

          Interested manufacturers are invited to contact Whitman
          Software to discuss licensing CHASM for bundling with
          MS-DOS based computer systems.

          Distribution of CHASM outside the United States is through
          licensed distributors, on a royalty basis.  Interested
          distributors are invited to contact Whitman Software.

       3. Royalty Information:

          No royalties are required to distribute programs produced
          using CHASM.  However, if you send me a copy of any major
          program you have produced using CHASM, I'll give you a free
          page of advertising in this document.

       4. Educational Discount:

          Substantial discounts are available for multi-CPU licenses
          of CHASM's Advanced version to educational institutions.
          Contact Whitman Software for details.

    C. An Offer You Can't Refuse.

       CHASM is User-Supported software, distributed under a
       modification of the FREEWARE (tm) marketing scheme developed by
       the late Andrew Fluegelman, whose inspiration and efforts are
       gratefully acknowledged.

       Anyone may obtain a free copy of CHASM's Subset version by
       sending a blank, formatted diskette to the author. An
       addressed, postage-paid return mailer must accompany the disk
       (no exceptions, please).

       A copy of the program, with documentation, will be sent by
       return mail.  The program will carry a notice suggesting a
       payment to the program's author.  Making the payment
       is totally voluntary on the part of the user.  Regardless of
       whether a payment is made, the user is encouraged to
       share the program with others.  Payment for use is
       discretionary on the part of each subsequent user.
























                                                                   83

       The underlying philosophy here is based on three principles:

       First, that the value and utility of software is best assessed
          by the user on his/her own system.  Only after using a
          program can one really determine whether it serves personal
          applications, needs, and tastes.

       Second, that the creation of independent personal computer
          software can and should be supported by those who benefit
          from its use.

       Finally, that copying and networking of programs should be
          encouraged, rather than restricted.  The ease with which
          software can be distributed outside traditional commercial
          channels reflects the strength, rather than the weakness,
          of electronic information.

      If you like this software, please help support it.  Your
      support can take three forms:

      1. Become a registered user.  The suggested payment for
         registration is $40.

      2. Suggestions, comments, and bug reports.  Your comments will
         be taken seriously - user feedback was responsible for most
         of the changes listed in CHASM's revision history.

      3. Spread the word.  Make copies of the Subset for friends.
         Write the editor of your favorite computer magazine.
         Astronomical advertising costs are one big reason that
         commercial software is so overpriced.  To continue offering
         CHASM this way, I need your help in letting other people
         know about CHASM.































                                                                   84

      Those who make the $40 payment to become registered users
      receive the following benefits:

      1. An upgrade to the Advanced version of the program. The
         Advanced version executes twice as fast as the Subset and
         supports macros, conditional assembly and other features.
         An order form for the Advanced version is given at the end
         of this manual.

      2. User support, by phone or mail. The phone number and address
         for help are given below.  SUPPORT IS ONLY AVAILABLE TO
         REGISTERED USERS.  If you call without registering, be
         prepared to listen to a Tanstaafl lecture (*).

      3. Notices announcing the release of significant upgrades.

     (*) Tanstaafl = There Ain't No Such Thing As A Free Lunch.  A
         basic truism of the universe, first expounded by R.A.
         Heinlein.  There is also no such thing as free user support.

    CHASM is copyrighted, and users are requested NOT to make copies
    of the Advanced version other than for their own use.  I am
    strongly opposed to copy protection, and would regret being
    forced to protect CHASM.  Please recognize the amount of time and
    money which went into producing CHASM, and respect the wishes of
    the author.

          David Whitman
          P.O. Box 1157
          North Wales, PA 19454

          (215) 234-4084 (evenings/weekends only)
































                                                                   85

    Appendix A: 8088 Mnemonic List

    This appendix lists the mnemonics which CHASM will recognize,
    grouped roughly by function.  Consult "The 8086 Book" for
    definitions of these instructions, and for the operands each will
    accept.  Mnemonics marked with an asterisk (*) will accept a 'B'
    or 'W' suffix for ambiguous memory references.

    Arithmetic:

    AAA      AAD       AAM       AAS       ADC*      ADD*      CBW
    CWD      CMP*      CMPS*     DAA       DAS       DEC*      DIV*
    IDIV*    IMUL*     INC*      MUL*      NEG*      SBB*      SUB*

    Data Movement:

    LAHF     LDS       LEA       LES       LODS*     MOV*     MOVS*
    POP      POPF      PUSH      PUSHF     SAHF      XCHG     XLAT

    Logical:

    AND*     NOT*      OR*       TEST*     XOR*

    String Primitives:

    CMPS*    LODS*     MOVS*     SCAS*     STOS*

    Instruction Prefixes:

    LOCK     REP       REPE      REPNE     REPNZ     REPZ      SEG

    Program Counter Control: (unconditional)

    CALL     CALLN     CALLF     JMP       JMPF      JMPN      JMPS
    RET

    Program Counter Control: (conditional)

    JA       JAE      JB      JBE      JC        JCXZ       JE
    JG       JGE      JL      JLE      JNA       JNAE       JNB
    JNBE     JNC      JNE     JNG      JNGE      JNL        JNLE
    JNO      JNO      JNP     JNS      JNZ       JO         JP
    JPE      JPO      JS      JZ       LOOP      LOOPE      LOOPNE
    LOOPNZ   LOOPZ




















                                                                   86

    Processor Control:

    CLC      CLD       CLI       CMC       HLT       NOP       STC
    STD      STI       WAIT

    I/O:

    IN       OUT

    Interrupt:

    INT      INTO      IRET

    Rotate and Shift:

    RCL*     RCR*      ROL*      ROR*      SAL*      SAR*      SHL*
    SHR*















































                                                                   87

    Appendix B: 8087 Mnemonic List

    ===> Advanced version only.

    This appendix lists the 8087 mnemonics recognized by CHASM's
    Advanced version, grouped roughly by function.

    Arithmetic:

    FADD     FADDP    FCHS     FDIV     FDIVP     FDIVR    FDIVRP
    FIADD    FIDIV    FIDIVR   FIMUL    FISUB     FISUBR   FMUL
    FMULP    FPREM    FSUB     FSUBP    FSUBR     FSUBRP

    Mathematical Functions:

    F2XM1    FABS     FPATAN   FPTAN    FRNDINT   FSCALE   FSQRT
    FXTRACT  FYL2X    FYL2XP1

    Data Movement:

    FBLD     FBSTP    FILD     FIST     FISTP     FLD      FLD1
    FLDL2E   FLDL2T   FLDLG2   FLDLN2   FLDPI     FLDZ     FST
    FSTP     FXCH

    Comparison:

    FCOM     FCOMP    FCOMPP   FICOM    FICOMP    FTST      FXAM

    Processor Control:

    FCLEX    FDECSTP  FDISI    FENI     FFREE     FINCSTP   FINIT
    FNCLEX   FNDISI   FNENI    FNINIT   FNOP      WAIT

    Processor Status:

    FLDCW    FLDENV   FNSAVE   FNSTCW   FNSTENV   FNSTSW    FRSTOR
    FSAVE    FSTCW    FSTENV   FSTSW



























                                                                   88

    Appendix C: Differences Between CHASM and That Other Assembler

    Virtually all magazine articles about assembly language
    programming on the IBM PC assume that the reader is using That
    Other Assembler - you know, the outrageously priced one.  This
    appendix will try to summarize the differences between the two
    programs.  Please note that I do not own a copy of That Other
    Assembler, and therefore this section is not complete, nor even
    guaranteed to be correct.  I continue to work on this section,
    and users of both products are invited to suggest additions or
    corrections, so that this section will continually improve with
    time.

    A. General Differences

    The biggest difference is philosophical.  The IBM assembler was
    designed for use by professional assembly language programmers,
    to write operating systems and other huge projects.  This is
    reflected in the large size and relative complexity of the macro
    assembler.

    On the other hand, CHASM was designed for use by beginners, to
    write relatively short programs.  This was done by leaving out
    some of the power offered by IBM's assembler, in exchange for
    simplicity and ease of use.  The main simplification involved
    producing object code in the COM format, rather than the EXE
    format chosen by IBM. There are two main consequences of this
    choice:

       1. You can't link routines assembled by CHASM to
          Microsoft languages. (Although you *can* include them in
          Turbo Pascal or BASIC programs.)

       2. Your program has to fit in one 64K segment.  If (shudder!)
          you want to write a 256K assembly language program, you're
          out of luck.

    Like Pascal, the IBM assembler is a strongly typed language.  By
    requiring you to specify the *type* of each memory location you
    will access in your program, the IBM assembler generally knows
    what size of memory operand you want.  If you don't like the
    declared size, you have to override the default with the PTR
    operator.  Thus, to loading the AL register from a location
    declared word is a syntax error, unless you specify BYTE PTR
    before the address.



















                                                                   89


    In analogy to the C language, CHASM is weakly typed. CHASM is
    perfectly happy extracting a byte from where you originally set
    aside a word - CHASM can't tell the difference. In most cases,
    CHASM can tell what size you want from context:  for example, if
    you're using a word register, it *must* be a word memory access. On
    the other hand, for any access to memory which doesn't have a
    register as the other operand, you must add either a 'B' or a 'W'
    to the instruction mnemonic used by IBM.

    B. Miscellaneous Differences:

       1. Short Jumps:

          IBM uses the SHORT keyword, CHASM uses an 'S' suffix.
          Example:

          JMP   SHORT label    ;ibm
          JMPS  label          ;chasm

       2. Offset Function:

          Where IBM precedes an operand with the keyword OFFSET,
          CHASM has a *function* called OFFSET. CHASM requires
          parentheses around the operand. Example:

          MOV   AX, OFFSET FCB  ;ibm
          MOV   AX, OFFSET(FCB) ;chasm

       3. Declaring Storage:

          A.  If you don't care what value a memory location is
              initialized to, the IBM assembler allows you to specify
              '?' as its contents.  In CHASM, if you don't care what
              value the variable is initialized to, just put down a
              zero.  Example:

                 DB   ?      ;ibm
                 DB   0      ;chasm

























                                                                   90


          B.  The IBM assembler allows the keyword DUP as an operand
              in storage declaring pseudo-ops.  This means to repeat
              the definition as many times as the number just before
              the DUP.  Example:

              DW   3 DUP(?)  ;ibm
              DW   0, 0, 0   ;chasm

    4. ASSUME Pseudo-op:

       IBM's ASSUME pseudo-op tells the assembler where the segment
       registers will be pointing.  CHASM always assumes that the CS,
       DS and SS registers point to the beginning of the code
       segment, and that the SS register has been set up to point to
       a valid stack area.  If you find an ASSUME pseudo-op with
       different assumptions for the CS, DS and ES registers you'll
       have to figure out the addresses for memory references in the DS
       and ES segments yourself.

    5. Segment Pseudo-op:

       This pseudo-op is used to set up multiple segments in the IBM
       assembler.  Since CHASM only allows one segment, there is no
       equivalent pseudo-op.  If there is only one segment definition
       in an IBM assembler program, everything is fine, just leave
       the pseudo-op out for CHASM.

       Often times the SEGMENT pseudo-op is used to provide
       addressing of an area in the BIOS, or perhaps the interrupt
       vector table at the beginning of memory.  For example, if a
       program needed to get at the BIOS data area, in the IBM
       assembler you would define a dummy segment with the same
       structure as that in the BIOS listing in Technical Reference:

         DATA          SEGMENT AT 40H
         RS232_BASE    DW    4 DUP(?)
         PRINTER_BASE  DW    4 DUP(?)
         EQUIP_FLAG    DW    ?
         MFG_TST       DB    ?
         MEMORY_SIZE   DW    ?
         IO_RAM_SIZE   DW    ?

       All this is really accomplishing is giving a name to some
       memory locations which are outside the actual program being
       written.


















                                                                   91

       In CHASM, you can accomplish the same thing using a structure.
       This will generate a series of immediate operands whose values
       correspond to the offsets of the labels in the dummy segment.
       You can then reference the locations by enclosing the label
       names in square brackets, to coerce from type immediate to
       type address.

         DUMMY         STRUC            ;simulate dummy segment
         RS232_BASE    DW    0, 0, 0, 0
         PRINTER_BASE  DW    0, 0, 0, 0
         EQUIP_FLAG    DW    0
         MFG_TST       DB    0
         MEMORY_SIZE   DW    0
         IO_RAM_SIZE   DW    0
                       ENDSTRUC
                       MOV AX, [EQUIP_FLAG]

    6. Labels:

       The macro assembler indicates a local label by appending a
       colon (:).  The colon does not become part of the label, and
       is not included when referencing the label.  CHASM's labels
       are all global, and although they may end with a colon, the
       colon will become part of the label itself, and must then be
       used when referencing the label.  Example:

       a2:   mov ax,cx      ;ibm
             jmp a2         ; "

       a2:   mov ax,cx      ;chasm
             jmp a2:        ;  "

       CHASM does provide support for local labels in macros.  See
       the discussion on internal labels in the macro section of this
       document.

    7. Entry Point:

       The macro assembler allows you to specify the point within
       your program where execution will begin.  A label is put
       on the entry point, then to indicate entry, the same label is
       placed on the "END" pseudo-op.  Since COM programs must always
       start at offset 100H, CHASM doesn't allow setting an entry
       point, or use the END pseudo-op.




















                                                                   92

    Appendix D: Description of Files

    Your CHASM distribution disk contains a number of files.  This
    appendix will give a brief statement of the purpose of each.

    FILE           DESCRIPTION
    ----------------------------------------------------------------
    CHASM.CFG       Sample configuration file, for IBM printer.

    CHASM.COM       The CHASM program (either subset or advanced)

    CHASMS.COM      This file may appear on the disk of advanced
                    version users.  It is the current subset version,
                    that can be shared with others.  Please rename it
                    CHASM.COM on their disk, to avoid confusion.

    CHASM.DOC       This document.

    EXAMPLE.ASM     Sample source file.

    COM2DATA.ASM    Source code for COM2DATA filter.

    COM2DATA.DOC    Documentation for COM2DATA.

    FREEWARE.DOC    References to other User Supported programs.

    PRIMER.DOC      Simple introduction to assembly language.

    Occasionally, various other sample source files for CHASM will be
    distributed.  These files will have extension ASM, and will be
    accompanied by a corresponding DOC file.

































                                                                   93

    Appendix E: Bug Reporting Procedure

    Although each version of CHASM is tested extensively prior to
    release, any program of this magnitude is bound to contain a few
    bugs.  It is the intention of Whitman Software to correct any
    genuine problem which is reported.

    If you think you have found a bug in CHASM, please take the time
    to report it for correction.  Although any report is helpful,
    correction of the problem will be easiest if you provide the
    following:

       1. The version of CHASM you are using.  Your problem may have
          been fixed already!

       2. A brief description of what you believe the problem to be.

       3. A printed listing of a source file which manifests the
          problem.

          * DON'T send a 5,000 line program which has one
            manifestation of the bug!  Isolate the problem area, or
            write a short sample routine that demonstrates the bug.

    Unlike normal commercial software, where corrections are saved up
    for a major revision, bugs in CHASM are fixed as soon as reported,
    with a new version released almost immediately (which is why there
    are so many versions in CHASM's revision history).

                   =====> BONUS <======

    If you send a copy of your problem source file on disk, it will
    be returned with either a new, corrected version of CHASM, or
    with an explanation of what you were doing wrong to *think* you'd
    found a bug.





























                                                                   94

    Appendix F: Using CHASM on "Compatible" Systems

    CHASM was written specifically for the IBM PC, but should
    function normally on true "compatibles".  This appendix is a new
    section to summarize compatibility data for various systems.

    Please help make this document section useful to others.  If you
    are using (or are unable to use...) CHASM on a non-IBM computer,
    please write with your experiences.  Does CHASM work correctly on
    your system? Are there specific problem areas?  Can they be
    worked around?

    If you are using a non-IBM system, I strongly recommend that at
    least to start out, you include the line:

          /VIDEO 2

    in your CHASM.CFG file (see the section on "Modifying CHASM's I/O
    Defaults" for a discussion of the CHASM.CFG file).  This will
    force CHASM to use BIOS calls to access your video screen.  By
    default, CHASM writes directly to the screen hardware for maximum
    speed.  Without this line, if your hardware is not *strictly* IBM
    compatible, CHASM's output could be invisible, or your system
    could even hang up and require re-booting.

    The following systems are reported to run CHASM sucessfully:

           Artisoft XT
           AT&T 6300
           Chameleon
           Columbia 1600-1
           Compaq, Compaq DeskPro, Compaq Plus
           Corona PC-2
           Heath 151
           IBM PC, XT, AT, 3270 PC, 3270 PC/G
           ITT XTRA
           Kaypro 16
           Leading Edge Model D
           Mega XT
           PC Designs FD-1
           Sanyo 555
           Sun-ST
           Superior PC
           Tandy 1000, 2000
           Televideo 1605
           Zenith 150


















                                                                   95



    The following systems have one or more problems:

    ================================================================
    Tandy 1200HD - CHASM crashes on some systems.  The problem seems
    to be related to the exact amount of free memory available on the
    system.  You can prevent the crash by slightly changing the
    amount of free memory, to either a higher or lower number.
    Probably the easiest way to do this is to change the number of
    disk buffers, or load an extra device driver such as ANSII.SYS.
    Call Whitman Software if you have trouble.
    ================================================================
    ================================================================
    IBM PCjr. - Several users report getting as far as the source file
    prompt, at which point the program crashes.  Several other users
    (invariably with more than 128K of memory) report that CHASM works
    fine.  The PCjr uses part of user memory for the screen buffer, and
    PCjr users probably need 192K to run CHASM.
    ================================================================












































                                                                   96

          ********ADVANCED VERSION ORDER FORM********

    Please add me to the list of registered CHASM users, and send me
    an upgrade to Advanced CHASM.  I understand that CHASM is
    copyrighted, and agree not to distribute any unauthorized copies
    of this Advanced version.

    Note that version 4 requires DOS 2 (or later)
    and 128K of memory. (192K for PCjr)

    Computer Model: ____________________________________

    Diskette format:            Total Memory: _______K

       __ single sided/9 sector

       __ doubled sided/9 sector

    Check one:

           ___ I enclose a check for $40

           ___ I am a past customer.  The enclosed check brings my
               total payment up to $40.


    Where did you hear about CHASM? ________________________________

    Name:    _______________________________________________________

    Address: _______________________________________________________

    City, State, Zip: ______________________________________________


    ================================================================
         Send order form and check to:

              Whitman Software
              P.O. Box 1157
              North Wales, PA 19454























                                                                   97

      ==============PRINTER ENHANCEMENT===================


    Michael Hoyt, of Soft and Friendly Software, has produced a set
    of printer enhancement programs using CHASM, which is sold under
    the name Prowriter Utilities.  The package supports the following
    printers:

        NEC 8023A-C
        Prowriter I  (C. Itoh 8510)
        Prowriter II (C. Itoh 1550)

    The package contains three programs:

        PRINT_CHARACTERS
        PRINT_SCREEN
        PRINT_SET

    Once PRINT_CHARACTERS is run, it attaches itself to DOS, and
    makes your printer have exactly the same character set as your
    video monitor.  The conversion is very professionally done.
    Particularly impressive are the line drawing characters, which
    actually form connected lines, both horizontally and vertically.

    As if this wasn't enough, PRINT_CHARACTERS adds italics
    capability as well.  The italics make very effective emphasis in
    documents and letters, and look really good.

    PRINT_SCREEN is a graphics screen dump, activated by the normal
    Shift/PrtSc sequence.  Several options are available which trade
    off speed and print quality.  Since I have the mono card, I
    haven't tried PRINT_SCREEN, but Michael sent me a sample printout
    which looked quite nice.

    PRINT_SET is a menu-driven program to turn on and off the various
    special printing modes supported by these printers.  A simple but
    effective program.

    I've been using this package with my NEC 8023 for a few months
    now, and I like them quite a bit.  To get a copy, send $35 to:

        Soft and Friendly
        RR 2 Box 65
        Solsberry, IN 47459




















                                                                   98

         ================= NEW PRODUCT ====================
    VPRINT version 2.00

    VPRINT traps printer output to create a "virtual printer".
    Normal printer output is sent to a disk file of your chosing.
    Redirection of printer output allows you to:

       * Produce formatted disk files with software packages that
         don't support "printing to disk".

       * Set up word processors and other software to work with your
         printer.  Using DEBUG to examine output trapped to disk
         allows you to see exactly what's being sent to your printer,
         to immediately pinpoint problems.

       * Capture output generated on one computer, to be printed on
         another system.

       * Take disk "snapshots" of your video screen.  With VPRINT
         enabled, the PrtSc key copies your screen to disk.

       * Delaying output for later printing.  VPRINT uses less memory
         than most print spoolers (only about 3K), but runs almost as
         fast.  If you can't afford lots of memory for a print
         spooler, you can VPRINT quickly, then print the file during
         a time when your computer is idle.

    VPRINT is distributed as User-Supported software, with a
    suggested payment of $15 from satisfied users.  VPRINT is written
    in CHASM, and registered users get access to VPRINT's heavily
    commented source code, which can be studied to learn about
    writing memory resident software.

    To get VPRINT, send a either $15 for a registered copy, or a disk
    and stamped return mailer for a evaluation copy to:

              Whitman Software
              P.O. Box 1157
              North Wales, PA  19454

    Be sure to specify that you're interested in VPRINT.























                                                                   99


         ================= ALSO AVAILABLE ==================

    If you use the IBM/Microsoft BASIC compiler, chances are your
    programs are bigger and slower than they have to be.  If all
    unreferenced line numbers are removed from your source program,
    and the /N switch is used, BASCOM will "optimize" your program.
    The result is tighter, more efficient code.

    NUMZAP is a utility which carefully scans your source file, and
    deletes all the non-essential line numbers.  Performing this task
    by hand would be prohibitively time consuming and you'd probably
    introduce errors into your program in the process.  NUMZAP will
    do the job in minutes, 100% error free.

    The old BASIC version of CHASM was passed through NUMZAP, and the
    resulting compiled code shrank by a factor of 10% (!).  That 10%
    reduction could make the difference between your program running
    in 64K, or having users with minimal systems get "Out of Memory"
    messages just before your program crashes.

    An added advantage to using NUMZAP is that bigger programs can be
    compiled.  You may not be aware that there is a limit on the size
    of program which the compiler can handle.  BASCOM uses up space
    remembering the offset of each line number in your program. If
    you have too many numbered lines, BASCOM will run out of room and
    you'll get a unending series of "TC" (Too Complex) error
    messages.  By eliminating the unneeded line numbers, you give
    BASCOM more elbow room.  The free space available to compile
    CHASM increased 27% (!) after using NUMZAP.

    NUMZAP is distributed as User-Supported software, with a
    suggested payment of $15 from satisfied users.  To get NUMZAP,
    send a either $15 for a registered copy, or a disk and stamped
    return mailer for a evaluation copy to:

       Whitman Software
       P.O. Box 1157
       North Wales, PA  19454

    Be sure to specify that you're interested in NUMZAP.























                                                                  100


    Index


    $.............................19,23    copyright information............80
    /132..............................7    COUNT............................29
    /80...............................8    DB.........................13,29,49
    /BEEP.............................9    debugging........................65
    /BG...............................7    decimal numbers..................16
    /DPAGE............................9    delimiters.......................11
    /DWIDTH...........................9    description of files.............92
    /FF...............................8    diagnostic messages..............59
    /FG...............................7    direct addressing................18
    /LINES............................8    DM...............................30
    /PAGELEN..........................8    DS.........................13,30,49
    /PATH..........................9,56    duplicate labels.................14
    /TIMER...........................10    DW.........................13,31,49
    /VIDEO.........................6,94    educational discount.............82
    8086 Book........................12    EJECT............................31
    8087.......................25,28,52    EJECTIF..........................31
    8087 registers...................18    ENDP..........................31,35
    =................................37    ENDSTRUC...................32,36,49
    aborting assembly................56    EQU.....................12,13,16,32
    advanced version order form......96    error messages...................59
    ambiguities......................25    ERRORLEVEL.......................57
    arithmetic operators.............22    EXE format.......................64
    ASCII............................17    execution of assembled program...64
    assembler variables..............37    expert mode......................57
    BASIC.........................66,66    expression result types..........22
    binary numbers...................16    expressions................17,19,22
    BSAVE.........................29,67    fields...........................11
    bug reporting procedure..........93    hex numbers......................16
    changes to CHASM.................76    IBM macro assembler..............88
    characters.......................17    IF............................32,43
    CHASM revision history...........76    immediate data...................16
    CHASM's source code..............80    INCLUDE..........................33
    CHASM.CFG.........................6    indirect addressing........19,50,72
    CHKJMP...........................37    indirect branching............26,54
    coercing expression results......23    INLINE........................32,73
    COM format.......................64    input files......................11
    COM2DATA......................66,66    instruction prefixes.............27
    comments.........................12    internal labels..................41
    compatibles....................4,94    interrupt vectors................65
    conditional assembly..........32,42    JMP..............................26
    configuring CHASM.................6    JMPS.............................26
    conversion of programs...........88    label significant characters.....14


















                                                                  101


    labels.....................12,13,20    red tape.........................80
    legal nonsense...................80    registers........................17
    LENGTH function............17,24,49    REP..............................27
    limitations.......................3    requirements......................4
    LIST.............................33    reserved characters..............11
    listing.......................55,55    reserved strings.................15
    location counter..............19,23    resolution of ambiguities........25
    LOCK.............................27    royalty information..............82
    MACRO............................33    running assembled programs.......64
    macro blank parameters...........41    running CHASM....................55
    macro internal labels............41    SEG..............................27
    macro nesting....................42    segment override........18,27,53,72
    macro parameters.................40    segment registers................18
    macros...........................38    short jumps......................26
    MAP...........................34,75    source code (CHASM's)............80
    memory operands..................18    standard DOS files...............11
    messages.........................59    strings..........................21
    mnemonic list (8087).............87    STRUC.........................36,49
    mnemonic list (8088).............85    structures.................17,48,69
    modifying CHASM'S I/O defaults....6    symbol table dump................56
    multi-segment programs...........54    symbolic debugging...............75
    NOCHKJMP.........................37    syntax...........................11
    NOLIST...........................34    system requirements...............4
    NUMZAP...........................99    Tandy............................95
    object code format...............64    Tanstaafl........................84
    OFFSET function...............17,23    The 8086 Book....................25
    operand expressions..............22    TURBO function...................17
    operands.........................16    Turbo Pascal...............17,67,80
    order form.......................96    Turbo Pascal function results....70
    ORG........................34,49,66    Turbo Pascal inline code.........73
    outside the program segment......54    TURBO(x) function................74
    pausing assembly.................56    user-supported software..........82
    PC-Write.........................11    VPRINT...........................98
    PCjr...........................4,95    WAIT.............................52
    permission to copy...............81    WAITOFF.......................36,52
    phase error.............32,46,49,61    WAITON...........................36
    PRIMER.DOC........................1
    PROC.............................35
    program segment prefix........64,64
    program termination..............65
    programming notes................80
    prompt mode......................55
    pseudo-ops.......................29
    PSP...........................64,64
    RADIX.........................16,35


















                                                                  102