NAME
	graph - plot a tabulated function

SYNOPSIS
	graph [file] [options]

DESCRIPTION
	Graph with no options takes pairs of points (two numbers per line) from
	the given file (or standard input) as x- and y- values and plots them
	on the screen, connected by straight lines.  A string surrounded by
	quotes "..." may follow a pair of points, and will be displayed
	starting at that point.  If an input file is specified, the program
	waits for a keypress, then resets the screen parameters and clears the
	screen before exiting.  If the data comes from the standard input, the
	program exits without clearing the screen or resetting it.

	On the Z-100, both 225*640 and 400*640 modes are supported.  The mode
	is specified by setting the environment variable GRAPHICS before
	running graph:

		SET GRAPHICS=1         ; 225*640 mode (the default)
		SET GRAPHICS=2         ; 400*640 mode

	Similarly, the following modes are supported on the IBM PC:

		SET GRAPHICS=4		; 200*320 color mode
		SET GRAPHICS=5		; 200*320 grey scale mode
		SET GRAPHICS=6 		; 200*640 monochrome mode (the default)

	The terminology above is IBM's, but note that a color monitor
	connected to the 15 pin connector on the IBM color graphics adaptor
	will display color if the graphics mode is set to either 4 or 5.  A
	color monitor connected to the RCA jack will display only a grey
	scale in mode 5.

OPTIONS

-a  [<step> [<start>]]  Automatically generate abscissas.  The first argument,
		if present, is the step between values (default 1).  The second
		argument, if present, is the starting value (default 0, or
		first argument from -x switch).

-b break (disconnect) the plot after each label.  (See switch -m to make the
		line segments different.  To break the plot without printing
		labels, use empty labels: "".)

-c <text>	argument is default label for data points

-g <style> argument is grid style: 0 for no grid, 1 for frame with tic marks
		(default), 2 for full grid.

-l <text>	next argument is label for graph (printed at top)

-m <n1> <n2> <n3>...  numeric arguments are linestyles for successive line
		segments (see switch -b).  If an argument is zero, the data
		points are plotted as dots not connected by lines.  Otherwise,
		each positive argument is a number of up to three digits WCS,
		where W is the linewidth (0-9, with 0 giving width 1), C is the
		color (with 0 being brightest), and S is linestyle (1-5, 1 for
		solid, 2 for dashed, 3 for dotted, etc.) Similarly, negative
		arguments generate markers of different colors and/or styles
		(box, cross, triangle, etc.).

-n		Omit numeric labels on axes (uses more of the screen for the
		graph, therefore effectively increases resolution slightly).

-t		Transpose x and y values before plotting (-x now refers to
		vertical axis).

-x[l] [min [max [junk]]] If l is present, x axis is logrithmic. First argument,
		if present, is lower x limit.  Second argument, if present, is
		upper x limit.  A third numeric argument may be present but
		will be ignored.  By default, these values will be determined
		automatically.

-y[l] [min [max [junk]]]  Similarly for y axis

-h  <n>		argument is the fraction of the vertical space to be used for
		the graph.

-u  <n>		argument is the fraction of the vertical space to move up
		before plotting.

-w  <n>		argument is the fraction of the horizontal space to be used
		for the graph (useful if screen dump routine doesn't dump the
		entire width of the screen).

-r  <n>		argument is the fraction of the horizontal space to move right
		before plotting.

NOTES
	Graph is largely equivalent to the program of the same name on Unix,
	with the following exceptions: Data may come from a file rather than
	the standard input.  Line segments that go out of bounds are windowed
	rather than being dropped.  Graph may adjust the specified lower or
	upper limits (outwards) to give convenient axis labels.  Steps along
	axes may not be specified.  The screen is always cleared before
	plotting.  The default grid type is frame with tics rather than full
	grid.  Axes may not be reversed by specifying a lower limit greater
	than the upper limit.

BUGS
	Clearing the screen is mandatory before each plot.

	If the data comes from the standard input, the screen parameters are
	not reset after plotting.  On the Z-100, the keyboard is left with key
	expansion disabled.  (These conditions can be corrected by running
	graph again and specifying a file).

AUTHOR
	Copyright (c) 1985 by James R.  Van Zandt (jrv@mitre-bedford) 27
	Spencer Dr., Nashua NH 03062, 603-888-2272.  Resale forbidden, copying
	for personal use encouraged.  Constructive comments welcome.