GRASP Advanced Technical Document number 0001                   Doug Wolfgram
-----------------------------------------------------------------------------

Calling GRASP functions from external programs   --------   September 6, 1986

     written by and for Microtex Industries, Inc. - Irvine, California

-----------------------------------------------------------------------------

GRASP version required:  GRASP version 1.10c - September 1986

This and all subsequent versions of GRASP have a function within them which
allows the GRASP functions to be called from external sources. This was
accomplished by defining function 'G' under interrupt 10h to pass a string
to the resident GRASP routines which is nothing more than a simple GRASP
command. The definition of the INT 10h function is as follows:

on entry:

Interrupt 10h

AH - contains the function number, 'G' 
CX - contains the length of the string
DX - contains a pointer to the string 

The general theory for applying this is to create a function which does this
for your programming language, then to write and compile your program
including calls to this function. In some cases, it will be in-line code
while in others it may be a routine in one of your libraries, or it may also
be an external function, as in our TPASCAL example in this document. Then,
create a simple GRASP program (perhaps only one line!) which EXECs to your
program. This will load the GRASP routines in memory and place them in 
available range for your program to use. 

-----------------------------------------------------------------------------
Some specific Examples 1: Generic 'C' function.

For most 'C' compilers, it is best to create a function which you can link
with your program, either stand alone, or in a library. The function, written
here for CI-C86 or AZTEC/MANX C, is quite simple.


; CTOGR.ASM
;
; written by John Bridges
;
; Call GRASP functions from your 'C' programs
;
; after assembling and linking this routine with your 'C' program, you would
; execute GRASP commands by entering 'C' function calls like:
;
; grasp("video a\r");
; grasp("pload picture1,1\r");
; grasp("pfade 20,1\r");
;
;
codeseg segment para public 'code'
	assume cs:codeseg

	extrn	strlen:near
	public	grasp

grasp	proc	near		; grasp(string)
	push	bp
	mov	bp,sp
	mov	ax,4[bp]	; pointer to string
	push	ax
	call	strlen		; standard C function to return length
	add	sp,2
	mov	cx,ax		; put length into CX
	mov	dx,4[bp]	; get pointer into DX
	mov	ax,ds
	mov	es,ax		; set ES to data segment
	mov	ah,'G'		; load function number
	int	10h		; execute it!
	pop	bp
	ret
grasp	endp

codeseg	ends
	end

Here is a sample 'C' program to illustrate how it works:

/*******************************
            CTEST.C 
      sample test program
********************************/
#include "stdio.h"

main()
{
	grasp("text 0,0,\"Hi there number 1\"\r\n");
}

Compile and link with ctogr.obj and your standard 'C' library.

Then, here is a sample GRASP program to call it:

video 1
exec ctest.exe
text 0,5,"Hi there number 2"
waitkey

The EXEC command will cause your program to call GRASP to print the first
message, then GRASP back under its own control will print the second, then
GRASP will wait for a keypress to end.

-----------------------------------------------------------------------------
Some specific Examples 2: Turbo Pascal function.

For Turbo Pascal, we will create an external COM file which contains the
calling function to GRASP, and then refer to it as an external function
call with TPascal. The external file is similar to our example for 'C':

; GREXT.ASM - external function call for TPascal to interface to GRASP
;
code	segment
	assume	cs:code

grasp	proc	near
	push	bp
	mov	bp,sp
	les	dx,[bp+4]
	push	bx
	mov	bx,dx
	mov	cl,es:[bx]
	pop	bx
	mov	ch,0
	mov	al,0
	mov	ah,'G'
	int	10h
	mov	sp,bp
	pop	bp
	ret	4
grasp	endp

code	ends
	end

This should be assembled and linked and then converted to a .COM file. The
GREXT.COM file in this example is provided for your convenience.

Then, create your TPascal file, which should be something like:

type
  anystring   = string[255];

var
  grcmd: anystring;

procedure grasp(var grcmd: anystring); external 'grext.com';

begin
  readln(grcmd);
  grcmd:=grcmd+chr(13)+chr(10);
  grasp(grcmd);
end.

This particular example prompts you for a line which is a command in
GRASP, then passes it to GRASP.

And, as in the 'C' example, your GRASP
program which calls your TPascal which calls your external function:

video A
color 3
exec ptest.com
text 5,4,"hi there how are you today"
waitkey

You will notice that this example sets the video mode to A, then the
program it calls (which is above) prompts you for a string. Type in
video 1, which is 80 column text. Then notice how the rest of the GRASP
program runs in that video mode. Notice also, that by applying the patch
defined in TURBO.PAT we are able to run a TPascal program without
screwing up the video mode!

-----------------------------------------------------------------------------