March 19, 1987


     SCRN.ARC is a collection of MSC callable functions that provide 
     fast direct screen reading and writing of chars, strings, and
     blocks of screen memory while *automatically* turning horizontal
     retrace checking on/off based on the type of video card in use. 
     The scrn_init() function checks for monochrome or EGA adapters,
     and if it finds neither, assumes that a CGA card is in use and
     turns on horizontal retrace checking to prevent snow. When retrace
     checking is enabled, all screen i/o is performed one byte at a time
     to prevent even left edge snowing. You also have the option of
     playing it safe and manually setting retrace checking to on.

     Included are functions for real and logical cursor positioning,
     color/attribute setting, scrolling, determining various video
     types and settings, etc....And just for fun, a zoom-in window
     similar to Procomm's exploding windows.  ZOOMDEMO.EXE is an
     example of most of the functions in use.

     IMPORTANT - Before using any scrn_xxx function, two steps must
     be taken, preferably from within main()'s source file:

          1) Declare a structure of type SCRN. Example: SCRN scrn;

          2) Initialize the structure. Example: scrn_init(&scrn);

     Without these two steps, your computer will probably freeze. Freezing
     can also be cause by passing an incorrect number of parameters,
     but the compiler will warn you about that as long as you include
     the function declarations in the video.h file. One other cause of
     freezing is incorrectly passing the structure address, like using
     the address operator (&) from inside a function you've already passed
     the structure's address to. I highly recommend using the MSC /W2
     switch to add warnings of such things during compiling.   	


     Most of the functions in SCRN.ARC are used in ZOOMDEMO.EXE and are
     documented in their source files. Here is a brief listing of each
     function's type declaration, it's description, and example usage.
     
     void scrn_init(SCRN *) - Initializes the screen data structure with
          information specific to the type of video adapter in use and it's
          current mode. Must be called prior to any other scrn_xxx functions.

          Ex: SCRN xxx;
              scrn_init(&xxx);
  

     void scrn_puts(char *, SCRN *) - Writes a string at the current logical
          cursor position, with the current attribute. The logical cursor is
          updated. 

          Ex: scrn_puts("Bop 'til you drop", &xxx);


     void scrn_putca(int, SCRN *) - Writes a char at the current logical 
          cursor position with the current attribute. The logical cursor
          is advanced.

          Ex: scrn_putca('X', &xxx);


     int scrn_getca(int *, SCRN *) - Reads the char and attribute at the 
          current logical cursor position. The return value is the char.
          The attribute is contained in int* upon return. The logical
          cursor is advanced.

          Ex: int ch, at;
              ch = scrn_getca(&at, &xxx);


     void scrn_save(int, int, int, int, char *, SCRN *) - Saves a rectangular
          area of the screen to a user defined buffer. 

          Ex: scrn_save(LEFT, RIGHT, TOP, BOTTOM, &buff, &xxx);


     void scrn_restore(int, int, int, int, char *, SCRN *) - Restores a user
          defined buffer to a rectangular area of the screen. Same parameters
          as scrn_save.



     void scrn_pos(int, int, SCRN *) - Positions the logical cursor (offset
          within the screen buffer).

          Ex: scrn_pos(10, 10, &xxx);


     void scrn_attrib(int, SCRN *) - Sets the attribute for subsequent writes.
          See video.h for attribute definitions.

          Ex: scrn_attrib(INVERSE, &xxx);


     void scrn_color(int, int, SCRN *) - Sets the foreground and background
          color attribute for subsequent writes. See video.h for colors.

          Ex: scrn_color(fore, back, &xxx);


     void scrn_set_cga(int, SCRN *) - Allows manual override of the automatic
          horizontal retrace checking switch. Passing 0 turns off retrace
          checking, 1 turns it on.

          Ex: scrn_set_cga(TRUE, &xxx);


     void scrn_border(int, int, int, int, SCRN *) - Draws a double lined
          border at the given parameters with the current attribute.

          Ex: scrn_border(LEFT, RIGHT, TOP, BOTTOM, &xxx);


     void scrn_hborder(int, int, int, int, SCRN *) - Draws a double lined
          half border with the current attribute. In other words, writes a
          top and bottom border with corners. Same parameters as scrn_border.



     void scrn_wzoom(int, int, int, int, char *, SCRN *) - Draws a zoom-in
          window with the current attribute and saves the area used to a
          user defined buffer which may be restored with scrn_restore.

          Ex: scrn_wzoom(LEFT, RIGHT, TOP, BOTTOM, &buff, &xxx);



     int vid_state(int *) - Returns the current video mode (mono, CO80, etc.)
          and places the screen column width in int*. See video.h for modes.

          Ex: int cols, mode;
              mode = vid_state(&cols);



     void vid_init(int) - Sets the desired video mode. See video.h.

          Ex: vid_init(CO80);   /* set video to color/80 columns */



     void vid_page(int) - Selects the desired video page.

          Ex: vid_page(0);    /* select page zero */



     void vid_set_cur(int, int) - Sets the real cursor position.

          Ex: vid_set_cur(10,10);



     void vid_get_cur(int *, int *) - Saves the real cursor position to
          two user defined integers.

          Ex: int row, col;
               vid_get_cur(&row, &col);  /* must pass address */



     void vid_cur_right(int) - Moves the real cursor right n times.

          Ex: vid_cur_rt(15); 



     void vid_cur_switch(int) - Turns the real cursor on/off.

          Ex: vid_cur_switch(OFF);  /* OFF = 0, ON = 1 */



     void vid_up(int, int, int, int, int, int) - Scrolls a rectangular
          piece of the screen up by n positions with a given attribute.

          Ex: vid_up(0, LEFT, RIGHT, TOP, BOTTOM, BLUE);
          If n = 0, the area will be blanked with the given attribute,
          in this case BLUE.


     void vid_down(int, int, int, int, int, int) - Scrolls down. Same
          parameters as vid_up.



     int vcard_type(void) - Returns a value indicating the current video card
          in use. 
                    0 = Monochrome adapter
                    1 = Color Graphics Card
                    2 = Enhanced Graphics Adapter   



     Now the disclaimer...Although a reasonable amount of research, testing,
     and experimenting has gone into this batch of functions, I make no
     guarantees, implied or expressed, etc., etc. 

     Also, having only recently learned MSC and MASM, I wholeheartedly
     welcome any comments or suggestions.

     Thanks...hope you find these useful.

     Tim Spencer - Compuserve [73657,1400]