NAME
                ticker -- timer interrupt service routine package

        SYNOPSIS
                void installtick(&counter);
                void removetick();
                unsigned int counter;     integer to decrement


        DESCRIPTION
        "ticker" is not actually a C function, but a routine which
        is installed on interrupt 1CH.  At each interrupt (18.21
        times per second) this routine decrements an integer (16 bits)
        whose address was passed during installation.  The C program
        can load and test this integer at any time to perform time-based
        operations.  When the variable is decremented to zero, it
        is not decremented any further; i.e., no underflow occurs.
        Therefore, the integer is actually an unsigned integer with
        a maximum count of 65535, or (65535/18.2) seconds.
        installtick() installs the ticker on interrupt 1CH and
        saves the address of the passed variable. removetick()
        restores the interrupt 1CH vector to its original state.
        Any other routines already installed on this vector are
        executed after ticker, since the ticker chains to the
        original vector after execution.


        EXAMPLE

                 int  counter;

                 main() {
                     installtick(&counter);
                     counter = 18 * 10;  /* about 10 seconds */
                     while(counter > 0); /* delay here */
                     removetick();
                     }

        CAVEAT
             It is imperative to call removetick() BEFORE terminating
             the program,  Otherwise, the system will crash!

        This function is found in SMTCx.LIB for the Turbo-C Compiler