CONTENTS


 1.  DESCRIPTION..........................................................   2

 2.  EXIT STATUS..........................................................   4

 3.  COMMANDS.............................................................   5
     3.1   Interrupt Keys.................................................   8

 4.  NUMERIC PARAMETERS...................................................   9

 5.  ENVIRONMENT VARIABLES................................................  11

 6.  EXAMPLES.............................................................  14

 7.  IN CASE OF DIFFICULTY................................................  15
     7.1   LOCKUPS........................................................  15
           7.1.1  Insufficient Memory  15
           7.1.2  Bad COMM Port Configuration  15
     7.2   Incorrect Batch Files..........................................  16
     7.3   No Carrier Detect..............................................  16
     7.4   PKARC 3.6......................................................  16
     7.5   COMMAND NOT FOUND..............................................  16
     7.6   DOS 3.x........................................................  16
     7.7   Perstor Controllers............................................  17
     7.8   IBM PS/2 Model 50Z.............................................  17
     7.9   Brain Damaged UARTS............................................  17
           7.9.1  Everex Internal Modems  17
     7.10  Weird Iron.....................................................  17
     7.11  Will the real YMODEM please stand up?..........................  17
     7.12  286 and 386 Extended Memory....................................  18

 8.  BACKGROUND OPERATION.................................................  19

 9.  CALLING DSZ FROM COMM PROGRAMS.......................................  20
     9.1   GT POWER 13.00/14.00...........................................  20
     9.2   PROCOMM........................................................  20
     9.3   PROCOMM PLUS...................................................  20
     9.4   Qmodem.........................................................  21
     9.5   BULLETIN BOARDS................................................  21

10.  FLOW CONTROL.........................................................  22

11.  ERROR MESSAGES.......................................................  23

12.  ASSOCIATED DOCUMENTS.................................................  26

13.  FILES................................................................  27

14.  CHANGES..............................................................  28










15.  Other Omen Technology Products.......................................  30

16.  FAIR PLAY............................................................  31
     16.1  Sharing DSZ Files..............................................  31
     16.2  REGISTRATION...................................................  32
     16.3  Files on Registration Disk.....................................  34
     16.4  Bulletin Board Registration....................................  34

17.  ACKNOWLEDGEMENTS.....................................................  36


















































        DSZ - a ZMODEM, True YMODEM(TM), XMODEM File Transfer Program


                                Chuck Forsberg

                             Omen Technology Inc


                                   ABSTRACT



                    ZMODEM - Not just another XMODEM hack

The ZMODEM file transfer protocol provides reliable file and command transfers
with complete END-TO-END data integrity between application programs.
ZMODEM's 32 bit CRC protects against errors that continue to sneak into even
the most advanced networks.

ZMODEM safeguards all data and supervisory information with effective error
detection.  (XMODEM and many recently introduced protocols do not protect
vital supervisory data!)

ZMODEM rapidly transfers files, particularly with buffered (error correcting)
modems, timesharing systems, satellite relays, and wide area packet switched
networks.  ZMODEM's streaming operation eliminates delays caused by
Kermit/XMODEM/YMODEM/JMODEM block acknowledgements.  ZMODEM eliminates the
classic XMODEM/YMODEM/JMODEM PACKET LENGTH compromises between transfer
efficiency and error recovery.  ZMODEM's packet length is the entire file.

User Friendliness is an important ZMODEM feature.  ZMODEM AutoDownload
(Automatic file Download initiated without user intervention) greatly
simplifies file transfers compared to traditional protocols.

DSZ's ZMODEM provides advanced file management features including Intelligent
Crash Recovery, flexible control of selective file transfers, and security
verified command downloading.

DSZ is one of many available programs that implement the ZMODEM file transfer
protocol.


















        DSZ - a ZMODEM, True YMODEM(TM), XMODEM File Transfer Program

                                Chuck Forsberg

                             Omen Technology Inc


                         Omen Technology Incorporated
                        The High Reliability Software

                     17505-V Northwest Sauvie Island Road
                            Portland Oregon 97231
      TeleGodzilla BBS: 503-621-3746 Speed 1200,2400,19200(Telebit PEP)
                              FAX: 503-621-3735
                       Compuserve:70007,2304  GEnie:CAF
                      UUCP: ...!tektronix!reed!omen!caf

  *************************************************************************
Registration bypasses the shareware announcement and unlocks the advanced
features in all past and future versions of DSZ.  You don't have to pay and
pay for new versions, one registration "does it all"!
  *************************************************************************







































Chapter 1 Pg 2            DSZ Reference Rev 02-23-89           Typeset 2-23-89



1.  DESCRIPTION

DSZ is a "protocol driver" that uses the ZMODEM, True YMODEM(TM), or XMODEM
protocol to transfer files over a serial port with a variety of programs.

ZMODEM Transfers feature 32 bit CRC, crash recovery, and advanced file
management.

DSZ has three main commands for ZMODEM transfers: "sz" sends file(s), "rz"
receives file(s), and "t" is a terminal emulation function with automatic no-
keystroke ZMODEM file downloads.

When calling bulletin boards to download files with ZMODEM you can avoid the
bother of starting DSZ for each transfer by calling DSZ first, before asking
the BBS for the download.          dsz t The "t" command allows you to
keyboard the file request to the BBS.  DSZ's ZMODEM AutoDownload then receives
the file automatically, without any wasted keystrokes or delay.  Try it,
you'll like it!  (The "t" command is described below.)

YMODEM downloads are almost as easy.  Use the "t" command as shown above, and
hit the F3 key after telling the board to download a file with YMODEM.

ZMODEM and True YMODEM(TM) transfers preserve exact file length and
modification time.

DSZ supports XMODEM-1k (XMODEM with 1024 byte blocks, sometimes mislabeled
YMODEM) and CRC-16 with the sx -k and rc commands.

DSZ is derived from Omen Technology's "Professional-YAM" high reliability
communications tools, (also known as PowerCom(TM)), and supports a subset of
Pro-YAM's file transfer related commands.  This documentation makes extensive
references to contemporary editions of the ZCOMM or Pro-YAM manual, and is
incomplete without it.  (Registered copies include an alternate, copyrighted
file.)

DSZ is designed to be called from a communications bulletin board program.
DSZ may also be called from other communications programs, but the combination
lacks much of the enjoyable user friendliness of a program with integrated
ZMODEM.

DSZ uses its own modem I/O.  The original interrupt vector, UART parity, and
interrupt configuration are restored on exit.  The original state of the 8259
interrupt mask bit for this vector is also restored on exit.

DSZ uses DOS standard output (stdout) for messages.  It never writes directly
to the screen.  DSZ expects its standard output to point to the console, a
logging file, or NUL, not the modem port.  If dsz's standard output is
redirected to the modem (as with ProComm's Host mode DOS shell), the
combination may lock up the computer.  If necessary, dsz's standard output may
be redirected back to the console device with the CON command.







Chapter 1 Pg 3            DSZ Reference Rev 02-23-89           Typeset 2-23-89



Users of pcAnywhere may use dsz's A command to disable pcAnywhere during file
transfers.























































Chapter 2 Pg 4            DSZ Reference Rev 02-23-89           Typeset 2-23-89



2.  EXIT STATUS

DSZ exits with 0 status for successful transfers, or the value of the Q
parameter (default 1) if a file transfer failed, or if no files were
transferred.  Many languages and "door" programs do not return this
information to the calling program.  Some languages and "door" programs freak
out (hang) on certain non-zero exit values.

A batch file that calls DSZ directly may be used to detect the DSZ exit status
with the DOS "errorlevel" construct.  Please refer to the Q numeric parameter
below for more information.

DSZ's log file entries may also be examined to determine the success or
failure of a file transfer.











































Chapter 3 Pg 5            DSZ Reference Rev 02-23-89           Typeset 2-23-89



3.  COMMANDS

dsz [A] [CON] [port N] [speed S] [handshake XX] [D] [d] command

DSZ commands are an improper subset of Pro-YAM/PowerCom/ZCOMM commands.  The
file transfer commands are fully described in ZCOMMDOC.ARC, the ZCOMM User's
Manual.  Portions of the ZCOMM User's Manual are provided in DSZBG.ZOO, a
Copyrighted file included with the DSZ registration disk.  Please refer to one
of those documents for details on the following commands.

         ***********************************************************
                                  NOTE WELL
Except as noted, all commands must be in entered lower case, NOT UPPER CASE.
(Case is significant!)
         ***********************************************************

When used (in any combination), the A, CON, port, speed, handshake, and d
commands must be given in the order shown.


A     Suspend pcAnywhere operation during file transfers.  This is necessary
      to avoid lockups caused by pcAnywhere host mode.  This command should be
      given to the program running under pcAnyehere host mode.

      EXAMPLE: C>dsz A sz *.foo



CON   Redirect message output to the DOS "CON" (console) device, overriding
      any previous redirections.  This is necessary to avoid lockups caused by
      Procomm host mode.  Most programs do not require this hack.  This
      command is unique to DSZ.

estimate length [speed] Use the specified length and optional specified
      effective speed for the next receive file to be created.  This command
      must come after any port, speed, or handshake commands.  Please refer to
      DSZBG.ZOO or the ZCOMM User's manual for details.

handshake XX Enable one of several choices of hardware handshake.  (The
      default is XOFF/XON software handshake).  This command is documented in
      the ZCOMM or Pro-YAM manual, and in DSZBG.DOC.  (The ZCOMM manual is
      available on all bulletin boards registered for DSZ as ZCOMMDOC.ARC.) On
      DSZ the "handshake" command may be abbreviated to "ha".

port N select port N (n = 1,2,3,4,5,6,7,8, 10,11,12,13,14,15,16,17,18) Default
      is port 1 (COM1) or read from the DSZPORT dos environment variable.
      COM10 to COM18 refer to the COM1 to COM8 ports on the PS/2.

      In multitasking operation, accessing a port used by another running
      program may hang the machine.
      EXAMPLE: to use COM2:






Chapter 3 Pg 6            DSZ Reference Rev 02-23-89           Typeset 2-23-89



      dsz port 2 rz

portx ... Select arbitrary port address and interrupt vector.  Please refer to
      DSZBG.ZOO or the ZCOMM or Professional-YAM manuals for information on
      this command.

speed S Set the specified speed.  This command is rarely needed because DSZ
      reads the port's current speed by default.  Please refer to the FLOW
      CONTROL, MAIN COMMANDS and SOFTWARE COEXISTENCE chapters in DSZBG.ZOO or
      the ZCOMM or Pro-YAM manual for important information about the speed
      command.

D     Disables the modem (drops Data Terminal Ready, DTR) if carrier is lost.
      This may be used to prevent spurious events (phone ringing) from
      interfering with the calling bulletin board's recovery from carrier
      loss.

d     Disables carrier dropout monitoring, for modems that do not properly
      drive the "Carrier Detect" input on the PC.  If you see a No Carrier
      Detect message, you need to give the d command.

LARG  Convert ARG to lower case, then parse arg.

pxN   Set a numeric parameter x to N.  These parameters are mostly a subset of
      the Pro-YAM/ZCOMM numeric parameters, and are listed below.  They assume
      their defaults each time DSZ is called.  Without an argument, p displays
      the numeric parameters and their values.

      EXAMPLE: C>dsz p

      z pxN Set zmodem numeric parameter x to N.  These parameters correspond
      to the Pro-YAM or ZCOMM "zmodem" parameters and rarely need changing.
      These parameters assume their defaults each time DSZ is called.  Without
      an argument, z p displays the zmodem numeric parameters and their
      values.

restrict Restrict pathnames to the current disk and directory tree, and
      disallow overwriting of existing files.  When DSZ is restricted, it will
      refuse to transfer files containing the string autoexec.bat and
      command.com in upper or lower case.  This provides some defense from
      malicious uploaded files.

t     [-8g] Talk with ZMODEM AutoDownload.  The optional -8g (available on
      registered copies only) allows "BBS (ANSI) graphics".  (A video device
      driver such as ANSI.SYS must be loaded to suppport some types of
      graphics.) A small subset of ZCOMM/Pro-YAM term function subcommands are
      recognized.  Keyboard F1 or ALT-X to exit.  F3 receives file(s) with
      True YMODEM(TM), ALT-P toggles parity between the 8n default and 8g
      (enables ANSI "graphics").  ALT-H toggles two local echo ("Half Duplex")
      modes; the second displays a newline (CR/LF) when Enter is keyboarded.
      Keyboarded ASCII characters are sent to the modem.  ALT-B sends a break.






Chapter 3 Pg 7            DSZ Reference Rev 02-23-89           Typeset 2-23-89



      Modem characters print on the screen.  A device driver such as ANSI.SYS
      may be used to recognize escape sequences.

      DSZ's ZMODEM AutoDownload detects the start of a ZMODEM file download
      and accepts the file(s) without operator intervention.

rz    [-abenprt+Yy] [dir] [file ...]          (ZMODEM receive) **

rb    [-abt+y] [dir] [file ...]     (YMODEM receive) **

rb -g [-abt+y] [dir] [file ...]     (YMODEM-g receive) **

rc    [-abt+y] file1                (XMODEM/CRC receive)

ro    [-abt+y] file1                (XMODEM OverThruster receive)

rx    [-abt+y] file1                (XMODEM receive)

rx    -g [-abt+y] file1             (Qmodem-G receive) **

      ** Download directory specification ignored w/o registration


sz    [-abefnprtYQS+y] [-w[N]]  file ...      (ZMODEM send)

sb    [-ft] [PREFIX=p | ONAME=n] file ...     (YMODEM, YMODEM-g send)

sb -k [-ft] [PREFIX=p | ONAME=n] file ...     (YMODEM-1k send)

sx    [-t] file1                    (XMODEM, XMODEM/CRC, Qmodem-G send)

sx -k [-t] file1                    (XMODEM-1k send)

v     Verify the serial number by writing a log entry (see DSZLOG).

      v      1     0 bps    0 cps   0 errors     0  128 s/n 13027

      The letter "v" indicates a verification entry.  The first numeric field
      is 1 if YMODEM-g is supported.  The last field is the serial number.
      Unregistered copies show a s/n of 0.

The meanings of optional arguments to the file transfer commands are described
in DSZBG.DOC and the ZCOMM/Pro-YAM manual.

The s (SlugBait) option prevents a receiver from receiving a file without
accounting for it.  Attempts to do so are flagged with a Q status in the log
file.  This option can cause a transfer that legitimately fails near the very
end of the file to be reported as Questionable rather than ERROR.

Send files may be specified indirectly:
                             dsz sz @C:files.lst






Chapter 3 Pg 8            DSZ Reference Rev 02-23-89           Typeset 2-23-89



sends the files in C:files.lst.  This provides another means of bypassing the
DOS command line limit.  The first letter must be "@" and the third letter
must be ":" to distinguish this from an ordinary pathname.  Pathnames in the
indirect may be separated with any combination of space(s), tab(s), CR and/or
LF.  No spaces may appear inside a pathname; "FOO     .BAR" won't work.

3.1  Interrupt Keys

Ctrl-Break Terminates the transfer in progress.

ALT-N Abruptly terminates (NUKES) the transfer in progress.

Ctrl-X Typing a dozen Ctrl-X characters to another ZMODEM program terminates
     ZMODEM operations.

ALT-F Skips the current file in ZMODEM transfers.

ALT-B Cancels the current ZMODEM session.







































Chapter 4 Pg 9            DSZ Reference Rev 02-23-89           Typeset 2-23-89



4.  NUMERIC PARAMETERS

DSZ uses the following main numeric parameters, settable with the pxN command.

EXAMPLE: C>dsz pQ0


In addition, DSZ uses the Pro-YAM/ZCOMM zmodem numeric parameters described in
the Pro-YAM/ZCOMM reference manual and in DSZBG.DOC.


B   Set the size of buffer used for disk reads and writes.  The default is
    1024, 4096 maximum.  If your copy of DSZ is running on a floppy disk
    system or a very slow turkey hard disk, a larger value may give better
    results.  Too large a value may exhaust memory, induce receiver timeouts,
    cause disconnects(!), or generate spurious CRC errors.  If performance
    logging doesn't work, this parameter is too big.  This parameter is
    supported on versions compiled with TurboC.

    EXAMPLE: C>dsz pB4096 sz A:floppy.fil

    Setting the buffer size larger may lock out the performance log, DSZFILES,
    and/or indirect pathname list in the "tiny model" DSZ flavor.  If you
    aren't bloody sure you need a bigger buffer, don't use one.

O   This parameter controls XMODEM OverThruster(TM).  It is described in
    dszbg.doc.  This file is part of the software package sent to paid
    registrants.

Q   Error code returned to DOS (default 1).  (Success always returns 0.) Some
    programs toss cookies when confronted with certain exit codes.

    EXAMPLE: C>dsz pQ-1 sz foo.bar


S   Timeout in seconds (default 15) waiting for restraint release (XON and/or
    handshake).

W   Wait for Enter key before exiting after an error.  Effective on registered
    copies.  Useful when calling DSZ from DESQview, allows the window to close
    unless there is an error message that should remain visible.

a   Calibrates certain protocol timeouts used with XMODEM and YMODEM transfers
    (Cybernetic Data Recovery(TM)).  This parameter does not affect ZMODEM
    transfers.

    The a numeric parameter is automatically set to 2000 for a 4.77 mHz PC or
    XT, 4000 for a PS2/30, 6000 for an 8 mHz 1ws AT, and 12000 for a PS2/80.
    If your computer has a speedup card or otherwise runs unusually fast (or
    slow!) for its type, you may set the a numeric parameter to a value that
    reflects its speed.






Chapter 4 Pg 10           DSZ Reference Rev 02-23-89           Typeset 2-23-89



    EXAMPLE: dsz port 2 pa4000 rb


    NOTE: Setting this parameter does not suppress the "Unknown Machine Type"
    message which is displayed before the command line is scanned.

d   A non zero value (the default) causes incoming files received with ZMODEM
    and full YMODEM transfers to have their Date set to that sent in the file
    header.  ZMODEM's file management features depend on the transmission of
    each file's modification date.  Files will have the same creation date,
    even if the two machines are in different time zones.  When transferring
    files to/from a Unix system, creation dates are interpreted according to
    GMT or Universal Coordinated Time.  File dating may be disabled with a pd0
    command.
    NOTE: Backdating file creation times may confuse some backup programs.

v   Verbose level (debugging output) Negative values inhibit some routine
    messages.  Setting v to 1 or greater causes serialized copies to ring the
    bell when a transfer is done.

z   Timezone in minutes behind GMT, used for ZMODEM and True YMODEM file
    transfers to coordinate the actual date of the file with computers in
    other time zones.  Effective on registered copies.  PDT or MST corresponds
    to 420.  This may be preset with the ZONE DOS environment variable.

































Chapter 5 Pg 11           DSZ Reference Rev 02-23-89           Typeset 2-23-89



5.  ENVIRONMENT VARIABLES

The following DOS environment variables may be set to modify DSZ operation.

DIRRX (Registered copies only.) Specifies the directory to receive (download)
    files.  If the sting in DIRRX ends with "/", directory and/or disk
    designators in the incoming pathname are stripped, and only the stem (name
    and extension) is used.  Otherwise, if an incoming file has an absolute
    pathname, the incoming pathname is used.

    EXAMPLE: set DIRRX=C:/rxdirect/

    The "set" command defining the receive directory may be placed in your
    AUTOEXEC.BAT file.

DSZFILES May contain a list of up to 9999 pathnames to transmit, with entries
    separated by spaces.  If present, DSZFILES is used in place of a normal
    command line list of files to send with the sb and sz commands.

    EXAMPLE: C>set DSZFILES=file1 file2 file3 *.c
    C>dsz port 2 handshake on sz -r

    In practice, this string would be built up by a calling program and passed
    to DSZ with a "spawnvpe", "execvpe", or similar subroutine call.

    SEE ALSO: Pathname list specification @C:files.lst

DSZLOG log file to receive entries for files sent and received.  (Default
    null).  Sample entries:

Z  46532 38400 bps 3324 cps   0 errors    66 1024 DSZ.COM 1177
Z 124087 19200 bps 1880 cps   0 errors     6 1024 MXY.TMP 1177

    Transfer times are based on the DOS time of day clock and have one second
    jitter.  As with all protocol throughput reports generated by Omen
    Technology programs (and contrary to the false claims of some critics),
    DSZ's throughput figures for ZMODEM, Kermit, and True YMODEM(TM) transfers
    do not take "credit" for pathname and/or protocol overhead characters.
    DSZ's throughput reports do not include the time required to send the
    pathname.  This understates the true time required to transfer files, but
    the time required to send the pathname often depends on the alacrity of
    the operator, and thus does not always reflect the performance of the
    protocol itself.

    Transfers measuring less than one second are reported as having 9999
    characters per second throughput.

    The unlabeled numeric field after the error (retry) count is the number of
    flow control stoppages encountered sending the file.  This number gives an
    indication of flow control restrictions (overloaded networks, etc.)
    encountered during the transfer.






Chapter 5 Pg 12           DSZ Reference Rev 02-23-89           Typeset 2-23-89



    The last numeric field before the file name is the YMODEM block size or
    ZMODEM subpacket length used for the last block in the file.

    The last field is the serial number of the other program, or -1 if this
    information is not available.

    The code letter indicates the type of transfer, Z (ZMODEM), S (X/YMODEM),
    R (X/YMODEM), E (error), or L (transfer terminated by loss of data
    carrier).

    WARNING: If DSZ encounters a loss of carrier or other fatal error
    condition before a file commences transmission, a log entry will not be
    made.

    EXAMPLE: C>set DSZLOG=C:/yam/dszlog


DSZOPT (Paid Registered copies only) String containing default options for DSZ
    file transfers.  Options are optional modifiers to the DSZ sz, rz, sx, rx,
    sb, rb commands.

    An 8n may be appended to the string to make BBS (ANSI) graphics the
    default for DSZ's t command.  The ability to preset these options is
    especially helpful for controlling ZMODEM automatic downloads from DSZ's t
    command.

    EXAMPLE: C>set DSZOPT=r
    Enables DSZ's Intelligent Crash Recovery(TM) as a default.

    Let's say you wish ZMODEM crash recovery, and BBS "graphics" for the DSZ
    term function:
    C>set DSZOPT=r8g


    WARNING: Do NOT include "ena" or any other commands in the DSZOPT string.
    With the exception of the "8g" mode, only **options** may be placed in the
    DSZOPT string!  (Options are the letters that modify the sz, rz, sb, etc.
    commands.  In "rz -r", "r" is an option.)

MAXBYTES Maximum number of bytes allowed for transfer.  If this number is
    exceeded, DSZ skips the offending files (ZMODEM) or aborts remaining files
    in the batch (YMODEM).

DSZPORT Default communications port override, default 1.
    EXAMPLE:
    C>set DSZPORT=2

ZONE sets the z numeric parameter to the number of minutes the current local
    time lags GMT time.  PDT or MST corresponds to 420.  PST corresponds to
    480.  This environment variable has no effect on unregistered DSZ copies.
    EXAMPLE:






Chapter 5 Pg 13           DSZ Reference Rev 02-23-89           Typeset 2-23-89



    C>set ZONE=420
























































Chapter 6 Pg 14           DSZ Reference Rev 02-23-89           Typeset 2-23-89



6.  EXAMPLES

dsz sz c:foo.* b:*.c          (send files with ZMODEM)

dsz sz -Z *.lst               (send files with compression)

dsz sz -r yzmodem.arc         (CRASH RECOVERY: resume interrupted transfer)

dsz rz -r                     (CRASH RECOVERY: resume interrupted transfer)

dsz handshake both sz yzmodem.arc       (Hardware+Software handshake)

dsz sz -n *.*                 (send files that are newer or rx has no copy)

dsz sz -Yn *.*                (Only send files that are newer than receiver's
copy)
                              (Do not send files that do not exist on
receiver's disk)

dsz rz C:/UPLOADS             (receive files to specified directory #)

dsz port 2 speed 38400 restrict rz

dsz rz  -y prog.arc           (ZMODEM, single file pathname override)

dsz z pr1 rx foo.dat          (XMODEM receive, remove file if error)

dsz pO60 ro foo.dat           (XMODEM/OverThruster receive, GEnie MNP #)

DSZ LRC L-Y NEWPROG.ARC       (generate lower case "rc -y" command)

dsz pv2 sz foo >debug.dmp     (Debugging data dump)

dsz sz @C:/bbs/files.lst      (Indirect file list)

# Paid registered copies only





















Chapter 7 Pg 15           DSZ Reference Rev 02-23-89           Typeset 2-23-89



7.  IN CASE OF DIFFICULTY

If you have difficulty getting DSZ to work, start with the following command
to DSZ directly from the DOS prompt, without running any TSR or other COMM
program:
                              dsz port 1 speed 2400 d t
(Change the port number and speed as necessary.) This connects you to the
modem.  Dial a bulletin board by typing AT commands to the modem ("ATDP621-
3746").  Log in as usual.  Then, request a ZMODEM download of a file you don't
already have.  The file will download automatically, you don't have to do
anything.  This procedure verifies the correct operation of DSZ.

The "sb" and "sz" commands exploit DOS's tree structured file system.  An "sz"
command with no file specified sends all the files in the current directory.
A directory or disk specifier expands to all files in that directory.


7.1  LOCKUPS

7.1.1  Insufficient Memory
DSZ complains when it detects insufficient memory to operate.  When calling
DSZ from another program, there may be ALMOST enough memory for proper
operation, but DSZ locks up during a transfer or the calling program freezes
after DSZ displays the "DSZ Finished" message.

Sometimes there is a message about insufficient memory, sometimes just a
lockup and no message.  To verify this problem, call CHKDSK from within your
comms program (not from DOS!) by defining it as an external protocol.  If you
use an interface program (Hotkeyz, Prodoor, etc.), you must call CHKDSK from
that program, as those programs also reduce the memory available to DSZ.

CHKDSK should report at least 64k free memory.  If less memory is reported,
reduce the size of the capture buffer, reboot the system with fewer/smaller
device drivers and TSR programs.  Calling DSZ directly from the comms program
instead of from an interface also saves memory.


7.1.2  Bad COMM Port Configuration
DSZ is fastidious about which interrupt vectors it takes over.  Unlike some
COMM programs, DSZ grabs only the correct interrupt vector for its interrupt
service routine.  This allows multi line operation under DESQview and other
multitasking systems.

Incorrectly configured serial ports that work with programs that pig out both
IRQ3 and IRQ4, will lock up with DSZ.  If DSZ locks up the machine as soon as
it tries to send or receive data, this is usually the fault.  Make sure the
comm port is strapped correctly; COM1 uses IRQ4, COM2 uses IRQ3.  DSZ will
lock up if the comm port is not properly set up.

In addition, DSZ will not work properly if two devices are connected to the
same IRQ line, even when some other programs (that don't use interrupts as






Chapter 7 Pg 16           DSZ Reference Rev 02-23-89           Typeset 2-23-89



intensively) do work normally on the same machine.


7.2  Incorrect Batch Files

Incorrect batch files are the number one source of problems using DSZ for
downloads.  DSZ's command line echo was added to assist in correcting
defective batch files.  Try running DSZ by itself, without any batch files or
TSR programs, calling it directly from DOS as described above.


7.3  No Carrier Detect

If you see a No Carrier Detect message, you really need to give the d command:
                              dsz port 1 speed 2400 d t

Better yet, correct your modem cable to allow proper operation of the Carrier
Detect signal (CD)!

Some BBS and/or "door" programs hang when the program (such as DSZ) they call
returns with a non 0 exit status.  Please refer to the "EXIT STATUS" chapter
of the document for more information.

7.4  PKARC 3.6

It has been reported that PK36 grabs some interrupts and doesn't restore them
on exit in an attempt to prevent hacks of the program.  Since eliminating that
particular version and cleaning up memory, highspeed xfers even with 8250
UARTS work properly again.

The problem with PK 3.6 appears to be most severe if a BBS operator has
doorware, etc that accesses the PK programs from a shell of some sort.  This
info may be helpful to users who are having otherwise inexplicable file xfer
problams.

Phil Katz has written me that this problem has been corrected in subsequent
versions.

7.5  COMMAND NOT FOUND

If you see this message, make sure DSZ is in the DOS PATH.  Sometimes this
error is caused by having too many environment variable strings.


7.6  DOS 3.x

DOS 3.x systems may need to have a "STACKS = 8,256" line in CONFIG.SYS to
prevent antisocial behavior. This is required on the NEC Multispeed, or if
certain TSR's are used.








Chapter 7 Pg 17           DSZ Reference Rev 02-23-89           Typeset 2-23-89



7.7  Perstor Controllers

Several reports have been received indicating Perstor disk controllers
interfere with data comunications.  Perstor is reportedly working on a fix.


7.8  IBM PS/2 Model 50Z

Early samples of this machine have a design error on the motherboard that
causes comms programs to lock up the machine.  Replacing the motherboard with
a correctly functioning unit from current production corrects the problem.
The part number of the replacement PS2/50 Z motherboard is 35F5928.
(Information provided by John M. Choma 73047,3566) In the U.S. IBM has
stonewalled on this issue, but in December 1988 agreed to replace the
defective motherboards under warranty.


7.9  Brain Damaged UARTS

Omen Technology has received reports of problems with defective 8250 type UART
integrated circuits in Leading Edge modem boards, serial port interfaces, and
computers.  The defective chip logic affects high performance software.
Replacing the buggy chip with a newer chip (16450 or NS16550AN) corrects the
problem.  The NS16550AN is a plug in replacement for 8250 and 16450 serial
chips.  386 and fast 286 machines should use the NS16550AN for best results.)
Arrow Electronics at 1-800-932-7769 sells National NS16550AN chips mail order
(credit card) in small quantities.


7.9.1  Everex Internal Modems
Numerous reports have been received concerning difficulties with Everex modem
cards.  Some of these cards contain buggy 8250 chips which are not up to the
demands of full duplex streaming protocols such as ZMODEM.  Replacing the
buggy 8250 chip with a 16450 (or better yet NS16550AN) chip corrects these
problems.


7.10  Weird Iron

A few machines, some with V20 CPUs, don't like DSZ.COM.  We have not been able
to repeat this; TeleGodzilla (using a V20) runs DSZ.COM without a hitch.
Switching to DSZ.EXE has cleared up the problems on other machines.


7.11  Will the real YMODEM please stand up?

Some XMODEM programs claiming to support YMODEM do not send or accept the
YMODEM pathname block.  1024 byte XMODEM is XMODEM-1k, not YMODEM as defined
by Ward Christensen in 1985 when he coined the word.  1987 and later versions
of YMODEM.DOC remind the reader of the official YMODEM definition, which has
not changed since YMODEM's coinage in 1985.






Chapter 7 Pg 18           DSZ Reference Rev 02-23-89           Typeset 2-23-89



7.12  286 and 386 Extended Memory

Virtual memory disk caches and ramdisks using 80286 or 80386 extended memory
require a kluge hardware reset of the CPU chip to return to the normal "real
mode" after accessing extended memory.  This interference to the interrupt
response time causes lost characters on comm ports, and may be minimized by
specifying shorter memory transfers.

Switching to a National NS16550AN UART chip helps tremendously, allowing
transfers at 115200 bps instead of 9600 bps with a standard 8250.  The
NS16550AN is a plug in replacement for 8250 and 16450 serial chips.  Arrow
Electronics 1-800-932-7769 sells National NS16550AN chips mail order (credit
card) in small quantities.












































Chapter 8 Pg 19           DSZ Reference Rev 02-23-89           Typeset 2-23-89



8.  BACKGROUND OPERATION

Three DESQview description files are provided to demonstrate background
operation with modest (66 kb window) memory requirements.  DSZ uses tight
C/ASM code, table driven CRC generators, and buffered receive and transmit for
good performance in the background without hogging CPU cycles.  On a QIC Labs
8 mHz PC-AT clone, DSZ can download files in the background (3 background
clock ticks, 9 foreground clock ticks) with a throughput better than 9600 bps.

2S   Prompts for file name(s) and sends them with ZMODEM protocol.  File: 2S-
     PIF.DVP

2T   Talks to the modem and allows manual YMODEM (F3) or automatic ZMODEM
     downloads.  File: 2T-PIF.DVP

2A   Like 2T, but using Quarterdeck's dvansi.com memory resident ANSI CRT
     device driver to process ANSI screen codes.  File: 2A-PIF.DVP DS.BAT is
     the batch file used by 2A.

These files are written for a port 2 local connection and \TMP directory, but
may be modified to suit your requirements using the DESQview CP command.  The
W numeric allows DESQview to close the window after DSZ finishes, providing a
pleasant user interface.

Other DVPs, Scripts, and Batch files are available on the DESQView conference
on the Sound of Music as DVDSZ20Z.ARC.

Operation at high speed (above 9600 bps) may require the DESQview "Optimize
communications" performance Advanced Setup option.

Newer versions of DESQview may require more "common memory" allocation (6-8 k
bytes) to operate with DSZ.

         ***********************************************************
                                   WARNING
When running DSZ under a multi tasking system such as DESQview, do not allow
two programs to access the same comm port at the same time.  At best, such
actions will disrupt communications.  At worst, your computer will attempt to
open a subspace channel to V'ger.

When running a comm program under DESQview or any related multitasking
executive, DSZ must be called directly from the comm program, in the same
window.  DO NOT open a separate window for DSZ unless you were about to power
down the computer anyway.
         ***********************************************************












Chapter 9 Pg 20           DSZ Reference Rev 02-23-89           Typeset 2-23-89



9.  CALLING DSZ FROM COMM PROGRAMS

It may be necessary to give a

SET COMSPEC=A:\COMMAND.COM

(change as needed) in your AUTOEXEC.BAT file to allow programs to call DSZ.

9.1  GT POWER 13.00/14.00

GT Power version 13/14 includes a YMRX.BAT (YMODEM-g receive) file with an
"rz" command.  You guessed it, "rz" is for ZMODEM protocol (the z means
ZMODEM!).  Please change the file to use the correct "rb -g" for YMODEM-g.

The files ZMTX.ARC and GT1300.NOT available on many bulletin boards contain
useful information for GT Power users.

9.2  PROCOMM

DSZ may not operate properly when called from Procomm if Procomm has files
open at the time.

A number of reports have been received of problems running DSZ from Procomm
Plus because of insufficient memory.  Please refer to the subchapter on
LOCKUPS.

When running under ProComm's Host mode, failure to use the DSZ CON command may
cause Procomm to lock up the computer, or at least interfere with file
transfers, etc.

EXAMPLE: DSZ CON sz %1


The POE, PCALL, DSZ_ZAP, and PROZ programs have been popular in interfacing
DSZ to Procomm's editor gateway.

Hint: the DOS PATH environment variable must include Procomm's directory to
allow POE to locate all the POE files,.  The POE files should be stored in the
Procomm directory.  Setting the "PROCOMM" environment variable is
insufficient.

9.3  PROCOMM PLUS

DSZ may not operate properly when called from Procomm if Procomm has files
open at the time.

Here are some handy settings for Procomm Plus.

First, set the DOS environment as necessary before running Procomm:
SET DSZPORT=2                           (Only needed for COM2)
SET DSZLOG=DSZ.LOG            (If you wish a log file)






Chapter 9 Pg 21           DSZ Reference Rev 02-23-89           Typeset 2-23-89



Then set Procomm's external protocol strings:
A- External protocol 1 upload filename  ...ZMODEMU
B- External protocol 1 download filename ... ZMODEMD

And then some short batch files:
ZMODEMU.BAT:                  DSZ sz %1 %2 %3 %4 %5 %6 %7 %8 %9
ZMODEMD.BAT:    DSZ rz

To make downloads easier, use the "dsz t" command described above.
ZMODEMT.BAT:                  DSZ t

9.4  Qmodem

The following is based on a message from Mike Cody, sysop of HomePlate 313-
385-9969 3/12/24/96 HST

Go into Qinstall and go to frame 3 Directories. Then select External protocols
#3 I think. Now you will see a definition area to tell Qmodem the
Letter,batchfile combo to use.

Now put Z in the letter definition, Zup.bat in the u/l batch zdown.bat in the
d/l batch, and Y in the btch protocol. Now save it at the menu with f10 and S.

Then go to DOS and create the following batch files in your Qmodem
directory...

Zdown.bat: DSZ port %2 speed %1 rz -r

Zup.bat: DSZ port %2 speed %1 sz %3

These are the batch files that will be called by Qmodem.  If uou did everthing
right when uoy hit PGDN or PGUP you will see an external protocol called Z)
Zmodem in the box. For an easier time do a serch for either External.arc or
maybe the string "Qmodem" in the file database as there is a file with several
external prootcols and batch files available in the Mahoney file section (EXEC
BBS).

9.5  BULLETIN BOARDS

When installing DSZ on a bulletin board or host system, be sure to check for
proper operation when the caller hangs up while a file is being sent or
received.

Currently, Only the TurboC version supports file sharing (shared read access
on files sent by  dsz).

Some bulletin board interface routines do not call DSZ to send a file until
they have verified the file's presence by opening the file.  If this checking
is done in DOS's default exclusive open mode, dsz's file sharing will be
defeated.







Chapter 9 Pg 22           DSZ Reference Rev 02-23-89           Typeset 2-23-89



10.  FLOW CONTROL

If you plan to send files over Telenet (PC-Pursuit), you must refer to the
Pro-YAM or ZCOMM Reference manual (in ZCOMMDOC.ARC) FLOW CONTROL chapter for
vital information on flow control considerations necessary for proper
operation of ZMODEM and other streaming protocols.



















































Chapter 11 Pg 23          DSZ Reference Rev 02-23-89           Typeset 2-23-89



11.  ERROR MESSAGES

COM2 1200 bps Carrier Detect enabled Handshake slow
Command line = (commands)
This is a normal message displayed to help resolve problems with incorrect
batch files.  The port number, speed, carrier detect ("enabled" or "DISABLED")
and "handshake" indicate the selected mode of operation.

DSZ FINISHED! exit code = 0
This is DSZ's normal exit when no unrecoverable errors have been detected.  If
an error such as failed file transfer had been detected, the exit code would
be 1, or the value set in the Q numeric parameter.

As the message implies, DSZ has done all of its processing, and has return the
communications port and vector to its original value before displaying this
message.  If the computer locks up after this message is displayed, there's
something wrong with the program that called DSZ, not with DSZ itself.

Unknown Machine Type XX, 'a' parameter preset to 6000 indicates a ROM BIOS
that does not follow the IBM specification for identifying the machine type.
If your computer causes DSZ to display this message, you may set the a numeric
parameter described elsewhere in this document.  This message is generated
before any commands are read, so do not be alarmed when setting the a
parameter doesn't make this message go away.  The a parameter does not affect
ZMODEM transfers.

Need more memory to run DSZ or Abnormal program termination is displayed by
the TurboC startup routine if DSZ is run in too small a memory partition.  If
you see this message, use a larger memory partition for DSZ or remove some
memory resident programs.  This message may also appear if the calling program
fails to free memory before calling DSZ.

No Carrier Detect is displayed when DSZ recognizes a loss or lack or carrier
detect signal from the modem.  This is caused by a line disconnect, defective
cable, or incorrect modem strapping.  It may be disabled with the d command.
Sometimes this is caused by setting the B parameter to too large a value.

Garbage Count Exceeded Indicates ZMODEM has not detected a valid start of
header in a reasonable number of characters.

If DSZ becomes "stuck" on emitting this messages, it is possible the sending
program may not be able to recognize and act upon transmission requests (ZROPS
headers).  The sending program should be corrected.  In the meantime, setting
a ZMODEM packet length with the "zmodem pl4096" command forces the sender to
wait for the receivers' progress reports.

Permission denied comes from the Microsoft C Library.  This may be caused by
attempts to modify a read only file or directory, or create a file in a
nonexistient directory.

A furtive flashing appearance of XOFF or FLOW during ZMODEM or YMODEM-g file






Chapter 11 Pg 24          DSZ Reference Rev 02-23-89           Typeset 2-23-89



sending signifies DSZ is responding to flow control restraint.  This is normal
operation when buffered modems or packet switched networks are used.  ZMODEM's
robustness and reliability allow creative users to transfer files over unusual
multiple computer lash-ups, causing modem data lights and computer status
displays to dance in unfamiliar rhythms.  Got ZRPOS indicates the receiving
program has detected a transmission error and has requested retransmission.
In other words, ZMODEM is doing its job of detecting and correcting missing
and garbled data.  If this happens more often than observed line errors would
indicate is reasonable, there may be a flow control problem in one of four
areas:

  + Between the sending program and its modem.  If using an interface speed
    higher than the transmission speed, or modem to modem error correction
    (MNP, LAPB, PEP, etc.), check that the modem and the sending program are
    configured for the same flow control methods.  Omen Technology's software
    is faster than most other programs, and may expose flow control problems
    not seen with slower software.

  + Between the sending modem and the network.  Correcting this requires
    "handshake both" to allow the sending program to honor both hardware (CTS)
    flow control from the modem and software flow control (XON/XOFF) from the
    network.

  + Between parts of the network.

  + Between the receiving modem and the receiving program.  This can happen at
    high transmission speeds when the receiver has specified a large I/O
    buffer size with the B numeric parameter.

    Excessive interrupt latency from extended memory ramdisks or disk caches,
    and poorly written hard disk drivers also wreak havoc on streaming
    protocols but do not affect start-stop protocols (XMODEM, etc.).

    To correct these problems, give the "handshake slow" command to the
    receiver.

Byte NNNN retry M: <error message> These messages appear when the protocol has
detected an error and is attempting to retransmit the garbled data.  These are
normal messages.

Serial Input Error: Line Status Register HH indicates a slow device driver,
TSR program, or other software is disabling interrupts too long for the
program to accept incoming data, and some characters are lost.  A slow
response to folow control also triggers this message.

The value of the line status register is displayed in HEX.  The following
error conditions when present OR into the Line Status Register.


01   The Interrupt level circular buffer has been overrun.  The remote did not
     respond to 's XOFF or hardware flow control, and continued to send






Chapter 11 Pg 25          DSZ Reference Rev 02-23-89           Typeset 2-23-89



     characters after being told not to.  This problem is alleviated by
     correct modem flow control configuration.


02   Data Overrun is caused by firmware, TSR programs, EGA/VGA board auto-
     select, or operating system software locking out interrupts for excessive
     periods.  Interrupt latency caused by EGA/VGA board auto-select can be
     corrected by disabling auto-select.  Other chapters in this document give
     additional suggestions for correcting excessive interrupt latency,
     primarily the handshake slow command and the NS16550AN UART chip.


08   Framing Error generally caused by line noise or an incorrect transmission
     speed or format (number of bits).  Most protocols require 8 bits no
     parity for proper operation.  This is set automatically by Omen
     Technology programs, but other programs may not be so smart.


10   Break Interrupt generally caused by line noise or an incorrect
     transmission speed or format (number of bits).


18   Break Interrupt and Framing Error (see above) in combination.

Please refer to the In Case of Difficulty chapter of this document for
solutions.

Less commonly encountered DSZ error messages are explained in the Pro-YAM
manual.




























Chapter 12 Pg 26          DSZ Reference Rev 02-23-89           Typeset 2-23-89



12.  ASSOCIATED DOCUMENTS

Consult the Professional-YAM, PowerCom, or ZCOMM manual chapter "OPTIONS FOR
FILE TRANSFERS" for descriptions of the file transfer options.  The "FILE
TRANSFER BASICS" chapter explains the relative merits of XMODEM, YMODEM,
ZMODEM, and other protocols and gives tips on their use.  The "MAIN COMMANDS"
chapter describes the rb, rx, rc, rz, sb, and sz commands.  The "MODEM
INTERFACING" and "FLOW CONTROL" chapters contain important information on the
use of buffered modems with DSZ.

Information on the ZMODEM Inter Application File Transfer Protocol may be
found in ZMODEM.DOC, part of YZMODEM.ARC (available on TeleGodzilla).

C Source code for XMODEM, YMODEM, and ZMODEM transfers is included in
RZSZ.ZOO.  This file includes a Pro-YAM/ZCOMM script to upload a bootstrap
file to a Unix system, force its compilation, and (if the compilation is
successful) upload the rz/sz source files.

The C source code now includes VAX/VMS support.






































Chapter 13 Pg 27          DSZ Reference Rev 02-23-89           Typeset 2-23-89



13.  FILES

2S-PIF.DVP, 2A-PIF.DVP, DS.BAT, 2T-PIF.DVP DSZ.COM, and DSZ.DOC constitute
Omen Technology's DSZ.ARC.

2S-PIF.DVP, 2A-PIF.DVP, DS.BAT, and 2T-PIF.DVP are only used with Quarterdeck
Office Systems' DESQview multitasking executive for background operation.
Their use is described in a previous chapter of this document.

ZCOMMDOC.ARC (manual), ZCOMMEXE.ARC (programs), ZCOMMHLP.ARC (help processor
and database), ZCOMM communications tools.  The ZCOMM files should be
available on the BBS you downloaded DSZ.ARC from.  If these files are not
available, the BBS is not fulfilling the concractual requirements of free BBS
registration of DSZ.

YZMODEM.ARC (available on TeleGodzilla) contains XMODEM, YMODEM, and ZMODEM
Protocol Descriptions.

RZSZ.ZOO contains ZMODEM "C" source code.  (COMPLETE VAX VMS and Unix/Xenix
programs).

DSZ.EXE compiled with the Xenix to DOS XC provides moderately higher maximum
throughput (1700 vs 1300 cps downloading to a 4.77 mHz XT).  The speed
difference is a function of the compiler, the source code is the same.  The
Xenix XC version requires more memory, and does not support file sharing or a
large I/O buffer.  This version is available in DSZEXE.ZOO.

ZCOMM and Pro-YAM also run at a higher speed than DSZ.COM.

DSZBG.ZOO contains DSZBG.DOC.  Part of the DSZ registration disk (and not for
public distribution), this file provides background information on the
ZCOMM/Pro-YAM commands provided in DSZ.

LOOZ.EXE unpacks .ZOO archives.  LOOZ.DOC describes LOOZ.EXE.  The ZOO archive
format is a machine independent improvement on the PC-DOS specific .ARC
format.





















Chapter 14 Pg 28          DSZ Reference Rev 02-23-89           Typeset 2-23-89



14.  CHANGES

Be sure to save your serial number/password (SNP) card and the putsnp program
you received from Omen to use with future versions of DSZ you may download!
The current DSZ version is maintained on GEnie, EXEC-BBS, CompuServe as well
as TeleGodzilla.

A reminder: the -Z option is effective only when it is given to the sending
program.

2-23-89 The term function now sends BREAK in response to the ALT-B key.
Handling of the Ctrl-Break vector has been changed so an untimely keyboarded
Ctrl-C or Ctrl-Break will not hang DOS.

A problem in the 1/17/89 and 2/2/89 versions corrupts files under unusual
circustances.  Please delete all instances of the 1/17/89 and 2-02-89 version.

2-15-89  DIRRX is enabled for BBS registrations (8xxx numbers).  Logic has
been added to simulate transmit interrupts on chips that have problems in this
area.  The "A" command does not require registration.  An interaction between
ONAME= or PREFIX= and the file count display has been removed.  Time/date
conversion routines have been enhanced to deal with files with missing dates.
The "v" command has been added to allow bbs programs to interrogate DSZ's
serial number.

2-06-89 A spurious error message at the completion of YMODEM downloads with a
download directory specified on the command line has been eliminated.

2-05-89 DSZ now returns a non 0 status unless at least one file has been
transferred.  An inappropriate pathname/disk specifier check on specified
download directories has been removed.

Previous versions:

Added the "A" command to prevent pcAnywhere host mode from locking up DSZ.
SlugBait logic has been simplified, reporting any failed file transfer where
any of the last 1K of the file was sent with Q status.

Introduced ZMODEM RLE compression with the -Z option.  (DSZ copies with paid
registration also accept "Z" in the DSZOPT environment variable.) ZMODEM RLE
compression packs runs of the same character in two or three character
sequences.  Compression is useful for screen dumps, uncompressed workspaces,
compiler listings, and other files rich with strings of repeated characters,
but not .ARC and compressed files to more than 1000 per cent (10x speedup!)
for the Personal Computing text file benchmark(!).  When sending to programs
that do not support ZMODEM compression, the -Z option is ignored.  The -Z
option is effective when specified to the sending program only.

Good news for tired frog stompers!  The ZMODEM rz/sz programs are now
available in a VMS C flavor.  The VAX/VMS source files are contained in the
RZSZ.ARC (RZSZ.ZOO) archive file.






Chapter 14 Pg 29          DSZ Reference Rev 02-23-89           Typeset 2-23-89



"Handshake slow" has been added to disable the RTS signal to the modem while
writing to disk, even if the interrupt buffer is not chock full of bytes.
This should help systems with excessive interrupt latency on disk writes.

Setting the v (verbose) parameter to 1 or greater causes serialized copies to
ring the bell when a transfer is done.

DSZ.DOC has been extensively rewritten and reorganized.  DSZ now supports the
advanced buffering of the National NS16550AN and Intel 82510 serial interface
devices.  Arrow Electronics 1-800-932-7769 sells National NS16550AN chips mail
order (credit card) in small quantities.


Pirated/hacked versions of DSZ have cost users and DSZ's developer thousands
of dollars in lost time and other expenses, in addition to injuring the
reputation of Omen Technology and its products.  Regrettably, Omen Technology
cannot support prior versions of DSZ because of this piracy.

Name             Length                           Date        Time   CRC
dsz.com          52622  Crunched   16%     44473  23 Feb 89   1:22p  981b
PKZIP -vt 32 bit CRC: B5F6F990

Your copy of DSZ should show this information as provided by

       arc v dsz
or
      pkxarc -v dsz or
      pkzip -vt dsz

If your copy shows a different CRC or file length, insist on a legitimate copy
and report the source of the bogus/pirated copy to Omen Technology Inc.  Omen
Technology has received reports of serious problems caused by unauthorized
patches to DSZ, and cannot assume liability for the performance of the
resultant code.























Chapter 15 Pg 30          DSZ Reference Rev 02-23-89           Typeset 2-23-89



15.  Other Omen Technology Products

Omen Technolgy makes Professional-YAM, a comphrensive comms program with
unmatched power.  Flavors are available for PC-DOS, Unix, Xenix, and OS/2
Protected mode.

ZCOMM is a full featured shareware version with a $40.00 basic registration.


















































Chapter 16 Pg 31          DSZ Reference Rev 02-23-89           Typeset 2-23-89



16.  FAIR PLAY

Unlike snazzy menu interfaces, reliable high speed transfer protocols take
many hours of testing, often over expensive phone connections, to develop.
Two decades of communications experience and protocol testing are distilled in
DSZ.

DSZ is a user supported program developed and supported by Chuck Forsberg,
owner of Omen Technology.  Countless hours of work and expen$ive resources
went to develop and support DSZ for the myriad environments users use it in.
The fact that most of the problems people encounter with DSZ are caused by
other software, hardware problems, failure to read the supplied documentation,
or pirating has not kept users from seeking and getting help, even if it means
calling the author in the middle of his sleep.

Beyond this, the world of communications is constantly evolving, and it
requires a significant ongoing effort to keep DSZ and its documentation up to
date with the current state of the art.  Individuals with little knowledge of
the dynamic nature of telecommunications (or hidden agendas) have
misrepresented the frequency of enhancements to DSZ as a sign that DSZ is
"unstable" and unworthy of "serious consideration".  If you think such sniping
is fair play, you are more than welcome to use one of the many other protocol
programs available, each of which claim to offer speed and reliability
comparable to DSZ.

Non registered users are welcome to use DSZ for a reasonable evaluation
period.  "Reasonable" means "until you've decided whether the program is worth
$20.00".  It does not mean "until some competing program gets around to adding
ZMODEM or True Ymodem(TM)".  Afterwards, ethical use of DSZ requires
registering the copy.

DSZ is not and never has been Public Domain.  Every version of DSZ has
included a Copyright Notice and a prohibition against sale or modification.
There is no usage counter or other Trojan Horse in DSZ, but if you use this
program, you have a moral and ethical obligation to register it.

Paid registration enables OverThruster(TM), YMODEM-g, and other advanced
features that are present in DSZ.ARC in encrypted form.  The registration
package serializes and decodes all past and future versions of DSZ.COM and
DSZ.EXE.

16.1  Sharing DSZ Files

You are welcome to share unmodified copies of DSZ.ARC with your friends and
associates for their evaluation.  This documentation file and the MAILER file
must be provided with all copies of DSZ except by prior written permission
from Omen Technology Inc.  If DSZ.ARC is "zipped" or otherwise repacked, no
files may be added to or removed from the archive.  Because of piracy
problems, Omen Technology must INSIST that DSZ be distributed only as part of
the DSZ.ARC file EXACTLY as provided by Omen Technology Inci, or in an archive
which displays a CRC value for DSZ.COM equal to that shown in the CHANGES






Chapter 16 Pg 32          DSZ Reference Rev 02-23-89           Typeset 2-23-89



chapter.

If you distribute DSZEXE.ZOO, DSZ.ARC must be included in the same directory
since DSZEXE.ZOO references files in DSZ.ARC.  The DSZEXE.ZOO file may not be
modified in any way, including repacking with another archive program.  I ask
this favor because Rahul's ZOO is a superior archiving format, and I want to
help it along.

If you see an improperly packed or otherwise modified DSZ archive or parts
thereof in a bulletin board, please ask the board's operator to replace such
files with DSZ.ARC exactly as provided by Omen Technology Inc.  Flame them
until they behave responsibly.

No version of DSZ may be sold without the prior written permission of Omen
Technology Inc.

Distribution or use of programs that modify, patch, disassemble, decompile, or
otherwise reverse engineer DSZ without prior written permission by Omen
Technology Inc is a bloody theft of services and a violation of federal
copyright law.  The same applies to debug scripts and documentation written
for the same purposes.  These perform the same function as pirate satellite
and/or cable descramblers, to obtain benefit from encrypted communications
without proper payment.  Piracy has been investigated by the FBI and
prosecuted under federal statutes.  Applicable law provides for damages and
recovery of attorney's fees.  Omen Technology has received reports of serious
problems caused by unauthorized patches to DSZ, and cannot assume liability
for the performance of the resultant code.  So far, none of the slime
producing such bilge have seen fit to sign their real name and address to
their cretinous attempts at ego gratification.

Distribution of DSZ in any medium without this documentation file is an
unauthorized modification to DSZ that deprives the rightful author of
registration revenues.  That is a theft of intellectual property.  Such
distribution also damages the author also obliges the user and author to waste
time and phone bills scrounging for the documentation, and answering questions
that are fully covered in the documentation.

If any version of DSZ is distributed with any other product, software or
hardware, the product documentation must clearly and prominently state that
the customer's continued use of DSZ requires registration directly with Omen
Technology or its duly authorized agent(s).  When DSZ is distributed on disk,
a contemporary copy of ZCOMMDOC.ARC should be included on the same disk.

Thank you for your support.

16.2  REGISTRATION

After a short evaluation period, ethical users must register their copy of DSZ
with a check for $20.00 in U.S. funds sent to:

       Omen Technology Inc.






Chapter 16 Pg 33          DSZ Reference Rev 02-23-89           Typeset 2-23-89



       P.O. Box 4681
       Portland, OR 97208
       For VISA/MC Registrations, voice call 503-621-3406
       FAX: 503-621-3735

The address on your check is sufficient, no need to fill out forms.

Don't bother scrounging for an envelope, just print the INSTANT MAILER
included in this archive!

Overseas registrations are sent out International Air Mail.  Users, especially
those overseas, may choose to register their copy of DSZ for $25.00 U.S.  by
providing their VISA or Mastercard card number with expiration date and their
name as it appears on their credit card.

Please contact Omen Technology before issuing unfunded purchase orders.

  *************************************************************************
The user registration package includes additional user documentation, a
printed serial number password (SNP) card, latest versions of the DSZ
programs, and the installation program which uses the SNP to enable andvanced
features and bypass the opening advertisement.

The registration package unlocks the extra value in all past and future
versions of DSZ.COM and DSZ.EXE.
  *************************************************************************

The unique serial number on the registration card is registered to the user,
and is acceptable proof of registration to corporate auditors.

The putsnp program inserts your unique DSZ Serial Number Password (SNP) into
you copy of DSZ with the following command:
       putsnp dsz.com
Putsnp accepts your SNP and asks appropriate questions before inserting the
SNP to enable the extra value in DSZ.

Some TSR programs have been known to interfere with putsnp.  If you have a
lockup running putsnp, run it without any TSR programs.


The only legitimate way to disable the opening advertisement in DSZ is to
insert an authorized SNP obtained from Omen Technology into DSZ with the
putsnp program.  Any other suppression or modification of the opening screen
is an illegal, unethical theft of services.  Omen Technology has received
reports of serious problems caused by unauthorized patches to DSZ, and cannot
assume liability for the performance of the resultant code.

Piracy is stealing.









Chapter 16 Pg 34          DSZ Reference Rev 02-23-89           Typeset 2-23-89



16.3  Files on Registration Disk

The following files are currently included on the Registration Disk sent to
paid registrants.

LOOZ.EXE       Program to unpack .ZOO archives.


DSZEXE.ZOO     Contains DSZ.EXE.

               To dearchive with looz: looz x dszexe (Note: x must be lower
               case, X won't work!)

               Type "looz" without arguments to see the help message.


DSZ.ARC        Contains DSZ.COM, this document, DESQview description files,
               and an instant no-effort registration mailer.

               To dearchive with looz: looz x yzmodem (Note: x must be lower
               case, X won't work!)


RZSZ.ZOO       ZMODEM C source code, porting base for several dozen ZMODEM
               implementations

               To dearchive with looz: looz x rzsz (Note: x must be lower
               case, X won't work!)


PUTSNP.EXE     Installs your unique registered serial number to enable the
               extra value in DSZ.


DSZBG.DOC (in DSZBG.ZOO) Background information for DSZ, consisting of
               relevant parts of the ZCOMM User's Manual.  DSZBG.DOC is for
               paid registered users only; registered bulletin boards and
               unregistered users are welcome to read the same information
               contained in the ZCOMM manual (contained in ZCOMMDOC.ARC).

               To dearchive with looz: looz x dszbg (Note: x must be lower
               case, X won't work!)


16.4  Bulletin Board Registration

DSZ may be freely used and copied by public bulletin board systems which agree
to the conditions stated in the accompanying bbs_reg.txt file.  Those not
abiding to these conditions must obtain a paid registration for each node.

The purpose of free bulletin board registrations is to support and promote






Chapter 16 Pg 35          DSZ Reference Rev 02-23-89           Typeset 2-23-89



ZCOMM and Professional-YAM by popularizing the ZMODEM protocol.  BBS
registrations must be submitted on the form with signature and date.  BBS
registrations postmarked after the date shown on the form will be ignored.
Free bulletin board registrations are processed in batches, when there is a
major upgrade to ZCOMM.  BBS registrations support the features needed for BBS
operation with ZMODEM.



















































Chapter 17 Pg 36          DSZ Reference Rev 02-23-89           Typeset 2-23-89



17.  ACKNOWLEDGEMENTS

32 bit CRC code courtesy Gary S. Brown.

The High Reliability Software(TM), TurboLearn Script Writer(TM), Cybernetic
Data Recovery(TM), Intelligent Crash Recovery(TM), Error Containment(TM), Full
Time Capture(TM), True YMODEM(TM), OverThruster(TM), Password Guardian(TM),
CryptoScript(TM), and TurboDial(TM) are Omen Technology trademarks.

PowerCom was trademarked in 1985 by POLYTRON Corporation, Hillsboro Oregon.

DSZ and this documentation are Copyright 1988 by Omen Technology Inc, all
rights reserved.  True YMODEM(TM) is an Omen Technology Trademark signifying
YMODEM protocol support that meets the full YMODEM specification.

                         Omen Technology Incorporated
                        The High Reliability Software

                     17505-V Northwest Sauvie Island Road
                            Portland Oregon 97231
                Modem: 503-621-3746 Speed 1200,2400,19200 PEP
                              FAX: 503-621-3735
                       Compuserve:70007,2304  GEnie:CAF