GT POWER - 16.00
                 Copyright (c) 1985, 1990: by P & M Software Co.
                            All rights are reserved.



                             Host Mode Documentation


                                December 10, 1990




                             P & M Software Company
                             3104 E. Camelback Rd. #503
                             Phoenix, AZ      85016
                             U. S. A.



                             Voice Phone: (602) 285-9914
                             Modem Phone: (602) 285-1146























                                    - 1 -



                                Table of Contents
                    -----------------------------------------
     A Brief Summary . . . . . . . . . . . . . . . . . . . . . . .  4
     The Installation Of Host Mode . . . . . . . . . . . . . . . .  4
         The Modem Init String . . . . . . . . . . . . . . . . . .  4
         The Host Mode: Modem Init String  . . . . . . . . . . . .  4
         The Modem Answer String . . . . . . . . . . . . . . . . .  5
         The Modem Result Codes  . . . . . . . . . . . . . . . . .  5
         Logging Status During Host Mode . . . . . . . . . . . . .  5
         Hang-up During Host Mode  . . . . . . . . . . . . . . . .  6
         The BBS/CBS Path  . . . . . . . . . . . . . . . . . . . .  6
         The Default Message Base Path . . . . . . . . . . . . . .  7
         The Default File Section  . . . . . . . . . . . . . . . .  7
         File Reception Directory  . . . . . . . . . . . . . . . .  7
         The Sysop Message Base  . . . . . . . . . . . . . . . . .  7
     Security Considerations . . . . . . . . . . . . . . . . . . .  7
         DSZ.EXE, PCKERMIT.EXE and Other Externals . . . . . . . .  9
     Host Mode Text Files  . . . . . . . . . . . . . . . . . . . . 12
         Forcing a "More?" Prompt  . . . . . . . . . . . . . . . . 12
         Disable the "More?" Prompt  . . . . . . . . . . . . . . . 12
         Nest the Display of Bulletins . . . . . . . . . . . . . . 12
         Disable the ^K/^C Break . . . . . . . . . . . . . . . . . 12
         The Variable Substitution Line  . . . . . . . . . . . . . 12
         ANSI Graphics (.BBS vs .CBS)  . . . . . . . . . . . . . . 12
     File Descriptions . . . . . . . . . . . . . . . . . . . . . . 13
         GTSYSID.BBS . . . . . . . . . . . . . . . . . . . . . . . 13
         GTWELCOM.BBS  . . . . . . . . . . . . . . . . . . . . . . 13
         GTPASSWD.BBS  . . . . . . . . . . . . . . . . . . . . . . 13
             Field Descriptions  . . . . . . . . . . . . . . . . . 14
             GTPASSWD Comment Entries  . . . . . . . . . . . . . . 17
         GTBULLET.BBS  . . . . . . . . . . . . . . . . . . . . . . 17
         BULLETx.BBS . . . . . . . . . . . . . . . . . . . . . . . 17
         GTMENU.BBS  . . . . . . . . . . . . . . . . . . . . . . . 17
         GTHELP.BBS  . . . . . . . . . . . . . . . . . . . . . . . 17
         GTBYE.BBS . . . . . . . . . . . . . . . . . . . . . . . . 17
         GTBYEx.BBS  . . . . . . . . . . . . . . . . . . . . . . . 17
         GTUSER.BBS  . . . . . . . . . . . . . . . . . . . . . . . 17
         GTDIR.BBS . . . . . . . . . . . . . . . . . . . . . . . . 18
             Comment Lines . . . . . . . . . . . . . . . . . . . . 18
             Directory Lines . . . . . . . . . . . . . . . . . . . 18
         GTDDIR.BBS  . . . . . . . . . . . . . . . . . . . . . . . 19
         GTBMENU.BBS . . . . . . . . . . . . . . . . . . . . . . . 20
         GTMDIR.BBS  . . . . . . . . . . . . . . . . . . . . . . . 21
         GTDOORS.BBS . . . . . . . . . . . . . . . . . . . . . . . 22
             GTDOORnn.BAT and GTDORnnn.BAT . . . . . . . . . . . . 23
         ANSWERn.BBS . . . . . . . . . . . . . . . . . . . . . . . 23
         QUESTn.BBS  . . . . . . . . . . . . . . . . . . . . . . . 24
         PQUESTn.BBS . . . . . . . . . . . . . . . . . . . . . . . 25
         GTQMENU.BBS . . . . . . . . . . . . . . . . . . . . . . . 25
         PROTOCOL.BBS  . . . . . . . . . . . . . . . . . . . . . . 25
         WELCOME.BBS . . . . . . . . . . . . . . . . . . . . . . . 26
         MBULLETx.BBS  . . . . . . . . . . . . . . . . . . . . . . 26
         SYSOP.BBS . . . . . . . . . . . . . . . . . . . . . . . . 26
         SCHEDULE.BBS  . . . . . . . . . . . . . . . . . . . . . . 29


                                    - 2 -



         TRASHCAN.BBS  . . . . . . . . . . . . . . . . . . . . . . 30
         FILES.BBS . . . . . . . . . . . . . . . . . . . . . . . . 31
     Host Mode Control Files and Directories . . . . . . . . . . . 32
     Running Host Mode . . . . . . . . . . . . . . . . . . . . . . 34
         SYSOP Commands  . . . . . . . . . . . . . . . . . . . . . 34
         Command Line Usage  . . . . . . . . . . . . . . . . . . . 34
         The HOST.BAT File . . . . . . . . . . . . . . . . . . . . 36
         The HOST.SCR File . . . . . . . . . . . . . . . . . . . . 36
         Using a LAN with GT . . . . . . . . . . . . . . . . . . . 37
             The CB Simulator  . . . . . . . . . . . . . . . . . . 38
     The Host Mode LOG . . . . . . . . . . . . . . . . . . . . . . 41
     The Shell to DOS  . . . . . . . . . . . . . . . . . . . . . . 41
         COMMAND.COM . . . . . . . . . . . . . . . . . . . . . . . 41
         DOS 2.xx  . . . . . . . . . . . . . . . . . . . . . . . . 41
     Using the Shell to DOS  . . . . . . . . . . . . . . . . . . . 42
     The Usage of Color  . . . . . . . . . . . . . . . . . . . . . 43
     The Logon Doors . . . . . . . . . . . . . . . . . . . . . . . 43
     The Logoff Doors  . . . . . . . . . . . . . . . . . . . . . . 44
     Appendix  . . . . . . . . . . . . . . . . . . . . . . . . . . 45
         Extended ASCII Codes  . . . . . . . . . . . . . . . . . . 45
         Sample ANSI Sequences . . . . . . . . . . . . . . . . . . 45
         Power-Loss Protected Operation  . . . . . . . . . . . . . 46
         Sample Files For Power-Loss Protected Operation . . . . . 47
         GT POWER under DESQview . . . . . . . . . . . . . . . . . 48

     (tm) DESQview is the trademark of QuarterDeck Office Systems.






























                                    - 3 -



     Brief Summary
     -------------
     The host mode provided within GT POWER allows you to run an unattended
     session with your system.  That is,  if you expect  to  receive  calls
     from  other  computer systems (say from clients or a set of authorized
     remote users) then you can tell GT POWER that it should  automatically
     answer the telephone for you,  verify the caller's credentials, and if
     found to be valid,  to provide that user with a menu of functions that
     can   be  performed.   All  of  that,   of  course,   without  further
     intervention on your part.

     Security is of paramount importance when  running  in  host  mode  for
     obvious   reasons.   Please   read   the  section  entitled  'Security
     Considerations' before attempting to operate this system.


     Installation of Host Mode
     -------------------------
     The most important thing about host mode is proper installation of the
     modem control strings and result codes.  These strings and codes  must
     not just control the modem,  they MUST WORK TOGETHER.  For example, if
     the modem init strings specify "verbose" result codes, then the result
     code table better have the "verbose" codes  in  it,  not  the  "terse"
     codes.  There  are 11 specific areas that *must* be installed;  all of
     these options and strings are accessible via the ALT-I command.  Let's
     discuss each of these items in turn:

     1.   The "Modem Init String".  The default value is:

                           AT V1 Q0 E0 X1 S0=0 S2=43|

          Assuming that one wants to  use  the  default  string,  there  is
          really  only one thing that one SHOULD DO to this string:  change
          the Xn command.  The most powerful Xn command available  on  your
          modem  is  the  one  to  choose.  With  a USRobotics Courier 2400
          modem,  use either X5 or X6.  With a normal Hayes-compatible 1200
          baud modem, use X1.  X4 would be normal for most Hayes-compatible
          2400 baud modems.  For other modems consult the modem manual.

          NOTE:
               Many  so  called  "Hayes-compatibles" are compatible in name
               only.  We get many calls for support from  individuals  with
               non-Hayes  modems.  Please  read your modem manual carefully
               because it is very hard to support all the different modems.

     2.   The "Host Mode:  Modem Init String".  This string is found  under
          item #30 of the configuration screen.  The default value is:

                           AT V1 Q0 E0 M0 X1 S0=1 S2=255|

          There are several things one could do to this string.  First, one
          must modify the X1 command to match the value added to the  Modem
          Init  String  above.  Secondly,  if one desires the speaker to be
          heard during host mode,  remove the M0 from the string.  Thirdly,


                                    - 4 -



          the  S0=1  may  be changed to S0=0,  THIS IS THE ONLY OTHER VALID
          VALUE!  If S0=0 is used, the modem will not answer automatically,
          GT will count the rings and command the modem to answer after the
          2nd ring (or if the /Rn command line switch is  used,  after  the
          Nth  ring).  This  is  why S0=1 and S0=0 are the only permissible
          values!  Refer  to  the  main  GT.DOC  file  for  a  complete
          discussion of the available command line switches.

     3.   The  "Modem Answer String".  This string is located with the Host
          Modem Init String under item #30  of  the  configuration  screen.
          The default value is:

                           ATA|

          GT  will  issue  this string to the modem whenever the ring count
          reaches 2 (or the number  indicated  by  the  /Rn  switch).  This
          string should not be changed,  unless GT should not be allowed to
          answer the modem.  For example,  one could erase this string  and
          set S0=5,  so that the modem would answer on the 5th ring,  but I
          don't advise anyone do this.

     4.   The "Result Codes".  Because the modem init strings above contain
          V1,  "verbose" result codes should be  programmed.  They  can  be
          found  under  item #29 of the configuration screen.  There are 16
          possible results.  If the modem does not support  all  of  these,
          simply  leave  the  extra  strings  in  their default state.  The
          program comes with the default result codes set for  use  with  a
          USRobotics  Courier HST modem.  Please consult the manual for the
          modem in use and modify this table to match.  Remember,  use  the
          "verbose" (word codes), not the "terse" codes.  It IS POSSIBLE to
          use  the "terse" codes,  but they are not as compatible with such
          services as PC Pursuit.

          If  one of the newer high speed modems is in use,  such as a v.42
          type,  it is most likely that the modem  has  more  CONNECT  type
          result  codes than GT has space in its table.  To get around this
          problem,  and avoid the necessity of  continually  expanding  the
          result  code  table,  GT  will  automatically  recognize  CONNECT
          messages that match the standard form.  For example:

                                CONNECT 9600/REL

          This code is not one of the default codes in the  table,  but  GT
          will recognize it, since it matches the standard form:

                       (1) The word CONNECT, followed by
                       (2) The DCE baud rate, followed by
                       (3) The error correction indicator.

          GT will automatically recognize this and take the proper  action.
          To  enable  this smart result code handling,  the modem *must* be
          setup to return "verbose" codes.

     5.   It  is  highly recommended that logging be TRUE during host mode.


                                    - 5 -



          Otherwise,  all records of  the  host  mode  activities  will  be
          discarded.

     6.   How  to  allow GT to hang-up during host mode.  Since the "escape
          code" must be disabled during host mode,  otherwise  some  caller
          may  crash  your system,  the normal hang-up string,  "~+++~ATH",
          will not work!  Therefore,  GT cannot hang-up the  modem,  unless
          you set the modem to normal DTR operation.  During host mode,  GT
          will drop the DTR signal whenever he wants the modem to  hang-up.
          Most modems come from the factory set so that they ignore the DTR
          signal  -  you  must reset a switch or,  in the case of the Hayes
          2400 modem, you must make an entry in the Modem init string to do
          this.  In any case, if the modem ignores DTR, it will not hang up
          during host mode operations.  Some modems which must be setup via
          the init strings to handle DTR properly use either  &D2  or  &D3,
          please  consult  the manual for the modem in use to determine the
          correct setting.

     7.   How does GT determine when a connection  is  lost?  The  GT  host
          monitors  the  carrier  detect  signal from the modem,  when this
          signal goes low,  then GT assumes that the  connection  has  been
          lost.  Most  modems  come  from the manufacturer with the carrier
          detect signal forced high.  "This is like having a telephone with
          no  ringer."  Quote  by  Tom  Jennings.  Obviously,  this must be
          changed.  Some modems have a switch that must be reset to  enable
          a true carrier detect,  others require setup via the init string.
          Many of the modems that require init string setup use &C1, please
          consult the manual for the modem in use to determine the  correct
          setting.

     8.   If this path is set,  GT will search that path for BBS/CBS files.
          GT will also search the  GTPATH  directory  for  the  files.  The
          GTPATH  directory  is search first,  then the BBS/CBS path.  This
          feature will be of great interest to LAN users,  who are  advised
          to become familiar with the DOS "subst" command, which will allow
          GTMDIR.BBS  and GTDIR.BBS to be the same across a LAN.  Here is a
          sample of the "subst" command:

                                 subst  e:  c:\

          If this command were invoked in the AUTOEXEC.BAT file on your LAN
          server,  then all references to drive E:  on the server would  be
          translated  to  drive  C.  This would be extremely helpful if the
          LAN workstations mapped the server's drive  C  to  E  also.  This
          would  mean  that both workstation and server could reference the
          same physical drive with the same drive letter, i.e. E.

          It is possible to also use the BBS/CBS path for  the  door  batch
          files, but it would be wise for LAN operators to make these files
          Read-Only,  otherwise  they  can cause a SHARE violation,  as DOS
          does not open them in a  shared  read  mode.  The  following  DOS
          command can be used to make batch files Read-Only:

                                 attrib +r *.bat


                                    - 6 -




          Assuming, of course, that the batch files to be altered are in
          the current default directory.

     9.   Another option available under the Alt-I, #26, the pathname setup
          section,  is the "Default Message Base PATH".  This option is  to
          be  used to indicate to GT where the main or default message base
          is located.  This is the message  base  that  the  user  will  be
          initially  given  access to upon calling the system.  This should
          be an open message base since all callers to the system that pass
          the logon procedure will have access to this area.

     10.  Another option available under the Alt-I, #26, the pathname setup
          section, it the "Default File Section".  This option indicates to
          GT where the main or default file section  is  located.  This  is
          the file section that callers will see initially when they access
          your  system.  This  should  be  an area with the lowest security
          access level, as everyone will be able to use it.

     11.  To designate the directory where the host  mode  receives  files,
          you  should  specify the DOWNLOAD directory path.  This option is
          specified under Alt-I, #26, the pathname setup section.  The user
          may be confused by the terminology here,  so let me  stress  that
          the  DOWNLOAD  directory  is  where  GT  POWER  *receives* files,
          whether in host or terminal modes.  Further, the UPLOAD directory
          path only pertains to Terminal Mode,  as the host mode file areas
          are  otherwise  controlled  via  entries  in  the GTDIR.BBS file,
          described below.

     12.  To specify the directory where the host mode will  save  messages
          to  the  sysop.  These  messages are entered with the 'M' command
          from the main menu.  This option is specified under  Alt-I,  #26,
          the pathname setup section.


     PLEASE NOTE:
          The pathnames mentioned above are all found on the pathname setup
          section, #26 of the Alt-I menu.


     Security Considerations
     -----------------------
     Many  of  GT  POWER's  design  considerations  were  directed  towards
     providing  absolute system integrity while in host mode.  This section
     is designed  to  highlight  some  of  those  considerations  with  the
     intention  of making the System operator of a host mode fully aware of
     both his protection and his responsibilities in that regard.

     The fundamental truth about security is that essentially  it  is  YOUR
     responsibility.  GT  POWER's  first  line of defense in your behalf is
     its password  function.  Without  a  preassigned  password,  a  remote
     caller  cannot  gain  access  to  the  functions provided by GT POWER!
     Thus,  it stands to reason that your first responsibility is to assign
     those  passwords and TO GUARD THEM.  Because there are several sets of


                                    - 7 -



     facilities that you will wish to control and to allow various users to
     be provided selectively, GT provides several 'levels' of authorization
     that may be assigned to each password.  In this way, all users who log
     on with the same password will have identical (and only those that are
     assigned) access to GT facilities.  For example,  GT POWER provides to
     users  who  have  a  sufficiently  high 'level' of authorization,  the
     ability to shell into DOS and,  thus,  have the ability to execute ANY
     DOS  COMMAND  from  their  remote location!  Obviously,  you would not
     casually distribute that password amongst your  user  community.  Most
     users  should  NEVER be allowed to Shell to your DOS!  (While in DOS a
     user could,  for example,  format your hard  disk  -  that  would,  of
     course,  result  in  the end of subsequent functionality of the entire
     system).   To  these  users  you  would  assign  a  lower  'level'  of
     authority.  To do so you would simply change their access level to the
     new level with the Sysop Tools program.

     One of the nicest features of the host mode provided by GT  POWER  are
     its  message  bases.  With  this  feature  the users of the system may
     leave 'mail' for other users and receive mail for themselves.  Indeed,
     there are two kinds of mail:  Public and Private.  Public mail may  be
     read by any user of the system.  Private mail,  on the other hand, may
     be read only by the person sending  it  or  by  the  recipient.  Here,
     then,  is  another  area  of security that you need to be aware of and
     control.  For example,  say that you allow your system to be called by
     clients of your firm and that they are encouraged to leave messages to
     you  in your absence.  It is possible that several of your clients are
     competitors of each other.  Thus,  it would be improper to allow  them
     to read messages sent by others.  This is the reason for Private mail.
     At  this point,  I would like to point out that there is no such thing
     as 'Private' from the Sysop!  That is,  the System operator  may  read
     any  message,  whether  addressed  to  him or not and whether they are
     marked Private or not.  Finally, lest the earlier remarks did not sink
     in,  any user who has access to the DOS via the Shell command (because
     of  his  assigned  extremely high 'level' of authorization) can easily
     read any messages while he is in the DOS Shell!

     As  far  as  sending  PRIVATE  messages  to  the  System  operator  is
     concerned,  any user may do that!  There is an 'M' command on the Main
     Menu that results in messages that only  the  Sysop  may  view.  These
     messages  are  automatically  addressed  to  the  Sysop  and marked as
     private.  They are placed in the  message  base  specified  for  sysop
     messages,   they   may   be  read  only  by  someone  with  the  Sysop
     authorization level.  This message base needs to be accessed at  least
     once by the sysop during setup, to insure that a message is entered to
     create  all control files.  Otherwise,  the system will not be able to
     process 'M' messages to the sysop.

     The hierarchy of access 'levels' based on password enables  the  Sysop
     to  control  which  directories on the disk those users have access to
     for purposes of downloading files.  However, each caller to the system
     will be granted access to the  "Default  file  section",  which  is  a
     config  option.  So please be sure that this file section contains the
     least sensitive material on your system.



                                    - 8 -



     For ease of use,  it is recommended that the user  construct  a  batch
     file  to invoke GT POWER,  especially host mode users.  It should look
     like this:

            C:                              To specify a default drive of C
            set GTPATH=C:\GT                Remember to set GTPATH!
            :loop
            GT1600 host.scr                 To invoke GT POWER
            if errorlevel 255 goto loop     To trap the quit 255, and
                                            restart the host mode.

     If the above batch file were called GT.BAT and placed in your system's
     PATH then you could safely invoke GT  by  simply  typing:  GT.  It  is
     important  to  note,  that one of the most frequent errors reported to
     the GT support staff is the incorrect setting of GTPATH.

     As you will see when you read the next section  (about  the  GTDIR.BBS
     file), you can allow your users to have access to all directories that
     have  a  matching  authorization  level  OR  LOWER.  Further,  you can
     specify that particular directories are  only  available  to  specific
     authorization levels.

     Where is all this authorization level information kept within  the  GT
     POWER system?  In a file called GTPASSWD.BBS.  That file is the key to
     the  security  of your system.  One of the subtle security features of
     GT POWER is that it will not allow that file,  even if it is contained
     in a directory that the user has been authorized to Download from,  to
     be transmitted over the telephone!

     NOTE:  That  the  external protocols can transfer prohibited files and
            for this reason, extreme care should be taken when using either
            DSZ.EXE or PCKERMIT.EXE.

     Similarly,  because the Log file that is optionally maintained  by  GT
     contains  the  user  names and passwords of those who have logged onto
     the system, it may not be transmitted over the telephone either.

     When  running  in  host  mode  the screen on the host system shows all
     keystrokes entered by the remote user (except while he is in  the  DOS
     Shell  or using a DOOR,  should that be allowed).  In other words,  if
     the remote user,  for example,  entered a Private message  to  another
     user, or to the Sysop, the text is showing on the host screen as it is
     typed.  If  the  user  were  to log off immediately after entering the
     message then it would  be  possible  that  the  text  of  the  message
     remained  on  the screen.  GT POWER erases the screen after the caller
     hangs up to prevent such a lapse in security.  If you  are  running  a
     host  mode  system  in  an  environment  where others might be able to
     observe the screen then it is recommended that you turn  your  monitor
     off while you are not in attendance.

     If  others may be in the area as you are communicating (chatting) with
     users and you wish to control the information on the screen you  would
     do  well  to  remember that the Alt-W keystroke will erase your screen
     instantly.


                                    - 9 -




     A user-name may be BANned from accessing the  system.  Note,  however,
     that  doing so merely encourages an undesirable to log on with another
     user name.  With the advent of personalized passwords,  this provision
     has  become more effective,  since one could setup the system password
     to have  a  low  access  level,  which  would  be  raised  only  after
     validation.

     Computer  time  is  a resource that you can also control in host mode.
     Each password may have a designated time limit beyond which the caller
     will be automatically logged off.  The number of calls per day made to
     your system by an individual caller is also subject to control.

     One  of  the  more  subtle  security  measures  needed  in a host mode
     ennvironment is called a 'Watchdog'.  In the  GT  POWER  system,  this
     function  is  provided  by a program called DOORMAN.  DOORMAN is a TSR
     program that should be loaded in your AUTOEXEC.BAT  file,  it  has  no
     command  line  options,  and  is  loaded simply by its name,  DOORMAN.
     Should an authorized user be in the DOS Shell or out in a DOOR, and if
     for any reason he were to drop his carrier (hang-up), the system would
     then be vulnerable to the next caller as that caller  could  find  the
     system "in" DOS and he would then have uncontrolled access to do as he
     pleased to your system.  In the situation mentioned,  loss of carrier,
     DOORMAN will force  your  system  to  reboot  and  if  you  setup  the
     AUTOEXEC.BAT  file  properly,  when  the system completes rebooting it
     will invoke GT and put it back in host  mode!  The  same  thing  would
     happen  if  a  power  failure occurs during host mode operation.  When
     power is restored the system will automatically  return  to  the  host
     mode of GT POWER.  Note,  however,  that for those systems that do not
     have a built in clock, the time and date of the system would no longer
     be correct.

     As a Sysop of a GT system you must be aware that there are some  legal
     considerations that you may face.  For example, should you allow users
     to place copyrighted programs onto your system and to then allow other
     users  to download those same programs,  then you are participating in
     an illegal activity!  Naturally there is no way to prevent a user from
     sending you copyrighted material,  provided he has upload  capability.
     There  are many things that you can do,  however,  to stop others from
     having access to that material.  For example,  GT POWER allows you  to
     cause  all  files that are uploaded to your system to be placed into a
     special receiving directory,  rather than into the directory the  user
     is currently using.  It makes good sense to make a receiving directory
     PRIVATE,  in  the  sense  that  it  is  NOT listed as available in the
     GTDIR.BBS to your remote users.  In this way, you may review the files
     received at  your  convenience  and  move  them  over  to  the  public
     directories if you are satisfied that they are either public domain or
     Shareware programs and files.

     Another  reason that you will want to do the above is that there are a
     few people out in the world that like to send what are  called  Trojan
     Horse programs to BBS's.  A Trojan Horse is a program that causes some
     form  of  damage  when it is run.  It would not be at all fair to your
     users to expose them to such programs.  So, when it is safe for you to


                                   - 10 -



     do so,  run the programs  you  receive  before making it publicly
     available (using  BOMBSQAD  or  a
     similar program to prevent a problem for you).  When you are satisfied
     that  the  programs received are safe then you can move them to public
     areas.

     NOTE: Running programs uploaded to a BBS is extremely  dangerous.  And
           can result is the crash of your system, i.e.  someone may break-
           in,  because you have run what seems to be  a  harmless  upload.
           Please be carefull!!

     And  in  the  event  that  a  user  does  send  you  a Trojan Horse or
     copyrighted code,  it is in your best interest to know who did so.  GT
     POWER  provides  an  optional  log file function.  If that is enabled,
     which is highly recommended,  then the log contains the  name  of  the
     person  who logged on and sent you the file.  GT also puts the name of
     the uploader with the file description given at the time of upload.

     This section of the document is substantially larger than you may have
     expected it to be.  The reason should now be obvious.

     YOU are the person responsible for security.  It is necessary that you
     know the previous information and take appropriate actions.

































                                   - 11 -



     Host Mode Text Files
     --------------------
     The following text files must be created  and/or  maintained  with  an
     editor  that  can  produce plain ASCII files.  Any of the display type
     BBS files may have a DC2, Ctrl-R,  character inserted into column 1 of
     line 1 to disable the "More?" prompt during display of the file, and a
     DC4, Ctrl-T, character inserted into column 1 of line 1 to disable the
     Ctrl-K and/or Ctrl-C user break,  or a ENQ, Ctrl-E, character inserted
     into column 1 of any line to force a "More?" pause  at  that  line.  A
     NAK,  Ctrl-U,  can  be inserted in column 1 of any line to introduce a
     variable substitution line.  The ACK, Ctrl-F,  can be used in column 1
     of a bulletin file to nest the display of other text files.

     +--------------------------------------------------------------------+
     |                                                                    |
     |     Ctrl-E ... ENQ ... Insert a "More?" at current location.       |
     |     Ctrl-F ... ACK ... Nest the display of bulletin files.         |
     |     Ctrl-R ... DC2 ... Disable "More?" during file display.        |
     |     Ctrl-T ... DC4 ... Disable ^K/^C break during file display.    |
     |     Ctrl-U ... NAK ... Introduce variable substitution line.       |
     |                                                                    |
     +--------------------------------------------------------------------+

     Please  note  that once the Ctrl-E command has been used the automatic
     insertion of "More?" prompts are terminated for the  duration  of  the
     current display.

     Using the Ctrl-R to disable the "More?" prompt is useful when the file
     contains such graphic or annimation techniques that would  be  spoiled
     by  such  interruption.  Except  for the GT?DIR.BBS files,  every .BBS
     file can have two versions:  (a) a color graphics  version  or  (b)  a
     plain  text  version.  This  is  coordinated  with  the  ANSI graphics
     question asked of callers before  they  logon  the  system.  The  .BBS
     extension  is  the default used if only one version of the file can be
     found by GT,  the .CBS extension is used to  indicate  to  GT  that  a
     graphics  version  is available.  If both versions are available,  the
     .CBS version will be shown to callers who elect graphics,  if graphics
     are not elected by the caller, the .BBS version will be displayed.

     The variable substitution line is interpreted by GT, and certain
     substitutions can be made.  The following are supported:

          A ... The DTE baud rate.
          B ... The DCE baud rate.
          C ... The caller's number (i.e. the 100th caller).
          D ... The current calendar date.
          F ... The caller's first name.
          G ... The caller's screen length setting.
          H ... The caller's home - city and state.
          L ... Time left for current session in minutes.
          M ... The current message base description.
          N ... The caller's full name.
          R ... The caller's upload amount in kilobytes.
          RF .. The caller's upload amount in number of files.


                                   - 12 -



          S ... The current file section description.
          T ... The current time of day.
          Wn .. Set width of the parameter that follows to 'n' columns.
          X ... The caller's download amount in kilobytes.
          XF .. The caller's download amount in number of files.
          n ... 'n' number of blank columns.

     In addition to these items, plain text may also appear on the variable
     substitution line, it must be quoted however, like this:

                "plain text between quotation marks"

          For example:

                ^U"          Name: "N
                ^U"         First: "F
                ^U"          Home: "H
                ^U"Time remaining: "L
                ^U"  Current time: "T
                ^U" Blank Columns: "30"30 of them."
                ^U"   Fixed width: "W30N"30 characters in width"

     The nesting of bulletin files with the Ctrl-F character  is  extremely
     useful,  but also hazzardous, if the nesting is done to a great level.
     For best results,  the nesting should be kept to a  single  level.  An
     example of usage is:

                                 ^FC:\GT\FOO.BAR

     Please note that there is no space between the Ctrl-F and the filename
     and that the full pathname must be given for the file.

     File Descriptions
     -----------------
     GTSYSID.BBS     This  file is displayed as soon as the GT host detects
                     a connection has been  established  with  an  incoming
                     call.  After  displaying  this  file,  GT will ask the
                     user if the terminal program he is using supports ANSI
                     graphics.

     GTWELCOM.BBS    This file is displayed to a caller just before  he  is
                     asked for his name by the GT host.  It should identify
                     the system to callers.

     GTPASSWD.BBS    This  file  contains the list of passwords that people
                     must know to access the system.  The entries  in  this
                     file  are composed of one line per password,  and each
                     line contains the following information,  beginning in
                     column 1:

     Lvlx ([xx:xx(,n,hh:mm,path)]) Pwd Auth (1st-Name Last-Name Phone-Number)

                     These  items  can  have  a  variable  number of blanks
                     between them,  but the "Lvl" must begin in  column  1.


                                   - 13 -



                     EACH  PASSWORD,  "Pwd",  MUST  BE UNIQUE and from 1-20
                     characters in length.

                     The () which have been  shown  around  the  call  time
                     limit, the daily call limit, the daily time limit, the
                     name,  and  phone  number fields,  indicate that these
                     items are optional and need not  be  included  in  the
                     file.

                     Field descriptions:
                     -------------------
                     Lvlx ... The Access Level assigned to this entry.  May
                              be any character from the following sets:  0-
                              9,  A-Z,  or a-z.  NOTE:  "0" is the  highest
                              level   and  "z"  is  the  lowest.   The  'x'
                              following 'Lvl' is  the  bullet  number  that
                              this  caller  will  be  shown.  Valid  bullet
                              numbers  are  0-9,   A-Z.   Read   additional
                              instructions bellow under BULLETx.BBS.

                     xx:xx .. The  Call Time Limit.  This field is optional
                              and is enclosed within [...].  If omitted, it
                              defaults to approximately 24 hours.

                     n ...... The Daily Call Limit.  This field is  a  sub-
                              field within the [...] of the Call Time Limit
                              field.  It  cannot  be  specified without the
                              Call  Time  Limit   being   specified   also.
                              Example:  [1:30,2]  would grant two calls per
                              day of 1:30 duration each.

                     hh:mm .. The Daily Time Limit.  This field is  a  sub-
                              field within the [...] of the Call Time Limit
                              field.  It  cannot  be  specified without the
                              Call Time Limit  and  the  Daily  Call  Limit
                              being specified also.  Example: [1:00,5,2:00]
                              would grant five calls per day, each of up to
                              1 hour each, but a maximum of 2 hours per day
                              total usage.

                     path ... The  upload  pathname.  This  specifies where
                              files uploaded by a particular class of  user
                              are to be stored.

                     pwd .... The  Password.  As  said above,  the password
                              may be from 1-20  characters  in  length  and
                              must  be  unique.  If  this  line  is a class
                              entry the "pwd" field should contain the word
                              CLASS in capital letters.

                     auth ... The Authorizations given to this entry.  They
                              come from the following list:

                              UP : Upload authorized.


                                   - 14 -



                              DN : Download authorized.
                              PR : Private mail authorized.
                              KL : Allow the killing of messages,  the same
                                   as the Sysop.
                              SY : Sysop priveledges authorized.
                              CH : Manual directory  change  is  authorized
                                   (in absence of the GTDIR.BBS file).
                              CB : CB Simulator authorized.
                              SH : Shell to DOS is authorized.
                              DR : Use of DOORS is authorized.
                              MS : Allows message reading.
                              FA : Allows   file   attach  when  using  the
                                   netmail programs.
                              FR : Allows  file  request  when  using   the
                                   netmail programs.
                              NL : Disable  the  L)ist directory command at
                                   the main menu.
                              NE : Disable the E)nter message command.
                              NP : Disable the sysop P)age command.

                              These  authorizations are listed seperated by
                              commas,   following  the  "pwd"  field.   See
                              examples  below.  The  CH  authorization is a
                              "do nothing"  authorization  in  most  cases,
                              because  most  systems  use a GTDIR.BBS file.
                              On these systems the CH option may be used as
                              a way to grant no  authorization,  because  a
                              total   lack   of  authorization  yields  the
                              default authorization set: DN,UP,PR,MS.

                     1st-Name Last-Name Phone-Number
                              These  three  fields  are  present when it is
                              desired  to  allow  the   caller   "callback"
                              priveledges.  In effect, if the caller's name
                              matches the name listed here and he gives the
                              correct  password,  the  system will offer to
                              call him at the listed  number.  This  allows
                              the  host  to  assume  the  cost of the phone
                              charges for the session.  The caller must  be
                              prepared  to  accept  the  call,  that is his
                              modem must be  in  "auto-answer"  mode.  Send
                              "ATS0=1|"  to  most  Hayes type modems to set
                              auto-answer  mode.   The  "|"  represents   a
                              "carriage return".  If the conditions are met
                              GT  will  return  the call within 15 seconds,
                              and will retry 3 times before giving-up  hope
                              of  establishing  the connection.  NOTE:  the
                              password assigned here for the callback, must
                              *not* be the same as  the  caller's  personal
                              password  --  the callback password *MUST* be
                              unique.

              NOTE:  It is possible to append a  single  character  to  the
                     level  indicator.  Thus  "A1"  would be a valid level.


                                   - 15 -



                     This extra character is  used  to  identify  a  custom
                     bulletin  file  for this caller.  This extra character
                     is optional,  but if present MUST BE a character  that
                     is  legal within a file name.  Read about BULLET files
                     below.

                Examples:
                     A  [2:00,100,5:00,c:\goodies] MASTER  SY
                     B1 [1:00] FRIEND  DN,PR
                     B1 [1:00,4,2:00,c:\up] CLASS DN,UP,PR
                     C  [1:30] JOGGER  DN,UP,PR,DR MARY ADAMS 1-213-555-1234
                     A  [2:00,10,4:00] CLASS SY
                     C2 [2:00,3,3:00] CLASS DN,UP,PR,DR

                     In  version 12.10 of GT POWER,  personalized passwords
                     were introduced.  When  a  caller  gets  his  personal
                     password  it is stored in the USER.CTL file,  with the
                     other user information.  The access level assigned  to
                     the  password  used  by  the  caller on the first call
                     (before a personal password was assigned) will be  the
                     access  level assigned to the caller until changed via
                     the SYSOP program.  To provide  a  time  limit,  daily
                     call  limit,  and  bullet#,  a  cross reference of the
                     access level stored in the users  record  in  USER.CTL
                     file  and  the GTPASSWD.BBS file is required.  This is
                     accomplished by placing CLASS cards  for  each  access
                     level  your  system  uses  into the GTPASSWD.BBS file.
                     The format of the CLASS card is the same as  a  normal
                     password  entry,  except the word CLASS must appear in
                     uppercase letters.  In  addition,  the  CLASS  entries
                     cannot  be used to provide callbacks,  normal password
                     entries must be provided for that  purpose.  Here  are
                     some example CLASS entries:

                Examples:
                     A1  [2:00,5,3:00]  CLASS  DN,UP,PR,DR,SH,MS
                     B3  [1:30,2,2:00]  CLASS  DN,PR,MS
                     K2  [:45,1,:45]    CLASS  DN,UP,PR,DR,MS

                     The  first CLASS entry establishes a class for callers
                     with an 'A' access  level,  grants  them  2  hours  of
                     session  time,  and  a daily call limit of 5 calls,  3
                     hours  of  time  per   day,   and   gives   them   the
                     authorizations:  Download,  Upload,  Private mail, use
                     DOORS,  Shell to DOS,  and read  messages.  The  other
                     entries  grant  lesser time amounts to the 'B' and 'K'
                     classes.  The 'B' class  is  given  Download,  Private
                     mail, and read messages authorizations.  The 'K' class
                     is given Download,  Upload,  Private mail,  use DOORS,
                     and  read  messages  authorizations.   Note:   if  you
                     neglect  to setup CLASS entries then once your callers
                     have been assigned their own personal  passwords,  and
                     this is automatically done by GT,  then they will have
                     unlimited time access  to  your  system,  the  default


                                   - 16 -



                     authorizations, and they will not be given a bullet#.

                     It  is  possible  to  add   comment   lines   to   the
                     GTPASSWD.BBS  file.  Any  line with a ';' in the first
                     column is a comment entry, and will be ignored by GT.

               +----------------------------------------------------------+
               |                                                          |
               |      Remember to give callers the MS authorization       |
               |      so they can "read messages".  And setup a CLASS     |
               |      entry for each different access level in use.       |
               |                                                          |
               +----------------------------------------------------------+

     GTBULLET.BBS    This  file  is  displayed  for the caller after he/she
                     completes logon.  It is useful to leave notes here for
                     expected callers.

     BULLETx.BBS     The "x" may be any character that can be a legal  part
                     of   a   filename.   This  character  must  match  the
                     character which is found after the level indicator  in
                     the password file,  to enable custom bulletin files to
                     be displayed for callers.  For example:  if a caller's
                     level  was  "BZ",  then the program would search for a
                     file named BULLETZ.BBS to display whenever the  caller
                     logged onto the program.

              NOTE:  Custom  bulletin  files  are  OPTIONAL.  If you do not
                     wish to use them, simply use single letters for access
                     level indicators.

     GTMENU.BBS      This file is displayed for callers as the  main  menu.
                     It  may  be suppressed by a caller by selecting X)pert
                     mode.

     GTHELP.BBS      This  file  is  displayed  if the caller requests help
                     from the main menu.

     GTBYE.BBS       This file is displayed for the caller when he/she logs
                     off,  i.e.  selects the G)oodbye command from the main
                     menu.

     GTBYEx.BBS      This is  a  custom  bye  file.  The  'x'  may  be  any
                     character  that can be a legal part of a filename.  It
                     comes  from  the  GTPASSWD.BBS  file,  as  the  letter
                     following   the  level  indicator.   Most  commonly  a
                     number.  See custom BULLETx.BBS files above.

     GTUSER.BBS      This file is created whenever a call  comes  into  the
                     system.  It  will contain the access level and name of
                     the current caller, or if no call is in progress,  the
                     previous caller to the system.  The file contains just
                     this 1 line of text.  The exact format is:



                                   - 17 -



     Lvl 1st-Name Last-Name auth baud ANSI-opt last-on limit event time

                     The line is free format with spaces delimiting fields.
                     The  "Last-Name"  field  will  consist  of  a   single
                     character,  a ';', if the caller has only 1 name.  The
                     ';' will act as a placeholder in that  case,  so  that
                     DOOR  programs will have an easier time unpacking this
                     data on the line.  The "auth" field will  contain  the
                     authorizations given this caller from the GTPASSWD.BBS
                     file when he logged onto the system.  The "baud" field
                     will  two  baud rates seperated by a ':',  for example
                     19200:2400.  The first baud rate is the DTE rate,  the
                     second  baud  rate is the DCE rate.  The split rate is
                     necessary for those using high speed  modems.  If  the
                     current  session  is  a  local  sysop logon,  then the
                     "baud" field will contain the word LOCAL, if the sysop
                     is  logged-on.   The  "ANSI-opt"  field  will  contain
                     "NOANSI" if the caller doesn't want ANSI graphics,  or
                     "ANSI" if he does want  the  graphics.  The  "last-on"
                     field  contains  the  date  the  user  last called the
                     system.  The "limit" field contains the remaining time
                     the caller has left for the current call.  The "event"
                     field contains the time remaining until the next event
                     is scheduled.  The "time" field contains  the  current
                     time in "xx:xx" format.  The time remaining fields are
                     integer showing time left in minutes.

                     The  purpose  of  this information is to supply needed
                     control information  to  external  programs  that  run
                     either in the Shell to DOS or DOOR environment.

     GTDIR.BBS       This  file  contains a list of directories that may be
                     accessed by callers.  There are two types of lines  in
                     this  file:  the  actual  directory  lines and comment
                     lines.  The comment lines are displayed to the  caller
                     when he asks to see the list of directories.  The list
                     displayed  will  contain  only  those  directories the
                     caller is authorized to access.  The formats:

                Comment Lines:
                     Contain a blank in the 1st column,  the  remainder  of
                     the line is displayed for the caller.

                Directory Lines:
                     Column  1  - access Level.  The minimum level required
                     to access the directory.  If this column  contains  an
                     "="  then  the  actual  line is shifted to the right 1
                     column and the "=" acts to reserve the  directory  for
                     the  indicated  access  level  - which would now be in
                     column 2. (See example.)

                     One or  more blank  columns follows  the level, then the
                     complete DOS name  of  the  directory,  including  all
                     drive and PATH information.  One or more blank columns


                                   - 18 -



                     follows the directory name,  then a description of the
                     directory is given.  When a caller selects the C)hange
                     directory command,  the list of choices  will  display
                     the  descriptions  you  provide  here,  so  try  to be
                     helpful.

                Examples:

                       This is a comment.  (Since column 1 is blank)
                     A  C:\DOS\TEST The description goes here.
                     =B C:\LOTUS\DATA This is for "B" level callers only.
                     C  A:\ The description again goes here.

                     This example shows three directories,  one with an "A"
                     access level,  one with a "C" access level.  These are
                     the  minimum  levels  that  callers must have to "see"
                     these directories.  The "=B" directory may be accessed
                     only by callers with the "B" access level.

     GTDDIR.BBS      This  file controls access to the GT DOOR system.  Its
                     function  is  much  like   GTDIR.BBS   is   for   file
                     directories.  It  serves  as  a way to add security to
                     doors,  document them and  pass  parameters  to  them.
                     Each  door must have an entry in this file,  there are
                     no comment lines in this file.  Each line in this file
                     follows the this syntax:

           Lvl  ([comment_here_with_no_spaces])  (Prompt message here:)

                     The () indicate which fields are optional and need not
                     be included in the file.

                     As  with  the  GTDIR.BBS file,  the "Lvl" controls the
                     minimum access level required to open  the  door.  The
                     [comment]  is  optional,  but  must be enclosed within
                     [...] if it appears and no blanks are  allowed  within
                     the  comment  field.  If a parameter must be passed to
                     the DOOR,  then the  optional  prompt  field  must  be
                     added.  The  answer given to this prompt by the caller
                     will be passed to the DOOR as  command  line  argument
                     %3.

                     Examples:
                         B  [this-is-door-1]
                         Z  [this-is-door-2]  Enter filename:
                         S  [this-is-door-3]

                     In the example above, the 2nd door has a prompt listed
                     that indicates that this door requires a  filename  be
                     passed.  This could be for example to implement an ZIP
                     view  type door,  where the name of the ZIP file to be
                     processed might need  to  be  supplied.  The  caller's
                     response will be passed as command line argument %3 to
                     the GTDOOR2.BAT file in this case.


                                   - 19 -




                     If you are  using  the  overlaid  doors  command  line
                     option,  /V:D,  it is possible to selectively override
                     the feature and have some doors that are not overlaid.
                     This may be done by putting an '&'  character  as  the
                     first  character  of the prompt (callers won't see it,
                     don't worry).  If you have no prompt for a door,  then
                     just end the line with the '&'.  For example:

                         E [EDLIN_Door_#1] &Enter Filename:
                         E [EDLIN_Door_#2] &

                     Either  method  would  serve  to insure that this door
                     does not overlay GT when it is activated.

               +----------------------------------------------------------+
               |                                                          |
               |     Please note, the order of the lines in this file     |
               |     must be 1st door on 1st line, 2nd door on 2nd line,  |
               |     etc.  The lines must be in 1, 2, 3... order.         |
               |                                                          |
               +----------------------------------------------------------+

     GTBMENU.BBS     This file is the bulletin menu file.  It  should  list
                     the  numbered  bulletin  files.  The numbered bulletin
                     files should be located in the "Default File Section",
                     and their file names should simply be 1, 2, etc.  This
                     menu file will be displayed as users logon your system
                     and besides the numeric bulletins,  two alpha  options
                     should  be  listed:  L)ist  logon  bullets  and  Q)uit
                     bulletin menu.  An example of a GTBMENU.BBS file:

                              1.  Bullet #1 description here.
                              2.  Bullet #2 description here.
                              .
                              .  etc.
                              .
                              L)ist logon bullets
                              Q)uit bulletin menu.

                     It  is  possible that these bulletin files can contain
                     ANSI graphics.  If so, they should be named with a CBS
                     extension.  For example:

                           1          Bullet #1, no extension, no graphics.
                           1.CBS      Bullet  #1,   with  .CBS   extension,
                                      contains graphics.
                           2          Bullet #2, no extension, no graphics.
                           2.CBS      Bullet #2,    with  .CBS   extension,
                                      contains graphics.

                     Remember:  These bullet files must be placed into  the
                                "Default File Section",  as defined under
                                the Alt-I pathname setup.


                                   - 20 -




                     Starting with GT 16.00,  these bulletin files  may  be
                     nested.  When  nesting  bulletins,  we will talk about
                     bulletin numbers with a decimal point embedded within,
                     i.e. 1.0.0 or 2.1.0.  Each successive level of nesting
                     requires  another  decimal  be  added  to  the  bullet
                     number,  to a maximum of 5 levels deep.  When equating
                     the bulletin numbers to file names,  the  periods  are
                     first  eliminated,   for  example  1.0.0  would  equal
                     filename 100,  and 2.1.0  would  equal  filename  210.
                     These  files  would  be  located  in the "Default File
                     Section",  as outlined  above.  If  we  consider  this
                     situation for a bit,  we see that there must be a sub-
                     menu structure applied to these bulletins, in order to
                     get them properly nested.  For example,  we might have
                     the following in the top level file, GTBMENU.BBS:

                             1.0  General Bulletins
                             2.0  Game Bulletins

                     The  1.0  would  refer  to the file 10 in the "Default
                     File Section" and the 2.0 would refer to the  file  20
                     in  the  "Default File Section".  Each of these files,
                     10 and 20,  would be sub-menus,  which  then  actually
                     referred  to the actual bulletins.  For example,  file
                     10 might look like this:

                     ;BMENU

                             1.1  Rules of the board
                             1.2  How to get more time
                             1.3  How to get higher access

                     The line beginning with  ';BMENU'  must  be  the  very
                     first line of file 10,  this signals GT that this file
                     is not actually a bottom level bulletin,  but  instead
                     is  another bullet menu.  Files 11,  12 and 13 are the
                     actual  bulletin  files  (and  therefore,   would  not
                     contain the ';BMENU' entry).

                     Because  these  bullet  menus  can  be  nested up to 5
                     levels deep,  some new letter commands  are  available
                     for usage in navigation.  As follows:

                         M    Return to main bulletin menu (GTBMENU.BBS).
                         P    Pop back to the previous bullet menu.

     GTMDIR.BBS      This  file controls the multiple message bases that GT
                     can support.  The format of this file is the  same  as
                     the  format  for  the GTDIR.BBS file,  except that you
                     have 1 additional option for column 1, you may place a
                     '*' in column 1 of an line in this file and then  that
                     message  area  will  become  a  'by  application only'
                     message base.  The  caller  applies  for  entrance  by


                                   - 21 -



                     trying to select the message area via the A)rea change
                     command.  GT  will  inform the caller that application
                     has been accepted and  the  Sysop  must  approve.  The
                     users  name  will  be  placed into the GTMAIL.CTL file
                     associated with the message base, but the BAN bit will
                     be set,  the Sysop must use Sysop Tools to  reset  the
                     BAN bit so that the caller can be admitted.

                     When setting up, the Sysop should insure that all sub-
                     directories  listed  in GTMDIR.BBS exist,  but GT will
                     automatically  provide  all  the  control  files   and
                     message directories, as needed.

                     All  message  areas  must  have an entry in this file.
                     The main default message area  must  be  open  to  all
                     callers  and must use the same pathname as the message
                     base  pathname  in  GT's   configuration   file.   The
                     GTMDIR.BBS  file  must  be located with the other .BBS
                     files in GT's home directory.

           +--------------------------------------------------------------+
           |                                                              |
           |    The PATH name portion of the lines in the GTMDIR.BBS      |
           |    file may be prefixed with either '^', '~', '<' or '$'.    |
           |                                                              |
           |       ^ ... Designates a message area that can support       |
           |             public messages only.                            |
           |       ~ ... Designates a message area that is used as a      |
           |             netmail area (see netmail docs).                 |
           |       < ... Designates a message area that is Read-Only.     |
           |             Only the Sysop can enter messages.               |
           |       $ ... Designates a message area that can support       |
           |             private messages only.                           |
           |                                                              |
           +--------------------------------------------------------------+

                     Examples:

                     Z   ^C:\GTBBS\OPEN       Public Message Base
                     E    C:\GTBBS\GENERAL    General Message Base
                     F    C:\GTBBS\SPECIAL    Special Message Base
                     Z   ~C:\GTBBS\PUBLIC     Public Netmail Area

     GTDOORS.BBS     This file is displayed for the caller when he  selects
                     the  O)pen  DOORS  option from the main menu.  It is a
                     pure text file,  which should contain your DOOR  menu.
                     Each DOOR is assigned a number,  1-999,  and should be
                     listed on this menu by the number needed to select the
                     door.

                     It is possible to have sub-menus,  which work  off  of
                     the  GTDOORS.BBS menu.  If the GTDOORS.BBS file looked
                     like this:



                                   - 22 -



                                   Main Door Menu
                                   --------------
                                   A.  Game Doors
                                   B.  Database Doors
                                   C.  Utility Doors

                     Then   if  the  caller  selected  'A',   the  sub-menu
                     GTDOOR-A.BBS would shown.  Or  if  'B'  were  selected
                     then  GTDOOR-B.BBS  would  be  shown.  Then whenever a
                     numeric entry was made,  the caller would be put  into
                     the  selected  door.  A  simple  carriage return would
                     take  the  caller  back  to  the   main   door   menu,
                     GTDOORS.BBS.

     GTDOORnn.BAT    These are the DOOR files themselves.  These are  batch
     GTDORnnn.BAT    files,  much  like  the  Shell to DOS batch file,  but
                     instead of executing another copy of  COMMAND.COM,  it
                     executes your DOOR program.  The mechanism of the DOOR
                     is  actually the CTTY commands at the start and end of
                     the file.  The CTTY redirects the console to  the  COM
                     port  at  the start of the DOOR file,  and back to the
                     console at the end.  Sample DOOR  files  are  included
                     with the package.  Here is a short example:

                                    %1 com%2
                                    edlin %3
                                    %1 con

                     The  %1  will become "ctty" or "rem",  and the %2 will
                     become the port number,  through substitution by  DOS.
                     The  "REM" substitution is used when the DOOR is being
                     run locally by the Sysop to check it out.  A DOOR that
                     works in the local mode may  not  work  for  a  remote
                     caller,  because  the DOOR program may not use the DOS
                     functions to perform I/O with the console.

                     Remember  that the 3rd command line argument is passed
                     from the GT host to the DOOR containing  the  response
                     from  the  caller to a prompt you have placed into the
                     GTDDIR.BBS file.  In this case,  it would  have  asked
                     the caller which file he wanted to edit.

                     Please  note  the  two  forms  of  the   door   names.
                     GTDOORnn.BAT  is  used  for door numbers 1 through 99.
                     For  doors  numbered  from  100   through   999,   use
                     GTDORnnn.BAT.  For example:

                               Door #5 ..... GTDOOR5.BAT
                               Door #45 .... GTDOOR45.BAT
                               Door #125 ... GTDOR125.BAT
                               Door #999 ... GTDOR999.BAT

     ANSWERn.BBS     This file contains the answers supplied by the callers
                     to  the 'n' questionaire,  that you have stored in the


                                   - 23 -



                     QUESTn.BBS  file.  The  format  of  this  file  is  as
                     follows:  each  answer given by a user is written on a
                     separate line to this file, the answers are grouped by
                     placing the users name,  from logon,  onto  the  first
                     line  of  the  group,  enclosed  within  <<  ...   >>,
                     following this each answer appears on a separate  line
                     and  each group is terminated with a line containing a
                     single period.  Here is an example:

                               << Paul Meiners >>
                               9350 Country Creek #30
                               Houston, TX 77036
                               713-772-2090
                               .
                               << Susie Meiners >>
                               1245 Sunnyside Dr.
                               Houston, TX 77081
                               713-894-3465
                               .

                     The  example  shown  above  contains  two  groups   of
                     answers.  As  GT  accumulates answers it will continue
                     to append them to the end of this file.  If this  file
                     does  not exist,  GT will create it.  The Sysop should
                     avoid editing this file,  because any attempt to do so
                     may render GT incapable of adding answers to it.

     QUESTn.BBS      This  file  contains  the  questionaire for callers to
                     fill out.  This feature is optional.  The file  is  in
                     template  format,  using  the  [------]  construct  to
                     indicate where GT should gather answers to  questions.
                     For example:

                                                  [------------]
                               Enter Phone Number:

                     Would  direct GT to collect the phone number,  showing
                     GT where to collect the answer and the  maximum  width
                     answer  to  accept.  Each  answer  can  be  up  to  80
                     characters long and there may be up  to  50  questions
                     per questionaire.

                     After  having filled out the questionaire,  the caller
                     will be asked if he wishes his answers to be recorded.
                     If he indicates in the negative,  GT will discard  the
                     answers.

                     The questionaire is optional, and if the user tries to
                     fill out a questionaire that cannot be found,  GT will
                     indicate to the caller that there is  no  questionaire
                     currently available.

                     Date/time   stamping  can  be  done  automatically  by
                     including a special code in  the  questionnaire  file.


                                   - 24 -



                     For example:

                          [%DT]

                     Would  cause  the current date and time to be recorded
                     in the answer file (no question would be asked  here),
                     of  course  the  balance of the questionnaire would be
                     processed in a normal manner.

                     There can be up to 99 different questionnaires for the
                     caller  to  choose  from.   The  GTQMENU.BBS  file  is
                     displayed with a list of all available questionnaires.

     PQUESTn.BBS     This  file  is  displayed  for  the caller immediately
                     after he selects the  questionaire  he/she  wishes  to
                     complete  from  the  questionnaire  menu.   It  should
                     explain  to  the  caller  the  basic  purpose  of  the
                     questionaire and allow him to consider if he wishes to
                     continue  to  fill  out the questionaire.  Immediately
                     after this file is displayed,  the caller will receive
                     a prompt, asking if he wishes to continue and fill out
                     the questionaire.

                     The PQUESTn.BBS file is optional.

     GTQMENU.BBS     This file is listed for the caller when he selects the
                     Q  option  from the main menu.  It is a menu file that
                     should contain a list (in text format) for the user to
                     choose which questionnaire he wishes to complete.  For
                     example:

                         1.  Order form for GT POWER.
                         2.  Order form for Turbo CALC.
                         3.  User poll.

                     This  shows  only  three  options,   as  many  as   99
                     questionnaires may be supported by the system.

     PROTOCOL.BBS    This  file  contains  the  protocol  menu that will be
                     displayed for  the  caller  if  he  initiates  a  file
                     transfer.  It  is  provided  so  that  the  Sysop  can
                     customize this menu to his own taste.  It is pure text
                     format, except for the first line,  which contains the
                     list of protocols the Sysop wishes to activate for his
                     system.  The  format  of  this  activation  line is as
                     follows:

                                  ;XYZB1TWKMSG

                     Where the ";" appears in column 1 of  the  line.  Each
                     letter activates a specific protocol, as follows:

                               X ... Xmodem
                               Y ... Ymodem


                                   - 25 -



                               Z ... Zmodem
                               B ... Ymodem Batch
                               1 ... 1k Telink
                               T ... Telink
                               W ... WXmodem
                               K ... Kermit
                               M ... MegaLink
                               S ... SEAlink
                               G ... Ymodem-G

                     By omitting the activation letter from this line,  the
                     Sysop may  disable  the  corresponding  protocol.  For
                     example:

                                      ;XYZT

                     Would activate and allow on the Xmodem, Ymodem, Zmodem
                     and  Telink  protocols.  The other protocols would not
                     be allowed.

                     The PROTOCOL.BBS file is optional,  if omitted GT will
                     display a canned protocol menu.

     WELCOME.BBS     Each  message  base  may  have  a  welcome screen.  It
                     present,  it resides in the directory with the message
                     CTL files and is displayed for the caller as he enters
                     the message base.  It is in the nature of a conference
                     welcome screen.  The WELCOME.BBS file is optional.

     MBULLETx.BBS    Each  message  base may have bulletins associated with
                     it.  These bulletin files will reside in the directory
                     with the message .CTL files and will be displayed  for
                     the   caller  after  the  WELCOME.BBS  file  has  been
                     displayed.  The bulletin numbers are coordinated  with
                     the regular bulletin numbers in the main GT directory,
                     which come from the bulletin numbers on the entries in
                     the GTPASSWD.BBS file.

                     The MBULLETx.BBS files are optional.

     SYSOP.BBS       The SYSOP.BBS file contains almost all of the  prompts
                     and  short  menus  used by the host mode.  They may be
                     customized to suite the sysop's taste.  But there is a
                     danger in changing the file too greatly,  the  overall
                     length  of  each  entry should not be greatly changed,
                     and each entry is limited  to  1  line.  In  addition,
                     when  new  releases  are made,  it may be difficult to
                     transfer the custom changes to the new file.

                     There are some special lines in  the  SYSOP.BBS  file.
                     The  1st line of the file is the welcome to chat mode,
                     it should be customized to let  the  caller  know  who
                     they  are  chatting  with.  The  3rd  line of the file
                     should have the name of the  sysop  replace  the  word


                                   - 26 -



                     'Sysop'.  This  will  allow  GT to personalize message
                     left to the sysop.  On line 158, the minimum length of
                     passwords required by the host mode  is  configurable.
                     The  minimum length may be set anywhere from 0 through
                     9 characters.  This is accomplished by  changing  line
                     158 in SYSOP.BBS to reflect the desired width.  For
                     example:

                 "Password is too short[!]  Must be [6] - [20] characters."

                     GT  scans this line looking for the very first number.
                     In this case,  GT would find the number  6,  and  that
                     would become the minimum length for passwords.

                     Near the end of the SYSOP.BBS file  are  more  special
                     lines.   First,   the   <Alt -_>   and  <Alt =+>  time
                     increment can be customized.  If a caller  is  online,
                     the  sysop  can  increment  his  time limit by a small
                     amount, use <Alt -_> to decrease the available time or
                     <Alt =+> to increase the available  time.  The  amount
                     of  the  increment  is shown on a line near the end of
                     the SYSOP.BBS file that begins like this:

                          "\n\n3 min. increment

                     The number following the "\n\n" is the amount  of  the
                     change.  It can be any number from 1 to 9 minutes.

                     A little farther down in the SYSOP.BBS file is a line
                     that looks like this:

                          ".ZIP .LZH .ARC"

                     This line contains the  default  extensions  that  are
                     used  to  satisfy  download  requests.  Each extension
                     must be separated from the  one  before  by  a  single
                     space,  and  each  extension  must  begin  with  a '.'
                     character.  This line can be changed or added  to,  if
                     need  be,  but there should probably be no more than 5
                     defaults  listed,  otherwise  system  performance  may
                     degrade.

                     Even closer to the end of the SYSOP.BBS file are two
                     lines that look like this:

                          "MENU="
                          "MMENU="

                     These lines may be modified to add items to the  menus
                     used  in  the GT host mode.  The MENU= line is used to
                     add items to the main menu and MMENU= is used  to  add
                     items  to  the  message menu.  Each item that is added
                     must have a two  character  invokation  sequence.  For
                     example:


                                   - 27 -




                          "MENU=[ZV]viewzip;Q;Enter filename:"

                     'ZV' is the command selection character (i.e. what the
                     caller will need to enter to  execute  this  command).
                     'viewzip'  is  the name of the batch file that will be
                     executed.   The  'Q'  is  the  minimum  access   level
                     required  before a caller can select this menu option,
                     and the 'Enter filename:' is a prompt  for  data  that
                     will be passed to the batch file.  The prompt for data
                     may  be  prefixed  with  a  '&',  as  with  entries in
                     GTDDIR.BBS,   to  selectively  override  the   overlay
                     process (command line option /V:D).  For example:

                     "MENU=[ZV]viewzip;Q;&Enter filename:;[MR]modread;Z;&"

                     The access level and prompt for data are optional, but
                     they  may  not be skipped over.  That is,  if you have
                     specified a prompt for data,  you must  also  have  an
                     access level specified.

                     In the example above,  showing [MR] for the batch file
                     'modread',  the '&' is shown without  any  prompt.  In
                     this case,  there would be no prompt for data, and the
                     command would not overlay GT.

                     Several commands can be  added  in  the  manner  shown
                     above  to each of these two lines in SYSOP.BBS,  MENU=
                     and MMENU=, but one must be carefull not to extend the
                     lines past 255 characters in length.

                     The interface to the  batch  files  invoked  by  these
                     items  is  similar  to  the command interface for door
                     batch file.  As follows:

                         Param     Description
                         -----     -----------
                           1       The CTTY or REM indicator.
                           2       The COM port number.
                           3       The prompted for data.

                     The last param, #3, is optional, of course.  And,  for
                     items  on  the MMENU= list,  GT automatically adds the
                     following four parameters:

                           4       -Ppathname, where 'pathname' is the path
                                   to the currently active message base.
                           5       The message number previously read by
                                   the caller.
                           6       Access control switch block, where a
                                   0=false and 1=true:
                                       a. Netmail message area.
                                       b. Public message area.
                                       c. Private message area.


                                   - 28 -



                                       d. Read-only message area.
                           7       Netmail credits available to this
                                   caller.

                     For example:

                        medit CTTY 1 foobar -PC:\GT\MSGB1 103 0100 200

                     Where:

                        medit ......... The name of the batch file from the
                                           MMENU= line in SYSOP.BBS
                        CTTY .......... The caller is coming in remote
                        1 ............. on COM port #1.
                        foobar ........ Data given by caller in response to
                                           the prompt (optional).
                        -PC:\GT\MSGB1 . The currently active message base.
                        103 ........... The previous message read by caller.
                        0100 .......... Access control switch block:
                                          0: Not netmail area.
                                          1: Public messages only.
                                          0: Not for private messages only.
                                          0: Not a read-only message base.
                        200 ........... This caller has 200 netmail credits.

     SCHEDULE.BBS    The "scheduler" is code within the GT host mode  which
                     allows  the  sysop  to schedule events.  The format of
                     the SCHEDULE.BBS file is  very  simple.  The  file  is
                     composed  of  lines that begin with a time or range of
                     times,   then  the  command  to  be  executed  at  the
                     specified  time.  The  entries  in  this  file for the
                     schedule *must* be in strict ascending numeric  order.
                     Notice   the   entry   below  for  '24:50',   in  GT's
                     terminology this is 50 minutes past  midnight.  To  GT
                     there  is  no 0 hour.  The hour between midnight and 1
                     a.m.  is the 24th hour,  and *MUST* be  shown  at  the
                     bottom  of  the schedule - remember,  strict ascending
                     numerical sequence.

                     Examples:

                     03:00       copy file1 file2
                     03:30       QUIT 5
                     04:00-05:00 QUIT 6
                     06:00       maint
                     24:50       QUIT 8

                     Based on the above example, at 3 a.m. the GT host will
                     copy file1 to file2 (any DOS command can  be  executed
                     like  this).  Then at 3:30 a.m.  the GT host will quit
                     execution and set an ERRORLEVEL of  5,  the  runstream
                     that  is  controlling GT must be prepared to deal with
                     this ERRORLEVEL,  else nothing will be done.  Also the
                     user  must  insure  that the GT host is restarted.  At


                                   - 29 -



                     any time between 4 a.m.  and 5 a.m.  the GT host  will
                     quit  execution  and an ERRORLEVEL of 6 -- this one is
                     meant to illustrate a quit to  the  netmail  function,
                     which  should always be started with a range of times,
                     so that in case it cannot start exactly on the  button
                     of  4  a.m.  the GT host will start it,  even if it is
                     late   starting.   Again   the   runstream   that   is
                     controlling  GT  must  be  prepared  to  deal with the
                     indicated ERRORLEVEL, 6 in this case, and must restart
                     the GT host *after* 5 a.m.  Then at 6 a.m. the GT host
                     will execute the 'maint' batch file.  NOTE:  when  the
                     GT host starts a command like this, it is done via the
                     SHELL  mechanism,  this requires alot of memory and it
                     is not recommended  if  you  are  using  multi-tasking
                     software.

                     A  sysop  may  also  add  a  special   line   to   the
                     SCHEDULE.BBS  file  which  will  allow  control of the
                     P)age function from the main menu.  The OFFICE command
                     allows the sysop to  specify  when  a  P)age  will  be
                     acceptable.  If  a  P)age  is attempted outside of the
                     specified time range, then the caller will be notified
                     about the sysop's OFFICE HOURS.

                     Here is the format:  OFFICE=08:00-21:00

                     The hours must be given in 24:00 notation,  and please
                     notice that leading zeros, must be supplied.  08:00 is
                     correct,  8:00  is  wrong!   No  embedded  spaces  are
                     allowed in this format.  It must be as shown above.

               +----------------------------------------------------------+
               |                                                          |
               |                          NOTE                            |
               |                                                          |
               |    Five minutes prior to a external event, GT POWER      |
               |    will cease accepting calls and wait for the event     |
               |    start time.  Callers who call in the vicinity of      |
               |    an event will have their time on the system cutback   |
               |    so that the caller will be off the system before      |
               |    the event is to start.                                |
               |                                                          |
               |                                                          |
               +----------------------------------------------------------+

     TRASHCAN.BBS    This file will test your creativity  <GRIN>.  All  the
                     dirty words go in here,  and then anyone, who uses one
                     of them in their name,  will not be allowed  to  enter
                     your system.  The words in the TRASHCAN.BBS must be in
                     _lowercase_,  otherwise  they  won't be recognized.  A
                     special wildcard character can  be  used  in  TRASHCAN
                     words,  the  '?'  character can be used to match *any*
                     character other than a blank.  The blank is treated as
                     a delimiter between first and  last  names,  and  each


                                   - 30 -



                     name  is  checked  against  the trashcan individually.
                     The check is only performed on  new  callers  to  your
                     system, so it doesn't slow the regular logon.  And use
                     of  the  trashcan is optional.  Just leave it out,  if
                     you don't want to  use  it.  An  example  TRASHCAN.BBS
                     file:

                                      d?mn
                                      h?ll
                                      scr?w
                                      f?ck
                                      sh?t

     FILES.BBS       When  you create a directory to contain files,  either
                     for upload or download,  you should include within the
                     directory  a  file named FILES.BBS.  It should contain
                     the descriptions of the  files  contained  within  the
                     directory.  When  the  caller  selects  the "F" option
                     from the main menu,  the content of this file will  be
                     displayed.

                     The  FILES.BBS  that  is  located  in  the appropriate
                     upload directory will be  updated  automatically  with
                     information supplied by the uploader as follows:

                     Position     Description
                     --------     -----------
                     1-12         Filename
                     13           Blank
                     14-21        File size in bytes
                     22-23        Blank
                     24-31        File upload date
                     32-33        Blank
                     34-41        File creation date
                     42           Offline indicator: '*' means offline
                     43           Blank
                     44-78        Caller who uploaded the file.

                     Following this header line will come up to 10 lines of
                     description.  Each line of description will begin with
                     a '|' as the first non-blank character (i.e. not equal
                     to  0x20).  The  format  of  the  description  may  be
                     changed by the sysop from the default used by GT,  the
                     only rule is that the first non-blank (i.e.  not equal
                     to 0x20) must be the '|',  otherwise GT will treat the
                     line as a header or a comment.

                     A header is  a  line  that  begins  with  a  non-blank
                     character,   i.e.   not  equal  to  0x20  (except  for
                     description lines, detailed above).  A comment line is
                     any other line that begins with a blank (0x20).

                     NOTE: 0x20 means the character is hex 20.  A blank.  A
                           character whose decimal ASCII value is 32.


                                   - 31 -



     Host Mode Control Files and Directories
     ---------------------------------------
     During  the  operation  of  the  GT  host  mode,   several  files  and
     directories will be created automatically.  The  Sysop  Tools  program
     must  be used to maintain these files,  when the need arises.  Here is
     an overview of the purpose of these files:

     MESSAGE.CTL     This  file  contains  the  header  information for all
                     messages maintained by the GT host.  Such  information
                     as  sender  name,  addressee  name,  date of entry and
                     whether or not the message has been received, are kept
                     here.

     USER_MSG.CTL    This file  contains  information  about  the  messages
                     which  have  been read by each caller who has joined a
                     message base.

     USER_MSG.IDX    The index  file  for  the  USER_MSG.CTL  file.  Speeds
                     access to individual caller records.

     USER.CTL        This file contains information about  the  callers  to
                     your  GT  host.  Such  as  their name,  where they are
                     calling from and their personal passwords and access
                     level.

     USER.IDX        The index file for the USER.CTL  file.  Speeds  access
                     to individual caller records.

     FILES.CTL       This file contains information about all the files  on
                     the  system  that  are  available for download.  It is
                     built by the FILES_DB.EXE program  (and  the  FILES_DB
                     must be run to build a new FILES.CTL whenever you move
                     files around on the system.  The presence of this file
                     enables  the  universal  download feature and helps to
                     eliminate duplicate uploads (that is,  GT will  lookup
                     filenames in this database prior to allowing an upload
                     from  a  caller  -  if you already have the file,  the
                     upload will not be allowed to continue).

     FILES.IDX       The index file for the FILES.CTL file.  Speeds  access
                     to  individual  file  records.  Even on very large BBS
                     systems,  access to the files database is accomplished
                     in less than a second or two.

     GTMSGS          This is a sub-directory where the text of the messages
                     is  stored.  Each  message  is  stored  without header
                     information,  which is stored in the MESSAGE.CTL file.
                     The messages are stored in files with an extension  of
                     .MES.  Each .MES file contains 10 messages  within  it.
                     As follows:

                         00001.MES   Contains messages  #1 through #10
                         00002.MES   Contains messages #11 through #20
                         ...etc...


                                   - 32 -




                     The  messages  are  stored in plain ASCII text format.
                     Each  message  begins  with  a  'start   of   message'
                     indicator with the following format:

                         Col 1 = Ctrl-X
                           2-4 = 'SOM'
                             5 = '0' through '9', depending of the relative
                                 position of the message within the file.

                     Within  00001.MES,  message  #2 would have a header of
                     ^XSOM1,  where  ^X  is  the  symbol  for  Ctrl-X.   In
                     00002.MES,  messages #12 would have a header of ^XSOM1
                     --- the same as message #2 in 00001.MES.  This  scheme
                     allows  for  the possibility of a "rapid" renumbering.
                     That is,  the internal numbers in the header lines are
                     relative,  not absolute.  Changing the name of the MES
                     file, i.e.  from 00002.MES to 00001.MES, automatically
                     would renumber the messages contained within.

     Except for the files database (FILES.CTL and .IDX) these files will be
     created  as  necessary  by  the  GT  host.  The program SYSOP.EXE will
     perform needed maintenance of these files: for example renumbering the
     messages,  deleting obsolete users,  providing reports  and  listings.
     HOWEVER, do not run SYSOP.EXE prior to establishing these files.

     For  batch  usage,  DELREN.EXE  is  provided  to  delete  and renumber
     messages - the command syntax for DELREN can be obtained by  executing
     the program with any parameters.



























                                   - 33 -



     Running Host Mode
     -----------------
     Once installed,  host mode is fairly self-explanatory,  but here is  a
     quick once over.

     Host mode is started by pressing "ALT -".  GT will automatically enter
     "Half  duplex"  mode.  This  is  so  that  anything  typed on the host
     console will echo so that it can be seen.  Then GT will send the  host
     mode  Modem Init String to the modem and wait for a call.  While GT is
     waiting for a call, there are 4 commands available:  [Esc], which will
     terminate host mode,  carriage return, which allows the Sysop to logon
     to GT's host mode from the local console, [Ctrl-L], which turns on the
     system printer for logging,  and [Ctrl-S] to load a fresh copy of  the
     schedule from disk.  Note that you must have logging enabled in the GT
     configuration,  via  Alt-I,  the  [Ctrl-L]  command merely enables the
     printer,  so that whatever is logged will also appear  on  the  system
     printer.  There  also  is  a  command  line  option to turn on the log
     printer.  If you place "/p" on the GT command line,  the  printing  of
     the  log  will  automatically  be turned on from the very start of the
     program.

     Once GT has answered an incoming  call,  there  are  several  commands
     available to the operator, as follows:

     +--------------------------------------------------------------------+
     |                                                                    |
     |                          SYSOP COMMANDS                            |
     |                                                                    |
     |      Alt-H      List available sysop commands.                     |
     |                                                                    |
     |      Ctrl-D     List current schedule on the screen.               |
     |      Ctrl-L     Toggle log printer on/off.                         |
     |      Ctrl-N     Raise caller's access level while on-line.         |
     |      Ctrl-P     Sysop initiated chat mode.                         |
     |      Ctrl-R     Reset time limit, gives caller more time.          |
     |      Ctrl-S     Load new schedule from disk.                       |
     |      Ctrl-T     Terminate after current caller disconnects.        |
     |      Ctrl-X     Abort the caller.                                  |
     |      Ctrl-Z     Terminate chat mode.                               |
     |      Alt -_     Decrement the time available to caller.            |
     |      Alt =+     Increment the time available to caller.            |
     |                                                                    |
     +--------------------------------------------------------------------+


     Command Line Usage
     ------------------
     When  you  start GT,  there are several command line switches that are
     available to you:


     name      You may indicate a script file to be executed upon  start-up
               of GT.



                                   - 34 -



     /D        You may indicate whether or not you wish to have GT drop the
               DTR signal to the modem when GT exits back to DOS.

     /C        You  may indicate whether you are connected via cable to the
               host computer.

     /F        This gives GT a "frontend" type interface.  If you run a
               "frontend" program like Binkley, you can use this command line option
               with GT.  The /F takes two sub-params, like this:

                   /F:nnnnn:m

               Where:

                   nnnnn ...... The DCE baud rate.
                   m .......... The COM port number.

               For example:

                   /F:2400:1

                   2400 baud on COM port #1.

               When  the caller logs off the system (or drops carrier),  GT
               will execute an exit to DOS with an ERRORLEVEL 254  or  255.
               You   should   insure   that  the  batch  file  traps  these
               ERRORLEVELs and returns control to the  "frontend"  program.
               See documentation that comes with the "frontend" program for
               further details.

     /K        You may initiate the capture mode from the very start of the
               program.

     /M        Suppress the "Check for personal mail?" function.

     /MN       This would allow the "Check for personal mail?" function to
               continue, *but* would change the default prompt from [Y/n]
               to [y/N].

     /P        You may enable logging to the system printer.

     /S        This option will allow the Sysop Page to be heard during
               quiet mode.  Normally, nothing would be heard during quiet
               mode.

     /Tn       This option will override the normal keyboard timeout value
               of 10 minutes.  When this timeout occurs, GT will disconnect
               the caller.  For example:

                   /T5     Lower the timeout to 5 minutes.
                   /T45    Raise the timeout to 45 minutes (my favorite).

     /1        You may configure the port addresses in use by  your  serial
               port.  The  actual  port  number to be configured,  1-4,  is


                                   - 35 -



               placed  after  the  slash.  The  new  base  address  of  the
               indicated  port  is  placed  after  the slash number with an
               intervening blank.  The address must be given with a leading
               $ sign and be in hex notation,  for example $3F1 would be  a
               valid address.  Refer to your hardware documentation for the
               correct  address  to use.  GT uses standard addresses if you
               do not override with this option.

               GT  allows  you  to also configure the IRQ used.  To specify
               the IRQ,  simply follow the port address with a ':n',  where
               the  'n'  is the new IRQ to be used.  The IRQ must be in the
               range '0' to '7'.  Be sure that the IRQ is not being used by
               any other device!

     /Rn       This option applies to the GT host mode.  It  specifies  the
               ring  number  upon which GT will answer incoming calls.  For
               example /R3 would cause GT to answer on the 3rd ring.  NOTE:
               that the host mode modem init string must  contain  S0=0  to
               allow this to work properly.

     /RBmm:nn  This  option applies to the GT host mode.  It specifies that
               GT should answer the modem after a "ring  back".  To  enable
               this to work properly,  the host mode modem init string must
               contain S0=0.  Once installed properly this option makes the
               GT host mode answer the phone on the 2nd or 3rd ring after a
               gap of between 'mm' and 'nn' seconds.  If  the  gap  between
               rings  is  less  than  'mm'  seconds  or  greater  than 'nn'
               seconds,  GT will not answer the phone.  This allows the use
               of  an  answering  machine  on  the  same  phone line as the
               computer.  The answering machine  should  be  programmed  to
               answer on a later ring, the 4th for example.  The 'mm:nn' is
               optional, and will default to a 9 to 32 second gap.

     /V:s      This option will cause selected funstions to overlay GT when
               they are executed.  The 's' parameter represents the list of
               functions that are to be  overlaid.  For  example,  's'  may
               contains  the following letters,  representing the functions
               shown:
                         E .... External protocols.
                         D .... Door batch files.
                         L .... Logon/Logoff batch files.

               If GT is overlaid  by  a  function,  then  when  the  caller
               disconnects,  GT  will  exit  to DOS with an 'errorlevel' of
               255.  So,  the HOST.BAT file must be built to trap  the  255
               'errorlevel':

                      HOST.BAT File
                      -------------
                         GT1600 /V:DL host.scr
                         IF errorlevel 255 HOST

                      HOST.SCR File
                      -------------


                                   - 36 -



                         host

     +------------------------------------------------------------------+
     |                                                                  |
     |   This listing of command line switches came from the main GT    |
     |   documentation file.  Please refer to that document for sample  |
     |   usage of these switches.                                       |
     |                                                                  |
     +------------------------------------------------------------------+

     Using a LAN with GT
     -------------------
     Running  a  multi-node  BBS  with  GT is easy.  GT will allow up to 32
     nodes on a network to share common message bases and file  areas.  The
     first thing you must do is decide on a structure for your network BBS.
     One  of  the systems must be identified as the 'server' and it will be
     referred to as "PID Zero" in the following description  (however,  you
     can  easily  have  multiple  servers).  The  LAN  Path must point to a
     location on the server where all the caller records  are  stored,  and
     where  the "PID_FILE.BBS" is maintained.  Once you have decided on the
     structure of the network, you must install GT on each node --- part of
     the installation process for GT on a  LAN  node  is  setting  the  LAN
     parameters under the Alt-I configuration.  Three pieces of information
     must be provided for each node:


         PID Number ... Must be a unique number between 0 and 31.

         PID Name ..... The name by which this node is known to the network
                        software.

         LAN Path ..... This  must  be  the  home  directory  for GT on the
                        network server.  The  LAN  Path  will  contain  the
                        USER.CTL, USER.IDX and PID_FILE.BBS (at the least).
                        These  are  created  automatically.  It  is assumed
                        that these files will be  shared  among  the  other
                        systems on the LAN.


     The  LAN  Path must be specified to get file and message sharing fully
     enabled.  Without a LAN  Path,  GT  will  assume  that  a  non-sharing
     environment is established (like a regular single node BBS).

     File sharing is implemented using the record locking facilities of DOS
     3.1+ SHARE.EXE.  It is recommended that you give this program adequate
     facilities  to do its job.  This command line seems to work well,  but
     more resources may need to be allocated on busy systems:

                               SHARE /F:7168 /L:70

     It should also be  noted,  that  some  LANs  require  your  CONFIG.SYS
     parameters  to  be changed.  For example FCBS may need to be specified
     on LAN servers, for example:



                                   - 37 -



                                   FCBS=24,12

     And  STACKS  are  very  important  under a LAN enviroment.  If you are
     using DOS 3.2,  I would recommend switching to DOS 3.3.  With DOS 3.3,
     I would recommend:

                                  STACKS=62,512

     DOS 3.2 has some bugs that do not make it a good choice for the DOS on
     the  LAN  server.  It has also been observed that BUFFERS are critical
     on a LAN.  Setting BUFFERS above 40 is a sure formula for a  crash.  I
     recommend:

                                   BUFFERS=35

     If this response of the server becomes to slow, due to the low setting
     of BUFFERS,  rather than raising the BUFFERS, I would suggest that you
     obtain a LAN compatible disk cache program.  Ask your LAN manufacturer
     to recommend one to you.

     Finally,  resist the temptation to overload the directory indicated as
     the  "LAN  Path".  For example,  do not have the workstations use that
     directory for  the  log  files.  This  would  result  in  chaos.  Each
     workstation must have its own GTPATH and LOG Path.

     Often  times  it is extremely handy to have a common pathname to reach
     directories on the network.  For this reason, the DOS SUBST command is
     very useful.  With it, you can assign a common pathname to shared disk
     space on servers.  For example:

                                   SUBST e: c:\

     Would allow the server to use drive E:  to make reference to 'c:\', as
     the workstations probably do.  Thus E:  becomes a common path to drive
     C: across the whole network.

     The CB Simulator is an online conferencing feature  that  is  intended
     for  use  on  multi-node  LAN  based  BBS systems (NetBIOS emulator is
     required).  The CB Simulator checks for the presence of NetBIOS before
     allowing callers to get stuck in the CB mode.

     Locally, when the host mode enters the CB Simulator, split screen mode
     is automatically invoked.  You should advise the  caller  to  manually
     invoke split screen mode on their terminals -- otherwise they will not
     see  what they type (remember,  split screen is half-duplex,  the host
     mode will  not  echo  the  caller's  keystrokes  during  CB  Simulator
     operations).

     When using the CB Simulator,  please make sure that you have allocated
     adequate  NCBs.  I  have  setup  the  following command for my NetBIOS
     startup:

                   lanbios irq=5 address=2 ncbs=35 sessions=15



                                   - 38 -



     I am not sure if 35 NCBs are enough,  but it seems to work fairly well
     on  a 3 node LAN.  On the server,  if it is not dedicated,  you should
     insure that the server can manage sufficient simultaneous tasks  -  my
     server  was set for 2 simultaneous tasks,  but I now have it setup for
     5.  This does consume memory,  to be sure,  each extra  task  requires
     considerable buffer space,  but it is required for the CB Simulator to
     work alongside the other network tasks.  On my server, I have found it
     necessary to overlay *all* external processes, due to the lack of free
     memory above GT.

     The following files must be created by the sysop, if the CB Simulator,
     command 'Z' from the main menu, is going to be used:

         CBWELCOM.BBS ...... Welcomes callers to the CB Simulator.
         CBHELP.BBS ........ Displayed in response to '@help' by the
                                caller.
         CBPAGE.BBS ........ Displayed to a caller who receives an '@page'
                                from another caller.
         CBGREET.BBS ....... Displayed for the caller after entering his
                                handle.  The file should be short and to
                                the point, i.e. introduce the automatic
                                '@who" list and tell the caller how to get
                                help.

     The following commands are available to callers in the CB Simulator:

         @help ........ Display the CBHELP.BBS file.
         @ignore ...... Ignore further pages from other callers.
         @page ........ Invite another caller, by handle, into CB mode.
                           Ex: @page foxy
                        Where 'foxy' is the handle of the caller you are
                        paging.  The handle is obtained from the '@who'
                        list.
         @quit ........ Quit from CB Simulator to the main BBS menu.
         @tune ........ Tune the CB Simulator to channels 1 through 98.
                           Ex: @tune 5
         @who ......... Find out who else in on the system and which
                        channel, if any, they are tuned to.
         @sys ......... For sysops only.  Allows broadcast messages or
                        messages directed to specific pids.
                           Ex: @sys 5 Hello Mike!
                           Ex: @sys The system is going down in 5 minutes!
                        The first example sends a message to pid  5,  where
                        Mike  is  logged  on.  The  second  example sends a
                        broadcast message,  to all pids,  telling them that
                        the system is about to go down.  Please note,  that
                        these pids do not have to be in the CB Simulator to
                        get the  message.  These  messages  will  interrupt
                        most things, except file transfers.

     NOTE: A pid corresponds to a "position" or "workstation" on the LAN.

     The  CB  Simulator  uses  the  NetBIOS  Datagram  feature  to pass the
     messages between pids on the LAN.  The Datagrams are sent to the group


                                   - 39 -



     name 'GT_POWER_CB_SIM" (the 16th byte  is  0x00).  GT  registers  this
     group  name  whenever  the host mode is started under NetBIOS in a LAN
     environment.  The Datagrams used by GT  are  of  a  fixed  format,  as
     follows  (for  those  of  you  that  want to try their hand at NetBIOS
     programming):

     Byte Offset        Description
     -----------        -----------
          0             'S' for special messages, such as '@sys'.
                        'C' for normal CB Simulator messages.
         1-2            The channel number the message is addressed to.
                        Channels 1-98 are the normal CB channels.  Channel
                        99 is used for broadcast messages.
         3-4            The originating pid number.  This is used to keep a
                        pid from processing messages that he originates.
                        Datagrams are received by *all* LAN stations having
                        registered the group name 'GT_POWER_CB_SIM'.
         5-6            Transaction code:
                            '00' - Normal message.  All 'C' type datagrams.
                            '01' - Who inquiry.     'S' type datagram.
                            '02' - Who reply.        "    "      "
                            '03' - Page inquiry.     "    "      "
                        The   transaction  codes  '01'  and  '02'  are  now
                        obsolete,  since the @who command uses the PID_FILE
                        to  get  its information.  Transaction code numbers
                        up to '50' are reserved for  future  expansion.  It
                        is  anticipated  that  '04' will be used for remote
                        submission of DOS commands,  and '05' will be  used
                        to remotely shutdown all pids.
          7             Unused.  Reserved.
          8             ','.  Constant.
         9-16           The sender's handle.  If no handle, then the first
                        name of the sender.
          17            ','.  Constant.
        18-127          Text.  In a page transaction, this is the handle of
                        the caller  being  paged.  In  other  transactions,
                        this may be blank or contain a regular message.  It
                        is  variable  length,   only  the  amount  of  data
                        required is transmitted,  up to the maximum of  128
                        bytes.
















                                   - 40 -



     Host Mode LOG
     -------------
     A  few sections above,  I suggested that logging be TRUE,  while GT is
     running in Host Mode.  Here is why:  during Host Mode  operations,  GT
     will log all of the calls received,  who called and the password used.
     A record will also be kept of who tranfered each  file,  how  long  it
     took  and the efficiency of the transfer.  I consider the gathering of
     this information to be critical to the operation of a GT Host.

     The Shell to DOS
     ----------------
     The DOS Shell allows remote callers to operate your computer remotely.
     When the "Shell to DOS" option of the main menu is selected,  GT  will
     shell  to  the  file GTDOOR.BAT.  This file will set up for the remote
     shell by executing the proper CTTY command,  then execute a  secondary
     DOS shell and let the user into the system.  He will have the console,
     so  be  cautious!  The  caller  will be instructed to issue the "EXIT"
     command to return to GT.

     While the DOS Shell is active and the caller is out in the system,  GT
     will  not  be  idle.  GT will act as a watchdog.  If the caller should
     hang up while the DOS shell is active, GT will force the system to re-
     boot and will drop the DTR signal to the modem.  If commands to  start
     GT  are  placed in the AUTOEXEC.BAT file and a script is used to start
     Host Mode,  then GT will automatically recycle.  The script command to
     start Host Mode is simply HOST.

     In order to get the DOS Shell to work,  the DOOR.EXE or TDOOR.EXE file
     must  be  available  in the GTPATH directory (and the GTPATH directory
     should probably be in the  DOS  PATH  statement  in  the  AUTOEXEC.BAT
     file).  DOOR.EXE  is used with the "Rapid" version of GT and TDOOR.EXE
     is used with the standard or "XT" version of GT.

     NOTE:  For  this process to work correctly,  the COMMAND.COM file must
            reside in a  directory  pointed  to  by  the  PATH  environment
            variable.  In order for this to work on a normal drive C:  hard
            disk, "C:\" should be added to the PATH variable.  For example:

                      PATH=c:\dos;c:\lotus;c:\gt;c:\

            This will ensure that the COMMAND.COM file can be  located  for
            execution by the GTDOOR.BAT runstream.

            A  problem  with the DOS Shell has been reported when using DOS
            2.xx.  This is caused by  the  fact  that  DOS  2.xx  does  not
            support  full  pathnames  when  requesting  the  execution of a
            program.  To work around this problem,  if you have  DOS  2.xx,
            you  should  place  the GTDOOR.BAT file in some other directory
            besides the GT home directory.  If GT finds GTDOOR.BAT  in  his
            home  directory,  then GT will issue an EXEC function with full
            pathname,  otherwise GT will not specify any pathname and  will
            rely  on  the DOS PATH command.  The directory where GTDOOR.BAT
            is stored must be pointed to by the DOS PATH  command  in  this
            case.


                                   - 41 -



     Using the Shell to DOS
     ----------------------
     What  can  one do,  once one is running DOS remote via a CTTY command?
     Well,  one can't use any of the Fn keys or the other special  keys  on
     the  IBM  key-board!  One  can't  run  any  program  that  does direct
     hardware control of the screen or keyboard.  All screen  and  keyboard
     input must be done through DOS.  Well,  then what can one do?  One can
     run any  DOS  command;  for  example  COPY,  ERASE,  DIR  and  others,
     including  EDLIN,  all work properly.  In fact,  any program that uses
     the standard DOS handles for input and  output  to  the  console  will
     work.  But  one  still  won't have F1 - F10 or the other special keys.
     Well, that's not quite so...if the Host Mode computer is setup so that
     the ANSI.SYS device driver is loaded via  the  CONFIG.SYS  file.  Just
     put a line like this one into the CONFIG.SYS file:

                               DEVICE=ANSI.SYS

     Naturally,  ANSI.SYS must be located in the root directory of the boot
     disk.  After that has been done,  re-boot the computer.  ANSI.SYS will
     then  be  loaded.  One can now re-map the keyboard so that the special
     keys are mapped to Ctrl keys instead.  This will enable programs to be
     run that use these keys; for example EDLIN uses the arrow keys as well
     as several function keys.

     How does one re-map keys with ANSI.SYS?  The following  sequence  must
     be issued for each key that needs to be re-mapped:

                            ESC [ ##;##;##;...p

     The  (...)  indicate that the sequence may be repeated as needed,  but
     each sequence only re-maps one  key.  Once  a  file  containing  these
     mapping  commands  has  been created,  they can be sent to ANSI.SYS by
     TYPEing the file.  The "##" in the sequence above indicate  the  ASCII
     codes  for  the  keys to be mapped.  For example,  let's map F3 to the
     Ctrl-D key.  The ASCII codes for F3 are 0,61 and the  ASCII  code  for
     Ctrl-D  is  4.  (Note:  the special keys have two codes - the first is
     always 0.  These  codes  are  really  called  extended  ASCII  codes.)
     Therefore,  the  proper  ANSI.SYS command to re-map F3 to Ctrl-D would
     be:

                            ESC [ 4;0;61p

     Note:  Blanks are included for  readability  only,  the  "p"  must  be
            lowercase,  and the symbol ESC stands for the escape character,
            CHR$(27).











                                   - 42 -



     Usage of Color
     --------------
     The GT Host mode now includes color built-in to  the  various  prompts
     and  menus.  These  colors  can be configured.  The colors used are of
     two different sets.  The first set is composed of the colors  for  the
     "Window foreground and background", and the "Phone directory high lite
     foreground  and  background".  These  colors should be subdued,  since
     they are used for normal informational type  displays.  For  important
     command  line  and  menu  displays,  the  program  will use the colors
     designated for "Option high lite" and "Option low lite".

     The user  can  customize  the  sysop  prompt  with  these  colors,  by
     including  the  color  codes  in the SYSOP.BBS file.  Here is the code
     scheme:

          %  ...... Used to kill the meaning of the next character.
          %% ...... Used to display the % character.
          $  ...... Shift   the   pallette  to  the  "Window  foreground  /
                    background" set.
          &  ...... Shift the pallette to the "Option  high/low  lite"  set
                    (the default).
          [] ...... High lites whatever is between the [ and ].
          ~  ...... Kills the color.  Goes back to standard B&W image.

     For example:

          $ [SYSOP] John~ here.

     This  would  shift pallette to the "Window foreground/background" set,
     high lite the word "SYSOP" and kill the color after the name "John".

     Actually,  this scheme was only intended to add color to the SYSOP.BBS
     file  and  other  built-in  menus  and prompts,  but some have already
     discovered that these colors  can  be  added  to  the  GTMDIR.BBS  and
     GTDIR.BBS files, to add color and emphasis.


     Logon DOOR
     ----------
     In the GT POWER home directory,  it is possible to create a DOOR file,
     with a special name,  that will be executed whenever a user logs  onto
     your system.  The file is named 'GTLOGON.BAT' and it is constructed in
     the  same  manner  as  a  normal  DOOR  batch file (shown above).  For
     example:

             GTLOGON.BAT
             -----------
                 %1 com%2
                    .
                    .    { Logon door executes here }
                 %1 con

     The sequence of events goes like this after a user calls your system:



                                   - 43 -



          1.  The GTWELCOM.BBS is displayed.
          2.  Then any BULLETx.BBS is displayed.
          3.  Then the GTBMENU.BBS is displayed.
          4.  Then the GTLOGON.BAT is executed, if available.

     It  is  possible  to have a special logon door for new callers.  It is
     named 'GTNLOGON.BAT'.  It will execute just prior to the regular logon
     door.  If you have logon/logoff doors overlaid,  then you  must  chain
     from  the  new caller logon door to the regular logon door.  Remember,
     this is only required if you use the command line  options  /V:L.  For
     example:

             GTNLOGON.BAT
             ------------
                 %1 com%2
                    .
                    .             { New user logon door executes here }
                    .
                 %1 con
                 GTLOGON          { Chain to regular logon, if overlaying }


     Logoff Batch File
     -----------------
     It is, also, possible to have a logoff batch file, 'GTLOGOFF.BAT',  in
     the  GT  home directory.  This is not a DOOR,  but simply a batch file
     that GT POWER will run,  if it  is  available,  whenever  a  user  has
     disconnected  from your system.  It may contain any normal DOS command
     or other processing as required, if enough memory is available.

     GT  remains  in  memory while this batch file executes in a normal DOS
     Shell.  It can be useful for sysops that want to backup their files if
     they are using a RAM disk for things like the log file.

     Please note, this is not a DOOR, that CTTY is not redirected, and that
     the 'watchdog' is not enabled during the execution of this batch file.

     In addition,  when you have a new caller to your system,  GT will run,
     if  available,  a  batch  file  called  'GTNLOGOF.BAT'.  If  you  have
     requested overlaid logon/logoff doors,  then you  must  chain  to  the
     logoff door (if you have one).  Remember, this is only required if you
     use the command line option /V:L.  For example:

             GTNLOGOF.BAT
             ------------
                    .            { No DOS redirection in logoff doors }
                    .
                    .            { New user logoff door executes here }
                    .
                 GTLOGOFF        { Chain to regular logoff, if overlaying }






                                   - 44 -



     APPENDIX
     --------
     Here is a handy list of extended ASCII codes:

               Key       Codes                 Key            Codes
               ---       -----                 ---            -----
               F1        0,59                  Right Arrow    0,77
               F2        0,60                  Left Arrow     0,75
               F3        0,61                  Up Arrow       0,72
               F4        0,62                  Down Arrow     0,80
               F5        0,63                  Home           0,71
               F6        0,64                  End            0,79
               F7        0,65                  PgUp           0,73
               F8        0,66                  PgDn           0,81
               F9        0,67                  Ins            0,82
               F10       0,68                  Del            0,83



     Here are some sample ANSI sequences!

                    Escape Codes         Meaning to ANSI.SYS
                    ------------         -------------------
                    ^[[4;0;61p           F3          -> Ctrl-D
                    ^[[5;0;62p           F4          -> Ctrl-E
                    ^[[19;0;77p          Right Arrow -> Ctrl-S
                    ^[[1;0;75p           Left Arrow  -> Ctrl-A

     With these kinds of mappings,  almost any program should  be  able  to
     run,  if  it uses the DOS handles for standard input and output.  This
     should make the "Shell to DOS" quite useful.

























                                   - 45 -



     Setup for Power-Loss Protected Operation
     ----------------------------------------
     It is quite easy to prepare a set of files  that  will  allow  you  to
     bring  GT  POWER  up  into  what  I  should  like to call a Power-Loss
     Protected Host Mode of operation.  First, however, a few concepts:

     Whenever power  is  first  applied  to  your  system,  (or  re-applied
     following  a blackout),  the system will boot your DOS into memory and
     that, in turn,  will look for two files;  CONFIG.SYS and AUTOEXEC.BAT.
     Finding the CONFIG.SYS, the DOS will tailor your environment according
     to  its  contents  (such  as setting a new maximum number of files and
     file buffers).  Finding the AUTOEXEC.BAT file will cause the system to
     immediately execute the set of DOS instructions found therein.

     GT POWER may be caused to  run  in  an  unattended  Host  mode  either
     through  GT commands entered at the keyboard (Alt-dash) or via script.
     The GT command to do so in a GT script is simply: HOST.

     The user should have a TSR called DOORMAN  loaded  if  the  'watchdog'
     function  is  required  during  a remote shell to DOS or a remote door
     activation.  DOORMAN will reboot the computer  in  the  event  that  a
     caller drops carrier while is the shell or door.

     Given  the  above,  to set up the system for Power-Loss_Protected Host
     mode operation of GT POWER you must construct the following files:

          Your normal AUTOEXEC.BAT
          A copy of the normal AUTOEXEC.BAT called AUTOEXEC.OLD
          A new file called AUTOEXEC.GT
          A new file called HOST.BAT
          A GT script file called HOST.SCR

     The first four of these files belong in your root directory while  the
     script  file  should  be  placed  in  the  same  directory as GT POWER
     resides.  When you want to enter the Power-Loss-Protected Host mode of
     GT POWER you need only type the single word HOST from  any  directory.
     The  result will be the invoking of the HOST.BAT file which,  in turn,
     copies the AUTOEXEC.GT file on top of  your  normal  AUTOEXEC.BAT  (so
     that if a re-boot occurs it will get control),  it then sets a default
     directory so that your  private  directories  are  not  accessible  to
     callers  into the system,  and then it invokes GT POWER specifying the
     name and location of the HOST.SCR script file you  created.  Thus,  GT
     will  be  given  control  and  placed  into  Host  mode.  Upon  normal
     termination,  GT exits to DOS which returns to the unexecuted  portion
     of  the HOST.BAT file and continues by doing a copy of AUTOEXEC.OLD (a
     copy of your original AUTOEXEC.BAT) on top  of  the  current  one  and
     ending.

     In the event of a power failure while in Host mode, or loss of carrier
     while  in  the DOS Shell,  the AUTOEXEC.BAT file that is in place will
     reset to the default (safe) drive and reinvoke the  Host  mode  of  GT
     POWER.




                                   - 46 -



     Sample Files for Power-Loss Protected Operation
     -----------------------------------------------
     Original AUTOEXEC.OLD:

          PATH=C:\DOS;C:\;C:\GT
          set GTPATH=C:\GT

     AUTOEXEC.GT:

          PATH=C:\DOS;C:\;C:\GT
          set GTPATH=C:\GT
          host

     HOST.BAT:

          copy    autoexec.gt autoexec.bat
          cd      \bullet
          gt1600  host.scr
          if      errorlevel 255   host
          cd      \
          copy    autoexec.old autoexec.bat

     HOST.SCR:

          host































                                   - 47 -



     GT POWER under DESQview(tm)
     ---------------------------
     GT POWER runs quite well as  a  task  under  the  DESQview(tm)  multi-
     tasking  system.  There  are  a few things that should be kept in mind
     when doing so, however.

     GT will auto-detect DESQview, and if you have told BIOS Video = FALSE,
     then  GT  will  write  directly to the DESQview screen buffer (greatly
     speeding  the  screen  update  process).  This  may  adversely  affect
     DESQview  aware  programs  run  in  a shell of GT,  since they may not
     properly tell DESQview which portions of the screen to update.  If you
     run into this problem,  tell GT BIOS Video =  TRUE.  This  will  cause
     screen updates to be slower, but the shell programs will work better.

     GT  will  automatically  give  up  unused  time  to DESQview,  so that
     programs running in other windows are not severely impacted  while  GT
     is idle.

     Also, you will need to provide enough memory for GT to run while under
     DESQview(tm).  If you do not have to consider KERMIT  or  ZMODEM  then
     you  can  run  GT  in  a  partition  of  as  small  as  360K  of  RAM.
     Experimentation has shown that in order  to  support  ZMODEM  and  the
     other  protocols  mentioned  above  you will need to set the partition
     size to 460K.

     GT,  as it requires rapid access to the serial port you are using  for
     communications must be the first task loaded in DESQview(tm).  And,  a
     performance option of DESQview(tm) (set by invoking the SETUP program)
     must be set showing the existence of High Speed Communications.  Other
     options that need to be set include the fact that GT is NOT  SWAPPABLE
     to  disk and time slices somewhere between 3 and 6 ticks in length per
     partition.

     Also,  it  would be best to tell DESQview not to virtualize the screen
     output while GT is active.  This will help in making screen output  as
     rapid as possible.

     (tm) DESQview is the trademark of QuarterDeck Office Systems.


                                 - THE END -















                                   - 48 -