PORT FINDER ver. 1.10 by mcTRONic Systems

     PORT  FINDER is a very versatile program.  It  will  display 
your  computer  type and bios date.  It will detect  and  display  
COM1 to COM4 and LPT1 to LPT3 ports that are responding.  You can 
swap  COM or LPT ports addresses instead of swapping cables.   If 
you are using DOS 3.3 and have COM3 and/or COM4, PORT FINDER will 
activate  both  COM3 and/or  COM4.  DOS  will then  recognize the
ports and you will  be able to  use the  DOS  MODE  command.  Any
other programs that operate through DOS should accept COM3 and/or
COM4.  Your serial  port count  will also be  increased.   If you
have a new  IBM PS/2  computer  COM3 and/or  COM4 will already be
activated.  You  can use  PORT FINDER  to reset  both COM and LPT
port addresses in  case you forget   what address  is what.  PORT
FINDER can also be used in a BATCH  file  to  detect   which  COM
ports  are  present.    An  Errorlevel  is  set  for all possible
combinations.  An  example batch file COMMTEST.BAT is included.

     Any  program  that directly addresses the COM or  LPT  ports 
will  not be affected by PORT FINDER.  Any program that uses  DOS 
to  address  the  COM or LPT ports, will work  with  PORT FINDER, 
allowing  you to  swap any  port address you like.  Activation of
COM3 or  COM4 port does require DOS 3.3 and a COM3 or COM4  port.
To  start  PORT FINDER  just enter  PF at  the DOS  prompt.  PORT
FINDER  allows  one or  two parameters  which are  used for  port 
manipulation.  A description of the PORT FINDER options follows.

PF [parm1] [parm2]

parm1:

12 - swap COM ports 1 and 2
13 - swap COM ports 1 and 3
14 - swap COM ports 1 and 4
23 - swap COM ports 2 and 3
24 - swap COM ports 2 and 4
34 - swap COM ports 3 and 4
RL - restore normal LPT port addresses, only parm2 option, RC
RC - restore normal COM port addresses, only parm2 option, RL
L  - indicate LPT ports will be swapped, ports are in parm2

parm2:

12 - swap COM ports 1 and 2, parm1 can not be RC, RL, or L
13 - swap COM ports 1 and 3, parm1 can not be RC, RL, or L
14 - swap COM ports 1 and 4, parm1 can not be RC, RL, or L
23 - swap COM ports 2 and 3, parm1 can not be RC, RL, or L
24 - swap COM ports 2 and 4, parm1 can not be RC, RL, or L
34 - swap COM ports 3 and 4, parm1 can not be RC, RL, or L
RL - restore normal LPT port addresses, only parm1 option, RC
RC - restore normal COM port addresses, only parm1 option, RL
12 - swap LPT ports 1 and 2 if parm1 is L
13 - swap LPT ports 1 and 3 if parm1 is L
23 - swap LPT ports 2 and 3 if parm1 is L












NOTES:

     Parameters  RC, RL, and L can be upper or lower  case.   The 
COM  ports  that are responding do not indicate  where  you  have 
swapped  the  ports too.  The LPT ports that  are  responding  do 
indicate  where the port addresses are before any  swap  commands 
are executed.  Enter all port numbers with low first then high.

     I highly recommend that you not leave any address holes  for 
either the COM or LPT ports.  As an example do not have only COM1 
and COM3 with no COM2.  Do not have a LPT2 and LPT3 with no LPT1.  
If you have one port it should be 1,  two ports should be 1 and 2 
and  so forth.  Swap only ports that you have.  While nothing  is 
wrong with testing out a port address you do not have by swapping 
an  address  you  have to it,  you and  your  system  may  become 
confused.   Use  the RC or RL functions to restore  all  standard 
port  address  locations.   If you have any  problems  with  your 
system after using PORT FINDER then stop using it.

TECHNICAL DATA:

MACHINE         COMx            I/O             INT.        MEM

ALL             COM1            3F8 HEX         IRQ4       40:00
ALL             COM2            2F8 HEX         IRQ3       40:02
PC/XT/AT        COM3            3E8 HEX         IRQ4       40:04
PC/XT/AT        COM4            2E8 HEX         IRQ3       40:06

PS/2            COM3           3220 HEX         IRQ3       40:04
PS/2            COM4           3228 HEX         IRQ3       40:06

SERIAL PORT COUNT IS AT MEM 40:11 BITS 2, 3, AND 4.


        ErrorLevel              COM1  COM2  COM3  COM4

            0                     0     0     0     0
            1                     X     0     0     0
            2                     0     X     0     0
            3                     X     X     0     0
            4                     0     0     X     0
            5                     X     0     X     0
            6                     0     X     X     0
            7                     X     X     X     0
            8                     0     0     0     X
            9                     X     0     0     X
           10                     0     X     0     X
           11                     X     X     0     X
           12                     0     0     X     X
           13                     X     0     X     X
           14                     0     X     X     X
           15                     X     X     X     X

                      (X means COMx is there)


     PORT ADDRESS     MEM

LPT1   3BC HEX       40:08 (may be included on MDA or other card)
LPT2   378 HEX       40:0A (may be addressed as LPT1 on PC,XT,AT)
LPT3   278 HEX       40:0C (may be addrresed as LPT2 on PC,XT,AT)





     LPT port addressing is very confusing.  PORT FINDER uses the 
above  setup  when the RL command is issued.  All  addresses  are 
lower port justified to leave no port address holes.  If you only 
have  LPT2 it will be placed in the LPT1 address location.   This 
is how DOS does it.  If you find the RL option leaves your  ports 
in the wrong place I am sorry.  Let me know of your problem.  Use 
the  port swap option or just reboot your system to get  them  in 
their right position.

DISCLAIMER:

     PORT  FINDER is not guaranteed in any way.  Use at your  own 
risk!   I have made every attempt to get it right but testing  it 
on  every  machine configuration is not possible.   If  you  have 
problems with PORT FINDER then stop using it and let me know.  

     This  program is yours to use and freely copy.  You can  not 
sell  PORT FINDER or change any fee for its use.  A  distribution 
fee of not more than $5.00 can be charged with my consent. 


                                        Thank You,

                                        James D. McDaniel
                                        7426 Corwall Bridge Ln.
                                        Houston, TX  77041-1709
                                        (713) 462-7687


*   If  you  need  a good mail list  program  then  send  for  my 
shareware program MAILALL.  It is the best and cheapest mail list 
program you can buy for a small company or personal use.

MAILALL  will maintain the names of up to 20 address  files  each 
with  4000 addresses on a hard disk or 1500 addresses per  floppy 
disk.   There are nine data fields and you can sort the  file  by 
any  two  that you wish.  MAILALL will print Labels (up  to  four 
across),  Reports,   and Envelopes.  You can edit  or  print  all 
functions  based on address search matches from one to  all  nine 
fields.   MAILALL  can import or export WORDSTAR  mailmerge  data 
files and can export MULTIMATE ADVANTAGE II mailmerge files.   It 
cost  just $27.50 shipped FIRST CLASS MAIL to you.  Send  for  it 
today!

PORT FINDER, COPYRIGHT (C) 1988 by mcTRONic Systems
MAILALL, COPYRIGHT (C) 1987, 1988 by mcTRONic Systems

DOCUMENT DATE:  August 25, 1988