DTR Fix for QuickBasic
                           Jeff Porter
                             1-5-86

As anyone who has tried to write any programs that use  COM1:  or
COM2: with MicroSoft QuickBasic knows, the DTR modem control line
is  dropped everytime a a communication file is opened or closed.
I don't know why MicroSoft drops the DTR line all the time; all I
know  is that it can be a serious problem with programs  such  as
RBBS-PC.   Therefore,  I  present the following patch to fix  the
problem.

This  patch  modifies the serial communication  routines  in  the
BCOM10.LIB  file so that the DTR line will be not be turned off.

Here  is  a  transcript  of  a  patch  session.    More  detailed
instructions follow it.

C>copy bcom10.lib bcom10bk.lib
      1 File(s) copied

C>debug bcom10.lib
-d540 L 10
xxxx:0540  0B D2 75 04 B5 FF EB 34-FA 83 C2 04 32 C0 EE EB   ..u....4....2...
-d830 L 10
xxxx:0830  14 8B FA E8 00 00 83 C2-04 32 C0 EB 00 EE C7 47   .........2.....G
-a54c
xxxx:054C mov al, 1
xxxx:054E
-a839
xxxx:0839 mov al, 1
xxxx:083B
-w
Writing 25C00 bytes
-q


1.   Make a backup copy of the BCOM10.LIB file, just in case.

2.   Run debug and load BCOM10.LIB

     C>debug bcom10.lib

3.   Display  the  following sections of data and see  that  they
     match.   This is to insure that you are patching the correct
     version of the library.

-d540 L 10
xxxx:0540  0B D2 75 04 B5 FF EB 34-FA 83 C2 04 32 C0 EE EB   ..u....4....2...
-d830 L 10
xxxx:0830  14 8B FA E8 00 00 83 C2-04 32 C0 EB 00 EE C7 47   .........2.....G

4.   If  debug shows the same information as listed  above,  then
     you may continue with the patching process.   If not,  go to
     the section Patching other Library Files.

5.   Do the following:

     -a 54c
     xxxx:054C mov al, 1
     xxxx:054E
     -a 839
     xxxx:0839 mov al, 1
     xxxx:083B

6.   Now write the file back to disk and quit debug.   The  patch
     is complete.

     -w
     Writing         bytes
     -q


                  Patching other Library Files

If  you  do  not  have  MicroSoft QuickBasic or  if  you  have  a
different  version than I,  you can probably still  perform  this
patch.   You  will  have to find the correct locations to  patch.
The  addresses  054C  and  0839 were  found  with  the  following
procedure:

1.   Search  for the byte sequence 83 C2 04 32 C0 in the  library
     file.   If you are lucky,  debug will find it in exactly two
     places.

     (for example:)
     -s 100 fff0 83 C2 04 32 C0

2.   Unassemble   the  addresses  you  found.    The  first   two
     instructions will be

          ADD  DX, +04
          XOR  AL, AL

     Within the next few instructions should be

          OUT  DX, AL

3.   If everything has gone correctly so far, just change the

          XOR  AL, AL

     to a

          MOV AL, 1

4.   Perform this change in both places where the

          XOR AL, AL

     instruction was found.


5.   Write the updated file.

------------- Additional Information for QuickBasic Version 2 ---------------

              By Jeff Sumberg - 02/03/87

The above instructions were correct in finding these items in 'other'
versions. In fact the only difference I found was that the patches were
required in only one location rather than two. Additionally I have located
the patch in BRUN20.EXE as well as BCOM20.LIB

MAKE BACKUPS FIRST BEFORE PATCHING!

To Patch BCOM20.LIB

C>Debug Bcom20.Lib
-a D36B
xxxx:D36B Mov AL,1
xxxx:D36D <cr>
-w
Writing xxxxx Bytes
-q

To patch BRUN20.EXE

C>Rename Brun20.exe Brun20.x
C>Debug Brun20.x
-a 6459
xxxx:6459 Mov AL,1
xxxx:645B <cr>
-w
Writing xxxxx Bytes
-q
C>Rename Brun20.x Brun20.exe

These patches were tested by me and appear to work OK. These only work when
compiling to BCOM20.OBJ, BRUN20.OBJ, & EXE. If you use the in-memory
compilation method, DTR will still drop when you close the port or the program
terminates so dont get upset. Apparently the DTR code is somewhere in QB.EXE
also, but I was unable to find it. Besides you wont be using the compiler when
you have this problem, its the finished product that was the trouble.

------------- Additional Information for QuickBasic Version 3.0 -------------

              By Clint Labarthe - 05/17/87  (305) 260-6397

The above instructions were correct in finding these items in version 2.0

MAKE BACKUPS FIRST BEFORE PATCHING!

To Patch BCOM30.LIB

C>Debug Bcom30.Lib
-a DC0B
xxxx:DC0B Mov AL,1
xxxx:DC0D <cr>
-w
Writing xxxxx Bytes
-q

To patch BRUN30.EXE

C>Rename Brun30.exe Brun30.x
C>Debug Brun30.x
-a 6969
xxxx:6969 Mov AL,1
xxxx:696B <cr>
-w
Writing xxxxx Bytes
-q
C>Rename Brun30.x Brun30.exe

These patches were tested by me and appear to work OK. These only work when
compiling to BCOM30.OBJ, BRUN30.OBJ, & EXE. If you use the in-memory
compilation method, DTR will still drop when you close the port or the program
terminates so dont get upset. Apparently the DTR code is somewhere in QB.EXE
also, but I was unable to find it. Besides you wont be using the compiler when
you have this problem, its the finished product that was the trouble.


------------- Additional Information for QuickBasic Version 4.0 -------------

              By Clint Labarthe - 12/23/87  (305) 260-6397

The above instructions were correct in finding these items in version 3.0
The instructions below are different for patching BCOM40.LIB. I found
the BCOM40.LIB info in a file: QBASIC40.PAT. I thank the author for it.

MAKE BACKUPS FIRST BEFORE PATCHING!

To Patch BCOM40.LIB

DEBUG BCOM40.LIB
-D 100 L 5
xxxx:0100

Take the first <3> numbers of 'xxxx' and add 85.  Example:  if you had
something like   114F:0100  then you would add 85 to 114 and get 199.
The new number you come up with will be 'yyy'. Remember this is HEX.

-S yyy0:0 FFFF 83 C2 04 32 C0

DEBUG will now give TWO locations where these bytes are located. Lets
call the first address is   xxxx:yyyy

-U xxxx:yyyy L 6

You should see three lines.  the  'xxxx:yyyy' should be represented by
a 'XOR AL AL'

-A xxxx:yyyy
xxxx:yyyy MOV AL, 1      (assemble MOV AL, 1 at the xxxx:yyyy)
xxxx:yyyy                (hit enter here)

Now repeat the process with the other number.  (starting at the U
command)
After you have done that, be sure to save the file:

-W
Writing xxxx bytes
-Q

To patch BRUN40.EXE

C>Rename Brun40.exe Brun40.x
C>Debug Brun40.x
-a 6D13
xxxx:6D13 Mov AL,1
xxxx:6D15 <cr>
-a 6FDD
xxxx:6FDD Mov AL,1
xxxx:6FDF <cr>
-w
Writing xxxxx Bytes
-q
C>Rename Brun40.x Brun40.exe

Thats it !