------------------------------------------------------------------
      ---/   Telegard Bulletin Board System -- Version 2.5 Standard   \---
     ---(      Copyright 1988,89,90 by Eric Oman, Martin Pollard,      )---
      ---\           and Todd Bolitho - All Rights Reserved           /---
       ------------------------------------------------------------------

                       **>  Changes In Telegard v2.5  <**


                            ________________________

                             ** REQUIRED CHANGES **
                            ________________________

    ---  Telegard's default video mode is now to display all output  through
         BIOS routines, to provide compatibility with systems that are  less
         than 100% IBM compatible.  If your system is a 100% compatible  (or
         a true IBM), go into System Configuration: System Flagged Functions
         and  toggle  option "W" to OFF.  This switches  Telegard's  display
         mode to direct screen writes (the old method, which is MUCH  faster
         on 100% compatibles).


                                 ______________

                                  NEW FEATURES
                                 ______________

    ---  The  Telegard message system has been enhanced to  support  FidoNet
         standard EchoMail and GroupMail conferences.  This was accomplished
         through  enhancements to the Message Base Editor  (BOARDS.DAT)  and
         the message system itself.  Yes, that's right; FidoNet  conferences
         are  accessed through the standard Telegard message  system.   This
         means that you (and your users) don't have to learn a whole new way
         of posting and reading messages in order to become part of FidoNet!
         (As  FidoNet standard messages aren't compatible with  Telegard,  a
         translator   program  is  needed  to  put  FidoNet  messages   into
         Telegard's  message  files,  and vice versa.  TGMAIL  is  one  such
         program, and it will be released very shortly.)

         The enhancements to the Message Base Editor include:

         ---  Option 3, which used to allow modification of the message path
              (unused  in version 2.4), now selects the message  base  type:
              Local, EchoMail, or GroupMail.  When configuring for  EchoMail
              and  GroupMail, the message path is once again  required,  but
              this  time,  it's only used as a holding area  for  converting
              messages.
         ---  Option  9,  which  configured the message base  depth,  is  no
              longer available (the storage area for the message base  depth
              --  which  was  unused, anyway -- is now  used  to  store  the
              message base type).
         ---  Option  C  selects the colors used to display  standard  text,
              quoted text, tear, and origin lines.
         ---  Option  M toggles flags that affect how FidoNet  messages  are
              stored and retrieved.
         ---  Option O defines an origin line for the base.
         ---  Bases  can  now be flagged as "real names only".   This  means
              that  Telegard will store the user's real name in the  FROM/TO
              fields,  even if the system allows handles (which are  frowned



              upon  in most FidoNet conferences).  Note that this option  is
              not restricted to EchoMail and GroupMail bases; it can be used
              for Local bases, as well.
         ---  Bases  can  also  be flagged to remove ANSI  and  8-bit  ASCII
              codes,  as  they  are  not  allowed  on  almost  all   FidoNet
              conferences (to maintain compatibility with non-IBM  systems).
              This  option,  like  "real names only", can  be  used  on  all
              three message base types.

         Other Message Base Editor enhancements are detailed later, as  well
         as  in  the documentation for version 2.5.   A  companion  archive,
         FIDO25.ZIP,  includes  sample configurations and  instructions  for
         getting your Telegard system up and running with FidoNet.

    ---  A  new  System  Configuration  section,  "FidoNet   Configuration",
         defines the default settings used for creating new message bases in
         the Message Base Editor, as well as the FidoNet address assigned to
         your system (zone:net/node.point).  The FidoNet address is shown in
         several places throughout the system, including the "WELCOME TO..."
         message during logon.  (If the net number is set to 0, however, the
         address  is not displayed.  This is because there is no such  thing
         as  net  0 in FidoNet.  New system initialization, and  old  system
         conversion,  sets  the address to 0:0/0.0, as most  Standard  sites
         aren't in FidoNet.)

    ---  Telegard  now  supports  the  use  of  a  FOSSIL  (Fido/Opus/SEAdog
         Standard  Interface Layer) communications driver.  A FOSSIL  driver
         not only provides more compatibility with systems that are not 100%
         IBM  compatible,  but  it provides  stability  and  reliability  to
         communications, particularly with high-speed modems.

         To  use a FOSSIL driver, get one (a good one is  X00.SYS),  install
         it,  and  set option "B" in System  Configuration:  System  Flagged
         Functions  to ON.  From then on, Telegard will communicate  through
         the FOSSIL driver.  (More information is in the 2.5 documentation.)

    ---  Enhancements to the message system:

         >>>  Telegard will automatically add a tear line and an origin line
              to the end of messages posted in EchoMail and GroupMail bases.
              These lines will look something like this:

              --- Telegard v2.5 Standard
               * Origin: Yet Another Fine Telegard System! (1:999/999.0)

              This  feature can be suppressed by disabling the "add  tear  &
              origin  lines"  flag in the Message Base  Editor.   Note  that
              EchoMail  messages  REQUIRE tear/origin lines,  but  they  are
              OPTIONAL for GroupMail messages.
         >>>  When reading EchoMail messages, the date that the message  was
              originally  written is displayed in the message  header  under
              the  name  of the board.  Note that this is done only  if  the
              external  mail  processing  utility  writes  the   information
              properly  to  the *.BRD file.  (The reason that  the  original
              date  isn't used as the message date is because  EchoMail  and
              GroupMail  messages are, more often than not, received out  of
              date-order.   This  would  really  screw  up  NewScanning,  as
              Telegard uses the date as the high-message pointer.)
         >>>  Messages  that have been placed into Telegard's message  bases
              (or  extracted from the bases) by the mail processing  utility



              are  marked as "scanned" so that they are not sent  out  again
              (causing  duplicates to appear in the message  stream).   This
              flag  can  be  toggled on and off via  the  "&"  command  when
              reading messages (available only to users with Co-SysOp access
              or higher).

    ---  Telegard  now provides BIOS display output and CGA  snow  detection
         through System Configuration: System Flagged Functions options  "V"
         and  "W",  respectively.   (BIOS output  is  slower,  but  provides
         compatibility  with systems that aren't 100% IBM compatible;  thus,
         BIOS output is now the default video mode.);

    ---  Enhancements to the overlay file (BBS.OVR):

         >>>  BBS.OVR can now be loaded into expanded memory (EMS).  This is
              accomplished  through  System  Configuration:  System  Flagged
              Functions,  option "X".  If enabled, Telegard will  place  the
              overlay file into EMS for lightning-fast access.  If  disabled
              -- or if the overlay manager could not place the overlay  into
              EMS  -- BBS.OVR is accessed from disk as usual.  (NOTE:   This
              option will *NOT* take effect until the next time you start up
              Telegard.  Thus, if you toggle this option, you must exist the
              BBS and restart it to make the change.)
         >>>  Telegard  now takes advantage of Turbo Pascal v5.5's  enhanced
              overlay functions to speed up overlay access from disk.  Thus,
              those of you who don't have EMS can still gain some additional
              speed.

    ---  MiniTerm  has  been  removed  from the overlay  file.   It  is  now
         available  as  a  separate executable file,  MINITERM.EXE,  in  the
         MTERM25.ZIP  archive.  This was done to gain space in  the  overlay
         file (which is already too damn big!); thus, the added features  in
         version 2.5 actually take up LESS space than the version 2.4 files!
         The "T" option is still available from the WFC menu; however, it is
         now restricted to executing the TERM.BAT file.  Thus, if you create
         TERM.BAT  to call MiniTerm, the system will act almost exactly  the
         same as it did before.

         Note that MiniTerm still operates exactly as it did under Telegard.
         It  uses Telegard's system and modem configuration, and will use  a
         FOSSIL  driver  if  available.   Thus,  MINITERM.EXE  can  ONLY  be
         executed from the main BBS directory, as it requires STATUS.DAT  to
         operate.

    ---  Message  base packing can now be accomplished via the "-P"  command
         line  option.  Thus, to pack the message bases during  an  external
         event,  use  the command "BBS -P", which will pack  the  bases  and
         return  to  DOS.  This is GREAT for FidoNet systems, as  you  don't
         need to screw around with Telegard's and the front-end's events  in
         order to pack the bases.

    ---  Support  for countries other than the United States has been  added
         as  far  as  user information goes  (city/state,  zip  code,  phone
         number,  etc.).   When changing selected information, the  user  is
         asked  where  he/she  is from:  The US, Canada,  or  other  foreign
         country.  If the US or Canada is selected, information is formatted
         accordingly; if not, the information can be entered free-form.

    ---  A new video display mode, AVATAR, is available.  AVATAR stands  for
         "Advanced  Video Attribute Terminal Assembler and  Recreator",  and



         was invented by Wynn Wagner III (the author of Opus).  It  replaces
         ANSI  sequences  with  much  more  efficient  2-  and  3-byte  code
         sequences,  which results in a remarkable increase in video  output
         speed.   Telegard supports the "Basic AVATAR" mode, as  defined  in
         the FidoNet Standards Committee document #25 (FSC-0025.TXT).

         To  support  AVATAR, option 16 of the Cmdkeys OP command  has  been
         enhanced.   Instead of toggling ANSI on and off, it now allows  you
         to select which video mode you want (TTY, ANSI, or AVATAR).   Quite
         a  few  popular communication programs (including Telix  v3.12  and
         Qmodem v4.1b) support AVATAR.  You should modify the description of
         command  "1" in your Personal Data menu to reflect  this  command's
         change of purpose.

         Some communication programs -- most notably, Telix v3.12 -- do  not
         interpret  AVATAR  colors  correctly.  To accommodate this,  a  new
         command -- Cmdkeys OP, option 25 -- is available, which will toggle
         AVATAR color adjustment on and off.  This command may be placed  in
         your Personal Data menu as command "6".

         IMPORTANT  NOTE:  Since AVATAR doesn't support ANSI graphics,  ANSI
         displays don't work properly.  Therefore, when Telegard is told  to
         display a file, *.MSG files are displayed instead of *.ANS files if
         AVATAR is enabled.  However, all is not lost; since *.MSG files can
         have Telegard MCI colors embedded in them, users can still see some
         colors.   Also,  an ANSI to AVATAR translator will be in  the  next
         release, so AVATAR users will be able to view ANSIs!

    ---  The area listing commands (Cmdkeys MA and FA) now offer a choice of
         listing modes.  The question "Display condensed listing?" is asked;
         pressing  "Y"  will  display  the  old-style  two-column  list   of
         message/file  bases.  Pressing "N" will display a detailed,  multi-
         column  list that gives more information about each base  than  the
         old-style list.

         Also, when the message bases are listed using the old-style method,
         Local message bases have the base number displayed via MCI color #5
         (default  of  yellow)  as  usual;  EchoMail  and  GroupMail  bases,
         however, have the base number displayed as MCI color #0 (default of
         white).  This helps differentiate the base types.

    ---  When downloading a file, Telegard will now display the size of  the
         file in bytes, as well as the size in blocks (128-byte and 1K).

    ---  Two new door MCI codes have been introduced:  @D, which returns the
         current file base's download path (i.e. "C:\FILES\TELEGARD\"),  and
         @I,  which returns the current file base's *.DIR filename and  path
         (i.e. "C:\BBS\GFILES\TELEGARD.DIR").


                                  ___________

                                   BUG FIXES
                                  ___________


    ---  New user logon bugs:

         >>>  When new users are asked for their real first and last  names,
              they  could  enter "=" if they were using their real  name  as



              their  user name.  However, THEY NEVER KNEW IT, because  there
              was NO message indicating that this could be done!  A  message
              is now printed that indicates that it can be done.
         >>>  New users could select different user and real names, even  if
              the system does not allow handles.  Fixed.  Now, when the user
              enters  his  user name, it is copied to the real  name  field,
              which  CANNOT be changed by the user (it can only  be  changed
              via the User Editor).

    ---  Door format file bugs:

         >>>  Telegard  was writing the value "999" in the minutes field  of
              the  DORINFO1.DEF file (Cmdkeys DD), NO MATTER NOW  MUCH  TIME
              THE USER HAD LEFT!  Fixed... with one exception:
         >>>  If   the   user  had  over  999  minutes  left,   some   doors
              (particularly  SMLNET,  a FidoNet interface  door)  would  not
              calculate the proper amount of time!  This was usually  caused
              by the doors themselves (an overflow error when the number  of
              seconds  left passes 65535).  In an attempt to alleviate  this
              problem,  Telegard will now write "999" in the  minutes  field
              ONLY  if  the amount of time is greater than or equal  to  999
              minutes.  (As this works out to 16 hours and 39 minutes, users
              should have PLENTY of time.)
         >>>  In  DORINFO1.DEF, the flag that indicated if a user  had  ANSI
              was  being reversed, so that non-ANSI users were getting  ANSI
              displays and vice versa!  Fixed.
         >>>  Hopefully,  any remaining problems with the other door  format
              files  are  solved.  Let us know if there are  still  problems
              with any of these formats.

    ---  Command line option bugs:

         >>>  Command  line  options  were being ignored if  they  were  not
              specified in lower case.  Fixed; options can now be  specified
              using any combination of upper and lower case characters.
         >>>  "-K"  (local I/O only) would not let the SysOp enter  anything
              at  the  keyboard, forcing the SysOp to  reboot  the  machine.
              Fixed.
         >>>  "-Q"  (quit after user hangup) would not hang up the phone  if
              the goodbye commands (Cmdkeys HC, HI, and HM) were used.  This
              affected  at least one program adversely (the D'Bridge  front-
              end  mailer would not initialize, as it requires the modem  to
              be  hung up).  Fixed.  Thanks to Evan Dictor  (Nathan  Brazil)
              for discovering this bug.
         >>>  Another problem with "-Q" was that Telegard would exit with an
              ERRORLEVEL of 0 instead of 255 (or whatever was specified with
              the "-EN" option).  Fixed.

    ---  Message system bugs:

         >>>  At  times, the linefeed displayed before each message (if  the
              clear  screen  flag  is  OFF)  would  be  skipped.   This  was
              noticeable during a NewScan (Cmdkeys MN) and while reading all
              Email messages (Cmdkeys *3).  Fixed.
         >>>  Very   stupid   bug  where,  when  inserting,   deleting,   or
              positioning  message bases, the NewScan information and  high-
              message  pointers would get all screwed up.  This was  a  VERY
              bad one, and it took a while to find.



    ---  Those short little messages that were displayed during logon  ("You
         were  validated on...", "So-and-so read your letter...", etc.),  in
         versions  prior  to the 2.x series, are now  displayed  again.   Be
         warned  that you and/or your users may suddenly receive a flood  of
         these messages, especially if you've been running a 2.x version  of
         Telegard  for quite a while!  (You may wish to delete  SHORTMSG.DAT
         to prevent this; Telegard will not "bomb" if it does not exist.)

    ---  Thanks  to  everyone who brought this to our attention;  even  *WE*
         didn't know this was happening!  (Apparently, the code was  removed
         at some point after version 1.8b, and never got put back in.)

    ---  When the BBS path names are modified in the system configuration, a
         backslash  ("\")  is now automatically appended to the end  of  the
         name  if  one does not exist.  This bug has been in  Telegard  ever
         since its inception, and it is *FINALLY* fixed!

    ---  During the initialization procedure, Telegard will now check to see
         if  the  number  of users recorded in STATUS.DAT,  and  the  ACTUAL
         number of users, match up; if they don't, Telegard fixes it.   This
         should cure the problems on those systems that report 150% or  more
         of their users voting on voting questions! <grin>

    ---  The  voting booth would occasionally crash with a RT 200  (division
         by zero) error.  This would happen only on nights with a full moon,
         on  a prime-numbered day, in months with the letter "J" in  them...
         you get the point.  Fixed.

    ---  When  performing  a batch upload, Telegard would hang up  the  user
         after the transfer was completed, NO MATTER WHAT THE USER SPECIFIED
         AT THE "ABORT/YES/NO/MAYBE" PROMPT!  Fixed.

    ---  When  you enter a long menu command ("//LONGCOMMAND"), you may  now
         hit [Ctrl-X] to backspace the cursor all the way back to "//"  (the
         way  it  USED to be).  This is useful if the SysOp and a  user  are
         chatting  on  the menu input line (we know LOTS of people  that  do
         that!).   If you want to back up even further -- to get rid of  the
         "//" -- just use the backspace key to do so.

    ---  Many,  many  more ANSI bugs have been  fixed...  unfortunately,  we
         can't guarantee that we got ALL of them.  The C version will have a
         newer,  FASTER  ANSI interpreter that will have no  conflicts  with
         windows  or ANYTHING.  But, in the meanwhile, there will more  than
         likely be some more problems.  We will just have to cope... sorry!

    ---  Shelling  to DOS (executing doors, external protocols, etc.)  would
         set  the video colors to some very interesting combinations.   (The
         most  interesting was black-on-black... not too  visible!)   Fixed;
         the colors are now properly reset to the normal grey-on-black.

    ---  The  @V  MCI, which shows all available commands  for  the  current
         menu,  would  include  the LASTMSG  and  GTITLE  special  commands.
         Fixed.  Thanks to Evan Dictor (Nathan Brazil) for finding this bug.



                                  ____________

                                   CONCLUSION
                                  ____________

    If  you  do put up a Telegard system, please let us know.   We  keep  an
    updated list of Telegard boards, and frankly, we are also interested  in
    what people have done with our system.

    Suggestions?  By all means, contact us; we are ALWAYS interested in  new
    ideas!  You may contact us at any of the Telegard systems below.

                           "We want to hear from ya!"

    System Name             Number        Hours   FidoNet    Main SysOp
    ----------------------  ------------  ------  ---------  --------------
    Grosse Pointe Centrale  313-885-1779  24 hrs  1:120/188  Eric Oman
    Warp Speed              313-544-0405   8p-8a  1:120/186  Todd Bolitho
    The I/O Bus           * 313-755-7786  10p-9a  1:120/187  Martin Pollard

               * = Temporary phone number!  It WILL be changing!

               All systems support 1200 baud and 2400 baud only.


                          Thanks for trying Telegard!