/*
 *
 *
 *			XMODEM.EXE
 *			Version 3.1
 *			----------
 *
 *
 * This is a special implementation of the XMODEM protocol transfer. It runs
 * "beneath" Crosstalk, and in invoked via the Crosstalk "RUN" command.
 *
 * CHANGES IN REVERSE ORDER:
 * ------- -- ------- -----
 *
 * 7/10/85 - While preparing v3.0, we broke the CRC routines. They
 *	     have been fixed. ANY v3.0 COPIES THAT ARE FLOATING
 *	     AROUND HAVE BAD CRC CODE! DESTROY THEM!
 *
 *	     Moral: If it ain't broke, don't fix it.
 *
 * 6/29/85 - Added commline I/O error checking. Overrun, Framing, and
 * v 3.0     Parity errors cause bad block. In short, we're no longer
 *	     relying only on checksum or CRC. Don't ask me how you
 *	     can get a Parity Error when you're running 8N1...
 *
 *	     Pulled initial purge of commline chars. While this is
 *	     exceedingly safe, it is a pain in the neck 'cause it
 *	     swallows the first NAK. Things go quicker this way.
 *	     This also gives a greater chance of catching the other
 *	     side's "C" CRC request and thus enabling CRC checking.
 *
 * 6/24/85 - Fixed RS232 support routines (assembler) to stay in
 * v 2.1     IRQ loop until IIR shows no more interrupts pending.
 *	     See rather lengthy explanation below.
 *
 * 3/03/85 - Initial version.
 *
 *
 * HISTORY:
 * --------
 *
 * Crosstalk STILL doesn't work right with XMODEM, especially sending files
 * (Crosstalk's XX command). And neither the send nor the receive (RX)
 * commands recognize the CRC option, which would greatly improve reliability.
 * So this stand-alone version of XMODEM was developed as an add-on Crosstalk
 * command. It uses CRC if the other side can support it, else uses the
 * usual 8-bit checksum.
 *
 *
 * USE:
 * ----
 *
 *    1) While online to the remote system via Crosstalk terminal mode,
 *	 start the other XMODEM transfer, just as you would do in preparation
 *	 for using Crosstalk's RX or XX commands.
 *
 *    2) Get to Crosstalk's COMMAND? prompt (via ESC or whatever key you've
 *	 set up as the ATtention key).
 *
 *    3) Use the Crosstalk RUN command to run this XMODEM to actually do the
 *	 file transfer:
 *
 *		RUn xmodem 1 s foo		(send "foo" using port 1)
 *		RUn xmodem 1 r b:xyz		(receive "b:xyz" using port 1)
 *		RUn xmodem 2 r xmodem.c 	(receive "xmodem.c" using port 2)
 *
 *    4) As the transfer proceeds, you will see status messages on your screen.
 *
 *    5) When the transfer is complete, you will be returned to Crosstalk.
 *
 * Things are made easier if you put the invariant part of the command into
 * a function key within Crosstalk. Mine are set up as follows:
 *
 *	FK 1 "@RUn c:xmodem 1 s "		(F1 = send a file)
 *	FK 2 "@RUn c:xmodem 1 r "		(F2 = receive a file)
 *
 * Then you just have to fill in the filename. From within Crosstalk all I
 * have to do to receive "foo.exe", for instance, is press:
 *
 *	<F2>foo.exe<RETURN>
 *
 * which Crosstalk translates into a DOS command of C:XMODEM 1 R FOO.EXE
 *
 *
 * RECOMMENDATIONS:
 * ---------------
 *
 * When you use the RUN command within Crosstalk, DOS has to load
 * TWO programs - COMMAND.COM and the one that you're RUNning. So
 * I strongly recommend that both COMMAND.COM and XMODEM.EXE reside on
 * ramdisk. Things really move when it's set up like that, and can be
 * rather pokey (thanks to DOS' file-opening code) if not.
 *
 * Maybe someday Crosstalk will have a cleaner interface to external
 * programs than this RUN thing. On my system I have XMODEM, KERMIT,
 * COMPUSERVE and MNP protocols, all implemented via this RUN thing.
 * And each time I drop into one of them, I have to wait the second
 * or so that it takes DOS to load COMMAND.COM and the program itself
 * from my ramdisk. Are you listening, Microstuf???
 *
 *
 * CAVEATS:
 * -------
 *
 * NOTE: Do not - repeat DO NOT - attempt to run this as a stand-alone transfer
 * program (i.e. - outside of Crosstalk). It has some very touchy and difficult
 * code that was specially developed just to allow "re-using" the serial port
 * without actually opening it. This program wants to use the same baud rate and
 * data structure that Crosstalk has already set up. So it doesn't set these.
 * It just (CAREFULLY) massages the 8250 and 8259 so that while this program
 * is running it has full input AND output interrupt-driven access to the port,
 * without disturbing the environment (hardware/software) set up by Crosstalk.
 *
 * If you run this without first having "opened" the serial port (by running
 * Crosstalk etc), then the 8250 will very likely go haywire.
 *
 * Just don't.
 *
 *
 *				- Joan Riff,  3 March 1985
 *
 *
 * 6/24/85 - Version 2.1 Notes:
 * ===========================
 *
 * Bob Baumann found a very subtle but fatal feature of the Hayes
 * 1200b internal modem. Unlike a standard 8250, the one on the
 * 1200b DOES NOT present one and only one IIR value per IRQ. Instead,
 * it presents the next-lower-priority IIR value AT THE VERY INSTANT
 * THAT THE CAUSE OF THE FIRST IS CLEARED BY THE IRQ ROUTINE. And
 * I do mean the very instant (like between instructions). We haven't
 * pulled a 1200b apart to see what's tied to the IIR bits, but it
 * looks like their 8250 is specially hooked to their modem, so
 * that the thing can present up to 4 separate "interrupts" per one
 * PC IRQ.
 *
 * I have heard from 1200b users who reported unspecified "problems"
 * using this program under Crosstalk. No wonder! If the 1200b gets
 * a parity error while receiving characters, for example,
 * then its 8250 will do one IRQ for the LSR, AND THEN IMMEDIATELY
 * PRESENT AN IIR FOR THE RECEIVED CHAR. Until that "received data
 * available" state is cleared, the 8250 stays in the interrupted
 * state.
 *
 * Standard 8250's (i.e. - all that I've seen except for Hayes') will
 * issue a second IRQ for the second condition.
 *
 * There are many IIR combinations that cause a fatal lockup of the
 * 8250 when used the way Hayes is using it. Thus neither XMODEM.EXE
 * nor Crosstalk can get chars in or out of the 8250. Only solution
 * was to exit Crosstalk and restart it (so that it would init the
 * 8250).
 *
 * The RS232 interface code has been changed in release 2.1 to
 * expect more than 1 IIR value per IRQ. This solves the problem.
 * Why fight it? So much for clean, interrupt-driven code. Sigh...
 *
 *
 *				- Joan Riff   6/24/85
 *
 */