Z.DOC:  What we know so far about the DSZ transfer engine
____________________________________________________________________________

  PROGRAM:      DSZ.COM   External Protocol Driver, Borland Turbo-C Version

  PROGRAM:      DSZ.EXE   External Protocol Driver, Microsoft-C LIB Version

  PROGRAM:      GSZ.EXE   External Protocol Driver, graphic display Version
----------------------------------------------------------------------------

       PURPOSE:         High-performance File Transfer Engines

----------------------------------------------------------------------------

   DESCRIPTION:         DSZ is a State-of-the-Art File Transfer Engine
                        that functions as a  DOS Console Terminal  or,
                        as an  External Transfer Protocol Driver  for
                        sending and receiving Files.  GSZ is functionally
                        equivalent to DSZ.EXE with the addition of graphics.
----------------------------------------------------------------------------

      FEATURES:     T   Zmodem Batch-T  DOS Telecommunications Console

                    A   Zmodem Batch-Z  with RLE compression for  ASCII
                    W   Zmodem Batch-W  with sliding window for TELENET
                    R   Zmodem Batch-R  with automatic  Crash  Recovery
                    M   Zmodem Batch with MobyTurbo enhanced throughput
                    Z   Zmodem Batch with 32-bit CRC  error correction
                    B   Ymodem Batch with 16-bit CRC  error correction
                    Y   Xmodem-1k /CRC /CheckSum /-G  error correction
                    X   Xmodem    /CRC /CheckSum /-O  error correction

                    G   Ymodem Batch-G  for hardware  error correction


----------------------------------------------------------------------------

   PERFORMANCE:         Observed Throughput  ( avg ZIP File Size = 100 Kb )


                        CCITT V.22bis 2400 Bps STD Modem

        233 +/- 5 c.p.s.  ZMODEM-m transfer ZIP Files,  CONNECT 2400

        230 +/- 5 c.p.s.  ZMODEM-Z transfer ZIP Files,  CONNECT 2400

        213 +/- 5 c.p.s.  ZMODEM-Z transfer ZIP Files through Telenet 2400

        108 +/- 5 c.p.s.  ZMODEM-Z transfer ZIP Files through Telenet 1200

               CCITT V.22bis 2400 Bps "MNP" OR V.42/V.42 bis Modem

        280 +/- 5 c.p.s.  YMODEM-G transfer ZIP Files,  CONNECT 2400 MNP
        275 +/- 5 c.p.s.  ZMODEM-m transfer ZIP Files,  CONNECT 2400 MNP

        223 +/- 5 c.p.s.  YMODEM-G transfer ZIP Files through Telenet 2400 MNP

        113 +/- 5 c.p.s.  YMODEM-G transfer ZIP Files through Telenet 1200 MNP

       throughput values will be about 2% less for V.42/V.42 bis transfers




              CCITT V.32/HST 9600 Bps "MNP" OR V.42/V.42 bis Modem

       1140 +/- 15 c.p.s.  YMODEM-G transfer ZIP Files,  CONNECT 9600 MNP

       1130 +/- 15 c.p.s.  ZMODEM-m transfer ZIP Files,  CONNECT 9600 MNP

       1050 +/- 15 c.p.s.  ZMODEM-Z transfer ZIP Files,  CONNECT 9600 MNP

    throughput values will average 2% less for V.42/V.42 bis transfers



           CCITT V.32 bis/HST 14400 Bps "MNP" OR V.42/V.42 bis Modem

       1728 +/- 20 cps  YMODEM-G transfer ZIP Files,  CONNECT 14400 MNP

       1690 +/- 20 cps  ZMODEM-m transfer ZIP Files,  CONNECT 14400 MNP

       1650 +/- 20 cps  ZMODEM-Z transfer ZIP Files,  CONNECT 14400 MNP

      throughput values will average 2% less for V.42/V.42 bis transfers
______________________________________________________________________________

                CHARACTERISTICS


      DSZ.COM :         Compiled with Borland Turbo-C run-time Library.

                        the COM Driver uses less memory than EXE Driver

                        the COM Driver executes when both are on d:\path


      DSZ.EXE :         Cross-compiled using the Microsoft "C" Library.

                        the EXE Driver does not support  MS-DOS "SHARE"

                        the EXE Driver uses table-driven look up of CRCs

                        the EXE Driver uses different run-time routines

                        use the EXE driver @9600 and up with slow CPU's

_______________________________________________________________________________ 

        AUTHOR:         Charles A. "Chuck" Forsberg
                        Omen Technology, Inc.

       ADDRESS:         17505-V Northwest Sauvie Island Road
                        Portland, Oregon  USA  97231

  REGISTRATION:         Enables advanced features of DSZ, and provides
                        the author with funding for new development.

                        For VISA/MC Registrations, call (503) 621-3406
                        ($5.00 fee charged for credit card registration)

   US & CANADA:         Mail $20.00 to  Omen Technology Inc
                                        P.O. Box 4681
                                        Portland, Oregon USA 97208-4681
                        Price includes 5-1/4" disk. Add $5.00 for 3-1/2" disk.

                        Also add $5.00 for shipping & handling unless
                        your full payment accompanies your order.

      OVERSEAS:         Mail $25.00 to  Omen Technology Inc
                                        P.O. Box 4681
                                        Portland, Oregon USA 97208-4681
                        Price includes 5-1/4" disk. Add $5.00 for 3-1/2" disk.

                        Also add $5.00 for shipping & handling unless
                        your full payment accompanies your order. (U.S. funds)

______________________________________________________________________________

                         DSZ  COMMAND  LINE  SYNTAX



        DSZ [parameters] [numeric parameters] command [-options] [File]


        SYNTAX:         The DSZ command line is lengthy, cAsE SeNsItIvE
                        and position dependent. Although the parameters
        and options provide advanced features and enable operation with
        a variety of modems and transmission mediums, all configuration
        of the driver is done from the DOS command line or environment.

        To realize the full potential of DSZ, one should make Batch Files
        to act as receivers and transmitters.  Using numeric parameters
        and command -options, receivers and transmitters are fine tuned.

        NOTE:           Some features are not enabled in unregistered
                        copies of DSZ.

         USAGE:


    DSZ [port n] [speed s] [ha x] [est 0 b] [d/D] [pB8192] command [-options]

                                                                                 

                ENVIRONMENT  VARIABLES  (** = registration required)



 ** SET DIRRX=d:\path                   specifies a directory to receive to

 ** SET DIRRX=d:\path\                  specifies absolute receive directory

    SET DSZFILES=File1 File2 File3      specifies Filename(s) to send batch

 ** SET DSZLOG=d:\path\DSZ.LOG          specifies log File name and location

 ** SET DSZOPT=ty8g                     specifies global command line options

    SET DSZPORT=2                       specifies serial port for operations

    SET MAXBYTES=1024000                specifies maximum bytes per transfer

    SET ZONE=420                        specifies minutes behind GMT for PST


-----------------------------------------------------------------------------
                        COMMAND  LINE  PARAMETERS


        CON             specifies redirection to the DOS console  CON:

                        use this parameter when operating in CTTY mode

                        alternatively, use  >CON  >PRN or >NUL  at the
                        end of a command line to redirect the display.

                        use  >filespec  to  "capture"  console data to
                        a disk File - press ALT-X (after RXD modem LED
                        stops glowing) to end capturing data.

                        the default device is CON:, unless redirected


         NOTE:          The CON parameter must be the first parameter
                        on the command line except when used with
                        PcAnywhere.


        port n          specifies the COMn: serial communications port

                        n = 1,2,3,4  for IBM PC/XT and PC/AT computers

                        n = 10,11,12,13  for IBM PS/2 computer systems

                        alternatively,  SET DSZPORT=n  in AUTOEXEC.BAT

                        the default communications port n = 1 for COM1


        speed s         opens the COMn: serial port with Bps Rate = s

                        s =  300, 1200, 2400, 4800, 9600, 19200, 38400,
                             57600, 115200
 

                        or, use  MODE COMn:,s,N,8,1,-  in AUTOEXEC.BAT

                        the default Bps Rate is initialized by MS-DOS

        ha x            enables hardware and/or software handshaking x

                        ha bo   enables XON/XOFF and RTS/CTS handshake

                        ha on   specifies RTS/CTS hardware handshaking
                        ha slow specifies RTS/CTS, drops RTS when writing
                                to the disk.

                        ha cts  specifies CTS (5) hardware handshaking
                        ha dsr  specifies DSR (6) hardware handshaking
                        ha dcd  specifies DCD (8) hardware handshaking

                        the default handshaking is XON/XOFF for Zmodem
                        and Ymodem Batch or, no handshaking for Xmodem
                        Zmodem MobyTurbo requires  ha on   or  ha cts

        est 0 b         estimates Batch Transfer times for Bps Rate b

                        Use this parameter to achieve better estimates
                        of Batch Transfer times when the port is setup
                        for a fixed speed and the modem Bps is lower.

                        syntax:         est filesize Baudrate

                        the default estimate is based upon the speed s

                        a filesize of 0 causes DSZ to use the actual DOS
                        file size when calculating the transfer time.

         NOTE:          The estimate parameter must follow port, speed,
                        and handshake parameters, when used.


        d               disables checking DCD (8) for a CARRIER - this
                        is useful for operating in terminal mode before a
                        CARRIER is present, and for direct connections.

                        the default check DCD (8) for a CARRIER is ON.

        D               enables  checking DCD (8) for a CARRIER and it
                        will drop DTR (20) if CARRIER is not detected:
                        useful for a BBS or other HOST installation.
                        This is DSZ's default mode when not specified
                        otherwise.


        A               Use with DSZ.EXE and PcAnywhere to suspend
                        PcAnywhere operations during file transfers.
                        The [A] parameter must appear first on the
                        command line.  Start all DSZ transfers on the
                        PcAnywhere Host first.

        F               Use with 16550 UARTS to leave the FIFO buffer
                        enabled after DSZ exits. The [F] parameter
                        must preceed the port statement on the command
                        line. 


        restrict        Since DSZ has the ability to transfer a full
                        path specification, bbs sysops will want to
                        place this command in their DSZ Zmodem/Ymodem
                        receivers to lock out intentionally misdirected
                        files. The [restrict] command restricts incoming
                        pathnames to the current D:\path and prohibits
                        the overwriting of any existing files. It also
                        causes incomplete files to be deleted and blocks
                        transfers having file names of AUTOEXEC.BAT and
                        COMMAND.COM.  The restrict command should be
                        placed immediately preceeding the rz statement
                        on the command line.

        o               Used in "tty" terminal mode to disconnect by
                        dropping DTR before exiting to DOS with the
                        F1 function key.  Requires that your modem be
                        capable of responding to toggling of the DTR pin.
                        ie:  DSZ t o




        pB8192          sets aside 8k of RAM as a Disk Buffer for DSZ
                        Legal values are 1024 through 16384 in DSZ.EXE
                        Use 1024 through 4096 with DSZ.COM.

                        Use this parameter to minimize Disk Read/Write
                        activity for operations at or below 2400 Bps.

                        the default Disk Buffer is 1024 bytes for DSZ

                        Do not use the pB buffer at speeds above 2400 bps
                        except on fast drives and ramdisks.

         NOTE:          Certain device drivers, memory managers, caches and
                        TSR programs can interfere with DSZ operations
                        and may have to be removed if interrupt conflicts
                        surface.


----------------------------------------------------------------------------
                               

                        COMMAND  LINE  NUMERIC  PARAMETERS



                        The Driver is rich with timing adjustments and
                        alternative configuration options.


        p               Use  DSZ d p t  to display numeric parameters

        z p             Use  DSZ d z p t  to display  "zmodem"  params

        p z p           Use  DSZ d p z p t  to display all DSZ numeric
                        parameters and their default values.


         NOTE:          Numeric parameters are specified by p_ values,
                        and "zmodem" numeric parameters by  z p_ .
                        DSZ supports many protocols, "zmodem" being
                        just one of them.

                        Numeric parameters are generally specified at
                        the end of a parameter list, before a command.

                        To get an accurate report of parameters on the
                        command line, use  p  or  z p  last, as in:

       EXAMPLE:         DSZ D pB8192 p z pL1024 pw4096 p sz -k *.*

                        which displays an accurate report of the  pB_
                        numeric parameter and the pL_ and pw_ "zmodem"
                        numeric parameters.




                p_      NUMERIC PARAMETERS



        pB8192          creates an 8 Kilobyte Disk Buffer for DSZ.

                        Use this parameter to minimize Disk Read/Write
                        activity for operations at or below 2400 Bps.

                        the default Disk Buffer is 1 Kilobyte for DSZ
                        use values between 1024 and 16384 (1-16k).


         NOTES:         The pB8192 parameter is applicable to both the
                        .COM and .EXE Driver in circa 1990 and later
                        versions. Previously it was not applicable to
                        the DSZ.EXE driver or recommended above 2400 bps.
                        The pB8192 parameter may be experimented with
                        at >2400 bps speeds when used in conjunction
                        with fast hard disks or a non-conflicting ramdisk.
                        Maximum buffer size in DSZ.COM is 4096 bytes.

                                                                    

        pO0             controls Xmodem "OverThruster" File transfers

                EXAMPLES OF OVERTHRUSTER CONFIGURATION



        pO-512  CompuServe XMODEM-Ovth  DSZ pO-512 ro Filename.ext

                Negative numbers up to a system dependent value less
                than the protocol block size increase throughput.

                Note that the number is negative (-)

                Tune the  pO_  parameter for a specific Host computer.

                Try  pO-512  for  CompuServe  as the standard setting.

                Retry 0:  Received dup Sector - reduce parameter pO_ .



        pO60    XMODEM/-1k/-Ovth        DSZ pO60 rx -o Filename.ext

                Positive numbers up to a system dependent value less
                than the protocol block size increase throughput.

                Tune the  pO_  parameter for a specific Host computer.

                Try  pO60  for 2400 Bps MNP as the standard setting.

                Retry 0:  Received dup Sector - reduce parameter pO_ .


        pO60    YMODEM/-1k/-Ovth        DSZ pO60 rb -o

                Parameter pO_ is useful for tuning a CRC-16 receiver to
                one  particular  Host  and  transmission  medium.


         NOTES:

                The idea behind -Ovth is for the receiver to transmit an
                ACK for Block a few ticks before all 1,024 bytes come in.
                Fiddling with the pO_ parameter, positive/negative values
                show different effects with different modems and mediums.

                "OverThruster" is an  "advance ACK"  configured receiver.
                Varying the  pO_ parameter  eeks out the last few  c.p.s.
                possible for CRC-16 based, Xmodem/-1k and Ymodem-K Batch.
                This is when you get down to configuring a receiver for a
                particular Host... like, she's got to have it.

                Because  -o closes the "artificial window" between sender
                and receiver, errors encountered during transfers will
                cause the transfer to catastrophically abort.

                Whenever hardware error correction is available, the -g
                "Gonzomode" is the fastest way to receive compressed files.

                OverThruster is only available for Xmodem transfers. 





        pS15            timeout in seconds to wait after receiving the
                        XOFF (CTRL-S) character or, after CTS went low.

                        the default wait for handshake is  15  seconds.


         NOTE:          Use CTRL-Break to unlock Receiver Console after
                        receiving an XOFF (CTRL-S).


        pG_             Controls the number of bytes loaded into the
                        16-byte FIFO buffer on 16550 UARTs. DSZ fills
                        all 16 bytes by default.  Reducing this value
                        may help some cheap MNP modems better handle flow
                        control.  Setting this parameter pG0 effectively
                        disables the UART buffer entirely.

         NOTE:          Once data has been handed off to the UART it is
                        sent on to the modem regardless of the status of
                        the CTS pin.  Some poorly designed (read cheap)
                        modems cannot accept a few additional bytes after
                        they exert FLOW control.

        pQ_             Forces a user specified error code to be returned
                        to DOS upon completion of a file transfer. Normally
                        a successful transfer returns an error code of 0.
                        ie:  DSZ pQ-1 sz myfile.zip forces an error code
                        of 1 at the end of the transfer.

        pV_             When set to a value of 1, Forces DSZ.COM and GSZ
                        to use direct video when writing to the screen
                        instead of BIOS calls. Speeds up displays. Typical
                        syntax:  GSZ pV1 rz  Default value is 0, and is not
                        supported in DSZ.EXE

        pW_             Wait for <enter> key to be hit before exiting after
                        an error (registered copies only). DSZ pW1 sz myfile.
                        Default value is 0 (exit immediately).

        pY_             Control byte for the FCR register in 16550 UARTS.
                        Setting pY129 may improve DESQview operation when
                        multiple DSZ sessions are active.  It is suggested
                        that a 16550 UART applications manual be consulted
                        before tinkering with the FCR register.

                                                                      

        pa2000          CPU calibration for Xmodem and Ymodem  8088-05

        pa4000          CPU calibration for Xmodem and Ymodem  8086-08

        pa6000          CPU calibration for Xmodem and Ymodem 80286-08/1

        pa8000          CPU calibration for Xmodem and Ymodem 80286-10/1

        pa10000         CPU calibration for Xmodem and Ymodem 80386-16/1

        pa12000         CPU calibration for Xmodem and Ymodem 80386-20/1


         NOTES:         the default pa_ timing is 2000 for a PC/XT i.d.

                        the default pa_ timing is 6000 for a PC/AT i.d.

        NOTE WELL: -->  it is unlikely that tinkering with these default
                        timings will provide any additional throughput.



        pd1             enables sending  File Date Header information,
                        the default Batch transfer timestamp method.

        pd0             disables sending File Date Header information,
                        and uses current (receiver) date for new Files.
                        DSZ pd0 sz myfile.zip may provide a marginal
                        increase in observed throughput of small files.


        pv0             disables DSZ "trace" mode, the default setting

        pv1             rings console BEL at the end of File transfers

        pv2             enables DSZ "trace" mode, displays Sector info

        pz0             time zone in minutes behind GMT world standard

        pz300           time zone in minutes behind GMT for  EST  Zone

        pz360           time zone in minutes behind GMT for  CST  Zone

        pz420           time zone in minutes behind GMT for  PST  Zone

                        alternatively, SET ZONE=nnn  in  AUTOEXEC.BAT
                        where nnn = minutes behind GMT

                                                                       

              z p_      ZMODEM NUMERIC PARAMETERS

      z pb0             disable sending of BREAK upon transfer error

      z pb1             enable sending of BREAK upon transfer error,
                        useful for clearing some high-speed modems.

      z pB2             duration in tenths of a second of the BREAK
                        signal - default is 200 milliseconds.

      z pC11            number of repetitions of a ZCOMMAND request
                        Unclear if supported in current versions of DSZ.
                        see ZCOMM or PRO-YAM docs for more information.

      z pe0             disables escape of ASCII control characters,
                        the default setting.

      z pe1             enables  escape of ASCII control characters,
                        useful on certain networks.

      z pl0             disables wait for ACK for each Zmodem sector,
                        the default setting (free flowing).

      z pl4096          enables  wait for ACK after every 4096 Bytes,
                        transforms Zmodem to -4K Block, CRC-32 Batch.

      z pL0             enables auto-config of  Zmodem  Sub-Packets (default)

      z pL128           configures Zmodem for  128 Byte Sub-Packets

      z pL256           configures Zmodem for  256 Byte Sub-Packets

      z pL384           configures Zmodem for  384 Byte Sub-Packets

      z pL512           configures Zmodem for  512 Byte Sub-Packets

      z pL1024          configures Zmodem for 1024 Byte Sub-Packets

         NOTES:         Larger Zmodem Sub-Packet sizes give better
                        performance on clear transmission lines.

                        Smaller Zmodem Sub-Packet sizes give better
                        performance on noisy transmission lines.

                        it is convenient to set sub-packet sizes to
                        one-fourth the effective Zmodem "window", as:

                                DSZ z pL256 pw1024 sz [Filespecs]

                                DSZ z pL384 pw1536 sz [Filespecs]

                                DSZ z pL512 pw2048 sz [Filespecs]

                                DSZ z pL1024 pw4096 sz [Filespecs]

      z pn0             defines the number of ASCII NULL characters
                        sent before each  ZDATA  frame - useful for
                        FastLink modems, whatever those are.
                                                                        

      z pp50            timeout in tenths of a second for a receiver
                        to wait for gaps within a packet. Default = 5 sec

      z pP_             a single lower case "p" following the speed
                        parameter will cause DSZ to report the type of
                        serial port UART detected.
                           0 = 8250/16450     1 = 16550     2 = 82510
                        Forcing a value of "1" with z pP1 and placing this
                        ahead of the speed parameter will bypass DSZ's
                        auto UART detect mechanism and may in certain
                        instances permit use of "brain damaged UARTs"

      z pr0             disables removal of incomplete Files received,
                        the default setting.

      z pr1             enables  removal of incomplete Files received,
                        useful for Host systems:  (DSZ z pr1 rz )

      z ps15            timeout in seconds to wait after receiving the
                        XOFF (CTRL-S) character or, after CTS went low.

                        the default wait for handshake is  15  seconds.

         NOTE:          Use CTRL-Break to unlock Receiver Console after
                        receiving an XOFF (CTRL-S).

      z pt100           timeout in tenths of a second for a receiver
                        to wait for a packet or acknowledgement from
                        the sender.  The default is  10  seconds.

      z pT600           timeout in tenths of a second for the sender
                        to wait for a packet or acknowledgement from
                        the receiver.  The default is  60  seconds.

      z pw0             disable "window"  flowing  ACK from receiver,
                        the default setting (free-flowing).

      z pw2048          enable  "window"  2 Kb for Telenet 1200 Bps,
                        requesting the receiver to send an ACK every
                        512 Bytes received.

      z pw4096          enable  "window"  4 Kb for Telenet 2400 Bps,
                        requesting the receiver to send an ACK every
                        1024 Bytes received.

         NOTES:         Larger Zmodem "windows" increase performance
                        but may cause excessive XOFF delays or loss
                        of data inside the network - to minimize the
                        frequency of XOFFs on Telenet, use:

                                SET? 0:33,35:10,41:1,64:4 <cr>

                        at the outdial PAD before transmitting Files.

                        the   z pw_   parameter is applicable to the
                        Zmodem sender, as in:  DSZ z pw4096 sz Files.
                        the  -wN option over-rides "z pw_" parameter.
                                                                        

      z pW1400          defines the number of characters the  Zmodem
                        receiver will eat when looking for the start
                        of a new frame.

         NOTE:          Increase  z pW_  to tune error recovery  for
                        networks with a large "window" of in-transit
                        packets.   "Garbage Count Exceeded"   errors
                        indicate that z pW_ is too low.


      z pZ0             the number of minutes to adjust a File date
                        when using  TELINK  or  CLINK  protocols to
                        transfer a File between time zones.
____________________________________________________________________________

                        TRANSFER  PROTOCOL  CONFIGURATIONS

   COMMANDS        TRANSMITTERS      (** = registration required)

        sz File(s)      Send Zmodem Batch [filespecs] to a Receiver.
                                      or
        sz @D:FILES.LST Send Zmodem Batch [filespecs] specified with
                        the ASCII File "FILES.LST" located on d:\path
                        to a Receiver.  Valid delimiters for Filespecs
                        within "FILES.LST" are a SPACE, TAB, or CR/LF.
                        Mind the use of the "@" character.

                        Alternatively, Files can be specified by using
                        SET DSZFILES=d:\path\FILE1.ZIP FILE2.ZIP (etc)
                        in the AUTOEXEC.BAT File.

 **     sz -S File(s)   Send Zmodem Batch [filespecs] to a Receiver and
                        interrogate the RECEIVING program for its serial
                        number.  The serial number received will then 
                        be saved in the performance log, DSZ.LOG.

        sz -m File(s)   Send Zmodem batch [filespecs] to a Receiver,
                        using MobyTurbo throughput enhancement. Helps
                        achieve nearly the same throughput as Ymodem-G
                        with the added benefit of CRC-32 error checking.
                        RTS/CTS handshaking required (ha on).

 **     sz -Z File(s)   Send Zmodem Batch [filespecs] to a Receiver,
                        using "RLE" compression. This reduces the time
                        required to transmit ASCII Files; there is no
                        benefit when sending ZIP type Files. Cannot be
                        used in conjunction with MobyTurbo mode (-m).

        sz -w File(s)   Send Zmodem Batch [filespecs] to a Receiver,
                        using a  "sliding window" - forcing a Receiver
                        to transmit an  acknowledgement  to the Sender
                        every window /4 bytes. This feature is useful
                        for sending Files over Telenet.

        sz -k File(s)   Send Zmodem Batch [filespecs] to a Receiver,
                        using 1,024 byte packets instead of auto-shift.
                        May increase average throughput by a few cps on
                        small files. No effect on files >100 kb.
                                                                         

 **     sb -k File(s)   Send Ymodem-1K or Ymodem-1K-G the Filespecs to
                        a Receiver.  The Receiver determines CRC or -G
                        error correction method. The Sender determines
                        128 byte or 1,024 byte (-1K) packet size.
        sx -k File      Send Xmodem-1k or Xmodem-1k-G [filespecs] to
                        a Receiver.  The Receiver determines CRC, Sum,
                        or -G error correction method. The Sender sets
                        the Xmodem packet size.  Xmodem-1K-C  is often
                        incorrectly called  Ymodem/CRC .

        sx File         Send Xmodem/CRC or Xmodem/Sum [filespecs] to
                        a Receiver.  The Receiver determines CRC, Sum,
                        or -O error correction method.

   COMMANDS        RECEIVERS

        rz -y           Receive Zmodem Batch and overwrite an existing
                        File with the same name.

 **     rz -y d:\path   Receive Zmodem Batch and overwrite an existing
                        File with the same name on directory d:\path
                        REGISTRATION REQUIRED for the d:\path feature.

 **                     Alternatively, a Receive pathspec is specified
                        by using  SET DIRRX=d:\path  in  AUTOEXEC.BAT

        rz -m           Receive Zmodem Batch using MobyTurbo mode for
                        faster transfer times. Specifying -m to the
                        receiver will force a DSZ transmitter to use
                        MobyTurbo unless transmitter is restricted -M
                        also requires RTS/CTS hardware handshaking.

        rz -M           Receive Zmodem Batch and force the DSZ transmitter
                        to NOT use MobyTurbo mode.  Useful with ASCII
                        transfers in conjunction with RLE compression
                        (DSZ rz -MZ)

        rz -r           Receive Zmodem Batch and overwrite an existing
                        File with the same name - starting at the last
                        byte of the existing File ( Crash Recovery )

        rz -rr          Receive Zmodem Batch (as above) with the additional
                        feature of doing a more thorough check of both files
                        before continuing (Intelligent Crash Recovery)

 **     rz -Z           Receive Zmodem Batch using "RLE" compression.
                        When used on the receiver, will force the DSZ
                        transmitter to use RLE unless restricted.

 **     rb -y           Receive Ymodem Batch and overwrite an existing
                        File with the same name.

        rc -y File      Receive Xmodem/CRC or Xmodem/Sum or Xmodem-1k,
                        overwriting "File" if it already exists.

         NOTES:         ZMODEM uses 32-Bit Cyclical Redundancy Checking

                        YMODEM uses 16-Bit Cyclical Redundancy Checking
                        YMODEM-1k-G requires modem hardware error correction

                        XMODEM uses 16-Bit CRC and falls back CheckSum
                        XMODEM-1k-G requires modem hardware error correction
                                                                          

         NOTES, contd:  both '-G' protocols, Ymodem-1k-G and Xmodem-1k-G
                        require that the modem do the error correction.
                        If one of these '-G' streaming protocols encounters
                        a "hit" the transfer will abort catastrophically.
                        This is why the '-G' streaming protocols cannot be
                        used successfully with non-error correcting modems.

   COMMANDS        RECEIVERS  -  High Speed MNP, V29, V32, V.32bis  Modems

 **     rb -gy          Receive Ymodem Batch-G  and overwrite existing
                        File with the same name - use with MNP or V.42
                        modems-
                        ...the fastest transfer protocol available today.

        rc -gy File     Receive Xmodem-1k-G  and overwrite an existing
                        File with the same name - use with MNP or V.42
                         modems-


        ro -y File      Receive Xmodem-O  "Overthruster" and overwrite
                        an existing File.  Useful for GEnie Downloads,
                        and Compuserve XMODEM Downloads.
____________________________________________________________________________
                        COMMAND  LINE  OPTIONS

        TRANSMITTER OPTIONS

  ZMODEM:       sz [-MmZSwNfkt8g]  [PREFIX=p] [ONAME=n]  Filespecs

  YMODEM:       sb [-fkt8g]  [PREFIX=p] [ONAME=n]  Filespecs

  XMODEM:       sx [-kt8g]  Filespec

        -M     disables MobyTurbo mode when given to either the transmitter
               or the receiver, and overrides -m on the receiver. Option only
               available with the DSZ Zmodem protocol.

        -m     enables MobyTurbo mode when given to either the transmitter
               or the receiver except when either transmitter or receiver is
               restricted -M.  This is the fastest way to transfer .ZIP files
               when using Zmodem. (Moby is a Zmodem option only and requires
               RTS/CTS  handshaking (DSZ ha on rz    or    DSZ ha on sz )

        -S     Interrogates the receiving program for its serial number and
               when obtained, stores this information in the performance log.

        -Z      enables ZMODEM 12-Bit Lempel-Ziv compression of File contents.
                ...this is the fastest way to transmit ASCII Files, and is
                much faster than MNP or V.42bis compression. (DSZ Zmodem only)

        -wN     Configure a Zmodem "window" of N bytes, over-riding a ZMODEM
                z pw_ numeric parameter if also present.  The default window
                is 3072 Bytes for the -w option.

        -f      enables (Batch) send Files to specified  d:\path  of receiver.

        -k      enables 1 Kb XMODEM or YMODEM Blocks or Zmodem initial packet.
                                                                           

        RECEIVER OPTIONS


  ZMODEM:       rz [-mMr+npyt8g]  [d:\pathspec]  [Filespecs]

  YMODEM:       rb [-go+npyt8g]  [d:\pathspec]  [Filespecs]

  XMODEM:       rc [-gyt8g]  Filespec

  YMODEM/Overthruster:     ro [-yt8g]  Filespec


        -m      enables MobyTurbo mode enhanced throughput. Use w/Zmodem only.

        -M      disables MobyTurbo mode. Use w/Zmodem only.

        -r      enables automatic Crash Recovery for Zmodem File transfers.

        -rr     enables Intelligent Crash Recovery for DSZ Zmodem transfers.

        -g      enables full-flowing XMODEM or, YMODEM-1K-G File transfers.

        -o      enables "OverThruster" mode for YMODEM-1K-O File transfers.



        CONSOLE TERMINAL OPTION for TRANSMITTERS and RECEIVERS


        -yt8g           This option will return the Sender or Receiver
                        to terminal mode after a File Transfer. Add this
                        option to Transmitter/Receiver command line or,

 **                     Use  SET DSZOPT=yt8g  in AUTOEXEC.BAT to make
                        all transfer commands return to the terminal mode
                        after Receiving or Sending File(s).

 **                     Use  SET DSZOPT=rt8g  in AUTOEXEC.BAT to make
                        all transfer commands return to the terminal mode
                        after Receiving or Sending File(s) with Crash
                        Recovery enabled.



                        Zmodem Terminal mode Receiver

        RT.BAT  = DSZ port 1 speed 2400 d pB8192 t -my8g

        enter RT to go on-line and ALT-X to go off-line (the DOS prompt).

                        Zmodem-Z Console Transceiver

        SZ.BAT  = DSZ port 1 speed 2400 D pB8192 sz -mSZty8g %1 %2 %3

        enter SZ [Filename]s] at the DOS prompt and use CTRL-Break to abort.
        Substitute correct port and speed as necessary.

        after sending Files  the Transmitter  becomes a Console Receiver.
        enter ALT-X to go off-line (the DOS prompt) and RT to go on-line.
                                                                            

        FILE HANDLING OPTIONS

        -p      transfer File if and only if it does not exist on d:\path .

        -r      receiver:  recover data to an existing File

        -r      sender:  command receiver to recover data to existing File

        -+      receiver:  append data to an existing File

        -+      sender:  command receiver to append data to an existing File

                sz -+ ONAME=MASTER.LOG *.LOG   transmits all .LOG Files from
                the sender's directory and appends them to File  MASTER.LOG
                on the receiver's directory.

        -f      transmit a full pathspec with the filespec to the receiver.

                sz -f \path\Filespec    sends File to \path\ on remote Dir.
                unless restricted.  Sysops should restrict to prevent files
                from landing on the wrong directory.

                sz -y PREFIX=\path\ *.LOG   transmits all .LOG Files from
                the sender's directory and overwrites on remote's \path\ .

        -n      transfer File if newer or non-existent on remote directory.

        -N      transfer File if newer or longer or non-existent on remote.

        -y      receiver:  overwrite data over an existing File w/same name

        -y      sender:  command receiver to overwrite an existing File

        -Y      transfer File if and only if it exists on remote directory.


        MISCELLANEOUS OPTIONS


        -a      requests the receiver to adjust Files to ASCII standards.

        -b      inhibits the receiver from altering binary information.

        -e      inhibits Zmodem sender from transmitting control characters.

        -S      interrogates the receiver for his DSZ serial number.

        -s      logs "questionable" aborts from a Zmodem receiver.

        -u      deletes the Filespec(s) sent after transfer is completed.

        -v      enables viewing of data being received during a transfer.

        -q      disables XMODEM and YMODEM "block" status line displays.

        -zT     specify T minutes behind GMT (Greenwich Mean Time) in place
                of pz parameter value, if also present.
____________________________________________________________________________ 


                        CONSOLE  (TERMINAL MODE) CONFIGURATION

        COMMANDS

        t -y8g          DSZ "tty"  8-N-1  Terminal Mode with automatic
                        Zmodem Batch Downloading -  Files received are
                        written to the current directory and overwrite
                        an existing File with the same name.

        t -r8g          DSZ "tty"  8-N-1  Terminal Mode with automatic
                        Zmodem Batch Downloading -  Files received are
                        written to the current directory and append to
                        an existing File with automatic Crash Recovery.

        t -gy8g         DSZ "tty"  8-N-1  Gonzole Receiver with Zmodem
                        Downloading -  Existing files are overwritten,
                        hit F3 to begin Ymodem-1K-G Batch Downloading.


         NOTES:         Use  DEVICE=ANSI.SYS  in  CONFIG.SYS  to make
                        a DOS ANSI Console DEVICE.

                        Use ANSI.COM in AUTOEXEC.BAT to make PC Mag's
                        ANSI-IBM Console RESIDENT.

                        Use DEVICE=FCONSOLE.DEV in CONFIG.SYS to make
                        a FANSI-ZMODEM Console Receiver.  This DEVICE
                        provides a scroll-back screen buffer that can
                        be saved to disk, enhanced keyboard and video
                        performance, and full ANSI X3.64 emulation.


        CONTROLS

                        Fkey-1       -  exits to DOS (not Shell), with
                                        no loss of CARRIER.

                        Fkey-3       -  begin to receive Ymodem Batch;
                                        Zmodem receive is automatic.

         NOTE:          Use  DSZ t -gy8g  to enable YMODEM-1K-G  auto
                        downloading via Fkey-3.


                         ALT-X       -  exits to DOS (not Shell), with
                                        no loss of CARRIER.

                         ALT-N       -  aborts DSZ and returns to DOS,
                                        but does not drop the CARRIER.

                         ALT-P       -  toggles 8th bit parity off/on,
                                        note 8g is required for ANSI.

                         ALT-H       -  toggles local echo on, autoLF,
                                        and echo/LF off (default). Use
                                        this for PC to PC connections.

                         ALT-F       -  cancels a File being received;
                                        a Batch Transfer continues with
                                        the next file in sequence.            




                         ALT-B       -  cancels a Batch transfer being
                                        received, returns to terminal.

                        CTRL-S       -  (XOFF) suspends receiving data

                        CTRL-Q       -  (XON)  resumes  receiving data

                        CTRL-X       -  (CAN)  cancels  receiving data

                        CTRL-Break   -  cancels any File Transfer then
                                        returns to terminal mode.  Use
                                        to unlock the local console if
                                        an XOFF (CTRL-S) is received.

                       SHIFT-PtScr   -  sends screen display to printer

                        CTRL-PtScr   -  trace console display on printer

      EXAMPLES:

                        Zmodem-T Console Receiver

        RT.BAT  = DSZ port 1 speed 2400 ha on d pB8192 t -myZ8g


                        Zmodem-R Console Receiver

        RZ.BAT  = DSZ port 1 speed 2400 ha on d pB8192 t -rmyZ8g


                        Zmodem-Z Console Transceiver

        SZ.BAT  = DSZ port 1 speed 2400 ha on D pB8192 sz -mSZty8g %1 %2 %3


                        Zmodem-W Console Transceiver

        SW.BAT  = DSZ port 1 speed 2400 ha on D pB8192 sz -mZwty8g %1 %2 %3



                        CONSOLE  TERMINAL  OPERATION



        enter RT to go on-line and ALT-X to go off-line (the DOS prompt).

        enter RZ to go on-line with Zmodem CRC-32 Crash Recovery enabled.

        enter SZ [Files] at the DOS prompt and use CTRL-Break to abort.

        enter SW Filespecs at the DOS prompt to transmit "window" Zmodem.
                                                                               


        Upon completion of a transfer the console is returned to terminal
        mode, acting effectively as a "transceiver".  Loading the program
        from a virtual (RAM) disk, the transition from DOS console to TTY
        is so fast that it feels as if "RT" is a DOS "RTTY" mode.

        To dial enter ATDT1234567 <cr>. To hang up enter three "+++" then
        wait for your modem's "OK" to appear and type  ATH <cr>.

        There is no software dialer inside DSZ.  With hardware dialing it
        really sings.  Software dialing is available from many integrated
        communications packages:  the DSZ "console transceiver" is closer
        to the DOS console and the Modem device than integrated packages.
        Rather like a Formula II car with no fenders or bumpers but with
        a very powerful Zmodem engine behind you.

        A DSZ console transceiver operator should be aware that his modem
        responds to typed commands beginning with the prefix "AT" and his
        console (display / keyboard) responds to "escape sequences", thus
        "emulating" an American National Standards Institute terminal.

        With FANSI CONSOLE installed, RT delivers efficient displays and
        a screen recall buffer.  With CED installed, operations from the
        DOS prompt are facilitated.  RT.BAT and associated receivers and
        transmitters can be fully integrated with DOS by using "CED syn".

        To capture data enter  RT >capture.dat   and punch  ALT-X  after
        your modem RXD light stops glowing ( no display during capture ).

        enter  RT >>capture.dat  to append data to an existing File.

                         CONSOLE STATUS DISPLAY

             enter  DSZ d pv2 p z p t  for a detailed console display.

  DSZ (TurboC) Copyright 01-08-89 by Omen Technology INC
           "The High Reliability Software"
  B =   1024   O =      0   Q =      1   S =     15   W =      0   a =   6000
  d =      1   v =      2   z =      0
  b =      0   B =      2   C =     11   e =      0   l =      0   L =      0
  n =      0   p =     50   P =      1   r =      0   s =     15   t =    100
  T =    600   w =      0   W =   1400   Z =      0   
  COM1 2400 bps  Carrier Detect DISABLED  Handshake Off S/N 12345
  DSZOPT = 'Zyt8g' Command line = 'd pv2 p z p t '
  Talking 8g. Type F1 to exit.


        STATUS:         the NUMERIC PARAMETERS and ZMODEM PARAMETERS
                        are listed by  letter = value.

                        the pv2 parameter enables detail during xfers,
                        including status of Zmodem-W "window" pacing.

                        the port  COM1:  device was opened (default).

                        the "d" parameter used above has DISABLED the
                        check for DCD (pin 8) Carrier Detect.
                                                                                

                        the hardware Handshake (RTS/CTS) is disabled,
                        XON/XOFF handshaking is in effect for Zmodem
                        and Ymodem Batch transfers by default.

                        environment options DSZOPT=Zyt8g are present.

                        DSZ Terminal mode was invoked with  -y option
                        from the environment enabling File over-write.

                        DSZ Terminal mode was invoked with -8g option
                        from the environment enabling high ASCII (the
                        default "parity" of  8n  "none" is equivalent
                        to a high-ASCII display filter).

                        CONSOLE INDICATORS & ERROR CODES



        2048 ZMODEM CRC-32  XOFF

                        indicates that the sender has received an XOFF
                        from the receiver or a network medium through
                        which he is transmitting.




        Sector 280 35k YMODEM-1k-g  FLOW


                        indicates that CTS (pin 5) is low, suspending
                        transmission to the modem or device until the
                        line goes high. A NORMAL OCCURRENCE when used
                        in conjunction with high speed error-correcting
                        modems!

        Output Restraint RELEASED


                        indicates that the sender or receiver has not
                        received an XON or CTS (8) high in 15 seconds.


         NOTES:         Use the NUMERIC PARAMETERS pS15 and z ps15 to
                        change the default 15 second timeout for XOFF.

                        Use the NUMERIC PARAMETERS pS15 and z ps15 to
                        change the default 15 second timeout for FLOW.

 
        ERROR RECOVERY

                        indicates that sender and receiver are trying
                        to continue the File transfer after an error.


        ZMODEM Crash Recovery at

                        indicates that the "-r" option was active and
                        the receiver is recovering data in a Filespec.  



        Not allowed to overwrite

                        indicates that the "-y" option was not active
                        and the receiver has attempted to over-write
                        an existing Filespec.


        File skipped by receiver request

                        indicates that the "-y" option was not active
                        for the receiver and the sender has attempted
                        to transfer an existing Filespec.

        No such file or directory

                        indicates that the Path/File specified on the
                        command line was nonexistent.

        Unknown Machine Type XX

                        indicates the pa6000 timing parameter may need
                        to be manually set for your computer. (RARELY)

        Garbage Count Exceeded

                        indicates the z pW1400 timing parameter should
                        be manually set for this transmission medium.

        Serial Input Error: Line Status Register XX

                        indicates a general communications failure, as:

                01      Receive buffer full - remote not responding to
                        XOFF software or RTS hardware flow control.

                02      Data overrun - receiving errors were caused by
                        interrupt latency effects.  Upgrade to a 16550AFN
                        UART and/or eliminate TSRs and DEVICEs.  This is
                        the most common type of DSZ error.  The problem
                        is definitely on the receiving end.

                08      Framing error - indicates Bps/Parity mismatch
                        or very high line noise.

                10      Break interrupt - also a Bps/Parity mismatch
                        or very high line noise.

                18      Framing error &/or Break interrupt - defective
                        UART in the serial I/O port.

        No Carrier Detect

                        indicates that the ENABLED check for a CARRIER
                        on DCD (pin 8) has found NO CARRIER present.
                        DSZ will exit abruptly.
                                                                         


        DSZ FINISHED! exit code = 0

                        indicates the errorlevel returned to DOS after
                        exit from Terminal Mode or completion of File
                        transfer.  Errorlevel = 1 for abnormal exit.

____________________________________________________________________________

                        TRANSMITTER  CONFIGURATIONS  FOR  TELENET


                        Send Zmodem Batch-W  Telenet 2400 (CONNECT 2400)

        SW.BAT  = DSZ port 1 speed 2400 pB8192 sz -Zw4096 %1 %2 %3

                        use this command when you are connected 2400
                        to your local PAD and a Host is CONNECT 2400
                        from the 2400 out-dial PAD.



                        Send Zmodem Batch-W  Telenet 2400 (CONNECT 1200)

   S3.BAT  = DSZ port 1 speed 2400 est 0 1200 pB8192 sz -Zw3072 %1 %2 %3

                        use this command when you are connected 2400
                        to your local PAD and a Host is CONNECT 1200
                        from the (2400 or 1200) out-dial PAD.


                        Send Zmodem Batch-W  Telenet 1200 (CONNECT 1200)

        S2.BAT  = DSZ port 1 speed 1200 pB8192 sz -Zw2048 %1 %2 %3

                        use this command when you are connected 1200
                        to your local PAD and a Host is CONNECT 1200
                        from the 1200 out-dial PAD.


       NOTES:           Larger Zwindows increase transfer performance but
                        may cause excessive XOFF delays from the network.

                        Downloading is more efficient than uploading and
                        Host systems can usually transmit without "-w".

                        TELENET  CONFIGURATION  PROCEDURES

   PROCEDURE:           to configure Telenet for ZMODEM CRC-32 Batch

                1)      ATDT7780825 <cr>        dial local Telenet PAD
                2)      @D <cr>                 link 8-N-1 Telenet PAD
                3)      D3 <cr>                 TERMINAL= buffered 12:1
                4)      C D/TXHOU/24,id,pw      request remote PAD link
                5)      ATZ <cr>                clear   out-dial modem
                6)      @ <cr>                  request Telenet command mode
                7)      SET? 5:1 <cr>           enable  XOFF from PAD to you
                8)      RST? 5:1 <cr>           enable  XOFF from PAD to host
                9)      CONT <cr>               return  to out-dial modem
               10)      AT*E1 <cr>              enable  auto-MNP seeking
               11)      ATDT9611604 <cr>        execute auto-dial of number


       NOTES:           ZMODEM "escapes" network commands and can compress
                        data before sending in a continuous flow.  Packets
                        adjust in size depending upon Bps and error rates.

                        The receiver checks each packet with a 32-bit CRC,
                        and requests retransmission of data from an exact
                        point should an error occur.

                        When an error does occur, a receiver discards the
                        data flowing in until the requested frame start is
                        found.  This "garbage count" is set to 1400 bytes
                        by default and can be made larger if required.

                        When sending, the network will accept a continuous
                        stream of data until an artificial "window" fills,
                        at which time it sends an XOFF (CTRL-S) to stop or
                        slow down (pace) the transmitter.

                        The frequency of XOFF delays is a function of the
                        network loading and the size of the real "window".


                        Zmodem-W File transfers are free-flowing however,
                        the receiver must return an acknowledgment after
                        every  window.  When the Zmodem window is equal
                        to the real network window, fewer  XOFF delays
                        and over-run errors are experienced.

                        The idea behind ZMODEM-W is for the receiver and
                        transmitter to pace themselves rather than having
                        the network set the pace by causing XOFF delays.

                        The Zmodem "-w" option configures a File transfer
                        for a 3 Kb "window" (by default) and can be reset
                        up  -w4096  or down  -w2048  for precision pacing.

                        A "window" ie: -w4096  usually indicates that free
                        flowing (no -w option) is possible.

   PROCEDURE:           to configure Telenet for YMODEM/-1K/CRC/-G Batch


                1)      ATDT7780825 <cr>        dial local Telenet PAD
                2)      @D <cr>                 link 8-N-1 Telenet PAD
                3)      D3 <cr>                 TERMINAL= buffered 12:1
                4)      C D/TXHOU/24,id,pw      request remote PAD link
                5)      ATZ <cr>                clear   out-dial modem
                6)      @ <cr>                  request Telenet command mode
                7)      SET? 5:1 <cr>           enable  XOFF from PAD to you
                8)      RST? 5:1 <cr>           enable  XOFF from PAD to host
                9)      SET? 0:33,35:10,64:4    increase artificial window
               10)      CONT <cr>               return  to out-dial modem
               11)      AT*E1 <cr>              enable  auto-MNP seeking
               12)      ATDT9611604 <cr>        execute auto-dial of number


       NOTES:           YMODEM sends binary data in 128 byte or 1K blocks,
                        and uses a Filespec Header for  Batch  capability.

                        The YMODEM receiver performs a 16-bit CRC test for
                        each data block, returning an ACK or NAK code to a
                        sender after each block is received and tested.     


                        When  -w4096  is possible there is  YMODEM-1K-G to
                        consider.  This is a balls-out protocol, no checks,
                        designed for MNP type modems.  Telenet features MNP
                        on all 2400 Bps Lines.  Even if your modem is not
                        MNP, enabling  the  outdial  modem's  MNP  provides
                        hardware error correction whenever a Host uses MNP.

                        Achieving a RELIABLE connect with a Host will often
                        enable his high-speed "-G" protocols.  But even so,
                        just firing up a  YMODEM-G Receive  in response to
                        a YMODEM-1K Sender causes him to go into "-G" mode.

                        From a  DSZ t -g  Console Receiver, just punch F3.
                        Without error-correction on one or both (PAD) ends,
                        using YMODEM-G can be risky.  To be sure, one line
                        hit or extraneous character in the data stream will
                        cause a transfer to abort ( often spectacularly ).

                        Using  YMODEM-G  pushes the ability of the network
                        to process continuous data at high speeds. Setting
                        SET 0:33,35:10  (equivalent to SET 4:10)  commands
                        the network to accumulate data into larger bundles
                        before sending them on. This reduces the frequency
                        of XOFF flow control delays when you upload... but
                        there are unpleasant side-effects on your console.

                        Parameter 0:33,35:2 can be SET from 35:1 to 35:80

                        Parameter 0:33,64:0 can be SET from 64:0 to 64:8
                        Parameter 64:4 is called "advance ACK" and defines
                        an "artificial window".  Changing the default 64:0
                        to increase the artificial window size may improve
                        efficiency... but there is some risk of data loss.

                        Tweaking the Telenet default  SET?  0:33,35:2,64:0
                        affects Zmodem-W and Ymodem-G transfer performance.
                        Note that any SET? commands can always be modified
                        after the out-dial modem has established a CONNECT.

     CAUTION:           Note that the RST? command should not be attempted
                        after the out-dial modem has established a CONNECT.

   PROCEDURE:           to configure Telenet for XMODEM/-1K/CRC/Sum/-G


                1)      ATDT7780825 <cr>        dial local Telenet PAD
                2)      @D <cr>                 link 8-N-1 Telenet PAD
                3)      D1 <cr>                 TERMINAL= video display
                4)      C D/TXHOU/24,id,pw      request remote PAD link
                5)      ATZ <cr>                clear   out-dial modem
                6)      @ <cr>                  request Telenet command mode
                7)      SET? 1:0,7:8 <cr>       change  <cr>@<cr> to BREAK
                8)      CONT <cr>               return  to out-dial modem
                9)      AT*E1 <cr>              enable  auto-MNP seeking
               10)      ATDT9611604 <cr>        execute auto-dial of number

       NOTES:           XMODEM sends pure binary data in 128 byte or 1 Kb
                        packets.  The XMODEM receiver performs a checksum
                        or 16-bit CRC test for each data block, returning
                        an ACK or NAK code to the waiting sender.          


                        Because the network medium causes a delay between
                        sender and receiver, the turnaround time required
                        to process an ACK or NAK is considerable.  XMODEM
                        with 1 Kb packets (often called Ymodem/CRC), uses
                        7 less ACK/NAK delays for every 1,024 bytes sent.

                        As in YMODEM-G, the XMODEM-G receiver requests an
                        XMODEM/-1K sender to transmit free-flow.  However
                        unlike YMODEM-G, XMODEM does not support XON/XOFF
                        and can garble data by blowing it into Telenet.


     CAUTION:           Because the network command <cr>@<cr> in any data
                        stream would cause an escape to net command mode,
                        change the <cr>@<cr> to a break signal to prevent
                        accidental abort of an XMODEM File transfer.

                        Note further that unless  CTRL-Break "send BREAK"
                        functions on your console, using SET 1:0,7:8 will
                        prevent subsequent access to net command mode!

   PROCEDURE:           to configure out-dial Racal-Vadic Modem for MNP


                1)      ATZ <cr>                clear   out-dial modem
                2)      CTRL-E <cr>             request Racal-Vadic mode
                3)      O <cr>                  request Option Groups menu
                4)      2 <cr>                  request Option Group 2 menu
                5)      19 <cr>                 request Option 19 menu
                6)      1 <cr>                  enable  auto-MNP seeking
                7)      0 <cr>                  request Option Group 2 menu
                8)      0 <cr>                  request Option Groups menu
                9)      4 <cr>                  execute changed options
               10)      D9611604 <cr>           execute auto-dial of number
               11)      R9 <cr>                 execute auto-redial of number

       NOTES:           Telenet's  Racal-Vadic mode presents menus in place
                        of "AT" commands. They are useful for exploring the
                        capabilities of out-dial hardware and for using the
                        built-in auto-dialer.

                        The R-V auto-dialer is faster than the "Hayes" ATDT
                        dialer and provides more information about the call.
                        The R-V hardware redialer will make up to 9 redials.

                        MNP seeking remains enabled until a CONNECT or ATZ.

                        Whether using the above procedure for "Racal-Vadic"
                        or simply using  AT*E1  from the "Hayes" mode, note
                        that MNP must be re-enabled after completing a call.

                        Note some 1200 Bps out-dial modems do not have MNP.

   PROCEDURE:           to disconnect from TeleNet and turn off all timers


                1)      I <cr>                  request Hayes mode
                2)      ATZ <cr>                clear   out-dial modem
                3)      @ <cr>                  request Telenet command mode
                4)      D <cr>                  request remote PAD unlink
                5)      +++                     request modem command mode
                6)      ATH <cr>                disable carrier            


____________________________________________________________________________


        EXAMPLES of DSZ USAGE with CCITT V.22bis STANDARD 2400 BPS MODEMS


                          Zmodem Console Receiver

        RT.BAT  = DSZ port 1 speed 2400 d pB8192 t -8g


                        Zmodem-Z Console Transmitter

        ST.BAT  = DSZ port 1 speed 2400 sz -Zt8g %1 %2 %3



        Standard 2400 Bps CCITT V.22bis  Modems can achieve 228 +/- 5 c.p.s.
        throughput on ZIP Files using the DSZ Zmodem Driver.



        TRANSMITTERS    (typical batch files for use alone or as external
                         drivers with another communications program)

                        Send Zmodem Batch CRC-32/RLE

                SZ.BAT  = DSZ port 1 speed 2400 pB8192 sz -Z %1 %2 %3


                        Send Zmodem Batch Mobyturbo

                SZ.BAT  = DSZ port 1 speed 2400 ha on pB8192 sz -m %1 %2 %3


                        Send Ymodem Batch/CRC-16

                SB.BAT  = DSZ port 1 speed 2400 pB8192 sb -k %1 %2 %3



                        Send Xmodem-1k/CRC/CheckSum

                SY.BAT  = DSZ port 1 speed 2400 pB8192 sx -k %1
                        Send Xmodem/CRC/Sum

                SX.BAT  = DSZ port 1 speed 2400 pB8192 sx %1



        RECEIVERS

                        Receive Zmodem Batch CRC-32

                RZ.BAT  = DSZ port 1 speed 2400 pB8192 rz

                                                                            

                        Receive Zmodem Batch Mobyturbo

                RZ.BAT  = DSZ port 1 speed 2400 ha on pB8192 rz -m


                        Receive Ymodem Batch/CRC-16

                RB.BAT  = DSZ port 1 speed 2400 pB8192 rb



                        Receive Xmodem/-1k/CRC/Sum

                RY.BAT  = DSZ port 1 speed 2400 pB8192 rc %1




         NOTES:         Use  SET DSZOPT=y  in AUTOEXEC.BAT to enable
                        overwriting existing Files when received.

                        Use  SET DSZOPT=r  in AUTOEXEC.BAT to enable
                        Crash Recovery of existing Files.

                        Use  SET DSZOPT=yt8g  in AUTOEXEC.BAT to make
                        all of the above commands return to "tty" mode
                        after Receiving or Sending File(s).

                        Use  SET DSZOPT=rt8g  in AUTOEXEC.BAT to make
                        all of the above commands return to "tty" mode
                        with Crash Recovery enabled.


____________________________________________________________________________

    EXAMPLES of DSZ USAGE with 2400 bps V.22bis MNP/V.42/42bis MODEMS

      NOTE: Port speed must always be higher than modem speed with MNP or V.42


                          Zmodem Console Receiver

        RT.BAT  = DSZ port 1 speed 9600 ha on est 0 2800 d t -mg8g


                        Zmodem-Z Console Transmitter

    ST.BAT  = DSZ port 1 speed 9600 ha on est 0 2800 sz -mZktg8g %1 %2 %3


                        Ymodem-G Console Transmitter

    SB.BAT  = DSZ port 1 speed 9600 ha on est 0 2800 sb -ktg8g %1 %2 %3



                                                                             

        The MultiTech MT224EH is a CCITT V.22bis MNP  level  5  modem,
        capable of 280 +/- 5 c.p.s. throughput for ZIP Files using  DSZ.

        The 224E should be configured to disable "compression" for ZIP
        File transfers; use  AT&E14&W0  to do this.  Note that RTS/CTS
        handshaking should be ENABLED -- and that XON/XOFF handshaking
        is DISABLED (to "flow through") for proper Modem operation.

        This Modem features "speed conversion".  The serial port UART
        is "locked" at 9,600 Bps and the 224E adjusts  automatically
        to a 1200 or 2400 Bps Host (with or without MNP).



        TRANSMITTERS for use with the MultiTech & similar 2400 bps modems:

                        Send Zmodem Batch CRC-32/RLE/MOBYTURBO

        SZ.BAT  = DSZ port 1 speed 9600 ha on est 0 2800 sz -mZ %1 %2 %3



                        Send Ymodem Batch/CRC-16/-G

        SB.BAT  = DSZ port 1 speed 9600 ha on est 0 2800 sb -k %1 %2 %3



                        Send Xmodem-1k/CRC/Sum/-G

        SY.BAT  = DSZ port 1 speed 9600 ha on sx -k %1



                        Send Xmodem/CRC/Sum/-O

        SX.BAT  = DSZ port 1 speed 9600 ha on sx %1





        RECEIVERS for use with the MultiTech and similar 2400 bps MNP modems:

                        Receive Zmodem Batch CRC-32

        RZ.BAT  = DSZ port 1 speed 9600 ha on est 0 2800 rz -m



                        Receive Ymodem Batch/CRC-16

        RB.BAT  = DSZ port 1 speed 9600 ha on est 0 2400 rb



                        Receive Ymodem Batch-G

        RGB.BAT = DSZ port 1 speed 9600 ha on est 0 2800 rb -g
                                                                             



                        Receive Xmodem/-1k/CRC/Sum

        RY.BAT  = DSZ port 1 speed 9600 ha on rc %1



                        Receive Xmodem/-1k/-G

        RG.BAT  = DSZ port 1 speed 9600 ha on rc -g %1



                        Receive Xmodem/-1k/-O

        RO.BAT  = DSZ port 1 speed 9600 ha on pO60 ro %1




         NOTES:         Use  SET DSZOPT=y  in AUTOEXEC.BAT to enable
                        overwriting existing Files when received.

                        Use  SET DSZOPT=r  in AUTOEXEC.BAT to enable
                        Crash Recovery of existing Files.

                        Use  SET DSZOPT=ytg8g  in AUTOEXEC.BAT to make
                        all of the above commands return to "tty" mode
                        after Receiving or Sending File(s).

                        Use  SET DSZOPT=rtg8g  in AUTOEXEC.BAT to make
                        all of the above commands return to "tty" mode
                        after Receiving or Sending File(s) with Crash
                        Recovery enabled.

        EXAMPLES of DSZ USAGE with CCITT V.32 MNP/V.42/V.42bis MODEMS


                          Zmodem Console Receiver

    RT.BAT  = DSZ port 1 speed 19200 ha on est 0 11000 d t -g8g


                        Zmodem-Z Console Transmitter

    ST.BAT  = DSZ port 1 speed 19200 ha on est 0 11000 sz -Zktg8g %1 %2 %3


                        Ymodem-G Console Transmitter

    SB.BAT  = DSZ port 1 speed 19200 ha on est 0 11000 sb -ktg8g %1 %2 %3


        The  USR 14400 HST,  the USR Dual Standard  and the new CCITT
        V.32bis modems are capable of 1728 +/- 20 cps throughput using
        DSZ to transfer ZIP files
                                                                            

        The USR modems should be configured to disable "compression"
        for ZIP File transfers.  Use  AT&K3&W  to do this.  Note that
        RTS/CTS handshaking MUST be ENABLED - and that XON/XOFF handshaking
        MUST be DISABLED for proper Modem operation.

        This Modem features "speed conversion".  The serial port UART
        is "locked" at 38,400 Bps and the modem adjusts  automatically
        to a 1200, 2400, 9600 or 14400 bps Host (with or without MNP).

        Owners of the USR HST, Dual Standard, V.32 and V.32bis modems must
        replace their  8250  or  16450 UART chip with a  NS16550AFN  UART
        to achieve high performance. (about $20 at larger electronics parts
        stores - you won't find it at Radio Shack -  get the part number
        ending with "AFN" for best performance).


        TRANSMITTERS for use with 14400 HST's and V.32bis MODEMS:

                        Send Zmodem Batch CRC-32/RLE/MOBYTURBO

        SZ.BAT  = DSZ port 1 speed 38400 ha on est 0 17000 sz -mZ %1 %2 %3


                        Send Ymodem Batch/CRC-16/-G

        SB.BAT  = DSZ port 1 speed 38400 ha on est 0 17000 sb -k %1 %2 %3


                        Send Xmodem-1k/CRC/Sum/-G

        SY.BAT  = DSZ port 1 speed 38400 ha on sx -k %1

                        Send Xmodem/CRC/Sum/-O

        SX.BAT  = DSZ port 1 speed 38400 ha on sx %1


        RECEIVERS for use with 14400 HST's and V.32bis MODEMS:

                        Receive Zmodem Batch CRC-32

        RZ.BAT  = DSZ port 1 speed 38400 ha on est 0 17000 rz -m


                        Receive Ymodem Batch/CRC-16

        RB.BAT  = DSZ port 1 speed 38400 ha on est 0 14400 rb


                        Receive Ymodem Batch-G

        RGB.BAT = DSZ port 1 speed 38400 ha on est 0 17000 rb -g


                        Receive Xmodem/-1k/CRC/Sum

        RY.BAT  = DSZ port 1 speed 38400 ha on rc %1
                                                                             


                        Receive Xmodem/-1k/-G

        RG.BAT  = DSZ port 1 speed 38400 ha on rc -g %1


                        Receive Xmodem/-1k/-O

        RO.BAT  = DSZ port 1 speed 38400 ha on pO60 ro %1

       NOTES:           Use  SET DSZOPT=y  in AUTOEXEC.BAT to enable
                        overwriting existing Files when received.

                        Use  SET DSZOPT=r  in AUTOEXEC.BAT to enable
                        Crash Recovery of existing Files.

                        Use  SET DSZOPT=ytg8g  in AUTOEXEC.BAT to make
                        all of the above commands return to "tty" mode
                        after Receiving or Sending File(s).

                        Use  SET DSZOPT=rtg8g  in AUTOEXEC.BAT to make
                        all of the above commands return to "tty" mode
                        after Receiving or Sending File(s) with Crash
                        Recovery enabled.

____________________________________________________________________________
        EXAMPLES of DSZ USAGE with EIA RS232-C  DIRECT CONNECTIONS

                          Zmodem Console Receiver

        RT.BAT  = DSZ port 1 speed 115200 ha on d t -yg8g


                        Zmodem-Z Console Transmitter

        ST.BAT  = DSZ port 1 speed 115200 ha on d sz -mZktyg8g %1 %2 %3


                        Ymodem-G Console Transmitter

        SB.BAT  = DSZ port 1 speed 115200 ha on d sb -ktyg8g %1 %2 %3



        Direct connection between computers creates an RS232 "network"
        by which two operators can communicate at very high speed.

        PC -to- PC  File transfers are useful when two computers have
        dissimilar removable media or, when they are far apart.

        By using an appropriate Null Modem Cable between serial ports,
        two high speed machines can transfer Files at up to 115,200 Bps.


                IBM PC SERIAL PORT  UART SPECIFICATIONS

                                                                              

             8250       The PC/XT 8250 Universal Asynchronous Receiver
                        Transmitter (UART) provides nine of the RS232C
                        lines from a  DB-25p  (25-pin, male) connector.
                        This is the standard PC serial port controller,
                        and is frequently  limited to  speeds of  less
                        than 9600 Bps. Usually adequate for 2400 Bps.

            16450       The "AT" 16450 Universal Asynchronous Receiver
                        Transmitter (UART) provides nine of the RS232C
                        lines from a  DB-9p (9-pin, male) connector or,
                        from a  DB-25p (25-pin, male) connector. It is
                        capable of operating at higher speeds.

            16550       The PS/2 16550 Universal Asynchronous Receiver
                        Transmitter (UART) provides nine of the RS232C
                        lines from a DB-9p (9-pin, male) connector and
                        features a 16-byte  FIFO  port  buffer.  It is
                        capable  of  operating  at  higher speeds than
                        either the 8250 or 16450 UART.

       NOTE:            UART 40-pin DIP devices are pin-compatible and
                        can be upgraded. The NS16550AFN is recommended
                        for any MS-DOS computer running the DSZ Driver.



                IBM PC SERIAL PORT  PLUG SPECIFICATIONS


                        The Serial Port is configured as RS232-C Data
                        Terminal Equipment (DTE) :


                        pin    DTE direction     signal

                       ( 1)    CHS    nul    chassis ground
                       ( 2)    TXD    out    transmit data
                       ( 3)    RXD    inp    receive data
                       ( 4)    RTS    out    request to send
                       ( 5)    CTS    inp    clear to send
                       ( 6)    DSR    inp    data set ready
                       ( 7)    GND    nul    signal ground
                       ( 8)    DCD    inp    data carrier detect
                      (9/20)   DTR    out    data terminal ready



       NOTE:            The Data Terminal Ready DTR signal is on pin 9
                        of DB-9p Male connectors and pin 20 of DB-25p.




                                                                               

                IBM PC to MODEM CABLE CONFIGURATION: STANDARD DTE-DCE


              signal        pin    DTE     pin    DCE        signal

         chassis ground    ( 1)    CHS    ( 1)    CHS    chassis ground
          transmit data    ( 2)    TXD    ( 2)    TXD    transmit data
           receive data    ( 3)    RXD    ( 3)    RXD    receive data
        request to send    ( 4)    RTS    ( 4)    RTS    request to send
          clear to send    ( 5)    CTS    ( 5)    CTS    clear to send
         data set ready    ( 6)    DSR    ( 6)    DSR    data set ready
          signal ground    ( 7)    GND    ( 7)    GND    signal ground
    data carrier detect    ( 8)    DCD    ( 8)    DCD    data carrier detect
    data terminal ready   (9/20)   DTR   (9/20)   DTR    data terminal ready



       NOTE:            Connecting a Modem or other  Data Communications
                        Equipment device requires a shielded, nine-wire,
                        straight connect cable, with one DB25p Male plug
                        for the device and either a DB9s or DB25s Female
                        socket for the computer.




                IBM PC to PC CABLE CONFIGURATION:  NULL MODEM DTE-DTE


              signal        pin    DTE     pin    DTE        signal

         chassis ground    ( 1)    CHS    ( 1)    CHS    chassis ground
          transmit data    ( 2)    TXD    ( 3)    RXD    receive data
           receive data    ( 3)    RXD    ( 2)    TXD    transmit data
        request to send    ( 4)    RTS    ( 5)    CTS    clear to send
          clear to send    ( 5)    CTS    ( 4)    RTS    request to send
         data set ready    ( 6)    DSR   (9/20)   DTR    data terminal ready
          signal ground    ( 7)    GND    ( 7)    GND    signal ground
    data terminal ready   (9/20)   DTR    ( 6)    DSR    data set ready

                                          ( 8)    DCD    data carrier detect
                                          ( 6)    DSR    data set ready
    data carrier detect    ( 8)    DCD
         data set ready    ( 6)    DSR



       NOTES:           Connecting a  Computer  or other  Data  Terminal
                        Equipment device requires a shielded, nine-wire,
                        "null modem" cable with  DB9s  or  DB25s  Female
                        sockets for the two computers.

                        Standard Practice  to make a null modem cable is
                        to modify straight-wired cable with an extractor/
                        insertion tool, switching:  2x3,  4x5,  and  6x9
                        (or 6x20 for DB25) on one end.  then...

                        Cut the DCD wire  2" from pin 8 on both ends, and
                        "strap" it to DSR pin 6 by soldering on both ends.
                        Take out the old DCD wire from the cable assembly.
  

                        ...alternatively the state of Data Carrier on pin
                        eight is ignored by using the  "d"  parameter.





____________________________________________________________________________







        EXAMPLES of DSZ CONFIGURATION for PCBOARD with 14400 HST

                    N   None Specified   ( always prompts )
                    X   Xmodem/CRC/Sum   ( 84% efficiency )
                    Y   Xmodem/-1K/CRC   ( 94% efficiency )
                    O   Xmodem/-1K/y-G   ( MNP efficiency )
                    B   Ymodem Batch-K   ( 94% efficiency )
                    G   Ymodem Batch-G   ( MNP efficiency )
                    Z   Zmodem Batch-Z   ( 96% efficiency )

                UPLOADING


                        PCBOARD  FILE  PCBRX.BAT

        @Echo Off
        Rem
        Rem     %1      COMn: Port Number n
        Rem     %2      COMn: Port Baud Rate
        Rem     %3      Up/Download Pathspec
        Rem     %4      CONNECT (Link) Speed
        Rem
                IF exist c:\pcb\$DOOR.LOG Del c:\pcb\$DOOR.LOG >Nul
        Rem
                DSZ port %1 speed %2 ha on d z pr1 rc %3
        Rem
                IF errorlevel 1 GoTo ERROR
                IF not exist %3 GoTo ERROR
                IF exist c:\pcb\PCBERR.FIL Del c:\pcb\PCBERR.FIL >Nul
                GoTo END
        :ERROR
                IF exist %3 Del %3 >Nul
                Copy c:\pcb\PCBERR.OLD c:\pcb\PCBERR.FIL >Nul
        :END
   

                        PCBOARD  FILE  PCBRY.BAT

        @Echo Off
        Rem
        Rem     %1      COMn: Port Number n
        Rem     %2      COMn: Port Baud Rate
        Rem     %3      Up/Download Pathspec
        Rem     %4      CONNECT (Link) Speed
        Rem
                IF exist c:\pcb\$DOOR.LOG Del c:\pcb\$DOOR.LOG >Nul
        Rem
                DSZ port %1 speed %2 ha on d z pr1 rc %3
        Rem
                IF errorlevel 1 GoTo ERROR
                IF not exist %3 GoTo ERROR
                IF exist c:\pcb\PCBERR.FIL Del c:\pcb\PCBERR.FIL >Nul
                GoTo END
        :ERROR
                IF exist %3 Del %3 >Nul
                Copy c:\pcb\PCBERR.OLD c:\pcb\PCBERR.FIL >Nul
        :END

                        PCBOARD  FILE  PCBRO.BAT

        @Echo Off
        Rem
        Rem     %1      COMn: Port Number n
        Rem     %2      COMn: Port Baud Rate
        Rem     %3      Up/Download Pathspec
        Rem     %4      CONNECT (Link) Speed
        Rem
                IF exist c:\pcb\$DOOR.LOG Del c:\pcb\$DOOR.LOG >Nul
        Rem
                DSZ port %1 speed %2 ha on d z pr1 rc -g %3
        Rem
                IF errorlevel 1 GoTo ERROR
                IF not exist %3 GoTo ERROR
                IF exist c:\pcb\PCBERR.FIL Del c:\pcb\PCBERR.FIL >Nul
                GoTo END
        :ERROR
                IF exist %3 Del %3 >Nul
                Copy c:\pcb\PCBERR.OLD c:\pcb\PCBERR.FIL >Nul
        :END

                        PCBOARD  FILE  PCBRB.BAT                       


        @Echo Off
        Rem
        Rem     %1      COMn: Port Number n
        Rem     %2      COMn: Port Baud Rate
        Rem     %3      Up/Download Pathspec
        Rem     %4      CONNECT (Link) Speed
        Rem
                IF exist c:\pcb\$DOOR.LOG Del c:\pcb\$DOOR.LOG >Nul
        Rem
                DSZ port %1 speed %2 ha bo d est 0 %4 pd0 z pr1 rb -p %3
        Rem
                IF errorlevel 1 GoTo ERROR
                IF not exist %3 GoTo ERROR
                IF exist c:\pcb\PCBERR.FIL Del c:\pcb\PCBERR.FIL >Nul
                GoTo END
        :ERROR
                IF exist %3 Del %3 >Nul
                Copy c:\pcb\PCBERR.OLD c:\pcb\PCBERR.FIL >Nul
        :END

                        PCBOARD  FILE  PCBRG.BAT

        @Echo Off
        Rem
        Rem     %1      COMn: Port Number n
        Rem     %2      COMn: Port Baud Rate
        Rem     %3      Up/Download Pathspec
        Rem     %4      CONNECT (Link) Speed
        Rem
                IF exist c:\pcb\$DOOR.LOG Del c:\pcb\$DOOR.LOG >Nul
        Rem
                DSZ port %1 speed %2 ha bo d est 0 %4 pd0 z pr1 rb -gp %3
        Rem
                IF errorlevel 1 GoTo ERROR
                IF not exist %3 GoTo ERROR
                IF exist c:\pcb\PCBERR.FIL Del c:\pcb\PCBERR.FIL >Nul
                GoTo END
        :ERROR
                IF exist %3 Del %3 >Nul
                Copy c:\pcb\PCBERR.OLD c:\pcb\PCBERR.FIL >Nul
        :END                                                            

                        PCBOARD  FILE  PCBRZ.BAT

        @Echo Off
        Rem
        Rem     %1      COMn: Port Number n
        Rem     %2      COMn: Port Baud Rate
        Rem     %3      Up/Download Pathspec
        Rem     %4      CONNECT (Link) Speed
        Rem
                IF exist c:\pcb\$DOOR.LOG Del c:\pcb\$DOOR.LOG >Nul
        Rem
                DSZ port %1 speed %2 ha on d est 0 %4 pd0 z pr1 rz -mp %3
        Rem
                IF errorlevel 1 GoTo ERROR
                IF not exist %3 GoTo ERROR
                IF exist c:\pcb\PCBERR.FIL Del c:\pcb\PCBERR.FIL >Nul
                GoTo END
        :ERROR
                IF exist %3 Del %3 >Nul
                Copy c:\pcb\PCBERR.OLD c:\pcb\PCBERR.FIL >Nul
        :END

                DOWNLOADING

                        PCBOARD  FILE  PCBSX.BAT

        @Echo Off
        Rem
        Rem     %1      COMn: Port Number n
        Rem     %2      COMn: Port Baud Rate
        Rem     %3      Up/Download Pathspec
        Rem     %4      CONNECT (Link) Speed
        Rem
                IF exist c:\pcb\$DOOR.LOG Del c:\pcb\$DOOR.LOG >Nul
        Rem
                DSZ port %1 speed %2 ha on d sx %3
        Rem
                IF errorlevel 1 GoTo ERROR
                IF exist c:\pcb\PCBERR.FIL Del c:\pcb\PCBERR.FIL >Nul
                GoTo END
        :ERROR
                Copy c:\pcb\PCBERR.OLD c:\pcb\PCBERR.FIL >Nul
        :END

                        PCBOARD  FILE  PCBSY.BAT

        @Echo Off
        Rem
        Rem     %1      COMn: Port Number n
        Rem     %2      COMn: Port Baud Rate
        Rem     %3      Up/Download Pathspec
        Rem     %4      CONNECT (Link) Speed
        Rem
                IF exist c:\pcb\$DOOR.LOG Del c:\pcb\$DOOR.LOG >Nul
        Rem
                DSZ port %1 speed %2 ha on d sx -k %3
        Rem
                IF errorlevel 1 GoTo ERROR
                IF exist c:\pcb\PCBERR.FIL Del c:\pcb\PCBERR.FIL >Nul
                GoTo END
        :ERROR
                Copy c:\pcb\PCBERR.OLD c:\pcb\PCBERR.FIL >Nul
        :END                                                             


                        PCBOARD  FILE  PCBSO.BAT

        @Echo Off
        Rem
        Rem     %1      COMn: Port Number n
        Rem     %2      COMn: Port Baud Rate
        Rem     %3      Up/Download Pathspec
        Rem     %4      CONNECT (Link) Speed
        Rem
                IF exist c:\pcb\$DOOR.LOG Del c:\pcb\$DOOR.LOG >Nul
        Rem
                DSZ port %1 speed %2 ha on d sx -k %3
        Rem
                IF errorlevel 1 GoTo ERROR
                IF exist c:\pcb\PCBERR.FIL Del c:\pcb\PCBERR.FIL >Nul
                GoTo END
        :ERROR
                Copy c:\pcb\PCBERR.OLD c:\pcb\PCBERR.FIL >Nul
        :END
                        PCBOARD  FILE  PCBSB.BAT

        @Echo Off
        Rem
        Rem     %1      COMn: Port Number n
        Rem     %2      COMn: Port Baud Rate
        Rem     %3      Up/Download Pathspec
        Rem     %4      CONNECT (Link) Speed
        Rem
                IF exist c:\pcb\$DOOR.LOG Del c:\pcb\$DOOR.LOG >Nul
        Rem
                DSZ port %1 speed %2 ha bo d est 0 %4 sb -k %3
        Rem
                IF errorlevel 1 GoTo ERROR
                IF exist c:\pcb\PCBERR.FIL Del c:\pcb\PCBERR.FIL >Nul
                GoTo END
        :ERROR
                Copy c:\pcb\PCBERR.OLD c:\pcb\PCBERR.FIL >Nul
        :END

                        PCBOARD  FILE  PCBSG.BAT

        @Echo Off
        Rem
        Rem     %1      COMn: Port Number n
        Rem     %2      COMn: Port Baud Rate
        Rem     %3      Up/Download Pathspec
        Rem     %4      CONNECT (Link) Speed
        Rem
                IF exist c:\pcb\$DOOR.LOG Del c:\pcb\$DOOR.LOG >Nul
        Rem
                DSZ port %1 speed %2 ha bo d est 0 %4 sb -k %3
        Rem
                IF errorlevel 1 GoTo ERROR
                IF exist c:\pcb\PCBERR.FIL Del c:\pcb\PCBERR.FIL >Nul
                GoTo END
        :ERROR
                Copy c:\pcb\PCBERR.OLD c:\pcb\PCBERR.FIL >Nul
        :END
                                                                          

                        PCBOARD  FILE  PCBSZ.BAT

        @Echo Off
        Rem
        Rem     %1      COMn: Port Number n
        Rem     %2      COMn: Port Baud Rate
        Rem     %3      Up/Download Pathspec
        Rem     %4      CONNECT (Link) Speed
        Rem
                IF exist c:\pcb\$DOOR.LOG Del c:\pcb\$DOOR.LOG >Nul
        Rem
                DSZ port %1 speed %2 ha on d est 0 %4 sz -km %3
        Rem
                IF errorlevel 1 GoTo ERROR
                IF exist c:\pcb\PCBERR.FIL Del c:\pcb\PCBERR.FIL >Nul
                GoTo END
        :ERROR
                Copy c:\pcb\PCBERR.OLD c:\pcb\PCBERR.FIL >Nul
        :END


       NOTES:           The Xmodem transmitter automatically detects
                        a CRC-16 or CheckSum receiver and adapts.

                        These receivers and transmitters drop DTR if
                        the carrier is lost during a transfer.


                PCBOARD  FILE  PCBPROT.DAT

        N,I,0,None Specified   ( always prompts ),N,N,N
        X,S,128,Xmodem/CRC/Sum   ( 84% efficiency ),N,Y,N
        Y,S,1024,Xmodem/-1K/CRC   ( 94% efficiency ),N,Y,N
        O,S,1024,Xmodem/-1K/y-G   ( MNP efficiency ),Y,Y,N
        B,D,1024,Ymodem Batch-K   ( 94% efficiency ),N,Y,N
        G,D,1024,Ymodem Batch-G   ( MNP efficiency ),Y,Y,N
        Z,D,1024,Zmodem Batch-Z   ( 96% efficiency ),N,Y,Y

        EXAMPLES of DSZ CONFIGURATION for PRODOOR with 14400 HST

        ;
        ;       UPLOADING
        ;
        94 B 0 R 0 Ymodem Batch-K  (94%)
        DSZ ha both est 0 $C$ pB4096 pd0 z pb1 pr1 rb -p
        ;
        94 Y 0 R 1 Xmodem/-1K/CRC  (94%)
        DSZ ha rts pB4096 z pb1 pr1 rc
        ;
        99 G 1 R 0 Ymodem Batch-G  (MNP)
        DSZ ha bo est 0 $C$ pB4096 pd0 z pb1 pr1 rb -gp
        ;
        99 O 1 R 1 Xmodem/-1K/y-G  (MNP)
        DSZ ha rts pB4096 z pb1 pr1 rc -g
        ;
        96 Z 0 R 0 Zmodem Batch-Z  (96%)
        DSZ ha rts est 0 $C$ pB4096 pd0 z pb1 pr1 rz -mp                   

        ;
        ;       DOWNLOADING
        ;
        94 B 0 T 20 Ymodem Batch-K  (94%)
        DSZ ha bo est 0 $C$ pB4096 z pb1 sb -k $@$
        ;
        94 Y 0 T 1 Xmodem/-1K/CRC  (94%)
        DSZ ha cts pB4096 z pb1 sx -k
        ;
        99 G 1 T 20 Ymodem Batch-G  (MNP)
        DSZ ha bo est 0 $C$ pB4096 z pb1 sb -k $@$
        ;
        99 O 1 T 1 Xmodem/-1K/y-G  (MNP)
        DSZ ha cts pB4096 z pb1 sx -k
        ;
        96 Z 0 T 20 Zmodem Batch-Z  (96%)
        DSZ ha cts est 0 $C$ pB4096 z pb1 sz -kZm $@$


       NOTES:           ProDoor provides a Batch Transfer interface to
                        the DSZ Driver and enhances  PCBoard's Message
                        and Conference capabilities.

                        ProDoor implements the "RZ" Command which will
                        initiate a Zmodem Batch Receive.

                        Because DSZ sends an  rz <cr>  to the Receiver
                        at the beginning of a Zmodem Upload, users can
                        Upload Zmodem to the ProDoor Command Prompt.

____________________________________________________________________________

        EXAMPLES of DSZ CONFIGURATION for DOS CTTY with 14400 HST

                  RX  SX  Xmodem/CRC/Sum   ( 80% efficiency )
                  RY  SY  Xmodem/-1K/CRC   ( 90% efficiency )
                  RO  SO  Xmodem/-1K/y-G   ( 99% efficiency )
                  RB  SB  Ymodem Batch-K   ( 90% efficiency )
                  RG  SG  Ymodem Batch-G   ( 99% efficiency )
                  RZ  SZ  Zmodem Batch-Z   ( 94% efficiency )

        It is useful for a Remote Sysop to have File Transfer capability
        from the  DOS  "Shell"  CTTY  Mode.  Place these DSZ Batch Files
        "on the path" of the HOST computer to achieve this.

                        RECEIVERS

        RX.BAT  = DSZ CON port 1 speed 38400 ha on D rc -y %1
        RY.BAT  = DSZ CON port 1 speed 38400 ha on D rc -y %1
        RO.BAT  = DSZ CON port 1 speed 38400 ha on D rc -gy %1
        RB.BAT  = DSZ CON port 1 speed 38400 ha on D rb -y
        RG.BAT  = DSZ CON port 1 speed 38400 ha on D rb -gy
        RZ.BAT  = DSZ CON port 1 speed 38400 ha on D rz -my                 


                        TRANSMITTERS

        SX.BAT  = DSZ CON port 1 speed 38400 ha on D sx %1
        SY.BAT  = DSZ CON port 1 speed 38400 ha on D sx -k %1
        SO.BAT  = DSZ CON port 1 speed 38400 ha on D sx -k %1
        SB.BAT  = DSZ CON port 1 speed 38400 ha on D sb -k %1 %2 %3
        SG.BAT  = DSZ CON port 1 speed 38400 ha on D sb -k %1 %2 %3
        SZ.BAT  = DSZ CON port 1 speed 38400 ha on D sz -mZ %1 %2 %3

       NOTES:           The DSZ 'CON' Parameter redirects the display
                        to the  DOS CON: device  for  CTTY  operations.

                        Alternatively, use  >NUL  at the end of a line.

                        Because DSZ sends an  rz <cr>  to the Receiver
                        at the beginning of a Zmodem Upload, Files can
                        be uploaded to the DOS Prompt with SZ Filespec
                        from the Remote Sysop's Console Transmitter.
____________________________________________________________________________
                        PRO-YAM HOST  TeleGodzilla  BULLETIN BOARD
                                     (DSZ Support)

       CONNECT:         (503) 621-3746  1200, 2400, 9600, 14400 MNP 8-N-1
                                        USRobotics 14400 bps Dual Standard
                                        1200 Telenet D/ORPOR/12

     DIRECTORY:     Enter DIRD at the Pro-Yam Host prompt to list Files

      DOWNLOAD:      sz DSZ.ZIP  -  DSZ.COM and DSZ.DOC Fileset

      DOWNLOAD:      sz DSZEXE.ZOO  -  DSZ.EXE Driver File

      DOWNLOAD:      sz ZCOMMDOC.ZIP  -  Zmodem Communications Reference

      DOWNLOAD:      sz YZMODEM.ZOO  -  Ymodem and Zmodem Protocol Reference

      DOWNLOAD:      sz RZSZ.ZOO  -  Zmodem Source Code in "C" Language

      DOWNLOAD:      sz *.*  -  Sends all files in the download directory.
===============================================================================

     DISCLAIMER:     It is  not our  purpose in creating this document to
                     attempt to  diminish the work of the program author,
     but rather to augment a fabulous program with our small contribution
     in the way of an easier  to understand  explanation of the otherwise
     complicated syntax, such that others might also enjoy this program's
     full potential.   We thank  Chuck Forsberg,  for his untiring effort
     in  revolutionizing  data  communications  with his  excellent   DSZ
     Program and his Zmodem file transfer protocol.
===============================================================================
         Prepared by:   Steve Shelton    co-Sysop of Sands ProBoard
                                      .oOo.
Last Update 08/14/91:   Bill Garfield    co-Sysop of Sands ProBoard
                        with the help of the Sands ProBoard members
===============================================================================
SANDS ProBoard, Houston, TX (713) 961-1604  2400 MNP/V.42bis & 9600 HST/V.32bis
===============================================================================