****************************************************************
        *                                                              *
        *          THE GUIDE TO HARD DISK SECTOR INTERLEAVING          *
        *                                                              *
        *                              by                              *
        *                         Steven Gibson                        *
        *                     GIBSON RESEARCH CORP.                    *
        *                       Box 6024, Dept S                       *
        *                       Irvine, CA, 92716                      *
        *                        (714) 854-1520                        *
        *                                                              *
        ****************************************************************


        In these "sophisticated" days of computers, where AUTOEXEC.BAT
        and CONFIG.SYS make casual conversation, it's rare to find a
        topic as interesting and critical but still mis-understood, as
        hard disk sector interleaving.

        Our researches into this area have discovered that MOST IBM AND
        COMPATIBLE personal computers are performance-crippled by mis-
        interleaved hard disk drives.

        Unfortunately, many disk controller companies, in competing with
        each other, have set their disk interleave defaults too tightly
        for many computers.  Such "specsmanship" directly hurts the
        innocent computer user (you) by dramatically limiting his hard
        disk data transfer rate.  This GUIDE carefully explains the
        situation and shows how to use the two included programs to
        determine whether your own IBM PC or compatible's hard disk
        drives have their sector interleave set correctly.

        Responding to this problem, Gibson Research Corp., publisher of
        the popular display screen enhancement utility FlickerFree, has
        recently developed an inexpensive software SOLUTION which first
        determines your system's optimum hard disk interleave factor
        then RESETS IT while leaving all your hard disk data in place!



                   UNDERSTANDING HARD DISK SECTOR INTERLEAVING

        It's a rare person who would not wish for additional performance
        from his personal computer's hard disk drive.  While much
        attention is given to the drive's Average Seek Time, which is a
        measure of the time required to move the read/write head from
        one track to another, there is another vital detail which
        determines overall hard disk performance and which is subject to
        the user's control.

        We will see that the too often neglected SECTOR INTERLEAVING
        factor of a hard disk has a dramatic impact on data transfer
        rates.

        As most people know,  the information stored on a floppy or hard
        disk is arranged in a series of concentric circular paths called
        tracks.  The disk drive's read/write head is specifically
        positioned over any desired track with an operation called a
        SEEK.  Thus an obvious limit on the speed with which a drive can
        find or place information would be the so called track-to-track
        and average seek times.

        A single track of a standard IBM compatible PC contains
        approximately nine thousand bytes of data.  But since we usually
        deal with data in much smaller chunks, each track is divided
        into smaller sections called sectors.  Think of a spinning pizza
        which has been cut into seventeen identical, and numbered,
        slices.  (Drives with RLL encoding pack 50% more data onto every
        track resulting in more than thirteen thousand bytes per track
        divided into 25 or 26 sectors.)

        Now suppose that we need to read the information contained in
        sector 1 of our current track.  We patiently wait for sector 1
        to rotate under our read/write head, reading its data at that
        time.  After absorbing this freshly read information, we realize
        that we also need to read the next sector, number 2.  However,
        by the time sector 1 has been moved into our computer and we've
        decided to read sector 2, the beginning of sector 2 has already
        started passing under the read/write head.  So we have no choice
        but to wait for the disk to rotate all the way around once more
        to deliver sector 2.  If we wished to read a nine thousand byte
        file composed of all seventeen disk sectors on this track,
        seventeen complete rotations of the disk, one for each sector,
        would be required!

        It wasn't long before a bright engineer realized that the entire
        problem could be easily resolved by spreading the sequentially
        numbered sectors out around the disk:  Instead of placing sector
        2 immediately after sector 1, sector 2 could be placed a few
        sectors later!  In this way, after reading sector 1, sector 2
        would be just about ready for reading by the time we were ready
        for it.   Such an elegant solution!

        If, for example, sequentially (logically) numbered sectors were
        staggered out every three physical sectors, then each rotation
        of the disk could read every third sector.  Therefore only three
        revolutions of the disk would be required to read an entire
        track.  Quite an improvement over 17 revolutions!  This sector
        staggering is known as SECTOR INTERLEAVING or SECTOR MAPPING.
        The physical spacing between logically consecutive sectors is
        known as the INTERLEAVE FACTOR.  This example used an interleave
        factor of three, shown as "3:1" and pronounced: "3 to 1".

        The new higher-density RLL controllers need to be correctly
        interleaved too.  With 26 sectors per track a non-interleaved or
        mis-interleaved disk would require 26 revolutions for an entire
        track transfer!

        Now here's the real rub:  In the current environment of mix and
        match highly modular personal computing, responsibility for
        determining and setting your hard disk drive's optimal sector
        interleave factor has "fallen through the cracks" as it were.

        You've never worried about it have you?  If you're inclined to
        believe that someone else has, (like your local dealer perhaps)
        you might be in for a real surprise.  Experiments with a wide
        variety of computers, drives, controllers, clock speeds, and
        interleave factors have shown that the hard disks of MOST
        PERSONAL COMPUTER SYSTEMS ARE NOT PROPERLY INTERLEAVED TODAY!

        So many computers are so badly interleaved that it's quite
        likely that you could increase your own hard disk's performance,
        by FOUR TO SEVEN TIMES just by optimally setting your disk's
        interleave factor!

        The interleave factor can be either too "loose" or too "tight".
        The result of operating with an interleave factor which is too
        loose is lower performance than a particular drive-controller-
        computer combination could achieve with tighter interleaving.
        For example the original IBM PC/XT is interleaved at 6:1 but can
        readily achieve 5:1 in a standard 4.77 Mhz machine and 4:1 in an
        8 Mhz PC.  This means that disks on accelerated PC's can read
        and write at 150% of their current rate!

        The consequence of operating with an interleave factor which is
        too tight is more disastrous, since missing that next sector
        induces the significant delay of another entire disk revolution!

        You might be saying to yourself "so what's an extra disk
        revolution between friends?", but consider this:  If your disk
        is properly interleaved, say with a factor of 3, the entire nine
        thousand byte track will be read or written in just 3 disk
        revolutions.  However, if the particular controller in your
        particular computer cannot achieve that interleave of 3, then 17
        or 18 entire revolutions will be required to read the same
        track.

          3 revolutions versus 18 is a performance difference of 600%!

        Since many files and most programs are well over nine thousand
        bytes long, and since DOS DOES REQUEST an entire track transfer
        in such cases, these 17-revolution track reads add up quickly.
        You would certainly feel the difference between waiting 3
        seconds for a program to start up, versus 18 seconds!

        The damning thing about proper hard disk sector interleave is
        its total dependency upon EVERY factor of your system.  For
        example, the AT&T 6300 requires 20 REVOLUTIONS for a full track
        transfer when reading a disk which is interleaved at the most
        common factor of 3:1!  Even it's faster brother, the 6300 Plus,
        requires 14 revs!  We have found that the AT&T's hard disk data
        transfer rate can be made FOUR TIMES FASTER when its interleave
        is optimized for it!  If you're using a 6300 or 6300+, your disk
        transfer rate is one quarter of what it could be!

        Another example:  Western Digital's RLL hard disk controller
        formats drives at a default interleave of 3.  Believe it or not,
        this interleave is too tight for good old standard 4.77 Mhz XT!
        Consequently 28 entire disk revolutions are required to read a
        SINGLE track!  If the interleave is set to 4 then only 4 revs.
        are required to read the same data, for a 700% throughput boost!

        So by now you're dying to know what's happening with the hard
        disk sector interleave of your own computers!  What interleave
        factors are being used, are they correct, and what you can do
        about it if not!

        Included with this INTLEAVE.DOC file are two small programs:
        SPINTEST.COM and SPINTIME.COM

        The main program, SPINTEST.COM determines how many disk
        revolutions your IBM compatible personal computer requires to
        read an entire 17 sector track from its hard disk.  (SPINTEST is
        also fully compatible with the 25 or 26 sector tracks used with
        the high-density RLL controllers.)

        Running SPINTEST on the many computers at Gibson Research, and
        in many local computer dealerships, we discovered something
        quite surprising:  Most computers being sold today are horribly
        interleaved.  We turned up many machines which required more
        than 17 entire revolutions just to read or write one full track!
        These same machines flew along at 4:1 but not at 3:1.

        For example, Gibson Research has a vintage Leading Edge Model-D
        with a standard Western Digital hard disk controller.  This
        machine always seemed to run more quickly than a newer generic
        PC clone equipped with a different Western Digital controller.
        Both hard disks received their original low-level (interleaving)
        format at the Western Digital default interleave of 3.  After
        all, those dealers must have thought, Western Digital knows
        what's best.   Right?   NOT NECESSARILY!

        Since the controller AND computer together determine the optimal
        interleave, it is IMPOSSIBLE for any controller manufacturer to
        set a single optimal interleave for everyone.  In fact, even the
        controller's revision level can be a determiner!  One of our two
        WD controllers ALWAYS MISSES sectors when the disk is inter-
        leaved at 3, while the other controller makes 3:1 ... in the
        same computer!

        To test this, one of our hard disks was given a low-level format
        at an interleave of four.  Afterward, the SPINTEST timing
        diagnostic program and a stop watch confirmed our suspicions:
        An MS-DOS file copy operation on the hard disk which had
        required 139 seconds when the disk was interleaved at 3:1 now
        took only 39 seconds at an interleave of 4:1!

        Interestingly, that "slower" controller which can't make the
        interleave of 3 on a standard 4.77 Mhz XT does just fine on a
        faster 8 Mhz clone computer.  So as you can see, the COMPUTER
        makes a difference too!  Any way you look at it, the issue of
        sector interleaving involves the complex interactions among the
        disk drive, the controller make and model (even the revision
        level), the processor, and system clock rate.



                 OVERVIEW OF THE INTERLEAVE DIAGNOSTIC PROGRAMS

        The issues of hard disk sector interleaving have gone unnoticed
        for so long because there has never been a clear way to see
        what's really going on deep inside a hard disk.  After seeing
        the importance of this issue, we decided to change this.  The
        two programs SPINTEST and SPINTIME determine, for any standard
        MFM or RLL controller, exactly how many revolutions the disk
        requires to transfer one entire track of data.  The programs
        were hand written in 100% machine language (as is everything
        Steve Gibson writes and Gibson Research publishes) to give them
        the required measuring resolution speed.



                              THE SPINTEST PROGRAM

        SPINTEST determines exactly how many revolutions your hard disk
        currently requires to perform a full track transfer. DOS
        transfers a full track whenever programs or files larger than 9K
        are read or written ... which is most of the time.  SPINTEST
        does NOT directly read your drive's interleave, but the drives
        interleaving performance can be easily inferred from SPINTEST's
        full track transfer revolution count.

        SPINTEST averages the time required for each of over two hundred
        full track reads in order to accurately determine the revolution
        count per read, then the number of revolutions required to read
        just one track and the controller's full-track data transfer
        rate are computed.  SPINTEST only reads data from your drive so
        data is NEVER altered.

        Over two hundred track reads were used because of the
        inconsistent disk transfer behavior of AT&T's 6300 machines.
        These exhibit a maddening inconsistency in their ability to
        transfer disk data.  Sometimes they get the next sector, and
        often not.  This means that a much looser than normal interleave
        generates MUCH BETTER overall disk throughput for AT&Ts.  For
        this reason, and to guarantee correct results on any machines
        which may behave similarly, SPINTEST performs many track reads
        and averages the results.



                              THE SPINTIME PROGRAM

        Since SPINTEST measures track read time, it must assume a given
        ratio between elapsed time and disk rotation rate.  Some weirdo
        clone computers have a clock which runs faster than normal when
        in their "turbo" (8 Mhz) mode, and some lap computers have tiny
        hard disks spinning at weird speeds.  If these do not sound like
        your situation SPINTEST will deliver correct readings and you'll
        not need SPINTIME's confirming measurements.

        But if EITHER of these cases might be you (if you have a weirdo
        clone computer or hard disk sporting laptop) SPINTIME will tell
        you for sure.  SPINTEST is only usable when SPINTIME gives
        standard readings.  The single (not surprising) exception to
        this is for the AT&T 6300 and 6300 Plus machines.  Due the
        overall problems they experience with disk transfers, SPINTIME
        may show a lower-than-3600 RPM reading.  For 6300's this is
        normal.

        SPINTIME is interesting regardless since it determines EXACTLY
        how fast your hard disk is really spinning!



                                    SPINTEST

        To run SPINTEST, simply type its name at the DOS prompt.
        IMPORTANT!: Read the section IMPORTANT SPINTEST AND SPINTIME
        NOTES below, before you begin!

        Since SPINTEST takes the average of over 200 track reads, the
        time required to run this test will vary between approximately
        14 seconds for a fast 2:1 interleaved machine to 98 seconds for
        an incorrectly interleaved 26-sector RLL encoded hard disk.  So
        simply type: SPINTEST at the DOS prompt and wait a minute or
        two.


                                    SPINTIME

        SPINTIME has two purposes:  To determine the speed of your
        system's clock (if you suspect that it might be weird) , and to
        verify that your system's hard disk is spinning at close to the
        standard 3600 RPM standard.  Your system's clock is checked by
        measuring SPINTIME's exact execution time.  It should require
        EXACTLY 60 SECONDS to run ... no matter what.  During that time,
        it is busy watching your hard disk spin, counting every revolu-
        tion.  After EXACTLY 60 seconds, it displays your drive's exact
        RPM (within its measuring resolution.)  IF SPINTIME's total
        execution time is NOT EXACTLY 60 seconds, OR the displayed RPM
        is not close to 3600, SPINTEST's reported revolution count won't
        mean anything either.

        SPINTIME's real value is to assure you that SPINTEST is
        delivering worthwhile answers.



                     IMPORTANT SPINTEST AND SPINTIME NOTES!

        Both programs assume and require DOS 2.0 or higher.  They
        operate on your system's FIRST hard disk only (drive C).  The
        hard disk must be bootable, have its controller plugged into a
        slot, not requiring special CONFIG.SYS device drivers for
        operation.

        SPINTEST and SPINTIME will never disturb your hard disk data,
        but if your disk is some kind of odd-ball they may not function
        correctly.

        The tests will be more accurate if your normal collection of
        memory resident programs (if any) are not in memory at the time.
        Many resident programs "steal" so much time from the computer
        that a delicate timing analysis could be upset.  It would be
        wise to boot your machine from a plain DOS diskette when running
        these tests for maximum reliability.

        Also, turn off (or better yet remove) any disk caching software
        you might be using.  Disk caching intercepts the disk reading
        performed by the programs and renders their measurements invalid
        (and rather humorous).  By the way, disk caching program per-
        formance is significantly improved through proper disk
        interleaving.



                                WHAT IT ALL MEANS

        So now you're wondering:  What do the numbers mean?  How do they
        compare with industry norms and everyone else's?  Should I be
        dancing on roof tops or wringing my dealer's neck?

        A hard disk spins at 3600 revolutions per minute, or 60
        revolutions per second.  A track has 17 sectors of 512 bytes per
        sector.  This means that data passes under your drive's head at
        a rate of 522,240 bytes per second.  (This number is 768,000 for
        RLL con-trollers with 25-sector tracks.) Your system will
        achieve some fraction of this maximum possible rate as
        determined by the number of rotations required to read or write
        each track.  522,240 (or 768,000) is divided by the number of
        revs per track (as SPINTEST does) to calculate your drive's data
        transfer rate.

        Since your system's performance is meaningful only when compared
        to other properly and improperly interleaved systems, the
        following table will give you a feeling for where the industry
        stands:


           1:1 - There IS a controller which achieves 1:1,
                 unfortunately it lacks Error Correcting Code
                 (ECC) which is critical for reliable operation.

           2:1 - Compac machines achieve 2:1.  Adaptec's 2070A
                 RLL controller can do 2:1 with an 8 Mhz machine
                 even though their low-level formatter stubbornly
                 refuses to allow a setting of less than 3!

           3:1 - Newer WD controllers and many other controllers
                 will handle 3:1.  The Adaptec 2070A RLL con-
                 troller will do 3:1 in a 4.77 Mhz machine.

           4:1 - Older WD controllers need 4:1, original IBM XT
                 controllers can do 4:1 in an 8 Mhz machine.
                 The AT&T 6300 Plus works best at 4:1 and WD's
                 RLL controller can only do 4:1.

           5:1 - IBM's original XT controller can do 5:1 in a
                 4.77 Mhz XT but comes interleaved at 6:1.  The
                 AT&T 6300 is best at 5:1 which increases over-
                 all throughput 400% over its default!

           6:1 - Only the original IBM PC/XT seems to have been
                 way out here.  These machines can be tightened
                 up, and if it has an inexpensive accelerator it
                 can probably run at 4:1 for 150% disk boost.


        We have seen that WD controllers which miss at 3:1 will do
        beautifully at 4:1.  Several InfoWorld readers have
        independently confirmed that AT&T machines (with WD controllers)
        perform best at the very loose interleave of 6:1.  Even the old
        true blue IBM controller which runs at 6:1 can always do 5:1,
        and even 4:1 in a faster than 4.77 Mhz machine.



                               DETERMINING FACTORS

        So what system factors influence and determine the optimal
        interleave setting for a given set of equipment?  After a sector
        of data has been read it must be moved from the controller's on-
        board buffer into the computer.  This is done with a process
        known as DMA (Direct Memory Access.)  The time required to
        transfer the sector determines how soon the controller will be
        ready to read the next sector. For this reason add-in
        Accelerator "Turbo" Cards do not generally change a machine's
        optimum interleave since the main system clock speed, which
        continues to control DMA memory accesses, is not changed.  The
        less expensive "Speed Booster" products which alter the basic
        system clock timing DO have a tremendous impact on optimal
        interleave by running the DMA faster and thus moving the data in
        and out faster.



                        GIBSON RESEARCH AND INTERLEAVING

        When we began these experiments we had NO IDEA that so many
        personal computers were so poorly interleaved.  Without the aid
        of our new special software, changing a hard disk's sector
        interleave "manually" requires first backing-up all hard disk
        data onto some secure medium.  Then a low-level re-formatting is
        performed.  This unfortunately messy task was never designed for
        the casual computer user since it requires unpublished knowledge
        of the internal details of your controller, using the DOS DEBUG
        command to poke hexadecimal values into the 8088's machine
        registers and starting the low-level format.  After this, the
        FDISK and FORMAT commands are used to create a partition table
        and lay down the high-level formatting information.  After all
        this, the backed up data must be copied back onto the drive.

        Then, if the experimentally chosen interleave was not correct,
        most of the process would have to be repeated with a different
        trial interleave factor.

        Gibson Research Corp., responding to the clear need for a better
        solution to the task of hard disk sector interleaving optimiza-
        tion has automated and streamlined this "re-interleaving"
        process with a product which was designed specifically to meet
        this need.

        This software product quickly determines the optimal interleave
        setting for any disk of any size in any system with any clock
        rate.  Once determined, the existing interleave of the disk can
        be RESET automatically, and in just a few minutes, leaving all
        your disk data intact and in place!  The product also performs
        several other useful hard disk utility functions which have
        never before been available.



                         GET YOUR DISK SPINNING RIGHT!!

        Even if SPINTEST turned in excellent results of 3 or 4 revs, you
        should STILL check out Gibson Research's new product for the
        other surprising (NEVER before offered) hard disk capabilities
        it brings ... and if you received results like 10, 12, or even
        17, 18, or 19 revolutions, there is NO DOUBT that your system
        could be running FOUR TO FIVE TIMES FASTER ... in minutes!

        To receive all the details about this product simply phone, or
        mail your name and address.  Ask for the INTERLEAVING INFO from
        the On-Line edition of the GUIDE. ... you'll be glad you did!!

                              GIBSON RESEARCH CORP.
                                Box 6024, Dept S
                                Irvine, CA 92716
                                 (714) 854-1520

             (If you're wondering about Gibson Research's first
             product, FlickerFree, ask for some info about it too!)

        ****************************************************************
        *                                                              *
        *               <-- The End ... Of the GUIDE -->               *
        *                                                              *
        ****************************************************************