HOW I ADDED A 1.44MB 3.5 INCH FLOPPY TO MY SYSTEM

         FIRST WHAT I HAD:

         SYSTEM: IBM AT WITH 339 BIOS DATED 11/15/85
                 OLDER BIOS'S WON'T WORK WITHOUT DEVICE DRIVER -
                 339 BIOS HAS 1.44MB SUPPORT.

         FLOPPY: TOSHIBA FDD 4603A0K - OTHER DRIVES MAY NOT HAVE
                 AUTO MEDIA SENSING FOR 1.44/720 MEDIA.
                 ON THE ADAPTER CARD FOR THE RIBBON CABLE
                 THERE IS A JUMPER ON PIN 34. SET IT TO
                 THE "B" POSITION TO ENABLE CHANGE-LINE
                 SUPPORT.
                 ON THE BOTTOM OF THE DRIVE THERE ARE TWO
                 JUMPERS. SET ONE IN THE "B" POSITION AND
                 ONE IN THE "2" POSITION AS SHOWN BELOW

                  A B  DS
                 . ._. .
                 .C. ._. 1
                  D   2

         THE PROBLEM:
                 WHILE THE AT BIOS HAD SUPPORT FOR THE 1.44MB
                 DRIVE, MY SETUP DIDN'T. SO, I WROTE A SMALL
                 PROGRAM CALLED SETUPD TO SET UP JUST THE
                 FLOPPY DRIVES. A 1.44MB DRIVE IS A TYPE 4.
                 SETUPD IS INCLUDED HERE WITH MASM SOURCE.

         USING THE DRIVE:
                 I PLUGGED MINE IN AS DRIVE A: AND USED IBM PC/DOS 3.30.
                 NO DEVICE DRIVERS WERE REQUIRED. TO FORMAT A 1.44MB
                 FLOPPY, READ, WRITE 1.44MB OR 720K DO NOTHING SPECIAL.
                 TO FORMAT A 720KB FLOPPY USE THE FOLLOWING FORMAT
                 COMMAND:

                 FORMAT A: /N:9 /T:80

         DID I DO EVERYTHING RIGHT ?
                 I DON'T KNOW, BUT IT'S PRETTY HARD TO ARGUE WITH
                 SUCCESS. I HAVE HAD NO PROBLEMS AT ALL.

         WILL MS DOS X.X,PC/DOS X.X, ETC. WORK?
                 I DON'T KNOW, I DON'T HAVE THEM TO TEST.