Natural Software
                                19 South 5th. Street
                             St. Charles, Illinois 60174
                                   (312) 377-7320


        This share-ware  utility program:  GEMCAP.COM, allows  you to capture
        screen images  from other  programs, save  them in  separate GEM .IMG
        files, and  later load  them into  other programs  that can read this
        format such as Ventura Publisher. 

        GEMCAP requires an IBM color graphics adapter (CGA) or EGA or compati-
        ble. It will not work with other display adapters such as Hercules.

        GEMCAP is a Terminate and Stay Resident (TSR)  program. When  you run
        it  from  the  DOS  command  line,  it will announce its presence and
        quietly sink into the background and  wait to  be called  into action
        (when  its  "hot  key"  is  pressed).  When  you run GEMCAP, you must
        provide it with the location and starting file  name to  use to store
        the screen  images it  captures. For  example, you might start GEMCAP
        with this command:

                    GEMCAP C:\SCREENS\SCREENA.IMG

        Now GEMCAP will store its screens  in the  SCREENS sub-directory. The
        first screen  it saves will be called SCREENA.IMG, the second will be
        called SCREENB.IMG. Each  subsequent  .IMG  file  will  increment the
        character in  the filename just before the extension. These files are
        graphic bit image files  compatible with  any program  that reads GEM
        .IMG files,  regardless of  whether the  original screen  was in text
        mode or graphics mode.

        To activate GEMCAP and save the  current screen  to a  .IMG file, you
        press the [Alt + left Shift] keys together. You will hear a beep when
        GEMCAP is  called. Three  beeps means  it successfully  wrote an .IMG
        file to the specified directory. Only one beep means it was unable to
        create the file (could not find the directory?). Only two beeps means
        it created  the file, but could not write the full 16k screen buffer,
        (disk full?).

        GEMCAP will  detect the  current video  mode and  adjust. It converts
        text mode screens into bit mapped graphics.

        Like any other TSR, GEMCAP may have compatibility problems with other
        software, especially other TSR's. If you have trouble, try installing
        GEMCAP by  itself and  adding your  other TSR utilities one at a time
        after you get GEMCAP to work.

        Removing GEMCAP:

        You can remove GEMCAP from memory (well, almost) by pressing the [Alt
        + Right  Shift] key  combination. This  disengages GEMCAP  so that it
        will not interfere with other software. This will  also release (most
        of) the  memory used  by GEMCAP.  When loaded and active, GEMCAP uses
        3856 bytes of memory. After removal  with [Alt  + Right  Shift], only
        288 bytes remain allocated. It's probably a good idea to do this only
        at the DOS command prompt!






        Different sized images:

        The size of the captured image is controlled by two words in the .IMG
        file. These are constants  in  the  GEMCAP  program.  The  first word
        specifies  the  pixel  size  in  width, the second word specifies the
        pixel size in height  (unit of  measure is  in microns).  The default
        values are: (in hexidecimal):

          Address        Value        
          0108           00D5 (width), 
          010A           01AA (heigth).

        To make  the displayed image one half the size of the default, change
        these values to


          Address        Value        
          0108           006A (width), 
          010A           00D5 (heigth).

        The steps using Debug to do this are: (you enter the stuff marked ^^)

               DEBUG XYZ.IMG                 (Load the image file)
	       ^^^^^^^^^^^^^
               E 0108                        (enter data at address 0108)
	       ^^^^^^
               XXXX:0108 00.00 D5.6A         (change  00D5   to  006A,  press
                            ^^    ^^           space bar between entries)

               E 010A                        (do the same for address 010a)
	       ^^^^^^
               XXXX:010A 01.00 AA.D5         (change 01AA to 00D5)
			    ^^	  ^^
               W                             (write the changes to the file)
	       ^
               Writing 4020 bytes

               Q                             (return to DOS)
	       ^
        You can experiment with other values. However, some combinations will
        cause truncations of pixels when the image is displayed.

        If you  find a  set of values that work for your application and wish
        to make them the default values for all  captured images,  change the
        corresponding values in the program (GEMCAP.COM) itself. These are at
        address locations 0951 and 0953  (hex)  when  GEMCAP  is  loaded into
        DEBUG.












        ShareWare:

        GEMCAP is  being distributed  as shareware. This means that it is not
        free. This means that you must  pay to  use it.  However, you  do not
        have to pay to try it, test it, and to determine if it is going to be
        useful to you. You  are probably  familiar with  the concept  by now.
        ShareWare programs give you the advantage of "test driving" them. The
        advantage to the developer  is a  relatively inexpensive distribution
        method.  For  this  concept  to  work and keep working for our mutual
        advantage, you really must register  and  pay  for  the  software you
        actually find useful.

        To register  your use  of GEMCAP,  send $20.00 to Natural Software at
        the address above. We  will  send  you  a  description  of  our other
        software offerings and provide telephone support. 

        If you  have suggestions for improvement, or problems please write or
        call.