PC-DUMP.EXE

                 PC Memory Download to Disk File
                       Rev. 2.0  11-23-87


   This program will download the contents of a block of PC system
memory - either RAM or ROM - and write it to a disk file. The byte
image in the disk file is suitable for editing using DEBUG, or for
blasting EPROM's.

   As selected from the options menu, you need to input the memory
segment address, the offset of the end of the memory block that is
to be written to the disk file, the pattern (all, even or odd) of
the bytes that are written to the disk file and the disk file name.
Input prompting and a preset response format will fairly well
confine your responses to acceptable ones.

(F1)  MEMORY SEGMENT ADDRESS :  The four-hexadecimal-digit memory
      segment (or paragraph) address of the beginning of the block
      of memory to be downloaded. This address must conform to the
      20-bit segmented addressing scheme used with the 8088.

(F2)  MEMORY BLOCK END OFFSET :  The four-hexadecimal-digit offset
      address of the end of the memory block that is being written
      to the disk file.  This is essentially one less than the total
      number of bytes in the overall memory block being downloaded,
      since the downloading begins at an offset of &H0000 from the
      memory segment address.  The maximum offset is &HFFFF, for a
      total memory block size of 64K bytes.

(F3)  DISK FILE NAME :  The filespec of the disk file in which the
      memory block contents will be written. The filespec should
      follow the DOS convention (d:filename.ext) for format.

(F4)  BYTES WRITTEN TO FILE :  Within the designated memory block
      you may select the pattern of bytes to be written to the disk
      file.  The default is to write all bytes.  To facilitate work
      with interlaced address ROMs, options are available to write
      only the even or odd numbered bytes to the disk file.  Note
      that pressing F4 rolls the option stack: no other keyboard
      entry is necessary.

   When you input the hexadecimal data for the memory segment
address and the memory block edd offset, PC-DUMP routines will
collect the input characters one at a time and display them in the
preset range. Upon receiving four characters, the program will put
the full hexadecimal number in the status line and return control
to the options menu. If you make a mistake during entry of these
data items, go ahead and input four characters and come back and
try again. Also, you should note that this program rigidly checks
for allowable keystrokes (the disk filespec is the one exception).

   EXAMPLE #1

       MEMORY SEGMENT ADDRESS (4 hex digits) = FE00
       MEMORY BLOCK END OFFSET (4 hex digits) = 1FFF
       DISK FILENAME (d:filename.ext) = A:ROMBIOS.DAT
       BYTES WRITTEN TO FILE = ALL

   The input shown above would download an 8K (8,192 bytes) block
of memory, beginning at segment address FE00(hex), to a disk file
on the A: disk drive.  All bytes in the indicated block are written
to the file.

   EXAMPLE #2

       MEMORY SEGMENT ADDRESS (4 hex digits) = F000
       MEMORY BLOCK END OFFSET (4 hex digits) = FFFF
       DISK FILENAME (d:filename.ext) = A:ATROM_LO.DAT
       BYTES WRITTEN TO FILE = EVEN

   The input shown above would download 32K (32,768) bytes making
up the even numbered (offsets 0, 2, 4, 6 ...) bytes in the 64K block
of memory, beginning at segment address F000(hex), to a disk file
on the A: disk drive.  This data is typical of the low-byte ROM in
the interlaced address ROMs of the PC-AT.




Rev 1 (docs)
TAM 11/23/87