3/5/92        Asynchronous Communications Eavesdropper        Page 1


     
                                 Version 2.0
     
                    Copyright (c) 1991,1992  Nick Jancewicz
                        P.O. Box 3491, Boulder CO 80307
     
     
     The Asynchronous Communications Eavesdropper (ACE) is intended for
     personal use and may be freely copied and distributed as long as it
     is not done for profit.  The author makes no warranties of any kind
     relating to this software and assumes no liabilty regarding its use.
     
     *************************************************************************
     
     Requirements:
     
     * ACE software
     * IBM-compatable PC with two serial ports (configured as COM1 and COM2)
     * DOS 2.1 or later with ANSI.SYS driver installed in the CONFIG.SYS file
     
     *************************************************************************
     
     ACE is a software utility that turns any IBM PC compatable equipped
     with two serial ports into a versatile serial communications monitor.
     It can display and capture to disk an both data streams between
     two devices operating in full-duplex mode.  ACE "eavesdrops" on both
     sides of a "conversation" between two serial devices with the aid of a
     special cable which taps into the wires over which the two devices
     communicate.  It thus provides an objective, "third-party" view of the
     data transmitted between the two serial devices and, in the event of
     communications difficulties, enables you to ascertain what went wrong
     and to identify which device is at fault.
     
     The characters transmitted by one device are displayed in regular video
     (white characters on black background) while the other device's
     transmissions are displayed in reverse video (black characters on
     white background).  Thus, the relative character order and timing are
     clearly distinguished.  As the data streams are displayed, an exact
     record can also be captured to a disk file for later inspection and
     analysis.  To switch between the regular and reverse video display
     attributes, ACE uses special ANSI escape sequences.  This requires
     that you have the standard DOS ANSI.SYS device driver installed on the
     host PC. This is done by inserting the line, "DEVICE=C:\DOS\ANSI.SYS"
     (or a similar line instructing DOS where on your disk the ANSI.SYS
     file can be found) in your config.sys file.  Alternatively, (or in
     addition) you may use the "dte" and "dce" command line parameters to
     label each device's transmissions and so distinguish them in that
     manner (see NOANSI.BAT under Miscellaneous Utilities below).
     
     A simple 3-way Data Tap (or Data Tee) is often used for the same
     purpose, but has the inherent problem of mixing transmissions from
     both devices on the same conductor so that when both devices transmit
     at the same time the results will be garbled.  In Boolean terminology
     this is known as a "Wired-OR" circuit because the two signals (i.e.
     the serialized characters) are logically ORed together by a
     double-diode circuit.  This is inappropriate for monitoring
     full-duplex communications, that is, where both serial devices can



     3/5/92        Asynchronous Communications Eavesdropper        Page 2


     transmit at the same time.  In most serial communication protocols,
     full-duplex is the rule rather than the exeception.  In debugging full
     duplex protocols, it is important to know which device transmitted
     first and in what order relative to the transmissions of the other
     device.  ACE, when used on a PC with two serial ports (COM1 and COM2),
     keeps the two signals separate from each other by a special cable
     which routes the transmissions from one device to the COM1 port and
     the transmissions from the other device to the COM2 port.
     
     Even in situations where only one COM port is available and a Data Tee
     must be used, monitoring with ACE still offers some advantages over
     using a modem communications utility.  Such general-purpose
     communications programs were never intended for monitoring binary
     communications and hence lack the ability to display (in a meaningful
     way) either binary transmissions or the "non-displayable" characters
     that are often intermixed with normal ASCII text.  Many modem
     utilities cannot capture an accurate recording of a communications
     session to disk due to the fact that they completely ignore nulls in
     the data stream.  Even worse, they also ignore parity errors, framing
     errors and break errors which are critical to detecting problems in
     transmission line quality and/or incompatible communications parameter
     settings between the serial devices under test.  When a parity,
     framing and/or break error occurs, ACE beeps and displays an error
     message.
     
     All of the parameters which ACE needs in order to monitor a serial
     communications session are supplied as command line options when you
     invoke it at the DOS prompt.  This makes it easy to set up batch files
     for monitoring various devices with different protocols and
     communications parameters (see the examples under Miscellaneous
     Utilities below).  Typing "ACE" by itself at the DOS command prompt
     results in a brief help screen being displayed which gives a summary
     of the required options and their respective order.  Most of these are
     self explanatory, i.e. baud rate, parity, number of data bits, and
     number of stop bits.  The command line usage is:
     
     ace baud parity data stop format [dte=s] [dce=s] [log=n] [-t] [-f] [file]
     
     where,
     baud      is the baudrate: 50,75,110,134.5,150,300,600,1200,1800,
               2000,2400,3600,4800,7200,9600,19200,38400 or 115200
     parity    is N,O,E,M or S for none, odd, even, mark or space parity
     data      is the number of data bits: 5,6,7 or 8
     stop      is the number of stop bits: 1 or 2
     format    is H to show non-displayable characters in ASCII Hex format,
               or N to show all characters in native format,
               or A to show all characters in ASCII Hex format
     file      is filename for logging session
     -t        enables timestamping of each transmission
     dte=s     specifies optional label to identify which is DTE
     dce=s     specifies optional label to identify which is DCE
               ("s" is a string which may contain backslash-prefixed
               ASCII Hex values, e.g. "\0D\0A")
     log=n     selects alternating log files and sets their max size to n bytes
     -f        selects fast display format
     
     The parameters shown in brackets are optional.
     



     3/5/92        Asynchronous Communications Eavesdropper        Page 3


     ACE has three possible display options for monitoring binary or mixed
     binary and ASCII text communications.  With the "H" option,
     non-displayable characters are converted to a readable format
     consisting of a backslash character followed by the two ASCII-hex
     digits representing the binary value for the character.  With the "N"
     option, all characters are displayed in "native" form i.e. if
     character codes below 20 hex or above 7F hex are encountered they will
     appear as special IBM graphics characters, producing an effect similar
     to what you see when you dump a binary file (e.g. an executable) to
     the screen with DOS's TYPE command.  The third option, "A", displays
     all characters in ASCII-hex.  This latter option is useful when
     monitoring binary protocols.
     
     There are several optional command line parameters which allow you to
     make the session more readable, i.e. the "dte" and "dce" options.
     These allow you to specify identifier strings to distinguish between
     the two devices being monitored which ACE will insert into the data
     stream as it is captured.  These strings may include binary values
     such as Carriage Returns and Line Feeds which are specified by
     "backslash escape sequences", e.g.  "\0D" and "\0A", respectively.
     You may also instruct ACE to insert a timestamp each time the data
     stream changes from one device to the other by including the "-t"
     command line option.
     
     The "log=n" option is useful for capturing long duration sessions to
     disk.  If used, this option will cause ACE to initially start
     capturing the session to a file called "log1".  When the size of the
     file nearly reaches the number of bytes specified by "n", the first
     file will be closed and ACE will start capturing to a second file
     called "log2".  When "log2" reaches the specified size, ACE will
     switch back to "log1" again.  This keeps your disk from filling up,
     which can happen in a very short time if you are dealing with a high
     communications throughput application.
     
     The "-f" option is for monitoring very high speed communications (e.g.
     115200 baud) or for monitoring with slower, XT class PCs. Most users
     will never need to use this option, but it is described here for the
     benefit of Dedicated Hacker types.  The "-f" option greatly reduces
     the overhead of displaying the data stream(s), by displaying just one
     character at a time from each port (by writing directly to the EGA
     video RAM).  You will want to specify a filename as the last command
     line parameter whenever this option is used so that ACE will dump the
     contents of its communication buffer to the specified file upon
     terminating.  This option is a bit of a kludge, but it does let you
     save the last 28,000 or so bytes that were received.  Note that the
     file is a BINARY IMAGE of ACE's communications buffer, regardless of
     the display format that was selected.  Each element in the buffer is
     two bytes, where the high byte encodes the UART status (refer to 8250
     data sheets for details) and the low byte is the received character.
     The first two bytes are the oldest character and its status and the
     last two bytes are for the most recent character received.  This file
     can be viewed with DOS's DEBUG or a binary file dump utility.
     
     The last command line option may be omitted but if present, specifies
     the name of a file for recording the communications session.  If the
     file already exists, ACE will append the current session to it
     otherwise a new file will be created.  Note that this option may not
     be used if the "log=n" option is used (they are mutually exclusive).



     3/5/92        Asynchronous Communications Eavesdropper        Page 4


     
     To terminate a communications session with ACE, press the Esc (escape)
     key at any time.
     
     RS-422 or RS-485 signals can be monitored through RS-232C COM1 and
     COM2 ports by connecting only the "negative" side (i.e. the one marked
     "-" or "B") of each differential pair.  However, like the Data Tee's
     double-diode trick, this is not guaranteed to work with all RS-232C
     receivers.  In my experience I have only ever encountered one COM port
     which would not work with the above technique.  Oddly enough it was an
     early model IBM Asynchronous Communications Adapter Card and it did
     NOT use the ubiquitous MC1489 RS-232C driver chip found on most other
     serial cards.
     
     *************************************************************************
     
     ACE Cable
     
     Although no special hardware is required for the host PC (aside from
     the two serial port adapters configured as COM1 and COM2) a special
     cable is required which allows the host PC to "tap" into the
     connections between the two DUTs (Devices Under Test).  One end of
     this cable connects "in-line" with the DUT while the other end
     connects to the two COM ports on the host PC. See Figure 1 below.
     
     The cable may consist of an RS-232C "patchbox" (similar in appearance
     to a "null modem" adapter, but containing a printed circuit board with
     a dual row of solder pads for soldering jumpers to establish custom
     interconnections between the two DB-25 connectors at either end) and
     two cables (or one cable with two DB connectors attached at the
     opposite end).
     
     The basic idea is to connect one cable in parallel with the DUT's TXD
     line and the other cable in parallel with the DUT's RXD line of the
     cable connecting the two devices to be monitored.  Each cable connects
     to one of the two serial ports (COM1 and COM2) in the PC which serves
     as the ACE monitor.  Thus, the RXD line of the DUT connects to the RXD
     input of COM1, and the TXD line connects to the RXD input of COM2.
     
     This approach should work with just about any device which has a fully
     compliant RS-232C interface, since the DUT is only subjected to one
     additional RS-232C electrical load by the parallel connection.  This
     is easily handled by a true RS-232C driver.
     
     On a typical RS-232C patchbox, you will need to solder in place
     jumpers for all of the signals used by the DUT. Most often, this
     requires only pins 2 (TXD), 3 (RXD) and 7 (Signal Ground) but for a
     deluxe, "do all, end all" cable you will want to connect pins 2, 3, 4,
     5, 6, 7, 8, 20 and 22 straight through.  The next step is to connect
     the cable(s) which "tap" into TXD, RXD and SG conductors in the
     patchbox and carry their respective signals to the two COM ports on
     the host PC. The approach I prefer is to use one cable on the patchbox
     end and then splice two shorter cables onto the end that connects to
     the host.  Two DB-25 connectors (or two DB-9s) can be used for the
     host end but I've found that most AT- compatable PCs typically have a
     DB-9 for COM1 and a DB-25 for COM2 so I usually use that combination.
     Note that the pin numbering and signal assignments for a DB-9 differs
     from that of the standard DB-25 connector as shown in Table 1.



     3/5/92        Asynchronous Communications Eavesdropper        Page 5


     
     
     Figure 1: ACE Cable
     
     
                     PC:  COM1      COM2
                         (DB-9)    (DB-25)
                          2  5      3  7
                          ^  |      ^  |
                          |  |      |  |
                          |  |      |  |
       DTE                |  |      |  |                     DCE
     (DB-25)              |  |      |  |                   (DB-25)
        2 ----------------*--|------|--|--------------------> 2
        3 <------------------|------*--|--------------------- 3
        7 -------------------*---------*--------------------- 7
     
     
     DTE (Data Terminal Equipment) and DCE (Data Communications Equipment)
     are the EIA's terminology (somewhat archaic) for the devices that
     transmit on pin 2 and pin 3, respectively.
     
     *************************************************************************
     
     Table 1: RS-232C Signals and Connector Pinouts
     
     Signal  DB-9    DB-25   Function             DTE  DCE
     ------  ----    -----   ------------------   ---  ---
     TXD     3       2       Transmit Data         O    I
     RXD     2       3       Receive Data          I    O
     RTS     7       4       Request To Send       O    I
     CTS     8       5       Clear To Send         I    O
     DSR     6       6       Data Set Ready        I    O
     SG      5       7       Signal Ground         -    -
     DCD     1       8       Data Carrier Detect   I    O
     DTR     4       20      Data Terminal Ready   O    I
     RI      9       22      Ring Indicator        I    O
     
     Note: I = Input, O = Output
     
     *************************************************************************
     
     Miscellaneous Utilities
     
     There are some additional utilities which can be used with ACE to
     modify captured session files in various ways.  These are mainly
     useful for converting captured session files into a printable format
     (for hardcopy output on a printer) although some of them have other
     uses as well.
     
     ACE12.BAT - demonstrates how to invoke ACE from a DOS batch file to
     monitor at 1200 baud, no parity, 8 data bits, 1 stop bit, with ASCII
     Hex display mode and capture to a session file called "test1".
     
     NOANSI.BAT - demonstrates how to use ACE on a PC without ANSI.SYS.  It
     invokes ace.exe at 1200 baud, no parity, 8 data bits, 1 stop bit, with
     ASCII Hex display mode, displays DTE data stream on a newline with
     "DTE: ", displays DCE data stream on a newline with "DCE: ", and



     3/5/92        Asynchronous Communications Eavesdropper        Page 6


     captures to a session file called "test2".
     
     FILT.EXE - filters a file (or the standard input device), by replacing
     any arbitrary sequence of bytes into a different sequence of bytes.
     This is like a global "search and replace" command except that it
     works on binary files and strings as well as standard ASCII.
     
     H2B.EXE - filters a file (or the standard input device), converting
     any ACE style backslash escape sequences into their binary equivalents
     (e.g. the displayable ASCII sequence "\02\04" gets converted into two
     binary bytes: 02, 04 or STX, EOT).  This utility is also handy for
     sending arbitrary byte streams to devices such as printers and
     plotters, e.g. escape sequences for printer initialization.
     
     ELITE.BAT - an example of how H2B.EXE can be used for initializing a
     printer.
     
     SLICE.EXE - divides a huge file into more manageble pieces.  Most text
     editors can't deal very effectively with multi-megabyte files
     (especially ones containing arbitrary binary sequences) so this
     utility can be used to break up a very large session file into smaller
     chunks which can then be processed more conveniently.
     
     SES2DOC.BAT - uses filt.exe to convert a session file captured without
     the dte and dce command line options into an editable document file.
     It replaces the ANSI escape sequences for reverse and regular video
     attributes with ASCII labels to identify which device transmitted
     what.