{COMMO} 5.3 Addendum
                            ____________________

     This Addendum contains the major additions and/or changes to the
     {COMMO} 5.2 documentation.  Print out this file and keep it with
     your printed manual.


     ===============================
     In the User Guide and Reference
     ===============================


     Under "Command Line Options"
     ----------------------------

     /vnnnnn        Size of String Variable Space.

          The size of String Variable Space can be adjusted from 512
          bytes to 65535 bytes.  The default is 1536 bytes.  Example:
          /v3000 will set the size to 3000 bytes.


     Setup File changes/additions
     ----------------------------

     _________________________________________________________

     {sld=no}       Stop serial input during disk I/O (yes/no)
     _________________________________________________________

          This should be set to "yes" if your system drops characters
          when a disk (hard or floppy) is accessed.  The symptoms are
          missing characters in the Terminal Screen when capture is on
          or excessive CRC/csum errors during internal protocol file
          transfers.

          This is equivalent to what some programs call "handshake
          slow."  In {COMMO} it works in conjunction with Hardware
          Flow Control (RTS/CTS), so both {COMMO} and your modem must
          have Hardware Flow Control engaged.

          If you use an external protocol driver be sure to set the
          "handshake slow" parameter in that program as well.




     _________________________________________

     {com=1,3f8,4}       Com1 port address/IRQ
     {com=2,2f8,3}       Com2 port address/IRQ
     {com=3,3e8,4}       Com3 port address/IRQ
     {com=4,2e8,3}       Com4 port address/IRQ
     _________________________________________

          These are the hardware serial port base address and IRQ
          assignments.  The settings shown are the most common, but
          some serial adapters are different.  The serial adapter
          manual may give a range of addresses, for example "3f8-3ff." 
          Use the first value as the base address.

          Port addresses are in hexadecimal and may range from 0 to
          ffff.  IRQ numbers are decimal and may range from 0 to 15
          (avoid use of IRQ numbers that are used by system hardware,
          e.g., 0, 1, 8, etc.).  IRQ numbers from 8 to 15 are
          available only on AT class machines.

     ____________________________________________________

     {set _dialsr,CONNECT}    Dialing success response(s)
     {set _dialfr,BUSY,NO CARRIER,NO DIALTONE}
                              Dialing failure response(s) 
     {set _dialir,RING}       Inter-dial response(s)          
     ____________________________________________________

          These reserved variables each define a list of response
          strings that are returned by your modem during dialing
          operations.  Most "Hayes compatible" modems use similar
          responses, but there may be subtle differences.  Consult
          your modem manual for details.

          "Success" responses are received when the modem has
          connected with a remote modem.  "Failure" responses occur
          when the number being called is busy, doesn't answer or when
          something is wrong with the telephone line.  {COMMO} will
          automatically redial the number after a failed attempt.

          Inter-dial Delay responses may occur during the delay
          between dialing attempts, usually when someone is trying to
          call you.  These may be handled by using the Inter-dial
          Delay macro label in the DIAL macro function.  See the Macro
          Programming Guide for details.

          Some modems use a CARRIER response to indicate the modem
          speed, e.g. CARRIER 2400.  In this case using CARRIER
          instead of CONNECT will improve the accuracy of the Usage
          Log.  In order to avoid confusion with a NO CARRIER
          response, you should use:

           {set _dialsr,CARRIER }    Notice the space after CARRIER.




          Do not include the speed in the CONNECT or CARRIER response
          if you are enabling AutoBaud.

          Responses are case sensitive and there should be no null
          strings or extra spaces.

     _____________________________________________

     {swp=}         Pathname for Swap to Disk File
     _____________________________________________

          This file will be used to save the program and data during a
          Swap to Disk.  You may optionally Swap to Disk when using
          the Shell to DOS key command or the EXECute macro function.

          It's a good idea to use a unique filename.  For example:

               {swp=c:\commo\swapfile.$$$}

          IMPORTANT:  You must also specify the "S" switch on any
          EXECute or SHELl macro functions where swapping is desired.

          Before using this feature, read the section "Using the Swap
          to Disk switch, EXEC-S" under EXECute in the Macro
          Programming Guide.

     ______________________________________________________________

     {dat=mdy}      Order of date parameters (m=month,d=day,y=year)
     ______________________________________________________________

          This item allows you to specify any order for the three date
          parameters.  The default shown would display May 20, 1992 as
          05/20/92.  "ymd" would display as 92/05/20.

          This format will appear in the Date Last Called field of the
          Dialing Directory, the Usage Log and the built-in variable
          "_dat".

     _______________________________________

     {tim=12}       Time format (12/24 hour)
     _______________________________________

          You can specify 12 or 24 hour time format.  12 hour will add
          "am" or "pm" as in "2:30 pm".  24 hour would show the same
          time as "14:30".

          The time format appears on the Status Line, in the Usage Log
          and in the built-in variable "_tim".




     _________________________________________

     {gdc=}         Graphic display characters
     _________________________________________

          This item allows you to specify the graphic characters used
          by {COMMO} to form the various display windows and is
          provided for compatibility with display adapters used in
          certain countries.

          When using this item, eleven ASCII character codes may be
          listed (omitted fields will revert to the defaults).  Codes
          are specified as decimal numbers from 1 to 255 (0, 10 and 13
          are not allowed).

          As an example, here is how the default characters would be
          listed:

               {gdc=213,184,212,190,205,179,185,204,176,250,177}

          where:

                    213 = upper left box corner
                    184 = upper right box corner
                    212 = lower left box corner
                    190 = lower right box corner
                    205 = horizontal line
                    179 = vertical line
                    185 = left side of box title
                    204 = right side of box title
                    176 = file window title fill
                    250 = input fill and password hiding
                    177 = Online Help separator bar

     Under "Uploading/Downloading"
     -----------------------------

     When you press PgUp or PgDn you will be presented with a menu
     from which you may select a file transfer protocol.  Protocols
     provide the ability to transfer (send and receive) any type of
     data using error detection and correction techniques.

     The PgUp and PgDn menus are implemented using {COMMO}'s powerful
     Macro Processor which enables you to execute internal and
     external protocols easily and seamlessly.  You may alter these
     macros to suit your individual needs.


     Internal Protocols
     ==================

     {COMMO} provides a number of variations on the Xmodem and Ymodem
     protocols which afford you varying degrees of convenience, speed
     and security.




     Xmodem is the most basic protocol, sending data one block at a
     time and waiting for a response to each block.  If the block was
     received with errors, the receiver requests retransmission.  A
     filename must be supplied at both ends of the transfer (they need
     not be the same).

     Ymodem adds the capability of batch (multi-file) transfers.  It
     also sends the name and size of each file just prior to
     transmission of the file (the receiver does not supply any
     filenames).

     NOTE:  If an incoming filename matches an existing filename in
     the target directory, the batch transfer will be cancelled.  You
     can force overwriting of like-named files by adding the "Y"
     switch to the Ymodem macros.

     There are a number of variations which apply to both Xmodem and
     Ymodem.  You should choose the best variations depending upon
     which protocols are offered by the remote system you are calling
     (and whether or not you have an error-correcting modem).

          CRC       This is a very reliable block-check method and
                    should be used whenever possible.

          Csum      This block-check method is not as reliable and
                    should not be used unless there is no other
                    option.

          1k byte block size       The larger block size is much more
                                   efficient and is preferred unless
                                   noisy lines are causing a lot of
                                   block retransmissions.

          128 byte block size      The small block size should be used
                                   only when there is no other option
                                   or on noisy lines.

          G         The "G" method eliminates the receiver's response
                    to each block and is much faster.  It still
                    performs error checking, but not error recovery. 
                    Therefore it should only be used with an error-
                    correcting modem or on a direct connection between
                    computers.

                    When an error is encountered, the transfer will be
                    cancelled.  Partial files will be kept.  The "G"
                    method always uses CRC and 1k blocks.

                    Software (XON/XOFF) Flow Control may be required
                    by some remote systems and/or public networks.  If
                    you get frequent errors when using the "G" method,
                    make sure Software Flow Control is on.

     IMPORTANT:  The macros that support the internal protocols are
     set up for the most common situations.  Many variations are




     possible by modifying these macros.  Please refer to descriptions
     of the functions RXMOdem, RYMOdem, SXMOdem and SYMOdem in the
     Macro Programming Guide for details.




     ==============================
     In the Macro Programming Guide
     ==============================


     A Macro Example in Detail
     =========================

     The following macro example from SAMPLES.MAC can be used to log
     in to many types of Bulletin Board Systems.  This is a Linked
     Macro, so the label "login" would appear in the Dialing Directory
     macro field for each system that uses it.  When you dial and
     connect to one of the systems, {COMMO} will automatically GOTO
     the macro.

     The subroutine "gls" (generic login subroutine) can also be
     called from macros that perform mailruns and other BBS
     operations.

     Note that labels and functions may be placed side by side on the
     same line (up to 255 characters).  For purposes of this example
     each item is placed on its own line.

     The main routine at "login" performs some initial functions and
     then calls the subroutine at "gls".  The subroutine looks for
     various prompts, responds to them and terminates after responding
     to the "password" prompt.


     {:login}

               The entry point.  All labels begin with a ":".

          {capture y,c:\commo\commo.cap}

               "y" means open the Capture File.  The pathname of the
               file is specified here, otherwise the current file
               would be opened.

          {asci ,}

               Set ASCII Upload to "no pacing."

          {call gls}

               CALL the macro at "gls".  When the subroutine executes
               a RETUrn, control will come back here.

          {}

               STOP and resume manual operation in the Terminal
               Screen.  Without this STOP processing would continue
               into subsequent macros.  Remember that labels are
               "passed over" during sequential macro processing.




     {:gls}

               The entry point of the "gls" subroutine.

          {setlook 60,hng,10,|}

               This function specifies parameters that go into effect
               whenever a LOOKfor executes.  It tells the Macro
               Processor to wait up 60 seconds for the string (or
               strings) and to GOTO the label "hng" if none of the
               strings appear within that time.  The timer is
               restarted each time a LOOKfor begins to execute.

               The SETLook also specifies that a "|" (carriage return)
               should be sent to the modem whenever 10 seconds have
               elapsed and no characters are received.  This is used
               to respond to prompts that are not explicitly specified
               in CALOoks, LOOKfors, etc. (e.g., "Press any key to
               continue").

               Use this latter facility with care since a BBS may
               spend time processing and not actually be expecting
               input from the caller.  The carriage returns sent will
               accumulate and be used to satisfy later prompts,
               causing things to get out of "sync."  Adjust the 10
               second timeout as needed.

     {:li1}
          {calo li1,li2,(enter)}

               The CALOok remembers a string to look for, but does not
               wait for the string (only a LOOKfor can do the actual
               waiting).  In this case the string "(enter)" is
               remembered.  The label "li2" is the macro to be CALLed
               when the string appears.  "li1" is the label to return
               to when the macro executes a RETUrn.

               When any of the remembered strings appear, the strings
               are all "forgotten."  Thus the CALOok is told to return
               to "li1" where all the strings can be set up again.

          {calo li1,li3,graphics (enter)}
          {calo li1,li4,first name}
          {calo li1,li5,last name}
          {calo li1,li3,is this correct}

               More CALOoks are used to set up more strings to look
               for.

          {golo li1,;passwor}

               A GOLOok will set up a string and GOTO the label if the
               string appears (only one label is used here).  In this
               example the specified string is to be ignored.  This
               was needed for a BBS that used the string




               "first;last;password" prior to the actual password
               prompt.

          {lookfor password}

               This is where the actual "looking" takes place. 
               Remember that CALOoks and GOLOoks only cause strings to
               be remembered but do not actually wait for the strings.

               The LOOKfor will wait for the string specified and also
               any other remembered strings (up to 16 total).  If the
               string in the LOOKfor appears, control passes to the
               next macro function.  All strings are "forgotten" when
               any one of them appears, or if the LOOKfor timer
               expires.

               "password" is assumed to be the last prompt in the
               login sequence.  

          {send ~%_pas|}

               Control then passes here and the string is sent to the
               modem.  The tilde (~) causes a half-second delay before
               sending the password.  The password in the Dialing
               Directory entry was stored into the built-in variable
               "_pas" when dialing began.

               Finally, a carriage return (|) is sent.

          {return}

               This will RETUrn to the "login" macro.

     {:li2}
          {send ~|}

               If a prompt requires a carriage return (|) to be sent,
               the CALOok would set up to come here.

          {return}

               The return point ("li1") was the first argument of the
               CALOok, so control returns there.

     {:li3}
          {send ~y|}

               This is used to reply to prompts that are to be
               answered with "y<cr>".

          {return}

     {:li4}
          {send ~Fred|}




               Response to "first name".

          {return}

     {:li5}
          {send ~Brucker|}

               Response to "last name".

          {return}


     ------------------------------------
     New or changed function descriptions
     ------------------------------------

     _________

     DECRement
     _________

     Default key:   none
     Description:   Subtract a number from a numeric variable.

     Examples:

          {decr count}        Subtract 1 from the variable "count".
          {decr apples,200}   Subtract 200 from "apples".

     Numeric variables and the numbers to be subtracted may range from
     0 to 65535.  The default number is 1.

     If the result is less than 0 or if either argument is out of
     range, then the variable will be set to the string "ERROR".

     If the variable is not numeric, the results will be
     unpredictable.

     See also INCRement.

     ____

     DIAL
     ____

     Default keys:  Alt-D, Alt-N
     Description:   Open Dialing Directory, dial marked systems.

     General form:

          {DIAL tries,label1,label2}

               tries     The maximum number of dialing tries.  If no
                         connection is established when the try count
                         is exhausted, the macro in the second




                         argument will be started.  May be 0 to 999. 
                         "0" means unlimited.  Default is 0.

               label1    A macro to GOTO if the try count in the first
                         argument is exhausted.  If no macro is
                         specified or if the macro label is invalid,
                         control will pass to the next function. 
                         Default is none.

                         If the "C" switch is used, the macro will be
                         CALLed.  When a RETUrn is executed, control
                         will return to the DIAL function.

               label2    A macro to GOTO when a response is matched
                         during the Inter-dial Delay.  Response
                         strings are listed in the reserved variable
                         "_dialir" and are usually defined in the
                         Setup File.

                         If the "C" switch is used, the macro will be
                         CALLed.  When a RETUrn is executed, control
                         will return to the DIAL function.

     Switches:

               C1 or C   Specifies that macros will be started via
                         CALL (instead of GOTO).  When the macros
                         execute a RETUrn, control returns to the DIAL
                         function and Multi Number Dialing will
                         resume.

                         The "C" switch applies to the Linked Macro
                         (from the Dialing Directory), the "tries
                         exhausted" macro and to the Inter-dial Delay
                         macro.

               C0        Start dialing macros via GOTO (default).

     Examples:

          {dial}              Open Dialing Directory window (similar
                              to Alt-D).

          {dial ,}            Multi Number Dial (similar to Alt-N).

          {dial 25,abc}       Multi Number Dial with try count.

          {dial-C ,}          Multi Number Dial, CALL Linked Macros.

          {dial-c ,,inter}    Multi Number Dial with Inter-dial Delay
                              macro.




     Marking Numbers for Dialing
     ---------------------------

     Numbers may be marked in one of several ways:

          1)   Manually in the Dialing Directory window.
          2)   By placing Dialing Strings on the {COMMO} command line.
          3)   Using the MARK macro function.

     Marked numbers will be redialed in sequence.  If a connection
     occurs and a valid Linked Macro is specified in the Dialing
     Directory, the macro will be started via GOTO (unless the "C"
     switch is present).  If no macro is specified in the Dialing
     Directory, control is passed to the next function.

     If no numbers are marked when executing the DIAL, control will
     pass to the next function.


     Automatic Resumption of Dialing
     -------------------------------

     Here are two methods for resuming at the end of a Linked Macro. 
     Both allow multiple systems to be called without operator
     intervention.

          1)   Use the "C" switch on the DIAL function.  Each Linked
               Macro should end with a RETUrn which will transfer
               control back to the DIAL.  When all numbers have been
               called, control will pass to the function following the
               DIAL.

          2)   At the end of each Linked Macro (after logging off),
               GOTO a macro such as this:

                    {:nocar} {pause 1} {ifcarrier nocar} {dial ,} {}

               This ensures that carrier has dropped before DIALing
               the next number.  The PAUSe allows data to display on
               the screen while waiting for carrier to drop.


     Testing Success and Failure Results
     -----------------------------------

     Details about a successful or failed dialing attempt are
     available in several reserved variables (see Appendix B "List of
     Reserved Variables" for complete descriptions):

          _dtc      Dialing termination code
          _dialrt   Dialing response text
          _mod      Speed reported by modem (normally in the CONNECT
                    or CARRIER response)




     After a successful attempt the variables "_dialrt" and "_mod" may
     be tested in your Linked Macro.  For example, if you expected a
     high-speed connect and the speed reported was 2400 or 1200, then
     you may want to hang up and try again later.

     You can get control after each failed attempt by using "DIAL 1",
     with or without a macro.  For example:

          1)   {dial-c 1,nocon} ...

               The Linked Macro and the "no connect" macro will be
               CALLed (the "C" switch).  The variables "_dtc" and
               "_dialrt" may be tested in the macro at "nocon".

          2)   {dial 1} ...

               Control will pass to the next function if a dialing
               attempt fails or when no more systems are marked (test
               "_dtc" to determine which).

     If the testing indicates that the system should not be dialed
     again (e.g., it did not answer, _dtc = 3), the UNMArk function
     can be used with the "L" switch to unmark the last number dialed:
     {unmark-l}.


     Handling Incoming Calls
     -----------------------

     Most modems return the string "RING" when a call comes in.  If
     this happens during the Inter-dial Delay, you may choose to stop
     dialing (to answer a voice call) or to send a brief message to a
     modem caller (during a BBS event, for example).

     Use "label2" on the DIAL function to process responses during the
     Inter-dial Delay.  For example:

          {dial ,,incoming}

     The macro at "incoming" will execute if the modem sends an Inter-
     dial Delay response string. 

     See also: SETDial, MARK, UNMArk.

     ______

     DIVIde
     ______

     Default key:   none
     Description:   Divide a numeric variable by a number.

     Example:

          {divi space,1024}        Divide "space" by 1024.





     Numeric variables may range from 0 to 65535, the divisors may
     range from 1 to 65535.  The default divisor is 1.

     The named variable will be set to the quotient, the built-in
     variable "_rem" will be set to the remainder.

     If the divisor is zero or if either argument is out of range,
     then the variable will be set to the string "ERROR".

     If the variable is not numeric, the results will be
     unpredictable.

     _______

     EXECute   (excerpts pertaining to Swap to Disk)
     _______

     Default key:   none
     Description:   Execute a DOS command.

     Switches:

               S1 or S   Swap to Disk before executing the program
                         (see details below).

               S0        Do not swap to disk (default).


     Using the Swap to Disk Switch: EXEC-S
     -------------------------------------

     The "S" switch will direct {COMMO} to write the program and
     associated data to the disk file specified with the Setup File
     item "swp=" (under "Paths and Files").  This will free up between
     50k and 180k of memory, depending on the sizes of your Scrollback
     Buffer, Dialing Directory and Macro File.

     If the Swap File cannot be opened or there is not enough disk
     space for the swap, the EXECute (or SHELl) will be attempted
     without swapping.  When the program or shell exits back to
     {COMMO}, the program and data will be restored from the disk
     file.  Any errors in this process will cause {COMMO} to exit to
     DOS.

     TIPS on using Swap to Disk:

     >    The serial port will be closed during the swap (normally it
          is left open to receive characters during EXECute and
          SHELl).  To avoid losing any data swapping should be
          initiated when the remote system is quiet (or when you are
          offline).

     >    Use Swap to Disk when running major applications such as
          external protocol drivers, offline mail readers, etc.  Using




          it with internal DOS functions (DEL, COPY, REN, etc.) or
          very small programs is inefficient and unnecessary.

     >    If possible, specify the Swap File on a RAMDISK.  This will
          speed up the swap considerably.  A ramdisk program is
          supplied with DOS (RAMDRIVE.SYS or VDISK.SYS) or you can
          obtain one from a BBS.

     >    Be sure to specify a complete pathname for the Swap File.

     >    Do not run any TSR (resident) programs when swapping is in
          effect.  Doing so may result in a swap error.

     _________

     INCRement
     _________

     Default key:   none
     Description:   Add a number to a numeric variable.

     Examples:

          {incr count}             Add 1 to the variable "count".
          {incr oranges,1234}      Add 1234 to "oranges".

     Numeric variables and the numbers to be added may range from 0 to
     65535.  The default number is 1.

     If the result is greater than 65535 or if either argument is out
     of range, then the variable will be set to the string "ERROR".

     If the variable is not numeric, the results will be
     unpredictable.

     See also DECRement.

     ________

     MULTiply
     ________

     Default key:   none
     Description:   Multiply a numeric variable by a number.

     Example:

          {mult money,10}          Multiply "money" by 10.

     Numeric variables and the multipliers may range from 0 to 65535. 
     The default multiplier is 1.

     If the result is greater than 65535 or if either argument is out
     of range, then the variable will be set to the string "ERROR".




     If the variable is not numeric, the results will be
     unpredictable.

     _______

     RXMOdem
     _______

     Default key:   none
     Description:   Receive a file using the Xmodem protocol.

     Switches:

               See RYMOdem (switches are the same).

     Example:

          {rxmo-ya c:\dl\file.zip}      Receive "file.zip", overwrite
                                        the file if it exists, sound
                                        the alarm.

     Only one file may be received with each RXMOdem function (the
     file must be explicitly named, but need not be given the same
     name as on the remote system).

     See RYMOdem for tips that apply to both RXMOdem and RYMOdem.

     See also SXMOdem, RYMOdem.

     _______

     RYMOdem
     _______

     Default key:   none
     Description:   Receive files using the Ymodem Batch protocol.

     Switches:

               C1 or C   Use CRC error correction (default).
               C0        Use Checksum error correction.

               G1 or G   Use streaming (fast) transfer method.
                         IMPORTANT:  Use only with error-correcting
                         modems or direct connections between
                         computers.
               G0        Use normal (error correcting) transfer method
                         (default).

               Y1 or Y   Overwrite an existing file when a received
                         file has the same name (the existing file
                         will be erased).
               Y0        Cancel the transfer if a received file has
                         the same name as an existing file (default).




               D1 or D   Cancel transfer if carrier detect is lost
                         (default).
               D0        Ignore state of carrier detect.

               A1 or A   Sound the alarm at the end of the transfer.
               A0        Do not sound the alarm (default).

               W         Wait for a keypress at end of transfer.
               Wn        Wait for "n" seconds, "n" may range from 0 to
                         999.  Press a key to cancel the wait.
                         Note:  Default (no "W" switch) is no wait.

     Examples:

          {rymo-ya %dldir}    Receive files into the download
                              directory, overwrite a file if it
                              exists, sound the alarm.

          {rymo-gw3}          Receive files using the "G" method into
                              the current directory.  Wait 3 seconds
                              before returning to the Terminal Screen.

     Ymodem is a "batch" protocol that will receive multiple files. 
     Filenames are transmitted by the sender and are used to name
     files at the receiving end.  A filename "collision" will cause
     the transfer to cancel unless the "Y" switch is used.  File sizes
     are also transmitted by the sender and are used to truncate the
     file to the proper size.

     TIPS on using RYMOdem and RXMOdem:

     >    The "G" method is specified by the receiver.  Be sure that
          the sender allows it before starting.

     >    Block size is established by the sender and may be changed
          on a block-by-block basis (always 1024 when the "G" method
          is used).

     >    Some conditions that will cancel a transfer:
            1) 10 consecutive errors.
            2) Any error when "G" method is used.
            3) The file to be received already exists and the "Y"
               switch is not present.
            4) The sender has transmitted CAN (^X) characters.

     >    The Exit Code (test with IFER) will be set at the end of the
          transfer.  The Exit Code will also be stored in the variable
          "_err".  0 means success, 1 means failure.

     >    If the Usage Log is enabled, an entry will be made after
          each file is transferred (or if a transfer is cancelled).

     See also SXMOdem, RYMOdem.




     _______

     SETDial
     _______

     Default key:   none
     Description:   Set parameters for dialing.

     Examples:

          {setdial 60,15}          Set the dialing cycle timer to 60
                                   seconds and the Inter-dial Delay to
                                   15 seconds.

          {setd ,3}                Change only the Inter-dial Delay
                                   timer.

     The first argument is the dialing cycle time limit.  This is the
     amount of time {COMMO} will allow after sending the dial command
     to the modem.  Range is from 1 to 999.

     The second argument is the inter-dial delay timer.  This is the
     amount of time before {COMMO} dials the next number.  Range is
     from 1 to 999.

     NOTE:  Changes to dialing parameters override the Setup File
     values and remain in effect until {COMMO} is exited.

     See also DIAL.

     _____

     SHELl
     _____

     Default key:   Alt-S
     Description:   Shell to DOS.

     Switches:

               S1 or S   Swap to disk before shelling to DOS (see
                         details under EXECute, "Using the Swap to
                         Disk Switch").

               S0        Do not swap to disk (default).

     Examples:

          {shell}             No arguments.
          {shell-s}           Swap to disk before shelling to DOS.




     ______

     SIGNal
     ______

     Default key:   none
     Description:   Set state of hardware signals.

     Switches:

               D1 or D        Set DTR high.
               D0             Set DTR low.
               R1 or R        Set RTS high.
               R0             Set RTS low.

     Example:

          {signal-d0r1}            Turn off DTR, turn on RTS.

     The "D" and "R" switches are used to control the RS-232C signals
     DTR (Data Terminal Ready) and RTS (Request To Send).  The default
     for each switch is to leave the signal unchanged.  Use these with
     care due to interaction with Hardware Flow Control, etc.

     _______

     SXMOdem
     _______

     Default key:   none
     Description:   Send a file using the Xmodem protocol.

     Switches:

               See SYMOdem (switches are the same).

     Example:

          {sxmo-ka c:\ul\file.zip}      Send "file.zip" using 1024
                                        byte block size, sound the
                                        alarm.

     Only one file may be sent with each SXMOdem function.

     See SYMOdem for tips that apply to both SXMOdem and SYMOdem.

     See also RXMOdem, SYMOdem.

     _______

     SYMOdem
     _______

     Default key:   none
     Description:   Send a file using the Ymodem Batch protocol.





     Switches:

               K1 or K   Use 1024 byte block size (Xmodem-1k).
               K0        Use 128 byte block size (default).

               D1 or D   Cancel transfer if carrier detect is lost
                         (default).
               D0        Ignore state of carrier detect.

               A1 or A   Sound the alarm at end of transfer.
               A0        Do not sound the alarm (default).

               W         Wait for a keypress at end of transfer.
               Wn        Wait for "n" seconds, "n" may range from 0 to
                         999.  Press a key to cancel the wait.
                         Note:  Default (no "W" switch) is no wait.

     Examples:

          {symo-ka %uldir\*.zip}        Send all .ZIP files in the
                                        upload directory using 1024
                                        byte block size, sound the
                                        alarm.

          {symo-k c:\subdir\*.*,@c:\ul\file.lst,info.txt,a:*.qw?}
                                        Send all files listed using
                                        1024 byte block size.

     Any combination of file specifications may be listed in the
     SYMOdem function (separated with commas).  These may include
     wildcard specifiers (*,?), the indirect file specifier (@) and
     any single files.

     If a filespec is preceded with the "@" sign, it will be assumed
     to be an "indirect file."  This means that it is a text file
     containing a list of filespecs.  Filespecs should be listed one
     per line and each line should end with a cr/lf.  Each filespec
     may contain wildcards.  For example:

          c:\subdir\*.*
          info.txt
          a:*.qw?

     TIPS on using SYMOdem and SXMOdem:

     >    CRC vs. Csum mode is established by the receiver.

     >    Use of "G" method is established by the receiver.

     >    Some conditions that will cancel a transfer:
            1) 10 consecutive errors.
            2) Any error when "G" method is used.
            3) The receiver has transmitted CAN (^X) characters.




     >    The Exit Code (test with IFER) will be set at the end of the
          transfer.  The Exit Code will also be stored in the variable
          "_err".  0 means success, 1 means failure.

     >    If the Usage Log is enabled, an entry will be made after
          each file is transferred (or if a transfer is cancelled).

     See also RYMOdem, SXMOdem.


                                  - end -