ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
   º                                                                         º
   º               INTEL EXTERNAL MODEM COMPUTER COMPATIBILITY               º
   º                                                                         º
   ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼


   The following information tells whether or not certain computers are
   compatible with your Intel product.  In some cases there are also special
   installation instructions.  "(Field Report)" means the information came
   from our customers and may not have been verified by Intel's compatibility
   lab.


   GENERAL INFORMATION

       Intel external modems are compatible with any computer or terminal with
       a serial port that supports asynchronous communications.  This includes
       IBM PC, XT, AT and compatibles, IBM PS/2 Models 30, 50, 50z, 70, and
       80, and Apple computers.


   AMIGA 500

       Intel tested this computer and is is compatible with Intel external
       modems.

       WARNING:    As stated in the Amiga owners manual, pins 9 and 10 of the
                   Amiga serial port are connected to +/-12 volts.  Users must
                   either buy a cable that doesn't use these pins or disconnect
                   these two pins from the cable.  FAILURE TO DO SO COULD DAMAGE
                   THE MODEM!


   AMIGA 2500

       Intel tested this computer and is is compatible with Intel external
       modems.

       WARNING:    As stated in the Amiga owners manual, pins 9 and 10 of the
                   Amiga serial port are connected to +/-12 volts.  Users must
                   either buy a cable that doesn't use these pins or disconnect
                   these two pins from the cable.  FAILURE TO DO SO COULD DAMAGE
                   THE MODEM!


   DATA TERMINALS

       The Intel 2400EX modem is compatible with data terminals that conform
       to the RS-232C serial port standard.  If the modem doesn't work, you
       may need a "null modem" cable, a cable that has pins 2 and 3 cross
       connected.  Pin 2 (send) on one end is connected to pin 3 (receive) on
       the other end.  Some terminals, such as the Televideo 925, can swap
       these pins internally.

       The pin assignments for the modem cable are as follows:

   ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

   1/91                       Intel FaxBack # 4324                     Page 1

   ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
   º                                                                         º
   º               INTEL EXTERNAL MODEM COMPUTER COMPATIBILITY               º
   º                                                                         º
   ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ (continued) ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼


             Pin      Description
            ÄÄÄÄÄ   ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
              2       Send
              3       Receive
              4       Ready To Send
              5       Clear To Send
              6       Data Set Ready
              7       Signal ground
              8       Carrier Detect
             20       Data Terminal Ready (DTR)
             22       Ring Indicator
     
       The minimum required pins are pins 2, 3, 7, and 20.




































   ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

   1/91                       Intel FaxBack # 4324                     Page 2