ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
   º                                                                         º
   º                9600EX Compatibility with Other Modems                   º
   º                                                                         º
   ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

    MODEM COMPATIBILITY IN GENERAL

        Intel modems and faxmodems are compatible with virtually all 300, 1200,
        and 2400bps modems.  Be aware that there are proprietary high speed
        standards that Intel does not support ("PEP" Protocol used with
        Telebits, HST Used by US Robotics Modems).


    HAYES ULTRA

        This modem has been tested with all Intel modems and is compatible.
        The Hayes Ultra is a V.32 compatible modem that incorporates V.42bis
        and MNP levels 1-5. All of our modems will talk to the Ultra at 300,
        1200, and 2400bps. Intel High Speed modems can talk to the Ultra at
        4800 and 9600bps when V.32 mode on the Ultra is enabled. Keep in mind
        the Ultra also has the Hayes Proprietary "ping-pong" 9600bps mode that
        is NOT V.32. When the Ultra has V.32 mode disabled, only other Hayes
        modems can talk to it at 4800 and 9600bps.

        SatisFAXtion/100:
        Intel's lab tested this modem with the SatisFAXtion/100 board, and it
        is compatible.


    HAYES SMARTMODEM V SERIES 9600

        This modem has been tested with all Intel modems and is compatible.
        All Intel modems can talk to this modem at 300, 1200, and 2400bps. Some
        versions of the Smartmodem 9600 have MNP and V.42 capabilities. At
        4800bps and higher, Hayes uses a proprietary "ping-pong" 4800/9600bps
        protocol that only other Hayes modems can connect to. Intel High Speed
        Modems  cannot talk to the Hayes Smartmodem V 9600 at any speed higher
        than 2400bps.


    HAYES SMARTMODEM 2400 V SERIES

        This modem has been tested with all Intel modems and is compatible.
        All Intel modems can talk to the Smartmodem 2400 at 300, 1200, and
        2400bps. Some versions of the 2400 V series support V.42bis. All
        versions support MNP.

        SatisFAXtion/100:
        Intel's lab tested this modem with the SatisFAXtion/100 board, and it
        is compatible.


    MULTITECH MULTIMODEM V.32

        The Multitech MultiModem has been tested at 300, 1200, and 2400bps with
        all other non-V.32 modems and was found to be compatible. Intel High
        Speed Modems can communicate with this modem at 4800bps and 9600bps.
        Some versions of this modem support V.42bis and/or MNP Level 4&5.

   ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

   June 4, 1992              Intel FaxBACK # 4328                       Page 1

   ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
   º                                                                         º
   º                9600EX Compatibility with Other Modems                   º
   º                                                                         º
   ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ (continued) ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

    MULTITECH MULTIMODEM 224

        This modem was tested with all Intel modems and found to be fully
        compatible at 300, 1200 and 2400bps. No error correction or data
        compression is offered in this unit.


    MULTITECH MULTIMODEM 224E

        This modem was tested with all Intel modems and found to be fully
        compatible at 300, 1200 and 2400bps. The 224E is similar to the 224,
        but offers MNP Levels 4&5.


    RACAL-VADIC 9632VP

        14.4EX, SatisFAXtion/400 & 400E:
        The Intel SatisFAXtion/400 & 400E and the 14.4EX will not connect with
        older versions of this modem when the Intel modem originates the call.
        If the 9632VP originates the call, the modems connect.  As of this
        writing, the current version of the 9632VP does not have this problem.

        9600EX:
        The 9600EX works with all versions of this modem.


    US ROBOTICS HST

        The US Robotics HST modem has been tested with all Intel modems and is
        compatible.  The US Robotics HST modem can connect to any Intel modem
        at 300, 1200, and 2400bps. At 4800bps and higher, it uses the
        proprietary HST (High Speed Technology) protocol that is supported only
        by other US Robotics modems. It will not connect to any modems at this
        high speed except for other US Robotics modems.

        SatisFAXtion/100:
        Intel's lab tested this modem with the SatisFAXtion/100 board, and it
        is compatible.


    US ROBOTICS HST DUAL STANDARD

        This modem has been tested with all Intel modems and found to be
        compatible.  The US Robotics dual standard can talk to all Intel modems
        at 300, 1200, and 2400bps. Be aware that there are two modes of 9600bps
        operation for this modem: HST and V.32. When the US Robotics is in HST
        mode, Intel High Speed Modems can only talk to it at 300, 1200, and
        2400 because the HST mode is proprietary to just US Robotics modems.
        When in V.32 mode, Intel High Speed Modems can talk to it at 4800 and
        9600bps.

   ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

   June 4, 1992              Intel FaxBACK # 4328                       Page 2

   ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
   º                                                                         º
   º                9600EX Compatibility with Other Modems                   º
   º                                                                         º
   ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ (continued) ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

    US ROBOTICS COURIER V.32

        The US Robotics Courier V.32 has been tested at Intel and is compatible
        with all Intel modems. This modem is the functional equivalent to the
        9600EX and will connect at 300, 1200, 2400, 4800 and 9600bps. Some
        versions of this modem support MNP Levels 4&5 and V.42bis.


    US ROBOTICS SPORTSTER

        Intel has tested this modem and has found it to be compatible with all
        of our modems. It will support speeds of 300, 1200, 2400, 4800 and
        9600bps but does not support error correction or data compression.


    TELEBIT T-1000

        The Telebit T-1000 has been tested by Intel with all modems and is
        compatible at 300, 1200 and 2400bps. At 4800bps and higher, Telebit
        uses a proprietary "PEP" protocol which is ONLY COMPATIBLE WITH OTHER
        TELEBIT MODEMS - THE T-1000 IS NOT V.32 COMPATIBLE. Some versions of
        this modem have MNP Levels 4&5 and/or V.42bis.


    TELEBIT T-1500/T-1600

        The Telebit T-1500 and T-1600 have been tested at Intel and are
        compatible with Intel modems at 300, 1200, 2400, 4800 and 9600bps. They
        are the functional equivalent to the 9600EX. Some versions of these
        modems support V.42bis and/or MNP Levels 4&5.


    TELEBIT T-2500

        The Telebit T-2500 has been tested with all Intel modems and was found
        to be compatible with all modems. When in V.32 mode, the T-2500 can
        connect to Intel High Speed Modemss at 4800 and 9600bps. Keep in mind
        that this modem has the ability to use Telebit's proprietary "PEP"
        protocol in addition to or instead of V.32. When in "PEP" mode, all
        Intel modems can talk to the T-2500 at 300, 1200 and 2400bps.

        Intel High Speed Modems can also connect with this modem using V.42bis
        data compression/error correction with Telebit ROM Version 7.02 or
        higher.


    TELEBIT TRAILBLAZER PLUS

        The Telebit Trailblazer Plus is compatible with all Intel modems at
        300, 1200 and 2400bps. At 4800bps and higher it uses Telebit's
        proprietary "PEP" mode that only other Telebits can use. Some versions
        have V.42bis and/or MNP Levels 4&5.

   ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

   June 4, 1992              Intel FaxBACK # 4328                       Page 3