ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
   º                                                                         º
   º               Configuring Communications Software: Q-Z                  º
   º                                                                         º
   ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

    QMODEM

        This program is compatible with Intel modems.  The first time you run
        Qmodem it automatically takes you to the "Setup Menu".  After the first
        time, use <ALT-N> to call up the "Setup Menu".

        þ   Press M to select the Modem menu
            -   Press C to select "Communications Parameters"
            -   Press A to select "Default baud rate"
            -   Highlight the baud rate for your modem then press <ENTER>
                    14.4EX                      :  57600
                    9600EX                      :  38400
                    All 2400 Baud MNP modems    :  4800
                    All 2400 Baud non-MNP modems:  2400
            -   Press J to select "Serial Port"
            -   Type the number of the COM port of your modem and press <ENTER>
            -   Press <ESCAPE>

        þ   Press M to select "Modem Commands"
            -   Press I to select "Initialization Command"
            -   Type  ATZ^M then press <ENTER>.
            -   Press <ESCAPE>

        NOTE:   QMODEM Comes with COM1 and COM2 defined, but COM3 and COM4 are
                undefined. If you installed your modem on COM3 or COM4, use the
                following commands to define the address and IRQ for COM3 or
                COM4. If you installed your modem on COM1 or COM2, skip over
                this section to the next.

        þ   If you installed your modem on COM3 or COM4, press P to select
            "Port Addresses" then follow these instructions:
            -   Highlight the "Base" address of your modem's COM port then
                <ENTER>
            -   Type 0, your modem's 3 digit address (2E8 or 3E8), then press
                <ENTER>
            -   Highlight the "IRQ" of your modem's COM port then <ENTER>
            -   Type your modem's IRQ number then <ENTER>
            -   Press <ESCAPE> twice

        þ   Press H to select "Host" options menu.
            -   Press I to select "Init Command".
            -   Type  ATZ^M (delete any extra characters) then <ENTER>
            -   Press <ESCAPE>









   ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

   December 13, 1991         Intel FaxBACK # 4356                       Page 1

   ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
   º                                                                         º
   º               Configuring Communications Software: Q-Z                  º
   º                                                                         º
   ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ (continued) ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

        þ   Press O to select "Options"
            -   Press T to select "Toggles"
            -   Set the following option for your modem:

                                      All 2400   All 2400   9600EX
                                      non-MNP    MNP        14.4EX
                                      --------   --------   ------
                [XON/XOFF] Flow ctrl.    ON         OFF       OFF
                CTS/RTS Flow ctrl.       OFF        ON        ON
                CTS When writing         OFF        OFF       OFF
                Redial sets baud rate    ON         OFF       OFF

            -   Press <ESCAPE> twice

        þ   Press E to select "Exit"
            -   Press S to select "Save changes"

        þ   Now configure your modem.
            -   In terminal mode, enter the correct command for your modem:
                9600EX                      : AT&F&W <ENTER>
                All 2400 Baud MNP modems    : AT&F\N3\Q3\J0&W <ENTER>
                All 2400 Baud non-MNP modems: AT&F&C1&D2&W<ENTER>

        That's all there is to it!


    QUICK LINK II

        This modem is compatible with Intel modems.  Here's how to configure
        Quick Link II.

        þ   Run Quick Link
        þ   Select "Modem Setup" from the "Setup"/"Modem Setup" menu
        þ   Set the "Init string" to  AT&F&C1&D2
        þ   Set "Dial prefix" to  ATDT
        þ   Set "Hangup string" to  ATH
        þ   Set "Modem port" to the phone icon
        þ   Select "Terminal options" from the "Setup"/"Terminal Options"menu.
                                      9600EX   All 2400   All 2400
                                               MNP        non-MNP
                                        ------   --------   --------
                XON/XOFF flow control  OFF       OFF        ON
                CTS/RTS flow control   ON        ON         OFF
                Baud rate             19200      4800       2400
                                       (38400 if possible)

        That's all there is to it!


    SMARTCOM II

        Intel has tested this software and version 2.1 is compatible with all
        Intel modems.  Smartcom II is designed for use with Hayes 2400 modems
        and any deviation can cause problems.  So before using Smartcom II with

   ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

   December 13, 1991         Intel FaxBACK # 4356                       Page 2

   ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
   º                                                                         º
   º               Configuring Communications Software: Q-Z                  º
   º                                                                         º
   ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ (continued) ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

        any Intel MNP modem (SatisFAXtion and 9600EX included), you must
        configure them identically to the Hayes.  Use the "Terminal emulation"
        option in Intel's TESTCOM program to send the command
        AT\J1\N0\Q0\V0&Wto the modem.

        Before using Smartcom II v3.0 with the SatisFAXtion or Connection
        CoProcessor (CCP) modem, you must remove the fax program from memory.
        If you don't, your system will lockup when you load Smartcom.  For
        SatisFAXtion, enter  CASMGR /U.  For CCP, enter  XCAM.

        Special notes about Smartcom II Version 3.0:

        þ   Version 3.0A is compatible with all Intel modems.
        þ   Version 3.0B is unknown.
        þ   Version 3.0C is incompatible because it checks for a Hayes ROM in
            the modem.  If the modem ROM's checksum doesn't exactly match
            Hayes, the program doesn't work with that modem.


    SMARTCOM III

        This program is compatible with all Intel modems.  Smartcom III is
        designed for use with Hayes modems and any deviation can cause
        problems.  So before using Smartcom III with any Intel MNP modem
        (SatisFAXtion and 9600EX included), you must configure them identically
        to the Hayes.  Use the "Terminal emulation" option in Intel's TESTCOM
        program to send the command  AT\J1\N0\Q0\V0&Wto the modem.


    TELIX/TELIX SE

        This program is compatible with Intel modems.  After entering Telix,
        configure the program and modem using these instructions.

        þ   Press <ALT-O> to access the "Configure Telix" menu.
        þ   Press T to select "Terminal Options".
            -   Press A to select "Baud" rate.
            -   Highlight the correct baud rate for your modem then press
                <ENTER>

                    9600EX               : 38400
                    All 2400 Baud MNP    :  4800
                    All 2400 Baud non-MNP:  2400

            -   Select the "Data Bits" and "Stop Bits" to match the systems you
                call most often.  If it doubt, set "Data Bits" to 8 and "Stop
                Bits" to 1.
            -   Press B to set the "COM port".
            -   Highlight the "COM port" on which you installed your modem then
                press <Enter>.
            -   Set f low control for your modem:

                        Modem                      XON/XOFF   CTS/RTS
                        ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ       ÄÄÄÄÄÄÄÄ   ÄÄÄÄÄÄÄ
   ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

   December 13, 1991         Intel FaxBACK # 4356                       Page 3

   ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
   º                                                                         º
   º               Configuring Communications Software: Q-Z                  º
   º                                                                         º
   ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ (continued) ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

                        9600EX                        OFF       ON
                        2400B MNP/2400EX MNP          OFF       ON
                        2400B Classic/2400EX          ON        OFF

            -   Press <Enter>

        þ   Press M to select the "Modem & Dialing" menu.
            -   Press  A  to select "Init String".
            -   Type:  ATZ^M  (delete any extra characters) then press <Enter>.
            -   Press <Enter> again.

        þ   Press W to "Write and Save".

        þ   Enter the correct command for your modem:

                9600EX                      :  AT&F\N3\Q3\J0\V1&W
                All 2400 Baud MNP modems    :  AT&F\N3\Q3\J0\V1&W
                All 2400 Baud non-MNP modems:  AT&C1&D2&W

        That's all there is to it!
































   ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

   December 13, 1991         Intel FaxBACK # 4356                       Page 4