ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
   º                                                                         º
   º        Intel 2400B Modem Technical Installation Instructions            º
   º                                                                         º
   ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼


    INTRODUCTION

        This document contains all the information an experienced user needs to
        install the Intel 2400 BPS modems.  If you're not an experienced user,
        you should use the modem's manual for installation instructions or have
        your dealer install the modem.

        Intel currently makes the following three 2400 BPS modems:

        2400B Classic   Internal modem for IBM PC, PC XT, PC AT, COMPAQ 386 and
                       100% compatible computers.

        2400B Modem 2   Internal modem for IBM PS/2 Models 50, 50Z, 60, 70 and
                       80, and 100% compatible computers.

        2400EX          External Modem for any computer with an external RS232
                       port connector.

        Refer to the installation sections that apply to the modem you're
        installing.


    SETTING SWITCHES

    2400B CLASSIC MODEM

        Before installing the 2400B Classic Modem into the computer, set its
        switches for an address not used by any other serial ports or mouse in
        your computer.  If you have just one serial port, COM2 should work
        fine.

                                               Port    Address    IRQ
          ÉÍÍÍÍÍÍÍÍÍ»            ÚÄÂÄÂÄÂÄ¿    ÄÄÄÄÄ-  ÄÄÄÄÄÄÄÄ-  ÄÄÄÄ-
          º þ þ þ þ º            ³Ü³Ü³Ü³ß³     COM1     3F8h       4
          º 1 2 3 4 º            ÃÄÅÄÅÄÅÄ´
          ÈÍÑÍÍÍÍÍÑÍ¼            ³ß³Ü³ß³Ü³     COM2     2F8h       3
            ÀÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÅÄÅÄÅÄ´
                        COM Port ³Ü³ß³Ü³ß³     COM3     3E8h       4
                        Address  ÃÄÅÄÅÄÅÄ´
                                 ³ß³ß³ß³Ü³     COM4     2E8h       3
                                 ÀÄÁÄÁÄÁÄÙ


    2400B MODEM 2

        The 2400B Modem 2 has no switches.


    2400EX EXTERNAL MODEM

        The 2400EX external modem has no switches.

   ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

   December 13, 1991         Intel FaxBACK # 4410                       Page 1

   ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
   º                                                                         º
   º        Intel 2400B Modem Technical Installation Instructions            º
   º                                                                         º
   ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ (continued) ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

    INSTALLING THE MODEM

    BEFORE YOU BEGIN

        Before installing any new device (modems included), always verify that
        your computer is operating correctly.  Fix any existing problems BEFORE
        installing an Intel modem.

        Once you know the computer is operating correctly, use the steps
        outlined in the appropriate section to install the Intel modem.


    2400B MODEM 2

        1.  Turn off the power switch on the system unit and any attached
            equipment.
        2.  Remove the system unit's cover.
        3.  Insert the modem into an empty slot inside the computer.
        4.  Replace the system unit's cover.
        5.  Plug one end of the telephone cable provided with your modem into
            the connector labeled LINE and plug the other end into the wall
            jack.
        6.  To continue using the phone, connect it to the modem by plugging
            the free end of the telephone's cord into the connector labeled
            PHONE on the modem.
        7.  Turn on the computer and boot up using the Reference Disk.
        8.  Press Enter when the IBM logo appears.
        9.  Type N when asked "Automatically Configure System?".
        10. If you haven't already done so, make a backup copy of your original
            Reference Diskette.
        11. Select Copy an Option Diskette to copy the Intel 2400B Modem 2
            Options diskette to your Reference Diskette.
        12. Select Set Configuration from the Main Menu.
        13. Select Change Configuration from the Set Configuration menu.
        14. Select a serial port for the 2400B Modem 2 to use which does not
            conflict with other serial ports in your computer.  SERIAL_2
            usually works fine.  An asterisk (*) appears when the current
            choice conflicts with an existing serial port.
        15. Save the configuration information and exit from the program.
            Remove the Reference Diskette from drive A and put in a safe place.












   ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

   December 13, 1991         Intel FaxBACK # 4410                       Page 2

   ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
   º                                                                         º
   º        Intel 2400B Modem Technical Installation Instructions            º
   º                                                                         º
   ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ (continued) ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

    2400B CLASSIC MODEM

        1.  Turn off the power switch on the system unit and any attached
            equipment.
        2.  Remove the system unit's cover.
        3.  Insert the modem into an empty slot inside the computer.
        4.  Replace the system unit's cover.
        5.  Plug one end of the telephone cable provided with your modem into
            the connector labeled LINE and plug the other end into the wall
            jack.
        6.  To continue using the phone, connect it to the modem by plugging
            the free end of the telephone's cord into the connector labeled
            PHONE on the modem.


    2400EX EXTERNAL MODEM

        1.  Obtain a cable which has a 25-pin connector on one end and a
            connector on the other end that mates with the serial port on your
            computer (usually either 9-pin, 25-pin, or DIN connector).  This
            cable is not included with the 2400EX.
        2.  Turn off the power switch on the system unit and any attached
            equipment.
        3.  Connect the 25-pin end of the cable to the connector on the 2400EX
            modem's rear panel.  Tighten the connector screws.
        4.  Connect the other end of the cable into your computer's serial
            port.  Tighten the connector screws.
        5.  Connect the modem power supply cable to the round connector on the
            back of the 2400EX.
        6.  Plug the power supply into a wall outlet.
        7.  Plug one end of the telephone cable provided with your modem into
            the connector labeled LINE and plug the other end into the wall
            jack.
        8.  To continue using the phone, connect it to the modem by plugging
            the free end of the telephone's cord into the connector labeled
            PHONE on the modem.


    FINISHING TOUCHES

    VERIFYING MODEM OPERATION

        Follow these steps to run the TESTCOM program to verify the modem's
        operation:

        1.  Turn on the modem.
        2.  Insert the Intel modem diagnostics diskette into drive A and set
            the default drive to A.
        3.  Type TESTCOM and press Enter.



   ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

   December 13, 1991         Intel FaxBACK # 4410                       Page 3

   ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
   º                                                                         º
   º        Intel 2400B Modem Technical Installation Instructions            º
   º                                                                         º
   ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ (continued) ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

    USING THE MODEM

        You need a communications program (such as Crosstalk, Procomm and
        Smartcom) to use the modem.
















































   ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

   December 13, 1991         Intel FaxBACK # 4410                       Page 4