STANDARD MICROSYSTEMS CORPORATION
                 PLUS AND ELITE FAMILY LAN ADAPTER DRIVERS
                       FOR USE IN NDIS ENVIRONMENTS

                            INSTALLATION GUIDE
                            ------------------


This installation guide provides the following instructions:

        1.0 Overview

        2.0 DOS Instructions
            2.1 Installing LAN Manager on DOS
            2.2 Installing 3Com 3+Open version 1.1 on DOS
            2.3 Installing IBM LAN Requestor on DOS
		2.3.1 Installing IBM PC LAN Support
		2.3.2 Installing IBM DOS LAN Requestor
            2.4 Installing IBM PC LAN on DOS
		2.4.1 Installing IBM LAN Support
		2.4.2 Installing IBM PC LAN After LAN Support
	    2.5 Installing Other Programs on DOS

        3.0 OS/2 Instructions
            3.1 Installing LAN Manager on OS/2
            3.2 Installing 3Com 3+Open version 1.1 on OS/2
            3.3 Installing IBM LAN Server on OS/2

	4.0 Installing Two Adapters in the Same System

        5.0 PROTOCOL.INI Parameters

	6.0 Error Messages


1.0	OVERVIEW

The NDIS driver is designed to work with both the Standard Microsystems
"PLUS" and "ELITE" (SMC8003/SMC8013) families of LAN Adapters. This driver
conforms to the Network Driver Interface Specification (NDIS) defined by
Microsoft/3Com. The driver has been tested with Microsoft LAN Manager,
3Com 3+Open, IBM LAN Server, IBM PC LAN, and other NDIS compatible network
operating systems and protocol stacks. 

The driver provides support for these three adapter types:

  7  Jumper-Configured

     These adapters can only be configured by setting jumpers 
     on the adapter boards.

       SMC8013EBT   SMC8003E     
       SMC8003EBT   SMC8003S     
       SMC8003SH    SMC8003WT  

  7 Software-Configurable

    These adapter cards have the ability to be configured using
    a software setup program.

       SMC8003EP    SMC8013EP    
       SMC8013EW    SMC8013W
       SMC8003EB    SMC8003W    
          
  7 Micro Channel

    This adapter type works only with the IBM Micro Channel bus
    protocol standard.

       SMC8003ET/A  SMC8003E/A   
       SMC8003W/A   SMC8003ST/A
       SMC8013WP/A  SMC8013WP/A
    
These files are included with this release of the SMC NDIS driver
and are located on the SuperDisk shipped with your Standard Microsystems
adapter board:

   INSTALL.DOC           Installation Guide (this File)
   RELEASE.DOC           Version history and release information
   SMCMAC.OS2            OS/2 NDIS MAC driver
   SMCMAC.DOS            DOS NDIS MAC driver
   SMCMAC2.OS2           OS/2 NDIS MAC driver for second LAN adapter
   SMCMAC2.DOS           DOS NDIS MAC driver for second LAN adapter
   PROTOCOL.INI          PROTOCOL.INI file sample

Install the adapter card in your PC using the instructions in the 
Installation Guide included with the adapter.  Proper installation 
can be verified by running the Diagnostic Program under DOS.

                             NOTE
         The Diagnostic Program will not run properly from 
	 the OS/2 compatibility box.

2.0    DOS INSTRUCTIONS

       The following section provides you with instructions for installation
       all drivers based on the MS-DOS platform. This includes instructions
       on modifying the CONFIG.SYS and PROTOCOL.INI files to configure the
       specific driver.

2.1    INSTALLING LAN MANAGER ON DOS

       The following instructions only apply to installing the LAN Manager
       on a DOS platform. Do not start LAN Manager until after it's 
       installed. Use the Microsoft instructions to complete the
       installation procedure. Microsoft includes support for the Standard
       Microsystems PLUS family adapters.  Select the Standard Microsystems
       adapter from the list provided by Microsoft.

       To install the LAN Manager on a DOS platform:
       
       1. Copy the LAN Manager Driver to the driver directory used by LAN
          Manager.  For example, when installing a LAN Manager server or
          enhanced workstation using the normal directory structure type:

             COPY SMCMAC.DOS C:\LANMAN\DRIVERS\ETHERNET

         When installing a LAN Manager basic workstation type:

             COPY SMCMAC.DOS C:\LANMAN

       2. Modify the PROTOCOL.INI in accordance with the adapter type. 

	  a. For jumper-configured adapters, use a text editor to add the 
	     following lines to the file:

               	[SMCMAC_NIF]
                   DriverName = SMCMAC$
	           IOBase = 0x280
	           RAMAddress = 0xD000
	           IRQ = 3
 
	     Replace the above IOBase, RAMAddress, and IRQ values with 
	     the values appropriate for your adapter card. If you aren't 
	     sure which adapter type you have, refer to Section 1.0 or 
	     use the setup above. A more complete explanation of these
	     parameters and their appropriate values are provided in
	     section 5.0. If you have a software-configurable or Micro 
	     Channel adapter, you can simplify your parameters by using 
	     step 2b.

	  b. For software-configurable and Micro Channel adapters, use a
	     text editor to add the following lines to the file:

    		[SMCMAC_NIF]
                  DriverName = SMCMAC$
	
       3. Reboot the system and bring up LAN Manager using the instructions 
	  supplied by the LAN Manager vendor.


2.2    INSTALLING 3+OPEN VERSION 1.1 ON DOS

       Install 3+Open using 3Com instructions.  3Com does not include
       support for Standard Microsystems adapters, therefore select a similar
       adapter such as 3Com EtherLink II during installation.

       To install 3+Open on DOS, follow these instructions:

       1.  Copy the SMCMAC.DOS Driver from this diskette to the driver
           directory used by 3+Open.  

	   For example, when installing a 3+Open DOS workstation using 
	   the normal directory structure type:

              COPY SMCMAC.DOS C:\3OPEN\DOSWKSTA\LANMAN\DRIVERS

       2. Modify CONFIG.SYS file to reference this adapter rather than 
          the adapter selected during 3+Open installation.  

	  For example, if the 3Com EtherLink II was selected during 
	  a workstation installation, use a text editor to change 
	  the line:

              DEVICE=\3OPEN\DOSWKSTA\LANMAN\DRIVERS\ELNNKII.DOS

	  to the line:

              DEVICE=\3OPEN\DOSWKSTA\LANMAN\DRIVERS\SMCMAC.DOS


                                 NOTE
             Other varieties of LAN Manager keep their drivers
             in different directories. The objective is to have
             the CONFIG.SYS reference the SMCMAC.DOS driver rather 
             than the adapter driver selected during installation.  
             Also the LAN Manager installation adds several drivers 
             to the CONFIG.SYS file. Only the MAC driver referring 
             to a particular board should be replaced. Other drivers, 
             such as PROTMAN.DOS should not be modified.

       3. Modify PROTOCOL.INI in accordance with your adapter type. 

	  a. For jumper-configured adapters, use a text editor to add 
	     the following lines to the file:

               	[SMCNDIS]
                   DriverName = SMCMAC$
	           IOBase = 0x280
	           RAMAddress = 0xD000
	           IRQ = 3

	     Replace the above IOBase, RAMAddress, and IRQ values with 
	     the values appropriate for your adapter card. If you aren't 
	     sure which adapter type you have, refer to Section 1.0 or 
	     use the setup above. A more complete explanation of these
	     parameters and their appropriate values are provided in
	     section 5.0. If you have a software-configurable or Micro 
	     Channel adapter, you can simplify your parameters by using 
	     step 3b.

	     The '[SMCNDIS]' statement is used in the Bindings command
	     to associate the protocol stack with the driver.

	 b.  For software-configurable and Micro Channel adapters, use a
	     text editor to add the following lines to the file:

    		[SMCNDIS]
                  DriverName = SMCMAC$

	     The '[SMCNDIS]' statement is used in the Bindings command
	     to associate the protocol stack with the driver.

      4. Locate the section of the PROTOCOL.INI file which describes the 
	 protocol stack for your configuration. Locate the 'BINDINGS =' 
	 statement within this section and use a text editor to modify this 
	 statement to reference 'SMCNDIS' rather than the name set during 
	 installation.

         For example, under 3+Open with the DLC/NETBEUI protocol stack and
         3Com EtherLink II selected during installation, in the PROTOCOL.INI
         file section labeled '[DLC]', the lines:

              [DLC]
                DriverName = DLC$
                BINDINGS = EtherlinkII

         must be changed to:

              [DLC]
                DriverName = DLC$  
                BINDINGS = SMCNDIS

	 This changes the bindings of the the protocol stack.

      5. Reboot the system and bring up 3+Open using the instructions 
	 supplied by the 3Com.


2.3    INSTALLING IBM LAN REQUESTOR ON DOS

       IBM LAN Server must run in conjunction with IBM PC LAN Support 
       first Program to work with a NDIS driver. Install IBM PC LAN 
       Support then IBM LAN Server.

2.3.1  Installing IBM PC LAN Support Program

       Here is the procedure for installing IBM LAN Support:

       1. Copy the SMCMAC.DOS file to the 'C:\LANMAN' subdirectory.

             COPY SMCMAC.DOS C:\LANMAN

       2. Install IBM LAN as the manual explains. Select 'Ethernet' as 
	  the network type.

       3. When asked by the install program whether the line DXMT0MOD.SYS is
       	  appropriate to add to the CONFIG.SYS file, edit the line to read:

             DEVICE=DXMT0MOD.SYS O=N  

	  This tells the IBM LAN SUPPORT program not to reset the card when it 
	  is starting.

       4. Change the line in the CONFIG.SYS file which reads 

             DEVICE=XXX.DOS

          to read 

    	     DEVICE=C:\LANMAN\SMCMAC.DOS  

       5. Modify PROTOCOL.INI in accordance with your adapter type. 

	  a. For jumper-configured adapters, use a text editor to add 
	     the following lines to the file:

               	[SMCMAC]
                   DriverName = SMCMAC$
	           IOBase = 0x280
	           RAMAddress = 0xD000
	           IRQ = 3
 
	     Replace the above IOBase, RAMAddress, and IRQ values with 
	     the values appropriate for your adapter card. If you aren't 
	     sure which adapter type you have, refer to Section 1.0 or 
	     use the setup above. A more complete explanation of these
	     parameters and their appropriate values are provided in
	     section 5.0. If you have a software-configurable or Micro 
	     Channel adapter, you can simplify your parameters by using 
	     step 5b.

	 b. For software-configurable and Micro Channel adapters, use a
	    text editor to add the following lines to the file:

    		[SMCMAC]
                   DriverName = SMCMAC$
	
      6. Reset the computer to start IBM LAN SUPPORT.

2.3.2  Installing IBM DOS LAN Requester

       Here is the procedure for installing the IBM DOS LAN Requester:

       1. Install, but do not start, DOS LAN Requester according to the
       	  instructions provided with DOS LAN Requester.

       2. Change the line in the CONFIG.SYS file that contains

             DEVICE=DXMT0MOD.SYS S=12 C=14 ST=12 

	  because the parameters might not be the same. Edit the line 
	  to read: 

	     DEVICE=DXMT0MOD.SYS S=12 C=14 ST=12 O=N 

          for the Standard Microsystems adapter.

       3. Modify PROTOCOL.INI in accordance with your adapter type. 

	  a. For jumper-configured adapters, use a text editor to add 
	     the following lines to the file:

               	[SMCMAC]
                   DriverName = SMCMAC$
	           IOBase = 0x280
	           RAMAddress = 0xD000
	           IRQ = 3
 
	     Replace the above IOBase, RAMAddress, and IRQ values with 
	     the values appropriate for your adapter card. If you aren't 
	     sure which adapter type you have, refer to Section 1.0 or 
	     use the setup above. A more complete explanation of these
	     parameters and their appropriate values are provided in
	     section 5.0. If you have a software-configurable or Micro 
	     Channel adapter, you can simplify your parameters by using 
	     step 3b.

	 b. For software-configurable and Micro Channel adapters, use a
	    text editor to add the following lines to the file:

    		[SMCMAC]
                  DriverName = SMCMAC$
	

2.4    INSTALLING IBM PC LAN ON DOS

       IBM PC LAN must run in conjunction with IBM PC LAN Support to work
       with a NDIS driver. Install IBM PC LAN Support first, then IBM PC 
       LAN.

2.4.1  Installing IBM PC LAN Support

       To install IBM PC LAN Support on your system, follow this procedure:

       1. Copy the SMCMAC.DOS file to the 'C:\LANMAN' subdirectory.

             COPY SMCMAC.DOS C:\LANMAN

       2. Install IBM PC LAN Support as described in the manual. Choose
          'Etherand' as the network type.

       3. When asked by the install program whether the line DXMT0MOD.SYS is
          appropriate to add to the CONFIG.SYS file, edit the line to read:
       
	     DEVICE=DXMT0MOD.SYS O=N  

          This tells the IBM PC LAN Support Program not to reset the card 
	  when it is starting.

       4. Change the line in the CONFIG.SYS file which reads:

       	     DEVICE=XXX.DOS 

	  to read 

	     DEVICE=C:\LANMAN\SMCMAC.DOS 

       5. Modify PROTOCOL.INI in accordance with your adapter type. 

	  a. For jumper-configured adapters, use a text editor to add 
	     the following lines to the file:

               	[SMCMAC]
                   DriverName = SMCMAC$
	           IOBase = 0x280
	           RAMAddress = 0xD000
	           IRQ = 3
 
	     Replace the above IOBase, RAMAddress, and IRQ values with 
	     the values appropriate for your adapter card. If you aren't 
	     sure which adapter type you have, refer to Section 1.0 or 
	     use the setup above. A more complete explanation of these
	     parameters and their appropriate values are provided in
	     section 5.0. If you have a software-configurable or Micro 
	     Channel adapter, you can simplify your parameters by using 
	     step 5b.

	  b. For software-configurable and Micro Channel adapters, use a
	     text editor to add the following lines to the file:

    		[SMCMAC]
                  DriverName = SMCMAC$

       6. Reset the computer to start IBM LAN SUPPORT.


2.4.2  Installing IBM PC LAN After LAN Support Installation

       To install the IBM PC LAN after installing the LAN Support, follow
       this procedure:

       1. Install IBM PC LAN as described in the manual.  Choose the Standard
	  Microsystems card option.  

       2. When the installation is complete, verify that the PROTOCOL.INI 
	  file contains the correct bindings.  The file is located in the 
	  'C:\LANMAN' subdirectory.

2.5    Installing Other Systems on DOS

       There are several other DOS environments capable of supporting the 
       NDIS driver. These include: DEC's DECnet, Wollongong's WIN TCPIP, 
       Banyan's Vines Workstation environment, Sun's PCNFS Workstation
       environment, NCSA's Telnet, and  FTP's PCTCP. These DOS environments 
       should handle the task of installation in much the same manner.

       1. Copy the SMCMAC.DOS file to the appropriate subdirectory. For
	  example:

             COPY SMCMAC.DOS C:\LANMAN

	  For information on which directory you must use to install the
	  driver, refer to the relevant manual.

       2. Modify the CONFIG.SYS file by adding this line:

    	     DEVICE=C:\LAN\SMCMAC.DOS  

	  Where the 'LAN' subdirectory is the location of the driver.

       3. Modify PROTOCOL.INI in accordance with your adapter type. 

	  a. For jumper-configured adapters, use a text editor to add 
	     the following lines to the file:

               	[SMCMAC]
                   DriverName = SMCMAC$
	           IOBase = 0x280
	           RAMAddress = 0xD000
	           IRQ = 3
 
	     Replace the above IOBase, RAMAddress, and IRQ values
	     with values appropriate for your adapter card. A more 
	     complete explanation of these parameters and their
	     appropriate values are provided in section 5.0. If you 
	     have a software-configurable or Micro Channel adapter, 
	     you can simplify your parameters by using step 3b.

	     The '[SMCMAC]' statement is used in the Bindings command
	     to associate the protocol stack with the driver.

	  b. For software-configurable and Micro Channel adapters, use a
	     text editor to add the following lines to the file:

    		[SMCMAC]
                  DriverName = SMCMAC$

	     The '[SMCMAC]' statement is used in the Bindings command
	     to associate the protocol stack with the driver.

      4. Locate the section of the PROTOCOL.INI file which describes the 
	 protocol stack for your configuration. Locate the 'BINDINGS =' 
	 statement within this section and use a text editor to modify this 
	 statement to reference 'SMCMAC' rather than the name set during 
	 installation.

       5. Reboot the computer.


3.0    OS/2 INSTRUCTIONS

       The following section provides you with instructions for installation
       all drivers based on the OS/2 platform. This includes instructions on
       modifying the CONFIG.SYS and PROTOCOL.INI files to configure the 
       specific driver.

3.1    INSTALLING LAN MANAGER ON OS/2

       Install, but do not start LAN Manager, using the Microsoft
       instructions.  Microsoft includes support for the Standard Microsystems
       PLUS family adapters. Select the Standard Microsystems adapter from the
       list provided by Microsoft.

       To install the LAN Manager on OS/2, follow this procedure:

       1. Copy the newest LAN Manager driver to your hard drive. Copy the
          OS/2 driver from this diskette to the driver directory used by LAN
          Manager.  

	  For example, when using the normal directory structure type:

              COPY SMCMAC.OS2 C:\LANMAN\DRIVERS\ETHERNET

       2. Modify PROTOCOL.INI in accordance with your adapter type. 

	  a. For jumper-configured adapters, use a text editor to add 
	     the following lines to the file:

               	[SMCMAC_NIF]
                   DriverName = SMCMAC$
	           IOBase = 0x280
	           RAMAddress = 0xD000
	           IRQ = 3
 
	     Replace the above IOBase, RAMAddress, and IRQ values with 
	     the values appropriate for your adapter card. If you aren't 
	     sure which adapter type you have, refer to Section 1.0 or 
	     use the setup above. A more complete explanation of these
	     parameters and their appropriate values are provided in
	     section 5.0. If you have a software-configurable or Micro 
	     Channel adapter, you can simplify your parameters by using 
	     step 2b.

	  b. For software-configurable and Micro Channel adapters, use a
	     text editor to add the following lines to the file:

    		[SMCMAC_NIF]
                   DriverName = SMCMAC$
	
       3. Reboot and bring up LAN Manager using the instructions supplied by 
	  the LAN Manager vendor.


3.2    INSTALLING 3+OPEN VERSION 1.1 ON OS/2

       Install 3+Open using 3Com instructions. 3Com does not include
       support for Standard Microsystems adapters, therefore select a
       similar adapter such as 3Com EtherLink II during installation.

       To install 3+Open on OS/2, follow this procedure:

       1. Copy the OS/2 driver from this diskette to the driver directory
          used by 3+OPEN.  

	  For example, when installing a 3+Open server using the normal
	  directory structure type:

              COPY SMCMAC.OS2 C:\3OPEN\SERVER\LANMAN\DRIVERS

          Or, when installing a 3+Open OS/2 workstation type:

              COPY SMCMAC.OS2 C:\3OPEN\OS2WKSTA\LANMAN\DRIVERS

      2. Modify the CONFIG.SYS or CONFIG.OS2 file to reference this adapter
  	 rather than the adapter selected during 3+Open installation.

         For example, if the 3Com EtherLink II was selected during a server
         installation, use a text editor to change the line:

              DEVICE=\3OPEN\SERVER\LANMAN\DRIVERS\ELNNKII.OS2

         to the line:

              DEVICE=\3OPEN\SERVER\LANMAN\DRIVERS\SMCMAC.OS2

         If the 3Com EtherLink II was selected during a workstation
         installation, use a text editor to change the line:

              DEVICE=\3OPEN\OS2WKSTA\LANMAN\DRIVERS\ELNNKII.OS2

         to the line:
 
              DEVICE=\3OPEN\OS2WKSTA\LANMAN\DRIVERS\SMCMAC.OS2

                                NOTE
       		Other varieties of LAN Manager keep their 
		drivers in different directories.  The 
		objective is to have the CONFIG.SYS reference 
		the SMCMAC.OS2 driver rather than the adapter 
		driver selected during installation.  Also 
		that the 3+Open installation adds several 
		drivers to the CONFIG.SYS file.  Only the MAC 
		driver referring to a particular board should 
		be replaced. Other drivers, such as PROTMAN.OS2
		should not be modified.

       5. Modify PROTOCOL.INI in accordance with your adapter type. 

	  a. For jumper-configured adapters, use a text editor to add 
	     the following lines to the file:

               	[SMCMAC]
                   DriverName = SMCMAC$
	           IOBase = 0x280
	           RAMAddress = 0xD000
	           IRQ = 3

	     Replace the above IOBase, RAMAddress, and IRQ values with 
	     the values appropriate for your adapter card. If you aren't 
	     sure which adapter type you have, refer to Section 1.0 or 
	     use the setup above. A more complete explanation of these
	     parameters and their appropriate values are provided in
	     section 5.0. If you have a software-configurable or Micro 
	     Channel adapter, you can simplify your parameters by using 
	     step 5b.

	     The '[SMCMAC]' statement is used in the Bindings command to
	     associate the protocol stack with the driver.

	 b.  For software-configurable and Micro Channel adapters, use a
	     text editor to add the following lines to the file:

    		[SMCMAC]
                  DriverName = SMCMAC$

	     The '[SMCMAC]' statement is used in the Bindings command
	     to associate the protocol stack with the driver.

      6. Locate the section of the PROTOCOL.INI file which describes the 
	 protocol stack for your configuration.  Locate the 'BINDINGS =' 
	 statement within this section and use a text editor to modify this 
	 statement to reference 'SMCMAC' rather than the name set during 
	 installation.

         For example, under 3+Open with the XNS protocol stack and 3Com
         EtherLink II selected during installation, in the PROTOCOL.INI file
         section labeled '[XNS_NETBIOS]', the line:

              [DLC]
                DriverName = DLC$
                BINDINGS = ETHERLINKII

         must be changed to:

              [DLC]
                DriverName = DLC$
                BINDINGS = SMC8003XMAC

         If the DLC/NETBEUI protocol stack was selected for use with
         3+Open, the same lines must be changed in the PROTOCOL.INI file
         section labeled '[DLC]'.

	 This changes the bindings of the the protocol stack.

      7. Reboot the system and bring up 3+Open using the instructions 
	 supplied by the 3Com.


3.3   INSTALLING IBM LAN SERVER ON OS/2

      This package has built-in support for the Standard Microsystems Ethernet
      series of cards. Install LAN SERVER as the IBM manual describes,
      choosing the Standard Microsystems card option that appears on the
      screen.  Do not start LAN SERVER yet.

      To install the IBM LAN Server on OS/2, follow this procedure:

      1. Copy the latest version of the driver over the driver included by 
	 IBM, like this:

               COPY SMCMAC.OS2 C:\CMLIB

      2. Modify PROTOCOL.INI in accordance with your adapter type. 

  	 a. For jumper-configured adapters, use a text editor to add 
	     the following lines to the file:

               	[SMCMAC]
                   DriverName = SMCMAC$
	           IOBase = 0x280
	           RAMAddress = 0xD000
	           IRQ = 3

	     Replace the above IOBase, RAMAddress, and IRQ values with 
	     values appropriate for your adapter card. If you aren't 
	     sure which adapter type you have, refer to Section 1.0 or 
	     use the setup above. A more complete explanation of these
	     parameters and their appropriate values are provided in
	     section 5.0. If you have a software-configurable or Micro 
	     Channel adapter, you can simplify your parameters by using 
	     step 2b.

	 b. For software-configurable and Micro Channel adapters, use a
	    text editor to add the following lines to the file:

    		[SMCMAC]
                   DriverName = SMCMAC$
	
      3. Reboot and bring up LAN SERVER using the instruction supplied 
	 by IBM.


4.0   INSTALLING TWO ADAPTERS IN THE SAME SYSTEM

      This release includes SMCMAC2.OS2 and SMCMAC2.DOS.  These drivers may
      be used to install a second adapter card.  When installing the LAN
      Manager software, select two Standard Microsystems family adapters.
      When LAN Manager setup exits, modify the CONFIG.SYS file and the
      PROTOCOL.INI file using this procedure.

      1. Modify CONFIG.SYS by changing one of the two SMCMAC.XXX entries
         from SMCMAC.XXX to SMCMAC2.XXX.  For example:

             DEVICE=C:\LANMAN\DRIVERS\ETHERNET\SMCMAC\SMCMAC.DOS
             DEVICE=C:\LANMAN\DRIVERS\ETHERNET\SMCMAC\SMCMAC.DOS

         should be changed to:

             DEVICE=C:\LANMAN\DRIVERS\ETHERNET\SMCMAC\SMCMAC.DOS
             DEVICE=C:\LANMAN\DRIVERS\ETHERNET\SMCMAC\SMCMAC2.DOS

      2. Modify PROTOCOL.INI by changing the second adapter entry to 
         specify the DriverName as SMCMAC2$ and changing all parameter
	 values so no conflict results.

	 a. For jumper-configured adapters, use a text editor to
	    modify the following lines for the second adapter entry:

	      [SMCMAC2_NIF]
		 DriverName = SMCMAC2$
		 IOBase = 0x300
		 RAMAddress = 0xD800
		 IRQ = 5

	    Make sure these parameter values do not conflict with
	    the first adapter entry, and that they match the settings
	    of the second adapter.

	 b. For software-configurable adapters, use a text editor to
	    modify the following lines for the second adapter entry:

	      [SMCMAC2_NIF]
		 DriverName = SMCMAC2$
		 IOBase = 0x300

	    Make sure the IOBase value does not conflict with the
	    value provided for the first adapter, and that it matches 
	    the second adapter setting. Always include an IOBase
	    statement with the DriverName.

	 c. For Micro Channel adapters, use a text editor to modify
	    the following lines for the second adapter entry:

	      [SMCMAC2_NIF]
		 DriverName = SMCMAC2$
		 SlotNumber = 4

	    Make sure the SlotNumber value does not conflict with the
	    value provided for the first adapter, and that it matches 
	    the second adapter setting. Always include a SlotNumber
	    statement with the DriverName.

      3. Modify adapter values so that the two adapters do not use the same 
	 values for I/O Base Address, RAM Address and IRQ.  

 	 Refer to the adapter's Installation Guide for information about 
	 these parameters.

      4. Load the drivers and reboot the system.


5.0   PROTOCOL.INI PARAMETERS

      Several parameters are typically specified in the SMCMAC section of
      the PROTOCOL.INI file. The only parameter that must be specified
      is the 'DriverName'. All others have default values supplied
      by the driver and can be left out of the PROTOCOL.INI file if the
      installed adapter matches the default configuration. Software-
      configurable and Micro Channel adapters ignore the values of IRQ, 
      IOBase and RAMAddress and instead use the values in the POS 
      registers set up when the card was installed.

      Below is a list of parameters and their definitions commonly found
      in the PROTOCOL.INI file.  Both default values and possible value
      ranges are provided for each parameter.

           IRQ     Specifies the interrupt used by the adapter.  The
                   default is 3.  IRQ3 is used by COM2.  If COM2 is in
                   use, choose another IRQ value.  The interrupt is
                   selected via a jumper on some adapters, or by way of
                   the EZSETUP program supplied with other adapters.
                   Consult the installation guide for information on how
                   to determine or modify the interrupt. This parameter
                   is always a decimal number in the range of 2 - 15.
                   Not all values are supported by all adapters.

        IOBase     Specifies the base I/O address used by the adapter.
                   The default is 0x280.  The address is selected via a
                   jumper on some adapters, or by way of the EZSETUP
                   program supplied with other adapters.  Consult the
                   Installation Guide for information on how to determine
                   or modify the address.  This parameter is a hexadecimal
                   number in the range of 0x200 - 0xFFFF.  Hexadecimal
                   numbers must be preceded by '0x' to distinguish them
                   from decimal numbers.  Remeber that not all values are 
		   supported by all adapters.

    RAMAddress     Specifies the Shared RAM segment address used by the
                   adapter.  This value is established under software
                   control by the driver.  The default Shared RAM segment
                   address is 0xD000.  This address is recommended unless
                   it conflicts with some other device in the PC.  Consult
                   the adapter Installation Guide or print the file
                   SYSMAP.DOC on the SuperDisk for more information on how
                   to select a shared RAM address.  The driver uses
                   hexadecimal values in the range of 0xA000 - 0xFFFF.

    SlotNumber     Specifies the number of the slot containing the adapter
                   card in a Micro Channel machine.  This parameter is a
                   decimal number in the range of 1 - 10.

   MaxRequests     Specifies the number of general request queue entries.
                   The default is 8.  This parameter is a decimal number
                   in the range of 6 - 24.

  MaxTransmits     Specifies the number of transmit queue entries.  The
                   default is 12.  This parameter is a decimal number in
                   the range of 6 - 24.

ReceiveBuffers     Specifies the number of receive buffer queue entries.
                   The default value is 12.  This parameter is a decimal
                   number in the range of 6 - 24.

ReceiveBufSize     Specifies the size in bytes of a receive buffer.  The
                   default value is 256.  This parameter is a decimal
                   number in the range of 256 - 1536.

 ReceiveChains     Specifies the number of receive chain header queue
                   entries.  The default is 12.  This parameter is a
                   decimal number in the range of 6 - 24.


6.0	ERROR MESSAGES

No SMC8003 Adapters Specified In Protocol.INI Present !

	No adapter is installed.  Install a Standard Microsystems Ethernet card.

	No PROTOCOL.INI entries found for this driver.  Ensure that a
	PROTOCOL.INI entry exists with DriverName = SMCMAC$ (or SMCMAC2$).

	Checksum of IOBase is incorrect.  Cycle power on the system.
 	Try configuring the adapter to an alternate IOBase.  If the
	problem persists,  consult your adapter vendor.
	

Protocol.INI parameters do not match the adapter configuration.

	POS data or AT bus software configured adapter data does not match
	the PROTOCOL.INI entry.  Edit the PROTOCOL.INI file, adjusting the
	parameter values to correspond to the adapter configuration.


Conflicting SMC8003 Adapter Parameters Specified In Protocol.INI !

	More than one PROTOCOL.INI entry is found for this adapter.  Ensure that
	DriverName = SMCMAC$ (or SMCMAC2$) appears only once in PROTOCOL.INI.
	

Unknown SMC8003 Family Board ID !

	The adapter installed is not supported by this driver.
	Consult your adapter vendor for more information.
	

A parameter value in the Protocol.INI file is out of range.

	One of the parameters in the PROTOCOL.INI file entry for this adapter
	is out of range.  Consult the INSTALL.DOC file you received with the
	driver for valid parameter values.
	





Trademarks:

Microsoft OS/2 LAN Manager is a trademark of Microsoft
Corporation.  3Com, 3+, 3+Open and EtherLink II are registered trademarks 
of 3Com Corporation.  EtherCard PLUS, EtherCard PLUS16 StarCard PLUS, 
StarLink PLUS and SuperDisk are trademarks of Standard Microsystems Corporation.