Upgrading from v3.01 to v3.02
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

     Upgrading from v3.01 is sample, you can replace the following files
     with the new ones

         TM.EXE          the main program
         TM.OVL          the main program (overlay)
         TM.RES          the resource file
         TMINST.EXE      the installation program
         TMS.EXE         the script compiler
         TMPHONE.EXE     the phone directory maintainance program
         TMSTAT.EXE      the usage statistic program
         HOST.SCR        the host script (inside HOST.EXE)

     You can use your old TM.CFG. There is no change in the configuration
     file. However, you are encourage to change dial prefix #1 in TM.CFG
     from
         DialPrefix1="AT D"
     to
         DialPrefix1="AT DT"
     Some users are not aware that there is a prefix pointer in the phone
     directory.

     The old script files (both *.SCR and *.TMS) are fully compatible with
     the new ones.

     All the updated files have a 6-23-92 3:02a time stamp, while unchanged
     files have a 1-03-92 3:01a time stamp.




 Upgrading from v2.xx to v3.02
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

     This upgrade procesure assumes that you have Telemate already installed
     in the directory \TM,

     1. Before you do anything, MAKE A BACKUP of the \TM directory. You WILL
        NEED some files from it later.
     2. Copy all files (or extract them from the .ZIP) to \TM. You can
        overwrite all the files.
     3. Copy the TM.CFG from your backup to \TM and at the DOS prompt run
        "UPGRADE TM.CFG".
     4. Copy the TM.FON and TM.MEM from your backup to \TM.
     5. Delete all *.TMS files.
     6. Run TMINST.EXE to check if all the options are setup correctly.
     7. If you are using the HOST script, you can run HOST.EXE to extract
        the host script, copy the HUSER.HST from the backup to \TM and
        then run the script HCONFIG.SCR to setup the host mode.

     If you want to install v3.02 in a different directory, say C:\TM3,

     1. Copy all the files (or extract them from .ZIP) to C:\TM3.
     2. Copy the TM.CFG from \TM to C:\TM3 and at the DOS prompt run
        "UPGRADE TM.CFG".
     3. Edit TM.CFG and changes the lines to
            DirTelemate="C:\TM3\"
            DirScript="C:\TM3\"
        * It is VERY IMPORTANT that you have the directory set up correctly.
          Otherwise, Telemate will not run.
     4. Edit your AUTOEXEC.BAT and change (or add) the line
            SET TMCFG=C:\TM3\TM.CFG
     5. Copy the TM.FON and TM.MEM from \TM to C:\TM3.
     6. Run TMINST.EXE to check if all the options are setup correctly.

     Notes:
     1. The new *.MAC and *.PAD are not compatible with the old ones. You
        will have to set up your macro again.
     2. If you are using a 101-key keyboard, you should turn ON the 'Enhanced
        Keyboard' option under the Options/Mouse & Keyboard dialog.
     3. The VT102 keypad table is changed in order to emulate the actual
        terminal more accurately. Please refer to Appendix B in the file
        TELEMATE.DOC for details on the keyboard assignment.