//			Troubleshooting
//
//   In the intervening time between releases, I have learned a
//   lot about how the glove behaves in different situations.
//   If you are experiencing problems such as jumpiness or
//   dimensions not responding, read the following very carefully.
//   Most problems with glove accuracy can be attributed to
//   one or more of the following conditions (in order of
//   commonness):
//
//	1) Sensors on or near hard, smooth surfaces.
//   This problem can be difficult to correct.  The ideal
//   place to use the glove is in a 20' x 20' "room" with
//   ALL WALLS (and ceiling) CARPETED.  You want to get as close
//   to this ideal as you can.  Try taping a thick blanket up
//   against a wall and attaching the sensors directly to the
//   blanket.  If its still not good enough, start putting blankets
//   up on other walls.  You will notice dramatically better
//   response the "softer" your make your environment.  The problem
//   results because the ultrasonic waves emitted by the glove
//   (and measured by the sensors) tend to bounce off smooth
//   hard surfaces.  The circuitry interprets the glove
//   position based on the assumption that the waves are coming 
//   DIRECTLY FROM THE GLOVE.  Waves that have been reflected off
//   ANY object in the room WILL be interpreted incorrectly, and
//   WILL cause the glove to seem "glitchy" or prevent the
//   glove cursor from sensing certain positions correctly.
//   "Soft" surfaces made of thick fabric dampen the waves
//   enough to keep the sensors from getting confused.
//   I know it is disappointing to learn that the sensors do
//   NOT belong on a computer monitor, or for that matter a TV,
//   but I'm telling you the truth.
//
//      2) Objects between glove and sensors.
//   It should be obvious that the ultrasonic waves cannot travel
//   through objects on their path to the sensors.  Less obviously,
//   objects that are simply in the vicinity of the path between
//   the glove and the sensors will reflect ultrasonic waves and
//   cause problems as described in #1.
//
//	3) User too near or too far from sensors.
//   You should keep the glove between five and ten feet away from
//   the sensors.  If the glove gets too close, it will become
//   unable to sense certain positions, and perhaps even fail
//   to detect changes on an entire axis.  If the glove gets too
//   far away, it will "move" even when you hand is still.  Also,
//   the position reported will be "grainier" that is, it will
//   lose resolution.
//   
//	4) Connector is wired incorrectly.
//   If you have verified all of the above and the glove still
//   fails to work as expected, you should check the wiring.
//   Another easily overlooked factor is the voltage.  Though I
//   have not experimented with this, I've read messages which
//   state that the voltage MUST be between +4.5V and +5.5V.
//   If you are using the 5V wire from your computer, there's
//   nothing to worry about as long as your computer behaves
//   normally.  The keyboard connector and the joystick connector
//   also have reliable 5V wires.
//
//   The only other possible problem could be that your computer is
//   too slow for the software (very unlikely) or the software is
//   incompatible with your computer, which is nearly impossible.
//
//   GLITCHY RESPONSE IS NOT THE FAULT OF THIS CODE!  There is VERY
//   little I could do with software to eliminate the problems
//   with shadowing (#1 and #2 above).  But you need NOT get used
//   to it!  My glove is responding near the accuracy of a mouse!!
//   Yours can too!
//
//   Thanks to Chris Babcock for suggesting the use of "soft"
//   surfaces in the glove's environment.
//
//	Copyright 1992   Mark Thomas Pflaging