SCAN_OS2 Version BETA 97
                Copyright (C) 1989 - 1992 by McAfee Associates
                             All rights reserved.

                       Documentation by Aryeh Goretsky.

























               McAfee Associates            (408) 988-3832 office
               3350 Scott Blvd, Bldg. 14    (408) 970-9727 fax
               Santa Clara, CA  95054       (408) 988-4004 BBS (32 lines)
               U.S.A.                       USR HST/v.32/v.42bis/MNP1-5
                                            CompuServe    GO VIRUSFORUM
                                            InterNet  mcafee@netcom.COM




                                      TABLE OF CONTENTS:


          SYNOPSIS . . . . . . . . . . . . . . . . . . . . . . . . . . .2
            - What is SCAN_OS2?
            - System requirements

          AUTHENTICITY . . . . . . . . . . . . . . . . . . . . . . . . .2
            - Verifying the integrity of SCAN_OS2

          WHAT'S NEW . . . . . . . . . . . . . . . . . . . . . . . . . .4
            - New features and viruses in this release

          OVERVIEW . . . . . . . . . . . . . . . . . . . . . . . . . . .5
            - General description of SCAN_OS2

          OPERATION and OPTIONS. . . . . . . . . . . . . . . . . . . . .7
            - How to use SCAN_OS2, detailed explanation of switches

          EXAMPLES . . . . . . . . . . . . . . . . . . . . . . . . . . .14
            - Samples of frequently-used options

          EXIT CODES . . . . . . . . . . . . . . . . . . . . . . . . . .15
            - For running SCAN_OS2 from batch files

          VIRUS REMOVAL. . . . . . . . . . . . . . . . . . . . . . . . .15
            - How to manually remove a virus

          REGISTRATION . . . . . . . . . . . . . . . . . . . . . . . . .16
            - How to register SCAN_OS2

          TECH SUPPORT . . . . . . . . . . . . . . . . . . . . . . . . .16
           - Information you should have ready when calling

          APPENDIX A . . . . . . . . . . . . . . . . . . . . . . . . . .17
           - Creating a virus string file with the /EXT option

          APPENDIX B . . . . . . . . . . . . . . . . . . . . . . . . . .18
           - How to check only memory for viruses
           - Validation codes:  Tips and Tricks
           - Reformatting infected floppies with DOS 5.00
           - Creating a Recovery Disk








                                              Page 1


SCAN_OS2 Version BETA 97                                Page 2

          SYNOPSIS

               SCAN_OS2 (VIRUSCAN for OS2) is a virus detection and
          identification program for IBM PC and compatible computers.
          SCAN will search a PC for known computer viruses in memory,
          the partition table, the boot sector and the files of a PC
          and disks.  SCAN_OS2 can also detect the presence of unknown
          viruses.
               SCAN_OS2 works by searching the system for sequences of bytes
          unique to each computer virus and then reporting their presence
          when found.  This method works for viruses recognized by SCAN.
          SCAN also checks for new/unknown viruses by looking for virus-
          like code patterns, plus comparisons against previously-stored
          validation (checksum) data.  When the enhanced validation mode
          is used, CLEAN-UP can restore infected partition tables, boot
          sectors, or files infected by unknown (new) viruses (See OPTIONS
          for more information on enhanced validation).  The data for the
          enhanced validation mode can be stored off-line on disks as a
          "Recovery Disk" in case of infection by an unknown virus.
          SCAN_OS2 can also check for new viruses from a user-created list
          of virus search strings.
               SCAN_OS2 requires 320Kb of RAM and DOS 2.0 or above (some
          features require DOS 3.1 or above).

          AUTHENTICITY

               SCAN_OS2 performs a self-check when run.  If SCAN has been
          modified in any way, a warning will be displayed and the user
          will be prompted to either continue or quit.  SCAN can still
          check for viruses, however, if SCAN reports that it has been
          damaged, it is recommended that a clean copy be obtained.
               SCAN versions 46 and above are packaged with the VALIDATE
          program to ensure the integrity of the SCAN_OS2.EXE file.  The
          VALIDATE.DOC file tells how to use VALIDATE.  VALIDATE can be
          used to check subsequent versions of SCAN for tampering.

               The validation results for Version BETA 97 should be:

                        FILE NAME: SCAN_OS2.EXE
                             SIZE: 157,188
                             DATE: 10-05-1992
              FILE AUTHENTICATION
                   Check Method 1: F6AF
                   Check Method 2: 04CE

          If your copy of SCAN differs, it may have been damaged or have
          options stored in it with the /SAVE switch.  Run SCAN with only
          the /SAVE option to remove any stored options and then re-run
          VALIDATE.  Always obtain your copy of SCAN_OS2 from a known
          source.  The latest version of SCAN_OS2 and validation data for
          SCAN.EXE can be obtained from McAfee Associates' bulletin board
          system at (408) 988-4004 or from the Computer Virus Help Forum
          on CompuServe (GO VIRUSFORUM).

SCAN_OS2 Version BETA 97                                Page 3


               Beginning with Version 72, all of McAfee Associates'
          SCAN_OS2 series are archived with PKWare's PKZIP Authentic File
          Verification.  If you do not see an "-AV" after every file is
          unzipped and receive the "Authentic Files Verified! # NWN405
          Zip Source: McAFEE ASSOCIATES" message when you unzip the files
          then do not use them.  If your version of PKUNZIP does not have
          verification ability, then this message may not be displayed.
          Please contact us if you believe tampering has occured to the
          .ZIP file.


















                    [This space intentionally left blank]

























SCAN_OS2 Version BETA 97                                Page 4


          WHAT'S NEW

               Version BETA 97 adds detection of 68 new viruses, bringing
          the total number of known viruses to 753, or counting variants,
          1,469.  For a complete description of known viruses please
          refer to Patricia Hoffman's VSUM.
               Viruses reported at multiple sites include the Cansu, a
          floppy disk boot sector and hard disk partition table infector
          that encrypts its own code.  The virus keeps track of how many
          diskettes it has infected and on every 64th infection displays
          a "V" sign.

               Beginning in Version 90, we have started optimizing our
          virus search strings by grouping similar viruses together
          into generic virus detection strings.  This speeds up the
          SCAN_OS2 program by reducing the amount of virus strings it
          has to look for and makes the program file smaller by reducing
          the size of its virus string data.

          At the present stage, two features present in SCAN will not operate
          in SCAN_OS2. The self_check, and the ability to save
          command line options (/SAVE). We are working on
          implementing those two important feature, but wanted to get
          some feed back from our test sites.

















          THE COMPUSERVE COMPUTER VIRUS HELP FORUM

               We are now sponsoring the Computer Virus Help Forum on
          CompuServe.  Updates to the SCAN_OS2 series, information about
          computer viruses, and technical support may be obtained by
          typing GO VIRUSFORUM at any CompuServe prompt.  A free
          introductory membership to CompuServe is also available.  For
          more information, please read the COMPUSER.NOT file.



SCAN_OS2 Version BETA 97                                Page 5


          OVERVIEW

               SCAN_OS2 is designed to work with stand-alone and networked
          PC's, for file servers use the NETSCAN program instead.
               SCAN checks files, subdirectories, diskettes or entire
          systems for pre-existing computer virus infections.  It will
          identify the virus infecting the system and the area where it
          was found.  Infected files can be removed either with the /D
          overwrite-and-delete option in SCAN which will erase the file,
          or with the CLEAN-UP universal virus disinfection program.  The
          CLEAN-UP program is recommended because in most cases it
          eliminates the virus and fully restores the program or system
          area.
               SCAN_OS2 Version BETA 97 identifies all 685 known computer
          viruses and their variants.  Some viruses have been modified so
          that more than one "strain" exists.  Counting modifications,
          there are 1,401 viruses.  This includes the twenty most common
          viruses which account for over 95% of all reported infections.
          The accompanying VIRLIST.TXT file lists describes all viruses
          identified by SCAN.
               All known viruses infect one or more of the following
          areas: the hard disk partition table (alias Master Boot Record);
          the DOS Boot Sector of disks; or one or more executable files on
          the system.  Executable files include operating system files,
          .COM files, .EXE files, overlay files, or any other files
          containing program code.  A virus that infects more than one
          area, such as a boot sector and an executable file is called
          a multipartite virus.
               SCAN_OS2 identifies every system area or file infected,
          and gives the name of the virus and the I.D. code used with
          CLEAN-UP to remove it.
               SCAN_OS2 can also check for unknown viruses with the Check
          Validation options (/CV, /CG and /CF).  This is done by
          calculating a checksum for files and system areas and then
          comparing against that checksum.  The checksum can be stored at
          the end of .COM and .EXE files or saved to a user-specified file
          which can then be stored offline (e.g., on floppies) for
          recovery purposes.  If the file has been modified, the check
          will no longer match, indicating that viral infection may have
          occurred.  When run in the Enhanced Validation (/CG or /CF)
          modes, information will be saved that can be used to restore
          files or areas of the system that have been damaged by
          unknown (new) viruses.
               SCAN_OS2 calculates checksums using two independently-
          generated CRC's (Cyclic Redundancy Check).  Files which are
          self-checking (e.g., Lotus 1-2-3) should not be validated with
          the /AV (Add Validation) or /AG (Add Generic) switches which
          modify files.  Instead, use the /AF (Add File) switch, which
          stores its data in a separate file.  See the entries for /AF,
          /AG, and /AV under OPERATION and OPTIONS for more information.



SCAN_OS2 Version BETA 97                                Page 6


               When SCAN is run with the /AV or /AG switches it adds
          validation codes to .COM and .EXE files only.  The validation
          codes for the partition table, boot sector, and system files are
          kept in a hidden file called SCANVAL.VAL in the root directory.
               SCAN_OS2 can check for unknown (new viruses) in the boot
          sector and partition table.  When virus-like code is found in
          either area SCAN indicates it has found a Generic Boot Sector
          or MBR Virus, respectively.
               SCAN_OS2 can be updated to search for new viruses by an
          External Virus Data File, which allows the user to input new
          search strings for viruses.
               After seven months have passed SCAN_OS2 will display a
          message that it may no longer be current.  However, SCAN will
          continue to function as normal.  This message can be bypassed
          by running SCAN with the /NOEXPIRE switch.
               SCAN_OS2 displays messages in English, French, or Spanish.





































SCAN_OS2 Version BETA 97                                Page 7


          OPERATION and OPTIONS

          IMPORTANT NOTE:  WRITE PROTECT YOUR FLOPPY DISK BEFORE SCANNING
                           TO PREVENT INFECTION OF THE SCAN_OS2 PROGRAM.

               SCAN_OS2 checks files and other areas of the system that
          can contain a computer virus.  When a virus is found, SCAN
          identifies the virus and the file or system area where it was
          found.
               SCAN examines files based on their extension.  The default
          extensions supported by SCAN are .APP, .BIN, .COM, .EXE, .OV?,
          .PGM, .PIF, .PRG, .SWP, .SYS, and .XTP.  Additional extensions
          can be added with the /EXT option, or use the /A to check all
          files on the disk.


          Valid options for SCAN_OS2 are:

          SCAN d1: ... d26:   /? /A /AF filename /AG filename /AV filename
                              /BELL /CERTIFY /CF filename /CHKHI /CG /CV
                              /D /DATE /E .xxx .yyy .zzz /EXT filename
                              /FAST /FR /H /HELP /HISTORY filename /MAINT
                              /MANY /NLZ /NOBREAK /NOEXPIRE /NOMEM /NOPAUSE
                              /NPKL /REPORT filename /RF filename /RG /RV
                              /SAVE /SHOWDATE /SP /SUB /UNATTEND @filename

          Options are:

                         \ - Scan root directory and boot area only
               /? /H /HELP - Display help screen
                        /A - Scan all files, including data, for viruses
              /AF filename - Store recovery data/validation codes to file
              /AG filename - Add recovery data/validation codes to files
                             EXCEPT those listed in filename
              /AV filename - Add validation codes to files EXCEPT those
                             listed in filename
                     /BELL - Beep whenever a virus is found
                  /CERTIFY - List files that do not have a validation code
              /CF filename - Check for viruses using recovery data/
                             validation codes stored in filename
                    /CHKHI - Check memory from 0Kb to 1088Kb
                       /CG - Check recovery data/validation codes on files
                       /CV - Check validation codes on files
                        /D - Overwrite and delete infected file
                     /DATE - Save the date and time SCAN_OS2 was last run
                             (use /SHOWDATE to display date and time)
              /E .xxx .yyy - Scan overlay extensions .xxx .yyy .zzz
             /EXT filename - Scan using external virus data file
                     /FAST - Speed up SCAN_OS2's output
                             (see below for specifics)



SCAN_OS2 Version BETA 97                                Page 8


                       /FR - Display messages in French
          /HISTORY filenam - Create infection log, appending to old log
                        /M - Scan memory for all viruses
                             (see below for specifics)
                    /MAINT - Scan "invalid media" error (damaged) disk
                     /MANY - Scan multiple floppies
                      /NLZ - Skip internal scan of LZEXE-compressed files
                  /NOBREAK - Disable Ctrl-C and Ctrl-Brk during scanning
                 /NOEXPIRE - Do not display expiration notice
                    /NOMEM - Skip memory checking
                  /NOPAUSE - Disable screen pause when scanning
                     /NPKL - Skip internal scan of PKLITE-compressed files
          /REPORT filename - Create infection log, deleting old log
              /RF filename - Remove recovery data/validation codes stored
                             in filename
                       /RG - Remove recovery data/validation codes from
                             files
                       /RV - Remove validation codes from specified files
                     /SAVE - Save specified command line options as new
                             defaults
                 /SHOWDATE - Show date and time SCAN was last run
                             (use /DATE to save date and time)
                       /SP - Display messages in Spanish
                      /SUB - Scan subdirectories under a subdirectory
                 /UNATTEND - Scan using DOS critical error handler
                 @filename - Scan using options from configuration file

              (d1: ... d26: indicate drives to be scanned)


               The /A option checks all files on the drive scanned.  This
          substantially increases the time required to scan disks, so
          it is recommended this swich only be used when installing new
          software or if a file-infecting virus has been found.  This
          option takes priority over the /E option.
               The /AF option logs recovery data and validation codes
          for .COM and .EXE files, boot sector, and partition table of a
          disk to a user-specified file that can be located on any drive.
          The size of the file is about 20K per 1,000 files validated.
          The syntax is /AF filename, where "filename" is the path and
          file where recovery data and validation codes are stored.
               The /AG option allows the user to store recovery data and
          validation codes for .COM and .EXE files, boot sector, and
          partition table of a disk.  Recovery information adds fifty-two
          (52) bytes to files.  The recovery information for the partition
          table, boot sector, COMMAND.COM and system files is stored
          seperately in a hidden file called SCANVAL.VAL in the root
          directory of the drive being scanned.  It is otherwise similar
          to the /AV option below.  Recovery requires the CLEAN-UP
          (CLEAN.EXE) program.



SCAN_OS2 Version BETA 97                                Page 9


               The /AV option allows the user to add validation codes to
          .COM and .EXE files being scanned.  If the whole drive is
          specified, SCAN will create validation data for the partition
          table, boot sector, COMMAND.COM and system files and store them
          seperately in a hidden file called SCANVAL.VAL in the root
          directory of the drive being scanned.  Validation adds ten (10)
          bytes to files; the validation data for the partition table,
          boot sector, and system files is stored separately in a hidden
          file named SCANVAL.VAL in the root directory of the scanned
          drive.  Files which are immunized against viruses or contain
          self-modifying code should not have validation codes added to
          them.  To prevent SCAN from adding validation codes to these
          files, a validation exception list must be created with the path
          and filename of each file NOT to be validated listed on each
          line.  Only one file should be on a line.  To put a comment in,
          start a line with the asterisk "*" character.  This sample file
          contains a list of programs NOT to validate:

          *This is Nantucket Corp's database program, Clipper
          C:\CLIPPER\BIN\CLIPPER.EXE
          *This is Lotus Development Corp's spreadsheet program, 1-2-3
          C:\123\123.COM
          *This is MS-DOS 5.00's self-modifying program, SETVER
          C:\DOS\SETVER.EXE
          *PKWare's data compression programs already perform a self-check
          C:\PKWARE\PKLITE.EXE
          C:\PKWARE\PKZIP.EXE
          C:\PKWARE\PKUNZIP.EXE
          *Stac Technologies hard disk swapping program
          C:\SWAPVOL.COM
          *Symantec's Norton Utilities V6.01 disk caching program
          C:\NORTON\NCACHE.EXE
          *WordStar Corp's word processor is self-modifying
          C:\WORDSTAR\WS.EXE

          The validation exception list should be an ASCII text file.  If
          a word processor is used to create the list, be sure to save
          the file as ASCII.
               The /BELL option will cause SCAN_OS2 to beep each time a
          computer virus is found.
               The /CERTIFY option will audit a system for files that have
          validation codes added to them with the /AG or /AV switches.
          Files that have no validation code will be reported as being
          uncertified by SCAN_OS2 and an ERRORLEVEL of 3 will be returned
          after SCAN is run.
               The /CF option checks recovery data and validation codes
          added by the /AF option.  The syntax is /CF filename, where
          "filename" is the path and file name where recovery data
          and validation codes are stored.




SCAN_OS2 Version BETA 97                                Page 10


               The /CG option checks recovery data and validation codes
          added by the /AG option.  If a file or system area has changed,
          SCAN will report that the file or system area has been modified
          and a viral infection may have occurred.  The /CG option takes
          priority over the /CV option.
               The /CHKHI option checks the memory above 640Kb that can be
          used on AT (286) and 386 systems for computer viruses.  This
          includes the 384Kb Upper Memory Area from 640Kb to 1024Kb, and
          the 64Kb High Memory Area from 1024Kb to 1088Kb.  On XT systems
          with extended memory cards installed, this will cause the first
          64K of RAM to be scanned again.  This option cannot be used
          with the /NOMEM option.
               The /CV option checks validation codes inserted by the /AV
          option.  If a file or system area has been changed, SCAN will
          report that the file or system area has been modified and a
          viral infection may have occurred.  Using the /CV option adds
          about 25% more time to scanning.  

          NOTE:  Some older Hewlett Packard and Zenith PC's modify the
          boot sector each time the system is booted.  This will cause
          SCAN to continually notify the user of boot sector modifications
          if the /CV switch is selected.  Check your system's manual to
          determine if your system contains self-modifying boot code.

               The /D option tells SCAN_OS2 to prompt the user to
          overwrite and delete an infected file when one is found.  A file
          erased by the /D option cannot be recovered.  If the CLEAN-UP
          program is available, it can be used to disinfect the file.
          Boot sector and partition table infectors cannot be removed by
          the /D option and require the CLEAN-UP virus removal program.
               The /DATE option stores the time and date the SCAN_OS2
          program was last run.  This is done by changing the date on the
          SCANVAL.VAL file.  If no such file exists, SCAN will create a
          0-byte long SCANVAL.VAL file in the currently-logged directory.
               The /E option allows the user to specify an extension or
          set of extensions to scan.  Extensions should include a period
          "." and should also be separated by a space after the /E.  Up to
          three extensions may be added with the /E.  For more extensions,
          use the /A option.
               The /EXT option allows SCAN_OS2 to search for viruses from
          a text file containing user-defined search strings in addition
          to the viruses that SCAN already identifies.  The syntax for
          using the external virus data file is /EXT d:filename, where d:
          is the drive name and filename is the name of the external virus
          data file.  For instructions on how to create an external virus
          data file, refer to Appendix A.

          NOTE:  The /EXT option provides users with the ability to add
                 strings for detection of viruses on an interim or
                 emergency basis.  When used with the /D option, it will
                 overwrite-and-delete infected files.  This option is not
                 for general use and should be used with caution.

SCAN_OS2 Version BETA 97                                Page 11


               The /FAST option will speed SCAN up by displaying fewer
          messages on the screen, skipping checking inside of LZEXE- and
          PKLITE-compressed files, and examining a smaller portion of
          files during scanning.  This may reduce the accuracy of SCAN.
               The /FR option tells SCAN_OS2 to output all messages in
          French instead of English.  The /FR option cannot be used with
          the /SP (Spanish) option.
               The /HISTORY option saves a list of infected files to
          disk.  The list is saved to disk as an ASCII text file.  If a
          list exists, then the results of the current scan will be added
          to the end.  The syntax is /HISTORY filename, where "filename"
          is the path and name of the report file.
               The /M option tells SCAN_OS2 to check system memory for all
          known computer viruses that can inhabit memory.  SCAN by default
          only checks memory for critical and "stealth" viruses, which are
          viruses which can cause catastrophic damage or spread the virus
          infection during the scanning process.  By default, SCAN will
          check memory for the following viruses:

             1024           1253          1554          1963
             1971           2560          337           3445-Stealth
             4096           512           Anthrax       Antitelefonica
             Brain          Caz           CD            Dark Avenger
             Dir-2          Doom II       Empire        Fish
             Flu-2          Form          Greemlin      Irish
             Joshi          Leech         Lozinsky      Microbes
             Mirror         Nomenklatura  NOP           No-Int (Stoned III)
             P1R (Phoenix)  Phantom       Plastique     Pogue
             SBC            Sentinel      Stoned        Sunday-2
             SVC            Taiwan3       Tequila       Turbo (Polish-2)
             Twin-351       V2100         V2P6          Whale

          If one of these viruses is found in memory, SCAN will stop and
          tell the user to power down, and reboot the system from a virus-
          free system-bootable disk.  The /M option adds 6 to 20 seconds.

          NOTE:  Using the /M option with another anti-viral software
                 package may result in false alarms if the other package
                 does not remove its virus search strings from memory.

               The /MAINT option is used to scan hard disks partitioned
          with DOS 4.0 or above that have been damaged by a boot sector
          or partition table infecting virus.  Attempts to access disks
          damaged in such a manner result in an "invalid media" message
          being displayed.  The /MAINT option will only scan the partition
          table and boot sector, not the files.
               The /MANY option is used to scan multiple diskettes placed
          in a given drive.  If the user has more than one floppy disk to
          check for viruses, the /MANY option will allows the user to
          check disks without having to re-run SCAN multiple times.
          After the system has been disinfected, the /MANY and /NOMEM
          options can be used together to speed up the scanning of disks.

SCAN_OS2 Version BETA 97                                Page 12


               The /NLZ option tells SCAN not to look inside files
          compressed with LZEXE, a file compression program.  SCAN will
          still check the LZEXE-compressed files for viruses that have
          infected after file compression.
               The /NOBREAK option prevents Ctrl-C or Ctrl-Brk from
          aborting the scanning process.
               The /NOMEM option is used to turn off all memory checking
          for viruses in order to speed up the scanning process.  It
          should only be used when a system is known to be virus-free.
          The /NOMEM option can not be used with the /CHKHI or /M options.
               The /NOEXPIRE option disables the warning message that
          SCAN displays after seven months warning that it may no longer
          be current with respect to known computer viruses.
               The /NOPAUSE option disables the "More? (H = Help )" prompt
          that is displayed when SCAN fills up a screen with messages.
          This allows SCAN to run on PC's with severe infections without
          requiring operator assistance.
               The /NPKL option tells SCAN not to look inside files
          compressed with PKLITE, a file compression program.  SCAN will
          still check the PKLITE-compressed files for viruses that have
          infected after file compression.
               The /REPORT option saves a list of infected files to
          disk.  The list is saved to disk as an ASCII text file.  If a
          list exists, then it will be overwritten with the new list.
          The syntax is /REPORT filename, where "filename" is the path
          and name of the report file.
               The /RF option will remove recovery data and validation
          codes for files from the recovery data and validation code
          file.  The syntax is /RF filename, where "filename" is the path
          and file where recovery data and validation codes are stored.
               The /RG option will remove validation codes and recovery
          information from files validated with the /AG option.
               The /RV option is used to remove validation codes from a
          file or files.  It can be used to remove the validation code
          from a diskette, subdirectory, or file(s).  Using /RV on a disk
          will remove the partition table, boot sector, and system file
          validation.  This option cannot be used with the /AV option.
               The /SAVE option is used to store SCAN options for
          subsequent executions of SCAN.  Options are stored by modifying
          the SCAN.EXE executable file.  For example:

               SCAN /NOMEM /REPORT FILE1 /NOPAUSE /SAVE

          will set the default options to /NOMEM, /REPORT and /NOPAUSE.
          If SCAN is run with just the /SAVE switch, then all options are
          removed and SCAN execute with its original settings.
               If you do not wish to modify the SCAN.EXE file, use the
          @filename option instead, which allows you to store the SCAN
          options in a separate text file.




SCAN_OS2 Version BETA 97                                Page 13


          NOTE:  VALIDATE 0.4 must be used to validate SCAN version 89 or
                 above if /SAVE is used.  /SAVE directly modifies SCAN.EXE
                 and the validate codes will no longer match if an older
                 version of VALIDATE is used.  VALIDATE 0.4 will generate
                 the correct validation results even if the /SAVE option
                 has been used.  Third party file-integrity check programs
                 may not produce the same results after the /SAVE option
                 is used.  The /SAVE option should be added to SCAN by the
                 Systems Administrator prior to final installation on PC's
                 if other integrity checking programs are in use.

               The /SHOWDATE option displays the time and date that SCAN
          was last run.  No virus checking is performed

          NOTE:  When run with /SHOWDATE, SCAN only displays the last run
                 date.  Viruses will *NOT* be checked for.

               The /SP option tells SCAN_OS2 to output all messages in
          Spanish instead of English.  This option can not be used with
          the /FR (French) option.
               The /SUB scans all subdirectories inside a subdirectory.
          Previously, SCAN would only recursively check subdirectories
          if a logical device (e.g., C:) was scanned.
               The /UNATTEND option tells SCAN_OS2 use the DOS critical
          error handler when accessing files.  If SCAN accesses a file
          which is in use by another program, it will continue scanning
          instead of displaying an error message.  This option requires
          DOS 3.10 or above.

          NOTE:  The /UNATTEND switch is required if you are running
                 SCAN from a DOS session inside Windows or OS/2.

               The @FILENAME option allows the user to store a list of
          options and/or system areas to be scanned in a configuration
          file.  Options need to be separated by a space, while system
          areas (disks, subdirectories, or files) need to be on separate
          lines.  A sample file might look like this:

          /A /BELL /CV /NOMEM /REPORT C:\SCAN_OS2\SCAN.LOG
          C:
          D:\BBS
          E:\MCAFEE\CLEAN-UP\CLEAN.EXE

          The first line contains the SCAN_OS2 options while other lines
          contain the names of disks, subdirectories, or files to scan.
          The configuration file should be an ASCII text file.  If a word
          processor is used to create the list, be sure to save as ASCII.






SCAN_OS2 Version BETA 97                                Page 14


          EXAMPLES

               The following examples show different option settings:

               SCAN C:
                   To scan drive C:

               SCAN A:R-HOOPER.EXE
                   Scans file "R-HOOPER.EXE" on drive A:

               SCAN A: /A /CV
                   To scan all files and check validation codes for unknown
                   viruses on drive A:.

               SCAN B: /D /A
                   Scans all files on drive B: and prompt for erasure of
                   any infected files, if found.

               SCAN C: D: E: /AV /NOMEM
                   To add validation codes to files on drives C:, D:, and
                   E:, and skip memory checking.

               SCAN C: D: /M /A /FR
                   Scan memory for all viruses, all files on drives C: and
                   D:, and output all messages in French.

               SCAN C: D: /E .WPM .COD
                   Scans drives C: and D:, including .WPM and .COD files 

               SCAN C: /EXT A:SAMPLE.ASC /BELL
                   To scan drive C: for known computer viruses and also
                   for viruses added by the user via the external virus
                   data file option, and beep whenever a virus is found.

               SCAN C: /M /NOPAUSE /REPORT A:INFECTN.RPT
                   To scan for all viruses in memory and drive C: without
                   stopping, and create a log file INFECTN.RPT on drive A:

               SCAN C: D: /NOPAUSE /REPORT B:VIRUS.RPT
                   To scan drives C: and D: for viruses without stopping,
                   and create a log on drive B: called VIRUS.RPT

               SCAN E:\DOWNLOADS /SUB
                   To scan all subdirectories under DOWNLOADS on drive E:

               SCAN C: D: E: /FAST /CERTIFY
                   To perform a fast scan of drives C:, D:, and E: and
                   check for any files that do not have validation codes.

               SCAN @C:\SCANOPTN.LST
                   To run SCAN_OS2 using configuration file SCANOPTN.LST
                   in the root directory of drive C:.

SCAN_OS2 Version BETA 97                                Page 15


          EXIT CODES

               After SCAN_OS2 has finished running, it will set the DOS
          ERRORLEVEL.  ERRORLEVEL's are used in batch files to pass the
          results of a program's actions.  The ERRORLEVEL's returned by
          SCAN are:

               ERRORLEVEL ³ DESCRIPTION
               ÍÍÍÍÍÍÍÍÍÍÍØÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
                   0      ³ No viruses found
                   1      ³ One or more viruses found
                   2      ³ Abnormal termination (program error)
                   3      ³ One or more uncertified files found
                   4      ³ Ctrl-C or Ctrl-Break aborted scan

          If a user stops the scanning process, SCAN will set the
          ERRORLEVEL to 3.  The /NOBREAK option can be used to prevent
          users from stopping SCAN.


          VIRUS REMOVAL

               What do you do if a virus is found?  You can contact McAfee
          Associates for help by BBS, FAX, telephone, Internet, or
          CompuServe.  There is no charge for support calls to McAfee
          Associates.
               The CLEAN-UP universal virus disinfection program can
          disinfect virtually all reported computer viruses.  It is
          updated with each release of the SCAN program to remove new
          viruses.  CLEAN-UP can be downloaded from McAfee Associates'
          BBS, the SIMTEL20 archives on the InterNet, the Computer Virus
          Help Forum on CompuServe, or from any of the agents listed in
          the enclosed AGENTS.TXT text file.
               It is strongly recommended that you get experienced help in
          dealing with viruses if you are unfamilar with anti-virus
          software and methods.  This is especially true for 'critical'
          viruses and partition table/boot sector infecting viruses as
          improper removal of these viruses can result in the loss of
          all data and the use of the infected disk(s).  [For a listing of
          critical viruses, see the /M switch listed under OPTIONS above.]
               For qualified assistance in removing a virus, please
          contact McAfee Associates directly or any of the Authorized
          McAfee Associates Agents in your area.  Agents may charge McAfee
          Associates' normal support rates for their services.
               If you wish to remove a file-infecting virus manually, you
          can run SCAN with the /A and /D switches to erase all infected
          files.
               Before removing a boot sector or partition table-infecting
          virus, it is recommended that you cold boot the infected PC from
          a clean DOS disk and backup any critical data.



SCAN_OS2 Version BETA 97                                Page 16


          REGISTRATION

               A registration fee of US$25.00 is required for the use of
          SCAN_OS2 by individual home users.  Registration entitles the
          holder to unlimited free upgrades from McAfee Associates' BBS
          or the Computer Virus Help Forum on CompuServe and technical
          support for one year.  When registering, a diskette containing
          the latest version may be requested for an additional US$9.00.
          Only one diskette mailing will be made.
               Registration is for home users only and does not apply to
          businesses, corporations, organizations, government agencies, or
          schools, which must obtain a license for use.  Contact McAfee
          Associates directly or an Authorized Agent for more information.


          TECH SUPPORT

               For fast and accurate help, please have the following
          information ready when you contact McAfee Associates:

               -    Program name and version number.

               -    Type and brand of computer, hard disk, plus any
                    peripherals.

               -    Version of DOS plus any TSRs or device drivers in use.

               -    Printouts of your AUTOEXEC.BAT and CONFIG.SYS files.

               -    A printout of what is in memory from the MEM command
                    (DOS 4 and above users only) or a similar utility.

               -    The exact problem you are having.  Please be as
                    specific as possible.  Having a printout of the
                    screen and/or being at your computer be will helpful.

          McAfee Associates can be contacted by BBS, CompuServe, FAX, or
          InterNet 24 hours a day, or by telephone at (408) 988-3832,
          Monday through Friday, 7:00AM to 5:30PM Pacific Time.

               McAfee Associates             (408) 988-3832 office
               3350 Scott Blvd. Bldg. 14     (408) 970-9727 fax
               Santa Clara, CA  95054-3107   (408) 988-4004 BBS (32 lines)
               U.S.A                         USR HST/v.32/v.42bis/MNP 1-5
                                             CompuServe     GO VIRUSFORUM
                                             Internet   mcafee@netcom.com

          If you are overseas, there may be an Authorized McAfee Associates
          Agent in your area.  Please refer to the AGENTS.TXT file for a
          listing of McAfee Associates Agents for support or sales.



SCAN_OS2 Version BETA 97                                Page 17
                                                          

          APPENDIX A:  Creating a Virus String File with the /EXT Option

          NOTE:  The /EXT option is intended for emergency and research
                 use only.  It is a temporary method for identifying new
                 viruses prior to the subsequent release of SCAN.  A
                 thorough understanding of viruses and string-search
                 techniques is advised for using this option.  A string
                 length of 10 to 15 bytes is recommended.

               The External Virus Data file should be created with an
          editor or a word processor and saved as an ASCII text file.  Be
          sure each line ends with a Carriage Return/Line Feed pair.


               The virus string file uses the following format:

          #Comment about Virus_1
          "aabbccddeeff..." Virus_1_Name
          #Comment about Virus_2
          "gghhiijjkkll..." Virus_2_Name
               .
               .
          "uuvvwwxxyyzz..." Virus_n_Name


          Where aa, bb, cc, etc. are the hexadecimal bytes that you wish
          to scan for.  Each line in the file represents one virus.  The
          Virus Name for each virus is mandatory, and may be up to 25
          characters in length.  The double quotes (") are required at the
          beginning and end of each hexadecimal string.
               SCAN will use the string file to search memory, the
          Partition Table, Boot Sector, System files, all .COM and .EXE
          files, and overlay files with the extension .APP, .BIN, .COM,
          .EXE, .OV?, .PGM, .PIF, .PRG, .SWP, .SYS, and .XTP.
               Virus strings may contain wild cards.  The two wildcard
          options are:

          FIXED POSITION WILDCARD
               The question mark "?" may be used to represent a wildcard
          in a fixed position within the string.  For example, the string:

                             "E9 7C 00 10 ? 37 CB"

          would match "E9 7C 00 10 27 37 CB", "E9 7C 00 10 9C 37 CB", or
          any other similar string, regardless of the fifth byte.








SCAN_OS2 Version BETA 97                                Page 18


          RANGE WILDCARD

               The asterisk "*", followed by range number in parentheses
          "(" and ")" is used to represent a variable number of adjoining
          random bytes.  For example, the string:

                             "E9 7C *(4) 37 CB"

          would match "E9 7C 00 37 CB", "E9 7C 00 11 37 CB", and
          "E9 7C 00 11 22 37 CB".  The string "E9 7C 00 11 22 33 44 37 CB"
          would not match since the distance between 7C and 37 is greater
          than four bytes.  You may specify a range of up to 99 bytes.
          Up to 10 different wildcards of either kind may be used in one
          virus string.
                                            

          COMMENTS
               A pound sign "#" at the begining of a line will denote a
          comment.  Use this for adding notes to the external virus data
          file.  For example:

                             #New .COM virus found in file FRITZ.EXE from
                             #Schneiderland on 01-22-91
                             "53 48 45 45 50" Fritz-1 [F-1]

          gives a description of the virus, name of the infected file,
          where and when it was found, etc.


          APPENDIX B:  Miscellaneous Application Notes


          CHECKING MEMORY FOR VIRUSES ONLY

               SCAN_OS2 can perform a quick check for viruses in memory
          only.  In this mode, SCAN will not check the disk for viruses.
          This option is useful for network administrators who need to
          check workstations for viruses before allowing them to log on to
          a LAN but cannot run the VSHIELD program due to memory
          constraints.  The command for this is:

               SCAN NUL /M /CHKHI

          By designating NUL as the drive to be scanned, SCAN will check
          system memory for viruses (up to 1088Kb if the /CHKHI option is
          used) and then return to DOS without scanning any disks.  SCAN
          returns the DOS ERRORLEVEL in the normal manner.






SCAN_OS2 Version BETA 97                                Page 19


          SCAN_OS2 VALIDATION CODES

               If you have installed any new software or programs on your
          system, and are running SCAN_OS2 or VSHIELD with the /CF, /CG,
          or /CV validation codes options, you will need to reinstall
          validation codes to the new files with the /AF, /AG, or /AV
          add validation codes options of SCAN.  In addition, the
          SCANVAL.VAL hidden file containing validation codes for the
          partition table, boot sector, COMMAND.COM, and system files may
          have to be replaced (unhide the file with the DOS ATTRIB command
          and then delete it).
               The quickest way to update the validation codes is to
          remove all validation codes from the hard disk and then add them
          back by running SCAN with the /RV and then the /AV options.

          NOTE: This applies to any new version of DOS, as well as any
          programs which you install on your system.


          REFORMATTING INFECTING FLOPPIES WITH DOS 5.00

               When reformatting infected floppy disks under DOS 5.0, be
          sure to add the /U switch to the FORMAT command.  This tells DOS
          to do an Unconditional Format of the disk, without saving the
          original infected boot sector of the disk.  This should be done
          to prevent the reinfection by unformatting the disk.


          CREATING A RECOVERY DISK USING THE /AF OPTION

               The /AF switch added in Version 90 of SCAN creates a
          separate file to store recovery data and validation codes.
          This file can be stored off-line (on a floppy disk, network
          drive, tape drive, etc.) and accessed on-demand to check for,
          and recover from,infection by unknown viruses.
               To create a Recovery Disk, format a system-bootable floppy
          and copy the SCAN_OS2 (SCAN.EXE) and CLEAN-UP (CLEAN.EXE) files
          to it.  Then run SCAN against the hard disk with the /AF option.
          For example:
                             SCAN C: D: /AF A:\SCANCRC.CRC

          will scan the C: and D: drives for known viruses and create
          a file named SCANCRC.CRC containing recovery data and validation
          codes.  After SCAN finishes, write-protect the disk.
               To check for virus infection, turn the PC off, insert the
          Recovery Disk, and turn the power back on.  The PC will now boot
          from the floppy disk.  At the DOS prompt, type:

                             SCAN C: D: /CF A:\SCANCRC.CRC

          to compare drives C: and D: against the recovery data stored
          in the SCANCRC.CRC file on the A: drive.

SCAN_OS2 Version BETA 97                                Page 20


               To disinfect your system, turn your PC off, insert the
          Recovery Disk, and turn the power back on.  The PC will now
          boot from the floppy disk.  At the DOS prompt, type:

                             CLEAN C: D: /GF A:\SCANCRC.CRC

          to restore drives C: and D: with the recovery data stored in the
          SCANCRC.CRC file on the A: drive.