README of PSERV2.ZIP	PTF-P-533
The following files are included with this release:

	pserver.nlm	51938	06-15-92	5:40p
	pserver.exe	108844	06-16-92	3:43p
	pserver.vap	65218	06-15-92	2:46p
	rprinter.exe	59756	06-04-92	10:40a
	pserv.doc		(This File)

PSERVER.VAP
02/11/91  64130
     This VAP shipped with NetWare 2.2 and 3.11.

07/10/91  64994
     This VAP contains the following fixes:
     1)   It fixes a problem that causes the rewind option to return to
          the beginning of a document, ignoring the page number
          specified by the user.  This problem occurs when in text
          mode.

     2)   This VAP also addresses a problem of tabs not working
          properly.

     3)   This VAP contains the auto load feature which allows an
          unattended load of the pserver.vap.  This auto-load
          feature will ONLY be available on a NetWare 2.2 File
          Server.

          AUTO-LOAD NOTES:
	  To load a VAP without being required to hit a "y" when
	  asked if you want to load value added processes, put
	  "VAP WAIT xxx" (xxx = 10 seconds to 300 seconds) in your
	  server.cfg file.  Make sure the server.cfg file in the
	  system directory.  When running this new pserver.vap on
	  a NW 2.2 server the VAP will prompt you for the Print
	  Server name the first time the VAP is loaded.  From that
	  point on the pserver.vap will remember the Print Server
	  Name until the name is cleared.

          To CLEAR a Print Server Name the user will simply type:
          PSERVER CLEARNAME
          at the console prompt on the NW 2.2 File Server.  This
          will cause the pserver.vap to prompt the user for a Print
          Server Name on the next load of the pserver.vap.

06/15/92  65218
     This Vap contains the following fixes:
     1)   It causes DTR and RTS on the serial port to stay high
          once the Print Server is installed.

     Installation:
     1)   Make a backup copy of the original PSERVER.VAP.

     2)   Copy new file PSERVER.VAP over the original version.

     3)   Reboot the file server.

PSERVER.EXE
02/11/91  107928
     This EXE shipped with NetWare 2.2 and 3.11.

07/10/91  108184
     This EXE contains the following fixes:
     1)   It fixes a possible problem that could create data corruption
          when printing large graphics documents with serial and
          parallel printers.  Although this bug has not been seen
          with the EXE, it has been known to occur with
          PSERVER.NLM.  This problem is created by a special
          condition which causes the pointer to override the print
          buffer.  As a result, garbage characters are printed in
          the middle of a document.  Once the block of bad data is
          printed, the printer resumes printing the document as it
          should.

     2)   This EXE also addresses a problem of the rewind function
          not working correctly when in text mode.  It was also
          found that tabs were not working correctly in the
          previous release.  This issue has been fixed in this EXE.

06/16/92  108844
     This EXE contains the following fixes:
     1)   It causes DTR and RTS on the serial port to stay high
          once the Print Server is installed.

     2)   This file also fixes a problem that causes print job
          corruption in the form of ascii characters or form feeds. 
          This corruption is known to occur on PaintJet printers,
          but may occur on others as well.

     Installation:
     1)   Flag PSERVER.EXE as SRW (Sharable Read Write) in the
          PUBLIC directory.

     2)   Rename PSERVER.EXE to PSERVER.OLD in the PUBLIC directory
          for backup purposes.

     3)   Copy PSERVER.EXE to the PUBLIC directory on your system.

     4)   Flag the new copy of PSERVER.EXE back to SRO (Sharable
          Read-Only).

PSERVER.NLM
02/11/91  51208
     This NLM shipped with NetWare 3.11.

07/10/91  50358
     This NLM contains the following fixes:
     1)   It fixes a bug that when printing large graphics
          documents with serial and parallel printers.  This
          problem is created by a special condition which causes
          the pointer to override the print buffer.  As a result,
          garbage characters are printed in the middle of a
          document.  Once the block of bad data is printed, the
          printer resumes printing the document as it should.

     2)   This NLM also addresses a problem of the rewind function
          not working correctly when in text mode.

06/15/92  51938
     This NLM contains the following fixes:
     1)   It causes DTR and RTS on the serial port to stay high
          once the Print Server comes up.

     2)   This file also fixes a problem that causes print job
          corruption in the form of ascii characters or form feeds. 
          This corruption is known to occur on PaintJet printers,
          but may occur on others as well.

     3)   This file also allows the user to specify how often the
          print server services jobs.  Currently, the polling time
          default is every 15 seconds.  The poll time can now be
          set by a load-time parameter using the following syntax:
               : LOAD PSERVER <PRINT SERVER NAME> POLL=xx
          where xx (1 - 30) equals the number of seconds the queue
          waits before checking for jobs to be serviced.  If the
          POLL parameter is not entered, the default value is used. 
          If an invalid POLL value or if incorrect syntax is
          entered, the user is given the correct syntax and the
          range of correct values and the user is then prompted to
          hit any key to continue.

     Installation:
     1)   If necessary flag PSERVER.NLM as SRW (Sharable Read
          Write).  If you plan to copy the file to the SYS:SYSTEM
          directory,  which is suggested, this will be necessary.

     2)   If an existing copy of PSERVER.NLM exists, rename it to
          PSERVER.OLD for backup purposes.

     3)   Copy PSERVER.NLM to the same directory as the other NLM
          files on your system (again this is usually SYS:SYSTEM).

     4)   Flag the new copy of PSERVER.NLM back to SRO (Sharable
          Read Only).

     5)   After the system is brought up, type LOAD PSERVER.
          : LOAD PSERVER <PRINT SERVER NAME> POLL=xx

RPRINTER.EXE
06/04/92  59756
     This RPRINTER.EXE contains the following fixes:
     1)   There is a problem found when attempting to establish a
          remote connection.  Often when the attempt is made, the
          print server responds with a message indicating that it
          is unable to establish a remote connection, and that the
          remote printer is already in use.

     2)   If a workstation batch file continually loads and reloads
          Rprinter, a workstation hang could occur.

     3)   This version of RPRINTER.EXE addresses a problem with
          RPRINTER v1.21 that was included with Netware V2.2 and
          V3.11.  The problem was that if XON\XOFF was defined,
          RPRINTER would continue to utilize hardware handshaking. 
          The result was that the printer buffer would overflow
          and/or the printer would go offline.

     4)   This version of RPRINTER.EXE also contains a fix for a
          problem that caused rprinter to quit accepting jobs after
          aborting a job that was waiting for a form to be mounted.

     5)   This version of RPRINTER.EXE also contains a fix for a
          bug that causes lost characters or slow printing when
          printing documents.  This is known to occur with a PS/2
          Model 60 or 50 when running Rprinter v1.21.

     6)   This version causes DTR and RTS on the serial port to
          stay high once the print server comes up.

     7)   This version contains a command line parameter to set the
          strobe time as follows:
          RPRINTER <PRINT SERVER NAME> PRINTER# Tx
          where x is a number from 1-9.

     8)   This version contains a fix for an intermittent problem
          when using DOS 5.0.  When loading RPRINTER the
          workstation would hang.

     Installation:
     1)   Flag RPRINTER.EXE as SRW (Sharable Read Write) in the
          PUBLIC directory.

     2)   Rename RPRINTER.EXE to RPRINTER.OLD in the PUBLIC
          directory for backup purposes.

     3)   Copy RPRINTER.EXE to the PUBLIC directory on your system.

     4)   Flag the new copy of RPRINTER.EXE back to SRO (Sharable
          Read-Only).


***************************************************************** 
DISCLAIMER

Novell, Inc. makes no representations or warranties with respect to
any NetWare software, and specifically disclaims any express or
implied warranties of merchantability, title, or fitness for a
particular purpose.

Distribution of any NetWare software is forbidden without the
express written consent of Novell, Inc.  Further, Novell reserves
the right to discontinue distribution of any NetWare software.

Novell is not responsible for lost profits or revenue, loss of use
of the software, loss of data, costs of re-creating lost data, the
cost of any substitute equipment or program, or claims by any party
other than you.  Novell strongly recommends a backup be made before
any software is installed.  Technical support for this software may
be provided at the discretion of Novell.
*****************************************************************