The Assembly Wizard's Library            page 1

    AsmWiz  Copyright (c) 1990-1992  Thomas G. Hanlin III



This is AsmWiz, a library of assembly language routines for
assembly language programmers.  It is copyrighted and may be
distributed only under the following conditions:

   All AsmWiz files must be distributed together as a unit in
   unmodified form.  No files may be left out or added.

You use this library at your own risk.  It has been tested by
me on my own computer, but I will not assume any responsibility
for any problems which AsmWiz may cause you.  If you do
encounter a problem, please let me know about it, and I will do
my best to verify and repair the error.

It is expected that if you find AsmWiz useful, you will
register your copy. This entitles you to receive the latest
version of AsmWiz, complete with full source code.  The source
code is designed for the Microsoft Macro Assembler (MASM) v6.0
and may require modifications to assemble with OPTASM, TASM,
A86, or older versions of MASM.

The AsmWiz library was designed for use with small assembly
programs and is compatible with the creation of COM files.  All
CALLs are of the NEAR variety.  If there is sufficient
interest, a FAR model will also be made.

For an example of how to set up your program to access the
AsmWiz library, how to LINK the routines, and so forth, see the
EXAMPLE.ASM, EXAMPLE.COM, and ?CREATE.BAT files (PACKING.LST
tells you which batch file to use with which assembler; there
are versions for A86, MASM, OPTASM, QuickASM, and TASM).

Note that DOS-dependent services expect DOS 2.0 or higher
versions, unless otherwise specified.


                       Table of Contents                 page 2



 Overview and Legal Info ................................... 1

 Base Conversions .......................................... 3

 Exception Handling ........................................ 4

 Delays and Countdowns ..................................... 5

 File Handling ............................................. 6

 Filename Manipulation ..................................... 8

 Long Integer Math ......................................... 9

 Memory Services .......................................... 10

 Mouse Services ........................................... 11

 Sound and Music .......................................... 12

 String Services .......................................... 13

 Telecommunications ....................................... 15

 Time and Date ............................................ 16

 Video Services ........................................... 17

 Miscellaneous Services ................................... 26

 Error Codes .............................................. 27


                       Base Conversions                  page 3



The Base Conversion Services provide the ability to convert
back and forth between a number and its ASCIIZ representation.
Any base from 2-36 may be employed, so these routines encompass
binary, decimal, hex and octal conversions.  Services are
provided for integers and long integers, both signed and
unsigned.


The following services are available:

   BC_ASC2INT    convert ASCIIZ string to unsigned integer
                       BL <-- base from which to convert
                    DS:SI <-- ptr to string
                    -------
                       AX = unsigned integer

   BC_ASC2LONG   convert ASCIIZ string to unsigned long int
                       BL <-- base from which to convert
                    DS:SI <-- ptr to string
                    -------
                    DX,AX = unsigned long integer

   BC_ASC2SINT   convert ASCIIZ string to signed integer
                       BL <-- base from which to convert
                    DS:SI <-- ptr to string
                    -------
                       AX = signed integer

   BC_ASC2SLONG  convert ASCIIZ string to signed long integer
                       BL <-- base from which to convert
                    DS:SI <-- ptr to string
                    -------
                    DX,AX = signed long integer

   BC_INT2ASC    convert unsigned integer to ASCIIZ string
                       AX <-- unsigned integer
                       BL <-- base to which to convert
                    ES:DI <-- ptr to string buffer (17 bytes)

   BC_LONG2ASC   convert unsigned long int to ASCIIZ string
                    DX,AX <-- unsigned long integer
                       BL <-- base to which to convert
                    ES:DI <-- ptr to string buffer (33 bytes)

   BC_SINT2ASC   convert signed integer to ASCIIZ string
                       AX <-- signed integer
                       BL <-- base to which to convert
                    ES:DI <-- ptr to string buffer (18 bytes)

   BC_SLONG2ASC  convert signed long integer to ASCIIZ string
                    DX,AX <-- signed long integer
                       BL <-- base to which to convert
                    ES:DI <-- ptr to string buffer (34 bytes)


                      Exception Handling                 page 4



The Exception Handling Services allow your program to take
control over exception conditions.  This covers critical errors
and Control-Break / Control-C handling.

The critical error handler gives you the ability to recover
from critical errors, which would otherwise cause the infamous
"R>etry, I>gnore, F>ail, A>bort?" prompt.

The break handler allows your program to ignore the Control-C
and Control-Break keys or to process them in an orderly
manner.  This is vital if you are using any of the AsmWiz
services which need to be shut down before the program
terminates.  Up to eight procedures can be called when ^Break
or ^C are used (they will be ignored if you turn off ^Break /
^C).


The following services are available:


   EH_INITCRIT   initialize the critical error handler

   EH_CRITERR    check for a critical error

   EH_CRITDONE   terminates the critical error handler

   EH_INITBREAK  initialize the ^C / ^Break handler

   EH_ADDBREAK   add a procedure to be called on ^C / ^Break
                       DX <-- procedure offset (CS-relative)

   EH_SETBREAK   allow or ignore ^C and ^Break
                       AL <-- 0 to ignore, 1 to allow

   EH_SUBBREAK   remove a procedure to be called on ^C / ^Break
                       DX <-- procedure offset (CS-relative)


                     Delays and Countdowns               page 5



The Delay Services are for those times when you want the
computer to sit around doing nothing for a while.  Delays of
various timing resolution are available for anything from small
to large waits.

Notes on the 100th-second delay and countdown services:

Since MD_DONE must be called before the program terminates, you
should use the EH_ADDBREAK service to insure that MD_DONE is
called if Control-Break or Control-C are permitted to abort the
program.

Timers 0-1 may be used by AsmWiz itself for various services.

See ASMWIZ.MAN for more details on the 100th-second delay
services.


The following services are available:


   MD_DELAY      delay for a number of 100ths of seconds
                       CX <-- delay (0-32767)

   MD_DONE       terminate 100th-second delay handler

   MD_GETTIMER   get a delay count
                       AL <-- timer number (0-7)
                    -------
                       CX = delay * 2 (0-65534)

   MD_INIT       initialize 100th-second delay handler

   MD_SETTIMER   set a delay count
                       AL <-- timer number (0-7)
                       CX <-- delay (0-32767)

   MD_TICK       delay for a number of clock ticks (18ths of seconds)
                       CX <-- delay (0-65535)


                        File Handling                    page 6



The File Handling Services provide a comprehensive and powerful
set of routines for file handling.  The usual open file,
read/write, file pointer manipulation, and close file
operations are supported, of course.  New conveniences include
automatic network support (file sharing is used if the DOS
version is high enough), optional input buffering for extra
speed, and special support for text files.  Critical error
handling is supported via the Exception Handling Services.

These services return with the carry flag set if there is an
error.  In that case, the AX register returns the error code.
Note that, unlike most other services, the file services are
allowed to change the AX register regardless of whether an
error occurred.


The following services are available:

   DF_CLOSE      close a file
                       BX <-- (virtual) file handle

   DF_DONE       terminate the File Handling Services
                 (closes all open files)

   DF_FLUSH      flush a file to disk (updates disk directory)
                       BX <-- (virtual) file handle

   DF_GETTIME    get file time/date stamp
                       BX <-- (virtual) file handle
                    -------
                       AX = time
                       DX = date

   DF_HANDLE     get DOS file handle given virtual file handle
                       BX <-- (virtual) file handle
                    -------
                       BX = (DOS) file handle

   DF_INIT       initialize the File Handling Services
                       DX <-- 0

   DF_LOCATE     set file read/write pointer
                       BX <-- (virtual) file handle
                       CL <-- 0 for offset from start
                              1 for offset from current posn
                              2 for offset from end of file
                    DX,AX <-- offset


                        File Handling                    page 7



   DF_OPEN       open a file for access
                       AX <-- set bit 0 for read
                                  bit 1 for write
                                  bit 2 for create
                                  bit 3 for text file
                                  bits 4-15 zero
                    DS:DX <-- pointer to ASCIIZ filename
                       CX <-- length of input buffer (0: none)
                    ES:SI <-- pointer to input buffer, if any
                    -------
                       BX = (virtual) file handle

   DF_READ       read from a file
                       BX <-- (virtual) file handle
                       CX <-- bytes to read
                              (for text files, is max bytes)
                    DS:DX <-- pointer to read buffer
                    -------
                       AX = bytes actually read
                            (if NC and not text mode)

   DF_TIME       set file time/date stamp
                       BX <-- (virtual) file handle
                       AX <-- time
                       DX <-- date

   DF_WHERE      get file read/write pointer
                       BX <-- (virtual) file handle
                    -------
                    DX,AX = offset

   DF_WRITE      write to a file
                       BX <-- (virtual) file handle
                       CX <-- bytes to write
                              (for text files, is ignored)
                    DS:DX <-- pointer to write buffer


                    Filename Manipulation                page 8



The Filename Manipulation Services allow various operations on
filenames which make it possible to duplicate the capabilities
of the DOS command shell. This includes finding a file which
matches a specified pattern, forcing a filename to match a
given pattern, splitting a filespec into its component parts,
and completing a (possibly partial) filespec.


The following services are available:

   FI_COMPLETE   complete a filespec from a partial spec
                    DS:SI <-- filename (may have drive,
                                 dir, "." or "..", etc)
                    DS:BX <-- default extension to be added
                                 (without ".")
                    ES:DI <-- 80-byte buffer for result
                    -------
                    Flags = CY if the filespec is not valid
                            NC if it went ok

   FI_MATCH      see if a filename matches a specified pattern
                    DS:SI <-- pattern (may contain wildcards)
                    ES:DI <-- filename (may not contain drive
                                 or path specs)
                    -------
                    Flags = ZF if the filename matches
                            NZ if the filename doesn't match

   FI_PATTERN    push a filename through a pattern spec
                    DS:SI <-- filename (no drive or
                                 directory allowed)
                    DS:BX <-- pattern
                    ES:DI <-- 13-byte buffer for results
                    -------
                    Flags = CY for some filename/pattern errors
                            NC if it went ok

   FI_SPLIT      split a path specification into drive,
                 directory, filename
                    DS:SI <-- path spec
                    ES:DI <-- 80-byte buffer for results


                       Long Integer Math                 page 9



The Long Integer Math Services provide support for the basic
arithmetic operations on unsigned long integers.  They allow
you to add two 32-bit integers, subtract one 32-bit integer
from another, multiply two 32-bit integers (giving a 64-bit
result), and divide a 63-bit integer by a 32-bit integer
(giving a 32-bit result and 32-bit remainder).

Since 32-bit integers are rather unwieldy unless you're using
an 80386 or above (in which case you don't need these services
anyway), the numbers are passed back and forth through a buffer
in memory.


The following services are available:

   MA_ADD32      add two unsigned long integers
                    DS:SI   <-- first operand
                    DS:SI+4 <-- second operand
                    -------
                    DS:SI+8 = result

   MA_DIV32      divide an unsigned 63-bit integer by an
                 unsigned long integer
                    DS:SI   <-- dividend (64 bits: high bit=0)
                    DS:SI+8 <-- divisor (unsigned long int)
                    -------
                    DS:SI+12 = quotient (unsigned long int)
                    DS:SI+16 = remainder (unsigned long int)

   MA_MUL32      multiply two unsigned long integers
                    DS:SI   <-- first operand
                    DS:SI+4 <-- second operand
                    -------
                    DS:SI+8 = result (unsigned very long
                                 integer: 64 bits)

   MA_SUB32      subtract one unsigned long int from another
                    DS:SI   <-- first operand
                    DS:SI+4 <-- second operand
                    -------
                    DS:SI+8 = result


                        Memory Services                 page 10



The Memory Services provide low-level routines for memory
manipulation.  They allow you to manipulate addresses, provide
a "smart" block move service that automatically handles
overlaps between source and destination areas, and allows you
to save or restore blocks of memory in BASIC's BSAVE format.

Among the address manipulation services are routines to convert
an address to have the smallest possible segment and highest
possible offset (or vice versa) to allow REP operations to
always handle up to 65,519 bytes without wrapping within the
segment.  This can also be useful in file operations.


The following services are available:

   ME_BINFO      get information about a BSAVE-format file
                    DS:DX <-- pointer to ASCIIZ filename
                    -------
                    ES:SI = segment:offset
                       CX = image size (bytes)
                    Flags = CY if unable to load file
                            if CY, AX is error code

   ME_BLOAD      load a BSAVE-format file into memory
                    DS:DX <-- pointer to ASCIIZ filename
                    -------
                    Flags = CY if unable to load file
                            if CY, AX is error code

   ME_BSAVE      save a block of memory to a BSAVE-format file
                    DS:DX <-- pointer to ASCIIZ filename
                    ES:SI = segment:offset
                       CX = image size (bytes)
                    -------
                    Flags = CY if unable to save memory
                            if CY, AX is error code

   ME_HIGHOFS    convert an address to have the lowest segment
                 & highest offset
                    DX:AX <-- segment:offset
                    -------
                    DX:AX = converted segment:offset

   ME_LOWOFS     convert an address to have the highest segment
                 & lowest offset
                    DX:AX <-- segment:offset
                    -------
                    DX:AX = converted segment:offset

   ME_MOVE       move a block of memory w/o overlap conflicts
                    DS:SI <-- source segment:offset
                    ES:DI <-- destination segment:offset
                       CX <-- bytes to move (0 - 65,519)


                        Mouse Services                  page 11



The Mouse Services provide a simple set of functions for
dealing with Microsoft-compatible mouse devices.  You may see
if a mouse exists, control the mouse cursor, and get
information about the mouse buttons.


The following services are available:

   MO_GLOCATE    set the mouse cursor location (graphics)
                       CX = X coordinate (0-MaxX)
                       DX = Y coordinate (0-MaxY)

   MO_GWHERE     get the mouse cursor location & button states
                       AL = left button (1: pressed, 0: not)
                       AH = right button (1: pressed, 0: not)
                       CX = X coordinate (0-MaxX)
                       DX = Y coordinate (0-MaxY)

   MO_HIDECURSOR hide the mouse cursor

   MO_INIT       see if a mouse is installed
                    -------
                       AL = number of mouse buttons
                            (0 if no mouse)

   MO_LOCATE     set the mouse cursor location (text)
                       DH <-- row (1-25)
                       DL <-- column (1-80)

   MO_RANGE      set the mouse cursor range (text)
                       CH <-- top row (1-25)
                       CL <-- leftmost column (1-80)
                       DH <-- bottom row (1-25)
                       DL <-- rightmost column (1-80)

   MO_SHOWCURSOR show the mouse cursor

   MO_WHERE      get the mouse cursor location & button states
                    -------
                       AL = left button (1: pressed, 0: not)
                       AH = right button (1: pressed, 0: not)
                       DH = row (1-25)
                       DL = column (1-80)


                        Sound and Music                 page 12



The Sound and Music Services provide the ability to generate
sound effects and music.  The current service is rather on the
primitive side.  It will be supplemented by a background
(interrupt-driven) music command language in a future version
of AsmWiz.


The following services are available:

   MU_SOUND      produce a sound of a specified duration
                 and frequency
                    AX <-- frequency (Hertz or cycles/second:
                              about 50-4000 is useful)
                    DX <-- duration  (18ths of seconds)


                   String Services (ASCIIZ)             page 13



The ASCIIZ String Services provide an assortment of services
for dealing with null-terminated strings.

Note that, although many of the string services are designed to
place the result of processing a first string into a second
string, it is not actually necessary to use two string
buffers.  The services are designed so that you can place the
results back into the original string buffer by using the same
address for both strings.


The following routines are included amongst the ASCIIZ String
Services:

   S0_COMPARE    compare two strings
                    DS:SI <-- first string
                    ES:DI <-- second string
                    -------
                    Flags = ZF if equal, NZ if not equal
                            CY if first < second
                            NC if first >= second

   S0_DUPE       form a string by duplicating a character
                    ES:DI <-- result string
                       AL <-- character to duplicate
                       CX <-- number of times to repeat

   S0_FIND       search for a substring within a string
                    DS:SI <-- substring
                    ES:DI <-- string
                    -------
                       AX = position of substring in string
                         (0 if not found; ZF set accordingly)

   S0_LEFT       copy a specified section from the left of
                 a string
                    DS:SI <-- source string
                       CX <-- number of characters to copy
                    ES:DI <-- result string

   S0_LENGTH     get the length of a string (excluding the
                 null terminator)
                    DS:SI <-- string
                    -------
                       CX = string length

   S0_LOCASE     convert a string to lowercase (international)
                    DS:SI <-- source string
                    ES:DI <-- result string


                   String Services (ASCIIZ)             page 14



   S0_MID        copy a specified section of a string
                    DS:SI <-- source string
                       DX <-- where to start copying from (1-xx)
                       CX <-- how many characters to copy
                    ES:DI <-- result string

   S0_RIGHT      copy a specified section from the right side
                 of a string
                    DS:SI <-- source string
                       CX <-- number of characters to copy
                    ES:DI <-- result string

   S0_TRIM       trim the "white space" (blanks and control
                 codes) from either or both sides of a string
                    DS:SI <-- source string
                       AL <-- set bit 0 to trim the left
                                  bit 1 to trim the right
                    ES:DI <-- result string

   S0_UPCASE     convert a string to uppercase (international)
                    DS:SI <-- source string
                    ES:DI <-- result string


                      Telecommunications                page 15



The Telecommunications Services provide functions that are
useful for telecommunications.  At the moment, this is limited
to services that aid in performing file transfers and similar
functions.


The following routines are included amongst the
Telecommunications Services:

   TC_CHKSUM     calculate the checksum for a block of data
                    DS:SI <-- pointer to a data block
                       CX <-- length of data block (in bytes)
                    -------
                       AX = checksum

   TC_CRC        calculate the 16-bit CRC of a block of data
                    DS:SI <-- pointer to a data block
                       CX <-- length of data block (in bytes)
                    -------
                       AX = resulting CRC


                    Time and Date Services              page 16



The Time and Date Services provide international time and date
handling.  Based on the country code given it by DOS, these
services return strings that represent the current time or date
in the appropriate format for that country.

These services provide a simple way to make your software work
properly on any computer anywhere, across the world.

See the COUNTRY entry under CONFIG.SYS in your DOS manual for
more details. Note that DOS version 3.0 or greater is required
to insure that the date and time delimiters are appropriate.
Otherwise, the date and time formats will still be correct, but
the delimiters used will be assumed to be "-" for the date and
":" for the time.  With DOS versions before 3.0, the time will
be presented in 12-hour (am/pm) format.


The following routines are included amongst the Time and Date
Services:

   TD_GETDATE    get the current date as an ASCIIZ string
                 DS:DX <-- pointer to a buffer (11 bytes)
                    AL <-- 0 for 2-digit year
                           1 for 4-digit year

   TD_GETTIME    get the current date as an ASCIIZ string
                 DS:DX <-- pointer to a buffer (8 bytes)


                        Video Services                  page 17



Displaying text is something that almost every program will
do.  The AsmWiz library contains numerous sets of video
services which make it easy to use the display in a consistent
manner.

The display services are divided into five sets of routines,
each of which provides similar capabilities:

   DV    DOS-level services
   BV    BIOS-level services
   MV    Machine-level services for text modes
   CG    Machine-level services for CGA graphics modes
   HG    Machine-level services for Hercules graphics mode

The DOS services provide the maximum level of compatibility.
They are also the slowest of the video services and the least
flexible.  The main practical advantage of using DOS services
is that they allow redirection, so the output of your program
can be sent to a file, a printer, or a serial port as well as
to the display.  Since DOS itself has only minimal video
support, you will need to make sure an ANSI driver is installed
before using these services. See your DOS manual on ANSI.SYS
for more information if you need it.

The BIOS services provide a very good level of compatibility.
They are faster and more flexible than the DOS services.  Like
the DOS services, these routines are quite likely to work on
nonstandard displays.

The machine-level services are the least compatible.  They will
work on any standard PC clone, but not on semi-compatible
hardware or with nonstandard display devices.  In return for
this disadvantage, these services are much faster than the
other services and provide a great deal more flexibility. Only
the machine-level services support Hercules graphics mode.


                        Video Services                  page 18
                     Text Display Speeds



Speed tests were conducted on an 8088 machine with a Phoenix
BIOS, running MS-DOS 3.30.  "Your mileage may differ".  The
tests were conducted on how quickly strings could be printed to
the display.

Speeds are listed relative to the slowest display method (DOS
services).



             +-----------+-----------+-----------+-----------+
             | DV_STROUT | BV_STROUT | MV_STROUT | CG_STROUT |
+------------+-----------+-----------+-----------+-----------+
| Mode 3     |           |           |           |           |
| text mode  |    100%   |    162%   |    572%   |    n/a    |
+------------+-----------+-----------+-----------+-----------+
| Mode 4     |           |           |           |           |
| CGA lo-res |    100%   |    114%   |    n/a    |    180%   |
+------------+-----------+-----------+-----------+-----------+
| Mode 6     |           |           |           |           |
| CGA hi-res |    100%   |    122%   |    n/a    |    204%   |
+------------+-----------+-----------+-----------+-----------+



From this chart, you can see that using BIOS display services
is 14% - 62% faster than using DOS services.  Using
machine-level services is 80% - 472% faster than using DOS
services, and about 60% - 250% faster than using BIOS services.

If system compatibility is a major concern, then note that the
DOS services are most compatible, followed by the BIOS services
and then the machine-level services.  The price you pay for
compatibility is speed and flexibility.  The machine-level
services are the fastest and most flexible, followed by the
BIOS services and then the DOS services.

It must be noted that almost all machines these days are 100%
compatible and will run any of these routines with no problem.


                        Video Services                  page 19
                   General Video Information
          (not applicable to Hercules graphics mode)



For all text routines, color/attributes are encoded as a single
byte value:

bit:    7   6   5   4   3   2   1   0
      +---+---+---+---+---+---+---+---+
      | B |  backgnd  | I |  foregnd  |
      +---+---+---+---+---+---+---+---+

B:  "blink".  Set if the color is blinking.

I:  "intense".  Set if the foreground color is intense
    (bright or light).

backgnd, foregnd:  the actual foreground and background
   colors.  The bits specify the red, green, and blue
   components of the color, giving the following list of colors:

       0    black     (if intense, is usually displayed as gray)
       1    blue
       2    green
       3    cyan
       4    red
       5    magenta
       6    brown     (if intense, is usually displayed as yellow)
       7    white


Text in CGA graphics modes is different.  If you use BIOS or
DOS services, you may only specify a foreground color, which
may be 0-3.  If you use the CGA machine-level services, you may
specify a background color as well as a foreground color.
Color encoding is the same as for text mode, with the exception
that there are no "blinking" or "intense" bits, and the color
range is 0-3 instead of 0-7.  The 0-3 range does not follow the
above color list; instead, the colors depend on which CGA
palette is in use.


                        Video Services                  page 20
                   General Video Information



Screen modes are specified as a single byte, as follows:

     Mode  Resolu.  Type  Colr  Use      Adapter   Services

       0   40x25    b&w     16  text       CGA     MV, BV, DV
       1   40x25    color   16  text       CGA     MV, BV, DV
       2   80x25    b&w     16  text       CGA     MV, BV, DV
 def-  3   80x25    color   16  text       CGA     MV, BV, DV
       4   320x200  color    4  graphics   CGA     CG, BV, DV
       5   320x200  b&w      4  graphics   CGA     CG, BV, DV
       6   640x200  color    2  graphics   CGA     CG, BV, DV
 mda-  7   80x25    b&w      -  text       MDA     BV
      13   320x200  color   16  graphics   EGA     BV
      14   640x200  color   16  graphics   EGA     BV
      15   640x350  mono     -  graphics   EGA     BV
      16   640x350  color   16  graphics   EGA     BV
      17   640x480  color    2  graphics   VGA     BV
      18   640x480  color   16  graphics   VGA     BV
      19   320x200  color  256  graphics   VGA     BV

BV = BIOS video services
DV = DOS video services
MV = Machine-level text services
CG = Machine-level CGA graphics services


                        Video Services                  page 21



All of the video services share a common nomenclature and
calling procedure. For many of the services, you will have a
choice of whether to use DOS, BIOS, Machine-level (text modes),
Machine-level (CGA graphics modes), or Machine-level (Hercules
graphics mode).  The level is specified as a two-letter code
prefix to the routine name, where the codes are as follows:

    DV    DOS Video
    BV    BIOS Video
    MV    Machine-level (text mode) Video
    CG    Machine-level (CGA graphics mode) Video
    HG    Machine-level (Hercules graphics mode) Video

The routine to display a string using DOS services, for
example, is named DV_STROUT (DOS Video service, String
Output).  It usually isn't a good idea to "mix and match" video
services of different types.


The following services are available:


    CHROUT      display a character
                BV,DV,MV,CG,HG
                   AL <-- character

    CLS         clear the screen and home the cursor
                BV,DV,MV,CG,HG

    COLOR       set the text color
                BV,DV,MV,CG,HG
                   AL <-- color/attribute

    CRLF        display a carriage return and a linefeed
                BV,DV,MV,CG,HG

    CLEOLN      clear from the cursor to the end of the line
                BV,DV,MV,CG,HG

    DELCHR      delete the character at the cursor
                MV

    DELLINE     delete the current line
                BV,dv,MV

    GETCOLOR    get the text color
                BV,MV,CG,HG
                   -------
                   AL = color/attribute


                        Video Services                  page 22



    GETMODE     get the current screen mode
                BV,MV
                   -------
                   AL = mode

    FIXCOLOR    whether to convert colors to monochrome
                BV,DV,MV
                   AL <-- whether to convert (0 no, 1 yes)

    FRAME       display a window frame
                MV
                   CH,CL <-- upper left corner (row, column)
                   DH,DL <-- lower right corner (row, column)
                   DS:SI <-- frame char list (-1 to -9 special)

    HIDECURSOR  hide the cursor
                BV,MV

    INIT        initialize the video service routines
                MV,CG

    INSCHR      insert a space at the cursor
                MV

    INSLINE     insert a row at the current line
                BV,dv,MV

    LOCATE      set the cursor position
                BV,DV,MV,CG,HG
                   DH <-- row (1-25/43)
                   DL <-- column (1-40/80/90)

    MODE        set the screen mode
                BV,DV,MV,CG,HG
                   AL <-- mode (see General Video Info)

    POPUP       display a pop-up window
                BV,MV
                   DS:DX <-- parameter pointer

    SAVESIZE    calculate bytes needed to save a screen area
                MV
                   -------
                   AL = bytes


                        Video Services                  page 23



    SCRREST     restore a saved screen area from a buffer
                MV
                   DS:SI <-- buffer pointer
                   DH,DL <-- upper left corner (row, column)

    SCRSAVE     save a screen area into a buffer
                MV
                   ES:DI <-- buffer pointer
                   CH,CL <-- upper left corner (row, column)
                   DH,DL <-- lower right corner (row, column)
                   -------
                      AX = bytes used to save screen area

    SHOWCURSOR  show the cursor
                BV,MV

    STROUT      display a string
                BV,DV,MV,CG,HG
                   DS:DX <-- pointer to ASCIIZ string

    WHERE       get the current cursor position
                BV,MV,CG,HG
                   DH <-- row (1-25/43)
                   DL <-- column (1-40/80/90)


                        Video Services                  page 24



The ability to display graphics was once limited and very
expensive, but this is no longer true.  PC-class computers have
a wide variety of graphics standards to choose from.  This is
useful whether you are interested in games, business charts,
computer-aided design, icon-based mouse interfaces, or any
number of other applications.  The AsmWiz library provides
numerous sets of graphics services which allow easy access to
the capabilities of whatever display is installed.

The graphics services are divided into sets of routines, with
each set of routines handling a specific video mode or modes.
This makes it possible to support just the modes you want,
without extraneous code being linked in.

All graphics services are machine-level and demand hardware
compatibility of both your computer and video adapter.  This is
necessary because DOS doesn't support graphics at all, and the
BIOS only supports very slow single-pixel handling.  If you are
able to run standard graphics programs on your computer,
however, you should experience no problems with these services.

All of the graphics services share a common nomenclature and
calling procedure.  The video mode is specified as a two-letter
code prefix to the routine name, where the codes are as follows:

   Prefix     Mode(s)     Adapter     Resolution(s)     Colors
   ------    --------     -------    ----------------   ------
     G13        13h         VGA           320x200         256
     G4        4, 5         CGA           320x200           4
     G6          6          CGA           640x200           2
     GD         0Dh         EGA           320x200          16
     GE         0Eh         EGA           640x200          16
     GE         10h         EGA           640x350          16
     GE         11h         VGA           640x480           2
     GE         12h         VGA           640x480          16
     GH      Hercules       HGA           720x348           2

The service to display a line in Mode 6, for example, is named
G6_LINE.  Note that GE_ covers most EGA and VGA modes.


                        Video Services                  page 25



The following graphics services are available:


    BOX         draw a box
                GH,G4,G6,GD,GE,G13
                   CX <-- left X coordinate
                   DX <-- top Y coordinate
                   SI <-- right X coordinate
                   DI <-- bottom Y coordinate
                   AH <-- whether to fill box (0 no, 1 yes)
                   AL <-- color

    GETPEL      get the current color of a point
                GH,G4,G6,G13
                   CX <-- X coordinate
                   DX <-- Y coordinate
                   -------
                   AL = color

    LINE        draw a line
                GH,G4,G6,GD,GE,G13
                   CX <-- left X coordinate
                   DX <-- top Y coordinate
                   SI <-- right X coordinate
                   DI <-- bottom Y coordinate
                   AL <-- color

    PLOT        plot a point
                GH,G4,G6,GD,GE,G13
                   CX <-- X coordinate
                   DX <-- Y coordinate
                   AL <-- color


                    Miscellaneous Services              page 26



The Miscellaneous Services provide a number of services for
various purposes, such as parsing the command line, determining
the active video adapter, scanning the environment for a
parameter, and generating pseudo-random numbers.  They
eliminate much of the tedium of these common chores.


The following services are available:

   MI_BOOT       reboot the computer (warm boot)

   MI_GETSCREEN  see what type of display is active
                    -------
                       AH = adapter type (1-6:
                               MDA, Herc, CGA, EGA, MCGA, VGA)
                       AL = color flag (0 color, 1 mono)

   MI_PARSE      parse a command line into filespecs & options
                    DS:SI <-- ptr to command line
                                 (for COM files, = CS:0080h)
                    ES:DI <-- ptr to filename buffer (128b)
                    ES:BX <-- ptr to option buffer (128 bytes)
                       AL <-- switch character (normally "/")
                    -------
                       AH = number of options
                       AL = number of filenames

   MI_RANDOM     generate a pseudo-random number
                       DX <-- random number range (1-4000)
                    -------
                       AX = random number (0 to DX - 1)

   MI_RANDOMIZE  initialize the pseudo-random number generator
                       AX <-- random number seed
                                 (use 0FFFFh for auto-seeding)

   MI_SCANENV    scan the DOS environment for a parameter
                    DS:SI <-- ptr to the DOS environment
                                 or similar table
                    ES:DI <-- ptr to the parm to search for
                    -------
                       CY if not found
                       NC if match found
                          if NC, DS:SI points to parm value


                         Error Codes                    page 27



DOS error codes are returned by various of the DOS services,
particularly the file and disk services.  The code is returned
in the AL register.  This is a list of some of the possible
errors.


      2      file not found
      3      path not found
      4      too many open files (no handle available)
      5      access denied
      6      invalid handle
      8      insufficient memory
     15      invalid drive specified
     16      tried to remove current directory
     18      no more files




Critical error codes are returned by the EH_CRITERR service in
the AH register.  This is a list of the possible errors.


      0      no critical error (if CY, it was a DOS error)
      1      write-protected disk
      2      unknown unit
      3      drive not ready
      4      unknown command
      5      data/CRC error
      6      bad request structure length
      7      seek error
      8      unknown media type
      9      sector not found
     10      printer out of paper
     11      write fault
     12      read fault
     13      general failure
     16      invalid disk change (only used by DOS 3+)