;****************************************************************************
;*
;*  Welcome to ASPI.  The following code is provided to assist you with 
;*  writing code to the Advanced SCSI Programming Interface (ASPI).  Run the 
;*  program ASPIPROG.EXE to see what the following program does when compiled.
;*
;*  The only support provided for ASPI developers by Adaptec is through this 
;*  sample code and the ASPI specification, which can be ordered through 
;*  Literature at (408) 945-8600 x2579.  The ASPI specification is available
;*  for DOS, OS/2, and NetWare 386.  Please do not call the Adaptec technical
;*  support line with ASPI programming questions.
;*
;*  This sample code provides examples of how to use the ASPI	programming
;*  interface.  The main program obtains the ASPI entry point	and calls
;*  subroutines for the different ASPI functions.
;*
;*	1. Obtains ASPI Entry Point
;*	2. Executes ASPI Host Adapter Inquiry Command
;*	3. Executes ASPI Get Device Type Command
;*	4. Executes ASPI Execute SCSI I/O Command
;*	5. Executes ASPI Reset SCSI Device Command using Posting
;*	6. Executes (3) and then executes ASPI Abort SCSI I/O command
;*
;*
;****************************************************************************
		.286
		.xlist
		include aspidefs.inc	;include file for ASPI definitions
		include scsidefs.inc	;include file for SCSI definitions
		.list

		.MODEL Small
		.STACK 300h

;****************************************************************************
;	DATA SEGMENT
;****************************************************************************
		.DATA
SCSIMgrString	db	"SCSIMGR$"      ;SCSI Mgr String (need to get entry)
		dw	0		;NULL-Terminate String
ASPI_Entry	dd	0		;Entry Address stored by GetASPIEntry
SRB		db	64+10+14 dup (0) ;SCSI Request Block
SRB2		db	64+10+14 dup (0) ;SCSI Request Block 2
Data_Buffer	db	50 dup (?)	;Data Buffer for Inquiry command
Flag		db	0		;flag used by post routine

;****************************************************************************
;	DISPLAY STRINGS
;****************************************************************************
Str_InquiryFail db  "Error issuing SCSI inquiry command",CR,LF,'$'
Str_NoASPI	db  "Unable to open ASPI Manager!",CR,LF,'$'

Str_ASPI_Stat	db  "  ASPI Status (HEX)               : %",CR,LF,'$'

Str_HA_Inquiry	db  CR,LF,"ASPI HOST ADAPTER INQUIRY COMMAND",CR,LF,'$'
Str_Num_HA	db  "  Number of Host Adapters         : %",CR,LF,'$'
Str_TID_HA	db  "  SCSI ID of Host Adapter 0       : %",CR,LF,'$'
Str_Mgr_ID	db  "  SCSI Manager ID                 : %%%%%%%%%%%%%%%%",CR,LF,'$'
Str_HA_ID	db  "  Host Adapter ID                 : %%%%%%%%%%%%%%%%",CR,LF,'$'

Str_Get_DevTyp	db  CR,LF,"ASPI GET DEVICE TYPE COMMAND",CR,LF,'$'
Str_Dev_Typ	db  "  SCSI Device Type                : %",CR,LF,'$'

Str_SCSI_IO	db  CR,LF,"ASPI SCSI I/O COMMAND (Inquiry Command)",CR,LF,'$'
Str_PQualTyp	db  "  Qualifier / Device Type (HEX)   : %",CR,LF,'$'
Str_Versions	db  "  ISO / ECMA / ANSI Version (HEX) : %",CR,LF,'$'
Str_Inq_Dat	db  "  Inquiry Data                    : %%%%%%%%%%%%%%%%%%%%%%%%%%%%",CR,LF,'$'

Str_Dev_Rst1	db  CR,LF,"ASPI RESET DEVICE COMMAND (with Posting)",'$'
Str_Wait4Post	db  ".",'$'
Str_HA_Inq2	db  CR,LF,"ASPI HOST ADAPTER INQUIRY COMMAND (Aborted)",'$'
Str_CRLF	db  CR,LF,'$'
;****************************************************************************
;	CODE SEGMENT
;****************************************************************************
		.CODE
start:		mov	ax,@DATA		;initialize ds and es
		mov	ds,ax
		mov	es,ax

;*	1. Obtains ASPI Entry Point
		call	GetASPIEntry									        ;Get ASPI entry point
		jc	ASPI_Done		                    ;Jump if no manager

;*	2. Executes ASPI Host Adapter Inquiry Command
		lea	si,SRB			                     ;point to SRB
		call	HAInquiry		                  ;Send ASPI HA Inquiry
		call	Poll_Status		                ;wait for status
		call	DispSRBInq		                 ;Display Inquiry Info

;*	3. Executes ASPI Get Device Type Command
		lea	si,SRB			                     ;point to SRB
		call	GetDevType	                 	;Send ASPI Get Device Type
		call	Poll_Status                		;wait for status
		call	DispDevTyp                 		;Display Device Type Info

;*	4. Executes ASPI Execute SCSI I/O Command
		lea	si,SRB                     			;point to SRB
		call	Load_Inquiry		               ;Load SCSI Inquiry into SRB
		call	XSCSI_IO		                   ;Execute SCSI I/O
		call	Poll_Status                		;wait for status
		call	DispInquiry		                ;Display I/O results

;*	5. Executes ASPI Reset SCSI Device Command using Posting
		lea	dx,Str_Dev_Rst1              	;load the string for outtext
		call	outtext 		                   ;output the text
		lea	si,SRB                     			;point to SRB
		mov	Flag,0		                    		;reset the post flag
		call	RST_SDevice	               		;Resets SCSI ID = 2
		lea	dx,Str_Wait4Post           			;point to Wait for Post String
PostLp1:
		mov	al,Flag 	                    	;get the post flag
		cmp	al,1
		call	outtext 	                   	;output the text
		jnz	PostLp1 	                    	;jump if not 1
		call	DispStat                   		;Display status

;*	6. Executes (3) and then executes ASPI Abort SCSI I/O command
		lea	dx,Str_HA_Inq2	             	;load the string for outtext
		call	outtext 		                  ;output the text
		lea	si,SRB                    			;point to SRB
		call	Load_Inquiry		              ;Load SCSI Inquiry into SRB
		call	XSCSI_IO                  		;Execute SCSI I/O
		call	Abort_SIO                 		;call abort SCSI IO
		call	Poll_Status               		;wait for status
		call	DispStat		                  ;Display status

ASPI_Done:	mov	ax,ASPI_DOSExit
		int	21h
		ret	                          			;Exit to DOS

;****************************************************************************
;
;		  %%% ASPIDISK SUPPORT ROUTINES %%%
;
;****************************************************************************
; Subroutine Name:  GetASPIEntry
;
; Description:	This gets the ASPI manager's entry point and stores it in
;		'ASPI_Entry.'
;		If no ASPI manager is found, an appropriate error message
;		is displayed.
;
; Entry:  Nothing
;
; Exit:   The memory location ASPI_Entry is loaded with entry point
;	  CF set if no ASPI manager found, else reset
;****************************************************************************
GetASPIEntry	proc	near
		mov	ax,ASPI_Open
		lea	dx,SCSIMgrString
		int	21h			               ;Open ASPI Manager
		jc	NoASPIManager		       ;Branch if none found
		push	ax			               ;Save ASPI File Handle

		mov	bx,ax			             ;BX = File Handle
		mov	ax,ASPI_Get_Entry
		lea	dx,ASPI_Entry		      ;Store entry point here
		mov	cx,4			              ;Four bytes to transfer
		int	21h			               ;Get ASPI entry point

		mov	ax,ASPI_Close
		pop	bx																			;BX = ASPI File Handle
                                		;BX = ASPI File Handle
		int	21h			;Close ASPI Manager
		clc				;Return with carry clear
		ret

NoASPIManager:	lea	dx,Str_NoASPI		;Display error message, no
		call	outtext 		;  ASPI manager found
		stc				;Return with carry set
		ret
GetASPIEntry	endp

;****************************************************************************
; Subroutine Name:  Poll_Status
;
; Description:	This subroutine polls the ASPI Status Byte and waits for
;		non-zero status.  When status goes non-zero we return.
;		Although this sample code will hange if status never goes
;		non-zero, an actual program should time out.
;
; Entry:  Assumes that si is pointing to an SRB that has just been issued
;
;****************************************************************************
Poll_Status	proc	near
poll_loop:	mov	al,[si]._SRStat ;get the status byte of SRB
		cmp	al,0		;compare to zero
		jz	poll_loop	;jump if still zero
		ret
Poll_Status	endp

;****************************************************************************
; Subroutine Name:  HAInquiry
;
; Description:	This subroutine sends the Host Adapter Inquiry Command to the
;		ASPI Manager.  First the SRB is totally cleared.  Then the
;		opcode and other fields of the SRB are set for HOST ADAPTER
;		INQUIRY command.
;
; Entry:  si points to the SRB
;
; Exit:   SRB is full of returned data
;****************************************************************************
HAInquiry	proc	near
		call	ClearSRB		;Zero out our SRB
		mov	[si]._SRCmd,HA_INQ	;ASPI opcode = HA inquiry
		mov	[si]._SRHAid,0		;Host Adapter 0
		mov	[si]._SRFlags,0 	;0=no length checking
		mov	[si]._SRTarget,0	;Target 0
		mov	[si]._SRLun,0		;Lun 0

						;CALLING ASPI !!
		push	ds			;push segment of SRB
		lea	bx,SRB
		push	bx			;push offset of SRB
		call	[ASPI_Entry]		;Call ASPI
		add	sp,4			;Restore stack
		ret
HAInquiry	endp

;****************************************************************************
; Subroutine Name:  GetDevType
;
; Description:	This subroutine sends the Get Device Type Command to the
;		ASPI Manager.  First the SRB is totally cleared then the SRB
;		is loaded with opcode and other parameters for the GET DEVICE
;		TYPE command.
;
; Entry:  si points to the SRB
;
; Exit:   SRB is full of returned data
;****************************************************************************
GetDevType	proc	near
		call	ClearSRB		;Zero out our SRB
		mov	[si]._SRCmd,GET_TYPE	;ASPI opcode = Get Device Type
		mov	[si]._SRHAid,0		;Host Adapter 0
		mov	[si]._SRFlags,0 	;0=no length checking
		mov	[si]._SRTarget,0	;Target 0
		mov	[si]._SRLun,0		;Lun 0

						;CALLING ASPI !!
		push	ds			;push segment of SRB
		lea	bx,SRB
		push	bx			;push offset of SRB
		call	[ASPI_Entry]		;Call ASPI
		add	sp,4			;Restore stack
		ret
GetDevType	endp

;****************************************************************************
; Subroutine Name:  XSCSI_IO
;
; Description:	This subroutine sends the Execute SCSI I/O Command to the
;		ASPI Manager.  It is assumed that the SCSI command has already
;		been loaded into the SRB.  Here the EXEC_SIO is loaded into
;		opcode of the SRB along with setting the other fields for a
;		24 byte read of SCSI INQUIRY data.
;
; Entry:  The SCSI Command Block is setup upon entry, si points to SRB
;
; Exit:   SRB is full of returned data
;****************************************************************************
XSCSI_IO	proc	near
		mov	[si]._SRCmd,EXEC_SIO	;ASPI opcode = execute SCSI IO
		mov	[si]._SRHaId,0		;Host Adapter 0
		mov	[si]._SRFlags,SRB_DIR_IN ;Set flags to direction in
		mov	[si]._SRTarget,0	;Target 0
		mov	[si]._SRLun,0		;Lun 0
		mov	[si]._SRBuflenLo,24	;Buffer xfer length LSB
		mov	[si]._SRBuflenHi,0	;Buffer xfer length MSB
		mov	[si]._SRSnsLen,20	;Sense Buffer length 20
		lea	ax,Data_Buffer
		mov	[si]._SRBufPtrLo,ax	;load Data buffer offset
		mov	[si]._SRBufPtrHi,ds	;load Data buffer segment
		mov	[si]._SRCDBLen,6	;SCSI CDB Length

						;CALLING ASPI !!
		push	ds			;push segment of SRB
		lea	bx,SRB
		push	bx			;push offset of SRB
		call	[ASPI_Entry]		;Call ASPI
		add	sp,4			;Restore stack
		ret
XSCSI_IO	endp

;****************************************************************************
; Subroutine Name:  RST_SDevice
;
; Description:	This subroutine sends the RESET SCSI DEVICE Command to the
;		ASPI Manager.  It attempts to reset SCSI ID 2 instead of
;		ID 0 in case ID 0 is the boot device of your computer.
;		Posting is used by this routine.
;
; Entry:  si points to the SRB
;
;****************************************************************************
RST_SDevice	proc	near
		call	ClearSRB		;Zero out our SRB
		mov	[si]._SRCmd,RESET_DEV	;ASPI opcode = Reset Device
		mov	[si]._SRHaId,0		;Host Adapter 0
		mov	[si]._SRFlags,SRB_POST	;set post bit
		mov	[si]._SRTarget,0	;Target 0
		mov	[si]._SRLun,2		;Lun 0
		mov	[si]._SRBuflenLo,0	;Buffer xfer length LSB
		mov	[si]._SRBuflenHi,0	;Buffer xfer length MSB
		mov	[si]._SRSnsLen,20	;Sense Buffer length 20
		mov	ax,OFFSET ASPI_Post
		mov	[si]._SRPostOff,ax	;load post routine offset
		mov	[si]._SRPostCS,cs	;load post routine segment

						;CALLING ASPI !!
		push	ds			;push segment of SRB
		lea	bx,SRB
		push	bx			;push offset of SRB
		call	[ASPI_Entry]		;Call ASPI
		add	sp,4			;Restore stack
		ret
RST_SDevice	endp

;****************************************************************************
; Subroutine Name:  Abort_SIO
;
; Description:	This subroutine sends the Abort SCSI I/O Request command to the
;		ASPI Manager.  First SRB2 is totally cleared then the SRB2
;		is loaded with opcode and other parameters for the ABORT SCSI
;		I/O COMMAND.
;
; Entry:  si points to the SRB to be annihilated
;
;****************************************************************************
Abort_SIO	proc	near
		push	si			;save pointer to SRB 2b killed
		lea	si,SRB2 		;point to another SRB
		call	ClearSRB		;Zero out SRB2
		pop	si			;restore pointer to SRB
		mov	SRB2._SRCmd,ABORT_SRB	;ASPI opcode = Abort SRB
		mov	SRB2._SRHAid,0		;Host Adapter 0
		mov	SRB2._SRFlags,0 	;0=no length checking
		mov	SRB2._AbortPtrLo,si	;load offset of SRB 2b killed
		mov	SRB2._AbortPtrHi,ds	;load segment of SRB 2b killed

						;CALLING ASPI !!
		push	ds			;push segment of SRB2
		lea	bx,SRB2
		push	bx			;push offset of SRB2
		call	[ASPI_Entry]		;Call ASPI
		add	sp,4			;Restore stack
		ret
Abort_SIO	endp

;****************************************************************************
; Subroutine Name:  Load_Inquiry
;
; Description:	This routine loads the SCSI inquiry command into the
;		SRB.
;
; Entry:  si points to the SRB
;
; Exit:   All registers preserved
;****************************************************************************
Load_Inquiry	proc	near
		call	ClearSRB		;Zero out our SRB
		mov	[si]._OpCode,SCSI_Inquiry ;load opcode
		mov	[si]._LUNumber,0	;set LUN = 0
		mov	[si]._LBAMiddl,0	;set byte 2 = 0
		mov	[si]._LBALeast,0	;set byte 3 = 0
		mov	[si]._Length,24 	;set length = 24
		mov	[si]._Control,0 	;set control = 0
		ret
Load_Inquiry	endp

;****************************************************************************
; Subroutine Name:  ClearSRB
;
; Description:	This routine zeros out the given ASPI SRB.
;
; Entry:  SI - ASPI SRB
;
; Exit:   All registers preserved
;****************************************************************************
ClearSRB	proc	near
		push	es			;Save registers
		push	ax
		push	cx
		push	di

		mov	cx,(64+10)/2		;Zero out 74 bytes
		mov	ax,ds
		mov	es,ax			;ES=DS
		mov	di,si			;ES:DI points to SRB
		xor	ax,ax			;Store zeros
		cld
		rep	stosw			;Zero out the SRB

		pop	di
		pop	cx
		pop	ax
		pop	es			;Restore registers and
		ret				;return to caller
ClearSRB	endp

;****************************************************************************
; Subroutine Name:  ASPI_Post
;
; Description:	This routine is executed when the Reset Device command
;		completes.  It simply flips a flag so that execution in
;		the RST_SDEV routine can continue.  This flag method is
;		used strictly for example purposes.
;
;
; Exit:   All registers preserved
;****************************************************************************
ASPI_Post	proc	far
		push	bp
		mov	bp,sp

		pusha
		push	ds
		push	es			;Save registers
		push	dx

;		mov	bx,[bp+6]		;BX = SRB's offset
;		mov	ds,[bp+8]		;ES = SRB's segment

; CODE TO DETERMINE WHICH SRB JUST COMPLETED

		mov	ds,[bp+8]		;set ds to our data segment
		mov	Flag,1			;set the flag

		pop	dx
		pop	es			;Restore registers and
		pop	ds
		popa
		pop	bp
		retf				;return to caller
ASPI_Post	endp
;***************************************************************************
;
;			 %%% DISPLAY ROUTINES %%%
;
;***************************************************************************
; Subroutine Name:  outtext
;
; Description:	Displays a message on the screen.
;
; Entry:  DS:DX - Pointer to '$' terminated character string
;
; Exit:   Nothing
;***************************************************************************
outtext 	proc	near
		push	ax		; save ax
		mov	ah,09h		; Do DOS Function Print String
		int	21h		; call interrupt routine
		pop	ax		; restore ax
		ret
outtext 	endp

;****************************************************************************
; Subroutine Name:  itoa
;
; Description:	Converts the digits of the given value to a '$'-terminated
;		character string.  Appends a carriage return and linefeed
;		to the end of the string as well if requested.
;
; Entry:  AX	- Number to be converted
;	  DS:DX - Pointer to string result
;	  CX	- Base of value (ie. 16 for hex, 10 for dec.)
;
; Exit:   All registers preserved
;****************************************************************************
itoa		proc	near
		pusha
		mov	bx,dx
		or	ax,ax			;Is input value zero?
		jne	NotZero 		;Branch if it's not
		mov	BYTE PTR [bx],'0'       ;  else fill string with
		inc	bx			;  a single '0' and exit
		jmp	SHORT itoa_exit

NotZero:	xor	di,di
NextDigit:	or	ax,ax			;Finished pushing remainders
		je	itoa_pop		;  onto the stack?
		xor	dx,dx
		div	cx			;Let's get the remainder
		push	dx			;Push the remainder
		inc	di			;Increment digit count
		jmp	NextDigit

itoa_pop:	or	di,di			;Finished popping digits?
		je	itoa_exit		;Branch and exit if we are
		pop	dx			;Pop a digit
		cmp	dl,10			;Is it a 0-9 digit?
		jb	DecDigit		;If it is convert to ASCII
		add	dl,'A'-10               ;  else convert to HEX
		jmp	SHORT PlaceChar 	;  alphabet
DecDigit:	add	dl,'0'
PlaceChar:	mov	[bx],dl 		;Store character in string
		inc	bx			;Move to next place in string
		dec	di			;Decrement pop count
		jmp	itoa_pop		;Pop next value

itoa_exit:
		mov	BYTE PTR [bx],CR	;Place Carriage Return &
		mov	BYTE PTR [bx+1],LF	;  and Line Feed and '$'
		mov	BYTE PTR [bx+2],'$'     ;  char at end of string
		jmp	SHORT itoa_exit1

		mov	BYTE PTR [bx],'$'
itoa_exit1:	popa				;Restore all registers
		ret
itoa		endp

;****************************************************************************
; Subroutine Name:  DispSRBInq
;
; Description:	This subroutine displays the information returned in the SRB
;		for the Host Adapter Inquiry Command.
;
; Entry:  Expects The SRB to be full of Host Adapter Inquiry Data
;
; Exit:
;****************************************************************************
DispSRBInq	proc	near
		lea	dx,Str_HA_Inquiry	;load the string for outtext
		call	outtext 		;output the text

		mov	cx,16			;set base= hex for iota
		lea	dx,Str_ASPI_STAT+36	;point to loc in string
		mov	al,SRB._SRStat		;load value to convert
		mov	ah,0			;zero out ah
		call	itoa			;convert to ASCII in string loc
		lea	dx,Str_ASPI_STAT	;load the string for outtext
		call	outtext 		;output the text

		lea	bx,Str_Num_HA		;Get Number of HA string loc
		mov	al,SRB._HACount 	;Get # of ASPI host adapters
		add	al,'0'                  ;AL = ASCII Host Adapter #
		mov	BYTE PTR [bx+36],al	;Place HA # in string
		mov	dx,bx			;load the string for outtext
		call	outtext 		;output the text

		lea	bx,Str_TID_HA		;Get Target ID of HA string loc
		mov	al,SRB._HAIdNum 	;Get ID
		add	al,'0'                  ;AL = ASCII ID
		mov	BYTE PTR [bx+36],al	;Place HA # in string
		mov	dx,bx			;load the string for outtext
		call	outtext 		;output the text

		mov	cx,16			;ID has 16 bytes (for movsb)
		lea	si,SRB._SCSIMgrId	;load source of string mov
		lea	di,Str_Mgr_ID+36	;load destination of string mov
		rep	movsb			;move string
		lea	dx,Str_Mgr_ID		;Get Manager ID string loc
		call	outtext 		;output the text

		mov	cx,16			;ID has 16 bytes (for movsb)
		lea	si,OFFSET SRB._HAIdString ;load source of string mov
		lea	di,Str_HA_ID+36 	;load destination of string mov
		rep	movsb			;move string
		lea	dx,Str_HA_ID		;Get Manager ID string loc
		call	outtext 		;output the text
		ret
DispSRBInq	endp

;****************************************************************************
; Subroutine Name:  DispDevType
;
; Description:	This subroutine displays the information returned in the SRB
;		for the Get Device Type Command.
;
; Entry:  Expects The SRB to be full of Host Adapter Inquiry Data
;
; Exit:
;****************************************************************************
DispDevTyp	proc	near
		lea	dx,Str_Get_DevTyp	;point to Get Dev Type string
		call	outtext 		;output the text

		lea	bx,Str_ASPI_STAT	;point to ASPI Status string
		mov	al,SRB._SRStat		;Get ASPI status
		add	al,'0'                  ;convert to ASCII
		mov	BYTE PTR [bx+36],al	;place Status in string
		mov	dx,bx			;load the string for outtext
		call	outtext 		;output the text

		lea	bx,Str_Dev_Typ		;Get SCSI Dev Type string loc
		mov	al,SRB._ScsiDevType	;Get # of ASPI host adapters
		add	al,'0'                  ;AL = ASCII Host Adapter #
		mov	BYTE PTR [bx+36],al	;Place HA # in string
		mov	dx,bx			;load the string for outtext
		call	outtext 		;output the text

		ret
DispDevTyp	endp

;****************************************************************************
; Subroutine Name:  DispInquiry
;
; Description:	This subroutine displays the information returned in the SRB
;		for the Get Device Type Command.
;
; Entry:  Expects The SRB to be full of Host Adapter Inquiry Data
;
; Exit:
;****************************************************************************
DispInquiry	proc	near
		lea	dx,Str_SCSI_IO		;load the string for outtext
		call	outtext 		;output the text

		mov	cx,16			;set for HEX base (iota call)
		lea	dx,Str_ASPI_STAT+36	;point to string location
		mov	al,SRB._SRStat		;load value to convert
		mov	ah,0			;zero out ah
		call	itoa			;convert to ASCII in string
		lea	dx,Str_ASPI_STAT	;load the string for outtext
		call	outtext 		;output the text

		lea	dx,Str_PQualTyp+36	;point to string location
		mov	al,Data_Buffer.PerQualTyp ;load value to convert
		mov	ah,0			;zero out ah
		call	itoa			;convert to ASCII in string
		lea	dx,Str_PQualTyp 	;Get Peripheral Qual Dev string
		call	outtext 		;output the text

		lea	dx,Str_Versions+36	;Get Peripheral Qual Dev string
		mov	al,Data_Buffer.Versions ;Get Byte from Data Buffer
		mov	ah,0			;zero out ah
		call	itoa			;convert to ASCII in string
		lea	dx,Str_Versions 	;load the string for outtext
		call	outtext 		;output the text

		push	si			;save pointer to SRB
		mov	cx,28			;load number of bytes to mov
		lea	si,OFFSET Data_Buffer.VendorID ;load source address
		lea	di,Str_Inq_Dat+36	;load destination address
		rep	movsb			;move the string
		lea	dx,Str_Inq_Dat		;load the string for outtext
		call	outtext 		;output the text
		pop	si			;restore pointer to SRB
		ret
DispInquiry	endp

;****************************************************************************
; Subroutine Name:  DispStat
;
; Description:	This subroutine displays the ASPI status byte
;
;
;****************************************************************************
DispStat	proc	near
		lea	dx,Str_CRLF
		call	outtext 		;output the text

		lea	bx,Str_ASPI_STAT	;point to ASPI Status string
		mov	al,SRB._SRStat		;Get ASPI status
		add	al,'0'                  ;convert to ASCII
		mov	BYTE PTR [bx+36],al	;place Status in string
		mov	dx,bx			;load the string for outtext
		call	outtext 		;output the text

		ret
DispStat	endp
;****************************************************************************
		END	START