COMPAQF.SYS   version 1.0   2/6/92
Compaq Fix Device Driver

Richard S. Sadowsky
TurboPower Software
PO Box 49009
Colorado Springs, CO 80949-9009

This program corrects a bug in recent model Compaq computers. The bug causes
TSRs written with any TurboPower library to hang the machine when run.

To use this utility, copy it to the root directory of the boot drive and add
the line DEVICE=COMPAQF.SYS to the CONFIG.SYS. For best results, make this one
of the first lines in CONFIG.SYS. This device driver takes only 96 bytes.

Technical notes
---------------
Compaq uses int 16h function F0h to change CPU speeds. TurboPower also uses
int 16h function F0h to inquire about resident TSRs. TurboPower uses
subfunction F0h (AX = F0F0h). Compaq uses other subfunction codes. However,
recent int 16h handlers in the Compaq BIOS do not check the validity of the
subfunction code. Therefore they attempt to use subfunction F0h to change
processor speeds, resulting in unpredictable results. The COMPAQF.SYS device
corrects this problem by trapping int 16h calls where AX = F0F0h and does not
pass them on to the Compaq BIOS' int 16h handler.