KBAM (KEYed Binary Access Method)





                                   Version 1.1




                               User Documentation

















     
     
     
     
     
     
     
     
     
     
     
            (c) Copyright 1992, David L. Syrja, All Rights Reserved.


     KEYed Binary Access Method (kbam)                             Page:  1
     ----------------------------------------------------------------------




          Table of Contents:

     
          Introduction  ...........................................  2
     
          File Structures:
               KEY File ...........................................  3
               DATA File ..........................................  4
     
          Including KBAM in your program ..........................  5
          Definition of Variables .................................  5
          Summary of commands .....................................  5
          Summary of result/error codes ...........................  5
     
          Commands:
               CREATE .............................................  6
               OPEN(S) ............................................  6
               TLOCK ..............................................  7
               TUNLOCK ............................................  7
               HEADER .............................................  7
               READF ..............................................  8
               READL ..............................................  8
               READ ...............................................  9
               READR ..............................................  9
               READP .............................................. 10
               READN .............................................. 10
               WRITE .............................................. 11
               WRITER ............................................. 12
               REMOVER ............................................ 12
               REMOVE ............................................. 13
     
          Multi-User considerations:
               Opening SHARED Files ............................... 14
               Accessing SHARED Files ............................. 14

          Example ................................................. 15

          Changes from Version 1.0 ................................ 16














     ----------------------------------------------------------------------
     (c) Copyright 1992         David L. Syrja         All Rights Reserved.


     KEYed Binary Access Method (kbam)                             Page:  2
     ----------------------------------------------------------------------

     INTRODUCTION:

          The KBAM routine is a Power Basic (2.10f) Unit (kbamu.pbu) 
     designed for large files with multi-user requirements of DOS based 
     Networks, multiple processes under DOS, or multi-user DOS.  It is the 
     author's attempt at creating a file structure similar to the ones used 
     with versions of Basic/Four Corp's Business Basic Language. 

          KBAM supports two types of file structures:

               - KEY (Index) file
               - DATA File

          KEY records are maintained in ascending sequence while DATA 
     records are stored in the sequence in which they are written. 

          The routine uses the SEEK, GET$, and PUT$ commands to read and 
     write to BINARY disk files.  A file may also be opened as BINARY 
     SHARED to allow for accessing by multiple processes.  DOS SHARE must 
     be loaded for this feature. 

          KEY finds are done by using a binary search technique.  Deleted 
     record space is flagged and recovered as new records are written into 
     the file.  The KEY or DATA records must be strings.  KEY record sizes 
     may be a minimum of 1 byte and DATA record sizes from 4 to 8189 bytes. 
     
          KEY writes are accomplished with a binary tree approach.  When a 
     KEY block becomes full, it is split in two to provide room for 
     additional records.  This means that an insertion of a KEY record is 
     only done in a block and the entire file does not have to be PUSHED 
     down or PULLED up.  Block sizes may be 512, 1024, 2048, 4096 or 8192.

          The routine supplied here only allows a maximum of 1,000 KEY 
     records.  Enough for you to try it, to see if you like it.  There is a 
     $50 fee for the FULL version - no additional run-time charges.  The 
     documentation refers to the maximums for the FULL version.  
     
          Kbam may execute faster if written in assembler, but, it isn't! 


          Comments and suggestions are most welcome. 
     
     
               Dave Syrja
               322 Glen Park Avenue
               San Rafael, CA  94901

               CompuServe: 73677,1000
     
     

     Disclaimer:  This routine is supplied as is and no claims are made to
                  its suitability or merchantibility.  It has undergone
                  exhaustive testing but is NOT certified to be error free.

     ----------------------------------------------------------------------
     (c) Copyright 1992         David L. Syrja         All Rights Reserved.


     KEYed Binary Access Method (kbam)                             Page:  3
     ----------------------------------------------------------------------

     File Structures:
     
     KEY File:
          The KEY file structure deals with Disk Blocks.  The first 2048
     bytes in the file is the file header: 

          Description                Loc  Lgth  Type   Comment
          -----------                ---  ----  ----   -------
          File identification          1     4   A     KBAM
               type                    5     1   A     I-KEYed Index
          KEY Record Size              6     2   CVI   1 to (bsz-2)/2-4
          Number of Records Used       8     4   CVL
          Block Size (bsz)            12     2   CVI   
          Last Access Pointers        14     6
          Index Block Map             20    32
          Used Block Bit Map          52  1997
     
          The used block bit map controls a total of 8*1997=15976 blocks 
     which are assigned as either INDEX blocks or KEY blocks and have a 2 
     byte block length indicator.  The Index Block Map in the header block 
     maintains the INDEX blocks (Maximum 16) in ascending sequence.  Each 
     INDEX block maintains the ascending sequence of a number of KEY 
     blocks. 
          The KEY blocks maintain the actual KEY records in ascending 
     sequence and the DATA record pointer.  The number of bytes required to 
     store the KEY record is the length of the KEY string plus 4 bytes for 
     the DATA record pointers. 
          The KEY file increases in size as new blocks are added and is 
     DYNAMIC in that respect.  When blocks are deleted, the used block bit 
     map is adjusted to make those blocks available.  The file DOES NOT 
     decrease in size when blocks are deleted, but will not increase in 
     size until after all deleted blocks are used.  Maximum file size is: 
     2048+15976*bsz or 2048+16*bsz+16*bsz*(bsz-2)/2 whichever is less.
          The maximum KEY records (best case) may be calculated as:
               m = Maximum number of KEY Records
               b = Block size                '512/1024/2048/4096/8192
               s = KEY record size
               k = fix((b-2)/(s+4))          'KEYs per block
               i = fix((b-2)/2)              'Indices per block
               kb = m/k                      'No. of KEY blocks 
               ib = m/(k*i)                  'No. of Index blocks (Max 16)
               ib+kb = 15976                 'Maximum number of blocks
          With a KEY record size of 16 the maximum records are:
               Block Size:   512    Maximum Records:   102,000
               Block Size: 1,024    Maximum Records:   416,976
               Block Size: 2,048    Maximum Records: 1,627,960
               Block Size: 4,096    Maximum Records: 3,257,512
               Block Size: 8,192    Maximum Records: 6,532,588
          Generally, the smaller the block size the faster the access.
     
          This structure may be used for creating a KEYed index into ANY
     file that can be opened as BINARY.
     

     ----------------------------------------------------------------------
     (c) Copyright 1992         David L. Syrja         All Rights Reserved.


     KEYed Binary Access Method (kbam)                             Page:  4
     ----------------------------------------------------------------------

     File Structures (cont'd):
     
     DATA File:
          This structure is supplied to store the DATA records.  They are 
     written to the file in the order of the WRITE requests.  Each record 
     has a one byte overhead which is used as a flag to indicate if the 
     record is active or deleted. 
          Each deleted record has a pointer to the previously deleted 
     record.  The file header maintains the record number of the last 
     deleted record and is as follows:

          Description                Loc  Lgth  Type   Comment
          -----------                ---  ----  ----   -------
          File identification          1     4   A     KBAM
               type                    5     1   A     D-DATA
          DATA record size             6     2   CVI   4-8189
          Number of records used       8     4   CVL
          Last record number used     12     4   CVL
          Last record number deleted  16     4   CVL
          DATA records                20     ?

          As new records are written to the file, they are written over 
     the last record deleted.  If there are no deletes, they are added to 
     the end of the file.  The file grows as new records are written.  
     Deletions do not decrease the physical disk space required.
          It is strongly suggested that the information necessary to re-
     create the KEY files be included as part of the DATA.  Systems do go 
     down occasionally (or the operator hits CTL-ALT-DEL) and files may be 
     corrupted.

























     ----------------------------------------------------------------------
     (c) Copyright 1992         David L. Syrja         All Rights Reserved.


     KEYed Binary Access Method (kbam)                             Page:  5
     ----------------------------------------------------------------------

     Including KBAM in your program:
          $link "KBAMU.PBU"
          declare sub kbam (integer,string,string,integer,integer,_
                            string,string,long,long,integer)
          call kbam (kbamf%,kbamn$,kbamt$,kbams%,kbamb%,_
                     kbamc$,kbamd$,kbamr&,kbamn&,kbame%)


     Definition of variables:
          kbamf% - File number
          kbamn$ - File name
          kbamt$ - File type   I-KEYed Index, D-DATA
          kbams% - Size of DATA or KEY record
          kbamb% - Block Size (KEY file only)
          kbamc$ - Command (case insensitive)
          kbamd$ - DATA or KEY record
          kbamr& - DATA record pointer
          kbamn& - Number of records in file
          kbame% - Result/Error code (kbam does not process DOS errors)


     Summary of commands (kbamc$):
          Command   Description                       KEY  DATA 
          -------   -----------                       ---  ----
          CREATE    Make File                          Y     Y
          OPEN      Open File                          Y     Y
          OPENS     Open File as SHARED                Y     Y
          TLOCK     Lock File Header                   Y     Y
          TUNLOCK   Unlock File Header                 Y     Y
          HEADER    Return File Header Information     Y     Y
          READF     Read First KEY/DATA record         Y     Y
          READL           Last KEY/DATA record         Y     Y
          READ      Read KEY record = kbamd$           Y      
          READR     Read DATA record = kbamr&                Y
          READP     Read KEY record < kbamd$           Y      
          READN     Read KEY record > kbamd$           Y
          WRITE     Write NEW KEY/DATA record          Y     Y
          WRITER    Write DATA record = kbamr&               Y     
          REMOVER   Remove DATA record = kbamr&              Y      
          REMOVE    Remove KEY record = kbamd$         Y


     Summary of Result/Error codes (kbame%):
          Code  Explanation            Code  Explanation
          ----  -----------            ----  -----------
           00   Command successful  
           01   File exists             07   Bad Command       
           02   File not KBAM file      08   Record not found   
           03   File is empty           09   Beginning of file    
           04   End of file             10   KEY already exists
           05   Deleted record          11   No Delete - no record
           06   Full file               12   Error in variable



     ----------------------------------------------------------------------
     (c) Copyright 1992         David L. Syrja         All Rights Reserved.


     KEYed Binary Access Method (kbam)                             Page:  6
     ----------------------------------------------------------------------
     
     CREATE
     ======
          Creates and initializes a kbam KEY or DATA file.

          Variables before call:
               kbamn$ - File name
               kbamt$ - File type (I-KEYed Index or D-DATA)
               kbams% - Number of bytes in KEY or DATA record.  Does NOT
                        include the size of the DATA pointer for KEY files.
                        KEY  Min/Max: 1/fix((bsz-2)/2)-4
                        DATA Min/Max: 4/8189
               kbamb% - Block size (KEY file only)
               kbamc$ - CREATE
     
          Variables after call:
               kbamn$ - File name
               kbamt$ - File type (I-KEYed Index or D-DATA)
               kbams% - Number of bytes in KEY or DATA record.
               kbamb% - Block size (KEY file only)
               kbamc$ - CREATE
               kbame% - 00 - command successful
                        01 - file already exists
                        12 - error in variables
     


     OPEN(S)          
     =======
          Opens a KEY or DATA file as BINARY or BINARY SHARED.
     
          Variables before call:
               kbamf% - If set at ZERO the freefile function is used to get 
                        the next available file number otherwise the number 
                        in kbamf% is used. 
               kbamn$ - File name
               kbamc$ - OPEN or OPENS
     
          Variables after call:
               kbamf% - File number of opened file
               kbamn$ - File name
               kbamt$ - File type (I-KEYed Index or D-DATA)
               kbams% - Number of bytes in KEY or DATA record.
               kbamb% - Block size (KEY file only)
               kbamc$ - OPEN or OPENS
               kbamn& - Number of records in file.
               kbame% - 00 - command successful
                        02 - not kbam file

          Note:
               OPENS requires DOS SHARE to be loaded.

     



     ----------------------------------------------------------------------
     (c) Copyright 1992         David L. Syrja         All Rights Reserved.


     KEYed Binary Access Method (kbam)                             Page:  7
     ----------------------------------------------------------------------
     
     TLOCK
     =====
          Locks the file header area by performing: LOCK #kbamf%,0
          This has the effect of temporarily locking the file to other 
          processes since the kbam routine attempts to read the file header 
          before performing any read/write/remove commands. 

          Variables before call:
               kbamf% - File number (must be opened file)
               kbamc$ - TLOCK
     
          Variables after call:
               kbamf% - File number
               kbamc$ - TLOCK
               kbame% - 00 - command successful
          Note:
               DOS SHARE must be loaded.
     
     
     TUNLOCK
     =======
          Unlocks the file header area by performing: UNLOCK kbamf%,0

          Variables before call:
               kbamf% - File number (must be opened file)
               kbamc$ - TUNLOCK

          Variables after call:
               kbamf% - File number
               kbamc$ - TUNLOCK
               kbame% - 00 - command successful
          Note:
               DOS SHARE must be loaded.
     

     HEADER
     ======
          Returns information from the file header.

          Variables before call:
               kbamf% - File number (must be opened file)
               kbamc$ - HEADER
     
          Variables after call:
               kbamf% - File number
               kbamt$ - File Type  I/D
               kbams% - Record Size (does not include 4 byte DATA pointer 
                        for KEY files)
               kbamb% - Block Size (KEY file only)
               kbamc$ - HEADER
               kbamn& - Number of records in file
               kbame% - 00 - command successful
                        12 - error in variable


     ----------------------------------------------------------------------
     (c) Copyright 1992         David L. Syrja         All Rights Reserved.


     KEYed Binary Access Method (kbam)                             Page:  8
     ----------------------------------------------------------------------

     READF
     =====
          Reads the first record in a kbam KEY or DATA file.

          Variables before call:
               kbamf% - File number (must be opened file)
               kbamc$ - READF
     
          Variables after call:
               kbamf% - File number
               kbamt$ - File Type  I/D
               kbams% - Record Size (does not include 4 byte DATA pointer 
                        for KEY files)
               kbamb% - Block Size (KEY file only)
               kbamc$ - READF
               kbamd$ - KEY or DATA record
               kbamr& - Pointer to DATA record
               kbamn& - Number of records in file
               kbame% - 00 - command successful
                        03 - file is empty
     



     READL
     =====
          Reads the last record in a kbam KEY or DATA file.

          Variables before call:
               kbamf% - File number (must be opened file)
               kbamc$ - READL
     
          Variables after call:
               kbamf% - File number
               kbamt$ - File Type  I/D
               kbams% - Record Size (does not include 4 byte DATA pointer 
                        for KEY files)
               kbamb% - Block Size (KEY file only)
               kbamc$ - READL
               kbamd$ - KEY or DATA record
               kbamr& - Pointer to DATA record
               kbamn& - Number of records in file
               kbame% - 00 - command successful
                        03 - file is empty
     









     
     ----------------------------------------------------------------------
     (c) Copyright 1992         David L. Syrja         All Rights Reserved.


     KEYed Binary Access Method (kbam)                             Page:  9
     ----------------------------------------------------------------------
     
     READ (KEY file only)
     ====
          Reads a KEY record equal to kbamd$.  If the record does not exist 
          in the file, the next highest record is returned.  kbame% is set 
          to 00 if the record is found and to 08 if the next highest record 
          is found. 

          Variables before call:
               kbamf% - File number (must be opened file)
               kbamc$ - READ
               kbamd$ - KEY record to be found
     
          Variables after call:
               kbamf% - File number
               kbamt$ - File Type: I
               kbams% - KEY Record Size (doesn't include 4 byte pointer) 
               kbamb% - Block Size
               kbamc$ - READ
               kbamd$ - KEY record
               kbamr& - Pointer to DATA record
               kbamn& - Number of records in file
               kbame% - 00 - command successful
                        03 - file is empty
                        08 - next highest found
                        04 - end of file
     
          Note:
               The kbam routine pads out short KEYs with nulls before 
               performing the read.  It is possible to get to a particular 
               position in a file by providing a partial KEY.  kbam will 
               always return the next highest KEY.  (Also READN).


     READR (DATA file only)
     =====
          Reads a DATA record equal to kbamr&.
     
          Variables before call:
               kbamf% - File number (must be opened file)
               kbamc$ - READR
               kbamr& - Record number to be read
     
          Variables after call:
               kbamf% - File number
               kbamt$ - File Type: D
               kbams% - DATA Record Size
               kbamc$ - READR
               kbamd$ - DATA record
               kbamr& - Record Number
               kbamn& - Number of records in file
               kbame% - 00 - command successful
                        03 - file is empty
                        05 - deleted record
                        04 - end of file

     ----------------------------------------------------------------------
     (c) Copyright 1992         David L. Syrja         All Rights Reserved.


     KEYed Binary Access Method (kbam)                             Page: 10
     ----------------------------------------------------------------------

     READP (KEY file only)
     =====
          Returns the previous KEY to kbamd$.  (highest KEY < kbamd$)
     
          Variables before call:
               kbamf% - File number (must be opened file)
               kbamc$ - READP
               kbamd$ - KEY record
     
          Variables after call:
               kbamf% - File number
               kbamt$ - File Type: I
               kbams% - KEY Record Size (doesn't include 4 byte pointer) 
               kbamb% - Block Size
               kbamc$ - READP
               kbamd$ - KEY record
               kbamr& - Pointer to DATA record
               kbamn& - Number of records in file
               kbame% - 00 - command successful
                        03 - file is empty
                        09 - beginning of file
     
               Note:
                    Partial KEYs are padded with nulls.

     
     
     READN (KEY file only)
     =====
          Returns the next KEY to kbamd$.  (lowest KEY > kbamd$).
     
          Variables before call:
               kbamf% - File number (must be opened file)
               kbamc$ - READN
               kbamd$ - KEY record
     
          Variables after call:
               kbamf% - File number
               kbamt$ - File Type: I
               kbams% - KEY Record Size (doesn't include 4 byte pointer) 
               kbamb% - Block Size
               kbamc$ - READN
               kbamd$ - KEY record
               kbamr& - Pointer to DATA record
               kbamn& - Number of records in file
               kbame% - 00 - command successful
                        03 - file is empty
                        04 - end of file
     
          Note:
               The kbam routine pads out short KEYs with nulls before 
               performing the read.  It is possible to get to a particular 
               position in a file by providing a partial KEY.
     

     ----------------------------------------------------------------------
     (c) Copyright 1992         David L. Syrja         All Rights Reserved.


     KEYed Binary Access Method (kbam)                             Page: 11
     ----------------------------------------------------------------------

     WRITE (KEY file)
     =====
          Writes a NEW KEY record into the file.  Necessary to perform a 
          REMOVE and then a WRITE if the KEY remains the same and the DATA 
          pointer changes.  Duplicate KEYS are not allowed.
    
          Variables before call:
               kbamf% - File number (must be opened file)
               kbamc$ - WRITE
               kbamd$ - KEY record
               kbamr& - Record number of DATA record
     
          Variables after call:
               kbamf% - File number
               kbamt$ - File Type: I
               kbams% - KEY Record Size
               kbamb% - Block Size
               kbamc$ - WRITE
               kbamd$ - KEY record
               kbamr& - Pointer to DATA record
               kbamn& - Number of records in file
               kbame% - 00 - command successful
                        06 - file is full
                        10 - KEY already exists
          Note:
               Short KEY records are padded with nulls.  Long KEY records 
               are truncated on the right.
     


     WRITE (DATA file)
     =====
          Writes a NEW DATA record into the file.  Previously deleted 
          record space is utilized by this command.

          Variables before call:
               kbamf% - File number (must be opened file)
               kbamc$ - WRITE
               kbamd$ - DATA record
     
          Variables after call:
               kbamf% - File number
               kbamt$ - File Type: D
               kbams% - DATA Record Size 
               kbamc$ - WRITE
               kbamd$ - DATA record
               kbamr& - DATA record pointer (number)
               kbamn& - Number of records in file
               kbame% - 00 - command successful
                        06 - file is full
          Note:
               Short DATA records are padded with nulls.  Long DATA records 
               are truncated on the right. 
     

     ----------------------------------------------------------------------
     (c) Copyright 1992         David L. Syrja         All Rights Reserved.


     KEYed Binary Access Method (kbam)                             Page: 12
     ----------------------------------------------------------------------

     WRITER (DATA file only)
     ======
          Overwrites existing the DATA record.  The records used counter is 
          not incremented. 

          Variables before call:
               kbamf% - File number (must be opened file)
               kbamc$ - WRITER
               kbamd$ - DATA record
               kbamr& - DATA record pointer (number)
     
          Variables after call:
               kbamf% - File number
               kbamt$ - File Type: D
               kbams% - Record Size 
               kbamc$ - WRITE
               kbamd$ - DATA record
               kbamr& - DATA record pointer (number)
               kbamn& - Number of records in file
               kbame% - 00 - command successful
                        06 - file is full
          Note:
               Short DATA records are padded with nulls.  Long DATA records 
               are truncated on the right. 
     


     REMOVER (DATA file only)
     =======
          Removes the DATA record equal to kbamr&.
     
          Variables before call:
               kbamf% - File number (must be opened file)
               kbamc$ - REMOVER
               kbamr& - DATA record pointer (number)
     
          Variables after call:
               kbamf% - File number
               kbamt$ - File Type: D
               kbams% - DATA Record Size 
               kbamc$ - REMOVER
               kbamr& - DATA record pointer (number)
               kbamn& - Number of records in file
               kbame% - 00 - command successful
                        11 - no delete - no record









     
     ----------------------------------------------------------------------
     (c) Copyright 1992         David L. Syrja         All Rights Reserved.


     KEYed Binary Access Method (kbam)                             Page: 13
     ----------------------------------------------------------------------

     REMOVE (KEY file only)
     ======
          Removes the KEY record as specified by kbamd$.  Empty KEY and 
     INDEX blocks are recovered. 

          Variables before call:
               kbamf% - File number (must be opened file)
               kbamc$ - REMOVE
               kbamd$ - KEY record
     
          Variables after call:
               kbamf% - File number
               kbamt$ - File Type: I
               kbams% - Record Size
               kbamb% - Block Size
               kbamc$ - WRITE
               kbamd$ - KEY record
               kbamr& - Pointer to DATA record
               kbamn& - Number of records in file
               kbame% - 00 - command successful
                        06 - file is full
                        10 - KEY already exists
          Note:
               Short KEY records are padded with nulls.  Long KEY records 
               are truncated on the right.
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     
     ----------------------------------------------------------------------
     (c) Copyright 1992         David L. Syrja         All Rights Reserved.


     KEYed Binary Access Method (kbam)                             Page: 14
     ----------------------------------------------------------------------

     Multi-User considerations:


     Opening SHARED Files:

          To use a file in a multi-user environment it is necessary to open 
     the file with the OPENS command.  DOS SHARE must have been previously 
     loaded.



     Accessing SHARED Files:

          It is important to ensure that another process doesn't remove or 
     add records to the file when you are attempting to access it.  Kbam 
     provides the TLOCK and TUNLOCK functions to ensure that your I/O on 
     the file is complete before allowing access by another process.

          Kbam doesn't process DOS errors so you will have to provide the 
     necessary routines in your main program.  
     
         If you lock a file and do not unlock it, access may be unavailable 
     to the file.  KBAM only locks the first byte of the file so doing a 
     TUNLOCK command should should make the file accessible again. 

          Always TLOCK the file before doing any READ, WRITE and REMOVE 
     commands. 
     
          for example:

          Getfirst:                               
               try%=0                             'clear retry counter
               on error goto tryagain             'set error exit
               kbamf%=1                           'set file number
               kbamc$="TLOCK"                     'temp lock file
               call kbam (kbamf%,kbamn$,kbamt$,kbams%,kbamb%,_
                          kbamc$,kbamd$,kbamr&,kbamn&,kbame%)
               on error goto 0                    'reset error exit
               kbamc$="READF"                     'read first record
               call kbam (kbamf%,kbamn$,kbamt$,kbams%,kbamb%,_
                          kbamc$,kbamd$,kbamr&,kbamn&,kbame%)
               kbamc$="TUNLOCK"                   'unlock file
               call kbam (kbamf%,kbamn$,kbamt$,kbams%,kbamb%,_
                          kbamc$,kbamd$,kbamr&,kbamn&,kbame%)
               return
          tryagain:                               'Retry, may be TLOCKed by
               try%=try%+1                        'another process
               if try%>100 then resume errorhand
               resume
          errorhand:                              'Error handling routine





     ----------------------------------------------------------------------
     (c) Copyright 1992         David L. Syrja         All Rights Reserved.


     KEYed Binary Access Method (kbam)                             Page: 15
     ----------------------------------------------------------------------

     Example:
          You wish to create a DATA file called EXAMPLE.DAT with the 
     following information:

          Variable  Loc Lgth  Description
          --------  --- ----  -----------
                d$    1    8  Client number
                      9  200    "    information
                    209    8  Alpha Access

          The DATA file is to be accessed in two sequences, by Client 
     number and by an alphabetical access using two KEYed index files 
     EXAMPLE.CN and EXAMPLE.AA.

          $link "KBAMU.PBU"
          declare sub kbam (integer,string,string,integer,integer,_
                            string,string,long,long,integer)

          kbamf%=0                           'Create & Open Data File
          kbamn$="EXAMPLE.DAT"
          kbamt$="D"
          kbams%=216
          kbamc$="CREATE"
          call kbam (kbamf%,kbamn$,kbamt$,kbams%,kbamb%,_
                     kbamc$,kbamd$,kbamr&,kbamn&,kbame%)
          kbamc$="OPEN"
          call kbam (kbamf%,kbamn$,kbamt$,kbams%,kbamb%,_
                     kbamc$,kbamd$,kbamr&,kbamn&,kbame%)
          df%=kbamf%                         'Store File Number
     
          kbamf%=0                           'Create & Open Client Number Index
          kbamn$="EXAMPLE.CN"
          kbamt$="I"
          kbams%=8
          kbamb%=1024
          kbamc$="CREATE"
          call kbam (kbamf%,kbamn$,kbamt$,kbams%,kbamb%,_
                     kbamc$,kbamd$,kbamr&,kbamn&,kbame%)
          kbamc$="OPEN"
          call kbam (kbamf%,kbamn$,kbamt$,kbams%,kbamb%,_
                     kbamc$,kbamd$,kbamr&,kbamn&,kbame%)
          cf%=kbamf%                         'Store File Number

          kbamf%=0                           'Create & Open Alphabetical Index
          kbamn$="EXAMPLE.AA"
          kbams%=16
          kbamb%=1024
          kbamc$="CREATE"
          call kbam (kbamf%,kbamn$,kbamt$,kbams%,kbamb%,_
                     kbamc$,kbamd$,kbamr&,kbamn&,kbame%)
          kbamc$="OPEN"
          call kbam (kbamf%,kbamn$,kbamt$,kbams%,kbamb%,_
                     kbamc$,kbamd$,kbamr&,kbamn&,kbame%)
          af%=kbamf%                         'Store File Number

     ----------------------------------------------------------------------
     (c) Copyright 1992         David L. Syrja         All Rights Reserved.


     KEYed Binary Access Method (kbam)                             Page: 16
     ----------------------------------------------------------------------

          Records are written as follows:

          kbamd$=d$                                         'Write .DAT
          kbamc$="WRITE"
          kbamf%=df%
          call kbam (kbamf%,kbamn$,kbamt$,kbams%,kbamb%,_
                     kbamc$,kbamd$,kbamr&,kbamn&,kbame%)
     
          'kbamr& is returned as the DATA record file pointer
     
          kbamd$=left$(d$,8)                                'Write .CN
          kbamf%=cf%
          call kbam (kbamf%,kbamn$,kbamt$,kbams%,kbamb%,_
                     kbamc$,kbamd$,kbamr&,kbamn&,kbame%)
     
          kbamd$=right$(d$,8)+left$(d$,8)                   'Write .AA
          kbamf%=af%
          call kbam (kbamf%,kbamn$,kbamt$,kbams%,kbamb%,_
                     kbamc$,kbamd$,kbamr&,kbamn&,kbame%)
     
     
     
          Records are removed as follows:
     
          kbamd$=left$(d$,8)                                'Remove .CN
          kbamf%=cf%
          kbamc$="REMOVE"                                   'Note command!
          call kbam (kbamf%,kbamn$,kbamt$,kbams%,kbamb%,_
                     kbamc$,kbamd$,kbamr&,kbamn&,kbame%)
     
          kbamd$=right$(d$,8)+left$(d$,8)                   'Remove .AA
          kbamf%=af%
          call kbam (kbamf%,kbamn$,kbamt$,kbams%,kbamb%,_
                     kbamc$,kbamd$,kbamr&,kbamn&,kbame%)
     
          'kbamr& is returned as the DATA record file pointer
     
          kbamf%=df%                                        'Remove .DAT
          kbamc$="REMOVER"                                  'Note command!
          call kbam (kbamf%,kbamn$,kbamt$,kbams%,kbamb%,_
                     kbamc$,kbamd$,kbamr&,kbamn&,kbame%)
     

     Note: Do TLOCK command before reading, writing, or removing from 
           SHARED files.  Don't forget to TUNLOCK.

     
     
     
     
     
     
     


     ----------------------------------------------------------------------
     (c) Copyright 1992         David L. Syrja         All Rights Reserved.


     KEYed Binary Access Method (kbam)                             Page: 17
     ----------------------------------------------------------------------

     Changes from Version 1.0

          Version 1.1 has the Index Block Map in the file header area
     interchanged with the Used Block Bit Map.  Each read/write/remove 
     command in a KEYed Index file WAS reading the Used Block Bit Map.
     It is NOW only read when a new block is required.  Saves an auto-
     matic read of 1997 bytes and speeds up all accesses.
















































     ----------------------------------------------------------------------
     (c) Copyright 1992         David L. Syrja         All Rights Reserved.