Here it is!   The  long  awaited ANSI emulator for QuickBASIC
4.5!   It emulates DOS's "ANSI.SYS" driver.   This version is  in
pure  QB-  but  once I get it working to everybody's satisfaction
I'll code it in assembly and re-post it.  It'll be one hell of an
ANSI emulator...

    ANSI.SYS is a device driver  that  comes with DOS.   It replaces
the normal "CON" driver  with  an  extended,   more  versatile  one.
ANSI.SYS recognizes special escape code sequences- a string starting
with  a  CHR$(27)  and  a  bracket "[".   For instance,  sending the
following string  to  ANSI.SYS  will  enable  bold  characters to be
printed:

    ESC[1m
        ...and this will turn it off:
    ESC[0m

    ANSI.SYS can really only recognize a small subset  of  the  ANSI
protocol developed by the American National Standards Institute (hee
hee A.N.S.I.) The escape codes ANSI.SYS "sees" are:

  -long name-       -short name-   -escape sequence-
Cursor Position         CUP         ESC[y;xH or ESC[y;xf
Cursor Up               CUU         ESC[#A
Cursor Down             CUD         ESC[#B
Cursor Forward          CUF         ESC[#C
Cursor Backward         CUB         ESC[#D
Device Status Reprt     DSR         ESC[6n or ESC[n
Cursor Position. Report CPR         ESC[y;xR
Restore Cursor Position RCP         ESC[u
Save Cursor Position    SCP         ESC[s
Erase In Line           EL          ESC[K
Erase In Display        ED          ESC[2J or ESC[J
Set Graphics Redition   SGR         ESC[#;#;...#m

The following are supported by ANSI.SYS, but are not supported by
PANSI.BAS:

Set Mode                SM          ESC[=#h
Reset Mode              RM          ESC[=#l
Keyboard Reassign       IBMKKR      ESC["str"p

#  is a optional number(if a number is omitted then it is assumed to
be 1).   "y;x"  are  optional  X  and  Y  coordinates of the screen.
Again, if none are given, they are assumed to be 1;1.  For instance,
the following escape commands have the same effect:

ESC[H       moves cursor to upper-left hand corner of screen
ESC[1;1H    "                                              "

Also, one operand may be omitted (the X coordinate):

ESC[5H      moves cursor to line 5 column 1
ESC[5;1H    "                             "

Notes on the "DSR" sequence...
Did you know that there is a way to detect if a remote terminal  has
ANSI  or  not?    If  the  receiver  responds with ESC[y;xR when the
following sequence is sent:

ESC[6n

Then it has ANSI.  I have used a couple of BBS's and doors which use
this method of detecting ANSI.

Using PANSI.BAS:

PANSI.BAS is modular,  and all  functions  are  in  procedures.    I
programed  it  with  ease of use in mind.   To make PANSI.BAS into a
.QLB file, use:
bc /t pansi.bas
link /q pansi.obj,pansi.qlb,,bqlb45.lib+qb.lib
(assuming bqlb45.lib and qb.lib are in your current directory)

All of the procedures are documented at the start of the program.

If you discover any bugs(I'm still  not sure if I handled monochrome
adaptors correctly),  then please let me know so  I  can  fix  them.
That's one of the reasons why I'm posting it.

Have fun! There are 4 programs:
PANSI.BAS  -main program  Ultra-cool K_Rad ANSI emulator
PANSI2.BAS -example #1    okay ANSI file printer
PANSI3.BAS -example #2    dorky terminal program
PANSI.BI   -include file  it's only an include file not much to say
                          (but  as  include  files  go  this sucker
                           ranks with the elite!)
*********                                
NOTE:   You  must  change  the  SendStatus procedure in PANSI.BAS to
output the status string to your comm package!!!  Don't forget that!
*********

No more "OPEN "CON" FOR OUTPUT AS #1" ! Life's great, isn't it?

Rich Geldreich