ERRORS.DOC                                           19 August 1992
----------
This is the unofficial compendium of error messages that may appear
during AutoCAD sessions.  They have been assembled from earlier files
and subsequent messages.  Included are short descriptions of what may
cause such errors and what, if anything, can be done to correct the
offending situation.  Any error messages not appearing in this document
and their solutions can be sent to Brian Boatright at 76216,3252. This
file will be updated periodically.



Errors Encountered during Drawing Initialization:
------------------------------------------------

Command list interruption (a, b)

Indicates the use of a lisp command before the drawing environment has
been fully initialized.  Although I'm not sure, I think the first number
"a" refers to the nesting level and the second number "b" refers to the
command used.  The error can occur in ACAD.LSP, or a lisp routine loaded
from ACAD.LSP, or from a menu's *.MNL ... in all cases, the error
indicates that a lisp expression like (command) or (setvar) is being
used outside of a (defun).  The best policy is to contain all lisp
expressions in (defun), or else in the special S::STARTUP (defun).


EREAD     Entity Read

One of the most common errors, this generally occurs when AutoCAD is
reading the drawing file for editing purposes. As AutoCAD unpacks the
drawing database, it may encounter a corrupted entity, or a sequence of
bytes that constitutes gibberish in terms of AutoCAD's structured,
indexed database, or an unexpected entity. This may also occur when the
drawing database is being written back out.  Drawing files can be
corrupted due to a hardware error, power surge or abnormal AutoCAD
session termination. Common culprits are bad data sectors on floppies or
hard drives, corrupted archives, and drive controller errors. The
following indicate the specific causes:

   EREAD 1 =  Entity size exceeded the size indicated in the header.
   EREAD 2 =  Pointer found where the entity record was expected.
   EREAD 3 =  Disk error while reading an entity.
   EREAD 4 =  Disk error while writing an entity.
   EREAD 5 =  Tcode out of range (see Tcode).
   EREAD 6 =  CRC error after initial successful drawing load.

Usually the error occurs after the drawing is nearly loaded and AutoCAD
is regenerating the drawing.  At this point one can usually Ctrl-C out
of the regen and get to a command prompt.  Sometimes a save or a
wblock-save will filter out the error.	Occasionally a DXFOUT and
subsequent DXFIN into a new drawing have worked.  If these fail, usually
the only recourse is to use the backup file. In a later section recovery
methods are discussed and a number of programs mentioned that may, in
some cases, recover the original drawing file.


EREGEN    Entity Regen

Indicates that AutoCAD has encountered an error while generating a
specific entity. Once an entity is read, it has to be generated on
screen. This means reducing its component fields and geometry into
a sequence of graphics requests.  If the parameters associated with
the entity being generated result in an error, AutoCAD will abort. 
An example of this would be an out-of-context entity such as a
vertex encountered while no "polyline" entity was being generated.


GETSM

Similar to SMIO


HMATH     High Precision Math

Indicates that one of AutoCAD's mathematical library functions has
generated an error.  A negative circle radius (caused by a corrupted
database), or invalid rotation angles, for example, may result in these
errors.  Editing a DXF file and scanning for abnormal numbers generally
identifies the problem.


LTINIT    Linetype Table Initialization

Indicates that AutoCAD has encountered an error while reading and
initializing the linetype section of the drawing file.  This may be
remedied by entering a <Ctrl-C> as soon as the Drawing Editor
begins regenerating the drawing file, and then using the DXFOUT
command to create a DXF file.  One can then examine the DXF file
for invalid linetype descriptions/entries.


MENU (1,3)

Release 12 reorganized the ACAD.MNU into ACAD.MNL (for AutoLISP
routines), and ACAD.DCL (for dialog boxes).  You need to run the
ACADR12.LSP in your ACAD.LSP to be able to load old menues.


: OPEN ERROR -- File not found

If you see this error message while loading ACAD.EXE, it probably indicates
that an ADS file listed in your ACAD.ADS is not in the specified directory.


OUT OF RAM  or  OUT OF ENVIRONMENT SPACE

Try placing the following line into your Config.sys file:

    SHELL=COMMAND.COM /P /E:1024

Be sure to include the spaces.  Sometimes ACADFREERAM is not set right,
but if it always happens with the same drawing it may mean that AutoCAD
is being instructed to set up a table which is incredibly big -- like an
array with 1,000,000 copies of a block.


SMIO      Symbol Table I/O

Indicates that AutoCAD has encountered an error while reading or writing
to the symbol table section of the drawing file, which contains the
Layer, Linetype, Style, View, UCS, and VPORT entries.  Depending on when
this happened (while editing, during a PLOT, etc.), it could point to
corruption of the drawing file or of one of the temporary files
maintained in I/O page space by the drawing editor.


TCODE

Indicates a bad header record.  Possible work around is to examine the
header fields in the DXF file if the file is salvageable in that
fashion.



Errors Encountered during Drawing Editor Operation
------------------------------------------------

386|VMM: Stack pointer in unmapped pages

This error indicates a memory conflict involving protected mode drivers
and/or protected mode AutoCAD.  The message is being sent by the Virtual
Memory Manager working in protected mode.


AFPAGER

This message indicates the disk drive where the paging file is stored
has been filled.  Correct by either selecting another paging drive, or
freeing disk space.


BAGENT1

BAGENT1 error indicates that an invalid request has been received
from AutoLISP.  That's a pretty strange error to be getting, assuming
that the version of ACADL you're using matches the version of ACAD. Try
reloading either or both executables.


CS:EIP   (Code Segment: Extra (External?) Instruction Pointer)

This message indicates that a protected mode error has occurred. It is
usually caused by a TSR or ADI driver trying to write data into an area
of protected memory.


CVFIO     Compressed Vector File I/O

Indicates that the routine generating vectors for a plot or printer
plot sequence has encountered an error while reading or writing to
its temporary files.


DISK FULL

The "disk full" error message and the problems with saving blocks are
most likely related to a problem that AutoCAD had in addressing hard
disk partitions larger than 32 Meg (Actually this size may vary. The
number of cluster used on a harddisk seems to be the real culprit. This
may vary with different harddisk formatting schemes.)  This problem was
corrected in AutoCAD Release 9.04.


MWRITE failed m,n

An MWRITE error indicates that AutoCAD was trying to write the header
portion of the drawing file to disk (as for SAVE, END, or WBLOCK), but
the operation failed for some reason. The numbers indicate the expected
file position following the write (the length of the drawing file
header) and the actual file position.


NULL POINTER ERROR

Usually caused by a conflict in protected memory that is caused when a
TSR or ADI driver tries to write data into the protected area. May be
also caused by bad memory chips or lack of available disk space.


RFSUBS    Refresh File Subroutines

Indicates that AutoCAD's attempts to read/write to the (temporary)
refresh file have failed.  AutoCAD maintains a "refresh file" that
describes the present state of the graphics screen and refers to this
file during redraws, zooms and pans.  The error indicates that a
read/write to this temporary file has failed. Misbehaving memory boards
and hard disk controllers could cause this message to crop up.


RFSUBS NXT    (Same as above)

The message indicates that an I/O error of some sort (possibly a
premature end-of-file condition) occurred while AutoCAD was attempting
to read one of its temporary files (in this case, the "refresh" file,
which is AutoCAD's version of a display list). AutoCAD read a record
length from the file and then attempted  to read the associated record,
but encountered an error in doing so. This could be due to a software
error (bug), to any number of memory or disk hardware problems, to
improper assignment of extended memory environment variables, or to an
unrecognized RAM disk.


SCANDR    Scan Database Record

This indicates that AutoCAD has encountered an error while attempting to
update its temporary files at run-time.  While the AutoCAD Drawing
Editor is running, AutoCAD frequently has to mark changes and new
additions to the temporary files containing the present "state" of the
drawing database.  If any of these attempts to update the drawing
database or to update the files referenced by the Drawing Editor fail,
AutoCAD may abort with the above error.


SCANDR 10:  Unterminated complex entity recovery required.

The message means that during the scanning of the drawing file a entity
was found that wasn't correctly terminated.  Most likely a polyline
wasn't terminated properly in the file.  If this doesn't happen often it
was probably a small glitch like a bad sector on the hard disk, a power
fluctuation, or sunspots.  If you keep getting errors, however, you have
a problem somewhere.


XPAGEIO   EXtended I/O Paging

Indicates that AutoCAD's paging routines have encountered an error
during a read or write to its Extended I/O pages.  AutoCAD's Extended
I/O page space contains any detected LIM Expanded Memory and
conventional Extended Memory divided into "pages". As the drawing editor
generates data that does not fit in 640K of RAM, AutoCAD's paging
routines store data in any available Extended I/O page space.
Subsequent read requests are also routed to this data cache.  Failure to
read or write successfully to this chained set of data pages results in
this error.



Errors Specific to the MS-DOS / PC Environment
------------------------------------------------

CHECKFD     Check File Descriptor

Indicates that AutoCAD's file descriptor table has encountered an
error during bookkeeping.  It may be trying to close a file that
has already been closed.


FMTOUT	    Format Output

This is an error message in Release 10.  It indicates that AutoCAD's
output formatting code has encountered an error during initialization or
at run-time.  This error tends to indicate a problem with the math
co-processor.  Ensure that the motherboard switches for the math
co-processor are set correctly, and that the co-processor is seated
properly in the board sockets.


FREE      Free memory block

Indicates that AutoCAD has encountered an error while attempting to
release a block of memory.  This could be caused by an improper
operating environment or by the presence of TSR programs.  This could
point to a software bug (losing track of the buffer address, or
overwriting the housekeeping info in the buffer).  It could also be
caused by faulty hardware (dropped bit in memory or on disk).



Miscellaneous Errors
------------------------------------------------

SHELL: Error swapping temp file

Indicates a hardware error encountered while paging to extended memory
or hard disk during execution of the Shell command. 


SHELL: Insufficient memory to continue

Indicates that the AutoCAD shell handler has detected insufficient free
memory prior to invoking a DOS program.  While this can be caused by an
incorrect entry in the ACAD.PGP file for the program in question, it can
also be caused by the presence of a TSR program or a device driver that
has been loaded, and is fielding an interrupt that points back to the
heart of AutoCAD's code space. AutoCAD expects to "own" all such
interrupts (ones that point back to itself).  Whenever it encounters one
that it does not own, AutoCAD does not swap to DOS, to avoid running the
risk of de-stabilizing the machine (by swapping out a critical device
driver).  Network drivers and interrupt-driven mouse drivers like the
Mouse Systems Mouse driver are common culprits here.


VS: Not a string record  [Virtual String Record]

Indicates that AutoCAD has encountered an error while reading a
string from the ACADVS.OVL overlay file.  This file contains most
of the prompts and text information associated with AutoCAD.  A VS
error indicates that the ACADVS.OVL file has been corrupted. Reload
the file from your original set of diskettes and ensure that your
machine is set up properly.



POSSIBLE CAUSES AND GENERAL ERROR RECOVERY
------------------------------------------

Almost all errors are caused by corruption of one of the following:

     1. The drawing file that AutoCAD is reading
     2. The temporary files that AutoCAD has generated
     3. AutoCAD's working environment under MS-DOS

Drawing files can be corrupted due to several reasons:	floppy
diskettes may be bent or dirty, disk drives may need cleaning and
alignment, a voltage spike during a read or write to disk can
corrupt data, the disk drive may be highly fragmented, over-heated,
etc.  Remember that you cannot recover the drawing file in question
using a binary/hex editor to patch the data, or one of the popular
unerase utilities under MS-DOS, like Norton Utilities.	Norton's Disk
Doctor also will not recover corrupted drawing files since it only
relocates all the readable bytes to another area of the disk, ignoring
the unreadable ones.  AutoCAD drawing files are extremely sensitive and
as much as one misplaced bytes can render the file unreadable.	The hex
dump that follows the Error message is merely a traceback of internal
addresses, telling the AutoCAD programmer the sequence of most recent
function calls that preceded the error.  It holds little significance
for the general customer.

Temporary files can be corrupted at run-time due to the reasons
above, and also due to improper configuration.  For example, if you
are running AutoCAD on a machine with EXTended memory, ensure that
AutoCAD has detected the presence of any RAM disks or partitioned
EXPanded memory.  If it has failed to do so, then any data that
AutoCAD has paged into its Extended I/O page space runs the risk of
being over-written by other information that is being written to
the RAM disk or the "other memory partition".

Under MS-DOS, AutoCAD establishes and maintains a tight working
environment consisting of memory blocks, data resources and
software interrupts.  Should an ill-behaved TSR program or 
a device driver alter this carefully maintained state without
AutoCAD's knowledge, any data that AutoCAD is operating on runs the
risk of being corrupted during execution.

Whenever these error messages occur, AutoCAD is almost certainly
reporting a genuine case of data or environment corruption.  On
rare occasion, this may point back to a software bug within
AutoCAD.  These cases are almost always repeatable and occur due to
a specific sequence of events; e.g., if drawing a circle and
trimming it to 1/4" of its radius always generates an error in any
drawing, then you may have discovered a software bug.

What do I do if I encounter one of these errors ?

First of all, don't panic.  If the drawing file itself is corrupted, you
will encounter the error while calling up the drawing on any machine or
copy of AutoCAD.  In this situation, you can either:  return to the
backup of the drawing file in question (backing up your data on a
regular basis is critical), or use the procedure outlined in Appendix F
of the Reference Manual under "Disaster Handling". If neither of these
options work, you may choose to call on the following vendors for their
drawing file salvaging utilities. Please note that this does not
constitute an endorsement from Autodesk on the performance of these
utilities.


     Name of Utility          Company and Contact Information

     AutoSave                 Cyco Automation     800 336-6644
     Retriever                Pan Dimensional     707 869-0682
     D2D                      Great SoftWest      800 231-6880