Publication Part Number W0001-520
    Sheet  1 of 47
    
    
    
    
    
    
    
    
    
    
    
    
    
    
    
    
    
    
    
    
    
    
    
    
    
                              Title:  IBM PC, MS DOS
                                      CCPADI
                                   Version 3.0
    

    Publication Part Number W0001-520
    Sheet  2 of 47
    
                                     CONTENTS
            Heading                                                  Page
         
         General description...........................................4
         Installation..................................................6
         Operations....................................................7
         Main Screen...................................................7
         Info..........................................................8
         Communications................................................9
              PORT.....................................................9
              Network Plotting........................................10
              Baud Rate...............................................10
              Parity..................................................10
              Flow....................................................10
         Sync,eob,cksum...............................................11
              Nbr of syncs............................................11
              Sync code value.........................................11
              EOB code value..........................................12
              Checksumming............................................12
         Plotter......................................................13
         MISC options.................................................14
              Scale...................................................14
              Copies..................................................14
              Colors..................................................15
              Radix...................................................15
              CDCL....................................................15
         Loading CCPADI into memory...................................15
         OK  .........................................................16
         CANCEL.......................................................16
         Configuring AutoCAD 11.......................................17
         Configuring AutoCAD 10.......................................22
         

    Publication Part Number W0001-520
    Sheet  3 of 47
    
         Configuring CalComp Plotters.................................26
              1023 Artisan............................................27
              1025 Artisan............................................27
              1026 Artisan............................................27
              1043....................................................30
              1044....................................................30
              1073,1075,1077..........................................31
              2024....................................................32
              2026....................................................32
              52224...................................................36
              52424...................................................36
              52236...................................................36
              52436...................................................36
              67436...................................................36
              68436...................................................36
              68444...................................................36
              57424...................................................38
              57436...................................................38
              57444...................................................38
              58424...................................................38
              58436...................................................38
              58444...................................................38
              5912....................................................40
              5913....................................................40
              5902A...................................................40
              6603 VRC................................................42
              6613 VRC................................................42
         
         List of materials............................................46
         Systems requirements.........................................46
         Default Pen Definitions......................................47
         Pen Width Table..............................................47
         

    Publication Part Number W0001-520
    Sheet  4 of 47
    
                               GENERAL DESCRIPTION
    
    This CalComp ADI (Autodesk  Device Interface) Driver is a memory 
    resident routine connected to interrupt 78H of AutoCAD that generates 
    CalComp 907/PCI commands for CalComp plotters.
    
    The CCPADI 3.0 has several advantages over other CalComp plotter 
    drivers.
    
     - Supports all current CalComp plotters and Vector printers.
    
     - Outputs Serially at 8 different baud rates.
    
     - Can use 7,e,1 or 8,n,1 parity.
    
     - Can use XonXoff, Hardware, or CalComp AckNak flow control
         protocols.
    
     - Outputs Centronics Parallel by bypassing the bios which will allow
         for at least a 2 to 1 increase in through put.
    
     - Outputs to a user named plot file.
    
     - Can download pen definitions with the plot data to relieve user
         from pen mapping on the plotter.
    
     - Can download a copy command to the plotter, sending the plot only
         one time and producing up to 63 copies.
    
     - User can tailor CalComp specific data parameters such as sync
         codes, EOB codes, and checksumming to match an existing plotter
         setup.
    
     - Smaller file size (typically about one-half)
    
     - CDCL setup information can be included with the plot to configure
         the plotter.  Calcomp Device Control Language is a way to
         re-configure the plotter to match the incoming plot file.
    
    

    Publication Part Number W0001-520
    Sheet  5 of 47
    
         Autocad ADI driver Plot Size Limit.
    
         When the user selects the step size and plot size using Autocad's 
         "Configure Plotter" function,  the total X or Y steps in a plot 
         (plot size multiplied by the stepsize) cannot exceed 65535.
         
         For plotters that use 2032 stepsize it would limit them to a 30 X 
         30" plotting area.  CCPADI 3.0 solves this problem by allowing 
         the user to set the stepsize in AutoCAD to 1016 and then doubling 
         the plot data in CCPADI 3.0.
         

    Publication Part Number W0001-520
    Sheet  6 of 47
    
                                 INSTALLATION
    
    Step 1. Check the CalComp shipped diskette.
         
         Insert the CalComp shipped diskette in Drive A or B.    Type 
         DIR A: or B:.  Check your diskette and compare the files with the 
         Section "List of Materials".  Also read  "System Requirements" 
         before you begin.
         
    Step 2. Installing files to hard disk.
    
         An install program is provided for installing CalComp ADI drivers 
         to your hard-disk.  The program will allow the user to select the 
         drive letter on which CalComp ADI drivers will be installed.  
         INSTALL will create a sub-directory called \CALCOMP and copy all 
         needed files.
         
         To execute INSTALL:
            
            Make the CalComp supplied floppy the current drive by typing:
            
              A:  or  B:  and press enter
              INSTALL     and press enter
            
         The install program will display an introduction and ask the user 
         to press any key to continue.  Press a key.
         
         Next the install program will ask which ADI driver to install.  
         There are two drivers available.  CCP386 is a protected mode 
         driver to use with AutoCAD 386 Version 10 or 11.  CCPADI is a 
         real mode driver to use with any version of AutoCAD.  Use the up 
         or down arrow keys to highlight the required driver and press 
         return.
         
         Next the install program will ask the user to select the hard 
         disk for installation.  If multiply drives are available a list 
         of the available drive names will be displayed.  Use the up or 
         down arrow keys to highlight the required hard disk and then 
         press return.
         
         INSTALL will check for the existence of a sub-directory called 
         \CALCOMP on the selected hard drive.  If the sub-directory exists 
         a warning message will be displayed and asks if the user wants to 
         continue.
         
         INSTALL will copy all programs and supporting files to the hard 
         drive selected and in a sub-directory called \CALCOMP.
         
         INSTALLATION COMPLETE
         

    Publication Part Number W0001-520
    Sheet  7 of 47
    
                              CCPADI OPERATIONS
    
    CCPADI must be configured before the driver can be loaded into memory. 
         NOTE:
            CCPCFG is a Graphical User Interface (GUI) program that can be 
            operated with or without a mouse.  With a mouse you select the 
            options to execute and 'Click' the left button.  Without a 
            mouse use the keyboard and press the letter Capitalized within 
            the Menu or Button required.
    
    To start CCPCFG make the CALCOMP subdirectory the current directory by 
    typing from the DOS prompt:
    
         cd /CALCOMP     and press return
    
    Then:
    
         CCPCFG          and press return
    
    The main graphical screen will be displayed looking something like 
    this:
    
    ----------------------------------------------------------------------
    | date                      TITLE                               time |
    ----------------------------------------------------------------------
    | Info  Communications  Sync,eob,cksum  Plotter  Misc  oK  canceL    |
    ----------------------------------------------------------------------
    |                                                                    |
    |                                                                    |
    |                                                                    |
    |                                                                    |
    |                                                                    |
    |                                                                    |
    |                                                                    |
    |                                                                    |
    ----------------------------------------------------------------------
    

    Publication Part Number W0001-520
    Sheet  8 of 47
    
    The second line down is a Horizontal Menu.  There are 7 items listed 
    on the menu:
    
         Info            Displays information about the program 
    
         Communications  Used to configure the communications options
    
         Sync,eob,cksum  Used to set the CalComp specific options
    
         Plotter         Used to define target plotter
    
         Misc            Used to set various miscellaneous options
    
         oK              Used save the options in options file.
    
         canceL          Used to abort the program
    
                                     INFO
    
    To see information about CCPCFG select the Info menu item with the 
    mouse and Click the left button or type 'I' on the keyboard.  A pop-up 
    will appear.  To clear the Information pop-up, click the mouse again 
    or press a key.
    
    

    Publication Part Number W0001-520
    Sheet  9 of 47
    
                                COMMUNICATIONS
    
    To configure communications, select the Communications menu item with 
    the mouse and click the left button or type 'C' on the keyboard.  
    Another window will appear.
    
    |--------------------------------------------------------------------|
    |                     COMMUNICATIONS OPTIONS                         |
    |                                                                    |
    |    PORT             BAUD RATE                       PARITY         |
    |  --------            -----                          ---------      |
    |  | Com1 |            | 1 | 300                      | 7,e,1 |      |
    |  --------            -----                          ---------      |
    |  | coM2 |            | 2 | 600                      | 8,n,1 |      |
    |  --------            -----                          ---------      |
    |  | Lpt1 |            | 3 | 1200                                    |
    |  --------            -----                          FLOW           |
    |  | lPt2 |            | 4 | 2400                    ------------    |
    |  --------            -----                         | Xonxoff  |    |
    |  | File |            | 5 | 4800                    ------------    |
    |  --------            -----                         | Hardware |    |
    |                      | 6 | 9600                    ------------    |
    |                      -----                         | Acknak   |    |
    |                      | 7 | 19200                   ------------    |
    |                      -----                                         |
    |                      | 8 | 38400                                   |
    |                      -----                         --------------- |
    |                                                    | oK | canceL | |
    |                                                    --------------- |
    |--------------------------------------------------------------------|
    
                                     PORT
    
    This column of options tells CCPADI 3.0 where to send the plot data.  
    The ports labeled, Com1, Com2, Lpt1, and Lpt2 are the physical ports 
    attached to the PC operating this driver and AutoCAD.  These settings 
    will not allow the data to be re-directed.  These ports are controlled 
    by CCPADI 3.0 directly, and the output does not go through the BIOS.
    
    Select the output port or file with the mouse and click the left 
    button or for a keyboard type:
    
         'C'     for Com1
         'M'     for Com2
         'L'     for Lpt1
         'P'     for lpt2
         'F'     for File
    
    

    Publication Part Number W0001-520
    Sheet 10 of 47
    
                               NETWORK PLOTTING
    
    If you wish to re-direct the output from a LPT or COM port to a 
    network,  select 'File' and when CCPADI 3.0 ask for the output file 
    name,  type in the name of the BIOS port (COM1, COM2, LPT1, or LPT2).
    
                                  BAUD RATE
    
    Baud rate is the speed at which CCPADI 3.0 will transmit data to the 
    plotter.  This options is invalid if LPT1 or LPT2 or File have been 
    selected in the PORT option.  Select the required baud rate with the 
    mouse and click the left button or for keyboard operations press:
    
         1     for 300 baud
         2     for 600 baud
         3     for 1200 baud
         4     for 2400 baud
         5     for 4800 baud
         6     for 9600 baud
         7     for 19200 baud
         8     for 38400 baud
    
                                    PARITY
    
    This option is invalid if LPT1 or LPT2 has been selected in the PORT 
    option.  Another phrase for parity is character framing.  I will not 
    give you the long definition of parity but instead will tell you that 
    the two most common character framing options are available.  The 
    standard character framing used for AutoCAD is 7,e,1.  Select the 
    parity you require with the mouse and click the left button or press 
    'E' for 7,e,1 or 'N' for 8,n,1
    
                                     FLOW
    
    This option is invalid if LPT1 or LPT2 has been selected in the PORT 
    option.  Flow is the method of controlling the flow if data between 
    the computer and the plotter.  CalComp plotters will function 1 of 
    three ways (Xon-Xoff, Hardware, or Acknak).  Select the flow control 
    you require with the mouse and click the left button or for keyboard 
    operations press:
    
         'X'      for Xonxoff
         'H'      for Hardware
         'A'      for Acknak
    
    To Save the options, select the oK button with the mouse and click 
    the left button or press 'K' on the keyboard.  To quit and revert back 
    to the last saved settings, select the canceL button with the mouse and 
    click the left mouse or press 'L' on the keyboard.
    

    Publication Part Number W0001-520
    Sheet 11 of 47
    
                                SYNC,EOB,CKSUM
    
    CalComp online 907/PCI data is record orientated and each record 
    begins with one or two 'SYNC' codes.  This sync code can be any ASCII 
    character with a decimal value between 2 and 127 inclusive.  Each 
    record ends with an 'EOB/EOM' code.  This EOB code can be any ASCII 
    control character with a decimal value between 2 and 31 inclusive.  A 
    special character can be inserted in the data directly in front of the 
    EOB/EOM code called the Checksumming character.  This character is 
    used to check for record validity.  Checking record validity will do 
    you no good using any of the Flow Control methods with the exception 
    of ACKNAK.  If a transmission error occurs, Xonxoff or Hardware flow 
    control methods allow for no error recovery.
    
    The choice of flow control is left to your discretion, but the options 
    are available to assist you in matching other software packages that 
    do not give you these options.
    
                                 NBR OF SYNCS
    
    This option will toggle between 1 and 2 every time is selected.  
    Select Nbr or syncs with the mouse and click the left button or press 
    'N' on the keyboard.
    
                               SYNC CODE VALUE
    
    This option, when selected,  will display a pop-up used to change this 
    value.
    
               ------------------------------
               |  Enter Sync Code Value     |
               | ------ /\                  |
               | |  2 |                     |
               | ------ \/                  |
               |                            |
               | ------------               |
               | | ok | esc |               |
               | ------------               |
               | ---------------------------|
    
    The operations of this pop-up vary depending if you are using a mouse 
    or keyboard.
    
    If using a mouse select the up or down arrow to increase or decrease 
    the counter every time you click the left button.  When the correct 
    number of copies is displayed, select the 'ok' button and click the 
    left button.  If you wish to quit without making any changes to the 
    original value, select the 'esc' button and click the left button.
    

    Publication Part Number W0001-520
    Sheet 12 of 47
    
    If using the keyboard, you can use the up or down arrow keys to 
    increase or decrease the value every time you press a key.  Another 
    way is to simply type in the number of copies using the number keys on 
    the keyboard.  The left or right arrow keys will position the cursor 
    to where you can insert or delete an incorrect number.  The backspace 
    key will work as well.  When the correct number of copies is displayed 
    press return.  If you wish to quit without making any changes to the 
    original value,  DO NOT PRESS the escape key.  The ESCAPE key will 
    terminate the program.  Press return and re-select the Sync,eob,cksum 
    function by typing 'S' on the keyboard and change as needed.
    
    
                                EOB CODE VALUE
    
    The operations of this option is the save as with SYNC CODE VALUE.
    
    
                                 CHECKSUMMING
    
    This option will toggle between enabled and disabled every time is 
    selected.  Select Checksumming with the mouse and click the left 
    button or press 'C' on the keyboard.
    
    To Save the options, select the oK button with the mouse and click 
    the left button or press 'K' on the keyboard.  To Quit and revert back 
    to the last saved settings, select the canceL button with the mouse and 
    click the left mouse or press 'L' on the keyboard.
    

    Publication Part Number W0001-520
    Sheet 13 of 47
    
                                   PLOTTER
    
    This menu item will display a window allowing the user to select the 
    target plotter.
    
    ----------------------------------------------------------------------
    |                        PLOTTER OPTIONS                             |
    |                                                                    |
    |-----                 -----                         -----           |
    || A | 1023            | H | 2036                    | O | 5912      |
    |-----                 -----                         -----           |
    || B | 1025            | I | 52224/52424/57424       | P | 5913      |
    |-----                 -----                         -----           |
    || C | 1026            | J | 52236/52436/57436/67436 | R | 6603 VRC  |
    |-----                 -----                         -----           |
    || D | 1043            | K | 57444                   | T | 6613 VRC  |
    |-----                 -----                         -----           |
    || E | 1044            | L | 58424                   | U | Plotmaster|
    |-----                 -----                         -----           |
    || F | 1073/1075/1077  | M | 58436/68436                             |
    |-----                 -----                                         |
    || G | 2024            | N | 58444                                   |
    |-----                 -----                         --------------- |
    |                                                    | oK | canceL | |
    |                                                    --------------- |
    ----------------------------------------------------------------------
    
    Select your plotter from the list with the mouse and click the left 
    button, or for keyboard operations press:
    
         'A'       for the 1023
         'B'       for the 1025
         'C'       for the 1026
         'D'       for the 1043
         'E'       for the 1044
         'F'       for the 1073 or 1075 or 1077
         'G'       for the 2024 Pacesetter
         'H'       for the 2036 Pacesetter
         'I'       for the 52224 or 52424 or 57424
         'J'       for the 52236 or 52436 or 57436 or 67436
         'K'       for the 57444
         'L'       for the 58424
         'M'       for the 58436 or 68436
         'N'       for the 58444
         'O'       for the 5912 Colorview
         'P'       for the 5913 Colorview
         'R'       for the 6603 VRC
         'T'       for the 6613 VRC
         'U'       for the 5902A Plotmaster

    Publication Part Number W0001-520
    Sheet 14 of 47
    
    To Save the options, select the oK button with the mouse and click 
    the left button or press 'K' on the keyboard.  To Quit and revert back 
    to the last saved settings, select the canceL button with the mouse and 
    click the left mouse or press 'L' on the keyboard.
    
    
                                 MISC OPTIONS
    
    These options are extra, used to tailor CCPADI 3.0 to the 
    configuration you are using:
    
    ----------------------------------------------------------------------
    |                            MISC OPTIONS                            |
    |                                                                    |
    |   SCALE        COPIES         COLORS          RADIX        CDCL    |
    |   -----         -----         -----          -----       -----     |
    |   | A | 1.0     | C | NO      | E | NO       | G | 95    | I | NO  |
    |   -----         -----         -----          -----       -----     | 
    |   | B | 2.0     | D | YES     | F | YES      | H | 59    | J | YES |
    |   -----         -----         -----          -----       -----     | 
    |                                                                    |
    |                                                    --------------- |
    |                                                    | oK | canceL | |
    |                                                    --------------- |
    ----------------------------------------------------------------------
    
    
                                    SCALE
    
    This options is used to double the data sent to CCPADI 3.0.  This is a 
    way to get around the AutoCAD ADI driver Plot Size Limit.  As we 
    discussed in the GENERAL DESCRIPTIONS use this option to double the 
    1016 stepsize configured in AutoCAD to 2032 stepsize for the plotter.  
    Select the scale factor required with the mouse and click the left 
    button or press 'A' for a scale factor of 1 or 'B' for a scale factor 
    or 2.
    
                                    COPIES
    
    CCPADI 3.0 has the capability to download the CCGL copies command to a 
    compatible plotter.  This option will tell CCPADI 3.0 to prompt the 
    user at plot time for the number of copies.  If your plotter is not 
    capable of accepting the copies command, these buttons will be grayed 
    out and inoperable.  Select the appropriate answer with the mouse and 
    click the left button or press 'C' for NO or 'D' for YES.
    
    

    Publication Part Number W0001-520
    Sheet 15 of 47
    
                                    COLORS
    
    CCPADI 3.0 has the capability to download the CCGL pen definitions 
    command to a compatible plotter.  If selected, CCPADI 3.0 will down 
    pen color and width commands to the plotter or to a file at the start 
    of every plot.  The colors and widths are listed in section titled 
    DEFAULT PEN DEFINITIONS.  Select the appropriate answer with the mouse 
    and click the left button or press 'E' for NO or 'F' for YES.  If your 
    plotter is not capable of accepting pen definition commands, these 
    buttons will be grayed out and inoperable. 
    
                                    RADIX
    
    This options will modify the plot data in order for the created plot 
    files to be upload to an EBCDIC computer for plotting on an attached 
    plotter.  The translation of ASCII to EBCDIC can vary between 
    computers and lowering the RADIX to 59 solves this problem.  If you 
    will not be uploading the plot files, always leave this option at 95.  
    Select the appropriate answer with the mouse and click the left button 
    or press 'G' for 95 or 'H' for 59.
    
                                     CDCL
    
    CCPADI 3.0 has the capability to download the CalComp Device Control 
    Language (CDCL) to a compatible plotter in order to configure the 
    plotter for the upcoming plot data.  Select the appropriate answer 
    with the mouse and click the left button or press 'I' for NO or 'J' 
    for YES.  If your plotter is not capable of accepting CDCL commands, 
    these buttons will be grayed out and inoperable. 
    
    To Save the options, select the oK button with the mouse and click 
    the left button or press 'K' on the keyboard.  To Quit and revert back 
    to the last saved settings, select the canceL button with the mouse and 
    click the left mouse or press 'L' on the keyboard.
    
    
                          LOADING CCPADI INTO MEMORY
    
    Since CCPADI is a memory resident, it must be memory resident before 
    AutoCAD is executed.  After execution of CCPCFG to configure CCPADI, 
    the driver can be loaded into memory.  Make the CALCOMP sub-directory 
    the current directory by typing at the DOS prompt:
    
         cd \CALCOMP    then press enter
         CCPADI         then press enter
    
    CCPADI 3.0 will display a banner message stating it is loaded.
    

    Publication Part Number W0001-520
    Sheet 16 of 47
    
                                     OK
    
    In order to SAVE all the options configured with CCPCFG, you must exit 
    the program by selecting the 'oK' menu item with the mouse and 
    clicking the left button or pressing 'K' on the keyboard.
    
    
                                     OK
    
    If you wish to exit the program and revert all options back to the 
    last saved settings, select the canceL menu item with the mouse and 
    click the left button or press 'L' on the keyboard.  A prompt will 
    appear asking if you really want to Quit.  Select Yes or No.
    

    Publication Part Number W0001-520
    Sheet 17 of 47
    
                        CONFIGURING AUTOCAD RELEASE 11
    
    Start up Autocad and answer each question prompted by AutoCAD as 
    follows:
    
              NOTE:  <cr> is the same as <return>
    
                   A U T O C A D (R)
    Copyright (c) 1982-91   Autodesk, Inc.  All Rights Reserved
    Release R11 c2 (4/5/91) 386 DOS Extender
    Serial Number:  xxx-xxxxxxxx
    Licensed to:    You the customer
    Obtained from:  Your ACAD dealer
    
    Main Menu
    
         0.  Exit AutoCAD
         1.  Begin a NEW drawing
         2.  Edit an EXISTING drawing
         3.  Plot a drawing
         4.  Printer Plot a drawing
    
         5.  Configure AutoCAD
         6.  File Utilities
         7.  Compile shape/font description file
         8.  Convert old drawing file
         9.  Recover damaged drawing
    
    Enter selection: 5 <cr>
    
                   A U T O C A D (R)
    Copyright (c) 1982-91   Autodesk, Inc.  All Rights Reserved
    Release R11 c2 (4/5/91) 386 DOS Extender
    Serial Number:  xxx-xxxxxxxx
    Licensed to:    You the customer
    Obtained from:  Your ACAD dealer
    
    Current AutoCAD configuration 
    
         Video Display:           IBM Enhanced Graphics Adapter
    
         Digitizer:               Microsoft Serial or Bus Mouse
    
         Plotter:                 Autodesk Device Interface
    
         Printer plotter:         None
    
    Press RETURN to continue:  <cr>
    

    Publication Part Number W0001-520
    Sheet 18 of 47
    
                   A U T O C A D (R)
    Copyright (c) 1982-91   Autodesk, Inc.  All Rights Reserved
    Release R11 c2 (4/5/91) 386 DOS Extender
    Serial Number:  xxx-xxxxxxxx
    Licensed to:    You the customer
    Obtained from:  Your ACAD dealer
    
    Configuration menu
    
         0.  Exit to Main Menu
         1.  Show current configuration
         2.  Allow detailed configuration
    
         3.  Configure video display
         4.  Configure digitizer
         5.  Configure plotter
         6.  Configure printer plotter
         7.  Configure system console
         8.  Configure operating parameters
    
    Enter selection <0>: 5 <cr>
    Your current plotter is Autodesk Device Interface
    Do you want to select a different one? <N> 
    
    If your current plotter is Autocad Device Interface plotter then skip 
    over available plotter/driver selection.
    
                                               Y <cr>
    
    

    Publication Part Number W0001-520
    Sheet 19 of 47
    
                   A U T O C A D (R)
    Copyright (c) 1982-91   Autodesk, Inc.  All Rights Reserved
    Release R11 c2 (4/5/91) 386 DOS Extender
    Serial Number:  xxx-xxxxxxxx
    Licensed to:    You the customer
    Obtained from:  Your ACAD dealer
    
    Available plotters:
    
          1.  None
          2.  ADI P386 plotter
          3.  Alpha Merics (obsolete)
          4.  Autodesk Device Interface
          5.  CalComp 906/907/PCI
          6.  Canon Laser Printer
          7.  Hewlett-Packard
          8.  Houston Instrument DMP Series
          9.  IBM 7300 Series
         10.  PostScript device
         11.  UNIX Plot device
    
    Select device number of ? to repeat list <1>: 4 <cr>
    
    Select output format:
    
         0.  ASCII file
         1.  Binary file
         2.  AutoCAD DXB file
         3.  Installed ADI driver
    
    Output format, 0 to 3 <0>: 3 cr
    Hexadecimal interrupt code (INT 0XXh) <78>: cr
    Does your plotter have multiple pens? <N> Y cr
    How many pens does it have, 2 to 127 <2>: 127 cr
    Does the plotter have multiple dashed line styles? <N> cr
    Is the plotter variable speed? <N> cr
    
    Next you will specify the maximum plot size the plotter
    can make, and the step size of the plotter.  You may 
    specify these either in millimeters or inches.  The
    next question selects the units.
    
    Specify plot size in millimeters? <N> cr
    Maximum horizontal (X) plot size in inches <11.00>: 50 cr
    Plotter steps per inch in the horizontal (X) direction <1000>: 1016 cr
    Maximum vertical (Y) plot size in inches <8.5> : 36 cr
    Plotter steps per inch in the vertical (Y) direction <1000>: 1016 cr
    

    Publication Part Number W0001-520
    Sheet 20 of 47
    
    If you have previously measured the lengths of a horizontal
    and a vertical line that were plotted to specific scale,
    you may use these measurements to calibrate your plotter.
    
    Would you like to calibrate your plotter? <N> N <cr>
    Size Units (Inches or Millimeters) <I> I or M <cr>
    Plot origin in Inches <0.00,0.00>: 0,0 <cr>
    
    Standard values for plotting size
    
    Size    Width   Height
    A       10.50     8.00
    B       16.00    10.00
    C       21.00    16.00
    D       33.00    21.00
    E       43.00    33.00
    MAX     50.00    36.00
    
    Enter the Size of Width,Height (in Inches) <MAX>: E <cr>
    Rotate plot 0/90/180/270 <0>: 0 <cr>
    Pen width in Inches <0.010>: <cr>
    Adjust area fill boundaries for pen width? <N> <cr>
    Remove Hidden lines? <N> <cr>
    
    Specify scale by entering:
    Plotted Inches=Drawing Units or Fit or ? <F>: <cr>
    
    

    Publication Part Number W0001-520
    Sheet 21 of 47
    
                   A U T O C A D (R)
    Copyright (c) 1982-91   Autodesk, Inc.  All Rights Reserved
    Release R11 c2 (4/5/91) 386 DOS Extender
    Serial Number:  xxx-xxxxxxxx
    Licensed to:    You the customer
    Obtained from:  Your ACAD dealer
    
    Configuration menu
    
         0.  Exit to Main Menu
         1.  Show current configuration
         2.  Allow detailed configuration
    
         3.  Configure video display
         4.  Configure digitizer
         5.  Configure plotter
         6.  Configure printer plotter
         7.  Configure system console
         8.  Configure operating parameters
    
    Enter selection <0>: 0 <cr>
    
    If you answer N to the following question, all configuration
    changed you have just make will be discarded.
    
    Keep configuration changes? <Y> Y<cr>
    
          FINISHED  The CalComp CCPADI driver is now configured.
    

    Publication Part Number W0001-520
    Sheet 22 of 47
    
                        CONFIGURING AUTOCAD RELEASE 10
    
    Start up Autocad and answer each question prompted by AutoCAD as 
    follows:
    
              NOTE:  <cr> is the same as <return>
    
              A U T O C A D
    Copyright (C) 1982,83,84,85,86,87,88,89 AutoDesk, Inc
    Release 10 c10 (12/21/89) DOS Extender
    Serial Number xxx-xxxxxxxxxx
    
    Main Menu
    
         0.  Exit AutoCAD
         1.  Begin a NEW drawing
         2.  Edit an EXISTING drawing
         3.  Plot a drawing
         4.  Printer Plot a drawing
    
         5.  Configure AutoCAD
         6.  File Utilities
         7.  Compile shape/font description file
         8.  Convert old drawing file
    
    Enter selection: 5 <cr>
    
              A U T O C A D
    Copyright (C) 1982,83,84,85,86,87,88,89 AutoDesk, Inc
    Release 10 c10 (12/21/89) DOS Extender
    Serial Number xxx-xxxxxxxxxx
    
    Configure AutoCAD.
    
    
    Current AutoCAD configuration
    
         Video Display:              IBM Enhanced Graphics Adapter
    
         Digitizer:                  Microsoft Serial or Bus Mouse
    
         Plotter:                    Autodesk Device Interface
    
         Printer plotter:            None
    
    Press RETURN to continue:  <cr>
    

    Publication Part Number W0001-520
    Sheet 23 of 47
    
              A U T O C A D
    Copyright (C) 1982,83,84,85,86,87,88,89 AutoDesk, Inc
    Release 10 c10 (12/21/89) DOS Extender
    Serial Number xxx-xxxxxxxxxx
    
    Configuration menu
    
         0.  Exit to Main Menu
         1.  Show current configuration
         2.  Allow detailed configuration
    
         3.  Configure video display
         4.  Configure digitizer
         5.  Configure plotter
         6.  Configure printer plotter
         7.  Configure system console
         8.  Configure operating parameters
    
    Enter selection <0>: 5 <cr>
    Your current plotter is Autodesk Device Interface
    Do you want to select a different one? <N> 
    
         If your current plotter is Autodesk Device Interface, then skip 
         over available plotter/driver selection.
    
                                               Y <cr>
    
              A U T O C A D
    Copyright (C) 1982,83,84,85,86,87,88,89 AutoDesk, Inc
    Release 10 c10 (12/21/89) DOS Extender
    Serial Number xxx-xxxxxxxxxx
    
    Available plotters:
    
          1.  None
          2.  ADI P386 plotter
          3.  Alpha Merics (obsolete)
          4.  Autodesk Device Interface
          5.  CalComp 906/907/PCI
          6.  Hewlett-Packard
          7.  Houston Instrument DMP Series
          8.  IBM 7300 Series
          9.  PostScript device
         10.  UNIX Plot device
    
    Select device number of ? to repeat list <1>: 4 <cr>
    

    Publication Part Number W0001-520
    Sheet 24 of 47
    
    Select output format:
    
         0.  ASCII file
         1.  Binary file
         2.  AutoCAD DXB file
         3.  Installed ADI driver
    
    Output format, 0 to 3 <0>: 3 cr
    Hexadecimal interrupt code (INT 0XXh) <78>: cr
    Does your plotter have multiple pens? <N> Y cr
    How many pens does it have, 2 to 127 <2>: 127 cr
    Does the plotter have multiple dashed line styles? <N> cr
    Is the plotter variable speed? <N> cr
    
    Next you will specify the maximum plot size the plotter
    can make, and the step size of the plotter.  You may 
    specify these either in millimeters or inches.  The
    next question selects the units.
    
    Specify plot size in millimeters? <N> cr
    Maximum horizontal (X) plot size in inches <11.00>: 50 cr
    Plotter steps per inch in the horizontal (X) direction <1000>: 1016 cr
    Maximum vertical (Y) plot size in inches <8.5> : 36 cr
    Plotter steps per inch in the vertical (Y) direction <1000>: 1016 cr
    
    If you have previously measured the lengths of a horizontal
    and a vertical line that were plotted to specific scale,
    you may use these measurements to calibrate your plotter.
    
    Would you like to calibrate your plotter? <N> N <cr>
    Write the plot to a file? Y or N <cr>
    Size Units (Inches or Millimeters) <I> I or M <cr>
    Plot origin in Inches <0.00,0.00>: 0,0 <cr>
    
    Standard values for plotting size
    
    Size    Width   Height
    A       10.50     8.00
    B       16.00    10.00
    C       21.00    16.00
    D       33.00    21.00
    MAX    163.80    23.50
    
    Enter the Size of Width,Height (in Inches) <MAX>: D <cr>
    

    Publication Part Number W0001-520
    Sheet 25 of 47
    
    Rotate 2D plots 90 degrees clockwise? <N>: N <cr>
    Pen width <0.010>: <cr>
    Adjust area fill boundaries for pen width? <N> <cr>
    Remove Hidden lines? <N> <cr>
    
    Specify scale by entering:
    Plotted Inches=Drawing Units or Fit or ? <F>: <cr>
    
              A U T O C A D
    Copyright (C) 1982,83,84,85,86,87,88,89 AutoDesk, Inc
    Release 10 c10 (12/21/89) DOS Extender
    Serial Number xxx-xxxxxxxxxx
    
    Configuration menu
    
         0.  Exit to Main Menu
         1.  Show current configuration
         2.  Allow detailed configuration
    
         3.  Configure video display
         4.  Configure digitizer
         5.  Configure plotter
         6.  Configure printer plotter
         7.  Configure system console
         8.  Configure operating parameters
    
    Enter selection <0>: 0 <cr>
    
    If you answer N to the following question, all configuration
    changed you have just make will be discarded.
    
    Keep configuration changes? <Y> Y<cr>
    
          FINISHED  The CalComp CCPADI driver is now configured.
    

    Publication Part Number W0001-520
    Sheet 26 of 47
    
                         CONFIGURING CALCOMP PLOTTERS
    
    You have the option of configuring CCPADI 3.0 to match an existing 
    plotter setup or you can take the defaults of CCPADI 3.0 and configure 
    the plotter to match.  
    

    Publication Part Number W0001-520
    Sheet 27 of 47
    
            Configuring the 1023, 1025, or 1026 (ARTISAN) plotter
    
    In the following prompts there will be several lines of instructions 
    for each question.  The ones preceded *D are the CCPADI 3.0 default 
    answers.  The ones preceded with *U are user definable and should be 
    written down so that CCPADI 3.0 can be configured to match.  If you 
    are going to configure CCPADI 3.0 to match the plotter setups,  do not 
    execute the *D instructions.
    
         *D    CCPADI 3.0 defaults
         *U    User defined
    
    Follow the instructions in Chapter 1 of the ARTISAN User's Guide to 
    load media.  Select the 'Manual' softkey.  When the plotter finishes 
    sizing the media,  the display will show:
    
              User#1     OrgRtrn
              Online      Replot
    
    Press the 'Next' key twice.  The display will show:
    
              Set-up        Test
              Size          Time
    
    Press the 'Set-up' softkey.  The display will show:
    
              Scale      PenParm
              Host    Form Align
    
    Press the 'Host' softkey.  The display will show:
    
              Format        Baud
              Data     Handshake
    
    Press the 'Format' softkey.
    
    *D  Use the lower left softkey to step through the list of data 
    Formats.  Stop when the display shows:
    
    *U        Data format
                 [PCI]
    
    Press the 'Exit key to return to Host menu.
    
              Format        Baud
              Data     Handshake
    

    Publication Part Number W0001-520
    Sheet 28 of 47
    
    Press the 'Baud' softkey.
    
    *D  Press the lower right softkey to step through the list of baud 
    rates.  Stop when the display shows:
    
    *U        Baud Rate
               [19.2K]
    
    Press the 'Exit' key to return to Host menu.
    
              Format        Baud
              Data     Handshake
    
    Press the 'Data' softkey.
    
    *D  Press the upper left softkey to change the number of data bits.  
    Stop when the number changes to [7 bit]
    
    *D  Press the upper right softkey to change the number of stop bits.  
    Stop when the number changes to [1 stop]
    
    *D  Press the lower left softkey to change the parity type.  Stop when 
    the parity reads [Even Parity].
    
    *U        [7 bit]   [1 stop]
                 [Even Parity]
    
    Press the 'Exit' key to return to Host menu.
    
              Format        Baud
              Data     Handshake
    
    Press the 'Handshake' softkey.
    
    *D  Press the lower left softkey to step through the list of handshake 
    protocols.  Stop when the display shows:
    
    *U        PCI Handshake
                [DirCntrl]
    
    Press the 'Exit' key to return to Host menu.
    
              Format        Baud
              Data     Handshake
    
    Press the 'Next' key.  The display will show the Sync menu:
    
              Sync        End Msg
              Chksum
    

    Publication Part Number W0001-520
    Sheet 29 of 47
    
    Press the 'Sync' softkey.
    
    *D  Press the upper left key to change the # of sync to 2
    
    *D  Press the '2' key twice to change the Sync Char to 22.
    
    The display will show:
    
    *U          # of sync [2]
                Sync char.     22
    
    Press the 'Exit' key to return to the Sync menu.
    
              Sync        End Msg
              Chksum
    
    Press the 'End Msg' softkey.
    
    *D  Press the '1' key and then the '3' key to change the End of Msg 
    char to 13.
    
    The display will show:
    
    *U   End of Msg Char 
                13
    
    Press the 'Exit' key to return to the Sync menu.
    
              Sync        End Msg
              Chksum
    
    Press the 'Chksum' softkey.
    
    *D  Press the lower left softkey until PCI mode chksum changes to 
    ENABLED.  The display will show:
    
    *U        PCI mode chksum
                 [ENABLED]
    
    If you have changed any of the above options, press the 'Exit' key 3 
    times.  The display will show:
    
              Save as User n?                  
    n is current user number
              Yes             No
    
         Press the lower left softkey to save configurations.
    
    If you were getting the current setups press the 'Exit' key 4 times to 
    return to the original menu.  The display will show:
    
              User#1     OrgRtrn
              Online      Replot
    
    Press the 'Online' softkey to plot.
    

    Publication Part Number W0001-520
    Sheet 30 of 47
    
                   Configuring the 1043 or 1044 Pen Plotter
    
    Set the switch on the back of the 1043/1044 plotter:
    
         Bit 1 2 3 4 5 6 7 8
             0 1 0 1 0 0 0 0   For Hardware handshaking but will work with
                                               any protocol.
    
    The Serial cable from the PC serial port should be attached to 'TO DTE 
    HOST' of the 1043/1044 plotter.
    
    Power the plotter on.  Press the 'Setup' key, then the number 7 and 
    then press the 'Enter Key'.  The display will show 'Host set up 
    number'.  Press 'Next', 'Enter', make changes if configuring the 
    plotter to match CCPADI 3.0 defaults, otherwise step through the Host 
    setups and write down what you find in order to Configure CCPADI 3.0 
    to match.  Repeat the process for 8 HOST set up modes ('Next' and 
    'Enter').
    
    For CCPADI 3.0 Defaults change to the following:
    
         Host Set Up Mode      Top              bottom
    
         0-Parity & bits/char  2 Even Parity    7 Bits/char
         1-Stop bits & clock   1 Stop Bit       0 Int clock
         2-Interface           0 Serial        00 IEEE Address
         3-Host Baud           19200            0 PCI Mode
         4-Muting & Checksum   NO Term muting   YES checksum
         5-Isochronous & EOM   NO Isochronous   13 End of Mess Char
         6-Direct Cntrl-Xon    YES Direct Cntrl NO XON/XOFF
         7-Term Baud & Duplex  19200            0 Full
         8-Sync Code & Value   2 Sync Code      22 Sync Code Value
    
    Press 'Save', Enter user number and press 'Enter' to save any changes 
    you might of made.
    

    Publication Part Number W0001-520
    Sheet 31 of 47
    
                Configuring the 1073, 1075, 1077 pen plotters.
    
    There are two types of controllers available for these plotters, the 
    PCI and the PLOT MANAGER.  It is best if Field Service is called in 
    order to determine what controller is present and how to set the 
    switches, jumpers or thumb wheel switches.  If you wish to attempt the 
    setup you will need the appropriate manual.
    

    Publication Part Number W0001-520
    Sheet 32 of 47
    
                   Configuring the 2024 or 2036 Pacesetter
    
    The Pacesetter plotters are unique in that they are the only CalComp 
    pen plotter capable of accepting data both serially or parallel.  The 
    setup procedures for the two are similar in most respects.
    
    The following paragraphs contain the procedures for changing the 
    communications parameters.  Each procedure is self-contained.
    
    To Change parameters, proceed as follows:
         
         1.  Power-on the plotter
         
         2.  Press the Menu key.
         
                                       NOTE
             The Port Type menu display only appears when the optional 
             Centronics interface is installed.  Skip this step and 
             proceed to step 4 if the plotter only has a RS-232C (serial) 
             port.
         
         3.  Press the up or down arrow keys until the display shows:
         
              Port Type:
         
             Use the left or right arrow keys to select Port Type:
         
              If serial                             If Parallel
         
              Port Type:                            Port Type:
               RS-232C                               Centronics
         
         4.  This step is only for serial communications.
             Press the down arrow key until the display shows:
         
              Protocol:
         
             Use the left or right arrow keys to select:
         
              Protocol:
                PCI
         
             If using parallel communications, skip to step 8.
         

    Publication Part Number W0001-520
    Sheet 33 of 47
         
         5.  Use the down arrow key to display:
         
              Baud Rate:
         
             Use the left or right arrow keys to select the correct baud 
         rate configured in AutoCAD.  CCPADI 3.0 defaults to:
         
              Baud Rate:
                 19200
         
         6.  Use the down arrow key to display:
         
              # of bits-parity
         
             Use the left or right arrow keys to select the correct number 
         of bits per character and the type of parity configured in 
         AutoCAD.  CCPADI 3.0 defaults to:
         
              # of bits-parity
                7-even
         
         7.  Use the down arrow key to display:
         
              Handshake:
         
            Use the left or right arrow keys to select the correct 
         handshaking configured in AutoCAD.  CCPADI 3.0 defaults to:
         
              Handshake:
                Hardware
         
         8.  Use the down arrow key to select:
         
              Sync # EOB CHK
         
            There are three pre defined configurations for this options 
         labeled A, B, or C.  Use the left or right arrow keys to display 
         each.  If one of the three selections match the configurations 
         stored in Autocad, display it and proceed to step 14.  CCPADI 3.0 
         defaults to:
         
              Sync # EOB CHK
              A:  22   2   13   ON
         
         

    Publication Part Number W0001-520
    Sheet 34 of 47
         
         9.  If none of the pre-defined configurations match your needs 
         select:
         
              Sync # EOB CHK
              Special Format-1 or 2
         
         10. Then press the down arrow key.  The following will be 
         displayed:
         
              PCI-# of sync
                   2
         
            Use the left or right arrow keys to change this value to match 
         the value configured in AutoCAD.
         
         11. Then press the down arrow key.  The following will be 
         displayed:
         
              PCI-Sync Char
                  22
         
            Use the left or right arrow keys to change this value to match 
         the value configured in AutoCAD.
         
         12. Then press the down arrow key.  The following will be 
         displayed:
         
              PCI-EOM Char
                  13
         
            Use the left or right arrow keys to change this value to match 
         the value configured in AutoCAD.
         
         13. Then press the down arrow key.  The following will be 
         displayed:
         
              PCI-Checksum
                 On
         
            Use the left or right arrow keys to change this value to match 
         the value configured in AutoCAD.
         
         

    Publication Part Number W0001-520
    Sheet 35 of 47
         
         14. Then press the down arrow key until the following is 
         displayed:
         
              Save as User:
                 NO
         
            Use the left or right arrow keys to select the user number 
         under which these value will be stored.
         
         15. Then press online.  The plotter is now ready for operation.
         

    Publication Part Number W0001-520
    Sheet 36 of 47
    
      Configuring the 52224, 52424, 52236, 52436, 67436, 68436, or 68444
    
    These setup instructions assume that a communications terminal is 
    attached to the TERM port located on the back of the plotter.
    
    Press <CTRL-P> and enter user PIN or press return.
    
    If you only wish to determine the present configuration of the plotter 
    use the DISPLAY command to display them.
    
    Determine which port is connected to your computer by tracing the 
    cable.  The 52224, 52236, 52424, and the 52436 have 1 parallel port 
    called 'PAR' and three serial ports called 'COM_1  COM_2  COM_3'.  The 
    67436, 68436 and the 68444 have two parallel and two serial ports 
    called PAR_1, PAR_2, COM_1, and COM_2 respectfully.
    
    If your PC is connected to a Parallel port type:
    
    DISP PAR on the 52224, 52236, 52424, 52436 to display the parallel 
    parameters or DISP PAR_n, where n is the parallel port number, on the 
    67436, 68436, or the 68444.
    
    To changed the Parallel parameters, TYPE:
    
         PAR  or PAR_n
    
         Input Monitor Dump                NO
    
         Host to Plotter CDCL              CENT
    
         Dead Job Time Out                 30
    
         Time Out Action                   Force
    
         Plot Command Language             907
    
         Steps Per Inch                    200 for the 52224 or 52236
                                           400 for the 52424, 52436,
                                                    67436, 68436, 68444
    
         Beginning of Record Sync Char    $16 hex
    
         Number of Sync Chars              2
    
         End of Record char                $D
    
         Checksum                          Y
    
         Print                             N
    

    Publication Part Number W0001-520
    Sheet 37 of 47
    
    If your PC is connected to COM_1, COM_2, or COM3 type
    
         COM_n                            n is either 1, 2, or 3
    
         Input Monitor dump                NO
    
         Baud Rate                         19200
    
         Character Framing                 7,e,1
    
         Host to plotter CDCL              CTS
    
         Plotter to Host CDCL              CTS
    
         Dead Job Time Out                 30
    
         Time out action                   Force
    
         Plot Command Language             907
    
         Steps per inch                    200 for the 52224 or 52236
                                           400 for the 52424 or 52436
                                                    67436, 68436, 68444
    
         Plot Data Protocol                CTS
    
         Beginning of Record Sync Char    $16
    
         Number of sync Chars              2
    
         End of Record Char                $D
    
         Checksum                          Y
    
    To save the setups type:
    
         SAVE n ALL    n is the user number.   The power on default user
                         number is 1.
    
    To retrieve a user setup type:
    
         USER n all    n is the user number.
    
    If the configurations are not saved they will be lost when the plotter 
    is powered off.
    

    Publication Part Number W0001-520
    Sheet 38 of 47
    
         Configuring the 57424, 57436, 57444, 58424, 58436, or 58444
    
    An example of configuring the 908K or XP board thru OPCOM.
    
         Refer to CalComp plotter users guide OPCOM (Operator 
         Communication) operations with the optional attached terminal.
         
         These setup instructions assume that a communications terminal is 
         attached to the TERM port located on the back of the plotter.
    
    PARALLEL COMMUNICATIONS:
    
      (Framing: bits, parity and stop bits are not applicable for
         Centronics interface).
    
         <CTRL-P>
    
    To change the communications parameters type:
    
         COM
    
         MODE                             CENT
    
         CSUM                             Y
    
         FRAME                             8,n,1
    
         EOB                              $D  or  13
    
         TACODE                            0
    
         CLOCKING                          ASYNC
    
         SYNC                             $16,$16  or  22,22
    
    To save the parameters type:
    
         SAVE n ALL   n is a user number
    
    To view the existing communications setups type:
    
         DISP COM
    

    Publication Part Number W0001-520
    Sheet 39 of 47
    
    If OPCOM is used,  these switches may be ignored.  This is provided as 
    reference for CalComp Customer Service and Field Analyst.
    
         An example of 908K Board Switch setting with CCPADI 3.0.
    
                         Bits
         Switches  8 7 6 5 4 3 2 1
    
           S3      0 0 0 1 1 1 0 1  (bit 8    diagnostic mode disabled
                                     bit 7    units = inches
                                     bit 6-4  plotter width = 36 inches
                                     bit 3-2  resolution = 400 dpi
                                     bit 1    indicates color)
    
           S4      1 1 0 0 0 0 0 0  (bit 8-7  disk type: 70 megabyte
                                     bit 6    single disk installed
                                     bit 5    tape bits/character: 8 bits
                                     bit 4    tape density: 1600 bpi
                                     bit 3-2  most significant strip
                                     bit 1    pen plotter limits emulation
                                              disabled)
    
           S5      0 0 1 0 0 0 1 0   bit 8-5  DIRECT CONTROL MODE
                   0 0 1 1 0 0 1 0            CENTRONICS
                                     bit 4-1  AutoCAD stepsize:  400/inch
    
           S6      0 1 1 0 1 1 0 1  (bit 8-4  End of buffer char = '13 $D'
                                     bit 3-1  character framing: 8 bit
                                              no parity, 1 stop bit 
    
           S7      0 1 0 0 0 0 0 0  (bit 8    terminal muting disable
                                     bit 7    checksum enable
                                     bit 6    X16 clocking
                                     bit 5-1  half duplex turn around
                                              character not used
    
           S8      1 0 0 1 0 1 1 0  (bit 8    double sync character
                                     bit 7-1  sync character = '22 $16'
    
         - Set Switch S1 to NORMAL and LOCAL
    
         - Set rotary switches S10 and S11 according to the host baud rate 
    and terminal baud rate, respectively.
    

    Publication Part Number W0001-520
    Sheet 40 of 47
    
        Configuring the 5912, 5913 ColorView, or the 5902A Plotmaster
    
    Enclosed on the floppy with CCPADI 3.0 is a program called SETUP.EXE.  
    This program is used to set the communication parameters.
    
                                    SETUP
    
                 CALCOMP Color Thermal Plotter Configuration
                     Copyright (C) Calcomp 1988 Rev. x.x
    
           Use the left/right arrow keys to scroll thru the options
           Use the up/down arrow keys to scroll thru the menu
    
           When the correct information is displayed use the <enter> key
    
         Model Type ...............  Model 5912
    
         Interface Mode ...........  PCI HCBS
    
    
    
    
         F5 key exits the program and returns to DOS
         ESC key restarts the program
         HOME key moves the cursor to the top selection on current screen
         END key moves the cursor to the last selection on current screen
         When New: is displayed enter the data with the numeric keys
    
    
    The initial screen will ask for either the 5912, 5913, or the 
    Plotmaster.  Use the arrow keys to select.  The interface mode is for 
    either PCI HCBS or PCI AUTOCAD.  If CCPADI 3.0 defaults are to be 
    accepted select PCI AUTOCAD.
    

    Publication Part Number W0001-520
    Sheet 41 of 47
    
                      Model 5912 Configurable Parameters
    
         Port connected to                COM1  (use arrow key for
                                                 other ports)
         Baud Type                        19200
         Parity Enable                    Enabled
         Parity Type                      Even
         Data Bits                        7
         Stop Bits                        1
    
                                       PCI DATA
         Number of Sync characters        2
         Sync character code              22
         Checksum enable                  Enabled
         Handshake type                   Direct Control
         End of Message Character         13
         Turnaround Code                  0
         Scale factor numerator           1
         Scale factor denominator         1
         X axis Origin Offset             0
         Y axis Origin Offset             0
         Print Timeout Value              300
         Plotmaster emulation             NO
    
         Change Screen with PgUp or PgDn
         Send Data (F2), Default (F4), System (F5), Restart <ESC>
    
    
         Change the parameters to look like the above if you are using 
    CCPADI 3.0 defaults.
    
    F2 will send the parameters to the Colorview and save them in EEPROM.
    
    F5 will exit the program.
    

    Publication Part Number W0001-520
    Sheet 42 of 47
    
              Configuring the 6603 or 6613 Colormaster Plus VRC
    
    The setups on the VRC unit us accomplished from the control panel.  
    Which after initialization should look something like this:
    
         ONLINE         Reset
         Setups         Tests
    
    Take the printer OFFLINE by placing the cursor on ONLINE and pressing 
    ENTER.  The following menu is displayed:
    
         OFFLINE        Reset
         Setups         Tests
    
    Position the cursor on Setups and press ENTER.  The following is 
    displayed:
    
         SETUPS
         User          Factory
    
    Position the cursor on User and press enter.  The following is 
    displayed:
    
         USER        DataFormats
         Printer           Ports
    
    Position the cursor on DataFormats and press enter.  The following is 
    displayed:
    
         DATA FORMAT
         CCGL     VDI   Epson
    
    Position the cursor on CCGL and press enter.  The following is 
    displayed:
    
         CCGL
         Numerator  : 02430
    
    Use the cursor to select each digit and change this value to read 
    00001.  Press enter when completed.  The following will be displayed:
    
         CCGL
         Denomintr  : 70633
    

    Publication Part Number W0001-520
    Sheet 43 of 47
    
    As with the Numerator used the arrow keys to select each digit and 
    change this value to read 00001.  Press enter when completed.  The 
    following will be displayed:
    
         CCGL
         X Offset  :+00000
    
    Press enter and the following will be displayed:
    
         CCGL
         Y Offset  :+00000
    
    Press enter and the following will be displayed:
    
         CCGL
         # of Syncs    :1
    
    Use the arrow keys to change this value to 2 if using CCPADI 3.0 
    defaults.  Press enter when finished and the following will be 
    displayed:
    
         CCGL
         Sync Code      :2
    
    Use the arrow keys to change this value to 22 if using CCPADI 3.0 
    defaults.  Press enter when finished and the following will be 
    displayed:
    
         CCGL
         End Code       :3
    
    Use the arrow keys to change this value to 13 if using CCPADI 3.0 
    defaults.  Press enter when finished and the following will be 
    displayed:
    
         CCGL
         Checksum:   Disable
    
    Use the arrow keys to change this value to enable if using CCPADI 3.0 
    defaults.  Press enter when finished and the following will be 
    displayed:
    
         CCGL
         TimeOut:    0010 S
    
    Use the arrow keys to change this value to 300 if using CCPADI 3.0 
    defaults.  Press enter when finished and the following will be 
    displayed:
    
         CCGL
         5902A Pens:  Yes
    

    Publication Part Number W0001-520
    Sheet 44 of 47
    
    Use the arrow keys to change this value to NO if using CCPADI 3.0 
    defaults.  Press enter when finished and the following will be 
    displayed:
    
         CCGL
         Param Set: HCBS
    
    You have now set all the CCGL Setup parameters.  To go to the USER 
    submenu, press CLEAR.
    
         USER        DataFormats
         Printer           Ports
    
    Select 'Ports' and press enter.  The following will be displayed:
    
         SERIAL PORT
         Baud Rate: 9600
    
    Use the arrow keys to change this setting to 19200 if you are using 
    CCPADI 3.0 defaults.  Press enter when finished and the following will 
    be displayed:
    
         SERIAL PORT
         Data Bits: 8
    
    Use the arrow keys to change this setting to 7 if you are using CCPADI 
    3.0 defaults.  Press enter when finished and the following will be 
    displayed:
    
         SERIAL PORT
         Stop Bits
    
    Use the arrow keys to change this setting to 1 if you are using CCPADI 
    3.0 defaults.  Press enter when finished and the following will be 
    displayed:
    
         SERIAL PORT
         Parity:  None
    
    Use the arrow keys to change this setting to even if you are using 
    CCPADI 3.0 defaults.  Press enter when finished and the following will 
    be displayed:
    
         SERIAL PORT
         Handshk:  CCGL
    
    Press enter when finished and the following will be displayed:
    
         SERIAL PORT
         Handshk:  XON/XOFF
    

    Publication Part Number W0001-520
    Sheet 45 of 47
    
    Use the arrow keys to change this setting to DTR/RTS if you are using 
    CCPADI 3.0 defaults.  Press enter when finished and the following will 
    be displayed:
    
         USER        DataFormats
         Printer           Ports
    
    Press the Clear button until the following is displayed:
    
         ONLINE         Reset
         Setups         Tests
    
    

    
    Publication Part Number W0001-520
    Sheet 46 of 47
    
                              LIST OF MATERIALS
    
    The CalComp Supplied floppy should contain the following files:
    
         BATCHPLT.EXE                    Program
         AN_D_SRH.DT2                    Batchplt support file
         AN_E_SRH.DT2                    Batchplt support file
         AN_D_PLT.DT2                    Batchplt support file
         AN_E_PLT.DT2                    Batchplt support file
         AR_D_PLT.DT2                    Batchplt support file
         AR_E_PLT.DT2                    Batchplt support file
         IS_D_PLT.DT2                    Batchplt support file
         IS_E_PLT.DT2                    Batchplt support file
         BATCHPLT.DOC                    Batchplt documentation
         INSTALL.EXE                     Installation program
         CCP386.EXP                      Protected Mode ADI driver
         CCP386.DOC                      Protected Mode Documentation
         CCPADI.EXE                      Real Mode ADI driver
         CCPCFG.EXE                      Real Mode Driver config program
         CCPADI.DOC                      Real Mode documentation
         SETUP.EXE                       Thermal Transfer Setup program
    
    
                             SYSTEM REQUIREMENTS
    
         IBM PC or Compatible
         EGA or VGA card and monitor
         DOS 2.0 or later
         AutoCAD 10 286/386  or  11 286/386
    

    
    Publication Part Number W0001-520
    Sheet 47 of 47
    
                           DEFAULT PEN DEFINITIONS
    
     PEN      COLOR         WIDTH in inches
    
      1       RED            0.01
      2       YELLOW         0.01
      3       GREEN          0.01
      4       CYAN           0.01
      5       BLUE           0.01
      6       MAGENTA        0.01
      7       BLACK          0.01
      8       ORANGE         0.01
      9       LIGHT RED      0.01
     10       BROWN          0.01
     11       LIGHT GREEN    0.01
     12       LIGHT CYAN     0.01
     13       LIGHT BLUE     0.01
     14       LIGHT MAGENTA  0.01
     15       1/2 BLACK      0.01
    
                               PEN WIDTH TABLE
    
            PLOTTER RESOLUTION
    
    WIDTH     200 DPI        300 DPI        400 DPI
              IN   MM        IN    MM       IN   MM
       1   .005   .13    .00375   .10    .0025   .06
       2   .010   .25    .00750   .19    .0050   .13
       3   .015   .38    .01125   .29    .0075   .19
       4   .020   .51    .01500   .38    .0100   .25
       5   .025   .64    .01875   .48    .0125   .32
       6   .030   .76    .02250   .57    .0150   .38
       7   .035   .89    .02625   .67    .0175   .44
       8   .040  1.02    .03000   .76    .0200   .51
       9   .045  1.14    .03375   .86    .0225   .57
      10   .050  1.27    .03750   .95    .0250   .64
      11   .055  1.40    .04125  1.05    .0275   .70
      12   .060  1.52    .04500  1.14    .0300   .76
      13   .065  1.65    .04875  1.24    .0325   .83
      14   .070  1.78    .05250  1.33    .0350   .89
      15   .075  1.91    .05625  1.43    .0375   .95
      16   .080  2.03    .06000  1.52    .0400  1.02