NETWORK.DOC
       Page 1 of 8


                   PROTECTED MODE ADI - NETWORK PLOT SPOOLING

       The CalComp protected mode ADI driver follows AutoCAD conventions 
       and provides the same network plot spooling support as an Autodesk 
       in-line driver.  There are basically two methods which can be used 
       on Novell networks:  plot to file with I/O redirection and plot to 
       file with AUTOSPOOL.  Since most network system software has 
       similar utilities, similar methods can be used on other networks.  
       These methods, including setup information, are described in the 
       following sections.

       Before proceeding, verify the following:

           The CalComp protected mode ADI driver is installed and has 
           been tested with a CalComp plotter in a local configuration.
           A workstation is connected and logged into the network.
           Print servers and print queues are setup and operational.


       THE NOVELL CAPTURE UTILITY

       The Novell CAPTURE utility can be used to redirect the output of a 
       logical DOS LPT device, such as LPT1, to a network print queue and 
       on to the plotter.

       Setup:

       1.  Start the CAPTURE utility before starting AutoCAD.  This can 
           be done at the DOS prompt or, for regular use, it can be 
           included in a login script or batch file.

       2.  Start AutoCAD and configure for plot to file from the 
           configure plotter menu.  To make this the default, answer YES 
           when you see the following question during configuration:

           Write the plot to a file?

           Plot to file is also an option which can be setup at plot 
           time.  Since the ADI driver ignores the handshaking selection 
           when plotting to a file, no other changes need to be made from 
           the plotter configuration menu.

       3.  Configure the plot file name for LPT1 (assuming that CAPTURE 
           is redirecting the output of LPT1).  From the operating 
           parameter menu, select option 3, default plot file name.  When 
           prompted, enter the following:

           LPT1

           For occasional use, you can also enter LPT1 as the file name 
           at plot time.

       

       NETWORK.DOC
       Page 2 of 8


       4.  Make sure that the plotter is connected to the print server.  
           Check the plotter setup and, if the connection is serial, 
           ensure that the baud rate, character framing and handshaking 
           (xon/xoff or hardware) match the Novell printer configuration 
           in PCONSOLE.

       This completes the setup for plot spooling using the CAPTURE 
       utility.


       NOTES ON USING CAPTURE

       If the Autoendcap option is enabled (default), captured plots will 
       be queued when AutoCAD completes the plot job.  This is useful if 
       you want to send single plot jobs to individual print queue files 
       and plot without exiting AutoCAD.  A new capture session starts 
       automatically with each plot job.

       If the Auotendcap option is disabled, captured plots will be 
       queued when you exit AutoCAD and type ENDCAP at the DOS prompt.  
       This is useful if you want to append multiple plot jobs in a 
       single print queue file.  ENDCAP also terminates the capture of an 
       LPT device.

       The Timeout option should be disabled (default) since it can cause 
       unpredictable results.

       Typical captured plots appear as "LPT1 Catch" in the print queue 
       job description.

       The following CAPTURE options should be used to prevent any 
       extraneous data from being sent to the plotter.  Instead of 
       including these in the command line, they can be set up as 
       defaults in PRINTCON.

           NoTabs            NoBanner        NoFormFeed

       For additional information please refer to the Novell Print Server 
       Manual and the AutoCAD Installation and Performance Guide.


       THE AUTOCAD AUTOSPOOL FEATURE AND THE NOVELL NPRINT UTILITY

       The AutoCAD AUTOSPOOL feature can be used to output plots to 
       unique files in a user defined plot spooler directory.  Once the 
       plot files are in the spooler directory, it is the responsibility 
       of a spooler program, such as the Novell NPRINT utility, to move 
       the files to a network print queue and on to the plotter.  AutoCAD 
       provides a hook with which to automate spooler execution in the 
       form of an environment variable, ACADPLCMD.  Once AutoCAD finishes 
       writing the plot file, it generates a command using the string 
       defined in ACADPLCMD, substituting a unique file name for the "%s" 
       in the string, and sends it to DOS for execution.  AutoCAD then 
       returns to the drawing editor or main menu, depending on where the 
       plot job was started.

       

       NETWORK.DOC
       Page 3 of 8


       Setup:

       1.  Make a directory or identify an existing directory for plot 
           spooling.  This directory can be on a local or network drive.  
           Both AutoCAD and NPRINT will need read/write access to this 
           directory.  For this example we will use Z:\PLOTS.

       2.  Define the environment variable, ACADPLCMD, for the spooler 
           program (NPRINT) using the SET command.

           SET ACADPLCMD=NPRINT %s

           Note that the "s" is lower case and there are no spaces around 
           the equal (=) sign and no trailing space at the end of the 
           line.

           If you want the plot files deleted from the spooler directory 
           once they're in the queue, use the Delete option with NPRINT.  
           For example:

           SET ACADPLCMD=NPRINT %s D

           For regular use, you can add the appropriate SET statement to 
           the AUTOEXEC batch file.  If you do, be sure to use two 
           percent (%) signs, since DOS batch files use the percent sign 
           to indicate parameters passed to the program.  For example:

           SET ACADPLCMD=NPRINT %%s

           Set ACADPLCMD=NPRINT %%s D

       3.  Start AutoCAD and configure for plot to file from the 
           configure plotter menu.  To make this the default, answer YES 
           when you see the following question during configuration:

           Write the plot to a file?

           Plot to file is also an option which can be setup at plot 
           time.  Since the ADI driver ignores the handshaking selection 
           when plotting to a file, no other changes need to be made from 
           the plotter configuration menu.

       4.  Configure the plot file name for AUTOSPOOL.  From the 
           operating parameter menu, select option 3, default plot file 
           name.  When prompted, enter the following:

           AUTOSPOOL

           For occasional use, you can also enter AUTOSPOOL as the file 
           name at plot time.

       

       NETWORK.DOC
       Page 4 of 8


       5.  Configure the plot spooler directory.  From the operating 
           parameter menu, select option 4, plot spooler directory.  When 
           prompted, enter the path and name of the directory created in 
           step 1, including a trailing backslash.  For example:

           Z:\PLOTS\

       6.  Make sure that the plotter is connected to the print server.  
           Check the plotter setup and, if the connection is serial, 
           ensure that the baud rate, character framing and handshaking 
           (xon/xoff or hardware) match the Novell printer configuration 
           in PCONSOLE.

       This completes the setup for plot spooling using AUTOSPOOL and the 
       NPRINT utility.


       NOTES ON USING AUTOSPOOL AND NPRINT

       Spooled plot files appear in the spooler directory and print queue 
       job description with unique file names.  Spooled plot files are 
       given unique names by AutoCAD in the format VXXXXXXX.YYY, where V 
       indicates a vector plot file, XXXXXXX is based on the current 
       time, and YYY is the network node name.  For example:  
       V1234567.RAY.  The default network node name is AC$ and can be 
       changed from the operating parameter menu, option 6.

       The following NPRINT options should be used to prevent any 
       extraneous data from being sent to the plotter.  These should be 
       set up as defaults in PRINTCON.

           NoTabs            NoBanner        NoFormFeed

       If the spooler program doesn't delete the old plot files from the 
       spooler directory, you will need to do this manually to prevent 
       filling up the hard disk.

       Besides NPRINT, you can also use your favorite spooler program.  
       Just define it in ACADPLCMD.  ACADPLCMD can also be used to start 
       a batch file, which in turn can perform some setup before starting 
       the spooler.  Or, instead of using ACADPLCMD, you can have a 
       spooler program running on a remote node, queueing up plot files 
       from the spooler directory.

       For additional information please refer to the Novell Print Server 
       Manual and the AutoCAD Installation and Performance Guide.

       

       NETWORK.DOC
       Page 5 of 8


                     REAL MODE ADI - NETWORK PLOT SPOOLING

       The CalComp real mode ADI driver provides network plot spooling 
       support using plot to file with I/O redirection.  There is 
       basically one method which can be used on Novell networks.  Since 
       most network system software has similar utilities, a similar 
       method can be used on other networks.  This method, including 
       setup information, is described in the following sections.

       Before proceeding, verify the following:

           The CalComp real mode ADI driver is installed and has been 
           tested with a CalComp plotter in a local configuration.
           A workstation is connected and logged into the network.
           Print servers and print queues are setup and operational.

       Plot to file with AUTOSPOOL is not supported.


       THE NOVELL CAPTURE UTILITY

       The Novell CAPTURE utility can be used to redirect the output of a 
       logical DOS LPT device, such as LPT1, to a network print queue and 
       on to the plotter.

       Setup:

       1.  Configure the ADI driver for plot to file.  Run the 
           configuration program, CCPCFG.  From the communications menu, 
           select the File option, save the settings and exit.  There is 
           no need to reload the driver, since it always reads its 
           configuration file before plotting begins.

       2.  Start the CAPTURE utility before starting AutoCAD.  This can 
           be done at the DOS prompt or, for regular use, it can be 
           included in a login script or batch file.

       3.  Make sure that the plotter is connected to the print server.  
           Check the plotter setup and, if the connection is serial, 
           ensure that the baud rate, character framing and handshaking 
           (xon/xoff or hardware) match the Novell printer configuration 
           in PCONSOLE.

       4.  Start AutoCAD and select a drawing to plot.  Configuring the 
           plot file name for LPT1 (assuming that CAPTURE is redirecting 
           the output of LPT1) is done at plot time.  Enter LPT1 when the 
           final prompt appears:

           Enter output file name <CCPADI.PLT>  ==>

           CCPADI.PLT is the initial default plot file name.  Subsequent 
           default plot file names will be the last file name used, in 
           this case LPT1.

       This completes the setup for plot spooling using the CAPTURE 
       utility.

       

       NETWORK.DOC
       Page 6 of 8


       NOTES ON USING CAPTURE

       If the Autoendcap option is enabled (default), captured plots will 
       be queued when AutoCAD completes the plot job.  This is useful if 
       you want to send single plot jobs to individual print queue files 
       and plot without exiting AutoCAD.  A new capture session starts 
       automatically with each plot job.

       If the Auotendcap option is disabled, captured plots will be 
       queued when you exit AutoCAD and type ENDCAP at the DOS prompt.  
       This is useful if you want to append multiple plot jobs in a 
       single print queue file.  ENDCAP also terminates the capture of an 
       LPT device.

       The Timeout option should be disabled (default) since it can cause 
       unpredictable results.

       Typical captured plots appear as "LPT1 Catch" in the print queue 
       job description.

       The following CAPTURE options should be used to prevent any 
       extraneous data from being sent to the plotter.  Instead of 
       including these in the command line, they can be set up as 
       defaults in PRINTCON.

           NoTabs            NoBanner        NoFormFeed

       For additional information please refer to the Novell Print Server 
       Manual and the AutoCAD Installation and Performance Guide.

       

       NETWORK.DOC
       Page 7 of 8


                       BATCHPLOT - NETWORK PLOT SPOOLING

       Batchplot doesn't directly support network plot spooling.  
       However, Batchplot can output plots to files in a user defined 
       plot spooler directory.  Once the plot files are in the spooler 
       directory, it is the responsibility of a spooler program to move 
       the files to a network print queue and on to the plotter.

       When the ADI driver is setup for plot to file, Batchplot forces 
       the driver to write its files to the AutoCAD plot spooler 
       directory.  Since Batchplot also generates the plot file names, 
       plot to file with I/O redirection and plot to file with AUTOSPOOL 
       are not supported.  

       Before proceeding, verify the following:

           The CalComp protected mode or real mode ADI driver and 
           Batchplot are installed and have been tested with a CalComp 
           plotter in a local configuration.
           A workstation is connected and logged into the network.
           Print servers, print queues and a spooler program are setup 
           and operational.

       Setup:

       1.  Make a directory or identify an existing directory for plot 
           spooling.  This directory can be on a local or network drive.  
           Both AutoCAD and the spooler program will need read/write 
           access to this directory.  For this example we will use 
           Z:\PLOTS.

       2.  Configure the ADI driver for plot to file.

           A.  Protected mode ADI driver:

               Start AutoCAD and configure for plot to file from the
               configure plotter menu.  Answer YES when you see the
               following question during configuration:

               Write the plot to a file?

               Since the ADI driver ignores the handshaking selection
               when plotting to a file, no other changes need to be made
               from the plotter configuration menu.

           B.  Real mode ADI driver:

               Run the configuration program, CCPCFG.  From the
               communications menu, select the File option, save the
               settings and exit.  There is no need to reload the driver,
               since it always reads its configuration file before
               plotting begins.

               Start AutoCAD.

       

       NETWORK.DOC
       Page 8 of 8


       3.  Configure the plot spooler directory.  From the operating 
           parameter menu, select option 4, plot spooler directory.  When 
           prompted, enter the path and name of the directory created in 
           step 1, including a trailing backslash.  For example:

           Z:\PLOTS\

           Save the settings and exit.

       4.  Make sure that the plotter is connected to the print server.  
           Check the plotter setup and, if the connection is serial, 
           ensure that the baud rate, character framing and handshaking 
           (xon/xoff or hardware) match the network spooler printer 
           configuration.

       This completes the setup for plot spooling using Batchplot.


       NOTES ON USING BATCHPLOT

       Batchplot file naming conventions:

           Normal plots:  Drawing file name with .P00 extension.  For 
           example:

                 COLUMBIA.P00

           Normal plots (multiple copies):  Drawing file name with .PXX 
           extension, where XX is the copy number starting with 00.  For 
           example:

                 COLUMBIA.P00  (first copy)
                 COLUMBIA.P01  (second copy)

           Nested plots:  BATCHPLT with .YYY extension, where YYY is the 
           sequence number starting with 001.  For example:

                 BATCHPLT.001  (first nested plot)
                 BATCHPLT.002  (second nested plot)

       AutoCAD default plot file names such as LPT1 and AUTOSPOOL are 
       ignored.

       The AutoCAD spooler automation hook, ACADPLCMD, is not supported.

       The spooler program should be transparent to the plot data, i. e., 
       it shouldn't send any extraneous data to the plotter.

       If the spooler program doesn't delete the old plot files from the 
       spooler directory, you will need to do this manually to prevent 
       filling up the hard disk.

       For additional information please refer to your spooler program 
       documentation and the AutoCAD Installation and Performance Guide.