COPYRIGHT
           
           Copyright 1990 Adaptec, Inc. All rights reserved. No 
           part of this publication may be reproduced, stored in 
           a retrieval system, or transmitted, in any form or by 
           any  means,  electronic,  mechanical,  photocopying,   
           recording, or otherwise,  without the  prior written  
           consent of  Adaptec, Inc.  691 South  Milpitas Blvd.  
           Milpitas, CA 95035
           
           CHANGES
           
           The material in this manual  is for information only  
           and is subject to change without notice.
           
           Adaptec reserves the  right to  make changes  in the  
           product  design  without   reservation  and  without   
           notification to its users.
           
           Additional information may be obtained from:
           
                             Adaptec
                  Literature Department - MS/40
                    691 South Milpitas Blvd.
                       Milpitas, CA 95035
           
                              PREFACE                                   
                      
           FCC Compliance
           
           This equipment  generates and  uses  radio frequency  
           energy and if not installed  and used properly, that  
           is, in  strict  accordance  with  the manufacturer's  
           instructions, may  cause interference  to  radio and  
           television reception.  It has  been type  tested and  
           found to  comply  with  the  limits  for  a  Class B  
           computing device in accordance with the specifications 
           of Subpart  J of  Part 15  of  FCC Rules,  which are  
           designed to provide reasonable protection against such 
           interference in  residential  installation. However,  
           there is no guarantee that interference will not occur 
           in a particular installation. If this equipment does  
           cause interference to radio  or television equipment  
           reception, which  can be  determined by  turning the  
           equipment off and on, the user is encouraged to try to 
           correct the  interference  by  one  or  more  of the  
           following measures:
                Reorient the receiving antenna
                Relocate the computer with respect to the receiver
                Move the computer away from the receiver
                Plug the computer into a different outlet so that computer
                and receiver are on different branch circuits.
           
           If necessary, the user should consult the dealer or an 
           experienced radio/television technician for additional 
           suggestions. The user may find the following booklet  
           prepared by  the  Federal  Communications Commission  
           helpful:
           "How  to  Identify  and  Solve Radio-TV  Interference  
           Problems"
           This booklet is  available from  the U.S. Government  
           Printing Office, Washington,  D.C. 20402,  Stock No.  
           004-000-00345-4.
           
           Caution: This equipment has been certified to comply  
           with the limits for Class B computing device, pursuant 
           to Subpart J of Part 15 of FCC Rules. Only peripherals 
           (computer input/output devices, terminals, printers,  
           etc.) certified to comply with the Class B limits may 
           be  attached  to   this  computer.   Operation  with   
           non-certified peripherals  is  likely  to  result in  
           interference to  radio and  TV reception.  Also this  
           equipment must be used with shielded power cables and 
           shielded  I/O   cables.  Finally,   any   change  or   
           modifications to  the  equipment  by  the  user  not  
           expressly approved  by the  grantee  or manufacturer  
           could void  the  user's  authority  to  operate such  
           equipment.
                       
                        TABLE OF CONTENTS

1.0    Introduction                                       1-1
       1.1  Document Scope                                1-1
       1.2  General Product Information                   1-1
       1.3  Product Features and Benefits                 1-2
       1.4  Product Specifications                        1-4
       1.5  Reference Documents                           1-4
           
 2.0   HARDWARE Installation                              2-1 
       2.1  Unpacking and Inspection                      2-1
       2.2  Board Installation in an AT System            2-1
            2.2.1  General Information                    2-2
            2.2.2  Factory Default Settings               2-3
            2.2.3 "Quick Installation" - System Defaults  2-4
           
 3.0   BOARD CONFIGURATION                                3-1
       3.1 Data Jumper Block J5                           3-1
       3.2 Jumper Block J6                                3-3
       3.3 Floppy Jumper Block J7                         3-5
       3.4 DMA Jumper Block J8                            3-6
       3.5 Interrupt Jumper Block J9                      3-7
       3.6 Terminators                                    3-8
           
 4.0   SOFTWARE DRIVERS                                   4-1
       4.1  Drivers Available for the AHA-1520/1522       4-1
       4.2  ASPI MS-DOS Manager                           4-2
       4.3  Installation of the DOS Driver                4-2
            4.3.1 Copying the Files                       4-2
            4.3.2 CONFIG.SYS File                         4-3
            4.3.3 CONFIG.SYS File Options                 4-4
       4.4  Running AFDISK                                4-8
       4.5  Exiting AFDISK                                4-9
           
 5.0   TROUBLESHOOTING                                    5-1
           
Appendix A  MESSAGE DISPLAYS                              A-1
           
Appendix B SCSI INTERNAL CONNECTOR PIN ASSIGNMENTS        B-1
           
Appendix C SCSI EXTERNAL CONNECTOR PIN ASSIGNMENTS        C-1
              
           
           SECTION  ONE                              INTRODUCTION              
           
           1.1 DOCUMENT SCOPE
           
           This manual  provides  the  information  required to  
           install the AHA-1520 and the AHA-1522 Small Computer  
           System Interface (SCSI) Host Adapters in AT bus-based 
           systems. This document is for use with the production 
           version of the board and  not with earlier prototype  
           versions. The production version is identified by the 
           presence of the AIC-6260AL chip  and has right angle  
           shrouded internal connectors at the top of the board.
           
           1.2 GENERAL PRODUCT INFORMATION
           
           Adaptec's new AHA-1520 and AHA-1522 SCSI host adapters 
           break the price performance barrier with multitasking 
           AT-to-SCSI I/O performance. With dramatically faster  
           data transfer  and I/O  management than  standard AT  
           systems, the AHA-152X will enhance I/O performance of 
           AT microcomputers significantly. The  AHA-1522 is an  
           AHA-1520 with a  dual AT  floppy disk  controller on  
           board.
           
           Not only does  the AHA-152X  enhance performance, it  
           adds versatility. Up to 56  devices can be connected  
           using this SCSI  interface, which  supports up  to 8  
           simultaneous I/O tasks, while only  using 1 AT slot.  
           Compatibility is assured by full support of the ANSI  
           SCSI Common Command Set and SCSI-2. 
           
           Adaptec's AHA-152X  family  excels  in  single  user  
           environments (i.e., stand alone  or network node) by  
           utilizing the  CPU's untapped  power to  improve I/O  
           performance of the overall system.  Since the CPU in  
           single user environments is rarely fully utilized, the 
           AHA-152X performs impressively  within this  sort of  
           setting. With its multi-tasking I/O capabilities, the 
           AHA-152X is  a  cost effective  solution  in certain  
           shared system situations.
           
           In addition,  the AHA-152X  manages SCSI  devices to  
           maximize     their     throughput.      With     the      
           Disconnect/Reconnect  feature,   the   AHA-152X  can   
           delegate simultaneous I/O commands. 
           
           AHA-152X customers gain  access into  Adaptec's ASPI  
           (Advanced SCSI  Programing  Interface)  family of  
           software. This family is made up of device modules 
           that interact with tape, disk, CD-ROM, WORM, DAT,  
           and NODEM_ devices, and operating system managers  
           (i.e. DOS,  OS/2,  Unix/Xenix,  and  Novell). The  
           device modules  communicate  with  the  operating  
           system managers  through  a  common specification  
           platform known as ASPI.
           
           The  key  benefit  to  our  customers  is  that  the   
           modularity  of  ASPI   allows  one   to  add  future   
           functionality without replacing  the entire software  
           driver. Adaptec  is  expanding the  ASPI  family and  
           providing the  ASPI  specification  to  third  party  
           developers.
                       
           1.3 PRODUCT FEATURES AND BENEFITS
             
           HIGH Data Transfer Rates
           
           ù 5 MBytes/sec synchronous burst on the SCSI bus
           ù 3 MBytes/sec  data  rate on  the  AT bus  (highest  
              speed allowable in the PIO environment)
           ù 2 MBytes/sec asynchronous SCSI data rate
           
           High Price/Performance Value 
           
            ù  PIO  with   optional  second-party  DMA  offers   
               configuration     options
            ù  Using  the   host  processor,  SCSI  overhead   is  
               minimal in single-tasking environments
            ù  16- or 8-bit host bus data transfer widths
            ù  Disconnect/reconnect feature allows the host 
               to perform other I/O tasks, while disconnected 
               device is busy 
           
           Software Support 
           
            ù  ASW-1210 ASPI DOS manager is available. This 
               permits optimal operation in the most popular 
               single-tasking operating system environment.
            ù  Compatible with Advanced SCSI features 
               available on Adaptec's ASPI (Advanced SCSI 
               Programming Interface)
            ù  Modular software driver structure leads to an 
               expanding library of off-the-shelf device modules. 
            ù  Pass-through interface available to 
               third-party developers
           
           Multitasking
           
             ù AHA-152X   supports  up   to  eight   simultaneous  
               I/O tasks
           
           Compatibility
           
            ù  On-board BIOS supports boot capability, and 
               up to two hard disk drives under DOS without a 
               software driver
            ù  Software drivers for all major operating 
               systems (DOS, OS/2, Unix, Xenix, Netware) offer 
               expandability beyond two disk drives 
            ù  Tested with more than two dozen AT's from 
               major PC manufacturers and more than 35 SCSI 
               devices
            ù  Supports Common Command Set and all SCSI-2 
               required features
            ù  Flexible floppy controller option supports 
               all standard AT floppy types
            ù  Efficient design (XT 1/2 card size) fits 
               easily into both AT desktops, as well as many slots 
               in laptops
           
           Connectivity
           
            ù Supports all SCSI addresses and LUN's up to 
              56 devices or up to 7 devices with embedded SCSI
            ù User can add existing or future devices 
              without using additional slots on the motherboard
            ù Supports both synchronous and asynchronous 
              devices: disk, Tape, CDROM, WORM, DAT, and other 
              SCSI peripherals
           
           The Best Value in Host Adapters
           
           ù  Five-year limited lifetime warranty 
              demonstrates product confidence and lowers the cost 
              of ownership
           ù  Surface mount technology ensures 
              dependability while affording economical 
              manufacturing
           ù  Highly integrated design improves reliability
           ù  Less than 0.7% return rate on like products 
              reflects Adaptec's manufacturing expertise and 
              commitment to quality
           ù  Most SCSI experience from 
              silicon-to-software: Adaptec has developed numerous 
              SCSI host adapters for proprietary and   
              industry-standard hosts
           
          1.4 PRODUCT SPECIFICATIONS
           
           ù  Physical Dimensions:
           
                  Length: 5.50" Width: 4.40" Height: 0.5"
           
           ù  Power Requirements:
           
                  5.25V to 4.75V tolerance on the AT power supply.
                  1 Amp maximum.
           
           ù  Environmental Requirements:
           
                  Temperature 0-55 degrees C (operating or storage) 
                  (32-131 degrees F)
           
          1.5 REFERENCE DOCUMENTS
           
           ù  IBM Technical Reference Personal Computer AT #6280070.
           
           ù  IBM Personal System/2 and Personal Computer BIOS Interface 
              Technical Reference #68x2260
           
           ù  Adaptec AIC-6260 Functional Specification.
           
           ù  Adaptec AHA-1520/1522 Technical Reference Manual.
           
           ù  Adaptec MS-DOS Driver Functional Specification.
           
           ù  Adaptec ASPI Interface Specification
           
           SECTION TWO                         HARDWARE INSTALLATION
 
           2.1 UNPACKING AND INSPECTION
           
           The carrier is responsible for damage incurred during 
           shipment. In case of damage, have the carrier note the 
           damage on both the delivery  receipt and the freight  
           bill, then notify your freight company representative 
           so  that  the  necessary  insurance  claims  can  be   
           initiated.
           
           After opening the shipping container, use the packing 
           slip, "READ  ME  FIRST," to  verify  receipt  of the  
           individual items  listed  on  the  slip.  Retain the  
           shipping container and packing material for possible  
           later reuse.
           
           NOTE: The AHA-1520/1522, like all electronic equipment 
           is  static   sensitive.  Please   take   the  proper   
           precautions when handling the board. You should avoid 
           static build  up  if  possible.  You  should  ground  
           yourself by touching a metal  table or your computer  
           frame. Keep the board in its conductive wrapping until 
           it is configured and  ready to be  installed in your  
           system.
           
           2.2 BOARD INSTALLATION IN AN AT SYSTEM 
           
           The  following  section   details  the  installation   
           procedure for the Adaptec AHA-1520 and AHA-1522 host  
           adapters. The installation of  the board consists of  
           checking the various on-board jumpers, inserting the  
           board into a full-length AT compatible slot connector, 
           and  connecting  a  SCSI  cable  from  the  on-board   
           connector to a SCSI device. A medium-sized flat blade 
           screwdriver will be needed after  the board has been  
           prepared, to physically install it into the AT-slot.
           
                                            
           2.2.1 General Information
           
           Standard AT architecture supports up to two hard disk 
           drives under DOS. The BIOS identifies these disks as  
           hard drives  0  and 1.  If  each drive  has  one DOS  
           partition on it, drives 0  and 1 would correspond to  
           drives C: and D: respectively. If drive 0 has two DOS 
           partitions, one partition would be accessed as drive  
           C:, and the other as drive D: under most versions of  
           DOS.  The  Adaptec  ASW-1210,  ASPI  (Advanced  SCSI   
           Programing Interface) AHA-152X DOS driver, will avoid 
           this limitation, allowing the AHA-152X to access up to 
           56 physical or logical devices. The AHA-152X BIOS also 
           fully supports the extended partitioning capabilities 
           of DOS 3.3 and 4.0. Drives A: and B: are reserved for 
           Flexible Diskette drives in the DOS environment.
           The notation "standard hard disk" identifies the disks 
           that can be set up to "Installed" or "Not Installed" 
           status by the SETUP program that is supplied with your 
           AT class computer. The SETUP program allows the user  
           to select the number of standard hard disks that are 
           recognized by the system regardless of whether or not 
           they are physically installed. SCSI disks can only be 
           accessed by the host adapter's BIOS if the number of 
           standard hard disks is equal to either 0 or 1. If the 
           system  recognizes  two  standard  hard  disks,  the   
           AHA-152X DOS  driver,  ASW-1210, will  be  needed to  
           access additional  SCSI  hard disk  drives  or other  
           devices under DOS.
           
           System Booting from a SCSI hard disk drive under DOS 
           can only be  achieved if  the standard  hard disk is  
           mapped out through  your AT  computer vendor's SETUP  
           program. The  system determines  the number  of hard  
           disks at power up. The only SCSI disk drives that the 
           host adapter  BIOS  will  recognize  are (Target:LUN  
           {logical unit number}) 0:0, and 1:0. The host adapter 
           will assign the SCSI drives found at these addresses  
           to hard disk 0  and/or hard disk  1 depending on the  
           number of standard drives recognized by the system.
           
           The boot target will  be from 0 not  1, which is the  
           industry convention (C:).
           
           The SCSI  target address  is  selected by  setting a  
           jumper or a dip switch on  the drive. The drive SCSI  
           address must be set to 0 to be recognized by the host 
           adapter BIOS if only one SCSI  drive is used. If two  
           SCSI drives are to be installed under the host adapter 
           BIOS, the SCSI address  should be 0  and 1. Refer to  
           your drive manual for SCSI address selection.
           
           2.2.2 Factory Default Settings 
           
           The Adaptec AHA-152X AT-to-SCSI Host Adapter has been 
           designed to operate as shipped, in the majority of AT 
           class computers. The host  adapter's factory default  
           settings should remain in their original positions, as 
           shown in Figure 1. The  AHA-1520 is shipped with the  
           following factory default settings:
           
                SCSI Disconnection     Enabled
                SCSI Address           7 
                SCSI Parity            Enabled
                Terminators            Installed
                Terminator Power       Supplying 
                Synchronous Negotiation Enabled
                DMA Channel            0
                Interrupt Channel      11
                AT Port Address        340h
                AT BIOS Address        DCOOOH, Enabled
                Floppy Disk Controller Enabled on AHA -1522
                Data Transfer Mode     PIO
           
           2.2.3 "Quick Installation"_System Defaults 
                
           STEP 1
           
           LOCATE PIN 1 ON THE SCSI CABLE YOU ARE GOING TO USE.
           
           When attaching the SCSI Bus  to the host adapter and  
           the peripherals, make sure that pin 1 orientation is  
           maintained throughout the bus. 
           
           Internal Cables: Pin 1 is denoted on most 50 pin gray 
           ribbon cables by  a red stripe.  Multi-color 50- pin  
           ribbon cables signify pin 1  with a brown color. Pin  
           one is located at the top of the 50-pin header on the 
           host adapter.  Check  your  peripherals  manual  for  
           correct pin 1 orientation. 
           
           External  Cables:  The  external  connector  on  the   
           AHA-152X is a D shell connector that ensures correct  
           pin 1 orientation on the  host adapter. Again, check  
           your peripherals manual for correct pin 1 orientation 
           on the drive.
           STEP 2
           
           CONNECT ONE END  OF THE  CABLE TO  THE INTERNAL SCSI  
           50-PIN CONNECTOR.
           
           Line up pin 1 on the cable  to pin 1 of the Internal  
           SCSI Connector  which  is  located  on  top  of  the  
           AHA-152X. Pin 1 of the Internal SCSI Connector is the 
           pin on the Internal SCSI Connector that is closest to 
           the Floppy Disk Connector.
           
           Firmly, but in a straight forward fashion, as to avoid 
           bending the end pins of the Internal SCSI Connector,  
           put the cable end on to this connector, lining up the 
           pin 1 association.
           
           If using an external device, attach this cable to the 
           External SCSI Connector, then use  the bail clips to  
           hold it snugly in place. Cable connection is shown in 
           Figure 2. Normally both connectors would be attached  
           only if both external and internal devices are being  
           connected.
           
                            [Picture]
           
           
                FIGURE 2. SCSI CABLE ATTACHMENT
                                            
           STEP 3
           
           INSTALL AHA-152X INTO THE AT BUS ON THE MOTHER BOARD
           
           TURN OFF  POWER  TO SYSTEM  AND  EXTERNAL EQUIPMENT.  
           Adaptec recommends that you  unplug your system from  
           the A/C outlet. 
           
           Remove the cover  of your AT  personal computer that  
           exposes the AT bus slots, typically the top cover if 
           the system were sitting flat on its base on a table.  
           With  most  AT  personal  computers,  a  flat  blade   
           medium-sized screwdriver can remove the screws at the 
           rear of the system cabinet.
           
           Locate an unused AT expansion slot in your AT system. 
           Be careful: some AT systems have both AT and XT style 
           slots on their  motherboards. AT  type slots  can be  
           recognized by that fact that they have 2 physical edge 
           connectors, one 62 pin and the other 36 pin, in line  
           with one another.
           
           Remove the corresponding system expansion slot cover  
           by turning the  screw that  secures it  from the top  
           counterclockwise. 
           
           Align the AT I/O Bus Connector  on the bottom of the  
           AHA-152X to  the open  AT slot  with the  slot cover  
           removed. Ensure the external connector passes cleanly 
           through the  cutout in  the rear  wall, as  shown in  
           Figure 4. Firmly plug the AHA-152X into this AT slot. 
           Use the screw from  the corresponding expansion slot  
           cover to secure  the AHA-152X's  bracket to  your AT  
           system frame. Be sure that the internal cable is not 
           interfering with  another circuit  card in  a nearby  
           slot.
           
           
           STEP 4
           
           ATTACH FREE END OF CABLE TO SCSI DEVICE
           
           If tangled, untangle the  cable so that  it will lie  
           freely within  the  AT  system  when  the  cover  is  
           replaced.
           
           Install the disk or other SCSI device as specified in 
           the manufacturer's directions.  Make sure  the pin 1  
           orientation is maintained.
           
           Replace the system cover to prevent personal injury.
           
           2.2.4 Powering Up the System
           
           First, plug the  system into your  A/C outlet. Next,  
           turn the power  switch to  the on  position. Now the  
           initialization routine performs all of the necessary  
           initialization  functions   and  will   display  the   
           following  message   if   the   system  successfully   
           recognizes the AHA-152X BIOS:
           
                ADAPTEC AHA-1520 BIOS
                VERSION 1.1
                COPYRIGHT 1990 ADAPTEC, INC.
                ALL RIGHTS RESERVED
           
           In addition, the number of  and type of SCSI devices  
           are displayed along with the  ID numbers of any SCSI  
           disk that are  successfully recognized  by the BIOS.  
           Devices will appear in on  the screen in the formats  
           described in Appendix A.
           
           If the system reports an initial number of hard drives 
           greater than 2, the following message is displayed:
           
                SYSTEM CONFIGURATION ERROR. 
           
           The AHA-152X BIOS allows the use of  0, 1, or 2 hard 
           disks on  the SCSI  bus under  DOS without  a device  
           driver.
           
           If 2 hard disks are attached to an internal hard disk 
           controller, and are already recognized by the system, 
           the BIOS passes control back to the standard hard disk 
           controller. A device driver will be needed to access  
           SCSI devices.
           
           If 1 hard disk is attached  to an internal hard disk  
           controller, and is already recognized by the system,  
           the BIOS attempts to assign the SCSI device (Target : 
           LUN) 0 : 0 as the second drive. (drive D:) If this is 
           unsuccessful, an initialization error is reported to  
           the system. ("SCSI DEVICE 0:0 NOT FOUND")
           
           If there are  0 hard  disks attached  to an internal  
           controller, the BIOS attempts to assign the first SCSI 
           device (Target : LUN) 0:0 as hard disk 0.(drive C:) If 
           this is  unsuccessful  an  initialization  error  is  
           reported to  the  system.  If  successful,  the BIOS  
           attempts to assign  another SCSI device  as the hard  
           disk 1. (drive D:) Device 0 : 1 is tried first, and if 
           that fails,  device  1 :  0  is tried.  There  is no  
           initialization error reported if a second drive is not 
           available.
           
           IF YOU  CONTINUE TO  HAVE  DIFFICULTIES, OR  WISH TO  
           CHANGE TECHNICAL ATTRIBUTES, CHECK BOARD CONFIGURATION 
           AGAINST THE DESCRIPTION IN THE NEXT SECTION.
  
           SECTION THREE                    BOARD CONFIGURATION

           This section is for users  to customize the AHA-152X  
           with other than the default factory settings. This is 
           done by means of jumpers located on the component side 
           of the board. Many of these selections are duplicated 
           in the  selections  available in  the  ASPI software  
           managers for the board (see Chapter 4 below). In the 
           case of  a setting  being made  in the  ASPI manager  
           conflicting with the selection made by jumper on the  
           board, the manager will override the jumper setting.  
           See Figure 1 for the location of the jumper blocks on 
           the board.
           
           Jumper blocks J5, J6, J8 and J9 are selectable by the 
           user on both the AHA-1520 and AHA-1522. Jumper block  
           J7 is available only on the AHA-1522.
           
           XX = Factory setting (jumper installed on pin pair)(factory 
                default)
           OO = Pin pair  with NO  jumper installed  from the factory
           
           To locate Jumpers, refer to the diagram of the AHA-152X shown in 
           Figure 1.
           
           3.1 DATA JUMPER BLOCK J5
            
           The jumper positions and descriptions are listed below
                                                    
                Pin Pair 1 oo - Data Transfer in DMA      
                         2 xx - BOOT         
                         3 oo - MESSAGE   
                         4 oo - MESSAGE   
                         5 xx - SYNCHRONOUS 
                         6 xx - DISCONNECT  
                         7 oo - RESERVED   
                         8 oo - RESERVED   
                                
           Pin Pair         Description
           
           Pin pair 1       Enables data transfer on the host bus to be         
                            performed using second party DMA.
           
                    
           Pin pair 2       Boot - When jumper is installed, the 
                            factory default, the BIOS will 
                            Intercept INT19 and perform the Boot 
                            operation.
           
           Pin pairs 3,4,   MSG0, MSG1 - These bits select certain 
                            messages to be displayed. This feature 
                            is offered as a convenience to the 
                            user. There are 5 classes of messages 
                            which are reported, depending the 
                            combination of these jumpers. Message 
                            classes available are:
            
                            
                          0 - Adaptec Header
                          1 - Jumper configuration information
                          2 - SCSI Device information
                          3 - Boot Progress report
                          4 - Error messages
                         
                          These messages are enabled in sets, 
                          depending on the configuration of the 
                          pin pair 3 and 4 jumpers.
           
                          Pair   3    4    Messages Enabled
                                 oo   oo   #0, #4 (default)
                                 oo   xx   #0, #3, #4 
                                 xx   oo   #0, #1, #2, #3, #4 
                                 xx   xx   #4 
           
                          Refer to Appendix A for details of the 
                          messages.
           
           Pin Pair 5     Synchronous negotiation - When the 
                          jumper is installed, the factory 
                          default, the AHA-152X will initiate 
                          synchronous negotiation. If the jumper 
                          is not installed, the board will still 
                          respond to negotiation, but only if the 
                          target starts the process.
          
           Pin Pair 6     Disconnect - When jumper is installed, 
                          the factory default, the AHA-152X will 
                          allow disconnection by the target 
                          (peripheral device). If disconnection 
                          occurs, the AHA-152X BIOS will issue 
                          INT15 (busy, wait for disk device) to 
                          allow the host CPU using other software 
                          to multi-task. When the jumper is 
                          removed, the AHA-152x will not allow 
                          disconnection, and also will not issue 
                          any INT15 calls.
            
           Pin Pair 7  
                           
                          Reserved. Factory default is removed
            
           Pin Pair 8  
                           
                          Reserved. Factory default is removed
           
           3.2 JUMPER BLOCK J6
            
           The jumper positions and descriptions are listed below
            
                            Pin Pair      
                            1 x x -       SCSI ID   
                            2 x x -       SCSI ID  
                            3 x x -       SCSI ID 
                            4 o o -       INT CHANNEL SELECT 0 
                            5 x x -       INT CHANNEL SELECT 1
                            6 o o -       DMA CHANNEL SELECT 0 
                            7 o o -       DMA CHANNEL SELECT 1 
                            8 o o -       SCSI PARITY DISABLE
            
           Pin Pair         Description
            
           Pin Pairs 1,2,3  SCSI ID - These bits indicate SCSI ID 
                            that the board should be set up for.
           
                         Pin Pairs     1     2    3   SCSI ID
                                       o o  o o  o o     0
                                       x x  o o  o o     1
                                       o o  x x  o o     2
                                       x x  x x  o o     3
                                       o o  o o  x x     4
                                       x x  o o  x x     5
                                       o o  x x  x x     6
                                       x x  x x  x x     7 (Default)
           
           Pin Pairs 4,5  Interrupt Channel - These bits indicate 
                          which interrupt channel has been 
                          selected on the board. The values and 
                          channel they represent are listed 
                          below.
            
                              Pin Pairs
                               4    5   Interrupt Channel Number
                              o o  o o           9
                              x x  o o           10
                              o o  x x           11 (Default)
                              x x  x x           12
           
           Pin Pairs 6,7  DMA Channel - These bits indicate which 
                          DMA channel has been selected on this 
                          board. Channel 0 is a 8 bit channel. 
                          Channels 5, 6, and 7 are higher 
                          performance 16 bit channels. The values 
                          are listed below. (Currently, only 
                          channel 0, 8-bit transfers are 
                          supported.)
            
                              Pin Pairs
                               6    7   DMA Channel Number
                              o o  o o        0 (Default)
                              x x  o o        5
                              o o  x x        6
                              x x  x x        7
           
           Pin Pair 8     SCSI Parity disable - When jumper is 
                          installed, parity checking is disabled 
                          on the SCSI Bus. When the jumper is 
                          removed, factory default, parity 
                          checking, is enabled on the SCSI Bus. 
           
           3.3 FLOPPY JUMPER BLOCK J7
            
           This jumper block is available only on the AHA-1522.  
           The jumper  positions  and  descriptions  are listed  
           below. 
           
                 Pin Pair   1   x x - FLOPPY ENABLE
                            2   x x - DMA REQ 2
                            3   o o - DMA REQ 3 
                            4   x x - DMA ACK 2
                            5   o o - DMA ACK 3
                            6   x x - IRQ 6 
                            7   o o - IRQ 10 
                            8   o o - DUAL SPEED
            
           Pin Pair   Description
           
           Pin Pair 1  FLOPPY ENABLE - When this jumper is 
                       installed, the factory default, the floppy 
                       disk drive is enabled to respond to I/O 
                       writes and reads. When the jumper is 
                       removed, this floppy drive is unable to 
                       respond to I/O writes and reads.
            
           Pin Pair 2  When this jumper is installed, the 
                       factory default, the AHA-1522 will use 
                       channel 2 for the floppy DMA request 
                       signal. If channel 2 is used for DMA 
                       request signal, channel 2 must also be 
                       used for the DMA Acknowledge signal.
           
           Pin Pair 3  When this jumper is installed, the 
                       AHA-1522 will use channel 3 for the floppy 
                       DMA request signal. If channel 3 is used 
                       for DMA request signal, channel 3 must 
                       also be used for the DMA Acknowledge 
                       signal.
           
           Pin Pair 4  When this jumper is installed, the 
                       factory default, the AHA-1522 will use 
                       channel 2 for the floppy DMA acknowledge 
                       (ACK) signal. If channel 2 is used for DMA 
                       acknowledge signal, channel 2 must also be 
                       used for the DMA request signal.
           
           Pin Pair 5  When this jumper is installed, the 
                       AHA-1522 will use channel 3 for the floppy 
                       DMA Acknowledge signal. If channel 3 is 
                       used for DMA acknowledge signal, channel 3 
                       must also be used for the DMA Request 
                       signal.
           
           Pin Pair 6  When this jumper is installed, the 
                       factory default, the AHA-1522 will use 
                       channel 6 as the floppy interrupt channel.
            
           Pin Pair 7  When this jumper is installed, the 
                       AHA-1522 will use channel 10 as the floppy 
                       interrupt channel.
           
           Pin Pair 8  DUAL SPEED - This jumper should be 
                       installed when a floppy drive with a dual 
                       speed spindle is used. This is not 
                       typical; hence, the factory default is 
                       that the jumper is not installed.
            
           3.4 DMA JUMPER BLOCK J8
            
                 Pin Pair   1   o o - DMA REQ 7
                            2   o o - DMA REQ 6
                            3   o o - DMA REQ 5 
                            4   x x - DMA REQ 0 (Default)
                            5   o o - DMA ACK 7
                            6   o o - DMA ACK 6
                            7   o o - DMA ACK 5 
                            8   x x - DMA ACK 0 (Default)
           
           Pin Pair n, n+4  This jumper block is used with 2nd party DMA
           (n=1-4)          to select the DMA channel to be used. 
                            One DMA REQ signal and one matching 
                            DMA ACK signal must be selected for 
                            proper operation. In addition, the 
                            same DMA channel information must be 
                            selected in jumper block J6 pin pairs 
                            6 and 7. The factory default is 
                            jumper installed only on pin pairs 4, 
                            and 8, of the J8.
           
           3.5 INTERRUPT JUMPER BLOCK J9
            
                 Pin Pair  1   o o - IRQ 12
                           2   x x - IRQ 11
                           3   o o - IRQ 10
                           4   o o - IRQ 9
                           5   o o - PRIMARY
                           6   x x - JA16
                           7   x x - JA14
                           8   x x - BIOSEN
            
           Pin Pairs 1-4  IRQ 9,10,11,12 -, Interrupt channel 
                          selection. One and only one of these 
                          pairs must be selected for proper 
                          operation of the software. The factory     
                          default is pin pair 2 installed. In 
                          addition, the corresponding interrupt 
                          channel in jumper block J6 (pin pairs 4 
                          and 5) must be chosen.
            
           Pin Pair 5    PRIMARY - When this jumper is installed, 
                         the   alternative I/O address range, 
                         140h, is chosen. The factory default is 
                         not installed, address 340h.
           
                         Note that in order to run with the 
                         alternate address while the BIOS is 
                         enabled, a special BIOS must be 
                         installed to accommodate this.
           
           Pin Pairs 6,7 JA16, JA14 - These jumpers select the 
                         BIOS     address location. The address 
                         is given in the table below.
            
                          Pin Pair   6    7   Address
                                    o o  o o  C8000
                                    o o  x x  CC000
                                    x x  o o  D8000
                                    x x  x x  DC000
                                              (Default, both installed)
            
           Pin Pair 8     BIOSEN - When this jumper is 
                          installed, the factory default, the BIOS 
                          responds to (is active) the address 
                          identified by pin pairs 6, and 7. If not 
                          installed, the BIOS will not be engaged.
           
           3.6 TERMINATORS
           
           The SCSI bus  must also  be terminated  correctly to  
           ensure proper operation. The first and last physical  
           SCSI  devices   on   the   SCSI   cable   must  have   
           terminators installed. All  other SCSI  devices must  
           have terminators removed. The AHA-152X host adapter is 
           usually the  first device  on the  SCSI Bus  and has  
           terminators installed at the factory.
           
           SECTION FOUR                   SOFTWARE DRIVERS

           The AHA-1520/1522 product has  software available to  
           facilitate use and performance of the board in the DOS 
           environment. This ASW-1210 ASPI module is supplied on 
           a Floppy Disk or made available as part of the system 
           utilities software.
           
           The ASW-1210 is a component of Adaptec's Advanced SCSI 
           Programming  Interface   (ASPI)  This   software  is   
           compatible with the MS-DOS Manager for host adapters  
           AHA-154X  and  AHA-1640  and   the  SCSI  hard  disk   
           partitioning program AFDISK.
           
           Drivers are necessary to connect  more than two hard  
           disk drives,  or  other  types  of  SCSI  peripheral  
           devices. It  is  recommended  for  all  customers to  
           install this software driver because it will help the 
           AHA-152X to enhance system performance. The ASW-1210  
           offers these upgrades of the board BIOS operation:
           
                from single tasks     to multitasking, threading
                BIOS code execution   to RAM code execution
           
           4.1 DRIVERS AVAILABLE FOR THE AHA-1520/1522
           
           The ASW-1210 DOS  driver is available  for using the  
           AHA-152X in the DOS operating system environment. This 
           driver is not necessary if only two SCSI disks are to 
           be  handled  in  the  system.  For  tape  and  other   
           peripherals, as well as more than two disks, a driver 
           is required. The ASW-1210 driver is also recommended  
           as a means of improving system throughput. 
           
           If you wish to operate outside of the DOS environment, 
           these driver modules are currently in development for 
           the AHA-152X, and will be available:
           
           ASW-1220 ASPI Manager for the OS/2 environment
           ASW-1240 ASPI Manager for the Novell NetWare 386 environment
           ASW-1250 ASPI Manager for the UNIX environment
           
           These products  come  with  their  own  installation  
           directions. Please refer to them in order to install  
           this software correctly. 
           
           4.2 ASPI MS-DOS MANAGER - ASW-1210
           
           The MS-DOS  operating  system uses  the  ASPI MS-DOS  
           Manager, the ASW-1210, to  communicate with the SCSI  
           host adapter  and  allow access  to  additional SCSI  
           devices connected to the host adapter. The ASPI MS-DOS 
           Manager is typically installed when:
           
             ù More than two hard disk drives are installed.
           
             ù A tape driver is installed, as is the case when 
               running SY-TOS.
           
             ù Interfacing to SCSI devices such as CD-ROMs, 
               Nodems WORM drives, or scanners.
           
           AFDISK is  included with  ASW-1210 and  performs the  
           functions of the MS-DOS FDISK and FORMAT utilities for 
           SCSI drives that can only be accessed through the ASPI 
           Manager. If your  system has more  than two physical  
           fixed-disk drives, you must install and run the AFDISK 
           program in order to:
           
               ù Partition SCSI hard disk drives into logical 
                 disks. Multiple partitions can be created on one 
                 physical SCSI hard disk.
           
               ù Format SCSI hard disk logical drives or 
                 partitions.
           
               ù Delete existing partitions
           
           4.3 INSTALLATION OF THE DOS DRIVER
           
           If you plan to  have the new  SCSI device become the  
           medium that will  store the  system's root directory  
           (Drive that you wish to boot off of), you will need to 
           complete the directions in  the section, Powering Up  
           Your System, given in Chapter 3 above.
           
           4.3.1 Copying the Files
           
           The first installation step is to copy the files from 
           the ASW-1210 Program diskette to the root directory of 
           drive C using the MS-DOS COPY command.
           
           Note: You might want to  create a separate directory  
           for the AFDISK files.
           
           The following  files  are included  on  the ASW-1210  
           program diskette:
           
           FILE             FUNCTION
           
           ASPI2DOS.SYS     ASPI Manager driver
           ASPIDISK.SYS     ASPI MS-DOS disk driver.
           AFDISK.EXE       SCSI disk partition and format utility.
           PROGHLP.HLP      AFDISK HELP file.
           SYS$MSG.DAT      AFDISK system disk file.
           SYS$ERR.DAT      AFDISK error message file.
           SYS$HELP.DAT     AFDISK help message file.
           $RUN.OVL         AFDISK overlay file.
           IBM$RUN.OVL      AFDISK overlay file for running Novell.
           IBM$NORM.B&W     AFDISK overlay file for monochrome    
                            monitor and CGA video card.
           
           Take a moment before proceeding to verify that these  
           files are present.
           
           4.3.2 CONFIG.SYS File
           
           In  order for  the ASPI  MS-DOS Manager  files to  be  
           loaded whenever the system is booted, the CONFIG.SYS  
           file must contain the following DEVICE= commands:
           
           DEVICE = ASPI2DOS.SYS
           DEVICE = ASPIDISK.SYS
           
           Go to your root directory of  the drive that will be  
           used to boot  your system;  typically the  C: drive.  
           Using any ASCII file editor, add the individual device 
           driver commands to  an existing  CONFIG.SYS file, or  
           follow the  instructions  in  the  MS-DOS Operations  
           Reference Manual to create a new CONFIG.SYS file.
           
           WARNING: Failure to load all  the device drivers, or  
           failure to load  the device  drivers in  the correct  
           order, causes the program to not be installed.
           
           Step C. Create the following lines in your CONFIG.SYS file:
                Buffers=20
                Files=20
                Device=ASPI2DOS.SYS
           
           These lines  comprise the  bare minimum  required to  
           install the software driver for the AHA-1520/22. 
           
           4.3.3 CONFIG.SYS File Options
           
           A more  comprehensive  configuration  calls  for the  
           definition of a  number of  options, using  the more  
           extended format of:
           
           DEVICE = ASPI2DOS.SYS [switches shown below]
           
           DEVICE = ASPIDISK.SYS [/D]
           
           Command Line Options can be entered in any order and 
           any number. The letters can be either upper or lower 
           case. Note that  the following pairs  of options are  
           mutually exclusive: (/TP, /TD), (/C,/C-), (/Y, /Y-),  
           (/U, /U-). The Command Line Options will override any 
           corresponding jumper settings or default values.
           
           Note: Unless  a special  configuration  is required,  
           command line  options DO  NOT need  to be  used. The  
           standard jumper  configuration  takes  care  of  all  
           command installations.
           
           Caution: These Command Line Options are recognized by 
           the Driver  only,  and  not by  the  BIOS.  The BIOS  
           recognizes jumpers only. The /H option should not be  
           specified  for  systems   with  the   BIOS  enabled.   
           Otherwise, the BIOS  and Driver  might run  with two  
           different SCSI addresses.

           Options:
           
           /C       Specifying this  option will prevent  SCSI   
                    targets from  disconnecting  during command  
                    execution. When this option is specified, the 
                    /C- option must not be specified.
           
           /C-      Specifying this option   will   allow  SCSI   
                    targets  to   disconnect   during   command   
                    execution. When this option is specified, the 
                    /C option must not be specified.
           
           /TD      This option allows the data transfer  mode to  
                    be specified as DMA. If DMA is selected, make 
                    sure the board is configured for DMA Channel 
                    0. Only 8-bit DMA is supported.
           
           /TP      This option allows the data transfer mode to  
                    be specified  as PIO.  When this  option is  
                    specified,  the  /TD  option  must  not  be   
                    specified.
           
           /Y       Specifying this option disables the checking  
                    of SCSI bus parity by the host adapter. When 
                    this option is specified, the /Y- option must 
                    not be specified.
           
           /Y-      Specifying this option enables the checking  
                    of SCSI bus parity by the host adapter. When 
                    this option is specified, the /Y option must 
                    not be specified.
           
           /U       Specifying this option  enables the  host   
                    adapter to  initiate  negotiation  with the  
                    target for synchronous  data transfer. When  
                    this option is specified, the /U- option must 
                    not be specified.
           
           /U-      When this option is specified, the  host   
                    adapter will not initiate asynchronous data  
                    transfer, unless  other  requested  by  the  
                    target. The host adapter will negotiate for  
                    synchronous  transfer  if   negotiation  is   
                    initiated by the target.
           
           /Ax      This  option  allows specification  of  the host  
                    DMA channel. The single digit decimal channel 
                    number is specified at the location indicated 
                    by "x". Only number 0 is valid. Other values 
                    may cause unpredictable results.
           
           /Hx      This  option  allows specification  of  the host  
                    adapter SCSI ID.  The single  digit decimal  
                    address  is   specified  at   the  location   
                    indicated by "x". Only  numbers 0 through 7  
                    are valid. Any other values will be rejected; 
                    an error message will be displayed, and the  
                    host adapter  will  default  to  the jumper  
                    setting.
           
           /Qx      This  option  allows specification  of  the host  
                    interrupt request  channel.  The  single or  
                    double digit decimal number at the location  
                    indicated  by  "x"  specifies  the  channel   
                    number. Only numbers  9, 10, 11,  or 12 are  
                    valid. Any other values will be rejected; an 
                    error message will be displayed, and the host 
                    adapter will default to the jumper setting.
                    The host adapter must be jumpered accordingly.
           
           /D       Specifying  this  option  will  enable  messages   
                    to be displayed during initialization.
           
           /L       Specifying  this option  will  cause all  LUNs to  
                    be addressed when determining which logical  
                    units are present  on the SCSI  bus. If not  
                    specified, only LUN=0 will be addressed for  
                    each SCSI target.
           
           /Pxxx    This  option  allows  the  AHA-1520  base port  
                    address to be changed from its default value. 
                    For example, /P140 will change the base port 
                    address from  340h to  140h. Only  two port  
                    addresses are valid: 340h (default) and 140h 
                    (alternate).  Any  other   values  will  be   
                    rejected; an error message will be displayed, 
                    and the default port  address will be used.  
                    The three  hex  digits are  entered  in the  
                    position indicated by "xxx". The host adapter
                    must be jumpered accordingly.
           
           /Nx      This  option allows  the AT  bus  on time  to be  
                    changed  from  its  default   value  of  15   
                    microseconds.  A  single  or  double  digit   
                    decimal number, representing microseconds, is 
                    entered in the position indicated by "x". The 
                    maximum valid  value  is  15  microseconds.  
                    Values greater  than  the  maximum  will be  
                    rejected; an error message will be displayed, 
                    and the default time will be used.
           
           /Fx      This option  allows the  AT bus  off time  to be  
                    changed  from  its   default  value   of  1   
                    microsecond. A single or double digit decimal 
                    number, representing microseconds, is entered 
                    in the position indicated by "x". The maximum 
                    valid  value  is  15  microseconds.  Values   
                    greater than the maximum will be rejected; an 
                    error message  wil  be  displayed,  and the  
                    default time will be used.
           
           /I       Specifying  this  option  disables  the  loading   
                    of  the  INT  13  rerouter.  WARNING:  THIS   
                    OPTION  SHOULD  NOT   BE  USED   IN  NORMAL   
                    OPERATION. IF USED AND THE BIOS IS ENABLED,  
                    SCSI DISCONNECTION MUST BE DISABLED FOR BIOS 
                    COMMANDS.
           
           /Z       This option  can be  used to  set all  options to  
                    their default values. /Z provides a shortcut 
                    to  specifying  each  option  individually.   
                    Entering /Z on the command line is equivalent 
                    to  entering   /C-/TP/Y/U/A0/H7/P340.   The   
                    default values specified by /Z can be changed 
                    by including options  on the  command line.  
                    This option duplicates  the jumper defaults  
                    and has limited value to a AHA-1520 user.
          
           An example of these options  added to the CONFIG.SYS  
           file might be:
                           device=ASPI2DOS.SYS /D 
                 
           After the  CONFIG.SYS  file is  created,  reboot the  
           system to  initialize the  drivers.  An installation  
           message appears during system  booting. The messages  
           may vary depending on the system configuration and the 
           command line options specified.  If the Installation  
           Successful message  does  not appear,  use  the TYPE  
           command to review the contents of the CONFIG.SYS file 
           as follows:
           
                         TYPE CONFIG.SYS
           
           Save this file in  your root directory  of the drive  
           from which you intend to boot.
           
           Insert the Floppy disk marked, Adaptec ASW-1210, into 
           your floppy disk drive. With the C:> prompt. enter:
           
                      Copy A:*.* C:
           
           When this is complete, you have installed the software 
           driver for the AHA-152X.
           
           4.4 RUNNING AFDISK
           
           MS-DOS provides access to physical hard disk drives C 
           and D.  You must  use  the MS-DOS  FDISK  and Format  
           programs for drives C and D.  DO NOT use AFDISK with  
           drive C and D.
           
           AFDISK partitions  the  drive  into  logical  disks;  
           multiple partitions can  be created  on one physical  
           disk. Partition size limitations vary depending on the 
           version of  MS-DOS  being used.  MS-DOS  version 3.3  
           allows 32MB  partitions,  while  MS-DOS  version 4.0  
           and v5.0 allow 1.0GB partitions.
           
           To use a hard disk partitioned by AFDISK as drive C or 
           D, you must use AFDISK to delete the partitions, and 
           then use MS-DOS FDISK to create new partitions.
           Starting AFDISK program  must be  run from  the root  
           directory of drive C  or the AFDISK  directory if an  
           AFDISK directory was created. When ready, type:
           
           AFDISK (at the DOS prompt)
           
           and press ENTER:
           
           The  AFDISK  utility  is  menu  driven.  Follow  the   
           directions on the screen to partition and format the  
           selected  SCSI  devices.  The  AFDISK  utility  also   
           includes   an   on-line    HELP   file    which   is    
           accessed by pressing the F1 key.
           
           4.5 EXITING AFDISK
           
           The AFDISK may be exited at any time without executing 
           by pressing the Esc key.                        
           
           When the SCSI device(s) are successfully partitioned  
           and formatted,  reboot  the system.  This  saves any  
           changes made and  allows use of  the newly installed  
           disk(s) or partition(s).
           
           SECTION FIVE                       TROUBLESHOOTING

           Problem 1: The system will not boot from the floppy 
                      diskette drive after initial hardware 
                      installation.
           
           1)  The  LED   on  the   AHA-152X  should   come  on   
                briefly at system power up. If  the host adapter 
                has detected an  internal failure and  a message 
                will be posted to the screen. The board should be 
                returned for repair or replacement to  the place 
                of purchase. 
           
           2)   If  the  AHA-152X  LED  and  the  SCSI  drive LED  
                are always on, the SCSI cable's pin 1 orientation 
                has probably  been  reversed  between  the  host  
                adapter and the drive. See section 2.2.3.
           
           3)   The  AHA-152X  BIOS  message  is  not  displayed   
                on the screen.  The AHA-152X  BIOS is  not being 
                recognized by the system.
                a)  Check  for  BIOS  address  conflicts between  the  
                    AHA-152X and other option boards.
                b)  Try  a   different  BIOS  address.  See   section  
                    2.2.6 Jumper J9.
                c)  Change   the  BIOS   wait   state  jumper.   See   
                    section 2.2.6 Jumper J9.
           
            4)  If  the  HOST  ADAPTER  NOT  FOUND  AT  PORT 340H  
                message is displayed  check the AT  port address 
                jumper setting. See section 2.2.6 jumper J9.
           
            5)  Floppy not cabled correctly.
           
           Problem 2: System will  not boot from  the SCSI hard  
                      disk drive:
           
           Solution of this problem depends on whether a software 
           driver for the  board is  being used  or not.  If no  
           driver is used,  refer to 2A.  If a  driver is being  
           used, refer to 2B.
            
           Problem 2A: The  "ADAPTEC" logo  does not  appear on  
                       the screen during booting
           
           This indicates that the BIOS is not running.
           
           1)   Make   sure  that   the  AHA-152X   is  properly   
                inserted in the AT slot.
           
           2)   Make  sure  that  a  conflict  in  addressing  is  
                not  present.  Check  the  jumpers   for  proper  
                installation.
           
           3)   Make  sure  that  the   hard  disks  are  mapped   
                out by using your AT Setup program.
           
           4)   Make   sure   that   the   INT   19   jumper  is   
                installed (see Section 3).
           
           5)   Make  sure  that  the  AT  setup  indicates  "no   
                drives installed".
           
           6)   Make  sure  that  if  using  the  DOS  operating   
                system, the intended boot disk has an active DOS 
                partition and a DOS format.
           
           7)   Make  sure   that  the   address  of   the  SCSI   
                drive that you want to boot from  is set to SCSI 
                ID 0:0. Check your drive manual  for information 
                setting the SCSI ID for that device. 
           
           8)   Make  sure  that  SCSI  parity  is  consistently   
                enabled or disabled on  all devices on  the SCSI 
                bus. See section 2.2.6 for details.
           
           9)   Make   sure  that   the  SCSI   terminators  are   
                correctly installed, Section 2.2.7.
           
           Problem 2B: The ASPI manger "ASPI2DOS" logo does not 
                       appear"
           
           1)   Make sure that the file, "ASPI2DOS.SYS" is in the 
                root directory of the boot drive.
           
           2)   Make sure that In the file, "CONFIG.SYS" there is 
                a line:
                
                 device=ASPI2DOS.SYS
            
           Problem 3: General difficulties using a SCSI drive as 
                       drive D: with a standard hard disk as 
                       drive C:
           
           1)   Make  sure  that  hard  disk  1  (D:)  is  mapped  
                out with your AT Setup program.
           
           2)   Make  sure  that  the SCSI  drive  that  you want  
                to use as drive D: is set to  SCSI ID 0:0. Check 
                your drive manual for information on setting the 
                SCSI ID for that device. 
           
           3)   Make  sure  that  SCSI  parity  is  consistently   
                enabled or disabled on  all devices on  the SCSI 
                bus. See sections 2.2.6 for details.
           
           4)   Make  sure   that  the  SCSI   bus  is  properly   
                terminated. 
           
           5)   Make  sure  that  if  using  the  DOS  operating   
                system, the disk has  a DOS partition and  a DOS 
                format. 
           
           Problem 4: General problems using a SCSI drive as 
                       drive D: with another SCSI drive as drive 
                       C:
           
           1)   Make  sure  that  both  standard  hard  disks are  
                mapped out with your AT Setup program.
           
           2)   Make  sure  that  the SCSI  drive  that  you want  
                to use as drive D: is set to  SCSI ID 1:0. Check 
                your drive manual for information on setting the 
                SCSI ID for that device. 
           
           3)   Make  sure  that  SCSI  parity  is  consistently   
                enabled or disabled on  all devices on  the SCSI 
                bus.
           
           4)   Make  sure   that  the  SCSI   bus  is  properly   
                terminated. 
           
           5)   Make  sure  that  if  using  the  DOS  operating   
                system, the disk has  a DOS partition and  a DOS 
                format. 
           
           Problem  5:  System  works   erratically.  Hangs  or   
                        the host adapter  can't always  find the  
                        drives.
           
           1)  Check SCSI parity for consistency.
           
           2)  Check Termination.
           
           3)  Check cable length and integrity.
           
           4)  If  host  adapter  and  drive  light  remain  on   
               during a hang condition, make sure that the SCSI 
               drive conforms to  the SCSI  Common Command  Set 
               revision or SCSI II.
           
           5)  If  only   the  host  adapter   LED  remains  on   
               during a hang,  it is  probably a  host adapter, 
               system interface problem. The system may  not be 
               capable of Second Party DMA transfers. Check with 
               the System manufacturer  for information  or use 
               default PIO mode. 
           
           MANAGER ERROR MESSAGES
           
           The following  is  a  list  of  error  messages  and  
           conditions under which they may occur. For details of 
           meessages that may be displayed, refer to Appendix A  
           and J5, pin pair 3 and 4.
           
           ASPI2DOS.SYS: Error Message
           
           Failed to initialize HA
           Check host  adapter, reinstall  if  necessary, check  
           jumpers and cables. Confirm that the motherboard BIOS 
           CMOS contents are set correctly with a SETUP program.
           
           ASPI2DOS.SYS Installation Failed
           Check  contents  of  CONFIG.SYS   file.  Remove  all   
           unnecessary device  drivers,  until  driver installs  
           successfully, then reload other drivers one at a time 
           to find the offending one.
           
           Illegal or no Hex Digit Found on command line option
           Illegal Digit Found on command line /X option
           Check syntax,  invalid  digit may  be  typed  in the  
           command line.
           
           ASPIDISK.SYS : Error Messages
           
           ASPIDISK.SYS is NOT installed
           Check  contents  of  config.sys   file.  Remove  all   
           unnecessary device  drivers,  until  driver installs  
           successfully, then re-load other drivers one at a time 
           to find the offending one.
           
           Could not access ASPI driver
           Check to see that  the ASPI drivers  are in the root  
           directory of  the  boot  drive.  Alternatively,  the  
           drivers could be placed in an alternate path, a long 
           as the correct path is specified in config.sys. e.g.  
           if the  drivers  are put  in  a  subdirectory called  
           C:\DRIVERS, then your config.sys file could load the  
           drivers like this:
           
                DEVICE=C:\DRIVERS\ASPI2DOS.SYS
           
           WARNING: Maximum number of logical drives exceeded. 
           DOS logical drivers limited to 26 (A through Z)
           
           No Host Adapter exists
           Reinstall the Host Adapter. Check cables and jumpers. 
           Confirm that the motherboard  BIOS CMOS contents are  
           set correctly with a SETUP program.
           
           DOS version under 3.30
           ASPIDISK.SYS requires MS or PC DOS version 3.3 or higher
           
           Failed to find any SCSI disks to support
           Check that the SCSI drive's  jumpers for SCSI ID and  
           LUN are set correctly.
           
           Get Device Type failed
           Check with your drive manufacturer to ensure that you 
           have the latest firmware for your SCSI drive.
           
           Get number of heads failed
           Read SCSI drive capacity failed
           If the  drive is  unable  to determine  capacity for  
           drives 0 through  7, contact  the drive Manufacturer  
           since Low-Level formatting may be needed.
           
           Failed to read master boot record
           Failed to read boot record
           Indicate difficulties reading records off the disk.  
           Check SCSI cabling, and microcode.
           
           
           For further questions, please use the Adaptec Bulletin 
           Board at 
           
                               (408) 945-7727
           (8 data bits, 1 stop bit, no parity, 1200 or 2400 baud)
      
           APPENDIX A

           Appendix A:        MESSAGE DISPLAYS
           
           
           Class 0 Message
           
           Adaptec AHA-1520 BIOS
           Version 1.1
           Copyright 1990 Adaptec, Inc.
           All Rights Reserved
           
           Class 1 Message
           
           JUMPER CONFIGURED OPTIONS:
           
           SCSI ID = 0
           Interrupt Channel = 9
           DMA Channel = 11
           SCSI parity = enabled/disabled
           transfer mode = DMA/PIO
           boot = enabled/disabled
           displayed Message Classes = #0, #1, #2, #3, #4
           initiate sync negotiation = enabled/disabled
           target disconnection = enabled/disabled
           
           Class 2 Messages
           
           Target 0: Vendor Identification, Product
                     Identification, Product Revision Level
                     (from Inquiry command)
           Target 0: disk drive ready, but Inquiry failed
           Target 0: device identification not available
           
           Class 3 Messages
           
           Reset SCSI bus.
           Diagnostics completed without error.
           Host adapter interrupt channel initialized.
           Delay for targets to recover from reset.
           No SCSI targets were set up.
        
           Class 3 Messages (continued)
         
           Checking SCSI Target 0:
               Executing SCSI Inquiry command.
               Target is connected. Wait for target ready.
               Target is ready.
               Executing "Get Disk Type" command.
               Target check completed.
           SCSI Target 0 set up as Drive C:
           Checking SCSI Target 1:
               Executing SCSI Inquiry command.
               Target is connected. Wait for target ready.
               Target is ready. Recall target.
               Executing "Get Disk Type" command.
               Target check completed.
           SCSI Target 1 set up as Drive D:
           
           Attempting to boot from floppy.
           Attempting to boot from hard disk.
           
           Class 4 Messages
           
           Boot from floppy failed.
           Boot from hard disk failed.
           
           Target 0: target not connected
           Target 0: target connected, but has a fault
           Target 0: target connected, but is not a disk drive
           Target 0: disk drive connected, but not ready
           Target 0: disk format not 512 bytes/block.
           
           HOST ADAPTER SELF DIAGNOSTIC FAILURE
           SCSI TARGET 0 NOT FOUND
           UNABLE TO INITIALIZE TARGET 0
           
           APPENDIX B

           Appendix B:   SCSI INTERNAL Connector Pin 
                         Assignments
         
         
            Signal Name  Pin   Pin        Signal Name       
         
               Ground     1     2          -DB(0)
               Ground     3     4          -DB(1)
               Ground     5     6          -DB(2)
               Ground     7     8          -DB(3)
               Ground     9     10         -DB(4)
           
               Ground     11    12         -DB(5)
               Ground     13    14         -DB(6)
               Ground     15    16         -DB(7)
               Ground     17    18         -DB(P)
               Ground     19    20         Ground
           
               Ground     21    22         Ground
               Ground     23    24         Ground
               Open       25    26         Term Power (Fused)
               Ground     27    28         Ground
               Ground     29    30         Ground
         
               Ground     31    32         -ATN
               Ground     33    34         Ground
               Ground     35    36         -BSY
               Ground     37    38         -ACK
               Ground     39    40         -RST
         
               Ground     41    42         -MSG
               Ground     43    44         -SEL
               Ground     45    46         -C/D
               Ground     47    48         -REQ
               Ground     49    50         -I/O
        
           APPENDIX C

           Appendix C:    SCSI EXTERNAL CONNECTOR PIN               
                          ASSIGNMENTS
         

           Signal Name   Pin   Pin        Signal Name       
               Ground     1     26         -DB(0)
               Ground     2     27         -DB(1)
               Ground     3     28         -DB(2)
               Ground     4     29         -DB(3)
               Ground     5     30         -DB(4)
         
               Ground     6     31         -DB(5)
               Ground     7     32         -DB(6)
               Ground     8     33         -DB(7)
               Ground     9     34         -DB(P)
               Ground     10    35         Ground
         
               Ground     11    36         Ground
               Ground     12    37         Ground
               Open       13    38         Term Power (Fused)
               Ground     14    39         Ground
               Ground     15    40         Ground
         
               Ground     16    41         -ATN
               Ground     17    42         Ground
               Ground     18    43         -BSY
               Ground     19    44         -ACK
               Ground     20    45         -RST
         
               Ground     21    46         -MSG
               Ground     22    47         -SEL
               Ground     23    48         -C/D
               Ground     24    49         -REQ
               Ground     25    50         -I/O
         
                                                      
       
           Class 2 Messages
           
           Target 0: Vendor Identification,