PREFACE 

FCC COMPLIANCE 

This equipment generates and uses radio frequency energy and if not installed 
and used properly, that is, in strict accordance with the manufacturer's 
instructions, may cause interference to radio and television reception. It has 
been type tested and found to comply with the limits for a Class B computing 
device in accordance with the specifications of Subpart J of Part 15 of FCC 
Rules, which are designed to provide reasonable protection against such 
interference in residential installation. However, there is no guarantee that 
interference will not occur in a particular installation. If this equipment 
does cause interference to radio or television equipment reception, which can 
be determined by turning the equipment off and on, the user is encouraged to 
try to correct the interference by one or more of the following measures: 

   Reorient the receiving antenna 
   Relocate the computer with respect to the receiver 
   Move the computer away from the receiver 
   Plug the computer into a different outlet so that computer and receiver are 
   on different branch circuits 

If necessary, the user should consult the dealer or an experienced 
radio/television technician for additional suggestions. The user may find the 
following booklet prepared by the Federal Communications Commission helpful: 
   "How to Identify and Solve Radio-TV Interference Problems" This booklet is 
available from the U.S. Government Printing Office, Washington, D.C. 20402, 
Stock No. 004-000-00345-4. 

Warning: This equipment has been certified to comply with the limits for Class 
B computing device, pursuant to Subpart J of Part 15 of FCC Rules. Only 
peripherals (computer input/output devices, terminals, printers, etc.) 
certified to comply with the Class B limits may be attached to this computer. 
Operation with non-certified peripherals is likely to result in interference 
to radio and TV reception. Also this equipment must be used with shielded 
power cables and shielded I/O cables. 

COPYRIGHT 

Copyright 1988 Adaptec, Inc. All Rights Reserved. 


No part of this publication may be reproduced, stored in a retrieval system, 
or transmitted, in any form or by any means, electronic, mechanical, 
photocopying, recording or otherwise, without the prior written consent of 
Adaptec Inc., 691 S. Milpitas Blvd., Milpitas, California 95035 

TRADEMARKS 

The trademarks referred to in this manual are identified and acknowledged as 
follows: IBM PC AT, PC-DOS, Micro Channel, Personal System/2, PS/2, Operating 
System/2, OS/2 are registered trademarks of International Business Machines 
Corporation. MS-DOS and XENIX are registered trademarks of Microsoft 
Corporation. UNIX is a registered of AT&T. Netware is a registered trademark 
of Novell, Inc. SCO is a trademark of the Santa Cruz Operation. 
              
CHANGES       
              
The material in this manual is for information only and is subject to change 
without notice.                         
                                
Adaptec reserves the right to make changes in the product design without 
reservation and without notification to its users. 
                                                 
Additional information may be obtained from: 
                                
                                     Adaptec, Inc 
                                Literature Department 
                               691 South Milpitas Blvd. 
                                 Milpitas, CA 95035 

                                                      Table of Contents

  1.0 Introduction                                                1-1 
     1.1 Document Scope                                           1-1 
     1.2 Purpose                                                  1-1 
     1.3 AHA-1640 Product Features                                1-1 
     1.4 Product Specifications                                   1-2 
     1.5 Reference Documents                                      1-3 

  2.0 Host Adapter Architecture                                   2-1 
     2.1 Hardware                                                 2-1 
        2.1.1 First Party DMA                                     2-1 
        2.1.2 SCSI Protocol Chip (ACI-6250)                       2-1 
        2.1.3 Host Adapter DMA Chip                               2-1 
        2.1.4 High Performance Control Processor                  2-1 
        2.1.5 Hardware Block Diagram                              2-2 
     2.2 Firmware                                                 2-3 
        2.2.1 Multithreaded Operation                             2-3 
        2.2.1.1 Mailboxes                                         2-3 
        2.2.1.2 Command Control Block                             2-6
        2.2.1.3 Command Descriptor Block                          2-6 
        2.2.1.4 Principles of Operation                           2-7 
        2.2.1.5 Task Queueing                                     2-7  
        2.2.2 Single-Threaded Operation through the BIOS          2-7 

  3.0 Installation                                                3-1 
     3.1 Unpacking and Inspecting                                 3-1 
     3.2 Installation                                             3-1 
        3.2.1 System Requirements                                 3-1 
        3.2.2 Hardware Installation                               3-1 
        3.2.3 Software Installation                               3-2 
        3.2.4 Common Problems during Installation                 3-5 
  
  4.0 Multithreaded Software Interface                            4-1 
     4.1 Hardware Overview                                        4-1 
     4.2 POS Register Interface                                   4-2 
        4.2.1 POS Register 0                                      4-4 
        4.2.2 POS Register 1                                      4-5 
        4.2.3 POS Register 2                                      4-5 
        4.2.4 POS Register 3                                      4-5 
        4.2.5 POS Register 4                                      4-6 
        4.2.6 POS Register 5                                      4-7 
     4.3 Preparation of Micro Channel DMA Hardware                4-7 
        4.3.1 8237 Compatibility Mode                             4-8 
        4.3.2 DMA Extended Mode                                   4-9 
     4.4 I/O Port Interface                                       4-9 
        4.4.1 Control and Status Port                             4-11 
        4.4.2 Command/Data Out and Data In Port                   4-13 
        4.4.3 Interrupt Flag Port                                 4-13 
     4.5 Reset Overview                                           4-15 
        4.5.1 Hard Reset Operations                               4-15 
        4.5.2 SCSI Reset Operations                               4-16 
        4.5.2.1 SCSI "Soft" Reset Option                          4-16 
        4.5.2.2 SCSI "Hard" Reset Option                          4-17 

                                i
                                                      Table of Contents

     4.6 I/O Command Port (IOCP) Command Set                      4-17 
        4.6.1 No Operation                                        4-18 
        4.6.2 Mailbox Initialization                              4-19 
        4.6.3 Start SCSI Command                                  4-19 
        4.6.4 Start BIOS Command                                  4-19 
        4.6.5 Adapter Inquiry                                     4-20 
        4.6.6 Enable Mailbox Out Available Interrupt              4-21 
        4.6.7 Set SCSI Selection Time Out                         4-21 
        4.6.8 Set Bus On Time                                     4-22 
        4.6.9 Set Bus Off Time                                    4-22 
        4.6.10 Set Transfer Speed                                 4-22 
        4.6.11 Return Installed Devices                           4-22 
        4.6.12 Return Configuration Data                          4-22 
        4.6.13 Enable Target Mode                                 4-25 
        4.6.14 Return Setup Data                                  4-25 
        4.6.15 Write Channel 2 Buffer                             4-27 
        4.6.16 Read Channel 2 Buffer                              4-27 
        4.6.17 Write Adapter FIFO Buffer                          4-27 
        4.6.18 Read Adapter FIFO Buffer                           4-28 
        4.6.19 Echo Command Data                                  4-28 
     4.7 Mailbox Description                                      4-28 
        4.7.1 Mailbox Out Definition                              4-29 
        4.7.2 Mailbox In Definition                               4-30 
     4.8 Command Block Definition                                 4-34 
     4.9 Scatter/Gather List Definition                           4-40 
     4.10 Description of Operation                                4-41 
        4.10.1 Initialization Procedure                           4-41 
        4.10.2 Execution of Initiator Mode Operations             4-41 
        4.10.3 Execution of Target Mode Operations                4-42 
        4.10.3.1 Target Mode with a Prepared CCB                  4-42 
        4.10.3.2 Target Mode without a Prepared CCB               4-42 
        4.10.4 CCB Queueing and Scan Order                        4-43 
                                                               
5.0 Single Threaded Operation                                     5-1 
     5.1 Single Threaded BIOS Command Interface                   5-1 
     5.2 BIOS Command Execution using Interrupt 13                5-1 
        5.2.1 Physical to Logical Address Translation             5-2 
        5.2.2 BIOS Command Return Codes                           5-2 
     5.3 BIOS Disk Commands                                       5-4 
        5.3.1 Reset Disk System                                   5-5 
        5.3.2 Read Status of Last Operation                       5-5 
        5.3.3 Read Desired Sectors from Memory                    5-5 
        5.3.4 Write Desired Sectors from Memory                   5-6 
        5.3.5 Verify Desired Sectors                              5-6 
        5.3.6 Identify SCSI Devices                               5-6 
        5.3.7 Read Drive Parameters                               5-7 
        5.3.8 Initialize Drive Pair Characteristics               5-7 
        5.3.9 Seek                                                5-7 
        5.3.10 Alternate Disk Reset                               5-8 
        5.3.11 Test Drive Ready                                   5-8 
        5.3.12 Recalibrate                                        5-8 
        5.3.13 Read DASD Type                                     5-9 

                                 ii
                                                      Table of Contents

  6.0 Device Drivers                                              6-1 
     6.1 PS/2_ Compatible POS Initialization                      6-1 
     6.2 PS/2_ Compatible BIOS                                    6-1 
        6.2.1 Initialization                                      6-1 
        6.2.2 System Boot                                         6-2 
        6.2.3 Hard Disk I/O                                       6-2 
     6.3 Unix/Xenix                                               6-2 
     6.4 DOS Driver                                               6-3 
     6.5 OS/2_ Driver Availability                                6-3 
     6.6 Virtual Memory Driver                                    6-3 
     6.7 AHA-1640 On-board Utilities                              6-4 
     6.8 Third Party Software Suppliers for AHA-1640              6-5 
                                                                 
 7.0 SCSI Features                                                7-1 
     7.1 SCSI Description, Initiator Mode                         7-1 
        7.1.1 Linked SCSI Commands                                7-2 
        7.1.2 Zero Latency Read Operation                         7-2 
     7.2 SCSI Description, Target Mode                            7-3 
        7.2.1 Initiator Conformance Level Requirements            7-3 
        7.2.2 Support of Synchronous Transfer                     7-3 
        7.2.3 SCSI Target Operation In Processor Target Mode      7-3 
        7.2.3.1 TEST UNIT READY                                   7-4 
        7.2.3.2 REQUEST SENSE                                     7-5 
        7.2.3.3 INQUIRY                                           7-7 
        7.2.3.4 SEND DIAGNOSTIC                                   7-8 
        7.2.3.5 SEND                                              7-8 
        7.2.3.6 RECEIVE                                           7-9 
        7.2.4 Incorrect Length Management                         7-9 
  
  8.0 Problem Determination                                       8-1 
     8.1 Self Diagnostics                                         8-1 
     8.2 Indicators                                               8-2 
     8.3 Problem Correction                                       8-2 
        8.3.1 Common Problems during Installation                 8-2 
        8.3.2 IOCP Command Errors and Corrective Actions          8-2 
        8.3.3 HA Status Error Indications and Corrective Actions  8-3 
        8.3.4 SCSI Error Indications and Corrective Actions       8-5 
  
  9.0 Glossary                                                    9-1 


                                iii

Section One                                                       Introduction
------------------------------------------------------------------------------

1.1 DOCUMENT SCOPE

This manual provides  the information  required to  install and  
program the AHA-1640 intelligent host adapter in a Micro Channel 
compatible computer system. 


1.2 PURPOSE


The Adaptec AHA-1640 provides a powerful multitasking interface  
between the Micro Channel and the Small Computer System Interface 
(SCSI) bus. The AHA-1640 is a high-performance intelligent host  
adapter supporting  a  maximum asynchronous  SCSI  rate  of 2.0  
Mbytes/second and a synchronous transfer rate of 5 Mbytes/second. 
The AHA-1640  supports multithreaded  I/O  operations, allowing  
simultaneous  operations  on  multiple  targets/Logical  Units.   
Disconnect/Reconnect  support  maximizes  bus  utilization  for   
multiple target  systems.  Target  Mode  operation  allows  the  
AHA-1640 to  receive  information  from  other  host  adapters.  
Scatter/gather capability allows a continuous stream of data from 
the SCSI bus to be distributed  across many segments of memory.  
Zero Latency Read (ZLR) speeds delivery of data from peripherals 
that support the function.

The Adaptec AHA-1640 meets  system application requirements for  
very high performance,  configuration flexibility, multitasking  
capability, and system  redundancy. The  AHA-1640 also provides  
standard hard disk controller services through BIOS calls.


1.3 AHA-1640 PRODUCT FEATURES


ù High-performance First Party DMA with  a burst data rate of 8  
  Mbytes/second
ù 16- and 8-bit transfers
ù Even or odd starting address transfers
ù Maximum synchronous SCSI transfer rate of 5.0 Mbytes/second
ù Asynchronous and synchronous peripherals supported simultaneously
ù Full arbitration support with fairness
ù Programmable Option Select (POS) to set arbitration level
ù POS to set interrupt level
ù POS to select port addresses
ù POS to select BIOS addresses
ù POS to obtain the card id (0F1FH)
ù True  multithreaded operation supporting up to 255 tasks simultaneously
ù Programmable mailbox architecture 
ù Adaptec BIOS for standard hard disk emulation
ù Internal and external SCSI connectors
ù Host memory scatter/gather capability
ù Processor type target functions supported  for 1 to 8 logical threads
ù Host adapter status and diagnostic results displayed by LED

             
                                  1-1

Section One                                                       Introduction
------------------------------------------------------------------------------

1.4 PRODUCT SPECIFICATIONS


ù Approximate Physical Dimensions

    Length: 323 mm (12.7")           
    Width: 100 mm (3.93")
    Height: 21 mm (0.82")
    
    Standard 16-bit Micro Channel form-factor.
    
    Electrical interface and interface timing as specified for  
    16-bit Micro Channel.

ù Power Requirements

    +5.0 +/- 0.25 Volts at 1.6 Amps maximum.

ù Environmental Requirements

    Operating temperature: 0-60ø C

    Storage temperature:    0-60ø C   


ù Reliability Information

    Mean Time Between Failures: 15000 hours 
       (calculated per Mil Handbook 217E, ground benign, 40øC)

    Mean Time Between Failures: TBD hours
       (experimental:)

    Mean Time To Repair: 30 minutes


ù SCSI Interface

    Electrical Interface:
    
      As specified by ANSI X3.131-1986 for single-ended operation.
    
      Minimum driver output: 48 milliamps, sinking @ 0.5 volts
    
           Signal true:          min:   0   volts     max:   0.8  volts   
           Signal false:         min:   2.0 volts     max:   5.25 volts
           Input hysteresis:     min:   0.2 volts     

           Terminator Power voltage:  min: 4.25 volts max:   5.25 volts
           Terminator Power current:  min: 800 ma.    max:   1.5 amp (fused)

                                  1-2

Section One                                                       Introduction
------------------------------------------------------------------------------

    Internal connector:

         Unshrouded 50-pin header,  compatible with unshielded  
         alternative  1   connector  as   specified   in  ANSI   
         X3.131-1986 Figure 4-1
         
         Partial list of compatible connector plugs:
         
         Manufacturer          Model           Part Number
         -------------------------------------------------           
         3-M                   N.A.            3425-6000
         T&B Ansley            N.A.            609-5000M
         Molex                 N.A.            15-29-8505
         
         
    External connector:
    
         Shielded 50-pin  connector as  specified  in proposed  
         SCSI-2 standard  X3T9.2/86-109  Revision  5, Appendix  
         D, Figure D-3
         
         Partial list of compatible connector plugs:
         
         Manufacturer          Model           Part Number
         -------------------------------------------------
         Amp                   Amplimite
         Fujitsu
         Honda
         
Meets radiation limits specified for a Class B computing device  
in accordance with the specifications in Subpart J of Part 15 of 
FCC Rules.  See  FCC Compliance  notes  and  recommendations in  
preface of this document.


1.5 REFERENCE DOCUMENTS


ù Small Computer Systems  Interface, ANSI X3.131-1986, American  
  National Standards Institute, N.Y., N.Y., 1986

ù IBM Personal  System/2 and  Personal Computer  BIOS Interface  
  Technical Reference,  Document 84X1514, April, 1987

ù IBM Personal  System/2 Model  50 and  60 Technical Reference, April, 1987

ù IBM Personal  System/2 Model  80 Technical  Reference, April, 1987

ù Enhanced Small  Computer Systems  Interface (SCSI-2), working draft, 
  X3T9.2/87-109  Revision 5, August 8, 1988.

ù Adaptec AHA-1640 Host Adapter, Installation Guide

ù Adaptec Host Adapter Programming Guide


                                  1-3

Section Two                                         Host Adapter Architecture 
------------------------------------------------------------------------------

2.1 HARDWARE 


2.1.1 First Party DMA


The AHA-1640 controls the  host Micro Channel  as a Bus Master,  
transferring data directly to and  from main system memory. The  
host adapter provides its own  DMA services, using the standard  
arbitration process  to  gain  control  of  the  Micro Channel.  
Operation as a Bus Master reduces  system overhead in two ways.  
First, the two memory cycle transfer required by an ordinary DMA 
Slave is reduced by operation as a  Bus Master to one cycle. In  
addition, host CPU  overhead is reduced  because the  CPU is no  
longer required to maintain the  DMA channel's address pointers  
and word  counts, manage  multitasking sub-channels,  or handle  
extra interrupts.

Adaptec's implementation of Bus Master operation achieves a 6.7  
Mbyte/second burst data rate.  This speed is especially valuable 
in multitasking systems where the tasks execute on a time-shared 
basis. Appendix A shows  a diagram of  the Micro Channel timing  
requirements.

The AHA-1640  DMA hardware  will handle  transfers of  odd data  
length and transfers beginning  on odd byte  boundaries with no  
performance degradation.

2.1.2 SCSI Protocol Chip (AIC-6250)

The AHA-1640 utilizes the AIC-6250 SCSI protocol chip to maximize 
the SCSI bus utilization. The AIC-6250 is an Adaptec VLSI device 
which allows the AHA-1640 to achieve 2.0 Mbyte/Sec asynchronous  
SCSI data transfer rates, and 5.0 MB/second synchronous transfer 
rates. The AIC-6250 will also enable the AHA-1640 to operate as  
both an initiator and as a target device. 

The  AIC-6250   has  separate   data   busses  for   the  local   
microprocessor and  for  the  system  data  bus.  This  further  
increases the  performance  of  the  AHA-1640  by  reducing the  
overhead associated with SCSI commands.

2.1.3 Host Adapter DMA Chip

The AHA-1640  uses  a  highly integrated  DMA  control  chip to  
implement  the  Bus   Master  functions.  The   high  level  of   
integration assures high performance and high reliability in the 
small form factor of the Micro Channel standard card.


                                  2-1

Section Two                                         Host Adapter Architecture 
------------------------------------------------------------------------------

2.1.4 High Performance Control Processor


The   AHA-1640   uses   a   high-performance   16-bit   control    
microprocessor to reduce system  overhead and provide extremely  
fast response time. Total SCSI bus overhead associated with the  
host  adapter  is  typically  300   to  500  microseconds.  The   
sophisticated multitasking and queueing capability together with 
the very low firmware overheads assures superior performance in  
any environment.


The  microprocessor   performs   diagnostic   and  verification   
operations for installation  and troubleshooting.  An LED under  
control of the microprocessor indicates that normal operation is 
occurring.


2.1.5 Hardware Block Diagram 







                           [Picture]

               FIGURE 2-1. HARDWARE BLOCK DIAGRAM
                                     


                                  2-2

Section Two                                         Host Adapter Architecture 
------------------------------------------------------------------------------
                                     
2.2 FIRMWARE


The AHA-1640  supports multithreaded  SCSI  initiator operation  
through a simple mailbox protocol. The firmware accepts up to 112 
Command Control Blocks (CCB's) and executes them from its local  
RAM. The firmware controls all of the SCSI activity that a task 
may require. This includes Arbitration, Selection, Disconnection, 
Reconnection, and Command completion.

Using the same mailbox protocol, the  AHA-1640 can operate as a  
processor type device serving as a multitasking target to other  
initiators. This  feature allows  high  bandwidth communication  
between multiple hosts. The communication capability can be used 
to  create   high  availability   computer   systems,  parallel   
processing systems, or  systems that can  use shared peripheral  
devices.

The Bus Master  mode of  operation allows  the host  adapter to  
scatter an incoming  data stream  into as  many as  16 separate  
memory segments,  or to  collect  segments into  a  single data  
stream.  This  scatter/gather   capability  provides  important   
performance enhancements  for many  operating systems  that use  
virtual memory or memory paging. Zero latency read and queueing  
provide the capability of further increasing system performance. 

In addition,  the AHA-1640  firmware  cooperates with  the BIOS  
installed on the host adapter to emulate the PS/2 hard disk BIOS 
interface. This  allows booting  operations from  attached SCSI  
hard drives. In addition, the emulation provides support for up  
to 2 SCSI hard  drives under DOS without  any requirement for a  
device driver.

The firmware also supplies diagnostic capability.


2.2.1 Multithreaded Operation


A multiuser, multitasking operating system issues a large number 
of I/O  tasks  in a  rapid  sequence. The  architecture  of the  
AHA-1640 makes  management  of  this  activity  very  easy  and  
straightforward for the operating system and its associated I/O  
drivers. This section briefly  explains the interaction between  
the system and the AHA-1640 required to accomplish an I/O task.


2.2.1.1 Mailboxes


The AHA-1640 uses a mailbox architecture for task communication  
between the host and host adapter. This allows the host adapter  
to perform  multithreaded  operations with  a  minimum  of host  
intervention.The mailboxes are  located in  main system memory.  
Each mailbox entry is four bytes long. After power up sequencing, 
host initialization  procedures,  and  the  boot  procedure are  
completed, the host issues an  initialization command to inform  
the host adapter of  the mailbox location.  There are always an  
equal number of Outgoing Mailboxes (MBO) and Incoming Mailboxes  
(MBI). MBIs are located  immediately after the  MBOs. A typical  
mailbox structure is shown in Figure 2-2.


                                  2-3

Section Two                                         Host Adapter Architecture 
------------------------------------------------------------------------------

                    
                          [Picture]
                                      
             FIGURE 2-2. TYPICAL MAILBOX STRUCTURE
                                     
                                     
In this example, there  are four MBOs and  four MBIs. The first  
byte of each MBO contains the command byte. The remaining three  
bytes point to a Command Control  Block (CCB). The CCB provides  
additional task information. AMBO is free  if the first byte is  
zero. The  first byte  of  each MBI  contains the  status  of a  
completed task. The remaining three bytes point to the CCB of the 
task. An MBI is free if the  Status byte is zero. Mailboxes may  
point to CCBs that control initiator tasks, that service target  
tasks or that perform a Bus Device Reset.


2.2.1.2 Command Control Block


A Command Control  Block provides  the information  required to  
control a SCSI command sequence when the AHA-1640 is performing  
initiator functions. The  block contains  pointers to  the data  
area to be used by the command. It contains areas for presenting 
status of both the host adapter  and the addressed SCSI device.  
In addition,  it  contains the  SCSI  Command  Descriptor Block  
defining the action to be taken by the addressed SCSI device. An 
error information buffer area is also provided. 

The AHA-1640 can also serve as a target, providing or accepting  
data blocks at the command of some other initiator. The AHA-1640 
acts like a standard  SCSI processor device.  In this case too,  
Command Control  Blocks  are  used  to  perform  the operations  
requested by other initiators to the AHA-1640.

The CCB is defined completely in Section 4.8.

A typical initiator CCB is shown in Figure 2-3.



                                  2-4

Section Two                                         Host Adapter Architecture 
------------------------------------------------------------------------------


                          [Picture]
                                     
               FIGURE 2-3. TYPICAL INITIATOR CCB





                                  2-5

Section Two                                         Host Adapter Architecture 
------------------------------------------------------------------------------


2.2.1.3 Command Descriptor Block 


The Command Descriptor Block (CDB), a part of the Command Control 
Block, is a standard format command packet that is transmitted to 
the addressed  SCSI  device.  It contains  all  of  the command  
information required by the SCSI  device to perform the desired  
operation. The  Command Descriptor  Block contains  the command  
Operation Code followed by a Logical Unit Number (LUN), command  
parameters if required and a control byte. A typical Group 0 six 
byte CDB is shown in Figure 2-4.

                                     
                           [Picture]

            FIGURE 2-4. TYPICAL GROUP 0 SIX BYTE COB
                                     
                                     
Please refer to the SCSI  specification ANSI X3.131, the Common  
Command Set  (CCS)  revision  4B,  and  the  SCSI  2 draft  for  
additional information on Command Descriptor Blocks.


2.2.1.4 Principles of Operation


At power-up, the host informs the  host adapter of the location  
and number of mailboxes. To start a task, the host builds a CCB  
and stores the memory address of the CCB into a free mailbox. A  
non-zero Mailbox Out command  byte is then  written to indicate  
that the mailbox entry is full and valid. The host then writes to 
an I/O port  (defined in Section  4) to indicate  that the host  
adapter should scan the MBO area. When a full MBO is found, the  
host adapter copies the mailbox's CCB pointer into its internal  
RAM and clears the Mailbox  entry by writing a  zero to the MBO  
command byte. This frees the MBO so that it can be used to start 
another task.  If  the  host  software  prefers,  an  MBO Empty  
interrupt can be generated every time that an MBO is cleared by 
the host adapter. 


After completing a task, the host adapter scans the MBI area for 
a free mailbox. When one is found, it is updated with the task's 
completion status and  CCB pointer. The  CCB pointer identifies  
the completed task. AMBI Full  interrupt is generated to notify  
the host that a task has been completed. The host scans the MBI  
area searching for a non-zero Status byte. When one is located,  
the host obtains the CCB pointer and frees the MBI by writing a  
zero into the Status byte. The host then examines the contents of 
the  CCB  to  determine  that   the  command  was  successfully   
completed.The freed  MBI  can  now  be  used  to  indicate  the  
completion of another task. The host adapter fills the MBI area  
in a round-robin fashion. If the host saves the position of the 
last active MBI entry, it can determine  the MBI of a new entry  
immediately without scanning.


                                  2-6

Section Two                                         Host Adapter Architecture 
------------------------------------------------------------------------------


The host adapter  never transmits a  new interrupt  to the host  
until the previous interrupt has been cleared and serviced by the 
host. The host should analyze the  interrupts and clear them as  
soon as  possible so  that the  host adapter  can post  any new  
interrupts quickly.  The host  adapter will  not wait  until an  
interrupt can be transmitted to the host before processing an MBO 
entry or creating a new MBI entry. Thus, in processing a single 
MBI interrupt, the host may find several MBI entries waiting by  
the time  the interrupt  processing  is finished.  Similarly, a  
later MBI interrupt for  the last of the  later MBI entries may  
find nothing to service because the  MBI entry was examined and  
processed as a result  of the first MBI  Full interrupt. If the  
interrupts are reset quickly by the host, the probability of an  
interrupt occurring when no MBI entry is available is much lower, 
providing an  important  performance  improvement.  If  the MBI  
entries are emptied by the host in a round-robin order, the scan 
for the next full entry is very  simple, since it is always the  
next MBI entry in the mailbox area.


2.2.1.5 Task Queueing


Multiple tasks may be  started against a  target/LUN or against  
multiple targets/Logical Units. Since only one task can be active 
against any one given LUN at a time, all other tasks for the same 
LUN are queued.  Other LUNs may  have active tasks  at the same  
time.

The host adapter executes commands  on a first-found, first-out  
basis for each  target/LUN combination. The  host adapter scans  
the MBO entries in  a round robin manner  starting at the first  
entry after the location  that was last  identified by the host  
adapter as full. If new  MBO entries are made by  the host in a  
similar round robin manner, then all entries will be queued and  
executed in  a  first  in,  first  out  (FIFO)  order for  each  
target/LUN combination. There  is no guarantee  of a particular  
order of execution between different target/LUN combinations.


2.2.2  Single threaded operation through the BIOS

A host adapter BIOS is provided to emulate the standard PS/2 hard 
disk BIOS and boot functions. With  this BIOS, the host adapter  
can be used in lieu of a standard hard disk controller on a PS/2 
compatible system.

The BIOS is compatible  with the standard  PS/2 hard disk BIOS.  
This allows DOS to access up to two hard disk devices on the SCSI 
bus without a  driver. All  normal I/O  functions are supported  
including  system  booting.   Single  threaded   operation  and   
multithreaded operation do  not operate  simultaneously. Single  
threaded operation cannot be  requested until all multithreaded  
operations  are   completed.   Similarly,   all   multithreaded   
operations must be complete before  a single threaded operation  
can be requested. For most multitasking operating systems, such  
as Xenix and OS/2,  single threaded operation  is normally used  
only for  the early  part of  the  boot operation,  after which  
multithreaded  drivers  take  over  all  control  of  the  SCSI   
operations.


                                  2-7

Section Three                                                    Installation 
------------------------------------------------------------------------------


3.1 UNPACKING AND INSPECTING


The carrier is responsible for damage incurred during shipment.  
In case of damage, have the carrier note the damage on both the  
delivery receipt and the freight bill, then notify your freight  
company representative so that the necessary insurance claims can 
be initiated.

After opening the shipping  container, use the  packing slip to  
verify receipt of the individual items listed on the slip. Retain 
the shipping container and packing  material for possible later  
reuse  should  return  of  the  equipment  to  the  factory  be   
necessary.

CAUTION: The  AHA-1640  is  carefully  designed  to  resist the  
effects of  static  electricity. However,  like  all electronic  
equipment, it can  be damaged or  its life can  be shortened by  
unusual static discharges.  Please take  the proper precautions  
when handling  the  board.  Keep the  board  in  its conductive  
wrapping until it is  ready to be installed  in your system. Be  
sure that  the host  computer  and the  personnel  handling the  
board are properly grounded while installing the board.


3.2 INSTALLATION


The following section details the installation procedure for the 
Adaptec AHA-1640  Micro  Channel  to  SCSI  host  adapter.  The  
installation of the board requires that the board be installed in 
a 16-bit Micro Channel  slot. The appropriate  SCSI devices and  
subsystems must then be  installed using a  shielded cable with  
shielded connectors for external devices and a ribbon cable for  
internal devices. Using the POS capability of the Micro Channel, 
the proper installation parameters are set in the host computer  
for transfer to the  host adapter during  the boot process. The  
proper software must then be installed. From then on, full SCSI  
operation is available.

CAUTION: The system must be  turned off during the installation  
procedure.

3.2.1 System Requirements

The  host  adapter  must  be  installed  in  a  Micro  Channel  
compatible host computer.  The proper  levels of  software and  
software drivers  must  be  available.  The  System  Reference  
Diskette for the  system must  have the  proper initialization  
file present to allow host adapter initialization. The file is 
named  @0F1F.ADF  and  is  available   from  Adaptec  for  OEM  
customization. Using the  information provided in  Section 4.2  
and knowing the proper  Adapter Description File  (ADF) format 
described in the IBM Technical Reference manuals, a customized 
@0F1F.ADF may also be prepared to meet special requirements.


                                  3-1

Section Three                                                    Installation 
------------------------------------------------------------------------------

3.2.2  Hardware Installation


The installation procedure of the SCSI Host Adapter/MC requires 
configuring of  the host  adapter  terminators, inserting  the  
board into a 16  bit connector, and connecting  the SCSI cable 
from the  internal  or external  SCSI  connector  to the  SCSI  
devices or subsystems. 

To install the host adapter, you should follow the installation 
steps in order.

1) Turn OFF the power to the computer system.

2) Configure  the  host  adapter  termination.  The  SCSI  bus  
requires that there be only two terminators installed and that 
the terminators must be placed at the farthest ends of the SCSI 
bus. If the  host adapter  is neither  the first nor  the last  
peripheral on the SCSI bus, the terminator resistor networks at 
locations RN2 and RN3  must be removed from  the host adapter. 
The terminator resistor networks  at RN2 and RN3  must also be 
removed if the host adapter is the first or last peripheral on 
the SCSI bus  and if  inline terminator modules  are connected  
directly to the external SCSI connector of the host adapter.

3) Open the  computer system  according to  the manufacturer's  
directions to expose the  adapter slots in  which the AHA-1640  
will be placed.

4) If only an external SCSI subsystem is to be used, no internal 
cabling is required. If  an internal SCSI peripheral  is to be 
used, install  the supplied  50-pin ribbon  cable to  the host  
adapter. This cable must  be oriented correctly. Pin  1 of the 
SCSI cable is designated  by a red  stripe. Pin 1  on the host 
adapter 50-pin SCSI header  is located on the  left hand side, 
farthest from the installation bracket and is designated by the 
words PIN  1  on  the  board  adjacent  to the  header.  After  
locating pin  1 on  the host  adapter and  on the  SCSI cable,  
carefully insert the connector located at the  end of the long 
end of  the cable  in  to the  host  adapter connector.  After  
ensuring that  all  pins  are lined  up  and  that  the pin  1  
orientation is correct, firmly seat the connector to the board. 
If it is ever necessary to remove the cable, gentle prying with 
a small thin-bladed  screwdriver may  be required.  Be careful  
not to bend or scar the header pins.

5) After installing  the SCSI cable,  the host adapter  can be  
installed in any one of the 16-bit slots in the computer. 

6) If internal SCSI peripherals are to be used, they should be 
installed in the drive bays in  accordance with the directions 
on the  peripherals.  The  50-pin  ribbon  cable  can  now  be  
attached  to  the  SCSI  peripherals.   Please  refer  to  the  
installation instructions to ensure proper pin 1 orientation of 
the SCSI  peripherals. Pin  1 orientation  must  be consistent  
throughout the system.

7) After installing the  host adapter and cabling  to the SCSI 
peripheral, review the installation steps to  be sure that all 
operations are correctly executed. Take  special care to check 
that the side of the  SCSI cable with the solid  red stripe is 
always  attached  to  pin  1  of  the  host  adapter  and  the  
peripherals and that  the connector  is mated with  the header  
correctly. Take special care  that the peripheral  devices are 
properly fastened  into  the computer  and  that all  required  
cabling is  completed. Be  sure  that the  system  is properly  
terminated.

8) Carefully  reinstall  the  cover  on  the  computer  system  
according to the manufacturer's instructions.

9) If an external SCSI subsystem is to be installed, it can now 
be cabled to the  external SCSI connector  projecting from the  
shielding bracket on the back of the SCSI Host Adapter/MC. The 
proper shielded  SCSI  cable  must  be  used.  The  subsystem,  
cables, and SCSI terminators  must be installed  in accordance 
with the directions provided with the external SCSI subsystem.


                                  3-2

Section Three                                                    Installation 
------------------------------------------------------------------------------

3.2.3 Software Installation


The SCSI Host Adapter/MC requires initialization parameters to 
be loaded when the host adapter is first installed or after the 
system standby  battery has  been changed.  The  host adapter,  
after the initialization parameters have once been loaded, will 
automatically be initialized  with these parameters  each time  
the system  performs a  boot operation.  The  System Reference  
Diskette is restricted from write operations, so a copy must be 
prepared if the parameters are to be backed up to a diskette.

The initialization parameters  are installed by  executing the  
following steps.

A)     Prepare the back-up Reference Diskette.

1) Install the System Reference Diskette in floppy drive A.

2) Turn on the host computer system. The system will boot using 
the  reference  diskette's  operating  system   and  the  host  
system's BIOS.

3) After the boot is complete, the system Main Menu will appear. 
Select the 'Back up  the reference diskette'  option and press  
the ENTER key. The Back Up menu will appear.

4) Follow the instructions on the Back Up menu to complete the 
diskette back up process. The instructions will require you to 
select the  drive  in  which  the  original  System  Reference  
Diskette will  be read  and  the drive  in which  the  back up  
diskette will be written. If the same  drive is used for both, 
you will be  given instructions to  swap the diskettes  at the  
appropriate times. To  be sure that  there is enough  space to  
include all the reference information on the back up diskette, 
the back up diskette  should have no other  information on it. 
If the  diskette  is unformatted,  the  Back  Up program  will  
automatically format the diskette.

5) Remove both the  System Reference Diskette and  the back up 
reference diskette and return to the Main Menu.


B) Set the initial parameters, save them in RAM, and back them 
up to the back up reference diskette.

1) Install the back-up copy of the System Reference Diskette in 
floppy drive A.

2) Boot by  pressing the  CONTROL, ALTERNATE, and  DELETE keys  
simultaneously.  The  system  will  boot   using  the  back-up  
reference diskette's  operating system  and the  host computer  
system's BIOS.

3) After the boot is complete, the system Main Menu will appear. 
Select the 'SET CONFIGURATION' option and press the ENTER key. 
The Set Configuration menu will appear. 

                                  3-3

Section Three                                                    Installation 
------------------------------------------------------------------------------

4) Press  the  proper  index  number  to  request the  'CHANGE  
CONFIGURATION' option.  The  Change  Configuration  menu  will  
appear, displaying the installed or  the default configuration 
for each installed function or  adapter. The following options 
may be changed:

                           TABLE 3-1
                                    
    OPTION                        DEFAULT VALUE
    -------------------------------------------
    Port I/O Address                       330H
                                        
    Arbitration Level                         1
    
    Interrupt Level                          15
    
    Adapter BIOS                DC000H, ENABLED
    
    SCSI Device Identifier                    7
    
    SCSI Parity Checking On/Off              ON
    
    Synchronous Transfer Initiated by Host   NO
    
    MCA Fairness On/Off                      ON
    
                                       
Each option may be  changed by stepping  through the available  
choices  using  the  specified  function  key.  Help  text  is  
available for each option to indicate how the choice should be 
made.  The  default  values  should  be  used  unless  address  
conflicts have been  identified by the  configuration program.  
Detailed information about each option and setting is contained 
in Section 4.2.

5) After the  desired choices  have been selected,  invoke the  
'SAVE CHANGE' function by pressing  the required function key. 
Those choices have now been assigned for the new host adapter.

6) Exit the CHANGE CONFIGURATION menu.

7) Using the  SET CONFIGURATION  menu, press the  proper index  
number to  execute the  BACK UP  CONFIGURATION  function. This  
stores the selected configuration on the floppy for future use.

8) Exit the SET CONFIGURATION menu to the Main Menu and remove 
the copy of the System Reference Diskette.

9) The SCSI Host Adapter/MC is now ready for normal operation. 
The selected operating system can now  be installed and booted 
in accordance with the installation and operating instructions 
for the operating system.

                                  3-4

Section Three                                                    Installation 
------------------------------------------------------------------------------


3.2.4 Common Problems during Installation


Problem                         Resolution

Host adapter cannot be          Review installation steps. Host adapter may be
found by configuration          inserted in slot incorrectly. 
program.                          

Host adapter finds solid SCSI   Review SCSI cable installation. Pin 1 is  
reset.                          likely to be incorrectly oriented. Cable may 
                                be displaced in the SCSI connector.

                                If inline terminators are installed, terminator
                                fuse F1 may need replacement.

Host adapter cannot find        Review peripheralinstallation. Peripheral is
attached peripheral device.     likely to be powered off or to have
                                incorrect SCSI device ID.

Host adapter operates           Review SCSI cable installation and
inconsistently                  configuration. Likely to 
                                have triple or missing terminators.  
                                May have overlapping SCSI device ID.

Other problems.                 Refer to Section 8, Problem Determination

                                Contact technical assistance personnel where
                                the AHA-1640 was purchased.  
 
                                
                                  3-5

Section Four                                  Multithreaded Software Interface 
------------------------------------------------------------------------------

This section  provides  detailed descriptions  of  the AHA-1640  
software interface to the Micro Channel host software operating  
in multithreaded mode. 


4.1 HARDWARE OVERVIEW


There  are  three  groups  of   addressable  hardware  and  one   
unaddressable set of  hardware that  are used  to implement the  
software interface between  the AHA-1640 and  the Micro Channel  
host.

                           [Picture]
                                     
   Figure 4-1. Software Interface for Multithreaded Operation
                                     

The unaddressable hardware is the DMA control logic that allows  
the host adapter access to the host system's memory. The memory  
contains the critical software objects used by the host adapter, 
including the Mailboxes, the Command Control Blocks, and the Data 
areas. The definition of all these software objects is intended  
to be upward  compatible with the  AHA-1540 PC AT  to SCSI host  
adapter, so  that all  driver  programs that  operate  with the  
AHA-1540A/1542A will also  operate with  the AHA-1640.  The DMA  
control logic  on the  host adapter  manages the  Micro Channel  
arbitration and data  transfer handshaking  necessary to access  
these areas of the host memory. All memory addresses used by the 
DMA control logic are real physical memory addresses, not virtual 
addresses. Any conversions  between real  and virtual addresses  
must be done by  the operating system  before the addresses are  
provided to the host adapter. During DMA transfers, the AHA-1640 
becomes a bus master. The DMA logic supports odd or even starting 
addresses and odd  or even data  lengths. All  DMA transfers to  
16-bit MCA addresses are  16-bit unless a  single first or last  
byte  must  be  transferred  to  meet  the  odd  byte  boundary   
requirements. 

                                  4-1

Section Four                                  Multithreaded Software Interface 
------------------------------------------------------------------------------

The POS registers are a set of addressable registers that can be 
managed by the host CPU when the CDSETUP signal is active. These 
registers are  normally  set up  by  the  system initialization  
programming. The register addresses and register bit definitions 
are described in Section 4.2.

The BIOS  EPROM is  available as  a  second set  of addressable  
information. The BIOS  address range is  established by setting  
the correct values in the POS registers at initialization time.  
Once the  system has  been  properly initialized,  the programs  
resident in the BIOS address space will automatically be executed 
when required.  Normally,  they  are  used  only  during single  
threaded operation and in initialization utilities.

The third set of addressable registers defined by the AHA-1640 is 
the I/O  Port interface.  The registers  in this  address space  
provide  a   simple   set  of   sense   information,  controls,   
initialization parameters, and  interrupt information necessary  
for the host  system to manage  the host  adapter. The register  
assignments and functions are defined  in Section 4.3. They are  
intended to be completely compatible with the AHA-1540A/1542A, so 
that all driver programming  designed to run on  the PC AT host  
adapter will operate correctly with the AHA-1640.

In addition to  these addressable  and non-addressable software  
communication paths to the host adapter, the host adapter has an 
interrupt path to the  host to request  services from the host.  
The interrupt uses one of the standard interrupt channels of the 
Micro  Channel.  The  interrupt  is  assigned  by  setting  the   
appropriate bits in the POS Registers.

The SCSI port  is controlled by  the AIC-6250,  an Adaptec SCSI  
protocol device  which  supports  arbitration,  selection,  and  
reselection with a minimum of processor intervention. This VLSI  
device also supports target mode and synchronous SCSI transfers.


4.2 POS REGISTER INTERFACE


The Programmable Option Select registers provide the functions to 
replace the jumpers required by previous host adapters. The POS  
registers provide the information necessary to define the address 
ranges of the BIOS  EPROM and the I/O  Ports. The POS registers  
also establish  certain hardware  states  required by  the host  
adapter during  its  initialization. These  states  include the  
enabling of the host adapter's hardware interface, the enabling  
of arbitration fairness and the enabling of certain SCSI options. 
In addition, a unique ID can be  read from the POS registers to  
identify the installed card as an AHA-1640.

                                  4-2

Section Four                                  Multithreaded Software Interface 
------------------------------------------------------------------------------

POS ADDRESS = 0100H

WRITE: Reserved, Do Not Write  READ: Adapter Identification, LSB = 1FH


 Bit 7                        Bit 7   ID   Bit 7 = 0
 Bit 6                        Bit 6    "   Bit 6 = 0
 Bit 5                        Bit 5    "   Bit 5 = 0
 Bit 4                        Bit 4    "   Bit 4 = 1
 Bit 3                        Bit 3    "   Bit 3 = 1
 Bit 2                        Bit 2    "   Bit 2 = 1
 Bit 1                        Bit 1    "   Bit 1 = 1
 Bit 0                        Bit 0    "   Bit 0 = 1


POS ADDRESS = 0101H

WRITE: Reserved, Do Not Write     READ: Adapter Identification, MSB= 0FH


 Bit 7                        Bit 7   ID   Bit 7 = 0
 Bit 6                        Bit 6    "   Bit 6 = 0
 Bit 5                        Bit 5    "   Bit 5 = 0
 Bit 4                        Bit 4    "   Bit 4 = 0
 Bit 3                        Bit 3    "   Bit 3 = 1
 Bit 2                        Bit 2    "   Bit 2 = 1
 Bit 1                        Bit 1    "   Bit 1 = 1
 Bit 0                        Bit 0    "   Bit 0 = 1

POS ADDRESS = 0102H

WRITE: POS Register 2        READ:  POS Register 2


 Bit 7  BIOS Disable         Bit 7    BIOS Disable          
 Bit 6  Reserved (0)         Bit 6    Reserved (0)
 Bit 5  Reserved (0)         Bit 5    Reserved (0)
 Bit 4  Reserved (0)         Bit 4    Reserved (0)
 Bit 3  Reserved (0)         Bit 3    Reserved (0)
 Bit 2  Reserved (0)         Bit 2    Reserved (0)
 Bit 1  Reserved (0)         Bit 1    Reserved (0)
 Bit 0  AHA-1640 Card Enable Bit 0    AHA-1640 Card Enable

                                  4-3

Section Four                                  Multithreaded Software Interface 
------------------------------------------------------------------------------



POS ADDRESS = 0103H

WRITE:  POS Register 3                 READ:  POS Register 3


 Bit 7   I/O Port Address Bit 3        Bit 7  I/O Port Address Bit 3         
 Bit 6   I/O Port Address Bit 2        Bit 6  I/O Port Address Bit 2
 Bit 5   BIOS Address Bit 16           Bit 5    BIOS Address Bit 16
 Bit 4   BIOS Address Bit 15           Bit 4    BIOS Address Bit 15
 Bit 3   BIOS Address Bit 14           Bit 3    BIOS Address Bit 14
 Bit 2   I/O Port Address Bit 10       Bit 2  I/O Port Address Bit 10
 Bit 1   I/O Port Address Bit 9        Bit 1  I/O Port Address Bit 9
 Bit 0   I/O Port Address Bit 8        Bit 0  I/O Port Address Bit 8

POS ADDRESS = 0104H

WRITE:  POS Register 4                        READ:  POS Register 4


 Bit 7     SCSI Device ID 22                  Bit 7 SCSI Device ID 22         
 Bit 6     SCSI Device ID 21                  Bit 6 SCSI Device ID 21
 Bit 5     SCSI Device ID 20                  Bit 5 SCSI Device ID 20
 Bit 4     SCSI Parity Enable                 Bit 4 SCSI Parity Enable
 Bit 3     SCSI Sync Negotiation              Bit 3 SCSI Sync Negotiation
 Bit 2     Interrupt Select 22                Bit 2 Interrupt Select 22
 Bit 1     Interrupt Select 21                Bit 1 Interrupt Select 21
 Bit 0     Interrupt Select 20                Bit 0 Interrupt Select 20 

POS ADDRESS = 0105H

WRITE:  POS Register 5              READ:  POS Register 5


 Bit 7     Channel Check Active     Bit 7      Channel Check Active         
 Bit 6     Reserved                 Bit 6      Reserved
 Bit 5     Sync Ready (=1)          Bit 5      Sync Ready (=1)
 Bit 4     Fairness Enabled         Bit 4      Fairness Enabled
 Bit 3     Arbitration Level 23     Bit 3      Arbitration Level 23 
 Bit 2     Arbitration Level 22     Bit 2      Arbitration Level 22
 Bit 1     Arbitration Level 21     Bit 1      Arbitration Level 21
 Bit 0     Arbitration Level 20     Bit 0      Arbitration Level 20 



4.2.1 POS Register 0

POS Register 0  contains the  least significant  byte of  the host adapter's  
Adapter Identifier. Since  the identifier is  0F1F, the low  order byte will  
contain 1FH. This register is a read only register.

                                  4-4

Section Four                                  Multithreaded Software Interface 
------------------------------------------------------------------------------

4.2.2 POS Register 1


POS Register  1 contains  the most  significant byte  of the  host adapter's  
Adapter Identifier. The high order byte is 0FH. This register is a read only 
register.

4.2.3 POS Register 2

POS Register 2 is a read/write register. 

BIOS Disable, bit 7  of the register, is  set to zero  by the reset process.  
When zero, the Micro Channel can access the BIOS EPROM using the address space 
specified by POS Register 3. If  the BIOS Disable bit is  1, accesses to the 
EPROM address space will not provide data to the Micro Channel.

Card Enable, bit 0 of the register, is set to zero by the reset process. When 
zero, the Micro Channel can only access  the POS registers of the card using  
the CDSETUP signal and  the appropriate bus protocol.  Any other attempts to  
access information  which would  normally  be in  the  address space  of the  
AHA-1640 will  be ignored  and no  lines will  be driven  back to  the Micro  
Channel. When one,  the Card Enable  bit allows the  AHA-1640 to participate  
normally in Micro Channel interchanges.

4.2.4 POS Register 3

POS Register 3 is a read/write register. The bits in the register define I/O 
Command Port address space and the BIOS address space in the following manner.

                  TABLE 4-1. I/O COMMAND PORT BASE ADDRESS

           POS Register Bit   I/O Command Port Base Address
           2 1 0 7 6
           
           0 0 0 X X          Reserved
           0 0 1 0 0          Port Address = 0130H (Allowed for BIOS) 
           0 0 1 0 1          Port Address = 0134H
           0 0 1 1 X          Reserved
           0 1 0 0 0          Port Address = 0230H (Allowed for BIOS)
           0 1 0 0 1          Port Address = 0234H
           0 1 0 1 X          Reserved
           0 1 1 0 0          Port Address = 0330H (Allowed for BIOS)
           0 1 1 0 1          Port Address = 0334H
           0 1 1 1 X          Reserved
           1 X X X X          Reserved
                             
                                  4-5

Section Four                                  Multithreaded Software Interface 
------------------------------------------------------------------------------

Port Addresses 0130, 0230, and  0330 are recognized by  the BIOS as possible  
host adapters which may have DOS system disks attached. The BIOS examines the 
installed adapters in order from slot 0 on to the maximum installed slot. The 
first host adapter encountered that has one  of the allowable port addresses 
will be selected as the host adapter which may have DOS system disks attached. 
All other host  adapters must have  appropriate device  drivers installed to  
access their attached devices.
                TABLE 4-2. BASE ADDRESS OF BIOS ADDRESS SPACE

           POS Register Bit       BIOS Address Space Base Address
           5 4 3
           
           0 0 0                  Unavailable, Reserved for Video Memory
           0 0 1                  BIOS Base Address = 0C4000H
           0 1 0                  BIOS Base Address = 0C8000H
           0 1 1                  BIOS Base Address = 0CC000H
           1 0 0                  BIOS Base Address = 0D0000H
           1 0 1                  BIOS Base Address = 0D4000H
           1 1 0                  BIOS Base Address = 0D8000H
           1 1 1                  BIOS Base Address = 0DC000H

                                 
4.2.5 POS Register 4

This POS Register is a read/write register.

The SCSI Device Identifier which will be used by the AHA-1640 for both Target 
and Initiator Mode operation is defined by bits 7-5 of the register. The SCSI 
Device Identifier  may take  on any  value from  7 to  0. Every  SCSI device  
attached to the SCSI Bus must have a different identifier.

The SCSI Parity Enable bit is in bit 4  of the register. If the bit is zero, 
SCSI parity is not checked. This is  required for certain systems containing 
older SCSI devices that did not  support the Data Parity bit.  If the bit is 
one, SCSI parity is verified  by the AHA-1640. This is  the normal state for  
modern SCSI systems.

The SCSI Synchronous Negotiation bit is in bit 3 of the register. If the bit 
is zero, the AHA-1640 will not initiate synchronous data transfer negotiation, 
but will respond if an attached SCSI device initiates the negotiation. If the 
bit is  one, the  AHA-1640  will both  initiate  negotiation and  respond to  
negotiation. The AHA-1640 will initiate synchronous  data transfer if it has  
been forced  to abandon  the result  of  previous synchronous  data transfer  
negotiations. Events that will  force the AHA-1640  to abandon those results  
include the host setting the HRST or  SRST bits in I/O Port Control Register  
(Section 4.4.1), another SCSI device transmitting a  Bus Device Reset to the 
host adapter, or a power on reset.

The Interrupt Selection bits define the interrupt  line that will be used to  
communicate with the host microprocessor across  the Micro Channel. The high  
order bit of the interrupt channel selection is not specified by the register 
and is always one. The  result is that the  following selection algorithm is  
used to choose the interrupt line to be used.

                                  4-6

Section Four                                  Multithreaded Software Interface 
------------------------------------------------------------------------------


                   TABLE 4-3. INTERRUPT CHANNEL SELECTION

           POS Register Bit       IRQ Channel to be used
           2  1  0
           
           0  0  0                Reserved 
           0  0  1                IRQ 9 
           0  1  0                IRQ 10 
           0  1  1                IRQ 11 
           1  0  0                IRQ 12 
           1  0  1                Reserved
           1  1  0                IRQ 14
           1  1  1                IRQ 15

                                            
4.2.6 POS Register 5

This POS Register is a read/write register.

The Channel Check Active bit of POS Register  5 is used to indicate that the 
AHA-1640 has detected a hardware failure. All the processor detectable errors 
are presented through  the I/O  port interface  or through  the multitasking  
interface. Channel Check  Active indicates that  the processor  is no longer  
providing inputs to the watch dog timer and is inoperable.

The Channel Check Status bit is not implemented in the AHA-1640.

The Sync Ready bit should always be set to one. 

The Fairness  bit  controls  the Micro  Channel  access  protocol.  When the  
Fairness bit is set to one, all other attached adapters are granted access to 
the Micro Channel  after the  AHA-1640 has  released the  Micro Channel. The  
AHA-1640 can only regain control of the Micro Channel after no other adapters 
request it. When the Fairness bit is  set to zero, the AHA-1640 will release  
the Micro Channel only when a higher priority adapter preempts it.

The Arbitration Level bits indicate the arbitration level that will be used to 
gain access to the  Micro Channel by the  AHA-1640's internal DMA circuitry.  
The host adapter will arbitrate as a Bus Master, and once the arbitration is 
successful, it will manage the required data  transfers until preempted by a 
higher priority Micro Channel function  or until the burst  of data has been  
transferred. Arbitration levels  from 1  to 15  can be  selected by  the POS  
Register.


4.3 PREPARATION OF MICRO CHANNEL DMA HARDWARE


The Micro Channel architecture provides a central DMA controller with one DMA 
channel for each arbitration  level. The BIOS normally  sets up the required  
DMA channels as each operation is requested. The AHA-1640 provides DMA Master 
operation to achieve higher data rates with less contention for Micro Channel 
bandwidth. To allow DMA Master operation, the central DMA controller channel  
corresponding to the AHA-1640's  selected arbitration level  must be masked.  
This is normally  done automatically  by the  on-board BIOS  during the boot  
process so that the host adapter can begin normal Bus Master operation with no 
additional  program  initialization.  If  other  programs  have  incorrectly   
modified the DMA setup, the DMA functions can be restored to the proper masked 
condition using either  the 8237  compatibility mode  or using  DMA extended  
operations. Both mechanisms are shown in the following sections.

                                  4-7

Section Four                                  Multithreaded Software Interface 
------------------------------------------------------------------------------

4.3.1 8237 Compatibility Mode


The DMA controller is  normally initialized to  the correct masked condition  
during the boot process. If the DMA controller must be restored to the masked 
condition, the programmer  can set  the proper  control bits  using the 8237  
compatibility mode.

The DMA controller can be masked using  the Mask Register (Set/Clear) if the  
program has only information about the single DMA channel. If the program has 
information about all the DMA channels, the  Write Mask Register can be used  
to set four of the DMA channels to the correct masked or unmasked state at the 
same time. All  system microprocessor access  to the DMA  controller must be  
with 8-bit I/O instructions.

I/O Register Address   Mask Register 

     000A                Channel 0-3, Mask Register (Set/Clear)
     000F                Channel 0-3, Write Mask Register
     00D4                Channel 4-7, Mask Register (Set/Clear)
     00DE                Channel 4-7, Write Mask Register


Definition of bits for Mask Register (Set/Reset):

Register Bit              Bit Definition

     7-3                  Reserved = 0

      2                   if 0, Clear Mask Bit
                          if 1, Set Mask Bit

     1,0                  if 00, Set/Clear Channel 0 or 4
                          if 01, Set/Clear Channel 1 or 5
                          if 10, Set/Clear Channel 2 or 6
                          if 11, Set/Clear Channel 3 or 7

                                  4-8

Section Four                                  Multithreaded Software Interface 
------------------------------------------------------------------------------

Definition of bits for Write Mask Register:

Register Bit              Bit Definition

     7-4                  Reserved = 0

      3                   if 0, Unmask Channel 3 or 7
                          if 1, Mask Channel 3 or 7

      2                   if 0, Unmask Channel 2 or 6
                          if 1, Mask Channel 2 or 6

      1                   if 0, Unmask Channel 1 or 5
                          if 1, Mask Channel 1 or 5

      0                   if 0, Unmask Channel 0 or 4
                          if 1, Mask Channel 0 or 4
                          
The following operation  is an example  demonstrating how to  mask Channel 2  
using the Mask Register (Set/Clear) Addresses:

    Set I/O Address 000A to the value 06H

The following operation is an example demonstrating how to mask Channel 2 and 
unmask Channels 0, 1, and 3:

    Set I/O Address 000F to the value 02H


4.3.2 DMA Extended Mode


The DMA controller  channels can  be masked using  the extended  mode of DMA  
control. In this case,  I/O Address 0018  is used as a  function register to  
specify the operation to be  performed. I/O Address 001A  is used to provide  
additional parameters for some specified functions. None of the Mask Register 
control functions require the use of I/O Address 001A.

Definition of bits for mask control functions executed by setting I/O Address 
0018:

Register Bit             Bit Definition

     7-4                 Program Command

                          if 9H, Set Specified Mask Bit
                          if AH, Clear Specified Mask Bit
                          if DH, Clear All Mask Bits

     3                   Reserved = 0

     2-0                 Channel number to which Program Command applies

                                  4-9

Section Four                                  Multithreaded Software Interface 
------------------------------------------------------------------------------

The following operation is an example of setting the mask bit for channel 2 to 
1 using the Extended DMA Mode:

    Set I/O Address 0018 to 92H

4.4 I/O PORT INTERFACE


Three port addresses are decoded  in the Micro Channel  I/O address space to  
provide access to the I/O  Port registers. The architecture  of the I/O Port  
registers is fully compatible  with the AHA-1540A/1542A.  The port registers  
form the primary communications channel between the host and the host adapter. 
The I/O ports are 8 bits wide. The  base port is for control and status. The  
second port  passes command  and data  parameters.  The third  port presents  
interrupt information. The port structure is summarized in the following table 
and described in detail in the following sections.

The base  port address  is  established by  the  proper setting  of  the POS  
registers. The base port address may be set to 130H, 134H, 230H, 234H, 330H, 
or 334H.


                      I/O PORT INTERFACE BIT DEFINITION


PORT ADDRESS = BASE + 0

WRITE: Control Register              READ:  Status Register

 Bit 7  Hard Reset (HRST)       Bit 7   Self Test in Progress (STST)
 Bit 6  Soft Reset (SRST)       Bit 6   Internal Diagnostic Failure (DIAGF)
 Bit 5  Interrupt Reset (IRST)  Bit 5   Mailbox  Initialization Required(INIT)
 Bit 4  SCSI Bus Reset (SCRST)  Bit 4   SCSI Host Adapter Idle (IDLE)
 Bit 3  Reserved (0)            Bit 3   Command/Data Out Port Full (CDF)
 Bit 2  Reserved (0)            Bit 2   Data In Port Full (DF)
 Bit 1  Reserved (0)            Bit 1   Reserved ( Undefined )
 Bit 0  Reserved (0)            Bit 0   Invalid H A Command (INVDCMD)


PORT ADDRESS = BASE + 1

WRITE: Command / Data Out              READ: Data In


 Bit 7     Command/Data Out  Bit 7   Bit 7   Data In Bit 7
 Bit 6            "          Bit 6   Bit 6      "    Bit 6
 Bit 5            "          Bit 5   Bit 5      "    Bit 5
 Bit 4            "          Bit 4   Bit 4      "    Bit 4
 Bit 3            "          Bit 3   Bit 3      "    Bit 3
 Bit 2            "          Bit 2   Bit 2      "    Bit 2
 Bit 1            "          Bit 1   Bit 1      "    Bit 1
 Bit 0            "          Bit 0   Bit 0      "    Bit 0

                                 4-10

Section Four                                  Multithreaded Software Interface 
------------------------------------------------------------------------------

PORT ADDRESS = BASE + 2

WRITE: Reserved, do not write        READ: Interrupt Flags

 Bit 7                              Bit 7   Any Interrupt 
 Bit 6                              Bit 6   Reserved
 Bit 5                              Bit 5   Reserved
 Bit 4                              Bit 4   Reserved
 Bit 3                              Bit 3   SCSI Reset Detected (SCRD)
 Bit 2                              Bit 2   HA Command Complete (HACC)
 Bit 1                              Bit 1   MBO Empty (MBOE)
 Bit 0                              Bit 0   MBI Full (MBIF)


4.4.1 Control and Status Port


Writing a one to the bits of the Control Port initiates certain special host 
adapter operations. There is no  requirement to return the  bits to the zero  
state, since they are  reset automatically after  the requested operation is  
initiated. Read operations  to the Status  port address  return host adapter  
status information. 

Base+0 Port, Write: Host Adapter Control Port.

     Bit 7 Hard  Reset (HRST):  The setting  of the  Hard Reset bit  to one  
           forces the host adapter into a state identical to a normal power 
           on state. Diagnostic functions  are executed and  all status for  
           ongoing SCSI operations is lost.  A Reset Condition is generated  
           on the SCSI  bus. While the  reset is being  processed, the Self  
           Testing in Progress bit (Host Adapter Status Port bit 7) is set. 
           When the reset  is complete, that  bit is reset  and the Mailbox  
           Initialization Required bit (Host Adapter Status Port bit 5) and 
           the SCSI Host Adapter Idle bit (Host  Adapter Status Port bit 4) 
           are set, indicating that the  AHA-1640 mailbox structure must be  
           re-initialized and that no other operations are active on the host 
           adapter. See Section 4.5, describing the overall reset structure.
     
     Bit 6 Soft Reset  (SRST): The Soft  Reset bit clears  all ongoing SCSI  
           and host  adapter  commands.  All  Command  Control  Blocks  are  
           abandoned, all queued commands are abandoned, and all Mailbox In 
           and Mailbox Out entries are cleared. No diagnostic functions are 
           executed. No Reset Condition  is generated on  the SCSI bus. The  
           SCSI Host  Adapter Idle  bit (Host  Adapter  Status Port  bit 4)  
           remains off until the reset processing is completed, at which time 
           it is  turned  on  to  indicate  that  normal  operation  may be  
           restarted. All  parameters  established  by  I/O  Port Commands,  
           including transfer speed and selection time-out, remain unchanged 
           by the Soft Reset  processing. See Section  4.5, which describes  
           the overall reset structure.
     
     Bit 5  Interrupt Reset  (IRST):  The setting  of  this bit  clears the  
           interrupt port of  all bits  that have  been set  and resets the  
           interrupt line. The host adapter  prevents interrupts from being  
           lost by setting new interrupts only after previous interrupts have 
           been reset. The host adapter will not raise new interrupts until  
           the previous interrupt information has been accepted and cleared. 
           If an  interrupt needs  to be  presented  while an  interrupt is  
           already active, the host adapter will save the interrupt for later 
           presentation. 
     
                                 4-11

Section Four                                  Multithreaded Software Interface 
------------------------------------------------------------------------------

     Bit 4 SCSI Bus  Reset (SCRST): The  setting of this bit  causes a SCSI  
           Bus Reset to be generated on the SCSI bus. The SCSI Bus Reset is 
           triggered at the time the SCRST bit is set to one and raises the 
           RST line  on the  SCSI Bus  for  the architected  25 microsecond  
           period. The reset is managed as a SCSI Soft Reset and will allow  
           partially completed operations to continue after the reset occurs. 
           See Section 4.5, describing the overall reset structure.
     
 Bits 0-3  Reserved:  Reserved  bits  must  be  set  to  zero to  avoid  
           compatibility problems  with  future extensions  of  the Control  
           Register. 


Base+0 Port, Read: Host Adapter Status Port

     Bit 7 Self Testing  in progress (STST): This  bit, when one, indicates  
           that the  host  adapter  is  performing  self-initialization and  
           internal diagnostics. The  bit is  asserted after  a power-on or  
           hard reset  (Control  Port  Bit 7  HRST  =  1).  When diagnostic  
           operation is complete, the STST bit is  set to zero and bit 5 or  
           bit 6 is set to indicate the successful or unsuccessful completion 
           of the diagnostics. If  bit 7 remains on,  it indicates that the  
           initialization or diagnostic  could not be  completed. The error  
           condition can be determined  as described in  Section 8. In most  
           cases, bit 6  (DIAGF) will be  set to indicate  that an internal  
           diagnostic failure occurred.
     
    Bit 6  Internal  Diagnostic  Failure  (DIAGF):  This  bit,  when  one,  
           indicates that the self-testing process has completed and that an 
           error was detected. The host adapter must be reset by setting the 
           Hard Reset bit (bit 7 of the Control Port) to clear the error. If 
           the AHA-1640 again detects an error, diagnostic utilities must be 
           performed to identify  the error  condition. The  diagnostic LED  
           will present  a  flash code  that  indicates the  nature  of the  
           failure. Section 8 describes the corrective procedures.
     
    Bit 5  Mailbox Initialization  Required  (INIT): This  bit,  when one,  
           indicates that the self-testing process has completed successfully 
           and that the AHA-1640 is ready  for mailbox initialization to be  
           performed. The base memory  address of the  Mailbox area must be  
           established by execution of  the Mailbox Initialization command.  
           After execution of  the Mailbox  Initialization command  and any  
           other desired initialization  operations, the  AHA-1640 is ready  
           for full operation.
     
     Bit 4 SCSI  Host Adapter  Idle (IDLE):  This bit,  when one, indicates  
           that the host adapter is in the idle state. The host adapter has  
           no outstanding I/O Command Port (IOCP) commands or SCSI commands. 
           The host processor must wait for the idle state before executing  
           any IOCP command except the Start SCSI (02) and Enable Mailbox Out 
           Interrupt (05) commands. 
     
     Bit 3 Command /  Data Out Port Full  (CDF): The host  uses the CDF bit  
           to synchronize command and data transfers to the host adapter. An 
           IOCP command byte or an outbound parameter byte can be placed in 
           the Command / Data Out Port when the port is empty, indicated by  
           the CDF bit being zero.  When a byte is placed  in the Command /  
           Data Out Port, the CDF bit is set to one and remains one until the 
           host adapter has obtained  and processed the  byte. When the CDF  
           bit returns to zero,  the next Command or  parameter byte can be  
           placed in the port.
     
                                     4-12

Section Four                                  Multithreaded Software Interface 
------------------------------------------------------------------------------

 Bit 2 Data In Port Full (DF): The  host uses the DF bit to synchronize 
           transfers of data from the host adapter to the host. When the DF  
           bit is set to one, the host adapter has placed a byte in the Data 
           In Port  for  the host  to  remove  and process.  When  the host  
           performs a read to the  Data In Port address, the  DF bit is set  
           back to zero automatically and not set  to one again until a new  
           data byte has been placed in the Data In Port by the host adapter 
           for the host.
     
     Bit 1   Reserved:  This bit is zero.
     
     Bit 0  Invalid  Host  Adapter  Command  (INVDCMD):  The  Invalid  Host  
           Adapter Command  bit is  set  to one  if  an invalid  command or  
           parameter byte was  received in  the Command  / Data  Out Port .  
           After sending a  command byte  or data  byte, the  host software  
           determines that the next byte is ready to send by waiting for the 
           CDF bit to be  reset. If the  command byte or  parameter byte is  
           not valid, the command sequence will instead be terminated by the 
           host adapter. The  host adapter  always terminates  a command by  
           raising the Host  Adapter Command Complete  (HACC) interrupt. If  
           the HACC interrupt is set to one and the INVDCMD bit is not set, 
           the command terminated normally. If the  INVDCMD bit is also set  
           to one, the  command or  parameter bytes  were determined  to be  
           invalid and the command terminated abnormally. The INVDCMD bit is 
           only valid from the time the HACC interrupt is set until the HACC 
           interrupt is reset. The  bit's value is  not predictable until a  
           new HACC interrupt is set for a new IOCP command.
     
     
4.4.2 Command / Data Out and Data In Port


The second I/O port address is used by  the host to write IOCP command bytes 
and accompanying parameter data bytes to the host adapter. It is also used by 
the host  adapter  to send  parameters  back to  the  host to  be  read. The  
Command/Data Out Port is used by the host to send host adapter initialization 
and management commands and  parameters that cannot be  sent by the standard  
Mailbox protocol. Information requested  by the IOCP  commands placed in the  
Command/Data Out Port is returned through the  Data In Port. The host should  
understand the format and number of bytes to be transmitted for each command  
so that extra invalid  bytes are not  passed across the  interface. Bytes in  
addition to  those  required by  the  particular  command are  likely  to be  
interpreted as invalid, although they may instead cause the execution of valid 
commands that were not supposed to be performed. 

The host should only write to the Command/Data Out Port when CDF is zero. This 
allows time for the host adapter to  process a previously written command or  
parameter byte. CDF is automatically set to  one when the host writes to the  
port and is reset to zero  after the host adapter removes  the byte from the 
port.

If an IOCP command needs additional data  bytes, the host waits until CDF is  
zero before writing the additional bytes to the Command/Data Out Port. Just as 
in the command transfer case, each parameter  byte written will set the CDF.  
The host can write additional  data bytes only after CDF  is again zero. The  
HACC interrupt will  indicate when the  command has  terminated, normally or  
abnormally. If INVDCMD is also set, the host adapter found either the command 
or data bytes to be invalid and terminated abnormally.

If an IOCP command  requires data transfer  from the host  adapter, the host  
adapter will place the  data bytes in  the Data In  Port and set  the DF bit  
(Status Port bit 2) to indicate that the requested parameter is ready for the 
host to read. When the host reads  the Data port, DF is automatically reset.  
The host should wait until DF is again set before attempting to transfer the 
next parameter byte. After the last data byte has been transferred, the HACC  
interrupt bit will be set indicating command completion. If the IOCP command 
was invalid, the HACC interrupt  will occur before all  data bytes have been  
transmitted and the INVDCMD bit will be set.

                                 4-13

Section Four                                  Multithreaded Software Interface 
------------------------------------------------------------------------------

4.4.3 Interrupt Flag Port


The Interrupt  Flag Port  contains  bits that  indicate  the reason  that an  
interrupt was provided to the  host from the host  adapter. The host adapter  
uses the interrupt  to notify the  host that  the host adapter  is ready for  
immediate service from the host. The Interrupt Flag Port is a read-only port. 
When an interrupt bit is set  by the host adapter to  indicate that the host 
should respond, the Any Interrupt  bit and the interrupt  line are both also  
set. When the host begins to examine the returned registers and mailboxes to  
determine the cause of the interrupt and to perform the operations needed to  
service the interrupt, the host  will first read the  Interrupt Flag Port to  
record which  interrupts must  be  serviced. The  host  will then  clear the  
interrupts by setting the IRST  bit (Host Adapter Control  Port bit 5). Once  
the host adapter has set the Interrupt Flag Port to indicate that one or more 
interrupts must be processed, it will not set the interrupt bits again until  
after the Interrupt Flag  Port has been  reset. This prevents  the host from  
accidentally resetting any interrupts that have been set after it has read the 
Interrupt Flag Port.  Other reset operations  will also  reset the Interrupt  
Flag Port and the interrupt  line, including the Hard  Reset bit (HRST), the  
Soft Reset bit (SRST), and the power on reset.

Base+2 Port, Read only:  Interrupt Flag Port

    Bit  7  Any  Interrupt:  This  bit,   when  one,  indicates  that  the   
            interrupt to the host has  been established. The actual identity  
            of the interrupting condition is provided in bits 0 to 3.
     
    Bit 6   Reserved:     Returned as zero.
     
    Bit 5   Reserved:     Returned as zero.
     
    Bit 4   Reserved:     Returned as zero.
     
    Bit 3  SCSI  Reset  Detected (SCRD):  This  bit,  when  one, indicates  
           that a SCSI  Reset has  been received on  the SCSI  bus. The Any  
           Interrupt bit and the Micro Channel  interrupt will also be set.  
           The host adapter supports SCSI Soft Reset (see Section 4.5). Any  
           ongoing target  or initiator  activities will  continue normally  
           after first  clearing the  SCSI bus.  In  some rare  cases, host  
           intervention will be required to restart a SCSI command that was  
           aborted by the  reset operation. The  host can  convert the SCSI  
           Soft Reset to a SCSI Hard Reset  by setting the Control Register 
           Soft Reset (Bit 6) to one, clearing all ongoing operations in the 
           host adapter. In  this case,  the host  must recognize  that any  
           operations not yet  completed will  never be  completed and must  
           perform appropriate error recovery  operations. See Section 4.5,  
           which describes the overall reset protocol.  The SCRD bit is not  
           set for host initiated SCSI Reset conditions caused by the setting 
           of the HRST bit or the SCRST bit, since the host is already aware 
           of the actions it has  requested and does not  need to have them  
           indicated again. If any interrupt flags have not yet been cleared 
           by the  host, no  new interrupts,  including  the SCRD,  will be  
           generated until the interrupts are reset.
     
     Bit 2  Host  Adapter  Command Complete  (HACC):  This  bit,  when one,  
           indicates that an IOCP  command has been  completed, normally or  
           abnormally. The Any Interrupt bit and the Micro Channel interrupt 
           will also be set. If the command was completed normally, only the 
           HACC bit will be on. If the  command was completed abnormally or 
           was aborted before it was completed, the HACC bit will be one and 
           the Invalid Command Bit (Status Register bit 5) will also be one. 
    
                                     4-14

Section Four                                  Multithreaded Software Interface 
------------------------------------------------------------------------------

           During parameter transfers to or from the host adapter, the HACC  
           bit should be examined to verify that the command is still being 
           processed and has  not been  ended abnormally.  If any interrupt  
           flags have not yet been cleared by  the host, no new interrupts, 
           including the HACC, will  be generated until  the interrupts are  
           reset.
     
     Bit 1  Mailbox Out  Available (MBOA):  This  bit, when  one, indicates  
           that an outbound Mailbox  entry is now available  for use by the  
           host. The Any Interrupt bit and the Micro Channel interrupt will  
           also be set.  Most operating systems  will choose  to leave this  
           interrupt disabled to avoid the  generation of extra interrupts.  
           The host adapter will normally empty  Mailbox Out entries to its  
           local RAM so rapidly that round-robin filling of the Mailbox Out  
           entries will assure that a Mailbox Out entry will already be empty 
           by the time that the host is ready to fill it again.
     
           If the host finds that all Mailbox Out entries are full, it can  
           enable the Mailbox Out Available interrupt by executing an Enable 
           Mailbox Out Interrupt command through  the I/O Command Port. The  
           Enable Mailbox Out Interrupt command is  one of the two commands  
           that can be executed  without waiting for the  IDLE state of the  
           host adapter. As soon as any Mailbox Out entry is cleared by the  
           host adapter, an MBOA interrupt will be generated to indicate to  
           the host that  an MBO entry  is available. An  MBOA interrupt is  
           generated after that each time a Mailbox Out entry is cleared by 
           the host adapter until an Enable Mailbox Out Interrupt command is 
           executed to force the reporting of MBOA interrupts to be disabled. 
           If any interrupt flags have not yet been cleared by the host, no  
           new interrupts, including the MBOA  interrupt, will be generated  
           until the interrupts are reset.
     
     Bit 0 Mailbox In  Full (MBIF): This  bit, when one,  indicates that an  
           entry has been placed by the host adapter in the Mailbox In. The  
           interrupt should  be  reset  as soon  as  possible  so  that any  
           subsequent interrupts  can  be detected.  The  host  adapter may  
           return information in other Mailbox In entries, so the host should 
           check the  next  entry to  determine  if  more than  one  set of  
           information has  been provided.  The MBI  entries are  filled in  
           round-robin order, so the host should  simply check the next MBI  
           entry after the last one that was found when a new MBIF interrupt 
           occurs.
     
           Once an interrupt of any  kind has been  set, a new interrupt   
           will not be set until the  original interrupt flags are cleared.  
           If an MBIF interrupt is set and other Mailbox In entries are made 
           before the interrupt  is cleared,  then all  the entries  can be  
           scanned as found. The new MBIF interrupt will not be generated if 
           the old  interrupts  have  not  yet  been  cleared.  Thus  it is  
           important to clear the MBIF interrupt  promptly so that the host  
           can complete the servicing of MBI entries and the MBIF interrupt  
           flag can then be  re-examined to determine  if other MBI entries  
           have been generated after those that have already been serviced.
     
     
4.5 RESET OVERVIEW


The reset  functions provided  by the  AHA-1640 are  extensive to  allow the  
fullest flexibility and architectural consistency, both with SCSI and with the 
Micro Channel.

                                 4-15

Section Four                                  Multithreaded Software Interface 
------------------------------------------------------------------------------

4.5.1 Hard Reset operations


Resets may be generated by the hardware  through two mechanisms. The CHRESET 
signal from the Micro Channel  is generated by the system  board to reset or  
initialize all installed adapters upon power on or during a low line voltage  
condition. The  system  can also  activate  this signal  under  host program  
control. In addition to the CHRESET signal, the setting of the HRST bit (bit 
7 of  the Host  Adapter Control  Port) will  force a  hardware reset  to the  
AHA-1640. Regardless of the source, a Hard Reset forces the following actions 
on the AHA-1640.

ù All  internal  registers  of  the AHA-1640  are  returned  to  their reset  
  condition.
ù The  host adapter's  microprocessor returns  all internal  information and  
  parameters to their initial state.
ù The host adapter's microprocessor reloads the microprocessor program RAM.
ù The host adapter performs all required internal diagnostics.
ù A standard SCSI  Reset condition is  generated to all  other attached SCSI  
  devices.
     
During the Hard Reset process, the AHA-1640 will indicate to the attached host 
that self-testing is in process by raising  the STST bit in the Host Adapter  
Status Port. After  the Hard  Reset process  is complete,  the AHA-1640 will  
indicate that initialization parameters are required from the host by raising 
the INIT  bit in  the Host  Adapter  Status Port.  Since the  host adapter's  
microprocessor must initialize the read only POS  registers, the read of the 
host adapter's card ID cannot be executed until several microseconds after the 
Hard Reset condition  has ended and  firmware initialization  has begun. The  
system initialization functions take long enough so that the host adapter has 
plenty of time to initialize the host adapter card ID.


4.5.2 SCSI Reset Operations


The SCSI Reset condition is defined in the SCSI Standard, X3.131-1986, Section 
5.2.2. A SCSI Reset condition may  be forced by any SCSI  device on the bus. 
The condition is forced by the assertion of the SCSI Reset signal.

The AHA-1640 has three mechanisms which may force a SCSI Reset condition. The 
SCSI Reset condition may be  invoked from the host  software if the software  
sets the SCRST bit (Bit 4  of the Host Adapter Control  Port). In this case, 
the normal SCSI Reset operations will be performed by the Host Adapter and the 
SCSI Reset signal will be asserted  on the SCSI bus. In  this case, the SCRD 
bit (Interrupt Flag Port bit 3) will not be set, since the host itself caused 
the reset.

The SCSI  Reset condition  may be  invoked by  the AHA-1640  as part  of the  
recovery mechanism  for a  bus  phase error.  Bus  phase errors  may include  
detection of  an  invalid  information transfer  phase  or  detection  of an  
impossible phase  sequence (Command  Phase after  a Data  Phase in  the same  
command). In this case,  the normal SCSI Reset  operations will be performed  
and the SCSI Reset signal will be asserted on the SCSI bus. In addition, the 
SCRD bit (Interrupt  Flag Port bit  3) will be  set to indicate  to the host  
computer that a SCSI Reset  condition occurred. The setting  of the SCRD bit  
also causes  the Any  Interrupt  bit (Interrupt  Flag  Port bit  7)  and the  
appropriate Micro Channel interrupt to be presented.

The SCSI Reset condition may be invoked by another attached SCSI device to the 
AHA-1640 as part of the other  device's recovery mechanism or initialization  
procedure. In this case, the normal SCSI Reset operations will be performed. 
In addition, the SCRD bit (Interrupt Flag Port bit 3) will be set to indicate 
to the host computer that a SCSI Reset condition occurred. The setting of the 
SCRD bit also causes the Any Interrupt bit (Interrupt Flag Port bit 7) and the 
appropriate Micro Channel interrupt to be presented.

                                 4-16

Section Four                                  Multithreaded Software Interface 
------------------------------------------------------------------------------

4.5.2.1 SCSI "Soft" Reset Option
     
     
The SCSI standard indicates two optional methods of handling the normal SCSI 
Reset operations. The AHA-1640 implements the "Soft" Reset Option, described 
in Section 5.2.2.2  of the  SCSI specification.  The "Soft"  Reset Option is  
designed to allow a SCSI Reset signal to correctly clear the SCSI bus, but to 
allow ongoing system operations to continue without any major interruptions. 
When the SCSI Reset occurs, any activity on the SCSI bus is immediately halted 
and all bus lines are cleared from  the bus. After the Reset condition ends,  
any operations in progress are again allowed to start up in the normal manner. 
No status or pointer information is destroyed. All disconnected commands are  
allowed to reselect  and continue  in the  normal manner.  This "Soft" Reset  
function allows a  multiple initiator system  to use reset  to clear certain  
types of bus failures without damaging ongoing tasks from any initiator.

The SCSI "Soft" Reset  option is useful in  multitasking systems that cannot  
tolerate the overhead of a complex reconfiguration and reinitialization after 
a normal  reset  operation. For  the  SCSI  "Soft" Reset  option  to operate  
correctly, all SCSI devices that communicate on the SCSI bus must support the 
"Soft" Reset option. If any SCSI devices support the "Hard" Reset option, it  
is likely that operations will be terminated without warning, and the system 
will have to time out and monitor the requirement to restart some activities.
     
     
4.5.2.2 SCSI "Hard" Reset Option


The "Hard" Reset  Option is designed  to restore all  attached SCSI devices,  
including both hosts and peripheral devices, to  their power on reset state. 
All system activities that  have not been recorded  on a non-volatile memory  
device or through another SCSI path are completely lost and must be restarted. 
The system must be  completely re-initialized. For  certain types of systems  
that  frequently  do  back-up  or   check  point  their  transactions,  that   
re-initialize quickly and easily, or that infrequently do resets, the "Hard"  
Reset Option is appropriate. The AHA-1640 responds to a SCSI Reset Condition 
by executing only the "Soft" Reset Option, but it notifies the host whenever a 
SCSI Reset condition has been established by causing an interrupt to the host. 
The host then has the option of converting the "Soft" Reset to a "Hard" Reset 
by forcing the host adapter to clear all the ongoing operations and return to 
its initial state. The host requests this by  raising the SRST bit (bit 6 of 
the Host Adapter Control Port). The host  must raise the SRST bit within 300  
microseconds to disable the restarting of operations according to the rules of 
"Soft" Reset. The raising of the SRST bit causes the host adapter to abandon 
all CCB's and  prepare itself to  begin accepting new  instructions from the  
host.  No  secondary   SCSI  Reset   signals  are   activated.  The  Mailbox   
initialization and all normal  SCSI initial conditions are  not reset by the  
SRST bit, so that system rebooting can be completed changing only that minimum 
set of parameters necessary to restart the system. Of course the system still 
has the right at any time that the IDLE bit (bit 4 of the Host Adapter Status 
Port) is on to execute any of the IOCP commands and modify the Mailbox Address 
or the SCSI initial conditions.

If the host requires that the SCSI be reset according to the SCSI "Hard" Reset 
option, the host  raises both the  SRST and  the SCSIRST bits  with the same  
instruction. The host adapter  will then set  a SCSI Reset  Condition on the  
SCSI Bus and clear all its CCB and status information, thus performing a SCSI 
"Hard" Reset with a single load to the Host Adapter Control Port.

                                 4-17

Section Four                                  Multithreaded Software Interface 
------------------------------------------------------------------------------

4.6 I/O COMMAND PORT (IOCP) COMMAND SET


The AHA-1640 supports  low-level types of  commands through  the I/O Command  
Port. The commands support host adapter initialization, performance parameter 
adjustment, and special commands used by the BIOS while emulating the standard 
hard disk controller. The IOCP command structure is fully compatible with the 
AHA-1540. IOCP commands are executed by placing the appropriate command byte  
in the Command/Data Out port. Parameters are then transferred out to the host 
adapter or into the host to provide the information necessary to complete the 
command. When the  command is completed,  either normally  or abnormally, an  
HACC interrupt is  generated in  most cases. Most  IOCP commands  can not be  
issued unless the host adapter is IDLE. 

Below is a table of the IOCP command operation codes.

         TABLE 4-4. I/O Command Port (IOCP) command Operation Codes

           
           Operation Code               Operation

                 00               No Operation
                 01               Mailbox Initialization
                 02               Start SCSI Command *
                 03               Start Micro Channel BIOS Command
                 04               Adapter Inquiry
                 05               Enable Mailbox Out Available Interrupt *
                 06               Set SCSI Selection Time out
                 07               Set Bus-On Time
                 08               Set Bus-Off Time
                 09               Set Transfer Speed
                 0A               Return Installed Devices
                 0B               Return Configuration Data
                 0C               Enable Target Mode
                 1A               Write Channel 2 Buffer
                 1B               Read Channel 2 Buffer
                 1C               Write Adapter FIFO Buffer
                 1D               Read Adapter FIFO Buffer
                 1F               ECHO Command Data

                                             
All IOCP commands  except Start SCSI  (02) and  Enable Mailbox-Out Available  
Interrupt (05) must be executed only when the IDLE bit (Status bit 4) is one. 
Many commands require additional parameter bytes which are then written to the 
Command / Data Out I/O port  (base + 1). Before each  byte is written by the  
host to the host adapter, the host must verify that the CDF bit (Status bit 3) 
is zero,  indicating that  the command  port  is ready  for another  byte of  
information. Some commands require information bytes to be returned from the  
host adapter to the host. In this case, the host monitors the DF bit (Status 
bit 2) to determine when the host adapter has placed a byte in the Data In I/O 
port for the host to read.  The DF bit is reset  automatically when the host 
reads the byte.

                                 4-18

Section Four                                  Multithreaded Software Interface 
------------------------------------------------------------------------------

4.6.1 No Operation (Operation Code 00)


No host adapter action  is taken, but  the HACC interrupt  is set indicating  
command completion. No additional information bytes are exchanged.


4.6.2 Mailbox Initialization (Operation Code 01)


This command is used to specify the  number of mailbox locations used by the  
host adapter and to specify the base memory location of the mailbox area. The 
host adapter requires  that four bytes  of outbound data  follow the command  
byte. The definition of those four bytes is shown below.

           00         Mailbox count    (>0)
           01      Mailbox address     (MSB)
           02      Mailbox address
           03      Mailbox address     (LSB)


     Byte  0      Mailbox Count:  The Mailbox count must be greater than zero. 
     
     Byte 1,2,3   Mailbox Address:  The  Mailbox address  specifies the first  
                                    byte of the Mailbox area. Byte 1 is      
                                    the most significant byte.
     
When the Mailbox Initialization command and parameters are received, the host 
adapter will then assume that a number of Mailbox Out entries and a number of 
Mailbox In entries  will be assigned  beginning at the  Mailbox address. The  
Mailbox count gives the number of each kind of mailbox entry to be used. The 
total number of bytes reserved for the  Mailbox area will be eight times the  
Mailbox count. 

At command completion, HACC will be set to one and INIT will be reset to zero. 
HACC will be reset as specified by Section 4.3.3.


4.6.3 Start SCSI Command (Operation Code 02)


This command indicates that the host has made at least one Mailbox Out entry 
and that the host adapter should begin  to scan for active MBO entries. Once  
scanning has  been started,  it continues  until all  MBO entries  have been  
serviced, either by  beginning the requested  operations or  by queueing the  
activities for  later  execution. Since  it  is  not easy  for  the  host to  
determine that scanning is still taking place, the host should normally issue 
this command  every time  a Mailbox  Out  is filled.  This command  does not  
require additional data bytes. To avoid  unnecessary interrupts, HACC is NOT  
set after command completion. HACC will be set with INVDCMD if the mailbox was 
not yet initialized.


4.6.4 Start BIOS Command (Operation Code 03)


This command is used by the Adaptec BIOS to communicate with the host adapter 
firmware. The command is  not available for  use by programs  other than the  
Adaptec BIOS.

                                 4-19

Section Four                                  Multithreaded Software Interface 
------------------------------------------------------------------------------


                [This page intentionally left blank]



                                 4-20

Section Four                                  Multithreaded Software Interface 
------------------------------------------------------------------------------

4.6.5 Adapter Inquiry (Operation Code 04)


After receiving this  command, the host  adapter returns four  bytes of data  
describing the host  adapter firmware  revision level.  After completing the  
transfer of  the four  bytes  of inbound  data,  the HACC  interrupt  is set  
indicating normal  command  completion.  The  bytes  contain  the  following  
information:


           00      Board Identification
           01      Special Options Identification
           02      Hardware Revision Level
           03      Firmware Revision (ASCII)

                                  
     Byte 0  Board ID:             The value in this byte allows software 
                                   supported on both the PC AT and on the 
                                   Micro Channel to distinguish the type of 
                                   supporting host adapter.
             
             Value                 Meaning
             
             00H                   Board is an AHA-1540
             41H ('A' ASCII)       Board is an AHA-1540A
             42H ('B' ASCII)       Board is an AHA-1640
             All Others            Reserved
     
     Byte 1  Special Options ID:   The value in this byte indicates what 
                                   special options are supported on the 
                                   AHA-1640 host adapter. Other host 
                                   adapters use other values in this byte.
     
             Value                 Meaning
             
             41H ('A' ASCII)       Board is standard model
             All Others            Reserved 
                                   
     
     
     Byte 2  Hardware Revision:    The value in this byte indicates what 
                                   hardware level of the AHA-1640 board is 
                                   provided. Other host adapters use other 
                                   values in this byte.
     
             Value                 Meaning
     
             31H ('1' ASCII)       Engineering Prototype
             32H ('2' ASCII)       Early Production / Pilot Production
             41H ('A' ASCII)       Initial Standard Production Level
             All Others            Reserved for future levels 
                                   
     
     Byte 3  Firmware Revision:    This value indicates an ASCII value from 
                                   0-9,A-Z that indicates the firmware 
                                   revision installed in the AHA-1640.
     
After completing this command, HACC will be asserted, indicating normal 
completion. 

                                 4-21

Section Four                                  Multithreaded Software Interface 
------------------------------------------------------------------------------

4.6.6 Enable Mailbox-Out Available Interrupt (Operation Code 05)


The Enable Mailbox Out Available Interrupt  command specifies that a Mailbox  
Out Available Interrupt should be generated whenever a Mailbox Out entry has 
been cleared by the host adapter. One byte of outbound data is transmitted to 
indicate whether the interrupt should be enabled or disabled.

 Byte 0 Enable/Disable Parameter:  The Enable/Disable parameter byte must be 
                                   either 00H or 01H. If the Enable/Disable 
                                   parameter byte is 00H, the Mailbox Out 
                                   Available interrupt is not returned. If 
                                   the Enable/Disable parameter byte is 01H, 
                                   the Mailbox Out Available interrupt is 
                                   returned as soon as a Mailbox Out has been 
                                   cleared by the host adapter. 

After completing this command, HACC will NOT be asserted to avoid generating 
additional interrupts. If the data byte is neither 00 nor 01, INVDCMD will be 
asserted indicating  an invalid  command. In  this case,  HACC will  also be  
asserted.

The Mailbox Out Available interrupt  is normally intended to  be used by the  
host as an indicator that a Mailbox Out entry is available after all entries 
have been found full by the  host. If used in other  ways, the interrupt may 
generate a large number of relatively useless interrupt handling activities.


4.6.7 Set SCSI Selection Time-out (Operation Code 06)


     This command sets the SCSI selection time-out value. The SCSI Selection 
     time-out value is used to determine whether or not a SCSI selection was 
     successful. If the SCSI BSY signal is not returned within the specified 
     time-out value, the  selection will  be terminated  and an appropriate  
     error message posted with the returned  CCB. This command expects four  
     outbound data bytes to be provided as defined below:

           00         Enable/Disable Selection Time-Out 
           01      Reserved (00)
           02      Time Out Value      (MSB)
           03      Time Out Value      (LSB)


     Byte 0  Enable/Disable Selection Time-Out: This parameter byte specifies 
                                   whether or not the Selection Time-out will 
                                   be used. If the byte is set to 00H, no 
                                   time-out will be performed. If the byte is 
                                   set to 01H, the time specified in bytes 02
                                   and 03 will be used as the Selection Time-
                                   Out by the SCSI. The default value 
                                   established by the reset process is 01H, 
                                   indicating the time out is enabled.
     
     Byte 1     Reserved:          This byte must be zero.
     
     Byte 2,3   Time Out Value:    This two-byte value specifies the time in 
                                   milliseconds that will be used for the 
                                   Selection Time-Out. The default value is 
                                   250 milliseconds. 
                                   
                                 4-22

Section Four                                  Multithreaded Software Interface 
------------------------------------------------------------------------------

After completing  this command,  HACC  will be  asserted,  indicating normal  
completion. INVDCMD will be asserted if the data byte 0 is neither 00 nor 01 
or if byte 1 is not zero, indicating an invalid command. 


4.6.8 Set Bus-On Time (Operation Code 07)


        Data Byte 0 -- Bus-On Time (not examined by AHA-1640)

This command performs no operation  and is accepted by  the AHA-1640 only to  
provide software compatibility with the AHA-1540A/1542A. After completing this 
command, HACC will  be asserted  indicating normal  completion. This command  
controlled the data transfer  burst time on the  AHA-1540A/1542A, but is not  
used on the AHA-1640 because the actual bus activity on the Micro Channel is 
controlled by the FIFO  management protocol of  the AHA-1640 and  by the bus  
arbitration and fairness protocols. 


4.6.9 Set Bus-Off Time (Operation Code 08)


        Data Byte 0 -- Bus-Off Time (not examined by AHA-1640)

This command performs no operation  and is accepted by  the AHA-1640 only to  
provide software compatibility with the AHA-1540A/1542A. After completing this 
command, HACC will  be asserted  indicating normal  completion. This command  
controlled the period between data transfer burst on the AHA-1540A/1542A, but 
is not used  on the AHA-1640  because the  actual bus activity  on the Micro  
Channel is controlled by the FIFO management protocol of the AHA-1640 and by  
the bus arbitration and fairness protocols. 


4.6.10 Set Transfer Speed (Operation Code 09)


The Micro Channel timing  is fully specified.  It is expected  that all well  
behaved Micro  Channel  attached  devices  will  provide  appropriate timing  
signals, including CHRDY. The Set Transfer Speed is not required for standard 
Micro Channel  implementations  and  is included  only  to  provide software  
compatibility with the AHA-1540A/1542A. It may also be required to establish  
special timings for special high speed versions of the Micro Channel.

One data byte follows this command. It performs no function.

        Data Byte 0   -- Not Examined

After completing this command HACC is set indicating normal completion. 


                                 4-23

Section Four                                  Multithreaded Software Interface 
------------------------------------------------------------------------------

4.6.11 Return Installed Devices (Operation Code 0A)


This command returns information about which  SCSI Targets and Logical Units  
(LUs) are installed on the  SCSI bus. The host adapter  issues the SCSI Test  
Unit Ready command  to each target/LUN  combination and  reports the results  
using eight bytes of data returned through the Data In Register. This command 
can be executed once after power-up or any reset. A bit having a value of one 
indicates that  the  associated LU  is  installed  and ready.  Each  byte is  
associated with the corresponding  target. Each bit within  a target byte is  
associated with a particular Logical Unit, bit 7 indicating the status of LU 7 
and so forth.

After receiving  this  command,  the host  adapter  returns  eight  bytes of  
information which specify the installed configuration as shown in Table 4-5.

                                 TABLE 4-5.
                                            
     Byte 0     Target 0 Configuration:
                 
                Bit 7              LU 7 Installed
                Bit 6              LU 6 Installed
                Bit 5              LU 5 Installed
                Bit 4              LU 4 Installed
                Bit 3              LU 3 Installed
                Bit 2              LU 2 Installed
                Bit 1              LU 1 Installed
                Bit 0              LU 0 Installed
                                   
     Byte 1     Target 1 Configuration
     Byte 2     Target 2 Configuration
     Byte 3     Target 3 Configuration
     Byte 4     Target 4 Configuration
     Byte 5     Target 5 Configuration
     Byte 6     Target 6 Configuration
     Byte 7     Target 7 Configuration
     
                                               
The byte associated with the SCSI Device Identifier of the host adapter will  
always be zero. After completing the information transfer, the HACC bit will 
be set to indicate normal completion.


                                 4-24

Section Four                                  Multithreaded Software Interface 
------------------------------------------------------------------------------

4.6.12 Return Configuration Data (Operation Code 0B)


The DMA arbitration priority, the Interrupt channel,  and the SCSI ID of the  
adapter are returned by this command. All three of these values are normally  
set through the POS registers, but for compatibility with the AHA-1540A/1542A, 
they can also be read back using this command. The three bytes of information 
are returned in the following format:

     Byte 0     DMA Arbitration Priority:
                
                Byte is reserved. Value returned is 00h.
     
     Byte 1     Interrupt Channel:
     
                Bit 7              Reserved (0)
                Bit 6              Interrupt channel 15
                Bit 5              Interrupt channel 14
                Bit 4              Reserved (0)
                Bit 3              Interrupt channel 12
                Bit 2              Interrupt channel 11
                Bit 1              Interrupt channel 10
                Bit 0              Interrupt channel 9
     
     Byte 2     SCSI Identifier
     
                Bits 7-3           Reserved (0)
                Bits 2-0           Binary value of SCSI Identifier

After completing this command, HACC will be set indicating normal completion. 
Note  that  the  DMA   channel  information  previously   available  in  the   
AHA-1540A/1542A in  information byte  0 is  now available  to the  host only  
through the POS registers.

                                 4-25

Section Four                                  Multithreaded Software Interface 
------------------------------------------------------------------------------

4.6.13 Enable Target Mode Command

A special host  adapter command (0C)  enables and disables  target mode. The  
host adapter  requires that  two bytes  of  outbound information  follow the  
command byte. The information bytes contain the following information:

Byte 0 Enable/Disable Target Mode: This parameter specifies which operating 
                                   modes the host adapter will use. If the 
                                   byte is set to 00H, the AHA-1640 will 
                                   operate only in Initiator Mode. If the 
                                   byte is set to 01H, the host adapter will 
                                   operate both as an initiator and as a 
                                   Processor type Target SCSI Device. Any 
                                   other value is invalid. The default value 
                                   after a Hard Reset, Soft Reset, or Power 
                                   On Reset is 00H (Initiator only).
     
Byte 1 Logical Unit Mask:          This parameter byte contains an 8-bit 
                                   bit-significant mask indicating the 
                                   Logical Units which will respond in Target 
                                   Mode. Bit 7 corresponds to LU 7, and so 
                                   forth. If the bit is one, the 
                                   corresponding LU will be treated as 
                                   installed. If the bit is zero, the LU 
                                   will be treated as not installed.
     
If the AHA-1640 does  not have the  Target Mode feature  installed, the host  
adapter will indicate an invalid host adapter command. If an attempt is made  
to change from  target mode  while there  are still  target mode  CCBs being  
processed by the host  adapter, the host  adapter will post  an invalid host  
adapter command indication. 

If the command  disables Target  Mode, the  Logical Unit  Mask byte  will be  
ignored. If the command enables Target Mode, the Logical Unit Mask byte must  
contain at least one  bit, indicating the  presence of at  least one Logical  
Unit.
 
The SCSI INQUIRY command will provide an indication to other initiators that 
the Logical Unit  is installed or  not installed  in byte 1  of the returned  
inquiry data.

If target mode  is not  enabled, the  host adapter  will behave on  the SCSI  
interface as if it were an ordinary SCSI initiator. Any attempt to select the 
host adapter will result in a SCSI selection time- out. Any Reset Operation,  
including Soft Reset, Hard Reset, and Power-On Reset will return the AHA-1640 
Target Mode to the disabled state. SCSI Resets, generated either by the host  
or by other SCSI Devices, will not change the previously established enabled 
or disabled state of Target Mode.


4.6.14 Return Setup Data (Operation Code 0D)


This command returns information  describing the setup  of the host adapter.  
The information returned reflects either the values supplied by previous host 
adapter commands or default  values. The command is  followed by an outbound  
data transfer and an inbound  data transfer. The outbound  transfer is a one  
byte parameter indicating the length of  the required inbound data transfer.  
The inbound data  transfer contains  from zero  to 255  bytes of information  
describing the setup of the host adapter. 

                                 4-26

Section Four                                  Multithreaded Software Interface 
------------------------------------------------------------------------------

 Outbound Data Byte:

     Byte 0     Data In Length:    The number of data bytes requested can be 
                                   from 0 to 255. A value of zero will be 
                                   accepted and no data will be returned.
     
Inbound Data Summary:
     

           00      SDT and Parity Status
           01      Reserved (00)
           02      Reserved (00)
           03      Reserved (00)
           04      Number of Mailboxes
           05      Mailbox Address (MSB)
           06      Mailbox Address
           07      Mailbox Address (LSB)
           08-FF   Reserved (00)

Inbound Data Bit Assignments:

     Byte 0     SDT and Parity Status: 
                                   
                
                Bit                Meaning
                
                  0                If this bit is zero, Synchronous Data 
                                   Transfer negotiation will not be initiated 
                                   by the host adapter, but will be responded 
                                   to if requested by an attached SCSI 
                                   Device. If the bit is one, Synchronous 
                                   Data Transfer negotiation will be 
                                   initiated by the host adapter under those 
                                   conditions which require such negotiation. 
                                   The state is set from POS Register 104, 
                                   bit 3.
                   
                  1                If this bit is zero, parity checking on 
                                   inbound SCSI transfers has been disabled. 
                                   If this bit is one, parity checking on 
                                   inbound SCSI transfers is enabled. The 
                                   state is set from POS Register 104, bit 4.
     
     Byte 1     Reserved:          This byte will always be zero.
     
     Byte 2     Bus On Time:       This byte will always be set to 00H. The 
                                   AHA-1540A/1542A would normally find 0FH as 
                                   the default in this location. 
     
     Byte 3     Bus Off Time:      This byte will always be set to 00H for 
                                   compatibility with the AHA-1540A/1542A.
     
     Byte 4     Number of          The number of Mailboxes established by    
                                   previous Mailboxes:   
                                   Mailbox Initialization command will be 
                                   returned in this byte. This number will be
                                   00H if the Mailbox Initialization command
                                   has not yet been successfully completed.
     
                                 4-27

Section Four                                  Multithreaded Software Interface 
------------------------------------------------------------------------------

     Byte 5-7   Mailbox Address:   The base address of the Mailbox area 
                                   established by a previous Mailbox 
                                   Initialization command will be returned in 
                                   this byte. The Most Significant byte is 
                                   byte 5. These bytes have no meaning if 
                                   Mailbox Initialization has not yet been 
                                   successfully completed.

If the command completes normally, the HACC interrupt will be set to one. If 
the Mailbox area has  not been properly  initialized, all 8  bytes are still  
requested by the host. If byte 4, the Number of Mailboxes, is zero, bytes 5-7 
must be ignored.
 

4.6.15 Write Channel 2 Buffer (Operation Code 1A)


After receiving  this  command,  the  host  adapter  expects  three outbound  
information bytes to be  transferred which point  to an area of  64 bytes in  
system RAM. The area  pointed to will  be transferred to  the host adapter's  
Channel 2 Buffer  using the host  adapter's DMA  circuitry. After completing  
the transfer of  the 64  bytes from  the indicated  buffer area to  the host  
adapter, the HACC interrupt  will be set  indicating normal completion. This  
command is used in conjunction with the Read Channel 2 Buffer command for host 
adapter diagnostics.

     Byte 0     Buffer area address, Most significant byte
     Byte 1     Buffer area address
     Byte 2     Buffer area address, Least significant byte 
                                   


4.6.16 Read Channel 2 Buffer (Operation Code 1B)


After receiving  this  command,  the  host  adapter  expects  three outbound  
information bytes to be  transferred which point  to an area of  64 bytes in  
system RAM. The area pointed to will be used as a buffer to receive 64 bytes  
of information transferred from  the host adapter's Channel  2 Buffer to the  
host's memory using the  host adapter's DMA  circuitry. After completing the  
transfer of the  64 bytes from  the Channel  2 Buffer to  the indicated host  
memory area, the  HACC interrupt will  be set  indicating normal completion.  
This command is used in conjunction with  the Write Channel 2 Buffer command  
for host adapter diagnostics.

     Byte 0     Buffer area address, Most significant byte
     Byte 1     Buffer area address
     Byte 2     Buffer area address, Least significant byte 
                                   


4.6.17 Write Adapter FIFO Buffer (Operation Code 1C)


After receiving  this  command,  the  host  adapter  expects  three outbound  
information bytes to be  transferred which point  to an area of  54 bytes in  
system RAM. The area pointed to will be transferred to the host adapter's FIFO 
buffer using the host adapter's DMA circuitry. After completing the transfer  
of the 54 bytes from the indicated buffer area to the host adapter, the HACC 
interrupt will be set indicating normal completion.  This command is used in 
conjunction with  the  Read Adapter  FIFO  Buffer command  for  host adapter  
diagnostics.

                                 4-28

Section Four                                  Multithreaded Software Interface 
------------------------------------------------------------------------------


     Byte 0     Buffer area address, Most significant byte
     Byte 1     Buffer area address
     Byte 2     Buffer area address, Least significant byte 
                                   

4.6.18 Read Adapter FIFO Buffer (Operation Code 1D)


After receiving  this  command,  the  host  adapter  expects  three outbound  
information bytes to be  transferred which point  to an area of  54 bytes in  
system RAM. The area pointed to will be used as a buffer to receive 54 bytes  
of information transferred from the host adapter's FIFO to the host's memory 
using the host adapter's DMA circuitry. After completing the transfer of the 
64 bytes from the FIFO to the indicated buffer area, the HACC interrupt will 
be set indicating normal completion. This command is used in conjunction with 
the Write Adapter FIFO Buffer command for host adapter diagnostics.

     Byte 0     Buffer area address, Most significant byte
     Byte 1     Buffer area address
     Byte 2     Buffer area address, Least significant byte 
                                   


4.6.19 Echo Command Data (Operation Code 1F)


This command is used to test the Command  / Data Out Port, the Data In Port,  
and the associated control bits in the other I/O Ports. After receiving this  
command, the host  adapter expects  one byte  of outbound  information to be  
transferred through the Command / Data Out Port. The host adapter then sends  
(Echos) the same data value back to the host through the Data In Port. After 
the host has  read the  data value provided  on the  Data In Port,  the host  
adapter  will  generate  the  HACC  interrupt  to  indicate  normal  command  
completion. 
        
     Byte 0, Out Outbound Echo Value
     
     Byte 0, In Returned Echo Value
     
     
4.7 MAILBOX DESCRIPTION


The AHA-1640 uses a mailbox architecture  for task communication between the  
host and the host adapter when executing SCSI commands as described in Section 
2. This allows the  host adapter to perform  multithreaded operations with a  
minimum of host intervention. The mailboxes are located in main system memory. 
Each mailbox  entry is  four bytes  long. At  power up,  the host  issues an  
initialization command to inform the host of the mailbox location. There are 
always an equal  number of Outgoing  Mailboxes (MBO)  and Incoming Mailboxes  
(MBI). The MBOs pass pointers  from the host to the  host adapter, while the  
MBIs pass pointers or activity  requests from the host  adapter to the host.  
The MBIs are  located immediately after  the MBOs.  Initiator operations and  
target  operations  use  the  same  mailboxes.  Both  initiator  and  target  
operations may be in process at the same time. A typical mailbox structure is 
shown in Figure 4-2.

                                 4-29

Section Four                                  Multithreaded Software Interface 
------------------------------------------------------------------------------




                               [Picture]

                    FIGURE 4-2. TYPICAL MAILBOX STRUCTURE
                                            
                                            
In this example, there are four MBOs and four MBIs. The Mailbox Count in the 
Mailbox Initialization  command was  set to  four. The  base address  is the  
address specified by Mailbox Address field. 


4.7.1 Mailbox Out Definition


The first byte  of each  MBO entry  contains the  Mailbox Command  byte. The  
remaining three bytes  contain an  address pointer  to the  first byte  of a  
Command Control  Block  (CCB).  The  CCB  provides  additional  task control  
information. AMBO entry is free if the first byte is zero. The host can make 
an entry in any free MBO and indicate  that it is filled out or completed by  
placing the proper MBO Command in  the first byte of the  MBO. After the MBO 
has been examined by the host adapter and all relevant information obtained by 
the host adapter, the host adapter sets the MBO Command byte back to zero to 
allow the host to fill it again.  For a multitasking operating system, it is  
desirable that the number of  mailboxes be sufficient to  allow at least one  
mailbox for each active independent task or activity.


The MBO format is described in detail below:

     Byte 0     MBO Command        This byte specifies the state of the MBO 
                                   entry.
     
                Value              Definition
     
                00H                Mailbox Out is free
     
                01H                SCSI or Host Adapter command is to be 
                                   started. CCB pointer indicates location 
                                   of CCB to be processed.
     
                02H                SCSI or Host Adapter command is to be 
                                   aborted. CCB pointer indicates location 
                                   of CCB to be terminated.
     

                                 4-30

Section Four                                  Multithreaded Software Interface 
------------------------------------------------------------------------------


     Byte 1     CCB Pointer (MSB)  
     Byte 2     CCB Pointer
     Byte 3     CCB Pointer (LSB)


The use of Mailbox Out (MBO) entries to pass pointers to CCBs is identical for 
target and initiator modes. The appropriate target  mode CCB may be prepared 
early and posted to the host adapter in preparation for an operation that is 
expected to happen. If a  SCSI operation occurs before  the CCB is prepared,  
the host  adapter processes  as much  of the  transaction as  possible, then  
requests a CCB from the host through  the MBI. The host is fully responsible  
for preparing the correct CCB from the information provided through the MBI.

One target CCB may be presented for each unique combination of LUN, Initiator, 
and direction. If a second CCB  to the same LUN and  initiator with the same 
direction bit is sent to the AHA-1640, the  CCB will be returned with a host 
status of 19H, Duplicate CCB Received.

Initiator type CCBs  may be queued  for an  LUN and Target,  as described in  
Section 4.10.2. The host adapter will always search for new MBO entries in a 
round-robin order, beginning with the entry after the last MBO entry that was 
processed. By always placing the MBO entries  in the MBO area consecutively, 
the host can assure that the SCSI commands will be executed in FIFO order with 
a minimum scan overhead.

If the Mailbox Out Available Interrupt is enabled by execution of IOCP command 
05 (Enable Mailbox Out Available Interrupt), the host adapter will take one of 
the following actions after each MBO entry is freed by the host adapter:

     1) If  the Any  Interrupt  bit in  the  Interrupt Flag  Port  is zero,  
           indicating that there are no interrupts pending, the host adapter 
           will set the Mailbox Out Available Interrupt and the Any Interrupt 
           bit and  indicate a  hardware interrupt  to  the host.  The host  
           adapter will then continue scanning for other stored MBO entries.
     
     2) If  the Mailbox  Out Available  Interrupt  has been  set to  one by  
           the previous clearing of a Mailbox Out entry and the interrupt has 
           not yet been cleared by the host, the host adapter will take not  
           post any new interrupt and will continue to scan for other stored 
           MBO entries. 
     
     3) If  interrupts  other  than  the  Mailbox  Out  Available Interrupt  
           are pending, the host adapter will wait for the pending interrupts 
           to be cleared before setting the Mailbox Out Available Interrupt. 
           This guarantees that the MBO Empty Interrupt will not be cleared  
           accidentally by clearing another interrupt. 


4.7.2 Mailbox In Definition


The Mailbox In entries are used to  pass completion information concerning a 
task from the host adapter to the host. In addition, requests for Target Mode 
CCBs are passed to  the host using MBI  entries. The first  byte of each MBI  
contains the MBI Status byte, summarizing the type of information being passed 
from the  host  adapter  to  the host.  The  remaining  three  bytes contain  
specialized information that provides more  detail about the information. In  
the case of a CCB Completed MBI, the bytes contain a pointer to the completed 
CCB. In the case  of a CCB  Required MBI, the bytes  contain the information  
necessary for the host to prepare an appropriate CCB. Only those MBIs with a 
MBI Status that  is non-zero  have information for  the host.  When the host  
returns the MBI Status byte to zero, the MBI Free state, the host adapter is 
allowed to place a new set of information in the MBI entry. 

                                 4-31

Section Four                                  Multithreaded Software Interface 
------------------------------------------------------------------------------


When a SCSI command completes, or if a new CCB is required, the host adapter 
scans the first byte of an MBI entry to find a free mailbox. The scan will be 
performed in  a round-robin  order so  that MBI  entries will  be made  in a  
round-robin order.  If a  free MBI  entry  is found,  the host  adapter will  
update the MBI's status byte with a  non zero value and update the following  
bytes with the  appropriate required pointers  or parameters.  Since the MBI  
entries are usually filled in a round-robin order, the host can usually find  
the full MBI immediately  by performing its  scan in a  round-robin order as  
well. The valid MBI formats are defined in Table 4-6.

                TABLE 4-6. Mailbox In Format for CCB Complete
                                            
     Byte 0     MBI Status         This byte specifies the state of the MBI 
                                   entry.
     
                Value              Definition
                                   
                00H                Mailbox In is free
     
                01H                CCB completed without error. CCB pointer 
                                   indicates location of successfully 
                                   completed CCB. 
     
                02H                CCB aborted by host. CCB pointer 
                                   indicates location of CCB that was aborted.
     
                03H                Aborted CCB not found. CCB pointer 
                                   indicates the supposed location of the CCB 
                                   that was to have been aborted. It is 
                                   likely that the CCB was already presented 
                                   to the host before the Abort CCB MBO 
                                   entry was completed.
     
                04H                CCB Completed with Error. The CCB fields 
                                   indicate the details of the error 
                                   condition. This code allows normal CCB 
                                   completion to be processed without 
                                   bothering to examine the completion codes 
                                   in the CCB. 
     
     Byte 1     CCB Pointer (MSB)
     Byte 2     CCB Pointer
     Byte 3     CCB Pointer (LSB)


                                 4-32

Section Four                                  Multithreaded Software Interface 
------------------------------------------------------------------------------



                     Mailbox In Format for CCB Required

     Byte 0     MBI Status         This byte specifies the state of the MBI 
                                   entry.
     
                Value              Definition
     
                10H                SCSI Target Command received with no CCB 
                                   available. The host must prepare an 
                                   appropriate CCB and place it in the MBO to 
                                   complete the SCSI command. The remaining 
                                   three bytes of the MBI specify the 
                                   information necessary to prepare a SCSI 
                                   command.
     
     Byte 1     Initiator and LUN
     
                Bit 7-5            Binary address of initiator that selected 
                                   the host adapter in Target Mode.
                Bit 4              The SCSI Target Command received was a 
                                   RECEIVE command. A CCB must be prepared 
                                   to transmit data to the Initiator.
                Bit 3              The SCSI Target Command received was a 
                                   SEND command. A CCB must be prepared to 
                                   transmit data from the Initiator.
                Bits 2-0           Binary address of the logical unit of the 
                                   Target Mode host adapter that was 
                                   addressed by the Initiator.
     
     Byte 2-3   Data Length        The high order two bytes of the data 
                                   length specified in the SEND or the 
                                   RECEIVE command. A CCB must be prepared 
                                   to transmit this amount of data plus up to 
                                   256 more bytes. It is assumed that the 
                                   data fields are self-defining or of a 
                                   known length in such protocols.
     

For the CCB Required Mailbox In entries, byte 0 takes on a distinctive value 
of 10H, indicating both that the MBI entry is filled and that the MBI entry is 
being presented to request a CCB appropriate to service a SCSI transaction for 
which no CCB was available.  The host adapter will  have disconnected on the  
SCSI after receiving the initiator and LU addresses and after having received 
either a SCSI SEND or a RECEIVE command. If the LU address is enabled by the  
Logical Unit Mask, the MBI will provide the addresses in bits 7-5 and bits 2-0 
and will indicate by setting either bit 3 or bit 4 that a SCSI SEND or RECEIVE 
command was accepted from the initiator. The host system is then expected to  
prepare a  CCB suitable  for  processing the  Send  or Receive  command. The  
information in bytes 2 and 3 is a copy of bytes 2 and 3 of the Send or Receive 
command CDB. This provides  the host an  approximation of the  length of the  
requested data transfer.  This length  is used by  the host  to allocate the  
correct amount of buffer to accept data in  a SEND command or to control the 
maximum amount of data that can be transferred in a RECEIVE command. 

If the LU address received is disabled, no MBI will be presented and a check 
condition will be posted to the Initiator. A subsequent REQUEST SENSE command 
will recover the error  indication. The error  will be an  Invalid LUN error  
with a sense key of 05h and an additional sense code of 25h.

                                 4-33

Section Four                                  Multithreaded Software Interface 
------------------------------------------------------------------------------


After each Mailbox In entry is stored  by the host adapter, it will indicate  
that Mailbox In  scanning must  be performed by  the host  by presenting the  
Mailbox In Full interrupt in the following manner:

1) If the Any  Interrupt bit is not  set to one in  the Interrupt Flag port,  
indicating that no interrupts are pending, the host adapter will set the
Mailbox In Full interrupt bit, the Any Interrupt bit, and raise the hardware 
interrupt line to indicate that there is at least one Mailbox In entry to be 
examined by the host system.
     
2) If the  Mailbox In Full  interrupt bit  has already been  set to indicate  
that an entry  was made in the Mailbox In area and if that interrupt has not 
yet  been cleared by the  host, no further notification is provided by the 
host adapter.
     
3) If interrupts other than the Mailbox In Full interrupt are pending, the  
host adapter will wait for all pending interrupts to be cleared  before 
setting the Mailbox In Full interrupt.

Note that careful host  Target Mode software design  is necessary to prevent  
ambiguity in the notification process. If a CCB was just prepared but the MBO 
has not yet been searched by  the host adapter at the  time the MBI entry is  
made to the host, the host may choose to examine the MBI entry and not act on 
it, having already provided the needed CCB. The host should also examine the  
entire MBI space to be sure that a previously supplied CCB which should have 
been able to service the  notification MBI entry was not  already used for a  
previous operation that  had been  posted by  the host  adapter but  not yet  
serviced by the host. Proper  care in host system  design will prevent these  
overlapping operations from becoming a problem.


                                 4-34

Section Four                                  Multithreaded Software Interface 
------------------------------------------------------------------------------

4.8 COMMAND BLOCK DEFINITION

The CCB specifies detailed information about a SCSI command. The format of a  
CCB is shown below. Each of the fields is separately explained following the  
table.

                        COMMAND CONTROL BLOCK FORMAT
                                      
                                      
     Byte 0     Command Control Block Operation Code
     
                Value              Definition
                                   
                00H                SCSI Initiator Command
                01H                Target Mode Command
                02H                SCSI Initiator Command with Scatter/Gather
     
     Byte 1     Address and Direction Control 
     
                Bits 7-5           CCB Op Code = 00, 02:  SCSI Target Id 
                                   CCB Op Code = 01:      SCSI Initiator Id
                Bit  4             Outbound data transfer, length is checked.
                Bit  3             Inbound data transfer, length is checked.
                Bit  2-0           Logical Unit Number
     
     Byte 2     SCSI Command Length
     
     Byte 3     Returned Sense Information Length
     
     Byte 4-7   Data Length (Byte 4 most significant)
     
     Byte 7-9   Data Pointer (Byte 7 most significant)
     
     Byte 10-12 Link Pointer (Byte 10 most significant)
     
     Byte 13    Command Linking Identifier
     
     Byte 14    Host Adapter Status (HASTAT)
     
     Byte 15    Target Device Status (TARSTAT)
     
     Byte 16-17 Reserved (00)
     
     Byte 18-n  SCSI Command Descriptor Block
                (Length specified by byte 2)
     
     Byte n-m   Reserved for REQUEST SENSE information bytes
                (Length of reserved space in byte 3)
     

The standard format of the Command Control Block is shown in Figure 4-3.

                                 4-35

Section Four                                  Multithreaded Software Interface 
------------------------------------------------------------------------------


                             [Picture]

                 FIGURE 4-3. COMMAND CONTROL BLOCK


The bytes of the CCB are defined further below:

Byte 0: Command Control Block Operation Codes

The AHA-1640 supports four CCB Operation Codes. The valid command values are 
shown below:

                 00   SCSI Initiator Command Control Block
                 01   SCSI Target Command Control Block
                 02   SCSI Initiator Command Control Block with Scatter/Gather
                 81   SCSI Bus Device Reset

If the Operation Code value is 00H, the SCSI command specified in the Command 
Descriptor Block  field  of  the  CCB  is  executed  against  the  addressed  
Target/LUN. The  other  fields of  the  CCB support  the  required Initiator  
functions of the AHA-1640.

If the Operation Code value is 01H, the CCB is intended to service a SEND or  
RECEIVE command sent to the host adapter as a target from another initiator.  
The values in the other fields are used to service the Target Mode operation. 
If an Operation Code of 01H is specified  to a host adapter that has not had  
its Target Mode enabled, the host adapter returns a Host Status indication of 
18H, Invalid CCB Parameter. 

If the Operation Code value is 02H, the SCSI command specified in the Command 
Descriptor Block field of the CCB is executed against the addressed Target /  
LUN. The definition of the  Data Length and the Data  Pointer is modified to  
support the Scatter/Gather function.

                                 4-36

Section Four                                  Multithreaded Software Interface 
------------------------------------------------------------------------------

If the value  is 81(hex)  a Bus  Device Reset  message will  be sent  to the  
addressed target.  This  command  forces  the  host  adapter  to  abort  all  
outstanding tasks against the  selected target. All  remaining CCB Bytes are  
ignored. 

Any other command value generates a Host Adapter Detected Error (Host Status 
byte of 16H).

Byte 1:  Address and Control Byte

This byte identifies the  address of the  devices that will  be serviced and  
provides information about the expected direction of data flow.

     Bit Field     Definition if Initiator CCB     Definition if Target CCB

     Bits 7-5      Target SCSI Device ID           Initiator SCSI Device ID

     Bits 4 and 3  Direction of Data Xfer          Service Send/Receive 

        00           Direction not checked          Invalid
        01           Data In expected               SEND Command 
        10           Data Out expected              RECEIVE Command
        11           No Data Xfer expected          No Data Xfer expected

     Bits 2-0      Target Logical Unit Number      HA Logical Unit Number


If the CCB is an Initiator CCB, this byte identifies the target SCSI device in 
bits 7,  6 and  5. If  the  CCB is  a Target  CCB,  the byte  identifies the  
initiator which the CCB will serve. 

Bits 4 and 3 are optionally set to determine the direction of data transfer. 
For an Initiator CCB, if neither bit  is set, the direction of data transfer  
will be established by the SCSI command being executed. For a Target CCB, if 
neither bit is set, the CCB will be returned with an indication of Invalid CCB 
Parameters (18H) in  the Host  Status field, since  each Target  CCB must be  
identified as to whether it will service a SEND or a RECEIVE command. If both 
bits are  set for  either type  of  CCB, the  command must  perform  no data  
transfer. If only  bit 3 is  active, the data  transfer will be  to the host  
adapter and from the external SCSI  device. If the CCB is  a target CCB, the 
data transfer will be required to be a Data Out phase, while if the CCB is an 
initiator CCB, the data transfer will be required  to be a Data In phase. If 
only bit 4 is active, the data transfer will be from the host adapter and to  
the external SCSI device. If the CCB is a target CCB, the data transfer must 
be a Data In phase, while if the  CCB is an initiator CCB, the data transfer  
will be a Data Out phase.

If bits 3 or 4 are set for an Initiator CCB, the data length will be checked. 
If the amount of data transferred exceeds the specified amount, the CCB Host  
Status field will contain an indication of  Data Over/Under Run (12H). For a  
Processor Target mode CCB, the handling of incorrect lengths is described in 
Section 7.2.4.

If the CCB is an initiator CCB, bits 2, 1 and 0 define the target Logical Unit 
which will be addressed. If the target  accepts an IDENTIFY message out, the  
value in bits 2,1,  and 0 will be  provided in the LUN  field of the message  
byte. The LUN field in the SCSI Command Descriptor Block (CDB) is expected to 
be zero. If the target does not accept an IDENTIFY message out, the LUN field 
in the SCSI CDB must contain the  correct Logical Unit address. SCSI devices  
with conformance level 2, including Common Command Set (CCS) disk drives and 


                                 4-37

Section Four                                  Multithreaded Software Interface 
------------------------------------------------------------------------------

all SCSI-2 devices will always accept the IDENTIFY message out. The few SCSI  
devices not meeting  those requirements must  be examined  on a case-by-case  
basis to determine whether the Logical Unit  Address should be placed in CCB  
Byte 1 or in the CDB.

If the CCB is a target CCB, bits 2, 1 and 0 define the Processor type Logical 
Unit within the host adapter which will use the CCB. When an initiator sends 
a SCSI command to the host adapter, the host adapter expects the initiator to 
require an IDENTIFY  message out.  The LUN  in the  message will be  used to  
properly select the target CCB that has  the same LUN and the same initiator  
device ID.

Byte 2: SCSI Command Length

This byte establishes the length, in bytes, of the space reserved for the SCSI 
Command Descriptor Block beginning at byte 18.  The actual length of the CDB  
may be shorter than the reserved space. The number of bytes transferred will  
be the number requested by the target as  long as the number does not exceed 
the reserved space.

Byte 3:  Request Sense Allocation Length

This byte indicates the length, in bytes, of the area reserved for information 
that may be obtained  by a REQUEST  SENSE command. The  reserved area begins  
immediately after the last  byte allocated by  the CCB for  the SCSI Command  
Descriptor Block. A value of 00H defaults to 14 bytes, sufficient to capture  
the sense key and  error code of  all normal extended sense  type devices. A  
REQUEST SENSE command is automatically generated by the host adapter if Check 
Condition status is presented at the end of a SCSI command. The host adapter 
uses the indicated Request Sense Allocation Length  as its byte count in the  
REQUEST SENSE Command Descriptor Block that it generates to obtain the sense 
information.

If an operation that treats  the AHA-1640 as a Target  Mode device fails and  
presents a Check Condition status byte, the  Initiator is expected to return 
automatically with  a  REQUEST  SENSE  command.  The  AHA-1640  will  return  
appropriate sense information in response to the command. If the command that 
originally failed was a  SEND or a  RECEIVE command, the  same REQUEST SENSE  
information bytes that will later be sent  to the Initiator are also sent to  
the host when the  CCB is returned.  The sense information is  placed in the  
specified Request  Sense Allocation  area with  a  length not  exceeding the  
Request Sense Allocation Length. The sense information is placed in the area 
in the same format that will be sent to the initiator when it is requested.

Bytes 4, 5, 6: Data Length

These bytes determine the length,  in bytes, of the  data transfer. CCB host  
adapter error 12h  (Data Over run  / Under  run) is posted  if the addressed  
target attempts to transfer more than the indicated number of bytes.

If the CCB  specifies a  Scatter / Gather  operation, the  Data Length field  
contains the length  of the  Data Segment List.  The operation  of Scatter /  
Gather is described in Section 4.9.

Bytes 7, 8, 9: Data Pointer

These bytes specify the real address of the first byte of the host memory data 
area to be used during the data phase of the SCSI command. 

If the  CCB specifies  a Scatter/Gather  operation,  the Data  Pointer field  
contains the pointer to the first byte of the Data Segment List.

                                 4-38

Section Four                                  Multithreaded Software Interface 
------------------------------------------------------------------------------

Bytes 10, 11, 12: Link Pointer

These bytes are used when a SCSI command contains a LINK or LINK WITH TAG bit 
in the command. When a Linked command is completed, the host adapter will use 
the contents of this field as  a pointer to the next  CCB to execute. If the  
Linked Tag bit is set, an interrupt will be generated before the next command 
is started. A completed CCB is always reported back in an MBI. 

Target Mode does not support the linking function.

Byte 13: Command Link ID

This byte is used in conjunction with linked commands. It is set by the host 
to identify commands in a command chain.

Linking is not supported in Target Mode.

Byte 14: Host Adapter Status

This byte is used to report the host adapter status (HASTAT). 
HASTAT has the following definitions:

        00 H                   No host adapter detected error
                                   The CCB was completed normally.
        0A H                   Linked command complete without error
                                   The SCSI command completed and linked 
                                   normally.
        0B H                   Linked command complete without error, 
                                   interrupt generated.
                                   The SCSI command completed and linked with 
                                   a LINKED COMMAND COMPLETE WITH FLAG message.
        11 H                  Selection time out
                                   The initiator selection or target 
                                   reselection was not complete within the 
                                   Set SCSI Selection Timeout period.
        12 H                  Data over run/Under run
                                   The target attempted to transfer more data 
                                   than was allocated by the Data Length 
                                   field or the sum of the Scatter / Gather 
                                   Data Length fields.
        13 H                  Unexpected bus free 
                                   The target dropped the SCSI BSY at an 
                                   unexpected time.
        14 H                  Target bus phase sequence failure
                                   An invalid bus phase or bus phase sequence 
                                   was requested by the target. The host 
                                   adapter will generate a SCSI Reset 
                                   Condition, notifying the host with a SCRD 
                                   interrupt.
        15 H                  MBO command was not 00, 01, or 02
                                   The first byte of the MBO command was 
                                   invalid. This usually indicates a 
                                   software failure.
        16 H                  Invalid CCB Operation Code
                                   The first byte of the CCB was invalid. 
                                   This usually indicates a software failure.

                                 4-39

Section Four                                  Multithreaded Software Interface 
------------------------------------------------------------------------------

        17 H                  Linked CCB does not have the same LUN
                                   A subsequent CCB of a set of linked CCB's 
                                   does not specify the same logical unit 
                                   number as the first.
        18 H                  Invalid CCB Parameter Received from Host
                                   A parameter of the CCB was invalid. The 
                                   CCB direction was invalid.
        19 H                  Duplicate CCB Received in Target Mode
                                   More than once CCB was received to service 
                                   data transfer between the same target LUN 
                                   and initiator SCSI ID in the same 
                                   direction.
        1A H                  Invalid Segment List Received
                                   A segment list with a zero length segment 
                                   or invalid segment list boundaries was 
                                   received.
        1B H                  Request Sense Command Failed
                                   Non zero status was received by the host 
                                   adapter in response to a REQUEST SENSE 
                                   command.


Byte 15: Target Status

For an initiator CCB, this byte is used to return the SCSI status byte sent to 
the host adapter  from the initiator.  For a  target mode CCB,  this byte is  
used to indicate to  the host what  status the host adapter  returned to the  
initiator. 
Target Status may have the following values: 

        02 -- Check Status (See REQUEST SENSE byte area)
        08 -- LUN Busy
        18 -- Reservation Conflict

If a SCSI command returns with BUSY status, the normal recovery process is to 
execute the command again. The  AHA-1640 takes that burden  off the host and  
periodically restarts the command automatically until the command is executed 
successfully.

Byte 16: Reserved (must be 0)

Byte 17: Reserved (must be 0)

Byte 18 - n: SCSI Command Descriptor Block

For an initiator CCB, this field holds the SCSI Command Descriptor Block (CDB) 
to  be  transmitted  to  the  selected  target  as  described  in  the  SCSI  
specification. The length of this command is defined in byte 02.

For a target mode CCB, this field is not prepared by the host, but instead is 
returned by the host adapter to the host. The CCB must have a minimum of six  
bytes allocated for the CDB.  The field contains the  actual SEND or RECEIVE  
CDB transmitted from the initiator. The SEND  command's control bytes can be 
examined to determine if the information presented is a normal SEND command or 
an Asynchronous Even Notification.

                                 4-40

Section Four                                  Multithreaded Software Interface 
------------------------------------------------------------------------------

Byte n.+1 - n+m:  Allocated for Sense Data

If a Check Status condition  is detected by the AHA-1640  as it completes an  
operation on the SCSI bus, the host adapter automatically executes a REQUEST 
SENSE command with  the data  length specified  by Request  Sense Allocation  
Length. The actual bytes  returned, up the maximum  indicated by the Request  
Sense Allocation Length, are placed in the area Allocated for Sense Data.

If a check condition  is detected by  the AHA-1640 while it  is operating in  
Processor Target Mode, the same information that  will later be recovered by 
the initiator that  received the  Check Status  is also  placed in  the area  
Allocated for Sense  Data so that  the host  processor is also  aware of the  
failure.

4.9 SCATTER/GATHER LIST DEFINITION

Using the normal CCB Operation  Codes of 00 and 01  (SCSI Initiator and SCSI  
Target CCBs),  the CCB  itself contains  a pointer  to the  first byte  of a  
contiguous area of data of a specified length. The direction of transfer with 
respect to the data area and the checking of the length of the data transfer 
to the  data  area  are  both  managed  by  the  AHA-1640  according  to the  
requirements of the particular mode and control bit set-up.

Using the scatter/gather  Operation Code of  02, the CCB  instead contains a  
pointer to a list of data segments and an indication of the length of the list 
of data  segments. The  data segment  list contains  pointers to  the actual  
location in host memory of the data segments  to be transferred as well as a 
precise indication of the length of each data segment. Each data segment list 
entry contains a three-byte  pointer to the  location of a  data segment and  
three-byte length indicator  telling how  long that  particular data segment  
shall be. The data segment list is arranged  in the order in which data will 
be gathered or distributed, the first pointer in the list being used first.

A typical data  segment list is  shown in  table 4-7. The  data segment list  
describes the  distribution  of  4096  bytes  distributed  in  four separate  
locations within  the memory.  The  beginning of  the  data segment  list is  
indicated by the data segment  list pointer. The length  of the data segment  
list (48 bytes) will be contained in the data segment list length field of the 
CCB.

                                 TABLE 4-7.
                                            
                                 [Picture]
                                            
                                            
A data segment  list can have  from one to  sixteen segments. A  list with 0  
segments or a list with more than 16 segments causes an Invalid Segment List 
error to be posted in the host status field.

                                 4-41

Section Four                                  Multithreaded Software Interface 
------------------------------------------------------------------------------

The AHA-1640 has certain constraints in  the data segment address boundaries  
and lengths that  can be implemented.  If these boundaries  are violated, an  
Invalid Segment List error will be posted in the host status field of the CCB. 
The simplest way  to assure  that these  boundaries are  not violated  is to  
require all boundaries between segments to be  one even word boundaries. The 
first segment may begin on any boundary and  the last segment may end on any 
boundary. All segments but the first and last should have even byte counts. 

The actual boundary limitation  is somewhat looser. If  the binary values of  
the starting address of a  segment, the byte count of  that segment, and the  
starting address of the next segment are all exclusive OR'd together, and the 
result of that exclusive OR is an even number, the boundary between those two 
segments is valid. Another way to express  the limitation is to require that  
the ending boundary of one segment must be the same as the beginning boundary 
of the next segment. If a segment ends  on a word boundary, the next segment 
must begin on a word  boundary. Similarly, if a segment  ends on an odd-byte  
boundary, the next segment must begin on an odd-byte boundary.

4.10 DESCRIPTION OF OPERATION 

This section describes the interface operations required to invoke the desired 
SCSI behavior. The AHA-1640 must be properly initialized before any of these 
operations can be performed.  The initialization steps  are described in the  
first section.

4.10.1 Initialization Procedure

The POS registers must be properly initialized by the starting code. The POS  
registers allow the selection and assignment of the I/O Port Addresses, of the 
BIOS PROM  addresses,  and of  the  required Micro  Channel  arbitration and  
initialization parameters.

After POS initialization is done, the I/O Command Port initialization commands 
must be executed.  The Mailbox  Initialization command  must be  executed to  
assign the Mailbox  area. The Enable  Target Mode command  may optionally be  
executed if Target Mode is to be allowed.

4.10.2 Execution of Initiator Mode operations 

To begin an  Initiator Mode  SCSI command, the  host first  allocates a data  
buffer area. A CCB is  then created to perform the  desired operation to the  
correct peripheral device and a pointer to the data buffer area is placed in 
the CCB. Once the CCB is completely defined, the host places a pointer to the 
CCB in an empty MBO location, places a Start SCSI Command in the MBO Command 
Byte and transmits a Start SCSI Command to the I/O Command Port. If it is not 
already scanning the MBO for an active  MBO entry, the Start SCSI Command to  
the I/O Port causes the host adapter to begin scanning for such an entry.

After finding an active MBO entry, the AHA-1640 copies the MBO Command field  
contents and CCB pointer  into its internal  RAM and clears  the MBO Command  
byte, freeing the mailbox. Up to 112 CCBs can be stored in the host adapter's 
internal RAM concurrently. The AHA-1640 maximizes the SCSI bus utilization by 
starting the next available CCB as soon as the bus is free. Disconnection and 
reconnection on the bus are automatically taken  care of by the AHA-1640. As  
the host  adapter  prepares  to  start the  SCSI  operation,  it  will first  
determine if a CCB addressed to that target/LUN is already being executed. If 
so, then the command will be placed in the task queue instead of being started 
immediately (See Section 4.10.4).    

                                 4-42

Section Four                                  Multithreaded Software Interface 
------------------------------------------------------------------------------

Commands are removed from  the queue in  the order that  they were received,  
establishing a first-in first-out (FIFO) command initiation order. Of course, 
the order of task completion  may vary due to the  different amounts of time  
required to  process  and complete  different  commands. If  BUSY  status is  
received by  the AHA-1640,  the CCB  is  returned to  the FIFO  queue  to be  
restarted later.

If a CHECK CONDITION status  is received from the  target, the AHA-1640 will  
issue a REQUEST SENSE command to get the sense data. The sense data is stored 
in the CCB after the SCSI command data. The driver software must reserve the 
allocated number of bytes at the end of the CCB to hold the sense data which  
is returned as a result of a receiving a check status.

If the MBO Command is to abort a SCSI command, the host adapter first searches 
the active and queued CCBs. If that CCB is found, the task is aborted at the  
earliest possible moment and an MBI entry is made to indicate that the CCB's 
execution was successfully  terminated. If  the CCB  is not  found among the  
active or queued CCBs,  the AHA-1640 completes the  command and reports that  
fact in  the MBI  Status  byte. The  CCB  may not  be found  because  it has  
previously been aborted, because an intervening reset occurred, or because the 
CCB was already finished normally and returned.

When executing a START SCSI command, the AHA-1640 does not verify that the new 
CCB resides in an unused memory area. Therefore, the host must not reuse a CCB 
location until it has been returned through  a Mailbox In entry and the host  
has examined all  the pertinent  information in  the CCB.  CCB addresses are  
used by the AHA-1640 and by the host as task identifiers.

4.10.3 Execution of Target Mode Operations

4.10.3.1 Target Mode with a Prepared CCB

Typical target operation is managed in the following way by the host software. 
After power-on initialization is  complete, the host  sends an Enable Target  
Mode command to the host adapter to enable Processor Target mode. After that, 
the host, from previous configuration knowledge, generates a pair of CCBs for 
each likely initiator and for each LUN supported by the host. One CCB is for 
outbound data from the initiator using the  SEND command, while the other is  
for inbound data from the target to the initiator using the RECEIVE command.  
The SEND command  CCB defines  a data buffer  for the  expected network type  
command from the initiator. The RECEIVE command CCB, if any, defines a set of 
data which is known  and expected by  the initiator, typically  a welcome or  
configuration type message packet.

As  the  initiator  finishes  its   initialization  procedure,  it  requests   
availability and configuration information using the TEST UNIT READY, REQUEST 
SENSE, and  INQUIRY commands.  Finally, it  may choose  to address  SEND and  
RECEIVE commands  to  the  Processor  type  targets  it  has  located during  
initialization.

When the initiator executes a SEND or  a RECEIVE command, the target accepts  
the selection on the SCSI  bus, accepts the command  from the initiator, and  
executes the proper data transfer to or from the area specified by the proper 
CCB. When all SCSI activity is finished successfully, the CCB is posted back  
to the host program by an entry in  the MBI. The host is notified that there  
is an entry in the MBI by an  interrupt from the host adapter. The host then  
prepares a new CCB to  control the target's next  activity expected from the  
initiator.

                                 4-43

Section Four                                  Multithreaded Software Interface 
------------------------------------------------------------------------------

4.10.3.2 Target Mode without a Prepared CCB

Alternatively, the processor type device may be addressed by an initiator when 
no CCB has yet been prepared for use by the host adapter. If the host adapter 
command enabling target mode has not yet been executed, the host adapter will 
act like any initiator.  It will not  accept any selection  sequence and any  
attempts to select it by its target ID  will cause the initiator to detect a 
selection time-out. 

If the host adapter has been enabled as a Processor Target by a host adapter 
command, any selection to the host adapter's target address will be accepted. 
The availability  commands  and identification  commands  (TEST  UNIT READY,  
REQUEST SENSE, and INQUIRY)  will be executed completely  and normally. If a  
SEND or RECEIVE command is received and if a CCB is not active, either because 
the host has not completed its program initialization or because the host has 
not finished analyzing  the results of  previous data transfers  and has not  
generated a new CCB, the Processor Target  will accept the selection, obtain 
the IDENTIFY Message Out  to determine what Logical  Unit has been selected,  
request the CDB from the SCSI, and then disconnect. The CDB will be partially 
interpreted so that the proper MBI can be generated to notify the host that a 
new CCB with a certain address, direction, and data length must be generated. 
When the new CCB is passed  to the host adapter by  an MBO entry, the CCB is  
filled up with  the command  information, the  SCSI is  reconnected, and the  
command is completed as described above.

4.10.4 CCB Queuing and Scan Order

The MBO is scanned by the host adapter in a round-robin order. When a new MBO 
entry has been placed in the  MBO, the host adapter first  looks in the next 
entry higher than the  location where an  MBO entry was last  found. If that  
entry is clear, the host adapter looks in consecutively higher entries until 
the end of the MBO list is reached, then begins again at the first MBO entry, 
scanning until the location where the last active MBO entry was encountered in 
that scan cycle. If no  active MBO entry was found,  the scan terminates. If  
any active MBO entries  are found, the  CCB pointer and CCB  for each active  
entry are transferred to the host adapter in the scanned order until the scan 
is complete. If the CCB can begin execution, it is started as soon as the CCB 
pointer and CCB have been moved to the host adapter. To minimize the overhead 
of the host adapter in the scanning process, the host should place new active 
MBO entries in the MBO in the same round-robin order in which scanning occurs.

When each  CCB has  been  moved to  the  host adapter,  it is  placed  in an  
appropriate queue. The  target mode CCBs  are placed  in a queue  that has a  
maximum length of one to await an initiator action that requires the initiator 
address, LUN, and data direction provided by the particular CCB. If a second  
target mode CCB is presented with the  same addresses and data direction, it  
will be rejected with a host status of Duplicate CCB Received in Target Mode.

Each initiator CCB is placed in a queue with other CCBs having the same target 
address and logical unit address as each CCB is found during the scan process. 
There is no  ordering relationship enforced  by the host  adapter among CCBs  
requesting service from different targets and logical units. For CCBs having  
the same target address and logical unit address, the CCBs are executed in the 
precise order that they were  found during the scan  process. By placing the  
CCBs in the MBO in round-robin order, the host can guarantee FIFO service for 
all CCBs directed  to a  particular LUN.  The queueing  of CCBs in  the host  
adapter allows the host adapter to begin the execution of a new operation on a 
LUN which has just finished an operation in the shortest time possible. It is 
not necessary for the host to service the MBI completion of the command before 
the new operation is  started. If errors occur  during queued operation, the  

                                 4-44

Section Four                                  Multithreaded Software Interface 
------------------------------------------------------------------------------


REQUEST SENSE command is  automatically executed between  CCBs and the sense  
information is transmitted  automatically to the  host in  the returned CCB.  
CCBs that must wait  for successful completion of  a previous SCSI operation  
must not be  placed in the  MBO until  the previous SCSI  operation has been  
returned successfully in an MBI entry. 

The MBI entries are made in the MBI using the same type of scan order. A new 
active MBI entry is made by the host  adapter in the next MBI entry location 
after the one used by the previous MBI entry. The scan process for empty MBI 
entry locations is performed in the same round-robin manner. The host can use 
this to facilitate its scan for active MBI entries by performing a round-robin 
scan beginning at the first MBI entry location after the last MBI entry that 
was cleared. More than  one MBI entry may  be active at a  time, so the scan  
should continue around the MBI until all entries have been examined.

The MBI Full interrupt should be cleared by the host as soon as possible after 
it begins MBI processing so that, when a scan has been completed by the host, 
a second scan will only be required if a new MBI Full interrupt has been set.



                                 4-45

Section Five                                Single-Threaded Software Interface 
------------------------------------------------------------------------------


5.1 SINGLE-THREADED BIOS COMMAND INTERFACE

The AHA-1640 BIOS resides on the host adapter board. It provides support for  
up to two  SCSI Common Command  Set disk  drives under DOS.  If SCSI devices  
other than CCS disk  drives or if support  for more than  two disk drives is  
required, a DOS  device driver must  be used. Support  for operating systems  
other than DOS usually requires appropriate drivers. The BIOS provides a very 
simple single-threaded  capability that  does not  make  use of  the Mailbox  
Interface used by more  sophisticated programs and  drivers. This capability  
allows the host system to boot from a SCSI disk drive and to support hard disk 
calls from any standard DOS program.

The BIOS communicates with the host adapter through a special set of commands 
passed under the IOCP  command 02H (Start Bios  Command). These commands are  
not available  to any  programs except  the Adaptec  BIOS. The  Adaptec BIOS  
provides a standard BIOS interface that meets  the requirements of the PS/2. 
The DOS interface to the standard BIOS is described in this section.

On a PS/2 compatible machine, up to two hard disks are supported by the BIOS 
resident on the  motherboard. Any other  drives must be  managed through the  
Mailbox Interface using an appropriate driver. The operation of the AHA-1640  
BIOS on attached SCSI devices  depends on the number  of standard hard disks  
installed directly on the system.

No PS/2 hard disks directly attached:

In this case, two  SCSI drives can  be supported by the  AHA-1640 BIOS. SCSI  
Device 0 Logical Unit Number  0 is designated as drive  0 (Drive C:). Either  
SCSI Device 0 LUN 1 or SCSI Device 1 LUN 0 may be designated as drive 1 (Drive 
D:). This set of addresses allows the use of two drives with either embedded 
controllers or bridge controllers.  Booting is performed  from SCSI Device 0  
LUN 0. When no  hard disks are  directly attached to the  Micro Channel, the  
AHA-1640 BIOS is operating in non-concurrent mode.
     
One PS/2 hard disk directly attached:

In this case, the  internally installed hard  disk is designated  as drive 0  
(Drive C:). SCSI Device 0 LUN 0 is designated as the second drive (Drive D:). 
Booting is performed from  the internally installed hard  disk. This mode of  
operation is  called concurrent  operation,  indicating that  the internally  
installed drive and one SCSI drive can operate together under the BIOS.
     
Two PS/2 internal hard disks attached:

In this case, all the disks  that can be supported by  the BIOS are directly 
installed. The AHA-1640 BIOS will not support any SCSI drives. 
     
                                 5-1

Section Five                                Single-Threaded Software Interface 
------------------------------------------------------------------------------

5.2  BIOS COMMAND EXECUTION USING INTERRUPT 13 

On IBM compatible systems,  disk I/O requests are  passed from the operating  
system to the BIOS through software interrupt 13H. CPU registers are used to  
pass information about the desired  operation and the associated parameters.  
This process is described in Section 1 of the IBM Personal Computer and PS/2 
BIOS Interface Technical Reference manual.

The AHA-1640 BIOS provides  SCSI support by  intercepting each interrupt and  
managing the request according to the drive address. If the drive is a floppy 
or internally installed fixed  disk, the call is  managed by the motherboard  
BIOS with no changes. If the selected drive is a SCSI disk drive, the request 
is handled  by the  Adaptec BIOS  resident on  the AHA-1640.  For concurrent  
operation, only calls to drive 81H (D:) are handled by the AHA-1640 BIOS. For 
nonconcurrent operation, calls to both drive 80H (C:) and 81H (D:) are managed 
by the AHA-1640 BIOS.

On each Interrupt 13 call, the correct host microprocessor registers are set 
by the operating system program to provide the required parameters to both the 
Adaptec BIOS and  the motherboard BIOS.  Most commands use  the registers as  
indicated in Table 5-1.
                                            
                                  TABLE 5-1

           Register      Function
           
             AH         BIOS Function Code
             AL         Number of Sectors
             CH         Low Order Byte of Cylinder Number
             CL         Cylinder and Sector Numbers
                           Bits 7,6      High Order Cylinder Bits
                           Bits 5-0      Sector Number
             DH         Head Number
             DL         Drive Number
             ES:BX      Data Buffer Address
                                                  
                                                  
5.2.1 Physical to Logical Address Translation


As shown  above, the  starting  sector address  for  read, write  and verify  
requests is passed as a physical address including a 10-bit Cylinder Number, 
an 8-bit Head Number, and a 6-bit  Sector Number. SCSI devices are addressed  
by logical block address without regard to the physical layout of the drive.  
For this reason, all SCSI devices are defined as drives with 64 heads and 32 
sectors per track and with the appropriate number of cylinders to provide the 
full capacity of the  drive using this physical  to logical translation. The  
SCSI logical address is formed by the BIOS by concatenating the values as show 
below:

Cylinder(10 bits) || Head(6 bits) || Sector(5 bits) = SCSI Logical Block Address


                                 5-2

Section Five                                Single-Threaded Software Interface 
------------------------------------------------------------------------------

5.2.2 BIOS Command Return Codes

The BIOS command, when complete, returns control to the requesting program at 
the next instruction after the  software interrupt. A return  code is set in  
the Carry Flag (CF) and a status code is placed in register AH for examination 
by the requesting  program. The  expected return  codes placed  in the Carry  
Flag follow.

           CF Contents at Return      Return Code
           --------------------------------------- 
           CF = 1 Status is non-zero. Unusual condition or error detected.  
           
           CF = 0 Status is zero.     Normal command completion occurred.
           
           
           AH Contents at Return Status of Operation
           -----------------------------------------
           AH = 00H              No error: The operation completed successfully.
           
           AH = 01H              Invalid Function Request: The operation    
                                 code or an associated parameter provided  
                                 by the  Interrupt 13 operation  was not  
                                 valid.
           
           AH = 02H              Unable to Read Address  Mark: One  of the   
                                 following additional  sense  codes (SCSI  
                                 ASC)  was   presented   in   the   sense   
                                 information returned by the REQUEST SENSE 
                                 command:
                                   
                                   12H (No AM Found on Data Field) 
                                   21H (Illegal Logical Block Address)
           
           AH = 03H              Write Protect Error: Returned SCSI ASC was:
                                   
                                   27H (Data Protect)
           
           AH = 04H              Read Error: Returned SCSI ASC during a   
                                 read operation was:
                                   
                                   14H (No Record Found)
                                   16H (Data Sync Error)
           
           AH = 10H              Uncorrectable ECC Error in Data: Returned   
                                 SCSI ASC during a read operation was:
                                   
                                   10H (ID ECC Error)
                                   11H (Unrecovered Read Error)
           
           AH = 11H              ECC Corrected Data Error: Returned SCSI    
                                 ASC during a read operation was:
                                   
                                   17H (Recovered Read Error w/o ECC)
                                   18H (Recovered Read Error w/ ECC)
           
           AH = 20H              General Controller Failure: A host     
                                 adapter detected failure occurred or one  
                                 of the following SCSI ASC's was returned:
                                   
                                 5-3

Section Five                                Single-Threaded Software Interface 
------------------------------------------------------------------------------


                                   01H   08H    40H     46H
                                   03H   09H    41H     47H
                                   05H   1BH    42H     48H
                                   06H   1CH    43H     49H
                                   07H   1DH    44H     

           
           AH = 40H              Seek Operation Failed: Returned SCSI ASC was:
                                   
                                   15H  (Seek Positioning Error)
                                   02H  (No Seek Complete)
                                  
           AH = 80H              Selection Time-out: A host adapter does not 
                                 respond to BIOS.
           
           AH = AAH              Device Not Ready: Returned SCSI ASC was:
                                   
                                    04H  (LUN Not Ready)
                                    28H  (Unit Attention, Ready)
                                    29H  (Unit Attention, Power On)
                                    2AH  (Unit Attention, Mode Select Change)
                                   
           AH   =   BBH          Unknown Target Sense Error Occurred: A    
                                 SCSI ASC other than those specified above 
                                 was  returned from the selected SCSI device.
           
           AH = CCH              Write Error:  Not Returned
           
           AH = FFH              Sense Operation Failed: BIOS unable to    
                                 retrieve sense information from target.
           
           
5.3 BIOS DISK COMMANDS


The commands that  can be  accepted from  the operating  system by  the BIOS  
include all those commands required for normal DOS operation, for booting of 
the DOS operating system, for the booting of other operating systems and for  
basic maintenance and verification of normal disk operation. The command set  
is summarized in table 5-2 and each command is described in more detail in the 
sections following.

           AH Register            Meaning
           
             00 H                Reset Disk System
             01 H                Read Status of Last Operation
             02 H                Read Desired Sectors into Memory
             03 H                Write Desired Sectors from Memory
             04 H                Verify Desired Sectors
             06 H                Identify SCSI Devices
             08 H                Read Drive Parameters
             09 H                Initialize Drive Pair Characteristics
             0C H                Seek
             0D H                Alternate Disk Reset
             10 H                Test Drive Ready
             11 H                Recalibrate
             15 H                Read DASD Type
                                 
                 
                                 5-4

Section Five                                Single-Threaded Software Interface 
------------------------------------------------------------------------------

                               TABLE 5-2
                                                  
                                                  
The Format commands  (AH =  05, 06, 07,  and 1AH)  are not supported  by the  
AHA-1640 BIOS.  The format  operation is  performed  under a  special format  
utility installed in ROM and initiated through the DEBUG program.

The Diagnostic Reserved commands (AH = 0A, 0B,  0E, 0F, 12, and 14H) are not 
supported by the AHA-1640 BIOS. 

The Park Heads command (AH = 19H) is not supported by the AHA-1640 BIOS.

The Reserved for Diskette commands (AH = 16, 17, 18) and the commands from 1BH 
up to FFH are not supported by the AHA-1640 BIOS. Any attempt to execute any 
of these unsupported commands will be ended by the BIOS and Carry Flag will be 
set to one. An error code of 01H (Invalid Function Request) will be returned 
in the AH register.


5.3.1 Reset Disk System


The BIOS is requested to reset the disk subsystem. A SCSI Reset operation is 
performed on the SCSI bus if the bus is busy at the time the Reset Disk System 
command is  received by  the host  adapter.  No other  SCSI or  host adapter  
activity occurs. The BIOS command is then  passed on to the standard BIOS so  
that any internally installed hard disks and floppy disk devices can also be  
reset. If the  BIOS is operating  concurrently with  an internally installed  
hard disk, the drive number is temporarily decremented by the AHA-1640 BIOS so 
that the  standard BIOS  does not  attempt to  reset the  drive that  is not  
installed.

Input Parameters:       AH = 00H
                        DL = Drive Number (80H or 81H)
                       
Output Parameters:      AH = Status of Operation
                        CF = Return Code

5.3.2 Read Status of Last Operation


The status of the last operation performed to the specified disk is returned. 
No SCSI activity occurs. The disk status is reset to zero.

Input Parameters:      AH = 01H
                       DL = Drive Number (80H or 81H)

Output Parameters:     AH = Status of Operation
                       CF = Return Code


5.3.3 Read Desired Sectors Into Memory


The sectors requested by the parameters are read from the disk to the system 
memory. The  SCSI command  is executed  as a  READ (EXTENDED)  command (SCSI  

                                 5-5

Section Five                                Single-Threaded Software Interface 
------------------------------------------------------------------------------

Operation Code 28H). If the operation fails and an error is reported through  
the BIOS status byte, the operation should  be retried one time. If a status  
of ECC Corrected Data Error (AH=11H) is returned, the data returned has been  
corrected and may be used with confidence. 

Input Parameters:      AH = 02H
                       DL = Drive Number (80H or 81H)
                       DH = Head
                       CH = Cylinder
                       CL = High Cylinder and Sector
                       AL = Number of Sectors to Read
                       ES:BX = Address of buffer area

Output Parameters:     AH = Status of Operation
                       CF = Return Code
                       
5.3.4 Write Desired Sectors from Memory

The sectors requested by the parameters are written from the system memory to 
the indicated  disk. The  SCSI  command is  executed  as a  WRITE (EXTENDED)  
command (SCSI Operation Code  2AH). If the  operation fails and  an error is  
reported through the BIOS  status byte, the operation  should be retried one  
time. 

Input Parameters:      AH = 03H
                       DL = Drive Number (80H or 81H)
                       DH = Head
                       CH = Cylinder
                       CL = High Cylinder and Sector
                       AL = Number of Sectors to Write
                       ES:BX = Address of buffer area

Output Parameters:     AH = Status of Operation
                       CF = Return Code
                       

5.3.5 Verify Desired Sectors 

The sectors defined by the parameters are verified to be correctly written on 
the SCSI  disk. The  SCSI  command is  executed  as a  VERIFY  command (SCSI  
Operation 2F) with the Byte Check bit set  to zero. If the VERIFY command is 
not supported by the selected disk, the Verify Desired Sectors will perform a 
SCSI READ command (SCSI Operation Code 28H) and throw away the received data. 
If the operation fails and an error is reported through the BIOS status byte, 
the operation should be retried one time. 

Input Parameters:      AH = 04H
                       DL = Drive Number (80H or 81H)
                       DH = Head
                       CH = Cylinder
                       CL = High Cylinder and Sector
                       AL = Number of Sectors to Verify

Output Parameters:     AH = Status of Operation
                       CF = Return Code

                                 5-6

Section Five                                Single-Threaded Software Interface 
------------------------------------------------------------------------------

5.3.6 Identify SCSI Devices

This is a special AHA-1640 BIOS call that is used to return the number of the 
first supported SCSI drive. The BIOS call returns information obtained during 
initialization of the BIOS  to determine what SCSI  drives are available. If  
the Carry Flag is set, the 1640 BIOS  is not installed or no SCSI drives are  
available under the  BIOS. In  the nonconcurrent  case (2  SCSI drives), the  
returned value will be 80H. If only one SCSI drive is installed, the returned 
value will be 81H. 
 
Input Parameters:      AH = 06H

Output Parameters:     AH = Status of Operation
                                     not set
                       BX = First Drive Supported
                       80H           Nonconcurrent operation
                       81H           Concurrent operation
                       CF = Return Code
                       0             BX information is valid
                       1             BIOS not installed or no BIOS SCSI drives
                        

5.3.7 Read Drive Parameters


A SCSI READ CAPACITY command is used to determine the maximum logical block of 
the selected drive.  This information is  then used to  calculate the proper  
number of cylinders to be  returned to the host system.  The number of heads  
returned will always be 64 and the number of sectors per track will always be 
32. The number  of drives  returned will  include both  internally installed  
drives and SCSI drives.

Input Parameters:      AH = 08H
                       DL = Drive Number (80H or 81H)

Output Parameters:     AH = Status of Operation
                       DL = Number of BIOS accessible drives attached (1 or 2)
                       DH = Maximum value for head number (3FH)
                       CH = Maximum value for Cylinder Range (Low Byte)
                       CL = Maximum value for Sector, High Cylinder Bits
                       Bits 7,6         High Order Cylinder Bits
                       Bits 5-0         Sector Number Maximum Value ( 20H)
                       CF = Return Code


5.3.8 Initialize Drive Pair Characteristics


This command performs no operation, since SCSI CCS drives are self configuring. 

Input Parameters:      AH = 09H
                       DL = Drive Number (80H or 81H)

Output Parameters:     AH = Status of Operation
                       CF = Return Code

                                 5-7

Section Five                                Single-Threaded Software Interface 
------------------------------------------------------------------------------

5.3.9 Seek


A seek to the  logical block address  defined by the  physical parameters is  
performed. The seek  is performed  using the  SEEK (EXTENDED)  command (SCSI  
Operation 2BH). The SEEK commands are not mandatory CCS commands and are not  
required for proper functioning of SCSI devices. If the addressed disk drive 
reports an error indicating that the SEEK (EXTENDED) command is not supported, 
the BIOS command will complete normally anyway. 


Input Parameters:      AH = 0CH
                       DL = Drive Number (80H or 81H)
                       DH = Head
                       CH = Cylinder
                       CL = High Cylinder. (Sector bits = 0)

Output Parameters:     AH = Status of Operation
                       CF = Return Code
                       

5.3.10 Alternate Disk Reset


The BIOS is requested to reset the disk subsystem. A SCSI Reset operation is 
performed on the SCSI bus if the bus is busy at the time the Reset Disk System 
command is  received by  the host  adapter.  No other  SCSI or  host adapter  
activity occurs. The BIOS command is then  passed on to the standard BIOS so  
that any internally installed hard disks and floppy disk devices can also be  
reset. If the  BIOS is operating  concurrently with  an internally installed  
hard disk, the drive number is decremented  by the AHA-1640 BIOS so that the  
standard BIOS does not attempt to reset the drive that is not installed.

Input Parameters:      AH = 00H
                       DL = Drive Number (80H or 81H)

Output Parameters:     AH = Status of Operation
                       CF = Return Code


5.3.11 Test Drive Ready


The BIOS command determines that the specified drive is available and ready by 
executing a TEST UNIT  READY command (SCSI  Operation Code 00H)  to the SCSI  
device. The command may have to be executed a second time if a Unit Attention 
condition was detected in the first execution of the TEST UNIT READY.

Input Parameters:      AH = 10H
                       DL = Drive Number (80H or 81H)

Output Parameters:     AH = Status of Operation
                       CF = Return Code

                                 5-8

Section Five                                Single-Threaded Software Interface 
------------------------------------------------------------------------------

5.3.12 Recalibrate

The BIOS command transmits a REZER0 UNIT command (SCSI Operation Code 01H) to 
the specified drive. Since the REZERO UNIT command is not a mandatory command 
and is not  required for  proper functioning  of the  SCSI device,  the BIOS  
command will complete  without indicating an  error even if  the SCSI device  
indicates that the command is invalid.

Input Parameters:      AH = 11H
                       DL = Drive Number (80H or 81H)

Output Parameters:     AH = Status of Operation
                       CF = Return Code

5.3.13 Read DASD Type

The AHA-1640  BIOS  executes this  command  by performing  an  INQUIRY (SCSI  
Operation Code 12H)  and a  READ CAPACITY (SCSI  Operation Code  25H) to the  
selected SCSI drive. The INQUIRY command is used to verify that the device is 
a Direct Access Storage Device.  The READ CAPACITY is  used to determine the  
number of logical blocks available. A special return format is used to obtain 
the required information.

Input Parameters:      AH = 15H
                       DL = Drive Number (80H or 81H)
Output Parameters:     AH = Status of Operation (Special Format)
                        
                          00H      Drive not present or DL invalid
                          01H      Reserved
                          02H      Reserved
                          03H      Fixed Disk installed

                       CX,DX    Number of 512 byte blocks available on disk
                       CF = Return Code


                                 5-9

Section Six                                                    Device Drivers 
------------------------------------------------------------------------------

6.1 PS/2 COMPATIBLE POS INITIALIZATION

Section 3 describes the initialization procedure required to enable the host  
adapter and to program the address spaces, interrupts, and hardware controls  
associated with the Programmable Option Select. The Adapter Description File 
(ADF) required for  the initialization procedure  is named  @0F1F.ADF and is  
normally included on  the System  Reference Diskette  for the  host computer  
system. If desired, a specialized ADF can be prepared using the POS register  
information specified in  Section 4.2  and the  format specified  by the IBM  
Technical Reference manuals.

Once the installation process is complete, the initialization program in the  
system BIOS automatically obtains the required POS information from the CMOS  
Ram non-volatile memory in the host system and transfers it to the correct POS 
registers whenever the  system is  powered up.  No operator  intervention is  
required to initialize the adapter at power-up time.


6.2 PS/2 COMPATIBLE BIOS


The PS/2 Compatible BIOS is provided to allow the user to use the AHA-1640 in 
lieu of, or in addition  to, a standard Micro  Channel hard disk controller.  
This compatibility includes booting from a SCSI device. Hard disk requests are 
sent to the  BIOS via  an INT 13  software interrupt.  CPU register contents  
specify the desired I/O function and associated parameters. The BIOS then uses 
host adapter IOCP commands to emulate  Micro Channel functions. Again, since  
the mailbox architecture is circumvented, Micro Channel BIOS functions run in 
a single-threaded mode.

The BIOS consists of three major functional components. These are:

1. Initialization Routine
2. System Boot Routine
3. Hard Disk I/O Routine


6.2.1 Initialization


The Initialization routine is called at power-up. This routine performs all of 
the necessary initialization functions and will display the following message 
if the system successfully recognizes the AHA-1640 BIOS.

  Adaptec AHA-1640 BIOS
  Copyright 1988 Adaptec, Inc.
  All Rights Reserved.

If any subsequent initialization of the AHA-1640 fails, the following message 
is displayed:

  HOST ADAPTER NOT FOUND AT PORT [address specified in POS registers].

                                 6-1

Section Six                                                    Device Drivers 
------------------------------------------------------------------------------

Otherwise, the AHA-1640 BIOS chooses a course of action based upon the number 
and types of hard disks already installed.  In each case, the number of hard  
disks already installed is displayed  along with the ID  numbers of any SCSI  
devices that are successfully used by the BIOS. No error message is displayed 
if a second SCSI drive is not available.

Possible Messages:

  HARD DISK C: ALREADY INSTALLED.
  HARD DISK D: ALREADY INSTALLED.
  HOST ADAPTER DIAGNOSTIC FAILURE.
  SCSI DEVICE 0 : 0 NOT FOUND.
  USING SCSI DEVICE 0 : 0 AS HARD DISK C:
  USING SCSI DEVICE 0 : 0 AS HARD DISK D:
  USING SCSI DEVICE 0 : 1 AS HARD DISK D:
  USING SCSI DEVICE 1 : 0 AS HARD DISK D:

If the system reports an  initial number of hard drives  greater than 2, the  
following message is displayed:

  SYSTEM CONFIGURATION ERROR.


The AHA-1640 BIOS allows the use of zero, one, or two hard disks on the SCSI  
bus under DOS without a device driver.

If two hard disks are attached to  an internal hard disk controller, and are  
already recognized by the system, the BIOS does nothing. A device driver will 
be needed to access SCSI devices.

If one hard  disk is attached  to an  internal hard disk  controller, and is  
already recognized by the system, the BIOS attempts to assign the SCSI device 
(Target : LUN) 0 : 0 as the second drive. (drive D:) If this is unsuccessful, 
an initialization error is reported to the system.

If there are zero  hard disks attached  to an internal  controller, the BIOS  
attempts to assign the first SCSI  device (Target : LUN) 0  : 0 as the first  
drive (drive C:). If this is unsuccessful, an initialization error is reported 
to the system. If successful, the BIOS attempts to assign another SCSI device 
as the second drive.  (drive D:) Device  0 : 1  is tried first,  and if that  
fails, device 1 : 0 is tried. There is no initialization error reported if a 
second drive is not available.


6.2.2 System Boot


System boot is invoked by  execution of an Interrupt  19. No interception of  
this interrupt is necessary, as the PS/2 BIOS manages the boot process. When  
the boot procedure attempts to read the boot track from drive C:, the AHA-1640 
BIOS will respond if drive  C: is a SCSI Drive.  Motherboard BIOS's that use  
interrupt 13 to perform booting should boot  normally from SCSI drives using 
the AHA-1640.


6.2.3 Hard Disk I/O


The BIOS enables up  to two SCSI drives  to be accessed  via interrupt 13 as  
described in Section Five.

                                 6-2

Section Six                                                    Device Drivers 
------------------------------------------------------------------------------

6.3 XENIX/UNIX DRIVERS

SCO  XENIX  support  will  be   available  at  production  release.  Generic   
(non-bootable) Xenix and Unix drivers are available for OEM integration.

6.4 DOS DRIVER

An optional  DOS Driver  is available  that enables  the AHA-1640  to access  
additional SCSI devices on the SCSI bus.  When operating under DOS, a device  
driver is needed to access  more than two hard disks,  tape devices or other  
types of SCSI peripherals. If all DOS operations will be confined to two SCSI 
disks or one internal and one SCSI disk, a device driver is not needed because 
of the on-board BIOS.

The DOS driver is installed by creating a DOS configuration (CONFIG.SYS) file 
that calls the device driver at boot time. Please refer to your DOS manual for 
information on creating  a CONFIG.SYS file.  At initial  system loading, the  
AHA-1640 device driver will determine the number of hard disks attached to the 
system. The device driver is normally only installed if one of the following  
cases is true.

1) There are two internal hard disks and one or more SCSI disks.
2) There is one internal hard disk and two or more SCSI disks.
3) There are no internal hard disks and more than two SCSI disks.


Table 6-1 shows how hard disks in a system are addressed:

           TABLE 6-1. DISK CONFIGURATIONS FOR DOS WITHOUT DRIVERS
                                            
                          [Picture]
                                            
                                            
The SCSI disk drives that are accessed by the device driver are 
divided into  32 Mbyte  logical  disks. There  can  be multiple  
logical disks on one physical SCSI disk drive. A utility program 
is also provided that performs the functions of the DOS FDISK and 
FORMAT utilities. This utility will perform FDISK and FORMAT to  
SCSI disks that can only be accessed through the device driver.  
These utility  programs  partition the  disks  and  create file  
directories so that DOS  files may be  copied and accessed from  
SCSI drives. Please refer to your DOS manual for details of FDISK 
and FORMAT.

SCSI II compatible and QIC 104 command set 1/4" tape drives are 
also be supported by the DOS device driver. The user accesses a 
SCSI tape drive by building a CCB as described in Section Five. 
The device driver passes the CCB  to the AHA-1640 and instructs  
the AHA-1640 to complete the command.

                                 6-3

Section Six                                                    Device Drivers 
------------------------------------------------------------------------------

6.5 OS/2 DRIVER AVAILABILITY

Contact Adaptec for information on OS/2 support.

6.6 VIRTUAL MEMORY DRIVER

Programs that make  use of the  V86 mode (Virtual  Mode) of the  
80386 while using the  interrupt 13 interface  of the BIOS will  
require a  special software  driver.  The driver  functions are  
already included in the Adaptec DOS  driver. If the system does  
not make use of the Adaptec DOS driver, a special software driver 
is available that  will allow this  type of  application to run  
under DOS.  Installation  instructions  are  provided  with the driver.

6.7 AHA-1640 ON-BOARD UTILITIES

The AHA-1640 BIOS contains a utility program that allows the user 
to perform several important functions. The utility programs are 
accessed using a self-explanatory menu. 

The utilities  are accessed  using the  DOS Debug  function. To  
access the utilities, boot using a  standard DOS system disk or  
diskette. When the  > prompt symbol  is appears  on the screen,  
enter the debug program by typing debug and pressing Enter. The  
debug program will load and present a new cursor, the - symbol. 
Enter the following line and press enter to invoke the On-board  
Utility program.

                            G=dc00:6

If a BIOS base address  other than DC000H is  being used on the  
adapter to be tested, replace the dc00 parameter with the actual 
BIOS base segment. The segment  is the upper 16  bits of the 20  
bit BIOS base address.

The menu options include the following items which are selected  
by pressing the index number of the menu function.

(1) A list of all devices installed on the SCSI bus may be requested. 
This information is retrieved via a RETURN INSTALLED DEVICES host 
IOCP command, followed by INQUIRY commands to all available 
targets. 

(2) A device may be selected for execution of the following two 
functions. Pressing the '2' key  toggles the selection from one  
installed device to the next. 

(3) A low-level, or primary, format of the selected Target/LUN can be 
requested. A MODE SELECT is issued first to set the block size at 
512 bytes per sector. Then a FORMAT command is issued which will 
format the drive with factory as well as grown defects.  Only 
one SCSI drive can be formatted at a time.

                                 6-4

Section Six                                                    Device Drivers 
------------------------------------------------------------------------------

(4) Integrity of a target can be checked by verifying an entire 
drive. Any correctable errors found will automatically be handled 
through the SCSI Reassign Blocks Command. If any uncorrectable 
errors are found the user will first be asked via a screen prompt 
if reassignment of the effected block should be performed.

(5) The user can leave  the AHA-1640 On-board Utility functions  
and return to normal DOS operation.

6.8 THIRD PARTY SOFTWARE SUPPLIERS FOR AHA-1640

This is a partial list of  the third party software and support  
suppliers for the AHA-1640. 

SCO Xenix

  The Santa Crux Operation, Inc.
  400 Encinal Street
  P.O. Box 1900
  Santa Cruz, CA 95061
  (408) 425-7222

Unix

  Interactive Systems Corporation
  2401 Colorado Avenue
  Santa Monica, CA 90404
  (213) 453-8649 (Contact Sales Department)

Unix   

  Microport Systems, Inc.
  10 Victor Square
  Scotts Valley, CA 95066
  (800) 722-8649

SYTOS (SYTRON Tape Operating System)

  Sytron Corporation
  135 Maple Street
  Marlboro, MA 01752
  East Coast : (617) 460-0106  (Contact William Mason)
  West Coast: (415) 558-8533  (Michael Evans)

Novell 2.1

  Ontrack Computer Systems
  6200 Bury Drive
  Eden Prairie, MN 55346
  (612) 937-11-7

                                 6-5

Section Seven                                                    SCSI Features 
------------------------------------------------------------------------------

7.1 SCSI DESCRIPTION, INITIATOR MODE

The AHA-1640 provides  a very  high performance  SCSI interface  
connection.  The   host   adapter  meets   the   ANSI  Standard   
X3.131-1986, describing the SCSI. The host adapter additionally  
meets conformance level 2 of  the specification by implementing  
the following SCSI options:

Accepts or manages the following messages:
         
  Command Complete
  Disconnect  
  Message Reject
  Identify
  Save Data Pointer
         
Performs arbitration
         
The following alternatives  are selected for  the AHA-1640 SCSI  
interface connection from those described by X3.131-1986.

Single-ended SCSI driver/receivers are used.
         
The Termination Power is supplied through a removable fuse, 
allowing the user to select whether or not termination power 
is provided at installation time.
         
Parity is always generated. Parity checking can be disabled 
through the POS registers.
         
The "Soft" Reset option is always performed by the AHA-1640. 
If the user desires the "Hard" Reset, an interrupt servicing 
program that detects the SCSI  Reset Detected interrupt in  
the Interrupt Flags Port must set the Soft Reset bit in the 
Control Port. This bit forces the host adapter to clear all 
SCSI related operations, but does not require execution of  
the diagnostic functions. 
         
Synchronous data transfer is supported. Negotiation for the 
synchronous transfer initiated by another SCSI device will  
be accepted  by  the  AHA-1640 at  any  time.  If  the POS  
registers have been initialized to  allow it, the AHA-1640  
will also initiate  synchronous data  transfer negotiation  
when it has detected that such negotiation may be required.
         
Multitasking is fully supported.
         
Modify Data Pointers is supported to allow Zero Latency Read 
operations.
         
In addition to these SCSI functions, the SCSI Common Command Set 
at level  4B  is  supported  in  the  BIOS  for single-threaded  

                                 7-1

Section Seven                                                    SCSI Features 
------------------------------------------------------------------------------

operation. While the CCS document was never made a standard, it  
describes a widely available set  of disk drive functions which  
are supported  by  the  host  adapter.  The  Host  Adapter BIOS  
commands are all  mapped in to  SCSI CCS commands  to allow the  
proper support of all the most common SCSI disk drives. The IOCP 
command "Return Installed  Devices" also  uses CCS  commands to  
determine which devices are available. The CCS commands used are 
compatible with the SCSI-2 draft documents.

The draft ANSI standard for SCSI-2 has been used as a reference 
for the implementation of all SCSI functions with the expectation 
that the host adapter  will be fully  compatible with the final  
version of the  SCSI-2 standard.  In particular,  the Processor  
type device command set has been selected from the SCSI-2 manual 
for Target Mode operation.

7.1.1 Linked SCSI Commands

The AHA-1640 supports linking of SCSI commands. When the link bit 
in the SCSI command control byte is set, the target will present 
either a 0A or  0B message at  command completion. The AHA-1640  
uses the the link pointer in a CCB to fetch another CCB. At the 
same time, the completed CCB status and address are stored in an 
MBI. If the target returns the 0B status, the AHA-1640 generates 
an interrupt to inform the host of the full MBI. The linked CCBs 
must address the  same target and  LUN since the  target is not  
re-selected. 

7.1.2 Zero Latency Read Operation

The AHA-1640 implements Zero Latency operation through the use of 
modify  data  pointer  messages.  Zero  Latency  can  eliminate   
rotational latency, depending on the length of the data transfer, 
by supporting out of order data transfers. This advanced feature 
is currently  only implemented  on the  ACB-4525Z SCSI  to ESDI  
controller, and is supported transparently to the user.

Since the Adaptec host  adapter family is  the first to support  
Zero Latency Read operation, this section is intended to briefly 
explain the required target support. Please refer to the Adaptec 
ACB-4525Z SCSI-to-ESDI controller manual for complete details of 
Zero Latency Read operation.

After seeking to the target track,  the ACB-4525Z or other disk  
device having the Zero Latency  Read feature will begin reading  
block IDs. If the  first block ID  is within range  of the data  
transfer, but is not the last block of the the data transfer, the 
ACB-4525Z will  begin reading  the  subsequent blocks  into its  
buffer. Before transferring  data, the  ACB-4525Z will  issue a  
MODIFY DATA POINTER  message to  the AHA-1640.  This supplies a  
positive number that is added to  the value of the current data  
pointer. The  ACB-4525Z  will now  send  the data  to  the host  
beginning at this point in the data blocks to be transferred. The 
ACB-4525Z will resume reading data into its buffer as soon as the 
first block of the data blocks to be transferred is found. Before 
sending this data to the host, the ACB-4525Z will issue a second 
MODIFY DATA POINTER message to the AHA-1640 which adds a negative 
number to the value  of the current data  pointer to return the  
data pointer  to  the  beginning  of  the  data  blocks  to  be  
transferred. This guarantees that a data transfer of one track or 
less will never require more than a single revolution since data 
can now be transferred out of order.

                                 7-2

Section Seven                                                    SCSI Features 
------------------------------------------------------------------------------

7.2 SCSI DESCRIPTION, TARGET MODE

7.2.1Initiator Conformance Level Requirements

Initiators that execute commands  against an AHA-1640 operating  
in Target Mode are  required to have  the following conformance  
levels, as described in  Appendix E of  the SCSI Specification,  
ANSI X3.131-1986. Conformance  must be present  with respect to  
each of the following items:

The initiator must use single-ended drivers. 
    
Termination power may optionally be  provided by the initiator,  
but must meet the  SCSI specification in  both its over-current  
protection  and  its  reverse  current  diode  protection.  The   
terminators may be installed on the AHA-1640 board or installed  
as in-line terminators at the cable connectors.
    
The implementation of parity is optional, but desirable. 
    
The initiator may support either  "hard" reset or "soft" reset.  
All attached devices must support the same type of reset. 
    
The initiator must  meet the requirements  of conformance level  
two. In particular, all LUN addressing must be performed by the  
IDENTIFY message, not by the LUN field in the CDB. 
    
Disconnection and reconnection must be supported.
    
The initiator  and  target  functions have  the  same  SCSI ID,  
selected by the POS Registers.

7.2.2 Support of Synchronous Transfer

Synchronous transfer is supported by the AHA-1640 in target mode 
without any instruction or support from the system processor. If 
an initiator  invokes a  synchronous transfer  negotiation, the  
AHA-1640 will complete the negotiation of the required transfer  
offset and period. If the proper POS register bits have been set, 
the AHA-1640 will also attempt to negotiate synchronous transfer 
during the initial selection period of the first command after an 
initialization or after a SCSI reset.

7.2.3 SCSI Target Operation in Processor Target Mode

When the AHA-1640 has  been set to  respond in Processor Target  
Mode, the  host adapter  appears on  the SCSI  bus as  a normal  
processor type device as defined by the SCSI specification. From 
one to eight LUNs  may be supported, depending  on the LUN mask  
byte in the Enable  Target Mode command.  Six SCSI commands are  
accepted:

           TEST UNIT READY  
           REQUEST SENSE 
           INQUIRY 
           SEND
            RECEIVE
            SEND DIAGNOSTIC

                                 7-3

Section Seven                                                    SCSI Features 
------------------------------------------------------------------------------

All other commands are rejected with CHECK CONDITION status. The 
sense information  will indicate  a Sense  Key of  05H (Illegal  
Request) with a  Sense Code  of 20H  (Invalid Command Operation Code).

The commands that do  not perform data transfer  to or from the  
host are  handled  completely  by  the  AHA-1640  with  no  CCB  
communication with the host system. Those commands are the TEST  
UNIT READY, REQUEST SENSE, SEND DIAGNOSTIC and INQUIRY commands. 
The SEND  and  RECEIVE  commands must  either  already  have or  
successfully request  a  CCB  from  the  host  with  the proper  
direction bits, the proper initiator address, and the proper LUN 
number to complete the SCSI operation.

Each time an initiator activates a  command to the AHA-1640, an  
internal sub-channel is  activated to  manage the  command. The  
sub-channel  is  dedicated  to  that  particular  LUN-Initiator   
transaction until all operations associated with the command are 
completed. Such operations include disconnection to obtain a CCB 
and pending error conditions.  If all sub-channels  are busy, a  
selection to the AHA-1640 will result in the AHA-1640 accepting  
the command and then generating BUSY status immediately. If this 
occurs, the initiator  must re-issue  the command  later. There  
are 112 sub-channels available, so it is very unusual for a busy 
indication to be required.


7.2.3.1 Test Unit Ready


                           [Picture]
                                     
    FIGURE 7-1. COMMAND DESCRIPTOR BLOCK FOR TEST UNIT READY
                                     
                                     
The TEST UNIT READY command  follows the SCSI specification. If  
the AHA-1640  has been  initialized by  the Enable  Target Mode  
command to the Processor  Target Mode, the  command will finish  
normally with GOOD status  and a COMMAND  COMPLETE message. The  
host adapter supports the normal definition of UNIT ATTENTION on 
the first operation after power on, after a SCSI Reset, or after 
a BUS DEVICE RESET.

If a TEST UNIT READY command is executed against an LUN which was 
not allowed  by  the  Enable Target  Mode  command,  then CHECK  
CONDITION status will be presented with sense data of Sense Key 5 
(Invalid Request) and an Error Code of 25H (Invalid LUN).

                                 7-4

Section Seven                                                    SCSI Features 
------------------------------------------------------------------------------

7.2.3.2 Request Sense


                           [Picture]
                                     
     FIGURE 7-2. COMMAND DESCRIPTOR BLOCK FOR REQUEST SENSE
                                     
                                     
If the AHA-1640 has returned CHECK CONDITION status to a previous 
command, the  REQUEST  SENSE  command  will  obtain  the  sense  
information associated  with the  error. The  sense information  
will be sent in the extended sense format according to the SCSI 
standard. The data format is given in the following Figure:

                           [Picture]
                                     
                 FIGURE 7-3. REQUEST SENSE DATA
                                     
                                     

                                 7-5

Section Seven                                                    SCSI Features 
------------------------------------------------------------------------------


The following errors are detected and presented by the AHA-1640  
while operating in Processor Target Mode:

  Error                               Sense       Sense 
                                       Key         Code
  
  No Sense Data                        00          00
      (Incorrect Length Indication may be present) 
  Invalid Command Operation Code       00          20
  Invalid LUN                          05          25 
  Invalid Command Parameter            05          26
  Power Up Attention                   06          29
  Reset Attention                      06          29
  Interface Parity Error               0B          47
  Initiator Detected Error             0B          48
  
One set of error data  may be buffered for  each initiator - LU  
association possible, up to a total of 56 sets of sense data. No 
Contingent Allegiance or Extended Contingent Allegiance state is 
established.

                                 7-6

Section Seven                                                    SCSI Features 
------------------------------------------------------------------------------

7.2.3.3 Inquiry


                           [Picture]
                                     
        FIGURE 7-4. COMMAND DESCRIPTOR BLOCK FOR INQUIRY
                                     
                                     
The INQUIRY  command  provides  the  information  necessary  to  
uniquely identify  the  Adaptec  AHA-1640  as  a Processor-type  
device. The following information is  returned to any selecting  
initiator from any selected AHA-1640 Logical Unit:

                           [Picture]

                    FIGURE 7-5. INQUIRY DATA
                                     


                                 7-7

Section Seven                                                    SCSI Features 
------------------------------------------------------------------------------

If a length shorter than the  required 36 bytes is specified by  
the INQUIRY command, the number of bytes specified by the command 
is transferred. If a length longer  than 36 bytes is specified,  
the command will only transmit 36 bytes.


7.2.3.4 Send Diagnostic


                           [Picture]

    FIGURE 7-6. COMMAND DESCRIPTOR BLOCK FOR SEND DIAGNOSTIC
                                     
                                     
The SEND  DIAGNOSTIC  command  invokes  a  subset  of  the host  
adapter's initial power-on diagnostics to  verify that the host  
adapter is fully functional. The  only diagnostic function that  
may be requested is  the Self Test function.  A request for any  
other function will cause an error of Invalid Command Parameters 
to be posted. Normal  completion of the  diagnostic function is  
indicated by GOOD status. Detection of a failure is indicated by 
CHECK CONDITION status and the posting of the appropriate error  
condition.

7.2.3.5 Send


                           [Picture]

         FIGURE 7-7. COMMAND DESCRIPTOR BLOCK FOR SEND
                                     
                                     
The SEND command has the format specified by the SCSI standard.

                                 7-8

Section Seven                                                    SCSI Features 
------------------------------------------------------------------------------

The SEND command transfers data from the initiator to the target. 
The  information  is  placed  in  the  area  specified  by  the   
appropriate CCB.  If an  appropriate CCB  has not  already been  
provided to the host adapter by the host software, an MBI entry 
requesting the appropriate CCB is sent to the host from the host 
adapter. In this case, the target host adapter disconnects from  
the SCSI until  the CCB is  made available to  the host adapter  
through the MBO protocol. An appropriate CCB must have the same  
initiator address, target LUN, and  direction as is required to  
complete the command.

The transfer length in the SEND command specifies the length in  
bytes of data that is sent during the DATA OUT phase. A transfer 
length of zero  indicates that no  data is  sent. Management of  
incorrect length transfers is described in Section 7.2.4.

The AHA-1640 supports the SEND command  with or without the AEN  
bit set. The CDB information is included in the returned CCB so 
that the receiving host programming can determine whether or not 
the information transmitted by the SEND command was application  
data or asynchronous event notification data.


7.2.3.6 Receive


                           [Picture]
                                     
        FIGURE 7-8. COMMAND DESCRIPTOR BLOCK FOR RECEIVE
                                     
                                     
The RECEIVE command has the format specified by the SCSI standard

The RECEIVE  command  transfers  data from  the  target  to the  
initiator. The information is taken  from the area specified by  
the appropriate CCB. If an appropriate CCB has not already been  
provided to  the  host  adapter  host  software,  an  MBI entry  
requesting the appropriate CCB is sent to the host from the host 
adapter. In this case, the target host adapter disconnects from  
the SCSI until  the CCB is  made available to  the host adapter  
through the MBO protocol. An appropriate CCB must have the same  
initiator address, target LUN, and  direction as is required to  
complete the command.

The transfer length in the RECEIVE command specifies the length  
in bytes  of data  that is  sent  during the  DATA IN  phase. A  
transfer length  of  zero  indicates  that  no  data  is  sent.  
Management of incorrect length transfers is described in Section 
8.3.2.6.

                                 7-9

Section Seven                                                    SCSI Features 
------------------------------------------------------------------------------

7.2.4 Incorrect Length Management

The messages transmitted using the SEND and RECEIVE commands are 
normally expected  to have  a length  that has  previously been  
agreed to by  the initiator system  software and  by the target  
system software. If the transfer length specified by the command 
is equal to  the transfer length  specified by  the CCB, normal  
operation takes place and no errors are posted.

If the transfer length specified  by the initiator's command is  
shorter than  the  space defined  by  the CCB,  all  data bytes  
expected and required by the initiator will be transmitted. The  
AHA-1640 will indicate GOOD status at  the end of the transfer.  
The target system's software however  must be notified that the  
entire area of data  defined by the CCB  was not transmitted. A  
Target Status of GOOD will be presented in the returned CCB. At 
the same time,  the Incorrect Length  Indication bit  (bit 5 of  
byte 2) will be set in the CCB Request Sense data area. Bytes 3 
through 6 of the Request Sense data area will contain the residue 
in two's  complement notation  of the  length requested  in the  
initiator command minus the length of  the data area defined by  
the CCB. In this  case, the residue will  be a negative number,  
since the requested length was less  than the area specified by  
the CCB. The MBI Status  Byte will be set  to 04 (CCB Completed  
with Error) to indicate that the CCB was completed with an error.

If the transfer length specified  by the initiator's command is  
longer than  the space  defined by  the  CCB, only  those bytes  
contained  within  the   CCB's  data  transfer   area  will  be   
transmitted. The AHA-1640 must indicate with an error condition  
to the  initiator that  not all  the  requested bytes  could be  
transferred. The AHA-1640 indicates a CHECK CONDITION at the end 
of the data transfer. The Request Sense information transmitted  
to the initiator as a result of an immediately following REQUEST 
SENSE command indicates that an  Incorrect Length Indication is  
present by setting bit  5 of byte  2. Bytes 3  through 6 of the  
Request Sense  information  transmitted to  the  initiator will  
contain the residue in two's  complement notation of the length  
requested in the initiator command minus the length of the data  
area defined by the  CCB. In this  case, the residue  will be a  
positive number, since the requested length was greater than the 
available area.  The  target  system's  software  must  also be  
notified that the  transfer length  requested by  the initiator  
exceeded the  assigned buffer  area. A  Target Status  of CHECK  
CONDITION will be  presented in the  returned CCB.  At the same  
time, the information that will later be posted to the initiator 
by the REQUEST SENSE command will be posted to the target system 
in the  CCB Request  Sense data  area.  This includes  both the  
Incorrect Length Indicator and the Residue. The MBI Status Byte  
will be set to 04 to indicate that the CCB was completed with an 
error.

                                 7-10

Section Eight                                           Problem Determination 
------------------------------------------------------------------------------

8.1 SELF DIAGNOSTICS 

The AHA-1640 executes self diagnostics upon power-up or after a  
hard reset. These  diagnostics test  the CPU  operation, verify  
that the control program information is correctly recovered from 
the firmware EPROM,  and check the  data transfer  paths on the  
board. If the self diagnostics are not successful, the AHA-1640  
will not identify itself during  the Programmable Option Select  
process and will therefore not be enabled.

The red light emitting diode (LED) on the host adapter indicates 
the result of the self diagnostic  process. When power is first  
applied to  the  board,  the  LED turns  on.  If  the  board is  
operating normally, the light will soon go off and stay off until 
SCSI activity is  requested by  the host.  If the board  is not  
operating correctly, a flash code number  is flashed on the LED  
to indicate  which  test  failed.  The  flash  code  number  is  
indicated by a series of 1 to 6 closely spaced flashes followed 
by a longer pause. The flash code is repeated continuously until 
the board is powered off, reset or repaired. The SCSI interface  
should be disconnected if these  diagnostic tests are being run  
for fault  isolation purposes.  The  flash code  and associated  
failure modes are indicated in table 8-1.


                TABLE 8-1. TABLE OF FLASH CODES
                                     

        FLASH CODE        POSSIBLE MEANINGS OF FLASH CODE

    LED Remains On        Host Adapter Control Processor inoperative.

        1 Flash           Firmware EPROM check sum failed.
                          RAM download failed.

        2 Flashes         RAM test failed.

        3 Flashes         AIC-6250 SCSI protocol chip verification failed

        4 Flashes         FIFO read data path test failed.

        5 Flashes         FIFO write data path test failed.

        6 Flashes         Channel 2 test failed.

                                     
If any  of these  failure  conditions is  identified,  the host  
computer should be powered down, the host adapter removed and the 
host adapter  inspected for  physical  damage. Such  damage can  
include EPROMs that are  not correctly installed  or not firmly  
seated,  broken  wires,  missing   or  damaged  components,  or   
conductive debris on the  board. If no  such physical damage is  
found, the AHA-1640 should be returned for repair. 

                                8-1

Section Eight                                           Problem Determination 
------------------------------------------------------------------------------

All boards are fully  tested, burned in,  cleaned and inspected  
before they are shipped. Care should be taken to keep the board 
in its protective  conductive wrapping  until it  is installed.  
With these simple precautions, mechanical damage can normally be 
avoided.

8.2 INDICATORS

The red  LED  on the  AHA-1640  is  used to  provide  the fault  
isolation information  described  above. In  addition,  the LED  
indicates when the host adapter is performing activities on the  
host interface and the SCSI interface. The LED is such a useful 
activity indicator that a connector is made available on the host 
adapter to allow an externally visible LED to be attached. 

As an activity indicator, the LED is turned on from the time that 
an IOCP command is transmitted to the host adapter until the HACC 
interrupt is  generated to  indicate that  the IOCP  command is  
complete. In addition, the LED will  be turned on whenever SCSI  
bus activity is occurring.  This is roughly  the same period of  
time that the SCSI BSY signal is present on the SCSI bus. If the 
light stays on when no activity is expected to be present on the 
bus, it  is  possible that  the  bus is  hung,  that unexpected  
activity is occurring or  that the SCSI  cables are incorrectly  
installed.

8.3 PROBLEM CORRECTION

The AHA-1640, other Micro Channel compatible components, and the 
attached peripheral devices are very reliable devices because of 
the high level of circuit integration in their design. Failures  
are so rare that most such devices use symptoms to identify the 
failing unit and use replacement of the failing unit to correct  
the failure. The  AHA-1640 has only  one replaceable component.  
If no  installation error  or mechanical  damage is  present, a  
failing AHA-1640  must be  replaced. The  AHA-1640 can  only be  
repaired at a qualified repair facility. This section presents a 
list of possible error symptoms together  with a list of likely  
corrective actions.

8.3.1 Common Problems during Installation

The description of installation problems and probably corrections 
is given in Section 3.2.4.

8.3.2 IOCP Command Errors and Corrective Actions

Operation of the I/O Port interface is controlled and monitored  
by host system software. Two bits in the Status Port (Base + 0), 
described in Section  4.4.1, are  provided to  indicate unusual  
conditions in the host adapter.

Internal Diagnostic Failure (Status Port, bit 6): 
This bit indicates that the self testing process after either a 
hard reset or a power on operation was terminated by an error 
condition. The error indicates that a critical failure was found 
in the AHA-1640 control circuitry or data paths.   The error 
should be presented to the host video display to indicate that 
diagnostic actions are required. The diagnostic action uses the 
host adapter diagnostic flash codes to determine if the AHA-1640 
is failing. The host system should be powered off, then opened 
so that the LED can be observed. All SCSI cables, both external 
and internal, should be removed from the host adapter. The 
system should then be powered on. If the LED flashes once and 
turns off, the host adapter has passed its diagnostics and should 
be accessible again. If the LED flashes one of the error flash 
codes, the AHA-1640 should be replaced. If the LED remains on 

                                8-2

Section Eight                                           Problem Determination 
------------------------------------------------------------------------------

and does not turn off, the host adapter is not able to begin 
operation at all. The host system may be holding the AHA-1640 in 
the reset state or the host adapter may have failed. To 
distinguish these two cases, the AHA-1640 should be replaced and 
the new host adapter operation should be verified. Be sure to 
power down the host system when removing or replacing the host 
adapter. If the diagnostics indicate that the AHA-1640 must be 
replaced, it should be sent to an authorized service facility for 
repair.

Invalid Host Adapter Command (Status Port, bit 0):  This bit is 
set to indicate that a command  or parameter transmitted to the  
host adapter was invalid.  This is an  indication that the host  
software, usually  an  operating  system,  special  application  
program, or device driver, has generated an invalid request. The 
responsible programming organization should be notified so that  
the invalid sequence or parameter can be corrected.


8.3.3 Host  Adapter  Status  Error  Indications  and Corrective  
Actions

The Host Adapter Status indications,  in addition to indicating  
several normal completion states, indicate three general groups  
of errors. One  set describes  software errors  in the requests  
made to the host adapter. Even  though most of these errors are  
caused by software design problems, the AHA-1640 may need to be  
replaced as an isolation step, since there exists a small chance 
that hardware failures in the AHA-1640 cause the appearance of a 
software error. 

A second  set describes  errors  detected by  the  host adapter  
firmware in the host adapter  hardware. The most likely failing  
component in this case is the AHA-1640, although certain system  
or cable failures may generate the appearance of a host adapter  
hardware error. 

A third set describes the appearance of unexpected or incorrect  
sequences executed by the attached  SCSI devices. In this case,  
the cables are the most likely failure point, with the peripheral 
device second and the  AHA-1640 third. The  host adapter status  
code should be returned to the host video display to indicate to 
the operator what errors have occurred and under what conditions 
the errors occurred. The following section describes those Host  
Adapter Status indications that indicate an error.

     NUMBER  TYPE   ERROR    DESCRIPTION AND CORRECTIVE ACTION

       11      SCSI    NO    Selection Time Out: 
                             The SCSI attempted to select a 
                             device that was not installed. 
                             Verify correct address values set 
                             to SCSI devices. Verify that SCSI 
                             cable routing includes the required 
                             devices. Verify SCSI cable 
                             integrity by replacement of cables. 
                             Verify that SCSI Selection Time Out 
                             value has been correctly 
                             established by IOCP command.

       12      HOST    NO    Data Over Run/Under Run:   Data 
                             length or direction specified by 
                             CCB did not agree with the data 
                             length actually provided by the 
                             attached peripheral device. Often 
                             a normal error or accompanied by a 
                             check condition indicating transfer 
                             truncation. Verify program 
                             requested correct length or 
                             direction. Verify peripheral 
                             provided expected data length, 
                             number of blocks, or block length.

       13      SCSI    YES   Unexpected Bus Free: 
                             The target dropped BSY without 
                             executing the proper message first.

                                8-3

Section Eight                                           Problem Determination 
------------------------------------------------------------------------------

 
                             This normally indicates 
                             that the BSY and/or other portions 
                             of the SCSI bus failed or that the 
                             target encountered such an invalid 
                             sequence that no recovery was 
                             possible. Some targets may have 
                             sense information available to 
                             qualify the error condition. 
                             Verify SCSI cable integrity. 
                             Verify SCSI cables are all properly 
                             connected. Replace SCSI cables. 
                             Replace peripheral. Replace AHA-1640.

       NUMBER  TYPE  ERROR   DESCRIPTION AND CORRECTIVE ACTION

       14      SCSI    YES   Target bus phase sequence failure: 
                             The initiator detected an invalid 
                             phase or an invalid phase sequence. 
                             If this occurs, it is likely that 
                             the host adapter forces a SCSI 
                             reset on the bus as the first phase 
                             of the recovery process. Verify 
                             SCSI cable integrity. Verify SCSI 
                             cables are all properly connected. 
                             Replace SCSI cables. Replace 
                             peripheral. Replace AHA-1640

       15      HOST    YES   MBO Command Byte invalid: 
                             This indicates a software failure 
                             or bug in the host's development of 
                             the MBO entry. Generally, this 
                             indication will only occur during 
                             initial debug processes of new 
                             operating systems. Replace the 
                             AHA-1640. Replace the host 
                             computer system. Contact the 
                             software developer for design 
                             support.

       16      HOST    YES   Invalid CCB Operation Code: 
                             This indicates a software failure 
                             or bug in the host's development of 
                             the CCB. Generally, this 
                             indication will only occur during 
                             initial debug processes of new 
                             operating systems. Replace the 
                             AHA-1640. Replace the host 
                             computer system. Contact the 
                             software developer for design 
                             support.

       17      HOST    YES   Linked CCB does not have same LUN: 
                             This indicates that the host 
                             software generated an invalid 
                             combination of link commands. 
                             Generally, this indication will 
                             only occur during initial debug 
                             processes of new operating systems. 
                             Replace the AHA-1640. Replace the 
                             host computer system. Contact the 
                             software developer for design support.

       18      HOST    YES   Invalid CCB Parameter Received from 
                             Host: This indicates that the host 
                             software generated an invalid CCB. 
                             Generally, this indication will 
                             only occur during initial debug 
                             processes of new operating systems. 
                             Replace the AHA-1640. Replace the 
                             host computer system. Contact the 
                             software developer for design support. 

                                8-4

Section Eight                                           Problem Determination 
------------------------------------------------------------------------------

       19      HOST    YES   Duplicate CCB Received in Target 
                             Mode: This indicates that the host 
                             system was not keeping correct 
                             management information for target 
                             mode operation and incorrectly 
                             generated a second CCB identical to 
                             one already active.    Generally, 
                             this indication will only occur 
                             during initial debug processes of 
                             new operating systems. Replace the 
                             AHA-1640. Replace the host 
                             computer system. Contact the 
                             software developer for design support. 

       NUMBER  TYPE    ERROR DESCRIPTION AND CORRECTIVE ACTION

       1A      HOST    YES   Invalid Segment List: 
                             A segment list was presented to the 
                             host adapter with a zero length 
                             segment or invalid segment 
                             boundaries. Generally, this 
                             indication will only occur during 
                             initial debug processes of new 
                             operating systems. Replace the 
                             AHA-1640. Replace the host 
                             computer system. Contact the 
                             software developer for design support.

       1B      SCSI    YES   Request Sense Command Failed: 
                             A REQUEST SENSE command generated 
                             automatically by the host adapter 
                             did not complete correctly. 
                             Non-zero status was returned.  
                             Verify SCSI cable integrity. 
                             Verify SCSI cables are all properly 
                             connected. Replace SCSI cables. 
                             Replace peripheral. Replace AHA-1640.


8.3.4 SCSI Error Indications and Corrective Actions


Error conditions detected  by SCSI peripherals  usually cause a  
CHECK CONDITION  Status  byte  to be  presented.  When  this is  
presented, the host  adapter automatically  retrieves the sense  
information from the SCSI peripheral by executing a REQUEST SENSE 
command according to the SCSI standard. The information returned 
is mapped for single-threaded BIOS operation into the categories 
of error conditions described in Section 5.2.2. For multitasking 
(mailbox) operation, the information returned is made available  
in the  area  allocated  for Sense  Data.  In  either  case, an  
intelligent attempt is made by  most operating systems to retry  
the operation  at least  one  time. Such  retry  operations may  
require the management  of queued operations  that have already  
started execution. This attempt to retry the operation is rarely 
successful, since SCSI  peripheral devices  have very extensive  
automatic retry and correction mechanisms designed to be executed 
before the error information is returned in the first place. 

Since it is rare that such an operation is successful, the host 
software and operating systems should make every attempt to make 
available key information about the error which can be analyzed  
by the system operator or  customer engineer. In small systems,  
it may be sufficient to present the important Sense Data together 
with the command that  created the error.  Some simpler systems  
may perform a preliminary analysis of the error information and  
generate a code or descriptive text that describes the error and 
indicates the  corrective action.  In  very complex  systems, a  
logging process may take place, allowing a customer engineer to  
analyze the  data at  some future  time.  In all  systems, such  
information is very important for host program verification and  
for system integrity verification, even if the designers choose  
not to make the information available to any system users other  
than the design and maintenance engineers.

                                8-5

Section Eight                                           Problem Determination 
------------------------------------------------------------------------------

The SCSI Sense  Data is generally  self-descriptive. The errors  
can be mapped in to four major categories, each category with its 
own diagnostic procedure.

The first category  includes those  errors caused  by incorrect  
command or parameter bytes or by incorrect sequences of commands. 
These errors  typically  are presented  only  during  the early  
development stages of an operating system or device driver, since 
a properly operating program will not generate invalid commands.

The second category includes those  sense codes associated with  
peripheral status presentation. Such sense  codes are not truly  
errors, in that they inform the  host program of an unusual but  
not unexpected condition. Such  sense codes include indications  
that a device  is not  ready, that  the device has  just become  
ready, that a device has  reached the end of  its media (End of  
Tape or  Blank Check),  or that  the  expected data  length and  
actual data length differed. These sense codes are normally used 
by the device driver to execute the correct operation in response 
to the condition. Such sense codes are not normally presented to 
the system user except as text that requests some action. As one 
example, an End Of Tape condition may require the system user to 
replace the tape cartridge.

The third category  of errors  points to  a particular hardware  
failure in the peripheral device or its supporting electronics.  
Such error conditions usually require the adjustment, repair, or 
replacement of the peripheral device or some of its components.  
In some cases, the  error condition may  also indicate possible  
cable or host adapter failures. These errors must be exposed to  
the system user so that the proper actions can be taken.

The fourth category of errors points  to a media failure in the  
peripheral device.  Such  errors include  bits  that  cannot be  
recovered from magnetic media and imperfections in the surface of 
optical  media.  Most  such  errors  are  recovered  using  the   
extensive retry and  correction algorithms  programmed into the  
peripheral device.  In  some technologies,  the  errors  may be  
caused by noise conditions or by marginal electronic failures in 
the read  or  write  path. Those  rare  errors  that  cannot be  
recovered usually indicate that some information important to the 
operating system or application has  been lost. The system must  
make this information available to the  system user so that the  
system user can replace the media or recover the data from a back 
up copy as required.  In addition, logging  of errors that were  
successfully recovered by the peripheral device is often useful  
as an indicator of the overall  reliability of the device or of  
the requirement for periodic maintenance.

                                8-6


Section Nine                                                         Glossary 
------------------------------------------------------------------------------
  
  AEN
    See Asynchronous Event Notification
  
  Asynchronous Event Notification
   A process by which a target can send unsolicited sense information to  
  an initiator using the  SEND command in order  to inform the initiator  
  about the occurrence of an important unusual occurrence.
  
  Asynchronous Data Transfer
    Data  transfer  performed  by   the  SCSI  interface  involving  the   
  interlocking of a signal  to the initiator  (REQ) and a  signal to the  
  target (ACK) such  that each step  of the data  transfer protocol must  
  occur before the next step can begin. Characterized by a low data rate  
  and independence of external timing constraints, including cable length 
  and circuit response times.
  
  Bus Device Reset
   A SCSI message that clears all activity  in the target to which it is 
  addressed.
  
  Byte
   An 8  bit unit  of data. An  octet. A  byte is normally  the smallest  
  addressable unit of a memory and the unit of transfer on the SCSI.
  
  CCB
    See Command Control Block
  
  CCS           
    See Common Command Set
  
  CDB           
    See Command Descriptor Block
  
  Command Control Block
   A software object prepared by the host microcomputer software for the 
  host adapter to  provide it  all the  control information  it needs to  
  execute a SCSI command. Abbreviated: CCB.
  
                                 9-1

Section Nine                                                         Glossary 
------------------------------------------------------------------------------
  
  Command Descriptor Block  
   A  block of  information  passed across  the  SCSI bus  to provide  the  
  command, parameter, and address information necessary for the target to 
  execute the desired functions. Prepared by the host software and placed in 
  the CCB to be passed to the target by the host adapter. Abbreviated: CDB.
  
  Common Command Set
   A defacto standard SCSI command set  for communication with hard disk 
  drives. The  Common Command  Set  (CCS) is  the  basis for  the SCSI-2  
  command set for all types of peripheral devices. 
  
  Control Microprocessor    
   An  integrated circuit  computer used  to  execute the  software that  
  controls the host adapter's operation.
  
  Device Driver
   A program that  is linked with  or attached to  an operating system  to 
  map the software interface of the operating system to the requirements  
  of attached peripheral devices and host adapters.
  
  DMA
    See Direct Memory Access
  
  Direct Memory Access
   A mechanism  that allows hardware  control of  the transfer of  streams 
  of data to or from the main memory of a computing system. The mechanism 
  may require  set  up  the  host  software.  After  initialization,  it  
  automatically sequences the  required data  transfer and  provides the  
  necessary address information.
  
  EPROM
   Erasable Programmable  Read Only  Memory. An  integrated circuit used  
  to store the host adapter firmware and the host adapter BIOS.
  
                                 9-2

Section Nine                                                         Glossary 
------------------------------------------------------------------------------

FIFO
    First In / First Out. 
                
  A queueing order in which items are removed from the queue for execution 
  in the same order in which they are placed in the queue.
  
  An integrated circuit that buffers data in such a manner that the each  
  byte placed in the buffer is removed from the buffer in the same order.
  
  Firmware
   The  software  that controls  and  manages  the host  adapter.  It is  
  'firm' as opposed  to 'soft'  because it  is designed  in to  the host  
  adapter and cannot be modified by the user.
  
  I/O Command Port Command
   A command transmitted to the host  adapter using the Command/Data Out 
  Port and the Data In Port. The commands are sequenced using the Control 
  Port, the Status Port, and the Interrupt Flag Port. Abbreviated as IOCP 
  command.
  
  Initiator     
   A SCSI device that  requests an operation to  be performed by another  
  SCSI device  (the  target).  The initiator  provides  all  the command  
  information and parameters required to  perform the operation, but the  
  details of the operation are actually sequenced by the target.
  
  IOCP Command
    See I/O Command Port Command
  
  Host
   A microcomputer  in which a  host adapter is  installed. The host  uses 
  software to request the  services of the  host adapter in transferring  
  information to and  from peripheral devices  attached to  the SCSI bus  
  connector of the host adapter.
  
  Host adapter
   A  hardware  printed  circuit  board  that  installs  in  a  standard  
  microcomputer backplane and provides a SCSI bus connection so that SCSI 
  devices can  be  connected to  the  microcomputer. A  host  adapter is  
  "intelligent" if it has a simple  high-level software interface to the  
  microcomputer. A  host adapter  is  "dumb" if  the  microcomputer must  
  directly manage the SCSI protocol using the microcomputer processor.
  
                                  9-3

Section Nine                                                         Glossary 
------------------------------------------------------------------------------

  Logical Unit
    A physical or virtual device addressed through a target. 
  
  Logical Unit Number
    An encoded three-bit identifier for a logical unit.
  
  LU            
    See Logical Unit
  
  LUN           
    See Logical Unit Number
  
  Mailbox In
   An area  in main memory  assigned by the  host microcomputer software  
  for communication with the host adapter. The host adapter places status 
  and pointer information in entries in the Mailbox In (MBI) to indicate 
  to the host microcomputer what operations  have been completed or what  
  information must be obtained from the host microcomputer.
  
  Mailbox Out
   An area  in main memory  assigned by the  host microcomputer software  
  for communication with  the host  adapter. The  microcomputer software  
  places commands and pointer information in  entries in the Mailbox Out  
  (MBO) to indicate what operations should be started by the host adapter.
  
  MBI           
    See Mailbox In.
  
  MBO           
    See Mailbox Out.
  
  Micro Channel
   A  microcomputer backplane  created  by IBM  for  the high  performance  
  PS/2_ series of small computers. The name is trademarked by IBM.
  
                                   9-4

Section Nine                                                         Glossary 
------------------------------------------------------------------------------

  Multi-tasking Operation
   The execution of commands in such a way that more than one command is 
  in progress at the same time, allowing the system to take advantage of  
  overlapping activities  by using  resources  that are  temporarily not  
  required for other operations. More than one  program or more than one 
  portion of a program may be operating in parallel.
  
  POS           
    See Programmable Option Select
  
  Programmable Option Select
   A feature  of the  Micro Channel  that allows  the setting of  hardware 
  related switches  through  the  microcomputer  software.  Programmable  
  Option Select (POS)  allows the  use of  geographic addressing  of the  
  backplane card slots  and pre-established  ID values  assigned to each  
  adapter card to properly verify and configure the microcomputer.
  
  PS/2
   A  family of  small computers  sold by  IBM, also  called the  Personal 
  System / 2 family of computers. The name is trademarked by IBM.
  
  RAM
   Random  Access  Memory. Memory  of  which  any byte  can  be accessed  
  directly in a  single memory cycle.  Information can be  read from and  
  written to the memory.
  
  SCSI
    The Small Computer System Interface.
  
  SCSI ASC
    SCSI  Additional  Sense   Code.  Byte  12   of  the  extended  sense   
  information. Provides  a  standardized  description  of  the condition  
  described by the sense information.
  
  SCSI Device
   A  device attached  to a  Small  Computer System  Interface bus  cable.  
  The device may be an initiator, a  target, or capable of both types of  
  operation. The device may be a peripheral  device, a host device, or a  
  device mixing both roles. 
  
                                 9-5

Section Nine                                                         Glossary 
------------------------------------------------------------------------------

  
  Single Threaded Operation
   Operation of the computing  system such that only  one program can be  
  operating or active at a time. The computing system must wait until all 
  resources are available before starting  an operation and cannot start  
  another operation until the first one  is completed. No overlapping of  
  latencies or program operation occurs.
  
  Synchronous Data Transfer
   A method of data transfer on  the SCSI bus involving clocking data on  
  to the  bus with  a  fixed-length fixed-frequency  strobe  pulses. The  
  acknowledgements may be  delayed several  clock periods  from the data  
  requests.  Synchronous  Data  Transfer  can  be  used  only  for  data  
  transmission on the SCSI  bus. It is  prohibited for command, message,  
  and status transmission.
  
  Synchronous Data Transfer Negotiation
   The  message  exchange  between the  initiator  and  the  target that  
  allows the negotiation of the data transfer frequency and delay between 
  requests and acknowledgements required  for synchronous data transfer.  
  Once negotiated, synchronous data transfer parameters remain unchanged  
  until certain reinitialization activities occur.
  
  Target
   A SCSI  device that performs  an operation  requested by an  initiator. 
  The target  may be  a peripheral  device performing  a service  for an  
  initiator. The target may also be a host adapter performing a Processor 
  type device service for an initiator.
  
  Word          
    A two byte (16 bit) unit of data.
  
  Writable Control Store
   RAM  containing  the  host adapter's  firmware  while  the firmware  is  
  being executed. The RAM is loaded from EPROM.
  
                                 9-6


                                                            8/25/89
********************************************************************

   ADAPTEC AHA-1640 PS/2 TO SCSI HOST ADAPTER EXTERNAL CONNECTOR

********************************************************************
NOTICE:  THIS IS PRELIMINARY AND ADAPTEC IS NOT RESPONSIBLE FOR
         ANY CHANGES, ERRORS, OR OMISSIONS TO THIS INFORMATION.
         THIS PUBLIC INFORMATION SHOULD NOT BE CONSTRUED AS A
         RECOMMENDATION BY ADAPTEC FOR ANY MANUFACTURER OR PART. 
********************************************************************

********************************************************************
I)  LIST OF MANUFACTURERS AND PART NUMBERS OF CABLE CONNECTORS
         THAT MATE WITH THE EXTERNAL SCSI CONNECTOR
      ON THE ADAPTEC AHA-1640 PS/2 TO SCSI HOST ADAPTER
********************************************************************

     AMP           Connector Part No:      749111-4    
                   Back Shell Part No:     749193-1

     FUJITSU       Connector Part No:      FCN-237R050-G/F
                   Back Shell Part No:     FCN-230C050-D/E (or -C/E)

     HONDA         Connector Part No:      PCS-XE50MA
                   Back Shell Part No:     PCS- E50LA

********************************************************************
II)  INFORMATION ON THE RECOMMENDED EXTERNAL SCSI CABLE MATERIAL
********************************************************************

  Partial description of cable:  100% shielded
                                 25 twisted pairs
                                 90 - 135 ohm -> intrinsic impedence

     C&T           Cable Part No:          16035

     Madison       Cable Part No:          4099

(Both these cable materials are IPI type cables.  Approximately 120
ohms measured differential TDR.)


********************************************************************
III)  INFORMATION ON COMPANIES THAT MAKE COMPLETE CABLE ASSEMBLIES
********************************************************************

Some companies that manufacture complete cable assemblies are:

     Amphenol Interconnect Products, Endicott, New York
     contact Bill Sopchak at (607) 786-4370  or (607) 754-4444

     Quintec Interconnect Systems, San Jose, California
     contact Lon Hudson    at (408) 272-8000