Fractal Landscape Generator v1.2
                    Copyright (c) 1992 Steve Anger
                 This program is freely distributable

  FRGEN is a utility to generate fractal landscapes and shapes using
successive triangle sub-division. The fractal data can be output as PoV
or Vivid scene description files or as raw triangle data.

  A note to PoV users: Although frgen automatically produces bounding
shapes for PoV files you can significantly speed up your renders if you
output the fractal data to 'raw' format and then run the data through
the program raw2pov (aka txt2pov).

Changes in v1.2
- replaced DKB output with PoV output.
- added Vivid and raw triangle output formats.

Changes in v1.1
- you can now start the fractal generation from any arbitrarily
  specified set of base triangles instead of the simple square base
  which was used in v1.0. You can now generate fractal spheres, boxes,
  specifically shaped mountain ranges, etc.

- the program will now create an efficient set of bounding shapes for
  the huge number of triangles generated. Scenes generated with v1.1
  will typically render 5 to 10 times faster than those generated with
  v1.0

- the 3D projection is now much more accurate, plus you can specify the
  view-point and look-at coordinates instead of just the viewing angle.


OPERATION

Usage: frgen infile[.fr] outfile[.ext] [[-,/]options]

Options: -sxnnn   Scale noise in x direction by nnn (0.0 - 1.0)
         -synnn     '     '    ' y     '      '  '     '     '
         -sznnn     '     '    ' z     '      '  '     '     '
         -bxnnn   Bias noise in  x direction by nnn (-1.0 - 1.0)
         -bynnn     '    '    '  y     '      '  '     '     '
         -bznnn     '    '    '  z     '      '  '     '     '
         -vxnnn   Set view_point x coord to nnn
         -vynnn    '      '      y   '    '  '
         -vznnn    '      '      z   '    '  '
         -lxnnn   Set look_at x coord to nnn
         -lynnn    '     '    y   '    '  '
         -lznnn    '     '    z   '    '  '
         -ennn    Use nnn as seed for random number generator
         -rnnn    Maximum recursion depth of nnn
         -d       Preview generated fractal on screen
         -o[n]    Set output format (-op = PoV, -ov = Vivid, -or = raw)
         -x       Exchange Y and Z coordinates on output

ex. C>frgen sphere.fr fract.dat -d -r2

infile[.fr]    This is the file which contains the basic specifications
               for the fractal. The first non-comment line of this file
               is a list of default options for this fractal (comment
               lines begin with a semi-colon). This line must be
               present. The rest of the file contains a list of
               coordinates for the triangles making up the base from
               which the fractal grows. The coords of the triangles are
               specified one per line in the following format:

                ax ay az  bx by bz  cx cy cz  [fix_ab  fix_bc  fix_ca]

               The numbers ax, ay, etc. are the x,y,z coordinates of the
               three vertices of the triangles. The three optional
               numbers fix_ab, fix_bc, and fix_ca can be either 1 or 0
               and specify  whether that edge of the triangle is forced
               to stay within the plane of the triangle or allowed to
               move freely (1 = fixed, 0 = free). The most common use
               for 'fixed' edges is to force  the outer edges of a
               mountain base to stay on the ground. If not specified,
               edges are assumed to be free.

               e.g. ; The default options are on the following line
                    -sx0.1 -sy0.2 -sz0.1 -by0.5 -r4 -vx10 -vy5 -vz-10
                    ; Two triangles in the x-z plane making up the base 
                         ; of a mountain
                    +10.0 0.0 0.0   0.0 0.0 +10.0  -10.0 0.0 0.0  1 1 0
                    -10.0 0.0 0.0   0.0 0.0 -10.0  +10.0 0.0 0.0  1 1 0

               Three sample input files are included:
               mountain.fr - Square based mountain.
               diamond.fr  - Simple diamond shape made of 8 triangles.
               sphere.fr   - Sphere made from 48 triangles.

outfile[.ext]  Output file to be created. The extension added will
               depend on the output format specified.

-sx -sy -sz    These three numbers specify the magnitude of the noise
               that will be used to perturb the triangles. Setting a
               scaling factor of 0.0 (-sx0 -sy0 -sz0) will generate a
               fractal that is unchanged from the starting shape while
               a scaling factor of 1.0 (-sx1.0 -sy1.0 -sz1.0) will
               create extremely distorted shapes. Values in the range
               0.05 to 0.25 usually work well. Default values are -sx0.1
               -sy0.1 -sz0.1

-bx -by -bz    These numbers specify the amount by which the noise is
               biased in the corresponding x,y,z direction. A positive
               value will cause the noise to tend to move in the
               positive direction of  the axis while a negative value
               will tend to move it in the opposite direction. e.g. If
               start with a triangle in the x-z plane, a setting of
               -bx0.0 -by0.5 -bz0.0 will cause the fractal to tend to
               bulge upward creating a mountain-like shape. Default
               values are -bx0.0 -by0.0 -bz0.0

-vx -vy -vz    The x, y, and z coordinates of the viewpoint.

-lx -ly -lz    The x, y, and z coordinates of the point you are looking
               at.

-e             You can use this option if you want to manually specify
               the seed used by the random number generator. This is
               useful if you want to reproduce the same fractal more
               than once but using different view points, numbers of
               triangles, etc.

-r             This specifies the number of times to sub-divide the
               triangles. Be careful when setting this number as the
               number of triangles generated will increase by a factor
               of 4 every time it is increased by 1. Default is -r3

-d             Turns the display preview on.

-op            Selects PoV output format.

-ov            Selects Vivid output format.

-or            Selects raw triangle output format.

-x             This option causes the Y and Z coordinates to be switched 
               when writing the output file. This is useful if your    
               rendering package uses the Z axis as vertical instead of 
               the Y axis.

                                   Internet: steve.anger@rose.uucp
                                      (alt)  lsuc!rose.uucp!steve.anger
                    You Can Call me Ray BBS: (708)358-5611