README of ACE120.ZIP               October 7, 1992

SUMMARY 
ACE120.ZIP is the latest Maintenance PTF for Access Server Version 1.20. 
It presently contains PTF 342.  In addition to the problems solved by prior
PTFs it solves the following:
   Unable to Find File Server
   Hang upon exiting Lan Workplace for DOS
   Very high file server utilization rate
   Hang when exiting NetBIOS applications
   Lost Characters  
   Keys like ESC, Ctrl, and Alt not working
   Some international keyboard symbols do not display
ACE120.ZIP also upgrades V1.20 Access Servers to V1.22.

WARNINGS
1.  This PTF can only be applied to Version 1.20 or 1.22 Access Servers.  
It WILL NOT WORK with Version 1.0 or 1.01 Access Servers.

2.  You must use a LOGIN.EXE dated 1/26/90 or later.  If you do not already
have one you can find one in any version of NetWare later than 2.15C or in
LOG363.ZIP in NOVLIB Library 6.

3.  This PTF is intended to be used together with PTF 302, or the more
recent ONLAN.ZIP (PTF 332) which contains software updates for the OnLAN/PC
terminal software.  ONLAN.ZIP to upgrade the ONLAN/PC on all workstations
after applying PTF 342 to your Access Server. 

4.  These files do not constitute the entire product and are to be used
only in conjunction with authorized purchased versions of Access Server. 
The product is Copyrighted under law and is not shareware.

INSTALLATION INSTRUCTIONS
1.  Erase the entire ACCESS and NASGEN Directories (this must include
NASCOMM.EXE which the PTF will replace with NASCOMM.COM) so that nothing
will remain from prior Access Server installations.

2.  Copy the original Access Server disks into the NASGEN Directory.

3.  Copy the IPX.OBJ provided with this PTF to your SHGEN or WSGEN
diskette/directory.  Generate a new IPX.COM with the new IPX.OBJ.  
Then use Access Server's INSTALL menu to update IPX.

4.  Copy all files in ACE120.ZIP (except ACE120.DOC and NASKBD.EXE) into
the NASGEN directory and select the First Time Install option.  If asked if
duplicate files should be deleted respond with a 'YES'.  Do not attempt to
unpak the pak files, Access Server will deal with that automatically.

NOTE: FIRST TIME INSTALL OPTION
     - Answer YES to the questions:
            > Update SYS:PUBLIC ?
            > Update SYS:LOGIN  ?

If the version was 1.20 it will change to 1.22. 

5.  Copy the new DVANSI.COM over any existing copies.

6.  Obtain a copy of PTF 322 (ONLAN.ZIP) and apply it to update the OnLAN
PC files on all of your remote terminals.
 
7.  If you will be using an "International Keyboard" (keyboard other than
USA) do the following:
   A. Create a LOCAL subdirectory in the ACCESS directory of the Access
   Server boot disk.
   B. Copy the following to the LOCAL subdirectory:
       - NASKBD.EXE (from this PTF)
       - KEYB.COM (from your DOS diskette)
       - KEYBOARD.SYS (from your DOS diskette)
   C. Make certain NASCP.EXE is in the ACCESS directory.
   D. With a text editor change the NASTART.BAT file located in the ACCESS
   directory from:
       REM %2:NLSFUNC
       REM %2:KEYB ll,nnn,%2:KEYBOARD.SYS  (see note)
   To: 
       REM %2:NLSFUNC
       %2:NASKBD S
       %2:KEYB ll,nnn,%2KEYBOARD.SYS   (see note)
       %2:NASKBD
   NOTE: substitute the letter and number code for the particular country
   keyboard in place of ll,nnn.
   E. Increase the second NASDISK line in the NAS boot disk CONFIG.SYS from
    /P11 to /P/18.  For example:
    From: 
       DEVICE=C:\ACCESS\NASDISK.SYS/P18/S
       DEVICE=C:\ACCESS\NASDISK.SYS/P11/S
    To:
       DEVICE=C:\ACCESS\NASDISK.SYS/P18/S
       DEVICE=C:\ACCESS\NASDISK.SYS/P18/S

PROBLEM/SOLUTION DETAIL
1.  A virtual session was occasionally unable to connect to the network. 
IPX.OBJ has been changed to correct the problem. 

2.  NASHOST.PAK has been changed to correct a "potential" hang problem.

3.  DVANSI.COM has been changed so that exiting LAN Workplace for DOS no
longer results in a hang.

4.  MACTONAS.NLM has been changed so that it will always yield control when
it should.  This will result in a much lower file server utilization rate. 

5.  MEMMGR.EXE has been changed so that Add Name requests will be properly
terminated when a NetBIOS session is exited.  
  
6.  NACSLOAD.BIN has been changed so that characters received with parity
errors will no longer be discarded.

7.  NASCP.EXE and NASKBD.EXE have been changed so that the keyboard program
will take effect even if called from within a virtual session.
The virtual session will:
     - move to the foreground so that it can control the keyboard hardware
     - execute the keyboard program
     - return to the background

8.  DOS 5 can now be used.  HOWEVER: 
   - the use of DOS 5 will result in less RAM per virtual DOS session.
   - the special features of DOS 5 should not be used.  In particular, 
   the memory manager features of DOS 5 can not be used. 

9.  In order to use NetBios, MEMMGR.EXE no longer has to be downloaded
from NetWire.  Use the MEMMGR.EXE included with this PTF together with a
NETBIOS.EXE dated 1/16/91 or later.  Place MEMMGR.EXE and NETBIOS.EXE in
the Access Server's NASAUTO.BAT so, that the order will be as follows:
                - IPX.COM
                - MEMMGR.EXE
                - NETBIOS.EXE

10.  NACSLOAD.BIN was changed so that a data rate of 38.4KBS is more
feasible with a WNIM board. 

11.  A configuration screen was added which can be used to change all of
the NASGEN parameters during or after installation.
 
12.  A change in IPX.OBJ corrected a cause of occasional Access Server
hangs.

13.  NASCP.EXE was changed so that users will be able to use NASCON even
if the console has a password.

14.  Access Server no longer traps Lotus 123 V3.1 CPU checks. 
Compatibility between Access Server and Lotus 123 Version 3.1 is thereby
improved.

15.  The edges of the "User Connected screen" will no longer show at times
that the screen should not show at all.  

16.  IPX.OBJ has been changed so that RESET will work more consistently.

17.  Parity can now be set, for ONLAN terminal mode, by a script file.
The syntax is:  
     PARITY EVEN, PARITY ODD, PARITY MARK, PARITY NONE, PARITY SPACE

18.  Dialback will now operate if the reconnect timer value for the
profile being used is zero.  

19.  The reconnect timer will now cancel if dialback was successful.

20.  Access Server no longer hang as a result of 8 or more sessions
simultaneously doing Onfile file transfers.

21.  The terminal type in the default profile can no longer be ignored and
instead be stuck at "Ask Caller".

22. Login Scripts which call for reattaching to a file server are now
supported.

23.  Support was added for Video Mode changes within applications.  (For
example Word Perfect's "View Document" command) 

24.  NASGEN will now work properly if NUM-LOCK is on during the gen.

25.  MAC file transfers will now work properly at speeds under 9600kbs.


ADDED FEATURES
1.  Additional modems are now supported.

2.  If the connection is made via IPX (rather than a telephone line) the
terminal type chosen will now be reported to the user.1.  If the connection
is made via IPX (rather than a telephone line) the terminal type chosen
will now be reported to the user.

3.  The packet size can now be changed from the default of 512 to the
maximum packet size allowed by the topology of your LAN.  
To do this:
   A. Add the following line to the DVINTF.CFG file in the ACCESS
   Directory.
      MAX BUFFER LENGTH=n  With n being the being the desired number.  
           For instance: MAX BUFFER LENGTH=1024
   B. Change the LOADHI SIZE in NASAUTO.BAT (NASAUTO.BAT can be found in
   the ACCESS Directory).
            - Determine the new LOADHI SIZE with the following formula:
            {(new packet size - 512)*30}+old LOADHI size=new LOADHI SIZE
        For instance: {(1024 - 512) * 30 + 42K = 58,368
   C. Make certain the file server is also configured for the selected
   buffer length.

4.  LOGIN.EXE is no longer stored in a RAM Drive. 

5.  Depending on environment, performance (speed of operation) may be
improved.

6.  There is now a single Onfile for both Macs and PCs.


Files in PTF 342
ACCESS.COM     9940    8-19-91  
ASTATUS.EXE    2830    5-20-92     *310
BUFFERS.COM    2752    9-07-90  
COMARTIC.COM   6897    1-23-92  
COMWNIM.COM    4645    1-23-92  
CONFIG.SYS     271     12-11-91  
DIALBACK.EXE   40513   1-08-92  
DV.EXE         131070  8-28-91  
DVANSI.COM     1715    4-27-92  
DVINTF.CFG     26      3-26-92 
DVNETEMX.PAK   50350   12-19-91 
DVNETX.PAK     42909   12-19-91 
FILELIST.CFG   1313    12-04-91 
FILELIST.CFI   436     12-04-91 
FILELIST.PRD   1928    12-20-91
IPX.OBJ        25488   7-08-92 
LPTDRV.SYS     947     12-03-91 
MACTONAS.NLM   5982    3-30-92 
MEMMGR.EXE     10925   4-13-92
NACSLOAD.BIN   7968    4-13-92     *294
NASMODEM.CNF   31486   6-3-92      *374
NASAUTO.BAT    1643    12-04-91
NASCP.EXE      264268  9-2-92      *374 
NASCOMM.COM    2739    8-14-91 
NASHOST.PAK    31849   4-09-92     *324
NASDISK.SYS    2064    12-11-91 
NASDVR_E.OVL   5632    11-14-91 
NASDVR_I.OVL   5623    11-11-91 
NASGEN.EXE     265893  1-21-92 
NASKBD.EXE     19529   5-12-92     *312
NASMODEM.CNF   22175   1-08-92 
NASSTART.BAT   606     12-04-91 
ONFILE.EXE     90913   10-11-91 
ONFILE.MSG     29825   10-11-91 
RMGRDV.DVR     2110    10-29-91 
SIGNON.PAK     27382   12-19-91 
STANDIO.SYS    1029    12-12-91 
ACE120.DOC
* Novell internal control number   

HISTORY
PTF 342 supersedes all prior Access Server 1.20 PTFs and continues all of
the fixes contained in them.  The immediately preceding PTF was PTF 323. 


                                  DISCLAIMER    
Novell, Inc. makes no representations or warranties with respect to any
NetWare software, and specifically disclaims any express or implied
warranties of merchantability, title, or fitness for a particular purpose. 

Distribution of any NetWare software is forbidden without the express
written consent of Novell, Inc.  Further, Novell reserves the right to
discontinue distribution of any NetWare software.
 
Novell is not responsible for lost profits or revenue, loss of use of the
software, loss of data, costs of re-creating lost data, the cost of any
substitute equipment or program, or claims by any party other than you. 
Novell strongly recommends a backup be made before any software is
installed.  Technical support for this software may be provided at the
discretion of Novell.