FPSERVER: A Fast Alternative to Novell's PSERVER.EXE
           ====================================================
                   Richard L. Hartman (RLH), Consultant
                 Novell Registered Professional Developer
                         5205 North Mulvaney Court
                             Spokane, WA 99212
          509-924-6576 / CompuServe 76350,2275 / GEnie R.HARTMAN9


===============================================================================
INTRODUCTION
===============================================================================

FPSERVER is a program which implements an intelligent print server on a
standard IBM compatible personal computer.  In this manner, it is very
similar to Novell's own PSERVER.EXE.  However, unlike Novell's product,
FPSERVER has been optimized for ultra-high data throughput - up to TEN
TIMES higher than PSERVER.EXE.



===============================================================================
ASSUMPTIONS ABOUT THE READER
===============================================================================

The material in this file has been written with the assumption that the
reader has a solid understanding of the IBM Personal Computer architecture,
DOS usage, and Novell NetWare operation.  In particular, it is assumed that
the reader already has an operational NetWare network with established
print queues running through some form of existing print server.

Many of the operations associated with setting up and maintaining printing
services on a NetWare network require Supervisor-level authority.  If you
are not your Network's Administrator, you may need to involve him/her in
the process of installing FPSERVER the first time.  (Subsequent changes to
FPSERVER's operation may be implemented without Supervisor assistance.)

Please consult the documentation for these other products if you have
questions regarding them.



===============================================================================
NECESSARY EVILS
===============================================================================

My apologies for the following sections, but they are unfortunately
necessary in today's world.  Please read them and then move on to the more
interesting material which follows.



Copyright
---------------------------------------

FPSERVER is an example of "AdWare" - a term I have coined to describe
software which, in addition to being a useful standalone application,
serves as an advertisement.  FPSERVER is an advertisement for my network
software consulting services.  Please see "About the Author" at the end of
this file for more information.

All of FPSERVER's files and materials are copyrighted, and I specifically
reserve all rights to them worldwide.  The unaltered, unmodified FPSERVER
is hereby placed in the public domain; it may be copied, distributed, and
used without restriction as long as it is not changed or modified in any
way.  You are free to upload it, IN ITS ENTIRETY, to bulletin boards and
other "common access" systems.

FPSERVER represents a significant investment of my time and effort. It is
my sincere hope that you will benefit from your use of this program.  My
intention in creating this and other AdWare is to promote my network
software consulting services.  I would appreciate you giving copies of
FPSERVER to anyone (everyone!) you know that uses Novell NetWare.  Doing so
costs you exactly nothing and encourages me to continue writing AdWare.

While you are not REQUIRED to register, I would certainly enjoy hearing
your comments and suggestions.  Constructive comments may be incorporated
into future upgrades, so your input is valuable.  For FPSERVER-related
issues, you may contact me via CompuServe or by mail (see above for account
number and address).  Please restrict telephone calls to actual consulting
business.

Please see "About the Author" at the end of this file for more information
on my consulting services.  Thank you for your support!



Disclaimer
---------------------------------------

FPSERVER, and all of its associated files and programs, is provided without
warranty of any kind.  The user of this software is solely responsible for
determining its suitability for any purpose, the accuracy of its operation,
and the results obtained by its use.

As written, FPSERVER does not contain any "viruses" or other malicious
routines.  However, such routines do exist and can be "attached" to
otherwise benign and beneficial programs, often without obvious indication.
FPSERVER does not attempt to detect the presence of such additions.  It is
solely the user's responsibility to determine the "purity" of this software
and its associated files.



===============================================================================
BACKGROUND (WHY IT EXISTS)
===============================================================================

FPSERVER is a high-speed alternative to Novell's PSERVER.EXE, and an
inexpensive (read: FREE) alternative to third-party print server software.
FPSERVER was written with one goal: Ultra-high data throughput.

With all due respect to Novell (they write excellent network operating
systems), their PSERVER.EXE is simply too slow for today's graphics
intensive output.  Running on an 80386DX-25 PC with light network traffic,
Novell's PSERVER.EXE might attain 4K bytes per second on a parallel port (a
more typical figure is 1500-2000 bytes per second).  With a typical 300x300
DPI A-size graphic being 400K-500K or larger, Novell's PSERVER can consume
four minutes or more just transferring the data to the printer.

Standalone, "wedgebox"-style print servers, such as Intel's NetPort and
Datacom's Series 8000, also provide too little bandwidth for today's
applications.  Their bandwidths (typically 8000 bytes per second) are only
marginally better than Novell's PSERVER.EXE - still far too slow for
near-megabyte print jobs.  Furthermore, such poor performance hardly
justifies a price tag of $500 or more EACH.

In contrast, FPSERVER can sustain a data rate of over 15,000 bytes per
second even on an old 8MHz 80286 PC's parallel port.  This is faster than
most printers can accept data, which means that the printer, instead of the
print server, becomes the limiting factor (as it ought to be).  The same
400K graphic suddenly takes LESS THAN A MINUTE to transfer.

FPSERVER supports up to four separate print devices from a single host PC.
And, unlike Novell's PSERVER.EXE, FPSERVER suffers little or no throughput
impact when servicing multiple print devices.  A dynamic linking/unlinking
algorithm eliminates the overhead associated with idle print devices, and a
real-time throughput analysis algorithm optimally distributes available
bandwidth between active print jobs.

The bottom line: FPSERVER eliminates the network printing bottleneck.



===============================================================================
DESIGN PHILOSOPHY
===============================================================================

As stated above, FPSERVER's design goal was ultra-high data throughput. All
Engineering projects involve some compromises (to which we refer as "design
decisions" or "tradeoffs").  For FPSERVER, every such compromise was
resolved in favor of speed.

A Print Server should act as a straight wire between the print queue and
the target printer.  This means that all formatting, translation, and other
data manipulation is performed on the user's workstation prior to the data
being placed in the print queue on the File Server.  The Print Server's
responsibility is to manage its printer(s) and run them as fast as
possible.

Based on this philosophy, FPSERVER does not include some of the
capabilities found in other print server software.  FPSERVER does, however,
include features not found in other programs.  So that you may obtain
better insight into the philosophy of FPSERVER, some of these differences
(and the reasons for them) are listed below.



Number of Ports
---------------------------------------

FPSERVER will support up to four ports on a single machine - two parallel
and two serial.  Increasing the number of supported ports beyond four would
have forced many other design decisions to be adversely compromised.  The
special multi-port boards which support more than two parallel or serial
ports on a single machine are not inexpensive, either.  Ultimately, I
decided that if FPSERVER could be made to run fast enough, it would be more
effective to use another old PC with standard (and inexpensive) parallel
and serial hardware as a second Print Server - especially since FPSERVER
itself is free.



Print Queues per Port
---------------------------------------

FPSERVER allows each port to service only a single print queue. Other
programs allow a port to service multiple queues.  Frankly, there are few
installations where this capability is used; those that do are usually
prioritizing time-sensitive print jobs over others because network printing
is so slow.  I chose to delete this capability because of its low usage,
the impact it had on overall throughput, and the fact that FPSERVER's
higher speed eliminates the need for job prioritization.



Monochrome Display
---------------------------------------

FPSERVER displays its information in black & white, while some other
programs offer color displays.  My experience showed that most
installations use their oldest, most phosphor-burned monochrome monitors
for Print Servers and give the color video systems to their users.
Furthermore, manipulating color attributes in video memory takes time away
from transmitting data to the printer.  I chose monochrome video because of
its universal compatibility, lower processor overhead, and the fact that
most installations will only see black & white anyway.



Print Queue Display
---------------------------------------

FPSERVER includes a detailed display for each port and queue being
serviced.  This is in sharp contrast to the displays offered by other
programs, which often include little to no useful data.  FPSERVER's
display includes:

    * The name of the print queue being serviced by each port

    * Each port's hardware status lines, including OFFLINE, PAPEROUT,
      ERROR, and DTR OFF

    * The owner, print job title, and print job size of the job currently
      being printed

    * The number of bytes which have been transmitted for the job currently
      being printed

    * The owner, print job title, and average throughput for the most
      recently completed print job

    * The owners and print job titles for the next three pending print jobs
      in the associated print queue



Intelligent Real Time Optimization
---------------------------------------

FPSERVER's primary design goal was high bandwidth.  Unfortunately, the best
way to achieve high performance is dependent on many different parameters.
Some, like machine type, clock speed, and average network latency, do not
vary greatly and could be entered by the user.  However, other parameters
such as typical job size and the speed at which print devices accept data
can vary dramatically from day to day and print job to print job.  To make
matters worse, those parameters which have the greatest effect on
throughput are also those which are the most difficult to predict - and
that have the widest spectrum of possible behavior.

To address this, FPSERVER incorporates a two layer real-time optimization
algorithm based on actual network and print device performance.  Port
throughput (the speed at which each print device is accepting data) and
network throughput/latency (the speed at which the network can supply data)
are used to control the amount of processor resource dedicated to each
task.  FPSERVER constantly monitors these conditions and adjusts its own
operating parameters to assure that the maximum possible data rate is
maintained on all ports.



Simple Configuration
---------------------------------------

FPSERVER's operational characteristics are controlled by two methods:
commands in an ASCII configuration file (FPSERVER.CFG) and commands
included on the DOS command line when FPSERVER is started.  All FPSERVER
commands are "human readable", allowing you to easily review the print
server's configuration.

Other file server programs obtain their data from encoded files which can
be manipulated only through ADDITIONAL programs.  The need to run separate
software to change - or even just review - the print server's configuration
makes setup and maintenance a lengthy, frustrating process.

FPSERVER first processes the contents of its FPSERVER.CFG file (if
present), then interprets command line parameters (if any).  Redundant
commands take precedence over earlier versions of the same command so that
you may temporarily modify FPSERVER's behavior via the DOS command line
without editing any files or running any other programs.  You do not even
need to be logged in to the network; just override (or supplement) the
FPSERVER.CFG file right on the command line and press Enter.



Clean Exit to DOS
---------------------------------------

FPSERVER allows its execution to be terminated with a single keystroke,
just as any other well-behaved program.  Pressing Escape immediately
returns the machine to DOS - cleanly, with no "resident" code modules or
"captive" memory.  Other print server programs offer no clean exit to DOS,
and instead require the machine to be rebooted - an inconvenient and
sometimes lengthy process.

The ability to cleanly exit to DOS is particularly helpful when used in
conjunction with FPSERVER's command line parameters (see above).  You may
experiment with various configurations by just pressing Escape (back to
DOS), pressing F3 (get last command line), editing the command line
parameters, and pressing Enter to restart FPSERVER.



Support for Remote Printers
---------------------------------------

FPSERVER manages up to four printers, one each on two parallel and two
serial ports as mentioned above.  Other programs allow data to be routed to
printers on remotely located workstations.  By definition, this is a slower
process since data must pass through the network a second time, and then
through another workstation, before reaching the target printer.
FPSERVER's design goal was speed - and thus support for this inherently
slower process was deleted.



Service Advertising Protocol
---------------------------------------

FPSERVER does not "advertise" its presence on the network with NetWare's
Service Advertising Protocol (SAP).  To be more specific, FPSERVER does not
issue Server Identity Broadcasts nor respond to Service Advertising
Queries.

Application software may identify print servers by querying the File
Server's bindery for Print Server objects (Object Type 07 hex).  Those
which are actually attached and logged in to the File Server may then be
determined with NetWare's GetObjectConnectionNumbers function call.



Miscellaneous Fancy Features
---------------------------------------

FPSERVER does not support "banners", "tab translation", and other data
manipulation or non-printing functions.  The exceptions are "Copies" (which
causes multiple copies of the print job's data to be transferred to the
printer) and "Notify" (for which I received so many requests that I finally
gave in and added it!).

FPSERVER acts as a very fast straight wire between the print queue and the
printer, just as if the printer were directly connected to each user's
workstation.  There is never a configuration compatibility problem caused
by FPSERVER's assumptions about data content.  It sends to the printer
exactly what the application software generates - nothing more, nothing
less.



===============================================================================
HARDWARE REQUIREMENTS
===============================================================================

Host PC (Print Server)
---------------------------------------

FPSERVER may be used on virtually any PC which conforms to the generally
accepted standards for IBM Personal Computer compatibility. There is no
minimum processor architecture or speed; an 8088-based PC running at
4.77MHz is quite adequate.  A numeric coprocessor is neither required nor
used, and if present will be ignored.

A video subsystem (interface and monitor) is required for initial setup.
During operation, FPSERVER will display printer status and queue contents
if a display is present.  Technically speaking, however, FPSERVER does not
require a display for day-to-day operation.

FPSERVER does not require a keyboard.  If you wish to use the host PC for
other functions in addition to being a print server, a keyboard may be used
to gracefully exit and later restart FPSERVER (a keyboard is probably also
required for your other purposes).  However, for dedicated print server
applications that power-up directly into FPSERVER, a keyboard is strictly
optional as long as the host PC will successfully boot without one.

A disk drive is required to hold FPSERVER and its configuration file (both
of which are relatively small).  A floppy drive is more than adequate for
this task; in fact, if DOS and other required files (AUTOEXEC.BAT,
CONFIG.SYS, etc.) will fit together with FPSERVER on a single floppy, that
disk can serve as the boot device and no hard drive is required at all.

One or more ports are required for communication between FPSERVER and the
print devices.  FPSERVER can support up to two parallel and two serial
ports at the standard I/O addresses established by the IBM Personal
Computer BIOS for LPT1, LPT2, COM1, and COM2.  The interrupt lines normally
associated with these ports (IRQ7, IRQ5, IRQ4, and IRQ3 respectively) are
ignored by FPSERVER and may instead be used for other purposes such as the
network interface card.

FPSERVER has been written using the small memory model, and so requires no
more than 128K free memory over that consumed by DOS and other resident
software.  FPSERVER does not require Extended memory (XMS) or Expanded
memory (EMS) and ignores it if present.  Loading DOS and other programs in
"high memory" (as DOS 5 allows) provides no additional functionality and is
not required unless the host machine otherwise has less than 128K free
memory for FPSERVER.

Based on the above, a minimum hardware specification for an FPSERVER host
PC would be an 8088 running at 4.77MHz with 256K of memory, one low density
floppy drive, one or more printer ports, no hard drive, no keyboard, and no
video.  A disk in the floppy drive would contain the following:

     Bootable DOS (disk formatted with the /S option)
     CONFIG.SYS file
     AUTOEXEC.BAT file which loads network drivers and invokes FPSERVER
     IPX.COM (from Novell)
     NETx.COM (from Novell)
     SHELL.CFG (optional: for IPX/NETx)
     FPSERVER.EXE
     FPSERVER.CFG (containing appropriate configuration data)


...all of which can comfortably fit on a 360K low density floppy.  Such a
host PC would cost less than $300 even if purchased NEW.



Print Devices
---------------------------------------

FPSERVER may be used with any external device that supports hardware
handshaking.  Device types are not limited to printers; any parallel or
serial device which conforms to the requirements below may be used with
FPSERVER.  Examples of "non-printer" devices include pen plotters, CRT
terminals, modems - any device which can make use of queued data.

Parallel devices must conform to the generally accepted Centronics
"standard" for parallel interfaces.  This is a well understood protocol
which incorporates hardware handshaking as part of its basic definition.
FPSERVER has two parallel modes: "Safe" and "Fast".  Refer to the
"Technical Details" section for more information.

Serial devices must provide hardware handshaking via the DTR (Data Terminal
Ready) signal.  This is the most common form of hardware handshaking for
serial devices and is supported by virtually every printing device
available.  Most PC compatibles expect DTR on pin 6 of the standard 25 pin
D-connector used for RS-232C; consult your computer's documentation for
more information regarding the pinouts used on its serial ports.

FPSERVER does not support software handshaking.  This includes X-On/X-Off,
ETX/ACK, ACK/NAK, and other purely software-based protocols.



Printer Cables
---------------------------------------

The cables used to connect from the host PC on which FPSERVER executes
to the print device(s) must meet certain minimum requirements.  These
requirements differ for parallel and serial connections; each is detailed
below.

For parallel connections, the cable must carry the following signals
between FPSERVER's host PC and the printer (pin numbers refer to those
traditionally used at the Centronics connector):


     STROBE (pin 1)
     DATA 1-8 (pins 2-9)
     BUSY (pin 11)
     GROUND (pins 19-30)


Parallel cables should also connect the following signals, although they
are not strictly required for successful operation:

     PE (pin 12)
     SLCT (pin 13)
     INIT (pin 31)
     ERROR (pin 32)


For serial connections, the cable must carry the following signals (typical
pin numbers are not specified for serial connections due to the wide
variety of connectors and pinouts used for RS-232C interfaces):

                        Printer             Host PC
                        =======             =======
                          TxD --------------> RxD
                          RxD <-------------- TxD
                          DTR --------------> DSR
                          GND --------------- GND


The arrows are included to clarify the direction of signal travel, since
both ports have signals with identical names.  It is important to note that
you CANNOT connect pins with the same name to each other; each must be
connected to its "complementary" pin.  The sole exception is Ground, which
has no direction or polarity.

Pay close attention to the DTR-DSR connection.  The PRINTER's DTR (which is
an output) must drive the HOST PC's DSR (which is an input).  Connecting
the opposite signals together - even though the names are the same - will
prevent FPSERVER (and most other software) from functioning correctly.

All pin numbers should be confirmed with your equipment's own
documentation.  In many cases wire "swapping" is necessary to move signals
to the correct pins.  A good test is DOS's COPY command; if COPY
successfully prints data on the print device, the cable is suitable for use
with FPSERVER.



Faster Clocks and Wider Buses
---------------------------------------

FPSERVER's throughput performance is much less dependent upon the host PC
than other print server software.  Most of its theoretical maximum
throughput can be achieved on machines with (relatively) low processing
power.  For example, reducing the host PC from an 80386 @ 25MHz to an 80286
@ 8MHz (half the bus width and one third the clock speed) will only
decrease throughput by 15-30%.  The advantage is that older, less
expensive, less "user-desirable" PC's can be used as print servers with
little or no performance penalty.

There are several reasons why a machine which is "twice as fast" does not
yield a doubling of throughput.  First, PC parallel and serial ports are
eight bit devices; all I/O involving these ports occurs eight bits at a
time regardless of the processor's bus width.  An AT's 16 or 32 bit bus is
still forced to interact with the port hardware eight bits at a time.

Second, most AT-style BIOS's insert wait states for eight bit I/O
operations which offset the advantage of increased clock speeds.  Most I/O
cards are designed for operation in an 8MHz (or at most 12MHz) bus; a 25,
33, or 40 megahertz processor simply idles while its wait states time out
during each input and output operation.

Because the code between port operations will be executed faster, some
increase in maximum throughput will be obtained with faster machines.
However, the relationship is not linear; a doubling of bus width or clock
speed will not yield twice the data rate.

Furthermore - and this is the most important consideration - print devices
are almost ALWAYS the limiting factor.  Very few can accommodate FPSERVER's
maximum output rate even when the host machine is just a 4.77MHz 8088-based
PC.  Only the fastest output devices (16+ PPM laser printers and some
high-end electrostatic plotters) will find themselves waiting between bytes
received from FPSERVER.

Before spending money on a faster PC host, be sure to run FPSERVER on a low
end machine and compare its test mode performance with the rates obtained
when driving a "real" printer.  Your oldest, slowest PC may be more than
fast enough for the printers in question.



===============================================================================
CONTROLLING FPSERVER'S OPERATION
===============================================================================

FPSERVER's configuration is controlled by commands which appear in a
configuration file and on the DOS command line.  All commands, regardless
of their location, use a common format.

For consistency, all commands which affect a single port begin with the
port's name (LPT1, LPT2, COM1, or COM2).  Those which affect the operation
of the software in general do not incorporate port names.

Commands are processed in the order that they appear.  Those in the file
FPSERVER.CFG are processed first, followed by any which appear on the
command line.  Later commands take precedence over earlier, making it
possible for command line parameters to temporarily override the contents
of FPSERVER.CFG (this is extremely useful for experimentation and early
setup).  No warning is issued if multiple, redundant commands are detected;
the later commands are simply processed and the earlier commands ignored.

Spaces may surround equal signs ONLY in the file FPSERVER.CFG.  Including
spaces around equal signs on the command line will confuse DOS's command
line parser and result in error messages.  Since spaces are never REQUIRED
for any command, it is recommended that commands not include spaces at any
time.  Examples in this file omit spaces in the recommended fashion.

All commands and their parameters are converted to capital letters prior to
interpretation and are thus case-insensitive.



Print Server Name
---------------------------------------

FPSERVER must log in to its host file server as a valid Print Server
object.  The name that FPSERVER should use may be specified with the
command:

    PRINTSERVER=name

...where:   name = the name of a valid Print Server object

Network Supervisors can create Print Server objects using Novell's PCONSOLE
utility.  Please refer to Novell's documentation for more information
regarding the creation of Print Servers.

FPSERVER does not support the use of passwords with Print Server objects.
Any existing password must be deleted from the desired Print Server object
prior to successful execution of FPSERVER.  Novell's PCONSOLE may be used
to delete Print Server object passwords.

There is no default for the PRINTSERVER command.  A name must be supplied.



Print Queue
---------------------------------------

The print queue to be serviced by a hardware port may be specified with the
command:

    portQUEUE=queuename

...where:   port = LPT1, LPT2, COM1, or COM2
            queuename = the name of a valid print queue, or NONE

During startup, FPSERVER will attach the specified hardware port to the
specified Print Queue.  The Print Server designated with the PRINTSERVER
command must be authorized to service the specified Print Queue or an error
will be reported and execution will terminate.

The special value NONE may be used to disable a hardware port and, thus,
the servicing of its associated print queue by this print server.  This is
particularly useful as a command line parameter for "turning off" print
queues temporarily without editing the FPSERVER.CFG file.

Network Supervisors can grant service rights for Print Queues to Print
Server objects using Novell's PCONSOLE utility.  Please refer to Novell's
documentation for more information regarding the relationship between
Print Server objects and Print Queues.

The default for the QUEUE command is NONE (port disabled).



Parallel Port Timing
---------------------------------------

The parallel port strobe timing mode may be specified with the command:

    portMODE=method

...where:   port = either LPT1 or LPT2 (not COM1 or COM2)
            method = either SAFE or FAST

FPSERVER supports two operational modes for the parallel ports: "Safe" and
"Fast".  The difference between them involves the timing of the Strobe
signal and the way that Centronics-equipped print devices are designed.
(This subject is discussed more thoroughly in the "Technical Details"
section.)

Generally, you should always specify FAST unless doing so results in
printer errors or garbled data.  No print devices tested to date have been
incompatible with the FAST setting, and using it significantly increases
FPSERVER's maximum throughput.  However, should the printer report an "I/O
Error" or start dropping characters, change that port's mode to SAFE and
compare the results.

The default for the parallel MODE command is FAST.



Serial Port Baud Rate
---------------------------------------

The baud rate for a serial port may be specified with the command:

    portBAUDRATE=value

...where:   port = either COM1 or COM2 (not LPT1 or LPT2)
            value = one of 110, 300, 600, 1200, 2400, 4800, 9600, 19200

FPSERVER supports the eight baud rates shown above.  The full baud rate
value - three, four, or five digits - must be supplied including trailing
zeroes (i.e. "96" is invalid).  Values other than those shown above will
yield an error message and terminate execution.

The default for the serial BAUDRATE command is 9600.



Serial Port Data Bits
---------------------------------------

The number of data bits for a serial port may be specified with the
command:

        portDATABITS=value

...where:   port = either COM1 or COM2 (not LPT1 or LPT2)
            value = either 7 or 8

FPSERVER supports either 7 or 8 data bits.  Values other than 7 or 8 will
yield an error message and terminate execution.

This value is independent of all other serial port configuration parameters
(i.e. there are no limitations on how many data bits may be used at what
baud rate, etc.).

The default for the serial DATABITS command is 8.



Serial Port Parity
---------------------------------------

The parity for a serial port may be specified with the command:

    portPARITY=value

...where:   port = either COM1 or COM2 (not LPT1 or LPT2)
            value = ODD, EVEN, or NONE

FPSERVER supports the standard ODD and EVEN parity options in addition
to no parity at all.  Values other than ODD, EVEN, or NONE will yield
an error message and terminate execution.

If ODD or EVEN parity is specified, FPSERVER will calculate and insert an
additional bit into each serial word.  Specifying NONE will disable parity
and reduce the length of each serial word by one bit.

The default value for the serial PARITY command is NONE.



Serial Port Stop Bits
---------------------------------------

The number of stop bits for a serial port may be specified with the
command:

    portSTOPBITS=value

...where:   port = either COM1 or COM2 (not LPT1 or LPT2)
            value = either 1 or 2

FPSERVER supports either 1 or 2 stop bits per serial word.  Values other
than 1 or 2 will yield an error message and terminate execution.

The default value for the serial STOPBITS command is 1.



Placing Remarks in FPSERVER.CFG
---------------------------------------

Remarks may be included in the FPSERVER.CFG file in the format:

    REMARK This is a comment

...or:

    REM This is a comment


The space after the REMARK or REM command MUST be included.  Any other
character will yield an error message and terminate execution.



A Minimal FPSERVER.CFG File
---------------------------------------

As noted in their individual descriptions, many of FPSERVER's configuration
commands default to standard values.  The number of commands actually
required for proper operation is therefore quite small.  In fact, a
completely operational print server can be established with only two
commands: the name of the Print Server object and the name of a print
queue.

An FPSERVER.CFG file containing the two commands:

     PrintServer=PS-ADMIN
     LPT1Queue=PQ-LASERJET3D


...will yield a print server which attaches to the File Server as the
PS-ADMIN Print Server object, obtains jobs from the PQ-LASERJET3D print
queue, and outputs them on the first parallel port using FAST mode.  LPT2,
COM1, and COM2 (if present) are disabled by default.

For a truly minimal configuration, the FPSERVER.CFG file can be eliminated
completely by including required commands on the command line itself.
Entering the following command at a DOS prompt:

     FPSERVER PrintServer=PS-ADMIN LPT1Queue=PQ-LASERJET3D   <enter>


...will satisfy FPSERVER's minimal parameter needs and yield exactly the
same operation as if the FPSERVER.CFG file mentioned above were present.
Note that no spaces are present around the equal signs, in keeping with
DOS's command line parser requirements.



A Typical FPSERVER.CFG File
---------------------------------------

The following is an example of a more typical FPSERVER.CFG file for a
hypothetical network which uses many of the commands described above:

    Rem ****************************************************************
    Rem !!! PLEASE CONTACT JOHN DOE IN MIS BEFORE CHANGING THIS FILE !!!
    Rem ****************************************************************
    Rem - Print Server in Administration area is named PS-ADMIN
    PrintServer=PS-ADMIN
    Rem - Admin. LaserJet IIID's queue is named PQ-LASERJET3D
    LPT1Queue=PQ-LASERJET3D
    Rem - LaserJet IIID works fine with Fast parallel ports
    LPT1Mode=FAST
    Rem - Admin. PaintJet's queue is named PQ-PAINTJET
    LPT2Queue=PQ-PAINTJET
    Rem - PaintJet likes Fast parallel too
    LPT2Mode=FAST
    Rem - Admin. HP7580 plotter's queue is named PQ-HP7580
    COM1Queue=PQ-HP7580
    Rem - Plotter set up for 19200 baud, 8 data, no parity, 1 stop
    COM1BaudRate=19200
    COM1DataBits=8
    COM1Parity=None
    COM1StopBit=1
    Rem - No COM2 hardware on this machine - assure disabled
    COM2Queue=NONE


Notice that uppercase and lowercase are mixed freely in this example. As
mentioned above, FPSERVER capitalizes all alphabetic characters prior to
processing them.  Feel free to make the file "human readable".



===============================================================================
INSTALLATION
===============================================================================

Installing FPSERVER.EXE
---------------------------------------

There is no complicated installation procedure for FPSERVER.  The program
file itself, FPSERVER.EXE, may be placed in any subdirectory.  However,
since most host PC's will be dedicated to the task of print servers, it is
recommended that FPSERVER.EXE be placed in the root directory of the boot
device (probably either A: or C:) to reduce the size and complexity of the
AUTOEXEC.BAT file.

In an internetworked environment where more than one File Server is
present, it is recommended that the PREFERRED SERVER command be included in
the SHELL.CFG file for Novell's IPX.COM and NETx.COM.  This will insure
that NETx attaches to the correct File Server during bootup.  (Including
the PREFERRED SERVER command is an excellent idea for all workstations in
an internetworked environment.)  Please refer to the Novell NetWare
documentation for more information regarding the SHELL.CFG file and its
PREFERRED SERVER command.



Creating the FPSERVER.CFG File
---------------------------------------

The FPSERVER.CFG file, if used, may be created with any editing program
that can produce a "pure" ASCII file on disk.  Pure ASCII, in this context,
indicates that the file must not contain word processing commands or other
non-human readable information (essentially, it should include only
numbers, letters, and standard punctuation characters).  DOS's EDLIN
program and all text editors work in this manner; most word processing
programs also have a "text output" or "ASCII output" option that prevents
the inclusion of special formatting characters.

FPSERVER.CFG must reside in the default subdirectory in effect when
FPSERVER is invoked.  This does not mean that they must reside in the SAME
subdirectory, although that is definitely the most desirable (and least
error-prone) configuration.  What it DOES mean is that if, before typing
FPSERVER at the command line, you type "DIR <enter>", FPSERVER.CFG must be
one of the files shown in the current subdirectory.

Obviously, the best situation is to have both FPSERVER.EXE and FPSERVER.CFG
in the same subdirectory, and make that subdirectory the current one, when
starting FPSERVER.  The easiest way to insure this is to place both files
in the root directory of the boot device and be in that root directory.



Temporary Modifications
---------------------------------------

One of the most convenient features of FPSERVER's configuration system is
the ability to temporarily override the contents of the FPSERVER.CFG file
with entries on the command line.  The fact that you need not be logged in
to the File Server between "sessions" of FPSERVER streamlines this even
further.

As an example, to change the queue being serviced by Novell's PSERVER.EXE,
you would have to perform the following steps (the following assumes that
the print server in question already has sufficient rights to service the
new queue):

     * Reboot the print server (since Novell's PSERVER.EXE does not provide
       a "clean" exit to DOS)

     * Log in using an account with sufficient rights to modify the
       parameters of the print server in question

     * Run Novell's PCONSOLE.EXE

     * Work your way down through the menu system until you reach the
       level at which the "Queues to be Serviced" can be edited

     * Delete the old queue and enter the new one, specifying the correct
       parallel or serial port as you do so

     * Back out of the menu system until you reach DOS again

     * Reboot the print server (if necessary) and run Novell's PSERVER.EXE


Through all of this, you will have to reboot the print server host PC
at least once and run two separate programs - just to try something a little
different.  If you do not like the results, you get to go through the entire
routine again just to put things back the way they were.

In contrast, FPSERVER can be reconfigured the same way with the following
steps:

     * Exit to DOS by pressing Escape on the print server's host PC

     * Press F3 to recover the "FPSERVER" command line that last started
       the software

     * Add the appropriate "portQUEUE=" command to the end of the command
       line (which will override any similar command in FPSERVER.CFG)

     * Press Enter!

This amounts to 13 keystrokes plus the length of the queue name.  There is
no need to reboot the host PC, or log in as someone else, to change
FPSERVER's operation - just a few keystrokes and a few seconds completely
reconfigures its behavior.

To restore things back to the way they were, simply press Escape, type
FPSERVER on the command line, and press Enter.  Ten keystrokes and
everything reverts back to the configuration specified in FPSERVER.CFG.



Permanent Modifications
---------------------------------------

To make configuration changes permanent, simply modify the FPSERVER.CFG
file using your ASCII text editor.  Again, this may be done by simply
Escaping out of FPSERVER, running the editor, and restarting FPSERVER. It
is not necessary to reboot the host PC nor log in to the File Server.



===============================================================================
NORMAL OPERATION
===============================================================================

Starting the Print Server
---------------------------------------

FPSERVER may be started by typing its name at any DOS prompt and pressing
Enter.  However, in most installations, the PC will be dedicated to the
print server application.  In such environments, FPSERVER may be included
as the last command in the PC's AUTOEXEC.BAT file to completely automate
its startup.

Configuration commands may optionally follow FPSERVER's name up to the
limit that DOS imposes on the length of the command line.  See the
"Controlling PSERVER's Operation" section earlier in this file
for more information regarding configuration commands and their parameters.

Regardless of the startup method chosen, the FPSERVER.CFG file must reside
in the default directory when FPSERVER is invoked.  See "Creating the
FPSERVER.CFG File", above, for more information.



The AdWare Screen
---------------------------------------

When FPSERVER is started, an "AdWare" screen appears which describes my
services as a Network Software Consultant.  This screen remains displayed
for 60 seconds (a downcounter at the bottom of the screen indicates time
remaining).  At the end of 60 seconds the screen is erased automatically.
This insures that FPSERVER will self-start after a power failure (assuming
it was invoked by the host's AUTOEXEC.BAT file) and is in keeping with my
philosophy that network resources should accept, but never REQUIRE, human
intervention.

To override the AdWare screen and avoid the 60 second delay, type the
initials "RLH".  Each correct keystroke generates a high-frequency tone;
incorrect keystrokes generate a low-frequency tone and reset the initials
back to "R".  You must type the three initials correctly, in order, to
erase the AdWare screen.  Making a mistake (and receiving a low-frequency
tone) simply means you must start with "R" again.

After the AdWare screen has been erased, the normal print server display
appears.



The Status Line
---------------------------------------

This normal print server screen is separated into four regions, one for
each of the four hardware ports supported by FPSERVER.  All are identical
in their content; the following description is applicable to all four port
displays.

The top, or status, line contains the traditional name for the associated
hardware port (LPT1, LPT2, COM1, or COM2). This is followed by the name of
the print queue to which this hardware port is logically attached (as
specified by the xxxxQUEUE command in either the FPSERVER.CFG file or the
command line). The print queue's name is truncated, if necessary, to fit on
the status line.

The right side of the status line displays port information.  The first
parameter reports throughput limitations and may take one of three values:

     Printer Limited     (Parallel only.)  FPSERVER is capable of
                         transferring data more quickly, but the printer's
                         BUSY line is not allowing it to do so.  The
                         printer asserts BUSY when it is unable to accept
                         another byte of data. This occurs after each byte
                         is transmitted and during intensive printer
                         processing.  FPSERVER must wait for BUSY to go
                         inactive again before transmitting the next byte.
                         This is the most common limiting factor for
                         parallel printers.

     Baud Limited        (Serial only.)  FPSERVER is capable of
                         transferring data more quickly than the selected
                         baud rate will allow.  Increasing the baud rate
                         may improve printing speed somewhat, but at some
                         point the printer will not be able to benefit from
                         further increases in baud rate.

     PServer Limited     The printer is capable of accepting data faster
                         than FPSERVER is able to supply it.  This may be
                         caused by a slow host PC, a slow or very busy
                         network, or an EXTREMELY fast print device.  Refer
                         to "Fine Tuning for Maximum Performance" later in
                         this file for tips on improving throughput.


Each port's status line also displays printer information to the extent
that it is available from the printer itself (more data is available from
parallel devices than from serial devices):

     OFFLINE             (Parallel only.)  The printer is off line.

     PAPEROUT            (Parallel only.)  The printer is out of paper.

     ERROR               (Parallel only.)  The printer is in an error
                         condition, other than Off Line and Paper Out, for
                         which no further information is available.  This
                         may be caused by an access cover being open, low
                         toner or ink, erroneous data, or loss of power.
                         Many printers indicate such errors on their front
                         panels. Consult the printer's documentation.

     DTR Off             (Serial only.)  The printer is momentarily not
                         accepting data.  This generally occurs when the
                         baud rate is faster than the printer's effective
                         throughput rate.  With data coming in faster than
                         it can be printed, the input buffer fills until
                         eventually the printer can accept no more data.
                         The printer then "turns off" the DTR line to
                         prevent further transmission until it has emptied
                         the buffer to some extent.


For parallel devices, the BUSY line is the only parameter which controls
the transfer of data.  OFFLINE, PAPEROUT, and ERROR are reported by
FPSERVER but do not affect data flow.  Many printers - especially those
with large input buffers - are capable of accepting data while offline
and/or out of paper, and FPSERVER supports them without limitation.

Serial devices use DTR as their sole means of flow control, and thus
FPSERVER must cease sending data when DTR goes "off".



The "Former" Line
---------------------------------------

The Former line appears immediately beneath the status line.  It displays
the owner, description, size, and average speed (in bytes per second) of
the most recently completed print job.

The average speed is calculated by dividing the job's size by its duration
in integer seconds.  A job's duration is considered to start when the first
byte of data is received from the file server and end when the last byte of
data is transferred to the printer.  ANY event which lengthens this amount
of time - and thus adversely affects the overall amount of time consumed by
the job - will correctly result in a decrease of the average speed.  This
includes running out of paper, going off line, and other "normal"
occurrances.



The "Current" Line
---------------------------------------

The Current line appears beneath the status line.  It displays the owner,
description, size, and progress of the job currently being printed.

The progress display appears on the right side of the Current line and
indicates the number of bytes which have been sent to the printer.  The
value is updated as the device accepts more data from FPSERVER.
Interruptions in data flow will cause this value to stop increasing (since
the device is not accepting data).

A job remains on the Current line until the last byte of data is accepted
by the printer.  When the last byte has been successfully transferred,
FPSERVER notifies the file server that the job has been completed (so it
can be removed from the print queue) and passes the completion information
to the Former line (described above).



The "Pending" Lines
---------------------------------------

The three remaining lines form a queue display showing jobs ready to be
printed.  Up to three jobs - one per line - can be displayed.  Multiple
pending jobs are shown in the order they will be printed, with the topmost
job being first.  Each pending job displays its owner and its description.

Jobs appear in the Pending area only when they are complete and ready for
service.  This differs from other print server programs, which often
display jobs still being uploaded to the file server.  The problem with
including such incomplete jobs is that a prioritized list, such as the one
in the Pending area, can be rendered inaccurate at any moment by a smaller
job which started later but finished uploading first.  Such a job can "jump
ahead" of the incomplete jobs - seeming to "pop" into the Current line
without ever having been in the queue.  FPSERVER prevents this problem by
only displaying those jobs which are complete and ready to go: the order in
which they are displayed is the order they will be printed.



Stopping the Print Server
---------------------------------------

Execution of FPSERVER may be stopped by pressing Escape (as noted in the
title at the top of its screen).  FPSERVER stops servicing active jobs,
frees allocated memory, and cleanly returns control to DOS.

Jobs which were being printed when Escape was pressed are reset, at the
File Server, and will be serviced when FPSERVER is restarted (or another
authorized print server notices them).  Exceptions to this can occur if
requested by the software which originated the job, but NetWare's standard
methods for queuing print data (CAPTURE and NPRINT) both allow prematurely
terminated servicing to restart without data loss.



Why Stop the Print Server?
---------------------------------------

One situation where the ability to easily stop, and restart, FPSERVER can
be particularly helpful is with "runaway" print jobs.  If data was emitted
in the wrong format, or directed to the wrong printer, it can result in a
long sequence of form feeds or other inconvenient events.  Unfortunately,
regaining control of this situation can be difficult since the data exists
in up to three places: the File Server (data still in the print queue), the
Print Server (data waiting to be transferred to the printer), and the
printer itself (data in its input buffer which has yet to be processed).

Regaining control involves running PCONSOLE (to delete the remaining data
from the print queue) and resetting the printer (to flush its buffers).
Unfortunately, there may still be data in the print server which will
immediately be transferred to the printer when its reset cycle is complete.
For other print server software, this involves a complete warm boot of the
host PC; with FPSERVER, it involves two commands.  At the keyboard, type:

     <Esc>
     FPSERVER   <enter>


...and FPSERVER will restart with its buffers empty.  If FPSERVER was
originally started from the keyboard (instead of the AUTOEXEC.BAT file), F3
may be used to "recall" the original command - thus reducing the number of
keystrokes to three (Escape-F3-Enter).

Be sure to have deleted the job from the queue with PCONSOLE prior to
restarting FPSERVER.  Otherwise, FPSERVER will begin servicing the job the
moment it restarts.



===============================================================================
ERROR MESSAGES AND TROUBLESHOOTING
===============================================================================

This section lists many of FPSERVER's error messages, the reasons that can
cause them to be displayed, and recommended actions.



Workstation is not attached to a file server
--------------------------------------------

REASON: Upon receiving control from DOS, FPSERVER confirms that the
workstation is "attached" to a File Server.  ("Attached", as defined by
NetWare, means that the physical and logical connections exist which allow
the workstation to log in to the File Server.)  This message is displayed
if such an  attachment cannot be found.

ACTION: Confirm that the workstation is physically and logically connected
to the File Server which hosts the print queues to be serviced.  It is not
necessary to be logged in.



Unable to log in as Print Server
---------------------------------------

REASON: FPSERVER is unable to log in to the File Server using the Print
Server object name specified in the PRINTSERVER= command.

ACTION: Confirm that the Print Server object's name is spelled correctly.
Because there is no default for the PRINTSERVER= command, the lack of any
specified Print Server object name will modify the error message to read:

     Unable to log in as Print Server (unspecified)

In this case, add the missing PRINTSERVER= command to either the
FPSERVER.CFG file or the command line.



Insufficient memory for required buffers
----------------------------------------

REASON: FPSERVER allocates buffers for all active ports.  Serial ports
require buffers of a fixed, 4096 byte size; parallel ports require a
minimum of 16384 bytes each but can use 50K or more depending upon the
amount available and the number of active ports.  The MINIMUM amount of
buffer memory required for operation is:

     (# of serial ports * 4096) + (# of parallel ports * 16384)

Obviously, a larger number of active ports will require more memory.
FPSERVER emits the above message when host PC does not have sufficient
memory to accommodate the buffers required.

ACTION: This message will only appear in the most minimal memory conditions.
FPSERVER was specifically designed to NOT require large amounts of memory;
128K free (as reported by CHKDSK) is more than adequate.

There are two solutions: Reduce the amount of memory required or increase
the amount of available memory.  The former can be accomplished by reducing
the number of active ports on the print server; the latter can involve
installing more RAM, or reducing the demands of other software on the PC's
memory (including DOS and the network shell programs).



Error in command line: <command>
------------------------------------------

REASON: FPSERVER has detected an error in one of the configuration commands
supplied on the DOS command line.  The error may be in the command itself
(misspellings, etc.) or in the value of the parameter associated with it.
The erroneous command is displayed for reference.

ACTION: Run FPSERVER again with the command corrected.  Refer to this file
for more information on the command in question if the error is not
obvious.



Error in configuration file: <command>
---------------------------------------

REASON: FPSERVER has detected an error in one of the configuration commands
supplied in the FPSERVER.CFG file.  The error may be in the command itself
(misspellings, etc.) or in the value of the parameter associated with it.
The erroneous command is displayed for reference.

ACTION: Run FPSERVER again with the command corrected.  Refer to this file
for more information on the command in question if the error is not
obvious.



Non-existent port cannot service queue <queuename>
--------------------------------------------------

REASON: A queue has been specified for a port which does not exist on the
host PC.  Actual physical hardware MUST exist for each port-queue
attachment; "MODE" and "CAPTURE" commands and other methods of redirecting
port output cannot be used with FPSERVER.

ACTION: Run FPSERVER again after removing references to non-existent ports
from the FPSERVER.CFG file and the command line.



Cannot attach to non-existent queue <queuename>
-----------------------------------------------

REASON: The specified print queue does not exist on the File Server to
which the host PC is logically attached.

ACTION: Confirm that the print queue name is correctly spelled.  Confirm
that the print queue exists on the File Server to which the host PC is
attached.



Insufficient rights to queue <queuename>
----------------------------------------

REASON: The Print Server object specified in the PRINTSERVER= command
does not have sufficient rights to service jobs in the specified print
queue.

ACTION: Confirm the desired print queue is specified.  Run Novell's
PCONSOLE and grant service rights to the specified Print Server object for
the specified queue.  Run Novell's PCONSOLE and confirm that the print
queue is enabled and that new print servers may attach to it.



Not listed as server for queue <queuename>
------------------------------------------

REASON: The Print Server object specified in the PRINTSERVER= command
is not listed as a valid print server for the specified print queue.

ACTION: Run Novell's PCONSOLE and add the specified Print Server object  to
the list of print servers allowed to service the specified print queue.



Too many servers attached to queue <queuename>
----------------------------------------------

REASON: NetWare allows a maximum of 25 simultaneously attached servers
to any one print queue.  NetWare did not allow FPSERVER to attach to the
specified print queue because it is already being serviced by 25 other
print servers.

ACTION: Confirm the desired print queue is the one specified.  Detach  one
or more other print servers from the print queue.



General failure attaching to queue <queuename>
----------------------------------------------

REASON: NetWare did not allow FPSERVER to attach to the specified print
queue for a reason other than those specifically addressed by the error
messages described above.

ACTION: Run Novell's PCONSOLE and confirm that the specified print queue's
operating parameters are acceptable.  Refer to Novell's documentation for
further information.



===============================================================================
FINE TUNING FOR MAXIMUM PERFORMANCE
===============================================================================

FPSERVER is seldom the limiting factor in a network printing system.  Many
other components and subsystems conspire to limit the ultimate printing
bandwidth.  This section discusses some of the more common limiting factors
and offers improvement suggestions.  Some, none, or all of these may be
applicable to your situation; consult your equipment's documentation and
manufacturer(s) for more specific information.



Printer Data Rates
---------------------------------------

The most common limiting factor is the print device itself.  Different
printers accept data at different rates.  In fact, the same printer will
often accept data at varying rates depending upon the data's formatting,
content, and other factors.

If the device has an input buffer, its initial data rate can be very high
while the buffer is being filled.  This is because the printer simply
stores the data (rather than processing and printing it) and writing data
into memory is a relatively fast operation.  Ultimately, however, the
buffer will be filled and the data rate must then drop to the speed at
which the device can generate an image on the output media - since that is
the rate at which new buffer space becomes available.

The type and content of the data is also significant.  For example: A fully
rasterized image, sent to a laser printer, places very little burden on the
printer's microprocessor and is basically transferred directly into the
page buffer.  The limiting factor in this case is often the engine speed;
the printer can move the paper only so fast regardless of how quickly data
can be accepted from the host and placed into memory.

The fastest data rates are generally achieved with single pages of fully
rasterized (graphics) laser printer data.  In these cases, the last byte of
data is transferred before the engine begins operation and thus the
mechanism speed is factored out.

"BPS" values drop when the print job exceeds a single page.  The first page
will still transfer into the empty page buffer very rapidly, but subsequent
bytes must wait for room to appear in the page buffer as its current
contents (the first page) are transferred to paper.  In addition, the
printer's microprocessor will devote less time to data reception since it
will also be running the engine (a workload which was not present during
the transfer of the first page's data).

High level printer "languages", such as Hewlett Packard's PCL 5 and
especially Adobe's PostScript, can yield even lower data transfer rates.
Unlike pure graphics - where one bit generally equals one pixel - very
small amounts of high level printer languages can create an ENTIRE PAGE of
rasterized data.  The conversion is handled by the printer's
microprocessor, which may accept a small amount of data and then "go deaf"
while those few bytes generate an entire page.  The dramatically reduced
"BPS" values that result from this condition do not mean that your printing
throughput is poor, but that each byte of data is generating a lot of
rasterized output.

Pure text can produce the lowest "BPS" values, again due to mechanism
speed.  As an example: Assume a laser print job contains ten pages of 25
characters each.  The data for the first page will transfer - and the
rasterized image will be created - almost instantly.  However, the second
(and subsequent) pages will be limited by the printer's need to physically
print the previous page.  Since a laser's engine speed is a constant, each
page takes the same amount of time to pass through the mechanism - and thus
fewer characters per page yields lower "BPS" values even though throughput
(as measured in PAGES) is constant.

In any case, FPSERVER is almost certainly capable of supplying data faster
than your print device is willing to accept it.  The appearance of the
"Printer Limited" message on the port's Status Line indicates that the
printer is refusing data when FPSERVER offers it.  You may confirm this -
and determine FPSERVER's maximum data rate in your environment - by using
FPSERVER's "Test" mode (described below).



FPSERVER's Test Mode
---------------------------------------

FPSERVER's parallel port routines have a special mode which can be used
to determine the maximum throughput possible in the tested environment.
This mode may be invoked by using the LPTxMODE= command as follows:

     LPT1MODE=TEST   <for LPT1>

...or:

     LPT2MODE=TEST   <for LPT2>


Selecting "Test" mode causes FPSERVER's parallel port routine to act as
if an infinitely fast print device were connected to the designated port.
All of the same routines are used - and the print job data is actually
transmitted - but printer-induced delays are ignored.

This is a complete bandwidth test which involves the disk drives on the
File Server, the network cabling and interfaces, the clock rate of the
print server's processor, the speed of the print server's parallel port
hardware - EVERYTHING associated with transferring a print job from the
File Server to the connector on the back of the print server.  The
resulting bytes per second (BPS) values indicate the absolute maximum
throughput of which FPSERVER is capable in the test environment.

Some notes regarding "Test" mode:

     * Files of sufficient size must be used for "Test" mode results to be
       significant.  The most accurate values will be obtained with jobs at
       least 500KB in size.

     * Multiple jobs should be run through "Test" mode so that the File
       Server's job startup overhead can be factored into the results.
       Multiple, back-to-back jobs should be queued up and ready to go
       prior to starting FPSERVER in "Test" mode.

     * Most printers will report errors if connected during "Test" mode.
       This is because FPSERVER does not honor their Busy line and thus
       transmits the data faster than the printer can accommodate it. It is
       recommended that printers be disconnected during "Test" mode to
       prevent erratic operation.

     * Printer status signals, such as OFFLINE, PAPEROUT, and ERROR are
       still reported in "Test" mode even though they have no effect on
       FPSERVER's operation.  They may be safely ignored.

     * Test mode may be temporarily invoked by including the LPTxMODE=TEST
       command on the DOS command line.  Normal FPSERVER operation will
       resume the next time it is started without the additional command.

     * Test mode may be used only with parallel ports.  Few serial devices
       support "dynamic" baud rates or per-byte hardware handshaking, and
       thus cannot obtain useful information from such a test.



Printer Speed Settings
---------------------------------------

One way to improve printer throughput is to optimize the printer's
configuration.  Many printers have setup options which can increase (or,
when incorrectly set, decrease) data throughput.

For example, the Hewlett Packard LaserJet IIISi's parallel port has an
optional HIGH SPEED mode which can be configured from the printer's front
panel.  Setting HIGH SPEED=NO causes the IIISi to use a Busy signal with a
minimum duration of 10 microseconds.  Setting HIGH SPEED=YES reduces the
minimum Busy duration to 1.5 microseconds - a significant reduction which
has a dramatic impact on data throughput.

Be sure to review your print device's documentation for speed-enhancing
configuration options.  You may wish to contact the manufacturer for
specific recommendations or suggestions.



Bridges
---------------------------------------

Bridges, used to connect multiple networks, can impose limitations on
overall throughput.  To understand why, it is useful to review the "data
path" for queued print data.

When a workstation requests that a job be printed, the data is directed
into a print queue.  The print queue resides on a File Server - the same
File Server to which FPSERVER attaches during initialization.  During job
servicing, the data is retrieved from the File Server's hard drive, sent
through the network interface card, over the cable, into FPSERVER's network
interface card, and out to the print device.  At a minimum, therefore,
queued print data must pass through two software programs (the File
Server's operating system and FPSERVER) and two network interface cards
(one each on the File Server and FPSERVER's host PC).

Internal bridges - i.e. multiple interface cards installed in the File
Server's backplane - are already in a "minimum" configuration.  The fact
that the data was received on one network interface card and is transmitted
on another is unimportant, since it is buffered to hard disk in the
meantime.  As a result, internal bridges do not restrict bandwidth.

In contrast, external bridges can impose significant bandwidth limitations.
The presence of an external bridge in the data path inserts at least one
more software program (the bridge operating system) and two more network
interface cards (one in and one out of the bridge).  In many installations
this is probably compounded by the fact that most bridges are slower 80286
systems with inherently poorer throughput.

The "packaged" bridges which are becoming available on the market may not
suffer from the same limitations as those which run on standard PC hosts.
However, to maximize throughput, it is strongly recommended that FPSERVER's
host PC be connected to a network cable which runs directly to the File
Server containing the serviced print queues.



Dedicated Network Cables
---------------------------------------

Contrary to popular belief, it is NOT necessary to connect a PC-hosted
print server to the File Server with a dedicated network cable.  Under most
circumstances (with most printers), the print server can share its cable
with other workstations and will not place an undue burden on the total
cable bandwidth.



Multiple Ports per Print Server
---------------------------------------

Many times the first approach to increasing print server throughput is to
reduce its number of active ports.  This is often very effective on other
print server software - but is COMPLETELY UNNECESSARY with FPSERVER.

FPSERVER incorporates a "dynamic linking/unlinking" algorithm which reduces
the overhead on inactive ports to ZERO.  Whenever the queue associated with
a given hardware port is empty, FPSERVER unlinks the associated software
routines from its service chain as if the port had never been activated.
Only when a job is ready for service does FPSERVER relink the associated
hardware's service routines and begin devoting resources to it.

Careful design has also lessened the impact of multiple simultaneous jobs.
Reductions of 10-20% are typical - rather than the 50% loss often
experienced with other print server software.  As stated earlier, FPSERVER
generally has far more bandwidth capability than the print devices which it
drives, and that bandwidth is automatically optimized across currently
active devices in real time.

FPSERVER's high throughput also reduces the likelyhood, and duration, of
coincident jobs.  Jobs are completed faster and are thus less likely to
incur even FPSERVER's small multi-job throughput degradation.

The bottom line is: There is little to no penalty when connecting multiple
devices to FPSERVER simultaneously.  What may have required multiple
dedicated print servers in the past can now be handled with a single PC.



16 Bit Network Interfaces and Drivers
---------------------------------------

The print server's network interface card can have more effect on overall
throughput than any other component.  Recommendations can be summarized
into the following: Use a 16 bit network interface card with a 16 bit
optimized driver.

16 bit network interface cards have been shown to have significantly
higher effective bandwidth than their 8 bit counterparts.  While parallel
and serial port hardware is, by definition, 8 bits in width, the interface
to and from the network interface card's buffer memory has no such
architectural restriction and should thus be as wide as possible.

16 bit network interface cards should have drivers optimized for use in a
16 bit environment.  It is possible to write a driver which is compatible
with both 8 bit and 16 bit hosts and interfaces.  Such "universal" drivers
do not take adequate advantage of the host PC's 16 (or 32) bit processor.
Call the network interface card manufacturer, if necessary, and confirm
that the driver is specifically intended for use on 16 bit (read: 80286 and
up) microprocessors.



Loading DOS and Other Programs "High"
---------------------------------------

DOS 5.0, and many third-party utilities, allow drivers and portions of the
operating system to be loaded above the traditional 640K DOS memory area
(into a region commonly known as "high memory").  This is traditionally done
in an effort to release memory in the lower 640K for use by applications
software.

FPSERVER uses a MAXIMUM of 128K free memory.  Amounts greater than that are
unused while FPSERVER is in operation and therefore wasted.  If, just prior
to running FPSERVER, CHKDSK reports 128K or more free, loading programs
"high" will yield absolutely no advantages.

Loading programs "high" CAN yield disadvantages, however.  A special device
driver is typically required to handle the redirection to software loaded
in "high" - and this driver can severely impact overall PC performance.
Measurements on DOS 5.0's EMM386.EXE showed a 50% DECREASE in I/O bandwidth
- presumably because EMM386.EXE was intercepting I/O operations in case
they were intended for a program loaded "high".  (This test was run without
ANY programs actually loaded high; just EMM386.EXE's presence in memory cut
I/O throughput in half.)

Use of Novell's XMSNETx.EXE and EMSNETx.EXE programs can impact throughput
because they too make use of memory outside the standard 640K.  While very
useful in memory-bound environments, these programs are a detriment to
FPSERVER's bandwidth; furthermore, they are unnecessary since FPSERVER's
128K is seldom too great a demand on the host machine's resources.

In summary, FPSERVER will operate perfectly with DOS, network drivers, etc.
loaded "high".  However, the low memory thus freed will very likely go
unused - and overall print server throughput will suffer needlessly.  It is
strongly recommended that the host PC load all software in the standard
640K DOS memory area for maximum performance.



Bus Clock Speeds
---------------------------------------

*******************************************************************************
*                               CAUTION!!!                                    *
*                                                                             *
*    The following section discusses altering the fundamental operating       *
*    characteristics of the host PC.  Only individuals VERY EXPERIENCED       *
*    with PC's and their internal operation should modify these parameters.   *
*    Incorrect settings can render your PC inoperative.  If you are not       *
*    COMPLETELY familiar with the architecture of your PC, please obtain      *
*    the assistance of a qualified PC Technician.                             *
*                                                                             *
*    Not all BIOS's allow these parameters to be modified.  Please consult    *
*    your computer's documentation or manufacturer for more information and   *
*    specific recommendations.                                                *
*******************************************************************************

Most AT-class PC's of recent vintage are fabricated using high integration
chipsets, where four or five "mega-chips" are equivalent to hundreds of
small- and medium-scale integration IC's.  The BIOS included with PC's of
this type generally have a secondary setup screen where operational
parameters may be manipulated to fine tune the machine's performance.  One
of these parameters, the Bus Clock, affects the speed with which operations
may be performed on the backplane - where the parallel, serial, and network
interfaces reside.

(For technical accuracy, it should be pointed out that there is no actual
"clock" signal, as such, on the backplane.  Instead, this signal serves as
the fundamental for the various timing and control signals which actually
run the asynchronous AT bus.)

The Bus Clock is usually derived from the processor clock via division by a
value selected in the BIOS setup screens.  Manipulating this divisor
inversely affects the Bus Clock (increasing the divisor decreases the speed
of the Bus Clock, and vice versa).

Typical Bus Clock divisor values which may be selected include 2, 3, and 4
which, on a 25MHz machine, would yield "bus speeds" of 12.5MHz, 8.33MHz,
and 6.25MHz respectively.  The early IBM AT used an "8MHz" bus clock, thus
defining the lowest speed at which cards intended to be compatible must
operate.  Since virtually all cards compatible with the AT backplane can
therefore be expected to run with an 8MHz Bus Clock, BIOS's for faster
(33MHz and 40MHz) processors usually include higher numbers to allow the
bus speed to reach the 8MHz range.

Since, as stated above, all AT cards are designed to accommodate 8MHz,
FPSERVER's host should always run its bus at 8MHz or above.  FPSERVER's
throughput MAY be improved by decreasing the divisor value, and thus
increasing the Bus Clock, to operate the backplane cards at a faster speed.
Reduce the divisor ONE INCREMENT AT A TIME and carefully observe the
effects.  You should reboot the machine multiple times to confirm reliable
operation at the new bus speed.

Regarding the Bus Clock's "upper limit": there seems to be an industry
threshold at 12MHz.  While cards do exist which have been designed to
operate beyond that speed, they are definitely the minority.  For safety,
consider 12MHz as the top end of the bus speed range.

Be sure to record the original values of all parameters before altering
them.  It may become necessary to restore them in the future as other cards
are added to the system.



I/O Wait States
---------------------------------------

*******************************************************************************
*                               CAUTION!!!                                    *
*                                                                             *
*    The following section discusses altering the fundamental operating       *
*    characteristics of the host PC.  Only individuals VERY EXPERIENCED       *
*    with PC's and their internal operation should modify these parameters.   *
*    Incorrect settings can render your PC inoperative.  If you are not       *
*    COMPLETELY familiar with the architecture of your PC, please obtain      *
*    the assistance of a qualified PC Technician.                             *
*                                                                             *
*    Not all BIOS's allow these parameters to be modified.  Please consult    *
*    your computer's documentation or manufacturer for more information and   *
*    specific recommendations.                                                *
*******************************************************************************

I/O Wait States are another set of parameters which, like the Bus Clock
described above, affect the speed with which operations may be performed on
the backplane.

Many AT-compatible cards cannot accommodate the I/O speeds of which current
microprocessors are capable. The limiting factor is often the IC's used on
the cards; many logic families, fast enough for 4.77MHz 8088's, simply
cannot sustain the command and data rates of later generation
microprocessors.

Recognizing this, the high-integration chipsets used in so many AT-class
machines allow the insertion of "wait states" into input and output
operations.  Simply stated, a wait state causes the processor to idle for a
known length of time - thus giving the external device a chance to react to
the processor's instruction.  The slower the device, the greater the number
of wait states.

Wait states impose a heavy penalty on performance - not surprising since
the microprocessor is essentially being told to "hurry up and wait".  Early
80286-class PC's, often advertised as 12MHz (or even 16MHz) machines, had
wait states on MAIN MEMORY and thus ran little faster than zero-wait-state
8MHz or 10MHz PC's.

The accepted norm is now to place all memory on the motherboard and run it
at full speed without wait states (or to include a cache which offsets some
of the impact of slow memory).  The same is not true, however, of ports,
video boards, and other peripherals.  Even when mounted directly on the
motherboard, the processor communicates with these components via I/O
instructions - rather than memory reads and writes - and thus any I/O Wait
States will directly impact their communications bandwidth.

As with the Bus Clock, acceptable values for I/O Wait States will vary
between different PC's, processor clock speeds, and combinations of
external cards.  Empirical analysis (read: trial and error) is the best
method, since the goal is to obtain the fastest reliable operation for the
machine in question.  Many BIOS's allow independent numbers of wait states
to be specified for 8 bit I/O operations (parallel and serial ports) and 16
bit I/O operations (most network interfaces), and different values may be
required for optimal performance.

FPSERVER's throughput MAY be improved by reducing the number of I/O Wait
States.  Reduce the number of wait states ONE INCREMENT AT A TIME and
carefully observe the results.  You should reboot the machine multiple
times to confirm reliable operation with the new values.

Be sure to record the original values of all parameters before altering
them.  It may become necessary to restore them in the future as other cards
are added to the system.



===============================================================================
TECHNICAL DETAILS
===============================================================================


Small Memory Model
---------------------------------------

FPSERVER is written in both C and assembly, compiled and linked for the
"small" memory model.  Since all of FPSERVER's code fits within the 64K
(single code segment) limitation imposed by the small memory model, its
only disadvantage is that the sum of the allocated port buffers cannot
exceed the small model's single 64K data segment.  Extensive testing
indicated that such larger buffers do not play a significant role in
FPSERVER's ultimate throughput.

The key advantage to using the small memory model is the elimination of
segment register manipulation.  The use of multiple data segments, with
their unique base addresses, would have required several speed-sensitive
routines to save, load, and restore segment registers.

Since the sole benefit of multiple data segments would have been larger
port buffers - and since such buffers do not yield an appreciable benefit -
throughput was favored and the small model was selected.  All pointers are
thus 16 bit values which can be manipulated within single registers and
with minimal memory read/write operations.



Interrupts
---------------------------------------

FPSERVER uses software interrupt 1C hex, the Timer Service Routine, for
various purposes.  It does NOT use nor redirect hardware interrupt 8 (IRQ
0), the hardware Timer Tick, but instead lets the Timer Tick service
routine call it via interrupt 1C hex.  FPSERVER's Int 1C routine "chains"
itself into the call sequence in the appropriate manner, and passes control
to the original Int 1C vector upon completion.  When FPSERVER is terminated
by pressing Escape, the original Int 1C vector is properly restored.

FPSERVER does not use any hardware interrupts.  All of the IRQ lines
normally associated with parallel and serial ports are ignored.  FPSERVER
does NOT disable them at the 8259A interrupt controller, however, so they
may be used for other purposes (such as the network interface card) if
necessary.  Please note that, if the interrupt lines are in use, an
appropriate driver must be installed to service them.



"Safe" vs. "Fast" Parallel Operation
---------------------------------------

There is no universally recognized timing diagram for a "Centronics"
parallel port.  Different manufacturer's specifications offer a variety of
minimum and maximum pulse widths for Strobe, Busy, Acknowledge, and the
other signals which comprise the hardware handshaking system for this
industry "standard".  Even different product manuals from Centronics itself
do not agree on a single set of values.

The vast majority of modern print devices treat Strobe as an "edge
sensitive" signal, which can be briefly interpreted as meaning that the
width of the pulse is less important than the fact that a pulse actually
occurred.  FPSERVER's "Fast" parallel mode takes advantage of edge
sensitive devices to dramatically increase data throughput.

However, print devices may exist which are "level sensitive", meaning that
they expect to see Strobe stay active for a some minimum period of time.
Since there is no industry standard for a Centronics port's strobe pulse
width, FPSERVER's "Safe" parallel mode uses a value of 500 nanoseconds as
stated in the original IBM Personal Computer Technical Reference manual
(IBM document number 6025005), page 2-81.

FPSERVER's "Fast" parallel mode has been tested with a wide range of
parallel devices and, to date, none have proven incompatible.  Both LPT1
and LPT2 default to "Fast" mode unless an LPT1MODE=SAFE or LPT2MODE=SAFE
command appears in the FPSERVER.CFG file or on the DOS command line.

"Safe" mode has been included to guarantee compatibility with the maximum
number of different parallel devices.  However, for maximum throughput,
"Fast" mode is highly recommended.



===============================================================================
BUGS AND OTHER ANOMOLIES
===============================================================================

Bugs
---------------------------------------

There are no known bugs in FPSERVER.  However, that does not mean that none
exist!  Bugs will be corrected as they are discovered (by me) or reported
(by you).

Please be sure to retry any failed operation before assuming it is a bug.
Any number of events can corrupt data flowing over a network cable (failing
network interface card, accidental disconnection of the cable, etc.).  If
it happens once, and you cannot repeat it, it probably isn't a FPSERVER
bug.

If you have what appears to be a legitimate bug, I WOULD LIKE TO HEAR ABOUT
IT!  Please be sure to document the hardware and software environment of
the bugs, along with (if possible) copies of the files which were being
printed at that time.  I may be contacted via CompuServe or mail (the
account number and address appear at the beginning of this file).



Anomolies
---------------------------------------

The only unexplained phenomenon known at this time occurred when FPSERVER was
operating across an external bridge from its host File Server.  Novell's
own PSERVER.EXE suffered from the same problem, so it may have had more to
do with the bridge than with the print server.

The symptom was the occasional emission of the following message from the
Novell NETx shell:

    Error Receiving from Network
    Abort, Retry?

There was no successful recovery from this error other than a soft boot
(Ctrl-Alt-Del).  The frequency of its occurrance was reduced somewhat by
adjusting the SPX/IPX parameters in the SHELL.CFG file (to make the
connection more tolerant of bridge-induced delays), but it was never
eliminated completely.

Moving the Print Server to a network cable which was directly connected to
the host File Server solved the problem - both for FPSERVER and Novell's
PSERVER.EXE.  Since printing can be a high bandwidth operation (at least
when you use FPSERVER!), it made sense to eliminate the bridge bottleneck
anyhow.

I would be very grateful for any insight offered on this particular issue.



===============================================================================
REQUEST FOR FEEDBACK
===============================================================================

As stated elsewhere in this document, you are not required to register your
copy or use of FPSERVER.  However, I would appreciate hearing about your
experiences with it.  I maintain a database of those users that contact me
and keep them informed, without obligation, of future enhancements to
FPSERVER and other AdWare that I write.



===============================================================================
ABOUT THE AUTHOR
===============================================================================

My name is Richard L. Hartman.  I have 12 years of formal experience in the
Electronics industry which started in analog circuitry and progressed
through the disciplines of discrete digital, integrated digital,
microprocessor, software, and management.  My employment history includes
both Engineering and Marketing departments for everything from five-man
startups to companies with thousands of employees.

Along the way I have designed many successful products - the most prominent
of which is probably the Key Tronic KB5151 Enhanced PC Keyboard, the first
to have separate cursor and numeric keypads.  Over 250,000 KB5151's have
been sold and its standard continues to influence keyboard design to this
day.

My consulting efforts are now concentrated in the area of Local Area
Networks - specifically the development of software which runs with, and
takes advantage of, Novell's NetWare Operating System.  I am a Novell
Registered Professional Developer and actively pursue all topics, in all
disciplines, which involve this market segment.

FPSERVER, and other AdWare like it, is my answer to the extremely high cost
of advertising in magazines and trade journals.  I simply cannot justify
the money necessary to elevate myself and my services above the "noise
floor" established by multi-million dollar companies and their multi-page
color advertisements.  Instead, I invest my TIME writing software which
(hopefully) has broad appeal and allows potential clients the opportunity
to sample my work without risk or expense.

My services include:

     Conceptual: A confidential, objective sounding board for new ideas
    Feasibility: Assessment of technical viability
    Engineering: Actual product design and development
   Modification: Adding network intelligence to existing products
        Testing: Verifying network compatibility
       Training: Adding network programming to your staff's skill set
 Recommendation: Network-oriented analysis of your current/future products

If you create network software - or are planning to - please contact me:

                   Richard L. Hartman (RLH), Consultant
                 Novell Registered Professional Developer
                         5205 North Mulvaney Court
                             Spokane, WA 99212
          509-924-6576 / CompuServe 76350,2275 / GEnie R.HARTMAN9