This README file of ISA311.ZIP accompanies ISADISK.DSK for NetWare v3.11.
The following file(s) are included for this revision:

	ISADISK  DSK    12320  6-17-92  2:37p

Problems/Purpose Addressed:

	Subsequent to some rare error conditions, the previous 3.11 ISADISK
	driver would exit to the debugger.  That error path has been removed
	from this driver and the error handling capabilities have been
	improved, along with the parameters used when loading ISADISK.

	This driver no longer requires the '/b' parameter to avoid the
	NetWare Ready Sector or CCM Sector search.  The default (no parameter)
	is to bypass NR or CCM.  In order to specify search for NR or CCM
	sectors on drives, one must use either '/n' or '/N' parameter when
	loading the driver.  It is important to note, however, that unless
	the drive is known to be a NR or CCM sector drive, one should avoid
	the use of the '/n' parameter.

	This driver may not require the '/l' parameter in many cases where the
	previous ISADISK driver did.  The parameter is only to be used when a
	controller or paddleboard is configured at I/O=170h.  Even in that
	case it may not be necessary to use the parameter.


To install this version of ISADISK:  
 
1)    Copy ISADISK.DSK to the same directory as the other NLM files on your
      system (SYS:SYSTEM is suggested).  
  
2)    LOAD ISADISK.DSK as you normally would.  

***************************************************************** 
                    DISCLAIMER  
  
Novell, Inc. makes no representations or warranties with respect to
any NetWare software, and specifically disclaims any express or
implied warranties of merchantability, title, or fitness for a
particular purpose.  

Distribution of any NetWare software is forbidden without the
express written consent of Novell, Inc.  Further, Novell reserves
the right to discontinue distribution of any NetWare software.

Novell is not responsible for lost profits or revenue, loss of use
of the software, loss of data, costs of re-creating lost data, the
cost of any substitute equipment or program, or claims by any party
other than you.  Novell strongly recommends a backup be made before
any software is installed.   Technical support for this software
may be provided at the discretion of Novell.
*****************************************************************