file=NWLITE.PAT (01Jun92 GLF)

Novell's Netware Lite 1.0 has a minor bug which will prevent the server
portion of the program from operating in an OS/2 VDM.  Under certain
conditions it will also crash DOS.  This patch will correct the defect
in the file SERVER.EXE.  This is not an official fix, and carries no
guarantees.  Novell has been sent this patch file and appropriately
informed of this condition.  Users should contact Novell to obtain
official fixes to the Netware Lite program product.

The problem is that SERVER.EXE assumes the JFN (Job File Number) for
handles 0 and 1 (standard in and out) to always be a value of 1.  This
is not always the true, since handles and the system file table are
independent.  The correct solution is to copy the JFN from the PSP of
SERVER.EXE for handles 0 and 1 to the new JFT (Job File Table).

To install this fix enter the following from either an OS/2 or VDM
command line:    PATCH NWLITE.PAT /A